ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                     ³       C M O S B A K       ³
                     ³                           ³
                     ³    CMOS backup utility    ³
                     ³                           ³
                     ³        Version 1.0        ³
                     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

                            by Garry Hansen

                        Another Freeware Utility
                            from Cheapieware
                                    
                             February 1995
                                    

                              REQUIREMENTS

                            DOS 3.3 or later
                            Colour monitor
                            286+


                         WHAT DOES CMOSbak DO?

CMOSbak saves the CMOS and, optionally, the extended CMOS data to a
small binary file.  Using CMOSbak, this data can be restored later if
CMOS memory is lost or corrupted.


                             WHAT IS CMOS?

CMOS stands for Complementary Metal Oxide Semiconductor.  Is is a
small, low-powered portion of RAM (Random Access Memory) which
keeps its contents when your computer is turned off.  In many computers
this memory is powered by a small, barrel-shaped battery.  Newer
computers often use an "accumulator" (in essence, a battery which is
recharged whenever the computer is turned on) or have a ten-year battery
built into the chip.

CMOS RAM contains essential configuration data which is used by your
computer at start up. This information includes hard drive parameter
tables for IDE drives, video configuration, the number and kind of
floppy drives on your system, and the date and time.

                         WHAT IS EXTENDED CMOS?

Earlier AT-class computers contained 64 bytes of CMOS.  Later 286 and
most 386 and later PCs contain at least 128 bytes.  The 64 or more bytes
beyond the first 64 bytes of the CMOS are often referred to as "Extended
CMOS" or XCMOS. They generally contain advanced BIOS data, such as
memory wait states, clock speeds, and the number of type of SIMMs or
SIPs in your system.

If you have a 386 or a more powerful computer, you probably have
Extended CMOS.   Late-model 286s may also have XCMOS.  Ancient PCs and
XTs did not contain a CMOS at all, and the configuration data was
established by setting DIP (Dual-In-line Package) switches on the
motherboard or peripheral cards.  DO NOT use CMOSbak if you have a PC or
XT computer.


                      WHY SHOULD I BACKUP MY CMOS?

Your computer needs the configuration data in the CMOS to perform
correctly. Although most computers provide an option for bypassing the
Extended CMOS, restoring power-on defaults by holding down a certain key
at bootup (such as the INS key), these default values are "safe" but not
optimal.  Most importantly, the basic CMOS contains hard drive parameter
tables which are necessary to run an IDE drive.  If your CMOS fails
(often as the result of a weak or dead battery), you will lose access to
your hard drive until you restore the parameters (number of cylinders,
heads, sectors, etc.).  At the least, this is annoying; at worst,
disasterous.

                         HOW DO I USE CMOSbak?

First, copy CMOSBAK.EXE and its documentation to a floppy disk.  Since a
CMOS failure could prevent access to a hard drive, it is best to run
CMOSbak from a floppy disk.

Determine whether your computer contains basic or extended CMOS.
CMOSbak will give you the option to save either 64 bytes or 128 bytes of
CMOS data. Attempting to restore 128 bytes of data to a 64-byte CMOS
could be dangerous.

Since CMOSbak will attempt to create or restore CMOS.SAV from the
current directory, change to the floppy drive containing CMOSbak before
running the program.  Please ensure that your floppy disk is not write
protected.

Follow the online instructions to save your CMOS data.  Store the disk
containing CMOSbak and CMOS.SAV in a safe place.  When you need to
restore your CMOS data, simple run CMOSbak again and select the restore
command.

                WILL CMOSbak MESS UP THE DATE AND TIME?

CMOS data includes date and time info.  Although CMOSbak saves this
information, it automatically skips it when restoring from a CMOS.SAV
file to avoid resetting your computer's clock and calendar.


                              DISTRIBUTION

CMOSbak is released as Freeware.  It may be freely used and distributed,
providing the software and documentation is complete and unaltered.
Vendors may charge a distribution fee of no more than $5.00.


                               DISCLAIMER

The author makes no warranties, expressed or implied, as to the quality or
performance of this program.  Your use of this program constitutes your
release of the author from liability or litigation for any indirect or
consequential damages arising from the use of this program or its associated
files.

In no event will I be liable to you for any damages, including any lost
profits, lost savings or other incidental or consequential damages arising
out of your use of inability to use the program, or for any claim by any
other party.