PNG (Portable Network Graphics) Specification, Ninth Draft

Revision date: 7 March, 1995

The latest hypertext version of this document is available on the World Wide
Web:

<URL:http://sunsite.unc.edu/boutell/png.html>

     Permission is granted to reproduce this specification in complete and
     unaltered form. Excerpts may be printed with the following notice:
     "excerpted from the PNG (Portable Network Graphics) specification,
     ninth draft." No notice is required in software that follows this
     specification; notice is only required when reproducing or excerpting
     from the specification itself.

Contents

   * 0. Status
   * 1. Introduction
   * 2. Data Representation
   * 3. File Structure
   * 4. Standard Chunks
   * 5. Deflate/inflate compression specification
   * 6. Filter algorithms
   * 7. Multi-image extension
   * 8. Recommendations for encoders
   * 9. Recommendations for decoders
   * 10. Appendix: Rationale
   * 11. Appendix: Sample CRC Code
   * 12. Credits

0. Status

This is the ninth draft of the PNG specification. All future drafts will be
backward-compatible with the graphics file format described by this document.
Implementations are invited, and a reference implementation is under
development; see below.

Changes since draft 8

   * Extensive editing
   * Filters chapter rewritten
   * Line-by-line filter selection
   * Adam7 interlacing in preference to GIF-style
   * Text chunks will be Latin-1
   * New text keywords
   * Compressed text support
   * Pixel unit in oFFs chunk
   * sBIT chunk added
   * cHRM: Chromaticity chunk
   * gAMA: Fixed (4 bytes)
   * HEAD renamed IHDR, TAIL renamed IEND
   * Time chunk is now modification time
   * 16-bit images have 16-bit alpha channels

Reference Implementation

It is anticipated that a finished standard and reference implementation will be
available by the end of March. The reference implementation will be freely
usable in all applications, including commercial applications.

1. Introduction

The PNG format is intended to provide a portable, legally unencumbered,
well-compressed, well-specified standard for lossless bitmapped image files.

Although the initial motivation for developing PNG was to replace GIF, the
design provides some useful new features not available in GIF, with minimal
cost to developers.

GIF features retained in PNG include:

   *  Palette-mapped images of up to 256 colors.
   *  Streamability: files can be read and written strictly serially, thus
     allowing the file format to be used as a communications protocol for
     on-the-fly generation and display of images.
   *  Progressive display: a suitably prepared image file can be displayed as
     it is received over a communications link, yielding a low-resolution image
     very quickly with gradual improvement of detail thereafter.
   *  Transparency: portions of the image can be marked as transparent,
     allowing the effect of a nonrectangular image area to be achieved.
   *  Ancillary information: textual comments and other data can be stored
     within the image file.
   *  Complete hardware and platform independence.
   *  Effective, 100% lossless compression.

Important new features of PNG, not available in GIF, include:

   *  Truecolor images of up to 48 bits per pixel.
   *  Grayscale images of up to 16 bits per pixel.
   *  Full alpha channel (general transparency masks).
   *  Gamma (brightness) indication, allowing automatic brightness adjustment.
   *  Early and straightforward detection of file corruption.
   *  Faster initial presentation in progressive display mode.

PNG is intended to be:

   *  Simple and portable: PNG should be widely implementable with reasonably
     small effort for developers.
   *  Legally unencumbered: to the best of the knowledge of the PNG authors, no
     algorithms under legal challenge are used.
   *  Well compressed: both palette-mapped and truecolor images are compressed
     as effectively as in any other widely used lossless format, and in most
     cases more effectively.
   *  Interchangeable: any standard-conforming PNG decoder will read all
     conforming PNG files.
   *  Flexible: the format allows for future extensions and private add-ons,
     without compromising interchangeability of basic PNG.
   *  Robust: the design supports full file integrity checking as well as
     simple, quick detection of common transmission errors.

The main part of this specification simply gives the definition of the file
format. An appendix gives the rationale for many design decisions. Although the
rationale is not part of the formal specification, reading it may help
implementors to understand the design. Cross-references in the main text point
to relevant parts of the rationale.

See Rationale: Why a new file format?, Why these features?, Why not these
features?, Why not use format XYZ?.

Pronunciation

PNG is pronounced "ping".

2. Data Representation

This chapter discusses basic data representations used in PNG files, as well as
the expected representation of the image data.

Integers and byte order

All integers which require more than one byte will be in network byte order,
which is to say the most significant byte comes first, then the less
significant bytes in descending order of significance (MSB LSB for two-byte
integers, B3 B2 B1 B0 for four-byte integers). References to bit 7 refer to the
highest bit (value 128) of a byte; references to bit 0 refer to the lowest bit
(value 1) of a byte. Values are unsigned unless otherwise noted. Values
explicitly noted as signed are represented in two's complement notation.

See Rationale: Byte order.

Color values

All color values range from zero (representing black) to most intense at the
maximum value for the bit depth. Note that the maximum value at a given bit
depth is not 2^bitdepth, but rather (2^bitdepth)-1. Intensity is not
necessarily linear; the gAMA chunk specifies the gamma response of the source
device, and viewers are strongly encouraged to properly compensate. See Gamma
correction, below.

Source data with a precision not directly supported in PNG (for example, 5
bit/sample truecolor) must be scaled up to the next higher supported bit depth.
Such scaling is reversible and hence incurs no loss of data, while it reduces
the number of cases that decoders must cope with. See Recommendations for
encoders: Bitdepth scaling.

Image layout

PNG images are laid out as a rectangular pixel array, with pixels appearing
left-to-right within each scanline, and scanlines appearing top-to-bottom. (For
progressive display purposes, the data may not actually be transmitted in this
order; see Interlaced data order.) The size of each pixel is determined by the
bit depth, which is the number of bits per stored value in the image data.

Three types of pixels are supported:

   *  Palette-mapped pixels are represented by a single value that is an index
     into a supplied palette. The bit depth determines the maximum number of
     palette entries, not the color precision within the palette.
   *  Grayscale pixels are represented by a single value that is a grayscale
     level, where zero is black and the largest value for the bit depth is
     white.
   *  Truecolor pixels are represented by three-value sequences: red (zero =
     black, max = red) appears first, then green (zero = black, max = green),
     then blue (zero = black, max = blue). The bit depth specifies the size of
     each value, not the total pixel size.

In all cases, pixels are packed into scanlines consecutively, without wasted
space between pixels. (The allowable bit depths are restricted so that the
packing is simple and efficient.) When pixels are less than 8 bits deep, they
are packed into bytes with the leftmost pixel in the high-order bits of a byte,
the rightmost in the low-order bits.

However, scanlines always begin on byte boundaries. When pixels are fewer than
8 bits deep, if the scanline width is not evenly divisible by the number of
pixels per byte then the low-order bits in the last byte of each scanline are
wasted. The contents of the padding bits added to fill out the last byte of a
scanline are unspecified.

An additional "filter" byte is added to the beginning of every scanline, as
described in detail below. The filter byte is not considered part of the image
data, but it is included in the data stream sent to the compression step.

Alpha channel

An alpha channel, representing transparency levels on a per-pixel basis, may be
included in grayscale and truecolor PNG images.

An alpha channel value of 0 represents full transparency, and a value of
(2^bitdepth)-1 represents a fully opaque pixel. Intermediate values indicate
partially transparent pixels that may be combined with a background image to
yield a composite image.

Alpha channels may be included with images that have either 8 or 16 bits per
sample, but not with images that have fewer than 8 bits per sample. Alpha
values are represented with the same bit depth used for the image values. The
alpha value is stored immediately following the grayscale or RGB values of the
pixel.

The color stored for a pixel is not affected by the alpha value assigned to the
pixel. This rule is sometimes called "unassociated" or "non premultiplied"
alpha. (Another common technique is to store pixel values premultiplied by the
alpha fraction; in effect, the image is already composited against a black
background. PNG does not use premultiplied alpha, since it precludes lossless
storage.)

Transparency control is also possible without the storage cost of a full alpha
channel. In a palette image, an alpha value may be defined for each palette
entry. In grayscale and truecolor images, a single pixel value may be
identified as being "transparent". These techniques are controlled by the tRNS
ancillary chunk type.

If no alpha channel nor tRNS chunk is present, all pixels in the image are to
be treated as fully opaque.

Viewers may support transparency control partially, or not at all. See
Recommendations for encoders: Alpha channel creation and Recommendations for
decoders: Alpha channel processing.

Filtering

PNG allows the image data to be filtered before it is compressed. The purpose
of filtering is to improve the compressibility of the data. The filter step
itself does not reduce the size of the data. All PNG filters are strictly
lossless.

PNG defines several different filter algorithms, including "none" which
indicates no filtering. The filter algorithm is specified for each scanline by
a filter type byte which precedes the filtered scanline in the precompression
data stream. An intelligent encoder may switch filters from one scanline to the
next. The method for choosing which filter to employ is up to the encoder.

See Rationale: Filtering.

Interlaced data order

A PNG image can be stored in interlaced order to allow progressive display. The
purpose of this feature is to allow images to "fade in" when they are being
displayed on-the-fly. Interlacing slightly expands the file size on average,
but it gives the user a meaningful display much more rapidly. Note that
decoders are required to be able to read interlaced images, whether or not they
actually perform progressive display.

With interlace type 0, pixels are stored sequentially from left to right, and
scanlines sequentially from top to bottom (no interlacing).

Interlace type 1, known as Adam7 after its author, Adam M. Costello, consists
of seven distinct passes over the image. Each pass transmits a subset of the
pixels in the image. The pass in which each pixel is transmitted is defined by
replicating the following 8-by-8 pattern over the entire image, starting at the
upper left corner:

1 6 4 6 2 6 4 6
7 7 7 7 7 7 7 7
5 6 5 6 5 6 5 6
7 7 7 7 7 7 7 7
3 6 4 6 3 6 4 6
7 7 7 7 7 7 7 7
5 6 5 6 5 6 5 6
7 7 7 7 7 7 7 7

Within each pass, the selected pixels are transmitted left to right within a
scanline, and selected scanlines sequentially from top to bottom. For example,
pass 2 contains pixels 4, 12, 20, etc. of scanlines 0, 8, 16, etc. (numbering
from 0,0 at the upper left corner). The last pass contains the entirety of
scanlines 1, 3, 5, etc. This selection process is called "decimating" the
image.

The data within each pass is laid out as though it were a complete image of the
appropriate dimensions. For example, if pixels are fewer than 8 bits deep, each
decimated scanline is padded to fill an integral number of bytes (see Image
layout). Filtering is done on the decimated scanlines in the usual way, and a
filter type byte is transmitted before each one (see Filter algorithms). Note
that the transmission order is defined in such a way that each pass will have
the same number of pixels on each decimated scanline that it transmits; this is
necessary for convenient application of some of the filters.

Caution: If the image contains fewer than five columns or fewer than five rows,
some passes may be entirely empty. Encoder and decoder authors should be
careful to handle this case correctly.

For progressive display, it is recommended that decoders expand each received
pixel to a rectangle covering the yet-to-be-transmitted pixel positions below
and to the right of the received pixel. This process can be described by the
following pseudocode:

Starting_Row [1..7] =  { 0, 0, 4, 0, 2, 0, 1 }
Starting_Col [1..7] =  { 0, 4, 0, 2, 0, 1, 0 }
Row_Increment [1..7] = { 8, 8, 8, 4, 4, 2, 2 }
Col_Increment [1..7] = { 8, 8, 4, 4, 2, 2, 1 }
Block_Height [1..7] =  { 8, 8, 4, 4, 2, 2, 1 }
Block_Width [1..7] =   { 8, 4, 4, 2, 2, 1, 1 }

pass := 1
while pass <= 7
begin
    row := Starting_Row[pass]

    while row < height
    begin
        col := Starting_Col[pass]

        while col < width
        begin
            visit (row, col,
                   min (Block_Height[pass], height - row),
                   min (Block_Width[pass], width - col))
            col := col + Col_Increment[pass]
        end
        row := row + Row_Increment[pass]
    end

    pass := pass + 1
end

Here, the function "visit(row,column,height,width)" obtains the next
transmitted pixel and paints a rectangle of the specified height and width,
whose upper-left corner is at the specified row and column, using the color
indicated by the pixel. Note that row and column are measured from 0,0 at the
upper left corner.

See Rationale: Interlacing.

Gamma correction

Gamma is a way of defining the brightness reproduction curve of a camera or
display device. When brightness levels are expressed as fractions in the range
0 to 1, such a device produces an output brightness level "obright" from an
input brightness level "bright" according to the equation

  obright = bright ^ gamma

PNG images may specify the gamma of the camera (or simulated camera) that
produced the image, and thus the gamma of the image with respect to the
original scene. To get accurate tone reproduction, the gamma of the display
device and the gamma of the image file should be reciprocals of each other,
since the overall gamma of the system is the product of the gammas of each
component. So, for example, if an image with a gamma of 0.4 is displayed on a
CRT with a gamma of 2.5, the overall gamma of the system is 1.0. An overall
gamma of 1.0 gives correct tone reproduction.

In practice, images of gamma around 1.0 and gamma around 0.45 are both widely
found. PNG expects encoders to record the gamma if known, and it expects
decoders to correct the image gamma if necessary for proper display on their
display hardware. Failure to correct for image gamma leads to a too-dark or
too-light display.

Gamma correction is not applied to the alpha channel, if any. Alpha values
always represent a linear fraction of full opacity.

See Rationale: Why gamma correction?, Recommendations for encoders: Encoder
gamma handling, and Recommendations for decoders: Decoder gamma handling.

Text strings

A PNG file can store text associated with the image, such as an image
description or copyright notice. Keywords are used to indicate what each text
string represents.

ISO 8859-1 (Latin-1) is the character set recommended for use in text strings.
This character set is a superset of 7-bit ASCII.

Character codes not defined in Latin-1 may be used, but are unlikely to port
across platforms correctly. (For that matter, any characters beyond 7-bit ASCII
will not display correctly on all platforms; but Latin-1 represents a set which
is widely portable.)

Provision is also made for the storage of compressed text.

See Rationale: Text strings.

3. File Structure

A PNG file consists of a PNG signature followed by a series of chunks. This
chapter defines the signature and the basic properties of chunks. Individual
chunk types are discussed in the next chapter.

PNG file signature

The first eight bytes of a PNG file always contain the following (decimal)
values:

137 80 78 71 13 10 26 10

This signature indicates that the remainder of the file contains a single PNG
image, consisting of a series of chunks beginning with an IHDR chunk and ending
with an IEND chunk.

See Rationale: PNG file signature.

Chunk layout

Each chunk consists of four parts:

Length
     A 4-byte unsigned integer giving the number of bytes in the chunk's data
     field. The length counts only the data field, not itself, the chunk type
     code, or the CRC. Zero is a valid length. Although encoders and decoders
     should treat the length as unsigned, its value may not exceed (2^31)-1
     bytes.
Chunk Type
     A 4-byte chunk type code. For convenience in description and in examining
     PNG files, type codes are restricted to consist of uppercase and lowercase
     ASCII letters (A-Z, a-z). However, encoders and decoders should treat the
     codes as fixed binary values, not character strings. For example, it would
     not be correct to represent the type code IDAT by the EBCDIC equivalents
     of those letters. Additional naming conventions for chunk types are
     discussed in the next section.
Chunk Data
     The data bytes appropriate to the chunk type, if any. This field may be of
     zero length.
CRC
     A 4-byte CRC (Cyclical Redundancy Check) calculated on the preceding bytes
     in that chunk, including the chunk type code and chunk data fields, but
     not including the length field. The CRC is always present, even for empty
     chunks such as IEND. The CRC algorithm is specified below.

The chunk data length may be any number of bytes up to the maximum; therefore,
implementors may not assume that chunks are aligned on any boundaries larger
than bytes.

Chunks may appear in any order, subject to the restrictions placed on each
chunk type. (One notable restriction is that IHDR must appear first and IEND
must appear last; thus the IEND chunk serves as an end-of-file marker.)
Multiple chunks of the same type may appear, but only if specifically permitted
for that type.

See Rationale: Chunk layout.

Chunk naming conventions

Chunk type codes are assigned in such a way that a decoder can determine some
properties of a chunk even if it does not recognize the type code. These rules
are intended to allow safe, flexible extension of the PNG format, by allowing a
decoder to decide what to do when it encounters an unknown chunk. The naming
rules are not normally of interest when a decoder does recognize the chunk's
type.

Four bits of the type code, namely bit 5 (value 32) of each byte, are used to
convey chunk properties. This choice means that a human can read off the
assigned properties according to whether each letter of the type code is
uppercase (bit 5 is 0) or lowercase (bit 5 is 1). However, decoders should test
the properties of an unknown chunk by numerically testing the specified bits;
testing whether a character is uppercase or lowercase is inefficient, and even
incorrect if a locale-specific case definition is used.

It is also worth noting that the property bits are an inherent part of the
chunk name, and hence are fixed for any chunk type. Thus, TEXT and Text are
completely unrelated chunk type codes. Decoders should recognize codes by
simple four-byte literal comparison; it is incorrect to perform case conversion
on type codes.

The semantics of the property bits are:

First Byte: 0 (uppercase) = critical, 1 (lowercase) = ancillary
     Chunks which are not strictly necessary in order to meaningfully display
     the contents of the file are known as "ancillary" chunks. Decoders
     encountering an unknown chunk in which the ancillary bit is 1 may safely
     ignore the chunk and proceed to display the image. The offset chunk (oFFs)
     is an example of an ancillary chunk.

     Chunks which are critical to the successful display of the file's contents
     are called "critical" chunks. Decoders encountering an unknown chunk in
     which the ancillary bit is 0 must indicate to the user that the image
     contains information they cannot safely interpret. The image header chunk
     (IHDR) is an example of a critical chunk.

Second Byte: 0 (uppercase) = public, 1 (lowercase) = private
     If the chunk is public (part of this specification or a later edition of
     this specification), its second letter is uppercase. If your application
     requires proprietary chunks, and you have no interest in seeing the
     software of other vendors recognize them, use a lowercase second letter in
     the chunk name. Such names will never be assigned in the official
     specification. Note that there is no need for software to test this
     property bit; it simply ensures that private and public chunk names will
     not conflict.

Third Byte: reserved, must be 0 (uppercase) always
     The significance of the case of the third letter of the chunk name is
     reserved for possible future expansion. At the present time all chunk
     names must have uppercase third letters.

Fourth Byte: 0 (uppercase) = unsafe to copy, 1 (lowercase) = safe to copy
     This property bit is not of interest to pure decoders, but it is needed by
     programs that modify a PNG file.

     If a chunk's safe-to-copy bit is 1, the chunk may be copied to a modified
     PNG file whether or not the software recognizes the chunk type, and
     regardless of the extent of the file modifications.

     If a chunk's safe-to-copy bit is 0, it indicates that the chunk depends on
     the image data. If the program has made any changes to critical chunks,
     including addition, modification, deletion, or reordering of critical
     chunks, then unrecognized unsafe chunks must not be copied to the output
     PNG file. (Of course, if the program does recognize the chunk, it may
     choose to output an appropriately modified version.)

     A PNG file modifier is always allowed to copy all unrecognized chunks if
     it has only added, deleted, or modified ancillary chunks. This implies
     that it is not permissible to make ancillary chunks that depend on other
     ancillary chunks.

     PNG file modifiers which do not recognize a critical chunk should report
     an error and refuse to process that PNG file at all. The safe/unsafe
     mechanism is intended for use with ancillary chunks. The safe-to-copy bit
     will always be 0 for critical chunks.

See Rationale: Chunk naming conventions.

CRC algorithm

Chunk CRCs are calculated using standard CRC methods with pre and post
conditioning. The CRC polynomial employed is as follows:

x^32+x^26+x^23+x^22+x^16+x^12+x^11+x^10+x^8+x^7+x^5+x^4+x^2+x+1

The 32-bit CRC is initialized to all 1's, and then the data from each byte is
processed from the least significant bit (1) to the most significant bit (128).
The 1's complement of the CRC is transmitted (stored in the file) MSB first.
For the purpose of separating into bytes and ordering, the least significant
bit of the 32-bit CRC is defined to be the coefficient of the x^31 term.

Practical calculation of the CRC always employs a precalculated table to
greatly accelerate the computation. See Appendix: Sample CRC Code.

4. Standard Chunks

This chapter presents the standard types of PNG chunks.

Critical Chunks

All implementations must understand and successfully render the standard
critical chunks. A valid PNG image must contain an IHDR chunk, one or more IDAT
chunks, and an IEND chunk.

IHDR Image Header
     This chunk must appear FIRST. Its contents are:

     Width:            4 bytes
     Height:           4 bytes
     Bit depth:        1 byte
     Color type:       1 byte
     Compression type: 1 byte
     Filter type:      1 byte
     Interlace type:   1 byte

     Width and height give the image dimensions in pixels. They are 4-byte
     integers. Zero is an invalid value. The maximum for each is (2^31)-1 in
     order to accommodate languages which have difficulty with unsigned 4-byte
     values.

     Bit depth is a single-byte integer giving the number of bits per pixel
     (for palette images) or per sample (for grayscale and truecolor images).
     Valid values are 1, 2, 4, 8, and 16, although not all values are allowed
     for all color types.

     Color type is a single-byte integer that describes the interpretation of
     the image data. Color type values represent sums of the following values:
     1 (palette used), 2 (color used), and 4 (full alpha used). Valid values
     are 0, 2, 3, 4, and 6.

     Bit depth restrictions for each color type are imposed both to simplify
     implementations and to prohibit certain combinations that do not compress
     well in practice. Decoders must support all legal combinations of bit
     depth and color type. (Note that bit depths of 16 are easily supported on
     8-bit display hardware by dropping the least significant byte.)

     Color    Allowed    Interpretation
     Type    Bit Depths

     0       1,2,4,8,16  Each pixel value is a grayscale level.

     2       8,16        Each pixel value is an R,G,B series.

     3       1,2,4,8     Each pixel value is a palette index;
                         a PLTE chunk must appear.

     4       8,16        Each pixel value is a grayscale level,
                         followed by an alpha channel level.

     6       8,16        Each pixel value is an R,G,B series,
                         followed by an alpha channel level.

     Note that an alpha channel, where present, is represented by either one
     byte per pixel (when bit depth=8) or two bytes per pixel (when bit
     depth=16).

     Compression type is a single-byte integer that indicates the method used
     to compress the image data. Compression methods are defined in a later
     chapter. At present, only compression type 0 (deflate/inflate compression
     with a 32K sliding window) is defined. All standard PNG images must be
     compressed with this scheme. The compression type code is provided for
     possible future expansion or proprietary variants. Decoders must check
     this byte and report an error if it holds an unrecognized code.

     Filter type is a single-byte integer that indicates the preprocessing
     method applied to the image data before compression. Filtering methods are
     defined in a later chapter. At present, only filter type 0 (adaptive
     filtering with five basic filter types) is defined. As with the
     compression type code, decoders must check this byte and report an error
     if it holds an unrecognized code. See Filter algorithms for details.

     Interlace type is a single-byte integer that indicates the transmission
     order of the pixel data. Two values are currently defined: 0 (no
     interlace) or 1 (Adam7 interlace). See Interlaced data order for details.

PLTE Palette
     This chunk's contents are from 1 to 256 palette entries, each a three-byte
     series of the form:

     red:   1 byte (0 = black, 255 = red)
     green: 1 byte (0 = black, 255 = green)
     blue:  1 byte (0 = black, 255 = blue)

     The number of entries is determined from the chunk length. A chunk length
     not divisible by 3 is an error.

     This chunk must appear for color type 3, and may appear for color types 2
     and 6. If this chunk does appear, it must precede the first IDAT chunk.

     For color type 3 (palette data), the PLTE chunk is required. The first
     entry in PLTE is referenced by pixel value 0, the second by pixel value 1,
     etc. The number of palette entries must not exceed the range that can be
     represented by the bit depth (for example, 2^4 = 16 for a bit depth of 4).
     It is permissible to have fewer entries than the bit depth would allow. In
     that case, any out-of-range pixel value found in the image data is an
     error.

     For color types 2 and 6 (truecolor), the PLTE chunk is optional. If
     present, it provides a recommended set of from 1 to 256 colors to which
     the truecolor image may be quantized if the viewer cannot display
     truecolor directly. If PLTE is not present, such a viewer must select
     colors on its own, but it is often preferable for this to be done once by
     the encoder.

     Note that the palette uses 8 bits (1 byte) per value regardless of the
     image bit depth specification. In particular, the palette is 8 bits deep
     even when it is a suggested quantization of a 16-bit truecolor image.

IDAT Image Data
     This chunk contains image data. The data has been filtered and compressed
     according to the filter type and compression method specified by the IHDR
     chunk.

     There may be multiple IDAT chunks; if so, they must appear consecutively
     with no other intervening chunks. The compressed data stream is the
     concatenation of the contents of all the IDAT chunks. The encoder may
     divide the compressed data stream into chunks as it wishes; chunk
     boundaries have no semantic significance. (Multiple IDAT chunks are
     allowed so that encoders can work in a fixed amount of memory; typically
     the chunk size will correspond to the encoder's buffer size.)

IEND Image Trailer
     This chunk must appear LAST. It marks the end of the PNG data stream. The
     chunk's data field is empty.

Ancillary Chunks

All ancillary chunks are optional, in the sense that encoders need not write
them and decoders may ignore them. However, encoders are encouraged to write
the standard ancillary chunks when the information is available, and decoders
are encouraged to interpret these chunks when appropriate and feasible.

gAMA Gamma Correction
     This chunk's contents are:

     Image gamma value: 4 bytes

     The gamma correction chunk specifies the gamma of the camera (or simulated
     camera) that produced the image, and thus the gamma of the image with
     respect to the original scene. Note that this is not the same as the gamma
     of the display device that will reproduce the image correctly.

     A value of 100000 represents a gamma of 1.0, a value of 45000 a gamma of
     0.45, and so on (divide by 100000.0). Values around 1.0 and around 0.45
     are common in practice.

     If the encoder does not know the gamma value, it should not write a gamma
     chunk; the absence of a gamma chunk indicates the gamma is unknown.

     If the gAMA chunk appears, it must precede the first IDAT chunk, and it
     must also precede the PLTE chunk if present.

     See Gamma correction.

sBIT Significant Bits
     To simplify decoders, PNG specifies that only certain bit depth values be
     used, and further specifies that values stored must be scaled to the full
     range of possible values at that bit depth. However, the sBIT chunk is
     provided in order to store the original number of significant bits.

     For color type 0 (grayscale), the sBIT chunk contains a single byte,
     indicating the number of bits which were significant in the source data.

     For color type 2 (RGB truecolor), the sBIT chunk contains three bytes,
     indicating the number of bits which were significant in the source data
     for the red, green, and blue channels, respectively.

     For color type 3 (palette color), the sBIT chunk contains three bytes,
     indicating the number of bits which were significant in the source data
     for the red, green, and blue components of the palette entries,
     respectively.

     For color type 4 (grayscale with alpha channel), the sBIT chunk contains
     two bytes, indicating the number of bits which were significant in the
     source grayscale data and the source alpha channel data, respectively.

     For color type 6 (RGB truecolor with alpha channel), the sBIT chunk
     contains four bytes, indicating the number of bits which were significant
     in the source data for the red, green, blue and alpha channels,
     respectively.

     If the sBIT chunk appears, it must precede the first IDAT chunk, and it
     must also precede the PLTE chunk if present.

cHRM Primary Chromaticities and White Point
     Applications that need precise specification of colors in a PNG file may
     use this chunk to specify the chromaticities of the red, green, and blue
     primaries used in the image, and the referenced white point. These values
     are based on the 1931 CIE (International Color Committee) XYZ diagram.
     Only the chromaticities (X and Y) are specified.

     The chunk stores eight values, each encoded as a 4-byte integer,
     representing the X or Y value times 100000. They are stored in the order
     White Point X, White Point Y, Red X, Red Y, Green X, Green Y, Blue X, Blue
     Y.

     If the cHRM chunk appears, it must precede the first IDAT chunk, and it
     must also precede the PLTE chunk if present.

tRNS Transparency
     Transparency is an alternative to the full alpha channel. Although
     transparency is not as elegant as the full alpha channel, it requires less
     storage space and is sufficient for many common cases.

     For color type 3 (palette), this chunk's contents are a series of alpha
     channel bytes, corresponding to palette indexes in the PLTE chunk. Each
     entry indicates that pixels of that palette index should be treated as
     having the specified alpha value. Alpha values have the same
     interpretation as in an 8-bit full alpha channel: 0 is fully transparent,
     255 is fully opaque, regardless of image bit depth. The tRNS chunk may
     contain fewer alpha channel bytes than there are palette entries. In this
     case, the alpha channel value for all remaining palette entries is assumed
     to be 255. In the common case where only palette index 0 need be made
     transparent, only a one-byte tRNS chunk is needed. The tRNS chunk may not
     contain more bytes than there are palette entries.

     For color type 0 (grayscale), the tRNS chunk contains a single gray level
     value, stored in the format

     gray:  2 bytes, range 0 .. (2^bitdepth) - 1

     (For consistency, 2 bytes are used regardless of the image bit depth.)
     Pixels of the specified gray level are to be treated as transparent
     (equivalent to alpha value 0); all other pixels are to be treated as fully
     opaque (alpha value (2^bitdepth)-1).

     For color type 2 (RGB), the tRNS chunk contains a single RGB color value,
     stored in the format

     red:   2 bytes, range 0 .. (2^bitdepth) - 1
     green: 2 bytes, range 0 .. (2^bitdepth) - 1
     blue:  2 bytes, range 0 .. (2^bitdepth) - 1

     (For consistency, 2 bytes per sample are used regardless of the image bit
     depth.) Pixels of the specified color value are to be treated as
     transparent (equivalent to alpha value 0); all other pixels are to be
     treated as fully opaque (alpha value (2^bitdepth)-1).

     tRNS is prohibited for color types 4 and 6, since a full alpha channel is
     already present in those cases.

     When present, the tRNS chunk must precede the first IDAT chunk, and must
     follow the PLTE chunk, if any.

bKGD Background Color
     This chunk specifies a default background color against which the image
     may be presented. Note that viewers are not bound to honor this chunk; a
     viewer may choose to use a different background color.

     For color type 3 (palette), the bKGD chunk contains:

     palette index: 1 byte

     The value is the palette index of the color to be used as background.

     For color types 0 and 4 (grayscale, with or without alpha), bKGD contains:

     gray:  2 bytes, range 0 .. (2^bitdepth) - 1

     (For consistency, 2 bytes are used regardless of the image bit depth.) The
     value is the gray level to be used as background.

     For color types 2 and 6 (RGB, with or without alpha), bKGD contains:

     red:   2 bytes, range 0 .. (2^bitdepth) - 1
     green: 2 bytes, range 0 .. (2^bitdepth) - 1
     blue:  2 bytes, range 0 .. (2^bitdepth) - 1

     (For consistency, 2 bytes per sample are used regardless of the image bit
     depth.) This is the RGB color to be used as background.

     When present, the bKGD chunk must precede the first IDAT chunk, and must
     follow the PLTE chunk, if any.

     See Recommendations for decoders: Background color.

hIST Image Histogram
     The histogram chunk gives the approximate usage frequency of each color in
     the color palette. A histogram chunk may appear only when a palette chunk
     appears. If a viewer is unable to provide all the colors listed in the
     palette, the histogram may help it decide how to choose a subset of the
     colors for display.

     This chunk's contents are a series of 2-byte (16 bit) unsigned integers.
     There must be exactly one entry for each entry in the PLTE chunk. Each
     entry is proportional to the fraction of pixels in the image that have
     that palette index; the exact scale factor is chosen by the encoder.

     Histogram entries are approximate, with the exception that a zero entry
     specifies that the corresponding palette entry is not used at all in the
     image. It is required that a histogram entry be nonzero if there are any
     pixels of that color.

     When the palette is a suggested quantization of a truecolor image, the
     histogram is necessarily approximate, since a decoder may map pixels to
     palette entries differently than the encoder did. In this situation, zero
     entries should not appear.

     The hIST chunk, if it appears, must follow the PLTE chunk, and must
     precede the first IDAT chunk.

     See Rationale: Palette histograms, and Recommendations for decoders:
     Palette histogram usage.

tEXt Textual Data
     A tEXt chunk contains a keyword followed by a text string. The keyword and
     text string are separated by a zero byte (null character). Neither the
     keyword nor the string may contain a null character. Note that the text
     string is not null-terminated (the length of the chunk is sufficient
     information to locate the ending). Both keyword and text are interpreted
     according to the ISO 8859-1 (Latin-1) character set. Newlines in the text
     string should be represented by a single linefeed character (decimal 10);
     use of other ASCII control characters is discouraged.

     Any number of tEXt chunks may appear, and more than one with the same
     keyword is permissible.

     The keyword indicates the type of information represented by the string.
     The following keywords are predefined and should be used where
     appropriate:

     Title            Short (one line) title or caption for image
     Author           Name of image's creator
     Copyright        Copyright notice
     Description      Description of image (possibly long)
     Software         Software used to create the image
     Disclaimer       Legal disclaimer
     Warning          Warning of nature of content
     Source           Device used to create the image
     Comment          Miscellaneous comment; conversion from GIF comment

     Other keywords, containing any sequence of printable characters in the
     character set, may be invented for other purposes. Keywords of general
     interest may be registered with the maintainers of the PNG specification.

     Keywords must be spelled exactly as registered, so that decoders may use
     simple literal comparisons when looking for particular keywords. In
     particular, keywords are considered case-sensitive.

     See Recommendations for encoders: Text chunk processing and
     Recommendations for decoders: Text chunk processing.

zTXt Compressed Textual Data
     A zTXt chunk contains textual data, just as tEXt does; however, zTXt takes
     advantage of compression.

     A zTXt chunk begins with an uncompressed Latin-1 keyword followed by a
     null (0) character, just as in the tEXt chunk. The next byte after the
     null contains a compression type byte, for which the only legitimate value
     is presently zero (deflate/inflate compression). The compression-type byte
     is followed by a compressed Latin-1 text data stream which makes up the
     remainder of the chunk. The compressed data stream uses the same Ziplib
     format specified below under Deflate/inflate compression specification.

     Any number of zTXt and tEXt chunks may appear in the same file. See the
     preceding definition of the tEXt chunk for the predefined keywords and the
     exact format of the text.

     See Recommendations for encoders: Text chunk processing and
     Recommendations for decoders: Text chunk processing.

pHYs Physical Pixel Dimensions
     This chunk specifies the intended resolution for display of the image. The
     chunk's contents are:

     4 bytes: pixels per unit, X axis (unsigned integer)
     4 bytes: pixels per unit, Y axis (unsigned integer)
     1 byte: unit specifier

     The following values are legal for the unit specifier:

     0: unit is unknown (pHYs defines pixel aspect ratio only)
     1: unit is the meter

     Conversion note: one inch is equal to exactly 0.0254 meters.

     If this ancillary chunk is not present, pixels are assumed to be square,
     and the physical size of each pixel is unknown.

     If present, this chunk must precede the first IDAT chunk.

     See Recommendations for decoders: Pixel dimensions.

oFFs Physical Image Offset
     This chunk's contents are:

     4 bytes: image position on the page, X axis (signed integer)
     4 bytes: image position on the page, Y axis (signed integer)
     1 byte: unit specifier

     Both position values are signed. The following values are legal for the
     unit specifier:

     0: unit is the pixel (true dimensions unknown)
     1: unit is the micrometer (also known as the micron; 1/1,000,000th of a meter)

     Conversion note: one inch is equal to exactly 25,400 micrometers.

     This chunk gives the position on a printed page at which the image should
     be output when printed alone. The X position is measured rightwards from
     the left side of the page to the left side of the image; the Y position is
     measured downwards from the top side of the page to the top of the image.

     If present, this chunk must precede the first IDAT chunk.

tIME Image Last-Modification Time
     This chunk's contents are:

     2 bytes: Year (complete; for example, 1995)
     1 byte: Month (1-12)
     1 byte: Day (1-31)
     1 byte: Hour (0-23)
     1 byte: Minute (0-59)
     1 byte: Second (0-60)    (yes, 60, for leap seconds; not 61, a common error)

     This chunk gives the time of the last image modification. Universal Time
     (UTC, also called GMT) should be specified rather than local time.

Summary of Standard Chunks

This table summarizes some properties of the standard chunk types.

Name  Multiple  Ordering constraints
        OK?
IHDR    No      Must be first
PLTE    No      Before IDAT
IDAT    Yes     Multiple IDATs must be consecutive
IEND    No      Must be last
gAMA    No      Before PLTE, IDAT
sBIT    No      Before PLTE, IDAT
cHRM    No      Before PLTE, IDAT
tRNS    No      After PLTE; before IDAT
bKGD    No      After PLTE; before IDAT
hIST    No      After PLTE; before IDAT
tEXt    Yes
zTXt    Yes
pHYs    No      Before IDAT
oFFs    No      Before IDAT
tIME    No

Standard keywords for tEXt and zTXt chunks:

Title            Short (one line) title or caption for image
Author           Name of image's creator
Copyright        Copyright notice
Description      Description of image (possibly long)
Software         Software used to create the image
Disclaimer       Legal disclaimer
Warning          Warning of nature of content
Source           Device used to create the image
Comment          Miscellaneous comment; conversion from GIF comment

5. Deflate/inflate compression specification

This draft proposes use of the inflate/deflate compression scheme, an LZ77
derivative which is used in zip, gzip, pkzip and related programs, because
extensive research has been done supporting its patent-free status. Inflate and
deflate code is available in the zip/unzip packages with a very permissive
license (yes, permissive enough for commercial purposes, see those packages for
details).

A formal, detailed specification of inflate and deflate is being written at
this time, and will be included in this document when finalized. The current
draft of the inflate/deflate specification is now available by anonymous FTP
from quest.jpl.nasa.gov in the directory /beta/ziplib/.

The compressed data stream will be stored in the Ziplib format, the
specification of which is also being written at this time. The current draft of
the Ziplib specification is also available by anonymous FTP from
quest.jpl.nasa.gov in the directory /beta/ziplib/.

6. Filter algorithms

This chapter describes the pixel filtering algorithms which may be applied in
advance of compression. The purpose of these filters is to prepare the image
data for optimum compression.

PNG defines five basic filtering algorithms, which are given numeric codes as
follows:

Code    Name
0       None
1       Sub
2       Up
3       Average
4       Paeth

The encoder may choose which algorithm to apply on a scanline-by-scanline
basis. In the image data sent to the compression step, each scanline is
preceded by a filter type byte containing the numeric code of the filter
algorithm used for that scanline.

Filtering algorithms are applied to bytes, not to pixels, regardless of the bit
depth or color type of the image. The filtering algorithms work on the byte
sequence formed by a scanline that has been represented as described previously
(Image layout).

When the image is interlaced, each pass of the interlace pattern is treated as
an independent image for filtering purposes. The filters work on the byte
sequences formed by the pixels actually transmitted during a pass, and the
"previous scanline" is the one previously transmitted in the same pass, not the
one adjacent in the complete image. Note that the subimage transmitted in any
one pass is always rectangular, but is of smaller width and/or height than the
complete image.

For all filters, the bytes "to the left of" the first pixel in a scanline must
be treated as being zero. For filters that refer to the prior scanline, the
entire prior scanline must be treated as being zeroes for the first scanline of
an image (or of a pass of an interlaced image).

To reverse the effect of a filter, the decoder must use the decoded values of
the prior pixel on the same line, the pixel immediately above the current pixel
on the prior line, and the pixel just to the left of the pixel above. This
implies that at least one scanline's worth of image data must be stored by the
decoder at all times. Note that although some filter types do not refer to the
prior scanline, the decoder must always store each scanline as it is decoded,
since the next scanline might use a filter that refers to it.

PNG imposes no restriction on which filter types may be applied to an image.
However, the filters are not equally effective on all types of data. See
Recommendations for encoders: Filter selection.

See also Rationale: Filtering.

Filter type 0: None

With the None filter, the scanline is transmitted unmodified; it is only
necessary to insert a filter type byte before the data.

Filter type 1: Sub

The Sub filter transmits the difference between each byte and the value of the
corresponding byte of the prior pixel.

Apply the following formula to each byte of each scanline, where x ranges from
zero to the number of bytes representing that scanline minus one (1), and
Raw(x) refers to the raw data byte at that byte position in the scanline:

Sub(x) = Raw(x) - Raw(x-bpp)

Note this is done for each byte, regardless of bit depth. Unsigned arithmetic
modulo 256 is used, so that both the inputs and outputs fit into bytes. The
sequence of Sub values is transmitted as the filtered scanline.

bpp is defined as the number of bytes per complete pixel, rounding up to one
(1). For example, for color type 2 with a bit depth of 16, bpp is equal to 6
(three channels, two bytes per channel); for color type 0 with a bit depth of
2, bpp is equal to 1 (rounding up); for color type 4 with a bit depth of 16,
bpp is equal to 4 (two-byte grayscale value, plus two-byte alpha channel).

Important: for all x < 0, assume Raw(x) = 0.

To reverse the effect of the Sub filter after decompression, output the
following value:

Sub(x) + Raw(x-bpp)

(computed mod 256), where Raw refers to the bytes already decoded.

Filter type 2: Up

The Up filter is just like the Sub filter except that the pixel immediately
above the current pixel, rather than just to its left, is used as the
predictor.

Apply the following formula to each byte of each scanline, where x ranges from
zero to the number of bytes representing that scanline minus one (1), and
Raw(x) refers to the raw data byte at that byte position in the scanline:

Up(x) = Raw(x) - Prior(x)

where Prior refers to the unfiltered bytes of the prior scanline.

Note this is done for each byte, regardless of bit depth. Unsigned arithmetic
modulo 256 is used, so that both the inputs and outputs fit into bytes. The
sequence of Up values is transmitted as the filtered scanline.

Important: on the first scanline of an image (or of a pass of an interlaced
image), assume Prior(x) = 0 for all x.

To reverse the effect of the Up filter after decompression, output the
following value:

Up(x) + Prior(x)

(computed mod 256), where Prior refers to the decoded bytes of the prior
scanline.

Filter type 3: Average

The Average filter uses the average of the two neighboring pixels (left and
above) to predict the value of a pixel.

Apply the following formula to each byte of each scanline, where x ranges from
zero to the number of bytes representing that scanline minus one (1), and
Raw(x) refers to the raw data byte at that byte position in the scanline:

Average(x) = Raw(x) - floor((Raw(x-bpp)+Prior(x))/2)

where Prior refers to the unfiltered bytes of the prior scanline, and bpp is
defined as for the Sub filter.

Note this is done for each byte, regardless of bit depth. The sequence of
Average values is transmitted as the filtered scanline.

The subtraction of the predicted value from the raw byte must be done modulo
256, so that both the inputs and outputs fit into bytes. However, the sum
Raw(x-bpp)+Prior(x) must be formed without overflow (using at least nine-bit
arithmetic). floor() indicates that the result of the division is rounded to
the next lower integer if fractional; in other words, it is an integer division
or right shift operation.

Important: for all x < 0, assume Raw(x) = 0. On the first scanline of an image
(or of a pass of an interlaced image), assume Prior(x) = 0 for all x.

To reverse the effect of the Average filter after decompression, output the
following value:

Average(x) + floor((Raw(x-bpp)+Prior(x))/2)

where the result is computed mod 256, but the prediction is calculated in the
same way as for encoding. Raw refers to the bytes already decoded, and Prior
refers to the decoded bytes of the prior scanline.

Filter type 4: Paeth

The Paeth filter computes a simple linear function of the three neighboring
pixels (left, above, upper left), then chooses as predictor the neighboring
pixel closest to the computed value. This technique is taken from Alan W.
Paeth's article "Image File Compression Made Easy" in Graphics Gems II, James
Arvo, editor, Academic Press, 1991.

Apply the following formula to each byte of each scanline, where x ranges from
zero to the number of bytes representing that scanline minus one (1), and
Raw(x) refers to the raw data byte at that byte position in the scanline:

Paeth(x) = Raw(x) - PaethPredictor(Raw(x-bpp),Prior(x),Prior(x-bpp))

where Prior refers to the unfiltered bytes of the prior scanline, and bpp is
defined as for the Sub filter.

Note this is done for each byte, regardless of bit depth. Unsigned arithmetic
modulo 256 is used, so that both the inputs and outputs fit into bytes. The
sequence of Paeth values is transmitted as the filtered scanline.

The PaethPredictor function is defined by the following pseudocode:

     function PaethPredictor (a, b, c)
     begin
          ; a = left, b = above, c = upper left
          p := a + b - c        ; initial estimate
          pa := abs(p - a)      ; distances to a, b, c
          pb := abs(p - b)
          pc := abs(p - c)
          ; return nearest of a,b,c,
          ; breaking ties in order a,b,c.
          if pa <= pb AND pa <= pc
          begin
               return a
          end
          if pb <= pc
          begin
               return b
          end
          return c
     end

The calculations within the PaethPredictor function must be performed exactly,
without overflow. Arithmetic modulo 256 is to be used only for the final step
of subtracting the function result from the target pixel value.

Note that the order in which ties are broken is fixed and must not be altered.
The tie break order is: pixel to the left, pixel above, pixel to the upper
left. (This order differs from that given in Paeth's article.)

Important: for all x < 0, assume Raw(x) = 0 and Prior(x) = 0. On the first
scanline of an image (or of a pass of an interlaced image), assume Prior(x) = 0
for all x.

To reverse the effect of the Paeth filter after decompression, output the
following value:

Paeth(x) + PaethPredictor(Raw(x-bpp),Prior(x),Prior(x-bpp))

(computed mod 256), where Raw and Prior refer to bytes already decoded. Exactly
the same PaethPredictor function is used by both encoder and decoder.

7. Multi-image extension

PNG itself is strictly a single-image format. However, it may be necessary to
store multiple images within one file; for example, this is needed to convert
some GIF files. For this purpose, a multi-image format will be defined in the
near future. PNG decoders will not be required to support the multi-image
extension.

8. Recommendations for encoders

This chapter gives some recommendations for encoder behavior. The only absolute
requirement on a PNG encoder is that it produce files which conform to the
format specified in the preceding chapters. However, best results will usually
be achieved by following these recommendations.

Registering proprietary chunks

If you want others outside your organization to understand a chunk type that
you invent, contact the editor of the PNG specification (boutell@netcom.com)
and specify the format of the chunk's data and your preferred chunk type name.
The authors will assign a permanent, unique chunk type name. The chunk type
will be publicly listed in an appendix of extended chunk types which can be
optionally implemented. Note that the creation of new critical chunk types is
discouraged unless absolutely necessary. This process will begin as soon as the
basic specification is finalized. In the event that Mr. Boutell is unable to
maintain the specification, the task will be passed on to a qualified volunteer
or organization.

New proprietary chunks will be only be registered if they are of use to others
and do not violate the design philosophy of PNG. Chunk registration is not
automatic, although it is the intent of the authors that it be straightforward
when a new chunk of potentially wide application in one or several fields is
needed.

If you do not require or desire that others outside your organization
understand the chunk type, you may use a private chunk name by specifying a
lowercase letter for the second character.

Please note that if you want to use a private chunk for information that is not
essential to view the image, and have any desire whatsoever that others not
using your internal viewer software be able to view the image, you should use
an ancillary chunk type (first character is lowercase) rather than a critical
chunk type (first character uppercase).

Also note that others may use the same private chunk name, so it is
advantageous to keep additional identifying information at the beginning of the
chunk data.

If an ancillary chunk is to contain textual information that might be of
interest to a human user, it is recommended that a special chunk type not be
used. Instead use a tEXt chunk and define a suitable keyword. In this way, the
information will be available to users not using your software.

New keywords for tEXt chunks may be registered with the maintainers of the PNG
specification. Keywords should be reasonably self-explanatory.

Bitdepth scaling

When scaling input values with a bit depth that cannot be directly represented
in PNG, an excellent approximation to the correct value can be achieved by
shifting the valid bits to begin in the most significant bit and repeating the
most significant bits into the open bits.

For example, if 5 bits per channel are available in the source data, conversion
to a bitdepth of 8 can be achieved as follows.

If the value for a sample in the source data is 27 (in a range from 0-31), then
the original bits are:

4 3 2 1 0
---------
1 1 0 1 1

Converted to a bitdepth of 8, the best value is 222:

7 6 5 4 3  2 1 0
----------------
1 1 0 1 1  1 1 0
|=======|  |===|
    |      Leftmost Bits Repeated to Fill Open Bits
    |
Original Bits

Note that this scaling can be reversed simply by shifting right.

Scaling by simply shifting left by three bits is incorrect, since the resulting
data would have a range less than the desired full range (continuing the
example, 248 = 11111000 is not full brightness).

It is recommended that the sBIT chunk be included when bitdepth scaling has
been performed, so that decoders will know the original data depth.

Encoder gamma handling

If it is possible for the encoder to determine the image gamma, or to make a
strong guess based on the hardware on which it runs, then the encoder is
strongly encouraged to output the gAMA chunk.

A linear brightness level, expressed as a floating-point value in the range 0
to 1, may be converted to a gamma-corrected pixel value by

  gbright := bright ^ gamma
  pixelval := ROUND(gbright * MAXPIXVAL)

Computer graphics renderers often do not perform gamma encoding, instead making
pixel values directly proportional to scene brightness. This "linear" pixel
encoding is equivalent to gamma encoding with a gamma of 1.0, so graphics
programs that produce linear pixels should always put out a gAMA chunk
specifying a gamma of 1.0.

It is not recommended that encoders attempt to convert supplied images to a
different gamma. Store the data in the file without conversion, and record the
source gamma. Gamma conversion at encode time is a bad idea because gamma
adjustment of digital pixel data is inherently lossy, due to roundoff error (8
or so bits is not really enough accuracy). Thus encode-time conversion
permanently degrades the image. Worse, if the eventual decoder wants the data
with some other gamma, then two conversions occur, each introducing roundoff
error. Better to store the data losslessly and incur at most one conversion
when the image is finally displayed.

Gamma does not apply to alpha channel values; alpha is always represented
linearly.

Alpha channel creation

Encoders should keep in mind the possibility that a viewer will ignore
transparency control. Hence, the colors assigned to transparent pixels should
be reasonable background colors.

For applications that do not require a full alpha channel, or cannot afford the
price in compression efficiency, the tRNS transparency chunk is also available.

If the image has a known background color, this color should be written in the
bKGD chunk. Even viewers that ignore transparency may use the bKGD color to
fill unused screen area.

Filter selection

For images of color type 3 (palette-based color), filter type 0 (none) is
usually the most effective.

Filter type 0 is also recommended for images of bit depths less than 8. For
low-bit-depth grayscale images, it may be a net win to expand the image to
8-bit representation and apply filtering, but this is rare.

For truecolor and grayscale images, any of the five filters may prove the most
effective. If an encoder wishes to use a fixed filter choice, the Paeth filter
is most likely to be the best.

For best compression of truecolor and grayscale images, we recommend an
adaptive filtering approach in which a filter is chosen for each scanline. The
following simple heuristic has performed well in early tests: compute the
output scanline using all five filters, and select the filter which gives the
smallest sum of absolute values of outputs. (Consider the output bytes as
signed differences for this test.) This method usually outperforms any single
fixed filter choice. However, it is likely that much better heuristics will be
found as more experience is gained with PNG.

Filtering according to these recommendations is effective on interlaced as well
as noninterlaced images.

Text chunk processing

If an encoder chooses to support output of zTXt compressed text chunks, it is
recommended that text less than 1K (1024 bytes) in size be output using
uncompressed tEXt chunks. In particular, it is recommended that the basic title
and author keywords be output using uncompressed tEXt chunks. Lengthy
disclaimers, on the other hand, are an ideal candidate for zTXt.

Encoders should discourage the creation of single lines of text longer than 79
characters, in order to facilitate easy reading.

9. Recommendations for decoders

This chapter gives some recommendations for decoder behavior. The only absolute
requirement on a PNG decoder is that it successfully read any file conforming
to the format specified in the preceding chapters. However, best results will
usually be achieved by following these recommendations.

Chunk error checking

Unknown chunk types must be handled as described under Chunk naming
conventions.

It is strongly recommended that decoders verify the CRC on each chunk.

For known-length chunks such as IHDR, decoders should treat an unexpected chunk
length as an error. Future extensions to this specification will not add new
fields to existing chunks; instead, new chunk types will be added to carry any
new information.

Unexpected values in fields of known chunks (for example, an unexpected
compression type in the IHDR chunk) should be checked for and treated as
errors.

Pixel dimensions

Non-square pixels can be represented (see the pHYs chunk), but viewers are not
required to account for them; a viewer may present any PNG file as though its
pixels are square.

Conversely, viewers running on display hardware with non-square pixels are
strongly encouraged to rescale images for proper display.

Truecolor image handling

To achieve PNG's goal of universal interchangeability, decoders are required to
accept all types of PNG image: palette, truecolor, and grayscale. Viewers
running on palette-mapped display hardware need to be able to reduce truecolor
images to palette form for viewing. This process is usually called "color
quantization".

A simple, fast way of doing this is to reduce the image to a fixed palette.
Palettes with uniform color spacing ("color cubes") are usually used to
minimize the per-pixel computation. For photograph-like images, dithering is
recommended to avoid ugly contours in what should be smooth gradients; however,
dithering introduces graininess which may be objectionable.

The quality of rendering can be improved substantially by using a palette
chosen specifically for the image, since a color cube usually has numerous
entries that are unused in any particular image. This approach requires more
work, first in choosing the palette, and second in mapping individual pixels to
the closest available color. PNG allows the encoder to supply a suggested
palette in a PLTE chunk, but not all encoders will do so, and the suggested
palette may be unsuitable in any case (it may have too many or too few colors).
High-quality viewers will therefore need to have a palette selection routine at
hand. A large lookup table is usually the most feasible way of mapping
individual pixels to palette entries with adequate speed.

Numerous implementations of color quantization are available. The PNG reference
implementation will include code for the purpose.

Decoder gamma handling

To produce correct tone reproduction, a good image display program must take
into account the gammas of both the image file and the display device. This can
be done by calculating

  gbright := pixelval / MAXPIXVAL
  bright := gbright ^ (1.0 / file_gamma)
  gcvideo := bright ^ (1.0 / display_gamma)
  fbval := ROUND(gcvideo * MAXFBVAL)

where MAXPIXVAL is the maximum pixel value in the file (255 for 8-bit, 65535
for 16-bit, etc), MAXFBVAL is the maximum value of a frame buffer pixel (255
for 8-bit, 31 for 5-bit, etc), pixelval is the value of the pixel in the PNG
file, and fbval is the value to write into the frame buffer. The first line
converts from pixel code into a normalized 0 to 1 floating point value, the
second undoes the encoding of the image file to produce a linear brightness
value, the third line pre-corrects for the monitor's gamma response, and the
fourth converts to an integer frame buffer pixel. In practice the second and
third lines are merged into

  gcvideo := gbright ^ (1.0 / (file_gamma * display_gamma))

so as to perform only one power calculation.

(Note that this assumes that you want the final image to have a gamma of 1.0
relative to the original scene. Sometimes it looks better to make the overall
gamma a bit higher, perhaps 1.25. To get this, replace the first "1.0" in the
formula above with "desired_system_gamma".)

It is not necessary to perform transcendental math for every pixel! Instead,
compute a lookup table that gives the correct output value for every pixel
value. This requires only 256 calculations per image (for 8-bit accuracy), not
one calculation per pixel. For palette-based images, a one-time correction of
the palette is sufficient.

In some cases even computing a gamma lookup table may be a concern. In these
cases, viewers are encouraged to have precomputed gamma correction tables for
file_gamma values of 1.0 and 0.45 and some reasonable single display_gamma
value, and to use the table closest to the gamma indicated in the file. This
will produce acceptable results for the majority of real files.

In practice, it is often difficult to determine the gamma of the actual
display. It is common to assume a display gamma of 2.2 (or 1.0, on hardware for
which this value is common) and allow the user to modify this value at their
option.

Similarly, when the incoming image has unknown gamma (no gAMA chunk), choose a
likely default value, but allow the user to select a new one if the result
proves too dark or too light.

Finally, note that the response of real displays is actually more complex than
can be described by a single number (display_gamma). If actual measurements of
the monitor's light output as a function of voltage input are available, the
third and fourth lines of the computation above may be replaced by a lookup in
these measurements, to find the actual frame buffer value that most nearly
gives the desired brightness.

Alpha channel processing

In the most general case, the alpha channel can be used to composite a
foreground image against a background image; the PNG file defines the
foreground image and the transparency mask, but not the background image.
Decoders are not required to support this most general case, and most likely,
few will. It is expected that most will be able to support compositing with a
single background color, however.

Viewers which cannot blend colors smoothly with the background should interpret
all nonzero alpha values as fully opaque (no background). This case is
reasonably simple to implement: transparent pixels are replaced by the
background color, others are unchanged.

If a viewer has no particular background against which to present an image, it
may ignore the alpha channel or tRNS chunk. (But alpha channel values must
still be properly skipped over when reading the image data.)

However, if the background color has been set with the bKGD chunk, the alpha
channel can be meaningfully interpreted with respect to it even in a standalone
image viewer.

Background color

Viewers which have a specific background against which to present the image
will ignore the bKGD chunk, but viewers with no preset background color may
choose to honor it. The background color will typically be used to fill unused
screen space, as well as any transparent pixels. If no bKGD chunk is present,
the viewer must make its own decision about a suitable background color.

Palette histogram usage

If the viewer is only short a few colors, it is usually adequate to drop the
least-used colors from the palette. To reduce the number of colors
substantially, it's best to choose entirely new representative colors, rather
than trying to use a subset of the existing palette. This amounts to performing
a new color quantization step; however, the existing palette and histogram can
be used as the input data, thus avoiding a scan of the image data.

If no histogram chunk is provided, a decoder can of course develop its own, at
the cost of an extra pass over the image data.

Text chunk processing

If practical, decoders should have a way to display to the user all tEXt and
zTXt chunks found in the file. Even if the decoder does not recognize a
particular text keyword, the user may well be able to understand it.

Decoders should be prepared to display text chunks which contain any number of
printing characters between newline characters, even though encoders are
encouraged to avoid creating lines in excess of 79 characters.

10. Appendix: Rationale

(This appendix is not part of the formal PNG specification.)

This appendix gives the reasoning behind some of the design decisions in PNG.
Many of these decisions were the subject of considerable debate. The authors
freely admit that another group might have made different decisions; however,
we believe that our choices are defensible and consistent.

Why a new file format?

Does the world really need yet another graphics format? We believe so. GIF is
no longer freely usable, but no other commonly used format can directly replace
it, as is discussed in more detail below. We might have used an adaptation of
an existing format, for example GIF with an unpatented compression scheme. But
this would require new code anyway; it would not be all that much easier to
implement than a whole new file format. (PNG is deliberately designed so that
it is very simple to implement, with the exception of the compression engine,
which would be needed in any case.) We feel that this is an excellent
opportunity to design a new format that fixes some of the known limitations of
GIF.

Why these features?

The features chosen for PNG are intended to address the needs of applications
that previously used the special strengths of GIF. In particular, GIF is well
adapted for on-line communications because of its streamability and progressive
display capability. PNG shares those attributes.

We have also addressed some of the widely known shortcomings of GIF. In
particular, PNG supports truecolor images. We know of no widely used image
format that losslessly compresses truecolor images as effectively as PNG does.
We hope that PNG will make use of truecolor images more practical and
widespread.

Some form of transparency control is desirable for applications in which images
are displayed against a background or together with other images. GIF provided
a simple transparent-color specification for this purpose. PNG supports a full
alpha channel as well as transparent-color specifications. This allows both
highly flexible transparency and compression efficiency.

Robustness against transmission errors has been an important consideration. For
example, images transferred across Internet are often mistakenly processed as
text, leading to file corruption. PNG is designed so that such errors can be
detected quickly and reliably.

PNG has been expressly designed not to be completely dependent on a single
compression technique. Although inflate/deflate compression is mentioned in
this document, PNG would still exist without it.

Why not these features?

Some features have been deliberately omitted from PNG. These choices were made
to simplify implementation of PNG, promote portability and interchangeability,
and make the format as simple and foolproof as possible for users. In
particular:

   *  There is no uncompressed variant of PNG. This would merely create another
     case for decoders to worry about, and it would make the format appear more
     complex for users. ("Why did my 60K file suddenly become 300K?")
   *  There is no lossy compression in PNG. Existing formats such as JFIF
     already handle lossy compression well. Furthermore, available lossy
     compression methods (eg, JPEG) are far from foolproof to use --- a poor
     choice of quality level can ruin an image. To avoid user confusion and
     unintentional loss of information, we feel it is best to keep lossy and
     lossless formats strictly separate. Also, lossy compression is complex to
     implement. Adding JPEG support to a PNG decoder might increase its size by
     an order of magnitude. This would certainly cause some decoders to omit
     support for the feature, which would destroy our goal of
     interchangeability.
   *  There is no support for CMYK or other unusual color spaces. Again, this
     is in the name of promoting portability. CMYK, in particular, is far too
     device-dependent to be useful as a portable image representation.
   *  There is no standard chunk for thumbnail views of images. In discussions
     with software vendors who use thumbnails in their products, it has become
     clear that most would not use a "standard" thumbnail chunk. This is partly
     because every vendor has a distinct idea of what the dimensions and
     characteristics of a thumbnail should be, and partly because vendors who
     keep thumbnails in separate files to accommodate varied image formats are
     not going to stop doing that simply because of a thumbnail chunk in one
     new format. Proprietary chunks containing vendor-specific thumbnails
     appear to be more practical than a common thumbnail format.

It is worth noting that private extensions to PNG could easily add these
features. We will not, however, admit them as part of the basic PNG standard.

Basic PNG also does not support multiple images in one file. This restriction
is a reflection of the reality that many applications do not need and will not
support multiple images per file. (While the GIF standard nominally allows
multiple images per file, few applications actually support it.) In any case,
single images are a fundamentally different sort of object from sequences of
images. Rather than make false promises of interchangeability, we have drawn a
clear distinction between single-image and multi-image formats. PNG is a
single-image format.

Why not use format XYZ?

Numerous existing formats were considered before deciding to develop PNG. None
could meet the requirements we felt were important for PNG.

GIF is no longer suitable as a universal standard because of legal
entanglements. Although just replacing GIF's compression method would avoid
that problem, GIF does not support truecolor images, alpha channels, or gamma
correction. The spec has more subtle problems too. Only a small subset of the
GIF89 spec is actually portable across a variety of implementations, but there
is no codification of the most portable part of the spec.

TIFF is far too complex to meet our goals of simplicity and interchangeability.
Defining a TIFF subset would meet that objection, but would frustrate users
making the reasonable assumption that a file saved as TIFF from Software XYZ
would load into a program supporting our flavor of TIFF. Furthermore, TIFF is
not designed for stream processing, has no provision for progressive display,
and does not currently provide any good, legally unencumbered, lossless
compression method.

IFF has also been suggested, but is not suitable in detail: available image
representations are too machine-specific or not adequately compressed. The
overall "chunk" structure of IFF is a useful concept which PNG has liberally
borrowed from, but we did not attempt to be bit-for-bit compatible with IFF
chunk structure. Again this is due to detailed issues, notably the fact that
IFF FORMs are not designed to be serially writable.

Lossless JPEG is not suitable because it does not provide for the storage of
palette-color images. Furthermore, its lossless truecolor compression is often
inferior to that of PNG.

Byte order

It has been asked why PNG uses network byte order. We have selected one byte
ordering and used it consistently. Which order in particular is of little
relevance, but network byte order has the advantage that routines to convert to
and from it are already available on any platform that supports TCP/IP
networking, including all PC platforms. The functions are trivial and will be
included in the reference implementation.

Interlacing

PNG's two-dimensional interlacing scheme is slightly more complex to implement
than GIF's line-wise interlacing. It also costs a little more in file size.
However, it yields an initial image eight times faster than GIF (the first pass
transmits only 1/64th of the pixels, compared to 1/8th for GIF). Although this
initial image is coarse, it is useful in many situations. For example, if the
image is a World Wide Web imagemap which the user has seen before, PNG's first
pass is enough to determine where to click. The PNG scheme also looks better
than GIF's, because horizontal and vertical resolution never differ by more
than a factor of two; this avoids the odd "stretched" look seen when interlaced
GIFs are filled in by replicating scanlines.

Why gamma correction?

Although gamma 1.0 (linear brightness response) might seem a natural standard,
it is common for images to have a gamma of less than 1. There are two good
reasons for this:

   *  CRT hardware typically has a gamma between 2 and 3. Hence, "gamma
     correction" is a standard part of all video signals. The transmitted image
     usually has a gamma of 0.45 (NTSC) or 0.36 (PAL/SECAM), so images obtained
     by frame-grabbing video already have this value of gamma.
   *  An image gamma less than 1 allocates more of the available pixel codes or
     voltage range to darker areas of the image. This allows
     photographic-quality images to be stored in only 24 bits/pixel without
     banding artifacts in the darker areas (in most cases). This makes "gamma
     encoding" a much better way of storing digital images than the simpler
     linear encoding.

In practice, image gamma values around 1.0 and around 0.45 are both widely
found. Older image standards such as GIF often do not account for this fact,
leading to widespread problems with images coming out too dark or too light.

PNG expects viewers to compensate for image gamma at the time that the image is
displayed. Another possible approach is to expect encoders to convert all
images to a uniform gamma at encoding time. While that method would speed
viewers slightly, it has fundamental flaws:

   *  Gamma correction is inherently lossy due to roundoff error. Requiring
     conversion at encoding time thus causes irreversible loss. Since PNG is
     intended to be a lossless storage format, this is undesirable; we should
     store unmodified source data.
   *  The encoder might not know the image gamma. If the decoder does gamma
     correction at viewing time, it can adjust the gamma (correct the displayed
     brightness) in response to feedback from a human user. The encoder has no
     such option.
   *  Whatever "standard" gamma we settled on would be wrong for some displays.
     Hence viewers would still need gamma correction capability.

Since there will always be images with no gamma or an incorrect recorded gamma,
good viewers will need to incorporate gamma correction logic anyway. Gamma
correction at viewing time is thus the right way to go.

Filtering

PNG includes filtering capability because filtering can significantly reduce
the compressed size of truecolor and grayscale images. Filtering is also
sometimes of value on palette images, although this is less common.

The filter algorithms are defined to operate on bytes, rather than pixels, for
simplicity and speed. Tests have shown that filtering is ineffective for images
with fewer than 8 bits per pixel. The filters will most often be used on
8-bit-precision data.

A final reason for not using pixel-based filtering is that if an 8-bit decoder
plans to discard the low order byte of 16-bit data, it can do so before
reversing the filter, boosting decoder speed.

The encoder is allowed to change filters for each new scanline. This creates no
additional complexity for decoders, since a decoder is required to contain
unfiltering logic for every filter type anyway. The only cost is an extra byte
per scanline in the pre-compression data stream. Our tests showed that when the
same filter is selected for all scanlines, this extra byte compresses away to
almost nothing, so there is little storage cost compared to a fixed filter
specified for the whole image. And the potential benefits of adaptive filtering
are too great to ignore. Even with the simplistic filter-choice heuristics so
far discovered, adaptive filtering usually outperforms fixed filters. In
particular, an adaptive filter can change behavior for successive passes of an
interlaced image; a fixed filter cannot.

The basic filters offered by PNG have been chosen on both theoretical and
experimental grounds. In particular, it is worth noting that all the filters
(except "none" and "average") operate by encoding the difference between a
pixel and one of its neighboring pixels. This is usually superior to
conventional linear prediction equations because the prediction is certain to
be one of the possible pixel values. When the source data is not full depth
(such as 5-bit data scaled up to 8-bit depth), this restriction ensures that
the number of prediction delta values is no more than the number of distinct
pixel values present in the source data. A linear equation can produce
intermediate values not actually present in the source data, and thus reduce
compression efficiency.

Text strings

Most graphics file formats include the ability to store some textual
information along with the image. But many applications need more than that:
they want to be able to store several identifiable pieces of text. For example,
a database using PNG files to store medical X-rays would likely want to include
patient's name, doctor's name, etc. A simple way to do this in PNG would be to
invent new proprietary chunks holding text. The disadvantage of such an
approach is that other applications would have no idea what was in those
chunks, and would simply ignore them. Instead, we recommend that text
information be stored in standard tEXt chunks with suitable keywords. Use of
tEXt tells any PNG viewer that the chunk contains text that may be of interest
to a human user. Thus, a person looking at the file with another viewer will
still be able to see the text, and even understand what it is if the keywords
are reasonably self-explanatory. (For the same reason, we recommend spelled-out
keywords, not abbreviations that will be hard for a person to understand.
Saving a few bytes on a keyword is false economy.)

The ISO 8859-1 (Latin-1) character set was chosen as a compromise between
functionality and portability. Some platforms cannot display anything more than
7-bit ASCII characters, while others can handle characters beyond the Latin-1
set. We felt that Latin-1 represents a widely useful and reasonably portable
character set.

There is at present no provision for text employing character sets other than
the ISO 8859-1 (Latin-1) character set. It is recognized that the need for
other character sets will increase. However, PNG already requires that
programmers implement a number of new and unfamiliar features, and text
representation is not PNG's primary purpose. Since PNG provides for the
creation and public registration of new ancillary chunks of general interest,
it is expected that chunks for other character sets, such as Unicode, will be
registered and increase gradually in popularity.

PNG file signature

The first eight bytes of a PNG file always contain the following values:

(decimal)         137  80  78  71  13  10  26  10
(hex)              89  50  4e  47  0d  0a  1a  0a
(C notation)     \211   P   N   G  \r  \n \032 \n

The first two bytes distinguish PNG files on systems that expect the first two
bytes to identify the file type uniquely. The first byte is chosen as a
non-ASCII value to reduce the probability that a text file may be misrecognized
as a PNG file; also, it catches bad file transfers that clear bit 7. Bytes two
through four (overlap with the first two intentional) name the format. The
CR-LF sequence catches bad file transfers that alter these characters. The
control-Z character stops file display under MSDOS. The final line feed checks
for the inverse of the CR-LF translation problem.

Note that there is no version number in the signature, nor indeed anywhere in
the file. This is intentional: the chunk mechanism provides a better, more
flexible way to handle format extensions, as is described below.

Chunk layout

The chunk design allows decoders to skip unrecognized or uninteresting chunks:
it is simply necessary to skip the appropriate number of bytes, as determined
from the length field.

Limiting chunk length to (2^31)-1 bytes avoids possible problems for
implementations that cannot conveniently handle 4-byte unsigned values. In
practice, chunks will usually be much shorter than that anyway.

A separate CRC is provided for each chunk in order to detect badly-transferred
images as quickly as possible. In particular, critical data such as the image
dimensions can be validated before being used. The chunk length is excluded in
order to permit CRC calculation while data is generated (possibly before the
length is known, in the case of variable-length chunks); this may avoid an
extra pass over the data. Excluding the length from the CRC does not create any
extra risk of failing to discover file corruption, since if the length is
wrong, the CRC check will fail (the CRC will be computed on the wrong bytes and
tested against the wrong value from the file besides).

Chunk naming conventions

The chunk naming conventions allow safe, flexible extension of the PNG format.
This mechanism is much better than a format version number, because it works on
a feature-by-feature basis rather than being an overall indicator. Decoders can
process newer files if and only if the files use no unknown critical features
(as indicated by finding unknown critical chunks). Unknown ancillary chunks can
be safely ignored. Experience has shown that version numbers tend to be set
unnecessarily high, leading to older decoders rejecting files that they could
in fact process (this was a serious problem for several years after the GIF89
spec came out, for example). Furthermore, private extensions can be either
critical or ancillary, and standard decoders will react appropriately; version
numbers are no help for private extensions.

A hypothetical chunk for vector graphics would be a critical chunk, since if
ignored, important parts of the intended image would be missing. A chunk
carrying the Mandelbrot set coordinates for a fractal image would be ancillary,
since other applications could display the image without understanding what it
was. In general, a chunk type should be made critical only if it is impossible
to display a reasonable representation of the intended image without
interpreting that chunk.

The public/private property bit ensures that any newly defined public chunk
types cannot conflict with proprietary chunks that may be in use somewhere.
However, it does not protect users of private chunks from the possibility that
someone else may re-use the same chunk name for a different purpose. It is a
good idea to put additional identifying information at the start of the data
for any private chunk type.

When a PNG file is modified, certain ancillary chunks may need to be changed to
reflect changes in other chunks. For example, a histogram chunk needs to be
changed if the image data changes. If the encoder does not recognize histogram
chunks, copying them blindly to a new output file is incorrect; such chunks
should be dropped. The safe/unsafe property bit allows ancillary chunks to be
marked appropriately.

Not all possible modification scenarios are covered by the safe/unsafe
semantics; in particular, chunks that are dependent on the total file contents
are not supported. (An example of such a chunk is an index of IDAT chunk
locations within the file: adding a comment chunk would inadvertently break the
index.) Definition of such chunks is discouraged. If absolutely necessary for a
particular application, such chunks may be made critical chunks, with
consequent loss of portability to other applications. In general, ancillary
chunks may depend on critical chunks but not on other ancillary chunks. It is
expected that mutually dependent information should be put into a single chunk.

In some situations it may be unavoidable to make one ancillary chunk dependent
on another. Although the chunk property bits do not allow this case to be
represented, a simple solution is available: in the dependent chunk, record the
CRC of the chunk depended on. It can then be determined whether that chunk has
been changed by some other program.

The same technique may be useful for other purposes. For example, if a program
relies on the palette being in a particular order, it may store a private chunk
containing the CRC of the PLTE chunk. If this value matches when the file is
again read in, then it provides high confidence that the palette has not been
tampered with. Note that it is not necessary to mark the private chunk
unsafe-to-copy.

Palette histograms

A viewer may not be able to provide as many colors as are listed in the image's
palette. (For example, some colors may be reserved by a window system.) To
produce the best results in this situation, it is helpful to have information
on the frequency with which each palette index actually appears, in order to
choose the best palette for dithering or drop the least-used colors. Since
images are often created once and viewed many times, it makes sense to
calculate this information in the encoder, although it is not mandatory for the
encoder to provide it.

The same rationale holds good for palettes which are suggested quantizations of
truecolor images. In this situation, it is recommended that the histogram
values represent "nearest neighbor" counts, that is, the approximate usage of
each palette entry if no dithering is applied. (These counts will often be
available for free as a consequence of developing the suggested palette.)

11. Appendix: Sample CRC Code

The following sample code represents a practical implementation of the CRC
(Cyclic Redundancy Check) employed in PNG chunks.

The sample code provided is in the C programming language. (See also ISO 3309
and ITU-T V.42 for a formal specification.)

/* table of crc's of all 8-bit messages */
unsigned long crc_table[256];

/* Flag: has the table been computed? Initially false. */
int crc_table_computed = 0;

/* make the table for a fast crc */
void make_crc_table(void)

  unsigned long c;
  int n, k;

  for (n = 0; n < 256; n++)
  {
    c = (unsigned long)n;
    for (k = 0; k < 8; k++)
      c = c & 1 ? 0xedb88320L ^ (c >> 1) : c >> 1;
    crc_table[n] = c;
  }
  crc_table_computed = 1;


/* update a running crc with the bytes buf[0..len-1]--the crc should be
   initialized to all 1's, and the transmitted value is the 1's complement
   of the final running crc (see the crc() routine below)). */

unsigned long update_crc(unsigned long crc, unsigned char *buf, int len)

  unsigned long c = crc;
  unsigned char *p = buf;
  int n = len;

  if (!crc_table_computed) {
    make_crc_table();
  }
  if (n > 0) do {
    c = crc_table[(c ^ (*p++)) & 0xff] ^ (c >> 8);
  } while (--n);
  return c;


/* return the crc of the bytes buf[0..len-1] */
unsigned long crc(unsigned char *buf, int len)

  if (!crc_table_computed) {
    make_crc_table();
  }
  return ~update_crc(0xffffffffL, buf, len);


12. Credits

Editor:

Thomas Boutell, boutell@netcom.com

Contributing Editor:

Tom Lane, tgl@sss.pgh.pa.us

Authors:

Authors' names are presented in alphabetical order.

   * Mark Adler, madler@cco.caltech.edu
   * Thomas Boutell, boutell@netcom.com
   * Adam M. Costello, amc@cs.wustl.edu
   * Lee Daniel Crocker, lee@piclab.com
   * Oliver Fromme, fromme@rz.tu-clausthal.de
   * Jean-Loup Gailly, jloup@chorus.fr
   * Alex Jakulin, alex@hermes.si
   * Neal Kettler, kettler@cs.colostate.edu
   * Tom Lane, tgl@sss.pgh.pa.us
   * Dave Martindale, davem@cs.ubc.ca
   * Owen Mortensen, ojm@csi.compuserve.com
   * Glenn Randers-Pehrson, glennrp@ARL.MIL
   * Greg Roelofs, newt@uchicago.edu
   * Paul Schmidt, photodex@netcom.com
   * Jeremy Wohl, jeremy@cs.sunysb.edu

The authors wish to acknowledge the contributions of the Portable Network
Graphics mailing list and the readers of comp.graphics.

End of PNG Specification