SimpTerm - V1.00 
 
                           Simple Terminal Emulator  
 
 
 
 
                    Copyright 1995, B&B Electronics Mfg Co  
                                  PO Box 1040  
                                 707 Dayton Rd 
                               Ottawa, IL 61350  
                                release: 3/9/95  
 



                               




1.0  General Information 
     1.1   Disclaimer of Warranty 
     1.2   License 
     1.3   Introduction 
 
2.0  Screen Layout 
     2.1   Main Menu 
     2.2   Terminal Screen(s) 
     2.3   Setup Window 
     2.4   Handshake Line 
 
3.0  Users Guide 
     3.1   Port Menu 
           3.11   Port | Open 
           3.12   Port | Close 
           3.13   Port | Setup 
           3.14   Port | Change 
           3.15   Port | Copy Settings 
           3.16   Port | Summary 
           3.17   Port | Exit 
 
     3.2   Control Menu 
 
          3.21  Control | RTS 
          3.22  Control | DTR 
          3.23  Control | Break 
          3.24  Control | Last 
          3.25  Control | FIFO 
          3.26  Control | Clear RX_Buffer 
          3.27  Control | Clear TX_Buffer 
 
     3.3   Options Menu 
 
          3.31  Options | Test Mode 
          3.32  Options | Set Trigger 
          3.33  Options | Monitor Mode 
          3.34  Options | Define String 
          3.35  Options | Log to File 
          3.36  Options | Transmit File 
 
     3.4  Display Menu 
 
          3.41  Display | Clear 
          3.42  Display | Split 
          3.43  Display | Settings 
          3.44  Display | Character 
          3.45  Display | Show/Hide 
          3.46  Display | 43/50 Lines 
 
     3.5  Config Menu 
 
          3.51  Config | Load 
          3.52  Config | Save 
          3.53  Config | Save As 
          3.54  Config | About 



1.0   General Information 
---------------------------------------------------------------------------- 
 
     1.1  Disclaimer of Warranty 
          THIS SOFTWARE AND MANUAL ARE SUPPLIED "AS IS".  B&B ELECTRONICS 
          HEREBY DISCLAIMS ALL WARRANTIES RELATING TO THIS SOFTWARE AND ITS 
          DOCUMENTATION FILE, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED 
          TO DAMAGE TO HARDWARE, SOFTWARE AND/OR DATA FROM USE OF THIS 
          PRODUCT.  IN NO EVENT WILL B&B ELECTRONICS BE LIABLE TO YOU OR 
          ANY OTHER PARTY FOR ANY DAMAGES.  YOUR USE OF THIS SOFTWARE 
          INDICATES THAT YOU HAVE READ AND AGREE TO THESE AND OTHER TERMS 
          INCLUDED IN THIS DOCUMENTATION FILE. 
 
     1.2  License 
          SimpTerm is neither free software nor is it in the public domain. 
          The software and its documentation, this file, are property of 
          B&B Electronics and may not be sold without written permission. 
 
          SimpTerm is distributed as shareware.  This means that you are 
          granted a limited license to use it for a period of 30 days.  If 
          you find it useful and decide to continue using it after the 
          trial period, registration is required. 
 
          Registered users will be granted a just-like-a-book license which 
          means a registered version of the software can be used by more 
          than one person and can be moved from one computer to another so 
          long as there is NO POSSIBILITY of it being used by two different 
          persons on two different computers at the same time, just like a 
          book can not be read by two different persons in two different 
          places at the same time. 
 
          If you register for a license you are eligible for assistance 
          from our tech-support team and will be granted one free upgrade 
          of SimpTerm.  You can register SimpTerm by phone, fax, E-Mail, or
          by mail.  The information is listed below: 
                  PH: 815-434-0846     FAX: 815-434-7094 
                  sales@bb-elec.com    P.O. BOX 1040 - OTTAWA, IL 61350

          You can also register SimpTerm by Compuserve:
                            type: GO SWREG 
             registration number: 5281

     1.3  Introduction 
          SimpTerm is a shareware software package that assists users in 
          solving serial communication problems.  Some of the features 
          included in SimpTerm are the following: 
            * Up to four ports can be opened at a time 
            * Any hardware supported baud rate 
            * RS-232/RS-485 support 
            * Handshaking control 
            * Loop back tests 
            * Triggers 
            * Monitor Mode which monitors communications between a DTE/DCE 
              (requires hardware). 
 


2.0   Screen Layout 
---------------------------------------------------------------------------- 
 
     2.1  Main Menu 
          The Main Menu is located on the top line of the screen.  It allows 
          you to access all the features of SimpTerm.  It is accessed by 
          pressing ALT+"highlight char".  Then the right/left arrow keys are 
          used to move to the next/previous menu while the down/up keys are 
          used to move to the next/previous menu items.  Some of the menu 
          items have a key or key sequence to the right of the option, this 
          is a hot key that can be used at any time to access that menu 
          function. 
 
    2.2   Terminal Screen 
          This is the area where all the characters that are transmitted 
          and received are displayed.  On color monitors the transmit 
          characters are displayed in yellow and the receive in cyan.  On a 
          black and white monitor the transmit characters are displayed in 
          white and the receive in gray.  If an Overrun Error, Parity Error, 
          Framing Error, or Break Interrupt is detected the character will 
          be blinking (see the Handshake Line section).  When a port is 
          in split mode (see Display|Split), a horizontal line will be 
          splitting the terminal screen in which the transmit characters 
          (DTE side) will be displayed in the upper half, and the receive 
          characters (DCE side) will be displayed in the lower half. 
 
          A 45 line ring buffer is maintained for each of the ports opened. 
 
    2.3   Setup Window 
          This window is located on the right side of the Terminal Screen 
          when the Settings option is selected (see Display|Settings).  This 
          is used for a constant reminder of the ports settings. 
 
    2.4   Handshake Line 
          The Handshake Line is located on the bottom of each of the opened 
          ports and is split up into four sections. 
 
          The first is the "DTE:" section.  This section displays the state of 
          the handshakes: DTR - Data Terminal Ready, RTS - Request to send, 
          and BRK - Break. 
 
          The second section is the "DCE:" section.  This 
          section displays the state of:  DSR - Data Set Ready, CTS - Clear 
          to Send, DCD - Data Carrier Detect, and RI - Ring Indicator. 
 
          The third is the state of the error flags.  This displays the 
          state of BRK - Break, OE - Overrun Error, PE - Parity error, and 
          FE - Framing Error.  If one or more of these errors occur on a 
          receive character, the state will be set until the next receive or 
          transmit character is displayed. 
 
          The fourth is the current size of the Transmit "TXB:" and Receive 
          "RXB:" buffers. 
 
          For all of these flags, when the state is found to be "high", the 
          representation characters will be displayed with a gray background 
          with a black foreground, otherwise they will be displayed with a 
          black background and a gray foreground. 




3.0  Users Guide 

     3.1  Port Menu 
 
          3.11  Port | Open 
                Allows the user to open a serial communications port.  An 
                "Address, IRQ, Transmit Buffer Size, and Receive Buffer Size," 
                is required to install a port.  The address is the location of 
                the port, and the IRQ is the interrupt request line the port 
                will be operating under.  Some of the more common address: 
                03F8h, 02F8h, 03E8h, and 02E8h are the usual address for 
                COM1-COM4 respectively, although any address through 3FFh may 
                be specified.  All IRQ's (2-15) are also supported. 
 
                The transmit and receive buffers are used as a temporary 
                holding areas for characters that are waiting to be transmitted 
                and characters that are received before they can be placed on 
                the screen.  The larger the receive buffer the less chance 
                there is to lose characters.  The minimum size of the each of 
                the transmit and receive buffers is 2 characters.  The 
                maximum size has to be less than the following: 
                      (2*Receive Buffer) + (Transmit Buffer)) < 65535. 
 
                When a port is opened, it transmits a NULL to determine if 
                the IRQ is set correctly. 
 
          3.12  Port | Close 
                Allows the user to close an existing port.  Any ports that 
                are left open are automatically resized to fill the screen. 
 
          3.13  Port | Setup 
                This dialog box allows you to set up the communication 
                parameters for the port. 
 
          3.14  Port | Change 
                This allows you to change a ports address, irq, receive 
                buffer size, or transmit buffer size without losing any of 
                the ports triggers, handshake settings, etc. 
 
          3.15  Port | Copy Settings 
                Copys the baud rate, parity, data bits, stop bits, triggers, 
                and all the display settings from one port to another. 
 
          3.16  Port | Summary 
                Shows a summary of the active port.  The address, irq, 
                transmit buffer size, receive buffer size, type of uart, and 
                FIFO trigger level if the UART is a 16550AFN.  The type of 
                UART's that are supported are: 8250 or 8250B, 8250A or 16450, 
                16550, or 16550AFN. 
 
          3.17  Port | Exit 
                Exits SimpTerm.  If a configuration file is open and changes 
                have been made since it has been open, you will be prompted 
                to save the changes before exiting.  If no configuration is 
                open it will just exit. 



     3.2  Control Menu 
 
          3.21  Control | RTS 
                Toggles the state of Request to Send. 
 
          3.22  Control | DTR 
                Toggles the state of Data Terminal Ready. 
 
          3.23  Control | Break 
                Toggles the state of the Break condition.  This condition is 
                caused by holding the transmit data line high. 
 
          3.24  Control | Last 
                Toggles continuous transmit.  The character that is repeated 
                could either be the last character that was typed 
                (transmitted) or a string that was defined and transmitted. 
 
          3.25  Control | FIFO 
                If the UART is a 16550AFN then the FIFO trigger level can be 
                set here.  It is a good idea to only change this when the 
                receive buffer is empty, otherwise characters could be lost. 
 
          3.26  Control | Clear RX_Buffer 
                If there are characters in the Receive Buffer they are 
                cleared.  Also this option is used to clear the receive 
                overflow flag which, when set is displayed on the handshake 
                line as "OF". 
 
          3.27  Control | Clear TX_Buffer 
                If there are characters in the Transmit buffer they are 
                cleared. 
 


     3.3  Options Menu 
 
          3.31  Options | Test Mode 
                Allows you to test a serial port or external device by either 
                looping back on itself pins 2 and 3 (transmit and receive) or 
                by connecting one port to another by configuring one as a DCE 
                device.  If two ports are being used in test mode, then the 
                active port transmits characters while the second port 
                receives. 


          3.32  Options | Set Trigger 
                A trigger is defined as a string that is looked for while a 
                port is receiving characters.  If this string is detected, a 
                second defined string is then transmitted out the port as a 
                reply to the trigger. 
 
                In the Set Trigger dialog box you can enable/disable each 
                of the triggers separately by the check box preceding each of 
                the triggers.  Also, there is a "Enable Port ? Triggers" 
                check box on the bottom of the dialog box that allows you to 
                enable/disable all of the triggers for that port.  This check 
                box does not enable triggers that are disabled by the 
                individual check boxs.  The "Make Global" check box allows 
                all the ports that have there "Enable Port ? Triggers" 
                enabled to use that ports triggers.  This allows the user to 
                set up one set of triggers for all ports open.  The "Trigger" 
                edit boxes contains the strings that a port is going to look 
                for before transmitting its reply.  This string is case 
                sensitive.  The "Reply" check boxes is the string that is 
                automatically transmitted when the "Trigger" is received. 
                Hexadecimal values can be specified in either the "Trigger" 
                or "Reply" edit boxes by placing the value between "<>".  For 
                example to "Reply" a Null you would include: <0> in the 
                "Reply" string. 
 
          3.33  Options | Monitor Mode 
                Allows you to monitor communications between a DTE and DCE. 
                This feature requires an external piece of hardware as well 
                as two ports being open at a time.  This piece of hardware 
                can be purchased from B&B Electronics (model 232MMA) for 
                $34.95, or can be constructed by yourself.  The cable 
                requires the pinouts in diagram  A.1. 




                     DCE Device                            DTE Device
                                     signal direction
                Shield --*-----------------------------*-------------- Shield
                    TD --|--------------------<--------|--*----------- TD
                    RD --|--*----------------->--------|--|----------- RD
                   RTS --|--|-----------------<--------|--|--*-------- RTS
                   CTS --|--|--*-------------->--------|--|--|-------- CTS
                   DSR --|--|--|--*----------->--------|--|--|-------- DSR
                   GND --|--|--|--|--*-----------------|--|--|-----*-- GND
                   DCD --|--|--|--|--|--*----->--------|--|--|-----|-- DCD
                   DTR --|--|--|--|--|--|-----<--------|--|--|--*--|-- DTR
                    RI --|--|--|--|--|--|--*-->--------|--|--|--|--|-- RI
                         |  |  |  |  |  |  |           |  |  |  |  |
                         |  |  |  |  |  |  |           |  |  |  |  |
                         S  R  C  D  G  D  R           S  R  D  D  G
                         H  D  T  S  N  C  I           H  D  S  C  N
                         I     S  R  D  D              I     R  D  D
                         E                             E
                         L                             L
                         D                             D

                                COM A                      COM B

                                        Diagram A.1
                           Pinouts for the Monitor Mode Adapter.

                COM A and COM B connect to the SimpTerm ports that you
                have opened.  COM A monitors the DCE side and COM B monitors
                the DTE side.

                When this mode is started, if two ports are not currently
                open, it prompts you to open a second port.  Then a dialog
                box comes up that looks similar to the following:

                              COM B (DTE)    COM A (DCE)
                              [X] Port 1     [ ] Port 1
                              [ ] Port 2     [X] Port 2


                Here you tell SimpTerm which port will be monitoring the DTE
                side (which is connected to COM B) and which port is going to
                be monitoring the DCE side (which is connected to COM A).
                The number of ports listed in the dialog box will correspond
                to the number of ports you have open.  After you select
                both of the ports you wish to do the monitoring, any leftover
                ports will be closed automatically.

                If either of the two ports selected have a 16550AFN type
                UART you will be prompted to disable the triggers.

                RS-422 communications can also be supported by purchasing
                a 422BOC cable from B&B Electronics for $74.95.

          3.34  Options | Define String
                There are nine hot keys that are available to assign to user
                defined strings.  Here strings can be set up that will be
                transmitted by pressing the hot key assigned to it.
                Hexadecimal numbers can be specified by placing them between
                "<>".  For example to transmit a NULL you could set up one
                string like the following, <0>.

          3.35  Options | Log to File
                This is a toggle switch which allows you to log all data
                transmitted and received to a file.  If the "Character
                Display" (see Display | Character) is defined to be anything
                but character, a "{T}" will be placed in front of the first
                character transmitted after a receive and a "{R}" will be
                placed after the first character received after a transmit.
                If the character mode is selected only the characters
                received and transmitted be be placed in the file.  This
                option can be turned off by selecting it for a second time.

          3.36  Options | Transmit File
                This is a toggle switch that once selected will transmit a
                complete file or will transmit until it is selected again
                which will cancel transmitting.


     3.4  Display Menu

          3.41  Display | Clear
                Clears the current ports screen as well as the display buffer.

          3.42  Display | Split
                Is a toggle switch that splits the current ports screen.
                When the screen is split, all the transmit characters will be
                displayed on the top half of the screen and all the receive
                characters will be displayed on the bottom half.  Otherwise it
                is in full screen mode, where all the transmit and receive
                characters will be combined.

          3.43  Display | Settings
                Turns the display of the port settings on and off.  If
                display port settings is off the terminal screen will expand
                to the full width of the screen.

          3.44  Display | Character
                Allows you to select the character display mode.  There are
                four options, Character, Hex, Decimal, and Mix.  In character
                mode the actual character will be placed on the screen.  In
                Hex, a hexidecimal representation of the character will be
                displayed inbetween "<>".  In decimal a decimal representation
                of the character will be displayed between "<<>>".  In mix mode
                all characters between 32 decimal and 126 decimal will be
                displayed as its character and the rest will be displayed
                between "<>" as a hexidecimal representation.  The check box
                "Change All Ports" located on the bottom of the dialog will
                change the display character for all the ports open.  There
                is also a Display Transmit Characters check box.  When this 
                check box is checked, all transmit characters will be 
                displayed to the screen, otherwise they will not be displayed.

          3.45  Display | Show/Hide
                This option allows you to temporarily hide a port.  This
                feature would be used if you have more than one port open and
                you require more display for a particular port.  When a port
                is hidden, all receive characters will be stored and will be
                displayed when the port is brought back to its visible state.

          3.46  Display | 43/50 Lines
                Toggles between 25 and 43/50 line displays.

     3.5  Config Menu

          3.51  Config | Load
                Loads a configuration file.

          3.52  Config | Save
                Saves a configuration file.  If a configuration is not
                currently open, a dialog box will come up for you to specify
                a name for the file.  The default directory is the directory
                where SimpTerm is located.  If a configuration file is
                currently open it saves the current settings to the file.

          3.53  Config | Save As
                Saves the current configuration file to a user suplied name.
                The default directory is the directory SimpTerm is located in.

          3.54  Config | About
                Displays copyright notice and version number.