REP2APR   Version 1.7

This converter will convert from a PADS-PCB .REP or .PHO aperture file to a 
GraphiCode .APR aperture file.  The converter can be used to convert single 
files or groups of files.

    usage: REP2APR <aperture file> [<outfile>]

    Example:
          To convert the aperture file "ALIST1.REP" for use with GraphiCode 
          products, type:
                REP2APR ALIST1

          This creates the GraphiCode aperture wheel file "ALIST1.APR".


          To convert "ALIST1.REP" to "NEWALIST.APR" type:
                REP2APR ALIST1 NEWALIST

          To convert several aperture files type:
                REP2APR *.REP

        Version 1.7 allows uninitialized shape codes - formerly it would
        stop reading if it encountered a blank shape name.

        Version 1.5 adds the capability to work with PADS 2000
        report files that are in METRIC or INCH rather than the
        default of MILS.  To convert a metric file type:

          To convert a metric file from PADS 2000 type:
                REP2APR MM *.REP

          To convert a inch file from PADS 2000 type:
                REP2APR IN *.REP


        This new version of REP2APR allows the conversion of the 
        aperture list as output by PADS DEFAULTS, PHO-PLOT routine.
        This capability provides for the easy generation of one
        single .APR file for each board loaded in GC-PREVUE. Using
        this approach will make it much easier to load several
        boards in GC-PREVUE even though each board may use many
        different apertures. 

        For different a .APR list for each .PHO type:

        REP2APR filename

        or to do them all at once type:

        REP2APR *.PHO

        This command will convert each PADS .REP file as entered in
        the filename to a GC-PREVUE .APR file (for example, foo.REP 
        creates foo.APR).


        To generate a master GC-PREVUE .APR file for a whole job:


        1. Generate Gerbers for the job so that the batch.dat for
           the job contains all the apertures needed.

        2. Leave PCB (or PADS2000) and then restart the program
           with the printer turned OFF. Restart the program and go into 
           the CAM routine and enter the directory for the job needing 
           the .APR file.

        3. Enter into the DEFAULTS, PHO-PLOT routine. At this point
           you should see the apertures listed for the job, click on
           PROCEED. Answer NO to updating the DEFAULTS.PAD file unless
           you want to store these apertures for use in future jobs.
           Answer YES to PRINT APERTURE LIST?. This will store the
           aperture list in the PCB.ERR (or P2000.ERR) file.
           If you did not turn of your printer the list will just print.

        4. Exit the program and go into the \PADS\FILES directory
           (or use PEDIT for this directory). Examine the .ERR file
           and be sure that the ONLY thing it contains is the aperture
           list output by the DEFAULTS, PHO-PLOT routine. Any other data
           will probably confuse REP2APR. Any aperture positions that
           contain zeros will not cause problems provided that they are
           not BETWEEN positions that are used. Save this file and exit
           the editor.


        5. At the DOS prompt enter:

           REP2APR PCB.ERR filename.APR

           This will generate a .APR file that will contain all the
           apertures needed by this job.
           It is recommended that the file name used for the .APR file
           match that of the job so that it is easy to know what .APR
           goes with which .PHO groups when using GC-PREVUE.
   
Any comments about this converter may be directed to THE SYSOP of the 
GraphiCode BBS (206)771-6980.