PIDSIM
			PID Control Loop Simulator


GENERAL

	 PIDSIM is a program for IBM PC compatibles that simulates PID control
	 loops, including level, pressure, and flow.  Virtually all aspects of
	 a loop's dynamic behavior can be changed to see the effects of white
	 noise, backlash, stiction, tuning, etc on control loop performance.
	 PIDSIM is a great teaching tool for at home study or formal in-plant
	 instruction.


HARDWARE REQUIREMENTS

	 PIDSIM requires an IBM-compatible PC with a VGA display, mouse, and
	 MSDOS 3.3 or higher.  A fast 386 or 486 machine is preferable, but it
	 will run adequately on a 286 or XT class machine. It has been tested
	 under MSDOS 3.3 - 5.0 and OS/2 Warp.


REGISTRATION

	 Please feel free to evaluate PIDSIM and distribute copies of
	 PIDSIM as long as all files are unaltered and distributed
	 together.  If you continue to use PIDSIM you are obligated
	 to register this program by sending a U.S. check or money order
	 for $25 to:

			   CMAR Software
			   RR 1 Box 24k
			   Sheridan, AR 72150

	 Arkansas residents should include 5% sales tax.

	 Upon registration, you will receive the latest version of PIDSIM
	 without the shareware notice.  The registered version of PIDSIM
	 will be licensed to you for single computer system use and may
	 not be distributed in any manner.

	 Please send any comments or suggestions you may have with regard
	 to PIDSIM. If feasible, they may be incorporated in future
	 updates.


 DISCLAIMER

	 Although PIDSIM has been tested extensively and is believed
	 to be free of errors if used correctly, no guarantee is
	 provided.  CMAR Software disclaims all warranties relating
	 to this software, whether express or implied, as to the
	 merchantability or fitness of this program for any purpose.
	 CMAR Software also assumes no liability for any damages,
	 either direct or inconsequential, which may result from use of
	 this program.


INSTALLATION

	 Compressed File - Unzip the file into any convenient location.  Run
	 install.exe to install the program

	 Distribution Disk - run install.exe to install the program


PROGRAM FILES

	 Install.exe - install program
	 Pidsim.exe  - program executable
	 Pidsim.doc  - this documentation file
	 File_id.diz - BBS file description


DEFINITION OF TERMS

	 PID - Proportional, Integral, Derivative

	 Proportional Gain - aka Controller Gain, generates a control
         action proportional to the control error.

	 Integral - (Reset), generates a control action proportional
         to the integral of the control error.

	 Derivative - (Rate), generates a control action proportional
         to the derivative of the control error.

	 Setpoint -  value set by operator which loop should control to.

	 Process Value -  current value of the control loop input

	 Process Output - current value of the control loop output

	 Backlash - a lost response from the process when the direction
         of movement of the actuator changes, due to actuator type, linkage 
         slop, etc.

	 Stiction - a result of static friction. When the actuator has
         been at rest, a certain amount of force is required to overcome
         the static friction, resulting in no movement for small changes in 
         output.

	 White Noise - completely random noise (in this simulation it is
         only as good as the compiler's random number generator, which is 
         never completely random)

	 PID Algorithm - this simulation uses the standard, noninteracting
         or ISA form of the algorithm.

	 Time Constant - the time required for 63.2% of a control action
         to be seen after the process output is stepped, aka tau.

	 Deadtime - a period of time in which no change in process input
         is seen in response to the process output being stepped

	 Open Loop - the controller is not acting on the process input, ie,
         the loop is in manual mode.

	 Closed Loop - the controller is acting on the process input to
         maintain the current setpoint value, ie, automatic mode.

	 Total Settling Time - time required for the process value to
         reach a new steady state after the process output is stepped.

	 Deadband - a specified range around the setpoint within which the
         controller will not change the output.

         Lambda - closed loop time constant

         Process Gain - the ratio of the change in the output to the change
         in the input

         Cut-Off Period - period at which the frequency response starts to
         decay

         Nominal Phase Margin - amount of additional phase lag that can be
         introduced before the system becomes unstable

         Nominal Gain Margin - factor by which the loop gain can increase
         and the loop will remain stable

         Phase Crossover Frequency - frequency at which the phase of the 
         closed loop system is -180 degrees

         Gain Crossover Frequency - frequency at which the gain of the closed
         loop system is unity

         Time to Overflow - seconds required for the tank to overflow at 
         maximum input and zero output from the present level

         Time to Empty - seconds required for the tank to empty at maximum
         output and zero input from the present level


MANIPULATING THE PROGRAM

	 The optional command-line parameters for PIDSIM are as follows:
		PIDSIM {<filename> /H /L /S}
		where:
		  <filename> is a previously saved session file
		  /H displays a command-line help screen
		  /L locks out the setup and autotune buttons
		  /S displays the program serial number (registered version)

         If a previously saved session file named default.dat exists in the
         current directory upon startup, it will be loaded into the program,
         thus allowing the ability to change the program default state.
	 After starting the program, the overview screen is visible, showing
	 the three control loops and valves.  The buttons at the bottom of the
	 screen allow control of the program via the mouse.  You may switch
	 back and forth from the overview to the graphic plots of the
	 individual loops.  To toggle execution of the simulation, press the
	 button labelled Str/Stp.  The rest of the buttons allow changing
	 the individual loop parameters.  The simulation must be stopped to
	 change these parameters.  The parameters to be changed apply to the
	 loop which is currently selected.

	 Loop Button
		change the setpoint, process value, process output, and
		loop status for the currently selected loop

	 Tuning Button
		change proportional gain, integral, derivative and deadband
		values for the currently selected loop

	 Limits Button
		change high and low range values for the setpoint, process
		value, and process output for the currently selected loop.
		set values for hi and lo alarms for current loop

	 Setup Button
		change the following simulation parameters:
		process time constant- sets the time response for the currently
                selected valve

		process deadtime- sets the deadtime for the current loop

		controller rate- defines the rate in seconds used for pid
                control calculations (global setting for all loops)

		simulation rate- actual execution rate of the simulation
                (global for all loops)

		zoom factor- display compression factor for the graphics plot
                (global for all loops)

		valve- selection of control valve for the selected loop.  The
                generic valve types are:
				quick-open
				linear
				parabolic
				equal-percentage
                the user-defined valve allows setting the actual 
                valve response by entering the desired process value 
                for a specific % valve opening

		backlash- defines amount of backlash present in % of output

		stiction- defines amount of stiction present in % of output

		white noise- defines amount of white noise present in % of
                output

		units- the program can be set to allow input of tuning
		parameters in % proportional band or engineering units

		log data- log simulation data to a text file which is
		compatible with the Entech Analyse (c) program.
		Specify the number of points to log and the filename
		of the text file.

		sine wave- injects a sine wave into the input of the currently
		selected loop.  The amplitude and period of the
		sine wave may be adjusted.

		tank volume- change the total tank volume

	 Read Button
		reads in settings from a previously saved simulation session

	 Save Button
		saves current program settings to a session file, do not enter 
                a file extension, as the extension will be forced to .dat

	 LIC1000 Button
		make the level control loop the current loop

	 PIC2000 Button
		make the pressure control loop the current loop

	 FIC3000 Button
		make the flow control loop the current loop

	 Overview Button
		displays the overview graphic

	 Graph Button
		displays the trend plot for the current loop

	 AutoTune Button
		Calculates suggested tuning for the current loop

	 Str/Stp Button
		toggles the simulation on and off

	 Reset Button
		changes all settings to the default startup state


TRADEMARKS

MSDOS is a trademark of Microsoft Corporation

OS/2 WARP is a trademark of International Business Machines

ANALYSE is a trademark of Entech Control Engineering
	   Entech Control Engineering Inc.
	   16 Four Seasons Place
	   Suite 100
	   Toronto, Ontario
	   (416) 626-6908

VERSION CHANGES
	v2.1:
		  first public release

	v2.2:
		  (1)  added ability to inject sine-wave into loop input
		  (2)  fixed bug in loop plot to correctly display values
			   when mouse clicked on plot
		  (3)  changed plotting algorithm to reduce flicker when plot
			   is wrapped at right edge
		  (4)  fixed bug in process deadtime when loop in manual
		  (5)  made pressure loop reverse-acting, which it should have
			   been from the start
		  (6)  added autotune fuction for calculating tuning values
		  (7)  reworked algorithm for modelling level loop, added
			   global parameter for tank volume
		  (8)  added loop parameters for high and low alarms (currently
			   only used for the level loop)

COMMENTS, SUGGESTIONS, BUG REPORTS

	INTERNET      cmarshal@cris.com

	U.S. MAIL     CMAR Software
                      RR 1 Box 24k
                      Sheridan, AR 72150