PC Flt Plan 2.2

                    Computer Flight Planning for DOS

    Copyright (c) 1990-1994 Geir A. Granviken. All rights reserved.

                       D O C U M E N T A T I O N

    ----------------------------------------------------------------
                            C O N T E N T S

    1.   GENERAL

    2.   TERMS FOR USING PC FLT PLAN
         2.1  General
         2.2  Disclaimer of all warranties and liability

    3.   INTRODUCTION
         3.1  About the program
         3.2  Documentation
         3.3  Hardware requirements
         3.4  Files
         3.4  Data entry keys

    4.   INSTALLING

    5.   STARTING PC FLT PLAN

    6.   PREPARING THE PROGRAM FOR USE
         6.1  Configuring
         6.2  Aircraft Data
         6.3  Nav-Database

    7.   HOW TO MAKE A FLIGHT PLAN
         7.1  Data making up a flight plan
         7.2  The Flight Plan Menu
         7.3  Create/Edit a Route

    8.   ROUTE EDITOR
         8.1  Legs
         8.2  Leg data items
         8.3  SID's, approaches etc
         8.4  Alternates
         8.5  Diversion fields
         8.6  Climb-/Descent data
         8.7  Map View

    9.   PRINT/VIEW A FLIGHT PLAN
         9.1  Flight Plan Data
         9.2  Print or Show the flight plan

    10.  ABOUT THE FLIGHT PLAN
         10.1 Leg Times
         10.2 Fuel
         10.3 Corrections
         10.4 How to use the ETO/RTO/ATO fields
         10.5 Vertical Navigation

    11.  COURSE-/DISTANCE COMPUTER

    12.  TERMS & ABBREVIATIONS USED IN THE PROGRAM
    ----------------------------------------------------------------


1.   GENERAL

     PC Flt Plan is a flight planning program for IBM compatible PC's.
     It is run from MS-DOS, or as a DOS program from Windows or OS/2. It
     may be used for VFR or IFR flight planning.

     Consult the included README file for any updates of the information
     in this documentation.

     CREDITS:

     The world map database (named FPLMAP.DTA in this program) was found
     in a public domain mapper program, by Steve R. Sampson, USA, and
     was described as follows: "The database is Micro World Data Bank
     II. It's based on the CIA WDB-II tape available from NTIS. Micro
     WDB-II was created by Micro Doc. Placed in the public domain by
     Fred Pospeschil and Antonio Riveria."

     The original database seems to have 5 resolution levels, where 1 is
     the highest. The file supplied here only covers levels 4 and 5,
     which is very crude on small map areas, but if you are able to
     obtain the original, it should be possible to use it in PC Flt Plan
     (see 8.8.7. for details on the data structure).

     Note: For file size considerations, the map database may not be
     supplied with all BBS versions.

     PC Flt Plan is made by:
     -------------------------------------------------------------------
     Geir A. Granviken                      Phone: (Intl+47) 31 28 55 65
     Norway                         E-mail: geir.granviken@thcave.bbs.no
     -------------------------------------------------------------------


2.   TERMS FOR USING PC FLT PLAN

2.1  General

     The terms for use of this program are found in the text file
     TERMS.DOC. The program may only be used if the user agrees to the
     terms stated in this file.

	     THERE IS NO LIABILITY OR WARRANTY OF ANY KIND.


3.   INTRODUCTION

3.1  About the program

     PC Flt Plan is used to make operational flight plans for VFR or IFR
     flights, - fixed wings or helicopters. (VFR = Visual Flight Rules,
     IFR = Instrument Flight Rules.)

     A flight can be defined to the destination and to one or two
     alternates. In addition, a list of other diversion fields may be
     created.

     The program has a nav-database with lat/long coordinates, magnetic
     variation, elevation and frequencies for airfields, navigational
     aids, intersections or other frequently used waypoints. The data
     included are examples only (they are correct though), but the user
     can enter his own waypoints into the database as he creates or
     edits a route, and in that way build up a database.

     The program also provides a small register where some key data for
     the different aircraft used may be stored.

     The routes created may be saved on disk.

     There are 4 different flight plan printouts to be selected from.
     One of these is a knee-board size flight plan.

3.2  Documentation

     This file makes up the documentation. The program should hopefully
     be fairly easy to use, and if you take a close look at the sample
     routes, it should be possible to make some sense of it. And there
     are no hidden features not shown in the menus or input options.

3.3  Hardware requirements

     - IBM PC/XT/AT/PS2 or compatible.

     - 512 KB RAM.

     - Any display type, but to use the map view function, a VGA, EGA,
       CGA, Olivetti-/AT&T type or Hercules display is required.

     - Hard-disk not required, but the program will work much faster. On
       a floppy disk system, the drive should be at least 720 KB.

     - A disk cache program is recommended but not required.
       SMARTDRV.EXE (or .SYS) which is included with DOS 5.0 and Windows
       is such a cache program, and works very well.

     - To be able to print out all four flight plan variants, the
       printer should be able to print IBM's graphic characters (line
       drawing characters).

3.4  Files

     The list may be slightly different between the sw/demo version and
     the registered disk. A complete list of all files in your current
     version is found in the README file.

     - README       - Text file, General info and last update
     - TERMS.DOC    - Text file, terms for use and distribution
     - FPL22.DOC    - Text file, documentation (This file)
     - PCFPL22.PIF  - Windows 3.1 Program Information File
     - INSTALL.EXE  - Install program (only with reg. version)
     - FPHELP.EXE   - Program to read the text files above
     - FPL.EXE      - Program file, main
     - FPLSETUP.EXE - Program file (normally called from main program)
     - FPL.DTA      - Data file (will be made by program if not present)
     - FPL2.DTA     - Data file ( "   "   "   "     "    "   "     "   )
     - FPLFLY.DTA   - Data file, aircraft data
     - FPL???.PRF   - Data files, a/c performance data
     - FPLMAP.DTA   - Data file, world map coordinates
     - FPLFAC.DTA   - Data file, nav database
     - FPLFAC.IDX   - Data file, nav database
     - FPLFAC.TXT   - Nav database in ASCII text format
     - FPLFIL.DIR   - Route file remarks (used by the program)
     - *.RT?        - Examples, saved routes
     - FPL.REG      - Data file, registration data.

3.4  Data entry keys

     The following keys are used when entering or editing data in input
     boxes throughout PC Flt Plan and the install program:

     - Quit, restoring the old data. <Esc>
     - Toggle Insert on/off......... <Ins>
     - To beginning of line......... <Home>
     - To end of line............... <End>
     - Next field................... <Tab> or <Dn> or <Enter>
     - Previous field............... <Shift><Tab> or <Up>
     - Accept the data and quit..... <Enter> in last field, or
                                     <Ctrl><Enter> in any field

     As in most programs, if you start typing anything in a field where
     the old content is highlighted, the latter will be erased. Use a
     direction key to remove the highlighting if you just want to edit
     the existing data.


4.   INSTALLING

     Note: Disk versions are supplied with an install program. If this
     is used, the instructions below may be disregarded.

     If you have a hard-disk, make a directory and copy the required
     files into this. The program may also be installed on a floppy
     disk. Even if you have a hard-disk, it might be convenient to also
     have the program on a floppy which you can bring with you.

     The files required to run the program are:

             - FPL.EXE              - FPLFAC.DTA
             - FPLSETUP.EXE         - FPLFAC.IDX
             - FPLFLY.DTA
             - FPLnnn.PRF (where "nnn" = "001", "002" etc.)

     The following files should also be copied into the directory if you
     want to see an example of data making up a flight plan:

             - FPL.DTA              - FPL2.DTA

     If these files are not present, they will be made by PC Flt Plan
     during program run. They contain the route and flight plan data
     from the last run.

     If you want to be able to load the sample route files, you should
     also copy the following files:

             - FPLFIL.DIR
             - Files ending with .RTx, where "x" is a number

     If the nav database is not prepared in your copy of the program
     (you will see this by the files FPLFAC.DTA and FPLFAC.IDX missing,
     and that there are no records in the nav database), a file called
     FPLFAC.TXT will be included. In that case you will need to build
     the nav-database from FPLFAC.TXT, - unless you want to make your
     own database. This is done by selecting IMPORT in the Nav-Database
     editor.


5.   STARTING PC FLT PLAN

     Make the disk and directory where the program was installed the
     current directory (i.e. CD C:\FPL), then type FPL <Return>. The
     first time, before you have gone through the configure option, you
     may enter a switch for display type. (This is not necessary if the
     install program was used, as this creates a configuration file with
     the default colour settings for the display type chosen.)

     The switches are:

     - M = Mono display connected to a mono adapter (MDA, Hercules)
     - B = Black & White display connected to a colour adapter
     - C = Colour display and colour adapter.

     To use a switch, type FPL, a space, the switch and then <Return>.
     Example, which starts PC Flt Plan with mono colour settings:

             fpl m<Return>

     FPLSETUP.EXE may be run directly, but is normally called from the
     PC Flt Plan Main menu. If you go through the CONFIGURE option in
     the Setup menu, a configuration file, FPL.CFG, will be created. Do
     not delete this. After you have configured the program, you no
     longer need to use any of the switches, nor will you be asked what
     display type you have on start-up.

     Note: Even if you have configured the program, starting it with a
     display switch will override the settings in your configuration
     file.


6.   PREPARING THE PROGRAM FOR USE

6.1  Configuring

     The first time the program is run, you should go through the
     CONFIGURE option in the Setup menu. When you press <Return>, you
     store the data in the input field and proceed to the next item. If
     you press <Esc>, configuring is terminated and all items are
     restored to their original settings. The various items are
     explained as you work your way through, but if you find any of them
     hard to understand, just leave the item unchanged and press
     <Enter>. None of the items are really required, except the colour
     settings, and maybe the printer codes (if you have problems getting
     the flight plan printed out).

6.2  Aircraft Data

     The next thing you should do, is to enter data for the aircraft you
     will use. This is done with the option AIRCRAFT DATA in the Setup
     menu. You may also specify aircraft data when making a flight plan,
     but it is much more convenient to have it in this little database.

     The aircraft data that can be stored are:

     - AIRCRAFT:  You may do this two ways: You can store the AIRCRAFT
       TYPE, i.e. Cessna 172. Or, if you will operate several different
       aircraft of the same type, you may have one entry for each
       aircraft and instead use the AIRCRAFT REGISTRATION here.

     - REMARKS:  The data here are not used in the flight plans so far,
       but the entry will be shown when you select an aircraft. If you
       have stored the aircraft by registration, you may put the type
       and configuration here.

     - ICAO FLIGHT PLAN NAME:  Not used by the program so far, but the
       entry is reserved for the aircraft code used in ICAO flight
       plans. Example: Cessna 172 is "C172".

     - WEIGHT UNIT:  K=Kg/L=Lbs. All weight data for an aircraft must be
       in the unit you enter here.

     - DRY OPERATING WT:  Aircraft weight, with full oil tanks,
       equipment, catering and crew. Includes everything except Payload
       and Fuel.

     - MAX ZERO FUEL WT:  If applicable. If not, enter 0.

     - MAX TAKE-OFF WT:  Max structural take-off weight.

     - MAX LANDING WT:  If applicable. If not, enter 0.

     - START/TAXI FUEL:  Fuel normally used for start-up and taxi before
       take-off.

     - RESERVE FUEL FLOW:  Fuel consumption rate normally used when
       calculating the reserve required by the flight rules you operate
       under.

     - HOLDING FUEL FLOW:  Fuel consumption rate normally used when
       calculating extra holding, extra reserves, company fuel etc.

     - MAX FUEL CAPACITY:  Max tank capacity, in same unit as all fuel
       flow figures.

     - WEIGHT OF MAX FUEL CAPACITY:  The WEIGHT of MAX CAPACITY above.
       Must be in the same unit as the other weight data. If they are in
       the same unit, lbs for example, you may enter 0.

     - UNUSABLE FUEL:  On some aircraft, some of the fuel in the tanks
       is considered not usable, or there may be a restriction on the
       aircraft not to be operated below a certain fuel level. If so,
       this fuel can not be counted as available fuel when planning a
       flight.

     - ACTUAL FUEL LOAD:  Typical Fuel Load in the same unit as the
       fuel-data above . If Fuel Load varies, you may enter 0, and enter
       the number when making the flight plan.

     - PERFORMANCE DATA:  A separate table for each aircraft that
       contains climb-, cruise- and descent performance for as many
       altitudes as you want.

       - CLIMB:  Average TAS, Fuel burned and Minutes used for climb
         from sea level to the altitudes specified.

       - DESCENT:  Average TAS, Fuel burned and Minutes used for descent
         from altitudes specified to sea level.

       - CRUISE:  TAS and Fuel Flow for the altitudes specified.

     Note: If FUEL FLOW-data and WEIGHT-data are in different units, for
     example gallons and pounds, PC Flt Plan must know the relationship
     between these to be able to calculate landing weights etc. This
     relation is found when the program is given MAX FUEL CAPACITY and
     WEIGHT OF MAX FUEL CAPACITY in their respective units.

6.3  Nav-Database

     GENERAL:
     The Nav-Database is accessed from the Setup menu. This is where
     airfields, navigational aids, intersections and other facilities or
     waypoints are stored. Any frequently used point may be stored here,
     like special check-points, landmarks, oil-rigs - you name it...
     When preparing the program for use, it is a good idea to enter the
     facilities in your local area. You can later add points as you
     create routes, since the route editor allows you to enter data for
     a facility not found in the nav-database, and save it.

     PC Flt Plan performs searches in the database on the facility's
     identifier. It uses an alphabetically sorted index file which is
     maintained automatically whenever records are added, imported or
     deleted.

     If the index file's sort order for some reason should be disturbed,
     the program will still find an existing facility in the nav-
     database manager (considerably slower though), but not in the route
     editor. The REINDEX option will correct this problem however. This
     option rewrites the index file, and can therefore also be used if
     the index file is corrupted or missing.

     DATABASE STRUCTURE:
     The database consists of the files FPLFAC.DTA and FPLFAC.IDX. It is
     strongly recommended to maintain backup copies of these files on a
     separate disk!

     Each facility makes up a record. Each record consists of the
     following fields:

     - IDENT:  Airport 3 or 4 letter code, VOR/NDB identifier, 5 letter
       intersection names etc.

     - TYPE OF FACILITY:  Airfield, VOR, NDB, intersection, VFR
       reporting point etc. Special codes are used, which appear in a
       window whenever needed.

     - NAME:  Name of the facility

     - LATITUDE:   North/South geographical coordinates

     - LONGITUDE:  East/West geographical coordinates

     - MAGNETIC VARIATION 

     - FREQUENCY:  As many airfields may have an array of different
       frequencies, this is mostly intended for nav-aids.

     - ELEVATION:  Only for airfields and heliports.

     IMPORTANT: Commas should not be used in any of the text fields, as
     these are used for separating the fields when exporting to- or
     importing from an ASCII file!

     Note that in most countries, the three letter and four letter
     airfield codes are totally different. The 3 letter codes are those
     used by airlines and their international SITA network, while in
     most countries the 4 letter ICAO codes are used in ATC flight
     plans, notams, weather forecasts etc. USA is a bit special though,
     if you take a 3 letter US airfield code and put a "K" in front of
     it, you have the 4 letter ICAO code. In PC Flt Plan, it is recom-
     mended to use the four letter codes for airfields, to distinguish
     them from the airport VOR's (In the US, the idents are often the
     same).

     Examples:
                               3 letter code    ICAO code
             London/Heathrow        LHR            EGLL
             New York/Kennedy       JFK            KJFK

     For those who want some more technical info: The file (fplfac.dta)
     is a random access file. All ident searches are done in a separate
     index file (fplfac.idx), which contains the idents and pointers to
     the corresponding record in the database file. The alphabetical
     quick search is very fast, even on large databases. Sequential
     search after a failed quick search is initiated only in the Nav-
     database manager, not in the route editor. This is also done in the
     index file.The PACK/REINDEX function completely rewrites the
     database in sorted order, leaving out records marked for deletion,
     and creates a new index file.

     CREATING/EDITING FACILITIES:
     From the Main menu, select SETUP, then select NAV-DATABASE. Here,
     facilities may be viewed, edited, added, listed or written to a
     text file in ASCII format. When you add a new facility, it will be
     placed in it's correct alphabetical position in the index file.
     This may become a bit slow if the database is large, but may be
     turned off in the configuration. If turned off, it will be
     necessary to use the REINDEX option to resort the index file after
     adding new records!

     When a record is deleted, it is not removed from the database, it
     will only be marked for deletion. To recall a deleted record, just
     select DELETE again, and the mark will be removed. To permanently
     remove records marked for deletion, use the PACK/REINDEX option.

     An alternate way to edit the database, is to use the EXPORT
     function (in the Nav-Database menu) to export it to an ASCII file.
     The file is comma delimited, which means that it may be imported
     into and edited in most database- or spreadsheet systems, or simply
     in a text editor. After external editing, use the IMPORT function
     to rebuild the database from the ASCII file. If you have specified
     a text editor in the configuration, you may call this from the
     function EXPORT/IMPORT/EDITOR. Otherwise, you have to leave PC FLT
     Plan, run your editor, then restart PC Flt Plan. The format of the
     ASCII file, necessary to import records correctly, is explained in
     detail in the program.

     ENTERING LAT/LONG & VARIATION WITH THE NUMERIC KEYPAD:

     When entering lat/long coordinates or magnetic variation, PC Flt
     Plan supports the numeric keypad for faster data entry. Instead of
     entering "N" and "E", you may press "+". In the same way, "S" and
     "W" may be replaced by "-". If your numeric keypad has the comma in
     place of the period (.), no worry, the program will translate all
     commas to periods when entering lat/long or variations.

     FUNCTIONS IN THE NAV-DATABASE EDITOR:

     - NEW RECORD:  To add a new facility. The program first asks for
       the identifier, and checks for no others records with the same
       ident.

       If the database covers several countries, you may run into
       duplicate identifiers. A way to handle that is to add the two
       letter ICAO country code. (Some large countries, like USA,
       Canada, Australia and Russia have one letter country codes.
       Except for USA, the second letter then indicates the region
       within the country.) An example: Midhurst VOR in England has the
       identifier "MID". The country code for Great Britain is "EG", so
       the ident may be entered as "MID EG". This will never be
       necessary for airfields however, as long as their 4 letter ICAO
       codes are used.

     - FIND RECORD:  Searches for a facility with a given identifier.

     - SEARCH ON NAME:  Searches the NAME fields, instead of the IDENT
       fields. Will find all records containing the name, or part of a
       name, you specify. For example "okman" will find "Brookmans
       Park".

     - EDIT RECORD:  Change any item in a record. If you change the
       ident, a search for duplicates will be performed.

     - DELETE RECORD:  Deletes the facility presently shown, and
       replaces it with a blank record.

     - LIST RECORDS:  Lists out facilities on screen. If anything is
       entered in the input field which appears, only records with
       identifiers starting with the letters you type will be listed.

     - REINDEX:  Recreates the index file. Use if the index is out of
       sort order, damaged or missing. The database file itself is not
       sorted.

     - PACK/REINDEX:  Will permanently remove all records marked for
       deletion, sort the database file itself, and rebuild the index
       file.

     - EXPORT/IMP./EDITOR:  From here, you may export the database to a
       comma delimited ASCII file, or import from the same. When
       importing, the records may be appended to the existing database,
       or replace the existing database. If an external editor is
       specified in CONFIGURE, this is also accessed from here. See
       below for the ASCII record format. The index file is automat-
       ically sorted after an import.

     - HELP:  A brief help screen.

     - QUIT:  Returns to the Setup menu.

     ASCII RECORD FORMAT FOR EXPORT/IMPORT:

    Ident        Name      Fac   Lat     Long    Var         Freq      Elev
   <------> <-------------> <> <-----> <------> <----> <-------------> <--->
   ZZZZZZZZ,Zzzzzzzzzzzzzzz,ZZ,Yddmm.m,Xdddmm.m,ddd.dX,nnnnnnnnnnnnnnn,nnnnn

     Examples:

   BIRK    ,Reykjavik      ,A ,N6407.9,W02156.3, 21.8W,               ,   45
   OA      ,Asker          ,L ,N5951.0,E01028.1,  0.9W,352            ,
   LAU     ,Lichtenau      ,N ,N5112.3,E00941.5,  0.9W,341            ,
   DANDI EG,               ,I ,N5520.6,E00500.0,  4.4W,D122DHE        ,
   OTR EG  ,Ottringham     ,VD,N5341.9,W00006.1,  5.4W,D113.9         ,

     The lines may be truncated like this if desired:

     BIRK,Reykjavik,A,N6407.9,W02156.3,21.8W,,45
     OA,Asker,L,N5951.0,E01028.1,0.9W,352,


7.   HOW TO MAKE A FLIGHT PLAN

7.1  Data making up a flight plan

     A flight plan is made from two sets of information:

     - ROUTE DESCRIPTION:  The route to be flown from point of depar-
       ture, through several waypoints to the destination, and if
       required, to one or two alternates and/or a list of diversion
       fields. Altitude/flight level and winds are entered for each leg. 
       If you have stored aircraft performance data in the aircraft
       database, true airspeed, fuel burn and vertical speed for climb-,
       cruise- and descent will be inserted automatically. For IFR
       flights, special legs like SID's, approaches etc. may be entered.

     - FLIGHT PLAN DATA: Aircraft (and it's data), reserves, fuel load
       and payload.

       When a route is saved to disk, most of the flight plan data are
       stored together with the route. When you load a route; winds,
       altitudes etc. may be changed quickly for the entire flight
       without having to edit each leg.

     Normally, you will first create the route to be flown, or load a
     previously saved route and make the necessary changes, - and then
     enter the flight plan data. The program takes you through an input
     screen for these data when you select PRINT/VIEW FLIGHT PLAN from
     the Flight Plan menu.

7.2  The Flight Plan Menu

     The Flight Plan Menu is the main "control center" when making a
     flight plan. From here you can perform the following tasks:

     - ROUTE EDITOR:  Create or edit the route to be flown.

     - AIRCRAFT:  Select the aircraft to be used. If the new aircraft
       has a performance file, all legs will be updated with the correct
       data. For manual TAS/ff legs or special legs, the data must be
       updated manually however! You should also go through the
       CLIMB/DESCENT page for an automatic update of climb- & descent
       perfomance.

     - CLIMB/DESCENT (VNAV):  Enter winds for the climb- and descent
       segments, and optionally replace the winds in all legs with a new
       value. Select destination or a waypoint as target for top of
       descent calculation. Note: Also when leaving the route editor,
       you are taken through this screen.

     - GLOBAL CHANGE TAS/WIND/FF:  Change winds, altitude, TAS etc. for
       all or several legs in one operation.

     - SAVE ROUTE:  Save the route and flight plan data to disk.

     - LOAD ROUTE:  Load a previously saved route. When loading, the
       progam will go through an update process. First it tries to look
       up all waypoints in the nav-database and update them if found
       (the index file must be in sort order for this to work). Then,
       all courses and distances are recalculated, in case lat/long or
       variation should have been changed.

     - NEW ROUTE:  Delete the present route from the work area, to
       create a new route.

     - PRINT/VIEW FLIGHT PLAN:  View-, print out- or write to a text
       file the finished flight plan. First takes you through a data
       entry screen for all other information concerning the flight,
       then shows an info screen with summary information along with the
       output menu.

     - MAP VIEW:  Show a graphical representation of the route, and
       optionally all other facilities within the mapped area. If a
       world map database is available, it can show all this on a land
       map.

     - QUIT:  Return to the Main menu.

7.3  Create/Edit a Route

     Select FLIGHT PLAN from the Main menu, this will bring you to the
     Flight Plan menu. To clear the route in the work area, if any, and
     start from scratch; select NEW ROUTE and answer Yes to erase.

     If you want to use a route saved on disk, select LOAD ROUTE, and
     select from the routes shown. Any route present in the work area
     will be deleted when loading a new one. You may edit the loaded
     route in the Route Editor, or you may change FL/Alt, TAS, Wind or
     Fuel Flow globally for all or several legs by selecting GLOBAL
     CHANGE from the Flight Plan menu.


8.   ROUTE EDITOR

8.1  Legs

     Enter the Route Editor from the Flight Plan menu. If an aircraft
     has not been selected for the route, you will be prompted for this
     first. Enter the aircraft directly, or press <F10> to bring up a
     pick list. You may input an aircraft not found in the aircraft
     register, and manually insert all necessary data when making the
     flight plan.

     In the route editor, select ADD LEG to create new legs.

     When some legs have been created, the <Down>, <Up>, <PgDn>, <PgUp>,
     <Home> and <End> keys can be used to move between the legs. Select
     EDIT if you want to make changes. The <Left>, <Right> and <Return>
     keys are used for menu selection.

     If you edit or delete a leg, you will notice a little delay while
     the program goes through all legs to connect the route
     automatically.

     Leg #0 holds the point of departure only. No further data are
     entered for this leg.

8.2  Leg data items

     LEG TYPES:

     - NORMAL:  Straight leg from one point to another. Course &
       distance calculated automatically, based on the lat/long
       coordinates and magnetic variation.

     - MANUAL CRS/DIS:  Straight leg, but course and distance are input
       manually instead of calculated by the program. May be used if
       measuring legs on a map without entering coordinates for the
       checkpoints, or if you want to enter course and distance exactly
       as they appear on an IFR chart.

     - ALTERNATE:  Legs after this make up the route to an alternate (or
       two).

     - DIVERSION LIST:  Legs after this make up a list of optional
       diversion fields. Must appear AFTER the main route legs and
       alternate legs.

     - OTHER:  Used for special legs like approach or SID. Anything may
       be entered in the little text box, like "Appr", "ILS", "STAR",
       "SID" etc.

     TO:

     The point where the leg ends. You enter the facility's identifier,
     and if necessary, the facility type code. The program then searches
     the nav-database. Unless you have two facilities with the same
     identifier (for example an airfield and a VOR), you do not need to
     enter the facility type code. (The codes are shown in the program
     when needed.)

     If the facility is not found in the nav-database, you may enter
     it's data manually. You will then also be asked if you want save it
     to the database.

     If entering facility data manually, the lat/long coordinates may be
     left blank if you want to enter course and distance manually
     instead of letting the program calculate these (See LEG TYPE CODES
     above). This may be useful if you plan a trip where you just pick
     landmarks on the map as waypoints and measure course/ distance with
     a ruler.

     FLIGHT DATA:

     Note: These data are cruise data. TAS, wind etc. for the climb- and
     descent segments will be applied on the legs/part of legs which
     fall into these segments by the program when producing the flight
     plan. Therefore you do not need to worry about climb and descent
     numbers when editing the route. Just start right out with cruise
     altitude, winds, TAS and fuel flow. Exception: Manual TAS & Fuel
     Flow, or special legs (approaches etc.) overrides climb- and cruise
     numbers!

     - FL/ALT:  Flight Level or Altitude. Mandatory if you want PC Flt
       Plan to automatically get TAS and fuel flow from the performance
       data file, and if you want climb-/descent calculations. The
       altitude must be written with an "A", for feet, or "F" for flight
       level, followed by the altitude in hundreds of feet. Examples:
       "F090" = Flight Level 90, "A050" = 5000 feet.

     - WIND:  Wind Direction (what direction the wind comes FROM), and
       Wind Speed in knots.

     - AUTOMATIC-/MANUAL TAS & FUEL FLOW:  To the left of the TAS & Fuel
       flow window is a little window where you enter "A" or "M". "A"
       means automatic mode; TAS and fuel flow will be obtained from the
       aircraft's performance data file, based on the altitude given. If
       you want to specify these data manually, enter an "M". If no
       performance data for the aircraft exist, only manual mode will be
       possible.

     - TAS:  True AirSpeed in knots.

     - F.FLOW:  Fuel consumption per hour.

8.3  SID's, approaches etc. (Mostly IFR-related)

     Since a normal leg is calculated as a straight line between the two
     waypoints, it will be incorrect if a SID or approach involves extra
     turns and manoeuvring (which they usually do). There is a feature
     which allows you to reserve a certain distance or time for such
     cases.

     If you want to start out on a Standard Instrument Departure (SID),
     you put the departure field in leg #0 as usual. In leg #1 you enter
     SID in the LEG TYPE field, and in the TO field you enter where the
     SID ends. After typing in TAS etc., you will be asked for GS, DIST
     and TIME for the SID. You need only enter two of these items. What
     you enter here will not be affected by the TAS and Wind given for
     the leg. But the program uses these data, if given, to tell you
     time and GS if the leg was flown direct. You can then adjust the GS
     and/or time figures as appropriate.

     Similarly, for an instrument approach, you enter "APP", "ILS" or
     whatever you like, except for the reserved codes, in the LEG TYPE
     field and in the TO field enter where the approach terminates
     (usually the airfield...).

     Note: If a SID or approach is just a straight leg (for example a
     straight in approach from a beacon), you may enter the data as for
     any other normal leg, without using the procedure described above.

8.4  Alternates

     When you have reached your destination, you may add legs to an
     alternate (or two), if needed. First you create a leg with an "A"
     as the Leg Type. No further data are entered in a leg with this
     code, it is used as a separation line. In the following legs, the
     route to the alternate is described. If you want a second
     alternate, enter a new leg with the "A" code after reaching the
     first alternate, then specify the route to the second alternate. If
     you have used the code twice, the route will now be divided into
     the following sections:

             - Before any "Alt" leg.... From DEP.FIELD to DESTINATION
             - After first "Alt" leg... From DESTINATION to ALTERNATE 1
             - After second "Alt" leg.. From ALTERNATE 1 to ALTERNATE 2

     (The reason you can have two alternates is that under some regul-
     ations, you can file an IFR flight plan to an airfield which is
     below weather minimums, - provided that you have two alternates.
     The first alternate must then have landing minimums, the second
     must be above alternate minimums.)

8.5  Diversion fields (IFR and VFR)

     In the real world, you sometimes have to change alternate right
     before departure, and you do not have the time to make a new flight
     plan. But this may be prepared for by having a list giving the time
     and fuel burn from the destination to various diversion fields on
     your flight plan. Even if you are flying VFR, such a list may
     become handy.

     A diversion list is created by entering a "D" or "Div" as the Leg
     Type, and a diversion field in each subsequent leg. Note that all
     this MUST be placed after the last leg in the main (and alternate)
     route! Each leg after the one with the code in contains only your
     DESTINATION as the FROM field, and a DIVERSION AIRFIELD in the TO
     field. You enter fuel flow etc. as normal, but note that these
     values should be an average for the entire flight from destination
     to the diversion field. But there is an additional item asked for;
     extra time in minutes for approach etc. This item may also be used
     for adding some extra minutes if the flight cannot be expected to
     be a straight line.

     When this feature is used, the list will appear in the flight plan,
     with time and fuel burn from the destination field to each of the
     optional diversion fields. Also, it will show the total fuel
     required if the airfield is used as the alternate instead of the
     planned alternate(s).

8.6  Climb-/Descent data

     After leaving the route editor, you should select CLIMB/DESCENT
     (VNav). You may also go directly to this from the route editor.
     Here you are taken through a data entry window for climb- and
     descent data. Note however that input for cruise winds will not be
     there when going directly from the route editor, because if
     anything is entered here, it will replace all winds you just
     tediously entered in the single legs....

     The first and last cruising altitudes, as guessed by the program,
     will be shown, but can be changed if incorrect.

     For top of descent calculation, the target for the descent may be
     set by pressing <S> when this button is highlighted. The program
     will calculate where you should start your descent according to
     what you want to aim for. You may select DESTINATION, and
     optionally an altitude above it's field elevation (for example the
     landing pattern altitude), or a WAYPOINT and altitude (in hundreds
     of feet) over this.

     Winds for climb and descent are the average values for these
     segments respectively.

     TAS, Fuel Flow and vertical speed for climb and descent, as
     obtained from the aircraft's performance data file, are displayed
     and may be adjusted manually if desired. If the cruising altitudes
     do not match any in the performance file, the values will be inter-
     polated between those for the nearest altitudes. If no performance
     data exist, the values must be entered manually.

8.7  Map View

     (Selected from the Flight Plan menu or in the Route editor)

     This function requires a graphics display. When you select MAP
     VIEW, you will see a graphical representation of the route and
     waypoints. From the Route Editor, the map will be centred around
     the current waypoint, while from the Flight Plan menu, the map will
     fit the entire route.

     If the program finds a world map database with the name FPLMAP.DTA,
     you may select M to draw a map on the screen. The database included
     only covers resolution levels 4 and 5, where 1 is the highest, so
     it is very crude on a small map area. Even with this resolution, it
     takes time to get the map drawed, since the database covers the
     whole world. Therefore the program is designed so that when you
     select any changes on the map, you will have to press M again to
     have the map redrawed.

     The program does not have graphical printing capability, but if you
     load the DOS program GRAPHICS.COM (which is a resident program)
     before starting PC Flt Plan (and before starting Windows, if used
     from here!), you can print out the display by pressing <Prt Scrn>
     (doesn't work on all printers). Note however that if running from
     Windows, the image will be pasted to the clip board instead (still
     requires GRAPHICS.COM)! Before you press <Prt Scrn>, press P to
     change all the colours to black & white. This also removes the menu
     from the display. To get the colours and menu back, press P again,
     or simply press <ESC> to quit the map display. This is somewhat
     crude of course, but it does work.

     If you are able to obtain a world map database with a higher
     resolution than the one included, it should be in the format of a
     random access file with each records made up by:

     - 1. Integer - Code for res. level and startpoints
     - 2. Integer - Latitude in decimal degrees/minutes times 60
     - 3. Integer - Longitude in decimal degrees/minutes times 60

     Rememeber to name the file FPLMAP.DTA. The original level 1
     database is reported to be around 1 Mb, so it will probably take
     considerable time to have a map drawed!


9.   PRINT/VIEW A FLIGHT PLAN

9.1  Flight Plan Data

     When the route has been defined, you select PRINT/VIEW FLIGHT PLAN
     from the Flight Plan menu. You will then be taken to an input
     screen, where the Flight Plan Data are entered. The following data
     may be entered or changed here:

     - DATE:  Date of flight.

     - FLTNO/CS:  Flight Number or Call-sign.

     - SKED DEP:  Scheduled time of departure (block).

     - SKED ARR:  Scheduled time of arrival.

     - FINAL RESERVE:  Reserve required by the flight regulations you
       operate under. Enter minutes and fuel flow.

     - ROUTE RESERVE:  Additional reserve in PERCENT. If used, the
       amount will be calculated as the specified percent of fuel
       required to destination and to the alternate(s), if any.

     - EXTRA HOLDING:  May be used for expected holding, company fuel or
       similar. Enter minutes and fuel flow.

     - START/TAXI:  Fuel used for start-up and taxi, before take-off.
       The minutes are estimated time from off block to airborne. Will
       be counted when ETA is calculated.

     - UNUSABLE FUEL:  On some aircraft, the last rest of fuel in the
       tanks is considered not usable, and can therefore not be counted
       as available fuel.

     - ACTUAL RAMP FUEL:  Planned fuel load. AMOUNT must be in the same
       unit as the fuel flow figures above. WEIGHT will be calculated
       automatically in relation to what you have specified in the
       aircraft database as weight of max fuel capacity.

     - DRY OPERATING WT:  Aircraft weight, with full oil tanks,
       equipment, catering and crew. Includes everything except payload
       and fuel.

     - ACTUAL PAYLOAD:  Planned payload.

     - FLIGHT PLAN REMARKS:  Two lines of remarks, that, if filled out,
       will be printed on the flight plan.

9.2  Print or Show the flight plan

     When you have entered the Flight Plan Data, a screen with a summary
     of the flight will be shown. From here you may print out the flight
     plan, view it on screen or write it to an ASCII text file.
     Explanation of some of the items showed:

     - TIME:  Airborne time (hr:mins) to destination.

     - BURN:  Start/Taxi-fuel + trip-fuel to destination.

     - DIST:  Distance (NM) to destination. Includes approaches.

     - AVG.WC:  Average wind component to destination (plus=tail-wind,
       minus=head-wind).

     - DEP:  Scheduled Time of Departure (block).

     - ETA:  Estimated Time of Arrival at destination. Taxi time at the
       departure field is counted in.

     - NO WIND:  Burn/Time to destination if there had been no winds.

     - REQUIRED FUEL:  Total fuel required, considering flight to
       destination, alternates(s) (if any), winds, reserves and
       start/taxi.

     - EXTRA FUEL:  The difference between Required fuel and Actual fuel
       load. The time shown is the approximate flight time this represe-
       nts, calculated from the average consumption to destination and
       alternate(s).


     If you have trouble printing out the flight plan, try to find the
     proper printer codes and enter them under the configuration option
     in the Setup menu.

     If this doesn't work, you may try another solution: Select PRINT
     FLIGHT PLAN TO FILE. The file written is in plain ASCII, and may be
     imported into a word processor and printed from here. For the
     "knee-board size", select a font with a pitch of around 17
     characters/inch and normal line height.

     The two A4-variants send only plain ASCII-text to the printer, and
     should therefore be usable on most printers.


10.  ABOUT THE FLIGHT PLAN

10.1 Leg Times

     In the flight plan produced, the time for each leg is rounded up or
     down to the nearest whole minute. But the small difference between
     the accurate leg time and the whole minute is added or subtracted
     to the next leg time. This is the same method used in professional
     flight planning systems used by airlines. The reason for this is
     that on a trip with many legs, the total time may become several
     minutes wrong if for example most of the legs happen to be rounded
     down.

10.2 Fuel

     The fuel amount shown in the last column of the flight plan is the
     remaining fuel you would have over the checkpoint if you departed
     with the TOTAL FUEL REQUIRED. This way you can see if you have all
     your specified reserves intact along the flight. If you have less
     fuel, you have started to consume your reserve, route reserve or
     extra holding fuel.

10.3 Corrections

     The correction factors shown on the flight plan are fuel and time
     to destination, and total fuel required if the conditions were:

     - NO WIND:  No winds at all.

     - +20KT:  20 knots more TAIL-WIND than the average wind component
       you get from the winds you have planned for.

     - -20KT:  20 knots more HEAD-WIND than the average wind component
       you get from the winds you have planned for.

     Example: If you get an average wind component of +7 knots (tail-
     wind), the "+20" will be the figures for 27 knots tail-wind, while
     the "-20" will be the figures for 13 knots head-wind. The "no wind"
     will be for no winds, no matter what the planned winds are.

10.4 How to use the ETO/RTO/ATO fields

     After take-off, you start filling out all the Estimated Time Over-
     head (ETO) fields all the way down to destination, using the leg
     times given. Usually, you will only put down the minutes, except
     when starting on a new hour.

     When you pass a waypoint, you write down the time in the Actual
     Time Overhead (ATO) column, then calculate the new estimated time
     for the next waypoint, and put this in the Revised Time Overhead
     (RTO) column for that point. This way, you will have a fresh
     estimate for the next reporting point for ATC (and yourself).

     As you now pass the waypoints, it will be very easy to see if you
     are ahead or behind the flight plan by comparing ATO and the
     original ETO (the latter was calculated in relation to the take-off
     time).

10.5 Vertical Navigation

     IMPORTANT: In the current version, climb- and descent calculations
     are only applied on the main route, not to the alternates! For the
     alternate legs, you must therefore take climb- and descent perfor-
     mance into account when filling out TAS, wind and fuel flow!

     If you have entered cruising altitudes in your legs, and climb- &
     descent performance data exists (from aircraft database or input
     manually), the program will calculate Top of Climb and Top of
     Descent. This is done when selecting PRINT-/VIEW FLIGHT PLAN.

     On legs that fall entirely into the climb- or descent segments, the
     appropriate TAS, wind and fuel flow values will be applied. Most
     often, ToC/ToD will end up between two waypoints, for these legs,
     TAS, wind and fuel flow will be interpolated using the values found
     in the leg (which should be cruise values) and the climb-/ descent
     data. When interpolating, the program will take into account how
     much of the leg is cruise and how much is climb/descent.


11.  COURSE-/DISTANCE COMPUTER

     This function is entered from the Main menu. It does nothing to
     your flight plan, but is used if you want to look up quickly how
     far it is between two points, and optionally how long it will take
     with various airspeeds and winds. It also provides more information
     on a track than the route editor:

     GREAT CIRCLE: - Initial course, in true & magnetic
                   - Final course,    "   "  "    "
                   - Average course,  "   "  "    "
                   - Distance.

     RHUMB LINE:   - Course, in true & magnetic
                   - Distance.

     (Great circles and rhumb lines are explained in chapter 12.)

12.  TERMS & ABBREVIATIONS USED IN THE PROGRAM

Acc...... Accumulated time
AMT...... Average Magnetic Track
ATC...... Air Traffic Control
ATO...... Actual Time Overhead (when passing a waypoint)
ATT...... Average True Track
Alt...... Altitude
Arr...... Arrival
Burn..... Fuel Burn
CS....... Call Sign
Dist..... Distance in nautical miles
DOW...... Dry Operating Weight. Weight of everything except payload
          (cargo/passengers) and fuel
Dep...... Departure
Dest..... Destination
ETA...... Estimated Time of Arrival
ETD...... Estimated Time of Departure
ETO...... Estimated Time Overhead
FF....... Fuel Flow (Fuel consumption per hour)
FL....... Flight Level
Flt No... Flight Number
GS....... Ground Speed. Speed in relation to the ground after wind
          effect is taken into account
Kts...... Knots ( = speed in nautical miles per hour)
LWT...... Landing Weight
MH....... Magnetic Heading
MLWT..... Max Landing Weight
MT....... Magnetic Track
MTOW..... Max Take-off Weight
MZFW..... Max Zero Fuel Weight
NM....... Nautical Miles (1 NM = 1.852 meters)
RoC...... Rate of Climb   (vertical speed in feet per minute)
RoD...... Rate of Descent (   "       "   "   "    "    "   )
RTO...... Revised estimated Time Overhead. (You may also encounter
          RTO used as an abbreviation for Rejected Take-Off.)
Rte Res.. Route Reserve. In percent of fuel used to destination and
          alternate(s)
TAS...... True AirSpeed
ToC...... Top Of Climb. The point where cruising altitude is
          reached
ToD...... Top Of Descent. The point where descent is initiated 
TOW...... Take-off Weight
VNav..... Vertical Navigation. Climb-/descent calculations.
WC....... Wind Component (Headwind or tailwind)
ZFW...... Zero Fuel Weight. Weight of everything except fuel.
          Larger aircraft usually have a max limit on this.

Great
Circle... The shortest line between two points on the earth. Over a
          large distance, or at high latitudes, the course may
          change considerably trough the flight.
Rhumb
Line..... (or loxodrome track) A line between two points on the
          earth which cross all meridians at the same angle, which
          means that the course is the same all along the route. 
          Over a large distance, or at high latitudes, a rhumb line
          will be significantly longer than the great circle.

    Note: PC Flt Plan calculate all legs as great circles, using
          the average course.