KSP-HOST (tm)



                            An Inbound Telnet Server

                                       for

                          MS/DOS Bulletin Board Systems




                                   Version 1.2










                              Copyright (C) 1995-96
                               All Rights Reserved


                                       by


                              KEY SOFTWARE PRODUCTS

                                440 Ninth Avenue
                        Menlo Park, California 94025-1802
                              BBS/FAX: 415-364-9847



                   KSP-HOST, KSP-SRVR, KSP-CALL, and KSP-NODE
                    are trademarks of Key Software Products.
                     WATTCP is a trademark of Erick Engelke.
               Power C and Multi-C are trademarks of Mix Software.
                   Lantastic is a trademark of Artisoft, Inc.
                      Novell is a trademark of Novell Corp.
                   Banyan Vines is a trademark of Banyan Inc.
             DESQview is a trademark of Quarterdeck Office Systems.





        



                                TABLE OF CONTENTS



        CHAPTER 1 - INTRODUCTION        ...........................    1
           1.1  Other KSP Software      ...........................    2
              1.1.1  KSP Telnet       .............................    2
              1.1.2  KSP FTP       ................................    3
              1.1.3  KSP SLIP       ...............................    3
              1.1.4  KSP Mail       ...............................    3
              1.1.5  So Many CD's      ............................    3

        CHAPTER 2 - INSTALLING THE NETWORK CONNECTION FIRST    ....    4
           2.1  Packet Driver Shim for Novell    ..................    4
           2.2  Packet Driver Shim for Novell w/Token-Ring SNAP  ..    5
           2.3  Packet Driver Shim for Lantastic    ...............    5
              2.3.1  Changes to CONFIG.SYS      ...................    5
              2.3.2  Changes to PROTOCOL.INI      .................    6
           2.4  Packet Driver Shim for Banyan Vines   .............    7

        CHAPTER 3 - THE WATTCP CONFIGURATION FILE     .............    8
           3.1  Network Parameters       ..........................    9
              3.1.1  The PC's Host Name     .......................    9
              3.1.2  The PC's Domain Name     .....................    9
              3.1.3  The PC's IP Address     ......................    9
              3.1.4  The Name Server's IP Address    ..............   10
              3.1.5  The Router's IP Address     ..................   10
              3.1.6  The PC's Network Mask     ....................   10
           3.2  TCP/IP Parameters (optional)      .................   11
              3.2.1  Timeouts        ..............................   11
              3.2.2  Maximum Segment Size (MSS)     ...............   11
           3.3  Parameters Specific to KSP Host    ................   11
              3.3.1  The Log File Directory     ...................   11
              3.3.2  Retrieving Hostname of Remote Client    ......   12
              3.3.3  Specifying the Fossil Ports     ..............   12
              3.3.4  Specifying the Buffer Size     ...............   13
              3.3.5  Maximum Number of Rings     ..................   13
              3.3.6  Sending a "CONNECT" string to the BBS  .......   13
              3.3.7  Specifying Modem Delay      ..................   14
              3.3.8  Disabling Automatic Load High     ............   14

        CHAPTER 4 - Programs in the KSP Host Package   ............   15
           4.1  KSP-NODE (Installed on each BBS Machine)   ........   15
              4.1.1  Command Line Parameters      .................   15
           4.2  KSP-CALL (Used to Test KSP-NODE)    ...............   16
              4.2.1  Command Line Parameters      .................   16
           4.3  KSP-SRVR (The Inbound Telnet Server)    ...........   16
              4.3.1  Command Line Parameters      .................   16

        CHAPTER 5 - SPECIAL CONFIGURATION CONSIDERATIONS      .....   18
           5.1  PCBoard        ....................................   18
           5.2  DESQview        ...................................   18



        



                                TABLE OF CONTENTS


           5.3  Novell        .....................................   18

        APPENDIX 1 - HOW TO REACH US     ..........................   20

        APPENDIX 2 - GETTING UPDATES VIA THE INTERNET    ..........   21

        APPENDIX 3 - LEGAL STUFF       ............................   22













































        




        Feb 11, 1996           KSP-HOST (tm) v1.2                       1


                        CHAPTER 1 - INTRODUCTION        


        KSP-HOST  allows  MS/DOS Bulletin Board Systems to accept inbound
        Telnet  connections.   In  addition to being able to contact your
        BBS  by  modem,  users  can  now  connect  to  your  BBS over the
        Internet using Telnet.  

        The  name  "KSP-HOST"  actualy  refers  to  a pair of programs: A
        program  called  KSP-SRVR  handles  reception  of  inbound Telnet
        sessions  and  communicates  with another program called KSP-NODE
        running on each of your BBS nodes: 

                                             ÉÍÍÍÍÍÍÍÍÍÍ»
              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶ KSP-SRVR º
              ³                            ÄÄ¶          º
              ³      (NetBios)             ÄÄ¶          ºÄÄÄÄÄ Internet
              ³                              º  Telnet  º      (TCP/IP)
              ³                   ÚÄÄÄÄÄÄÄÄÄÄ¶   Host   º
        ÉÍÍÍÍÍÏÍÍÍÍ»        ÉÍÍÍÍÍÏÍÍÍÍ»     ÈÍÍÍÍÍÍÍÍÍÍ¼
        º KSP-NODE º  ...   º KSP-NODE º
        ÈÍÍÍÍÍÑÍÍÍÍ¼        ÈÍÍÍÍÍÑÍÍÍÍ¼
        ÚÄÄÄÄÄÁÄÄÄÄ¿        ÚÄÄÄÄÄÁÄÄÄÄ¿
        ³ BBS Prog ³  ...   ³ BBS Prog ³      
        ³ (Node 1) ³        ³ (Node N) ³
        ÀÄÄÄÄÄÄÄÄÄÄÙ        ÀÄÄÄÄÄÄÄÄÄÄÙ

        This  arrangement allows Telnet users to use a single Internet IP
        address  or  hostname  (that  of the machine running KSP-SRVR) to
        contact  your  BBS.  KSP-SRVR then determines which BBS nodes are
        available,  and  routes  the  session  to one of those nodes.  As
        implied,  KSP-SRVR  can handle multiple telnet connections at the
        same time.  

        The   above   diagram   illustrates   how  things  are  organized
        logically;   the   actual   physical   organization  is  somewhat
        different: 















        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                       2


                   Local Ethernet (Novell, Artisoft, etc.)
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄ  
                      ³                   ³         ³             ³
        ÚÄÄÄÄÄÄÄÄÄÄ¿  ³     ÚÄÄÄÄÄÄÄÄÄÄ¿  ³   ÚÄÄÄÄÄÁÄÄÄÄ¿   ÚÄÄÄÄÁÄÄÄÄ¿
        ³ BBS Prog ³  ³     ³ BBS Prog ³  ³   ³  Packet  ³   ³ Router  ³
        ³ (Node 1) ³  ³     ³ (Node N) ³  ³   ³  Driver  ³   ³ E.g.,   ³
        ÀÄÄÄÄÄÂÄÄÄÄÙ  ³     ÀÄÄÄÄÄÂÄÄÄÄÙ  ³   ÀÄÄÄÄÄÂÄÄÄÄÙ   ³ KA9Q NET³
              ³       ³           ³       ³         ³        ÀÄÄÄÄÂÄÄÄÄÙ
        ÉÍÍÍÍÍÏÍÍÍÍ»  ³     ÉÍÍÍÍÍÏÍÍÍÍ»  ³         ³             ³
        º KSP-NODE ÇÄÄÙ     º KSP-NODE ÇÄÄÙ   ÉÍÍÍÍÍÏÍÍÍÍ»        ³
        ÈÍÍÍÍÍÑÍÍÍÍ¼        ÈÍÍÍÍÍÑÍÍÍÍ¼      º KSP-SRVR º        ³
              ³                   ³           º  Telnet  º     Internet
        ÚÄÄÄÄÄÁÄÄÄÄ¿        ÚÄÄÄÄÄÁÄÄÄÄ¿      º   Host   º    Connection
        ³  Fossil  ³  ...   ³  Fossil  ³      ÈÍÍÍÍÍÍÍÍÍÍ¼     (TCP/IP)
        ³  Driver  ³  ...   ³  Driver  ³
        ÀÄÄÄÄÄÂÄÄÄÄÙ        ÀÄÄÄÄÄÂÄÄÄÄÙ
              ³                   ³
            Modem               Modem

        As  indicated,  the  small TSR program KSP-NODE, acts as a switch
        so  that  each BBS node can accept either Telnet calls or regular
        modem  calls.   This  requires  every  BBS  node  to use a Fossil
        driver as shown.  

        Communication  between KSP-SRVR and KSP-NODE uses NetBios.  I.e.,
        KSP-SRVR  is a protocol converter that translates Internet TCP/IP
        packets   into  NetBios  packets,  and  vice-versa.   NetBios  is
        commonly  supported  by  most local area network software such as
        Lantastic or Novell.  

        The  packet  driver  (or  packet driver shim) is explained in the
        next  chapter;  detailed  information  regarding the installation
        and  configuration of KSP-SRVR and KSP-NODE appears in subsequent
        chapters.   

        The  router  shown  above  connects  your  local  network  to the
        Internet;  a  shareware  program  called  KA9Q NET can serve this
        purpose.  


        1.1 Other KSP Software       

        Key  Software  Products  offers  a  number  of other products for
        BBS's: 








        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                       3


        1.1.1 KSP Telnet        

        A   door  program  that  allows  callers  to  connect  to  remote
        computers  anywhere  on the Internet via your BBS.  Available now
        on our BBS.  


        1.1.2 KSP FTP        

        A  door  program  that  allows  callers to transfer files to/from
        remote computers anywhere on the Internet via your BBS.  


        1.1.3 KSP SLIP        

        A  door  program  that  allows callers to run any TCP/IP software
        from  home,  including using Mosaic to browse the World Wide Web.
        Available now on our BBS.  


        1.1.4 KSP Mail        

        A  Multi-Threaded  Server  for  SMTP  Mail  and NNTP Usenet news.
        Replaces  UUCP,  its  monthly  fees,  and slow transfer rates! No
        more  unwanted  newsgroups!  Instant  mail  without  waiting  for
        scheduled  events!   Works  with  any BBS software that presently
        uses  UUCP.   Requires a 24hr TCP/IP Internet connection. Can now
        receive NNTP news feeds! 


        1.1.5 So Many CD's       

        A  PCBoard PPE to handle off-line CD-Roms.  Seamlessly integrated
        into  PCBoard.   Users  post requests for off-line files and have
        then  returned  as  attachments to messages. Configurable message
        pack-out  dates  automatically  keep  your hard disk from getting
        cluttered.  Available now on our BBS.  















        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                       4


             CHAPTER 2 - INSTALLING THE NETWORK CONNECTION FIRST    


        Before installing KSP-SRVR, you must first install: 

             1.  The network interface hardware.  
             2.  A corresponding packet driver.  
             3.  A packet driver shim (if needed).  

        Detailed  directions for these preliminary steps are available in
        separate   documentation   that   comes  with  the  corresponding
        hardware or software.   

        It's  most  common  that multi-node BBS's are interconnected with
        Ethernet  and  either  Lantastic or Novell.  Unfortunately, these
        two  network  operating  systems  were  designed  using their own
        proprietary  protocols  rather than the TCP/IP protocol and their
        own  proprietary  software  rather than packet drivers to talk to
        their  Ethernet  interface  cards.   However, a piece of software
        called  a packet driver "shim" can be used to let both TCP/IP and
        their proprietary protocol coexist.  


        2.1 Packet Driver Shim for Novell     

        Novell's  network  software is installed in layers as TSRs in the
        order  shown  below.   These commands are usually found either in
        the  AUTOEXEC.BAT  file  or  in another batch file in a directory
        typically called C:\NWCLIENT.  

             LSL
             NE2000  }-- specific to your interface card
             IPXODI
             VLM

        The  packet driver shim (ODIPKT) logically sits on top of IPXODI,
        providing   a  packet  driver  interface  for  software  such  as
        KSP-SRVR: 

             LSL
             NE2000 +--- Frame Type (0-3)
             IPXODI |
             ODIPKT 2 97  }--- The packet driver shim
             VLM       |
                       +----- Packet Vector Interrupt (96-127)
                              (See comment below about hex vs. decimal)

        The  ODIPKT  command  line parameters may vary according to which
        version  of  the  software  you  have  and  how  your hardware is



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                       5


        configured.   The "Frame Type" parameter should correspond to the
        position  of  ETHERNET_II  among  the  frame  types  specified in
        NET.CFG;  zero  (0)  selects  the  first  frame type, one (1) the
        second,  and  so on.  The "Packet Vector Interrupt" number should
        correspond  to  an  unused  interrupt  vector.   Note  that older
        versions  of  ODIPKT  insist that this number be given in decimal
        (96-127)  rather  than  in hex (0x60-0x7F).  The necessary packet
        driver  shim can be downloaded from the Key Software Products BBS
        as file ODI-SHIM.ZIP.   


        2.2 Packet Driver Shim for Novell w/Token-Ring SNAP   

        Another  shim  called  ODITRPKT  exists for Novell that should be
        used  if the underlying network is Token-Ring_SNAP.  Installation
        is  similar  to  ODIPKT as described above, except that the first
        command  line  parameter  must  correspond to the Token-Ring_SNAP
        frame  type  in NET.CFG, and starts at "1" rather than "0".  This
        shim  can  be  downloaded  from  the Key Software Products BBS as
        file TKN-SHIM.ZIP.  


        2.3 Packet Driver Shim for Lantastic     

        Using   a   packet  driver  shim  with  Lantastic  requires  that
        Lantastic  be  installed  using  NDIS  (Network  Driver Interface
        Specification)  Support.  The necessary packet driver shim can be
        downloaded   from   the   Key   Software  Products  BBS  as  file
        DIS-SHIM.ZIP.  

        NDIS   allows  you  to  stack  multiple  protocols  on  a  single
        adapter.   This  lets  you use multiple protocol drivers (such as
        LANtastic  and  TCP/IP)  on  the  same adapter.  You can also use
        NDIS  to  include  third-party adapters that have NDIS drivers in
        your   LANtastic   network.    Supported  adapter  types  include
        Ethernet,  Token-Ring  and ARCNET (R) adapters.  The software and
        documentation  necessary  to  add  NDIS  support  to  an existing
        Lantastic network is available free of charge from Artisoft.  

        Once  you  have NDIS installed and working with Lantastic, adding
        the  shim is a simple matter of editing PROTOCOL.INI (part of the
        NDIS support) and CONFIG.SYS.  


        2.3.1 Changes to CONFIG.SYS       

        With  NDIS  installed,  there  will be two device driver lines in
        your CONFIG.SYS file that look something like the following: 




        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                       6


             DEVICE=C:\LANTASTI\PROTMAN.DOS /I:C:\LANTASTI
             DEVICE=C:\LANTASTI\AEXNDIS.DOS

        The  file  listed  in  the  second line may differ if you are not
        using  Artisoft's  interface  card; in that case, this file would
        typically  be  replaced  by  a  NDIS  driver supplied by the card
        manufacturer.  

        The  packet  driver  shim  itself  is installed as a third device
        driver after the first two, as in: 

             DEVICE=C:\LANTASTI\PROTMAN.DOS /I:C:\LANTASTI
             DEVICE=C:\LANTASTI\AEXNDIS.DOS
             DEVICE=C:\DRIVERS\DIS_PKT.DOS  }--- The packet driver shim


        2.3.2 Changes to PROTOCOL.INI       

        The  PROTOCOL.INI  file  is  a  text file created (usually in the
        C:\LANTASTI  directory) as part of the NDIS installation.  Before
        adding  the  packet  driver  shim,  it  typically  looks like the
        following,  but  with  the  "iobase"  and  "interrupt" parameters
        changed   according   to   your  hardware,  or  with  the  entire
        "[AEXNDIS_NIF]"   section  replaced  if  you  are  not  using  an
        Artisoft interface card.  

             [PROTMAN]
               DRIVERNAME = PROTMAN$
               DYNAMIC = YES

             [AEXNDIS_NIF]
               DRIVERNAME = AEXNDS$
               IOBASE = 0x300
               INTERRUPT = 15

        Adding  the packet driver shim requires adding another section to
        the PROTOCOL.INI file: 

             [PROTMAN]
               DRIVERNAME = PROTMAN$
               DYNAMIC = YES

             [AEXNDIS_NIF]               <---+
               DRIVERNAME = AEXNDS$          |
               IOBASE = 0x300                |
               INTERRUPT = 15                | These names must match!
                                             |





        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                       7


             [PKTDRV]                        |
               DRIVERNAME = PKTDRV$          |
               BINDINGS = AEXNDIS_NIF    <---+
               INTVEC = 0x61
               CHAINVEC = 0x66
               NOVELL = Y

        Note  that the name "AEXNDIS_NIF" must exactly match the spelling
        used  as  the  title of the previous section, "[AEXNDIS_NIF]"; if
        you  are not using Artisoft interface cards, then both occurences
        will  use  some  other identifier.  The "INTVEC" parameter may be
        anything  from  0x60  to 0x80; you may have to experiment to find
        an unused interrupt number.  


        2.4 Packet Driver Shim for Banyan Vines    

        Although  Key  Software  Products  has  never  used  it, and thus
        cannot  offer help on its installation, a packet driver shim does
        exist  for  Banyan  Vines  and  can  be  downloaded  from the Key
        Software Products BBS as file BAN-SHIM.ZIP.  































        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                       8


                 CHAPTER 3 - THE WATTCP CONFIGURATION FILE     


        In  order  to  run,  KSP-SRVR  and  KSP-NODE  need  to  know some
        information  about  your network and BBS configuration, and tries
        to   find   this  in  a  configuration  file  called  WATTCP.CFG.
        KSP-SRVR  and  KSP-NODE  look in three directories to locate this
        file.   First,  they  check  for  an  environment variable called
        WATTCP.CFG  that  specifies  the directory.  Second, they look in
        the  current  (default)  directory.   Third,  if still not found,
        they   look   in  the  directory  that  contains  the  executable
        (KSP-SRVR.EXE or KSP-NODE.EXE).   

        The  following  example  may  be  helpful  for  those  using  the
        environment  variable  approach:  If you place WATTCP.CFG in your
        PCB  directory,  then  your  AUTOEXEC.BAT file should contain the
        following command: 

                              set WATTCP.CFG=C:\PCB

          Note that there is no trailing "\" after the directory name!

        If  KSP-SRVR or KSP-NODE still can't find the configuration file,
        they  will  attempt  to  automatically configure by looking for a
        "BOOTP"  server on your network.  Most BBSs will not have a BOOTP
        server,  so  we  do not recommend this approach.  We only mention
        it  here  because  it  explains  why  you'll get a message saying
        "Configuring  through  BOOTP" if it can't find your configuration
        file.  

        The   WATTCP.CFG   configuration  file  is  a  normal  text  file
        containing  one  entry  per line.  A sample configuration file is
        included  in  this  distribution, but the values MUST be modified
        to   suit  your  particular  environment  or  else  KSP-SRVR  and
        KSP-NODE will not work!   

        The syntax of every entry follows the following format: 

           [ directive = [ "data" | data ] ] [ # comment | ; comment ]

        I.e.,  if  a  directive is not followed by data, the directive is
        ignored.   Similary,  lines  without directives are ignored.  The
        directive is NOT case sensitive; the data IS case sensitive.   

        e.g.,   netmask=255.255.252.0
                domainslist=ksp.com    ; Our domain

        Whitespace  is normally removed from data; data containing blanks
        must  be  surrounded by quotes.  An unquoted '#' or ';' marks the



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                       9


        beginning of a comment.  


        3.1 Network Parameters        

        The  following  parameters control how KSP-SRVR communicates with
        the rest of the TCP/IP network.  


        3.1.1 The PC's Host Name      

        This is the network name of the PC that runs KSP-SRVR.  

                Example: hostname=bbs 

        Note  that  the  host  name  does  not  include  the  domain name
        suffix.   For  example, the hostname of machine '"bbs.ksp.com" is
        simply "bbs".  


        3.1.2 The PC's Domain Name      

        This  is  the  network  name  of the subnet to which your PC (and
        possibly others) are connected.  

                Example: domainslist=ksp.com 

        Note  that  the  domain  name  does  not  include  the  host name
        prefix.   For  example, the domain name of machine '"bbs.ksp.com"
        is "ksp.com".  


        3.1.3 The PC's IP Address      

        This   is  the  unique  IP  address  assigned  to  your  KSP-SRVR
        machine.   It  is  the  one  Telnet users will use when trying to
        connect  to  your  BBS  through the Internet.  (They may also use
        the hostname.domainname format if supported by your nameserver.) 

                Example: my_ip=100.2.37.4  

        Note:  As  an  alternative, you may also set the IP address using
        an environment variable, as in: 

                              set ksp-ip=100.2.37.4

        NOTE:  An  "IP  address"  is  a logical addressing scheme used on
        TCP/IP  networks  such  as the Internet.  Each computer connected
        to  the  Internet  is  assigned  a unique IP address.  Your local



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      10


        network  "guru"  or access provider should be able to provide you
        with the IP addresses you need.   

        IMPORTANT:  The  IP  addresses  given  in  this document are only
        examples.   Do  NOT  attempt to use them - they will NOT work and
        your network administrator will probably get VERY upset! 


        3.1.4 The Name Server's IP Address     

        This  is  the  unique  IP  address  assigned  to  a  network name
        nerver.   You  may  specify more than on nameserver by using more
        than one "nameserver" line.  

                Example: nameserver=111.21.108.110 

        Your  local  network  "guru" or access provider should be able to
        provide  you  with the proper IP addresses of appropriate network
        name servers.  


        3.1.5 The Router's IP Address      

        This is the unique IP address assigned to the network router.  

          Syntax: gateway = ipaddr [ , subnet [ , subnet_mask ] ] 

                Examples: gateway=129.97.176.1
                          gateway=129.97.176.2,129.97.0.0
                          gateway=129.97.176.2,129.97.0.0,255.255.0.0

        Usually  the  (destination)  subnet  and  subnet mask need not be
        specified,  and  is  used to create a "default".  The other forms
        are  used  to  specify  one or more other gateways for particular
        subnets.  

        Your  local  network  "guru" or access provider should be able to
        provide you with the proper IP address of the network router.  


        3.1.6 The PC's Network Mask      

        Network  masks  are  used to distinguish destination IP addresses
        that  are  on  the  local  subnet  from those that are not.  This
        option may not be required, depending on your network topology.  

                Example: netmask=255.255.254.0 

        Your  local  network  "guru" or access provider should be able to



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      11


        provide you with the proper netmask if needed.  


        3.2 TCP/IP Parameters (optional)       

        KSP-SRVR  will  work  without using the following parameters, but
        they are provided if you wish to change them.  


        3.2.1 Timeouts         

        Most  network  operations (such as establishing a connection to a
        remote  host)  have a maximum time before a timeout error occurs.
        The  default  value is 30 seconds; a smaller value is unwise, but
        larger   values   may   be   necessary   for   particularly   bad
        connections.  

                Example: sockdelay=40 


        3.2.2 Maximum Segment Size (MSS)      

        The  default  value  of  MSS  is  1400.  If you know what maximum
        segment  size  means  and know what size you want, you can change
        it: 

                Example: mss=512 

                Note:  Some  Internet  access  providers  configure their
                dial-up  slip  and ppp accounts with a very small segment
                size.   You  may  need  to  set mss as low as 212 if your
                Internet connection is through such a connection.  


        3.3 Parameters Specific to KSP Host     

        Two  parameters in the WATTCP.CFG configuration file are specific
        to the operation of KSP-SRVR.  Each follows the syntax: 

                ksp-srvr.<parameter_name>=<value>


        3.3.1 The Log File Directory      

         Syntax: ksp-srvr.log_directory=<directory_spec> 

        Example: ksp-srvr.log_directory=c:\ksp 

        Purpose: Specifies  the  directory where the file KSP-SRVR.LOG is



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      12


                 stored.  Each entry is made using the following format: 

                        <date>,<time>,<client>,<minutes>,<node_id>

        Comment: This  parameter  is  optional;  if not specified, no log
                 file will be created.  


        3.3.2 Retrieving Hostname of Remote Client     

         Syntax: ksp-srvr.retrieve_hostnames=<option> 

        Example: ksp-srvr.retrieve_hostnames=disabled 

        Purpose: If  left enabled, IP addresses of remote clients will be
                 translated  into  hostnames using the domain name server
                 to  provide  a reliable identification.  Otherwise, only
                 IP  addresses  will  be  used.  Affects both the display
                 and the log files.  

        Comment: Default is enabled.  

        All  remaining  parameters  in  the WATTCP.CFG configuration file
        are BBS node-specific.  These parameters follow the syntax: 

                ksp-node.<parameter_name>=<value>
        or:     ksp-node[<id_range>].<parameter_name>=<value>

        where  "<id_range>"  is either a single ID number or a pair of ID
        numbers  separated  by a dash.  Parameters specified by the first
        form  apply  to all BBS nodes; parameters specified by the second
        form  apply only to those BBS nodes whose IDs match the specified
        range.  

        Note  that when more than one entry applies to the same node, the
        last  entry  prevails; thus the first form can be used to specify
        a  default  for all BBS nodes, followed by use of the second form
        to specify exceptions.  


        3.3.3 Specifying the Fossil Ports      

         Syntax: ksp-node[<node_range>].fossil_ports=<port_range> 

        Example: ksp-node[11-20].fossil_ports=1 
             or: ksp-node[5].fossil_ports=0-3 

        Purpose: Specifies  the  range of Fossil port numbers used by one
                 or  more BBS nodes.  There should be one fossil port for



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      13


                 each BBS node running on the same machine.  

        Comment: Fossil port numbers typically start at 0 (for COM1).  


        3.3.4 Specifying the Buffer Size      

         Syntax: ksp-node[<node_range>].buffer_size=<bytes> 

        Example: ksp-node[11-20].buffer_size=512 

        Purpose: Specifies  the  buffer size provided by KSP-NODE for one
                 or more BBS nodes.  

        Comment: This  parameter is optional.  If not specified, KSP-NODE
                 will  use  the  same  buffer  size (not "buffer") as the
                 Fossil driver.  


        3.3.5 Maximum Number of Rings      

         Syntax: ksp-node[<id_range>].maxrings=<number> 

        Example: ksp-node.maxrings=3
                 ksp-node[5-10].maxrings=0

        Purpose: Specifies  the  maximum  number  of rings to send to the
                 BBS when trying to establish a connection.  

        Comment: Set  this  value to zero for those nodes which configure
                 their modems for auto-answer.  


        3.3.6 Sending a "CONNECT" string to the BBS   

         Syntax: ksp-node[<id_range>].connect_string=<response> 

        Example: ksp-node.connect_string="CONNECT 14400/V32/LAPM.V42BIS^M^M"
                 ksp-node[5-10].connect_string="+FDM^M^MCONNECT 14400^M^M"

        Purpose: Specifies  the  connect  string  sent  to the BBS when a
                 telnet connection has been established.  

        Note: The  quotation  marks  are  required  immediately after the
                 equals  sign  and  at the end of the line to enclose the
                 string   pair   since   the  string  includes  a  blank.
                 Carriage  return followed by line feed is represented by
                 the pair of characters, "^M".  




        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      14



        3.3.7 Specifying Modem Delay       

         Syntax: ksp-node[<node_range>].modem_delay_seconds=<seconds> 

        Example: ksp-node[11-20].modem_delay_seconds=60 

        Purpose: It  usually takes several seconds from the moment that a
                 modem  detects  a  ring before the carrier is negotiated
                 and  a  connection  is established.  During this period,
                 the  "carrier  detect"  signal  from  the modem is still
                 inactive  and  cannot  be  used  to cause inbound Telnet
                 connections  to  be  refused by that BBS node.  To solve
                 this  problem,  KSP-NODE ignores all connection requests
                 from  KSP-SRVR  for  a specified number of seconds after
                 any  modem  activity  (such  as a ring).  This parameter
                 specifies that time period for one or more BBS nodes.  

        Comment: This  parameter is optional.  Default is 30 seconds.  If
                 the  modem is configured for auto-answer, set this value
                 for that node to zero.  


        3.3.8 Disabling Automatic Load High      

         Syntax: ksp-node[<node_range>].loadhigh=disabled 

        Example: ksp-node[11-20].loadhigh=disabled 

        Purpose: KSP-NODE  will  try  to  load into an upper memory block
                 (UMB)  if possible.  This parameter disables that option
                 for one or more BBS nodes.  

        Comment: This parameter is optional.  Default is enabled.  


















        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      15


                 CHAPTER 4 - Programs in the KSP Host Package   


        There  are  three  programs  in  the  KSP Host package: KSP-NODE,
        KSP-SRVR,  and KSP-CALL.  The purpose and installation of each is
        described below.  

        4.1 KSP-NODE (Installed on each BBS Machine)    

        KSP-NODE  is  a  small  Terminate and Stay Resident (TSR) program
        installed  on one or more BBS machines.  It provides an extension
        to  the  services  provided  by  a  Fossil driver, and so must be
        installed  after  the  Fossil  driver  and before running the BBS
        program.   

        For  the  duration  of a telnet session, KSP-NODE keeps the modem
        off-hook so that node will look busy to modem callers.  

        KSP-NODE  creates  a  small buffer for each serial port supported
        by  the  Fossil  driver.   In  addition  to the buffers, KSP-NODE
        needs  about  2,000 bytes of code space.  The size of the buffers
        can be specified as desired, but is typically around 512 bytes.  


        4.1.1 Command Line Parameters       

        KSP-NODE   requires   one   (and  optionally  two)  command  line
        parameters.   The  first  is  a unique ID number assigned to that
        machine.   If  you are multitasking several nodes on one machine,
        then  a  second  parameter  is  required,  and  together  the two
        specify  a  range  of  ID  numbers for all nodes on that machine.
        For example: 

                  KSP-NODE  4  8
                            ³  ³
                            ³  ÀÄÄ Last ID#
                            ÀÄÄÄÄÄ First ID#

        You  may  use your regular BBS node numbers for these ID numbers,
        although  that  is  not  required.   The only real requirement is
        that  no  two  BBS  nodes  share the same ID.  The ID numbers are
        used  in the WATTCP.CFG configuration file (see above) to specify
        certain  configuration  parameters  that  apply  to  specific BBS
        nodes.  

        If  you are multi-tasking under DESQview, then you should add the
        "/DV"  command  line  parameter  so  that KSP-NODE will let other
        processes run while it is waiting on the network: 




        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      16


                  KSP-NODE  /DV 4  8
                                ³  ³
                                ³  ÀÄÄ Last ID#
                                ÀÄÄÄÄÄ First ID#


        4.2 KSP-CALL (Used to Test KSP-NODE)     

        KSP-CALL  is  a  small  utility  program  intended  to be used to
        verify  proper  installation of KSP-NODE.  Basically, KSP-CALL is
        sort  of  a NetBios version of a Telnet client program.  That is,
        you  may  run it to log into any of your BBS nodes where KSP-NODE
        has been installed.  

        KSP-CALL  and  KSP-NODE  communicate  via  NetBios, and thus work
        only  within  the  limits  of  your own local area network (i.e.,
        within the context of your Novell or Lantastic network).  


        4.2.1 Command Line Parameters       

        If  no  command  line parameter is given, KSP-CALL will select an
        idle  BBS  node  and  establish a connection with it.  Otherwise,
        you  may  specify  a BBS node's ID number on the command line and
        KSP-CALL will try to establish a connection with that node.  


        4.3 KSP-SRVR (The Inbound Telnet Server)     

        KSP-SRVR  acts  like a telephone switchboard.  It accepts inbound
        Telnet  calls  from  the  Internet and then uses NetBios to route
        them  to  KSP-NODE  on  an  idle  BBS  node.  KSP-SRVR can handle
        several  Telnet  sessions  at  the  same time.  The actual number
        depends  on  memory requirements (see below), but in practice the
        usual limit is about sixteen simultaneous sessions.  


        4.3.1 Command Line Parameters       

        KSP-SRVR  has two command line parameters; both are optional.  If
        specified,  the  first  is  the  maximum  number  of simultaneous
        sessions  and  the second is the per-session buffer size.  Memory
        requirements  increase  as  the  product  of  sessions and buffer
        size;  the  larger  the  buffer  size,  the  fewer  the number of
        simultaneous  sessions  that can be supported.  The default is 16
        sessions and a buffer size of 512 bytes.  

        Note:  Unlicensed  (evaluation) copies of KSP-SRVR are limited to
        a  single  session,  five  minutes per session, and a total of 15



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      17


        minutes  running  time.   These restrictions are removed with the
        purchase of an "access key" (see ORDERFRM.DOC).  


















































        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      18


             CHAPTER 5 - SPECIAL CONFIGURATION CONSIDERATIONS      


        There  are  two common software environments that deserve special
        mention.   When running any of the KSP-HOST software under one of
        these  environments,  there  are  some  additional  configuration
        steps required.  


        5.1 PCBoard         

        There  are  two  versions  of  PCBoard  that  run  under  MS/DOS:
        PCBOARD.EXE  and  PCBOARDM.EXE.   The  latter is the "Multi-Port"
        version,  and  is  the  only  one  that can be used with a Fossil
        driver (required by KSP-NODE).  

        You  can  tell  whether  or  not PCBoard is configured to use the
        fossil  driver because it will display "PORT1F" instead of "COM1"
        (for example) on the waiting for calls screen.  

        Don't  forget  that  PCBoard  uses  port  numbers  which  are one
        greater  than  those used by Fossil drivers.  For example, Fossil
        designates  COM1 and COM2 as port 0 and port 1 respectively.  Yet
        PCBoard thinks of these as port 1 and port 2.  


        5.2 DESQview         

        To  run  any  software based on the Waterloo TCP/IP library under
        DESQview,   it's   absolutely   necessary  to  install  a  packet
        multiplexer  on  top  of  the packet driver or packet driver shim
        before  starting  DESQview.   This  is necessary whenever running
        more  than  one  program on the same machine, even if only one of
        them   is   a   Waterloo   TCP/IP  product.   A  freeware  packet
        multiplexer  is  available  from  Key  Software  Products as file
        KSPMUX*.ZIP, where the "*" is a two-digit version number.  

        To  run  the  KSP-HOST  software  under  DESQview,  you must also
        enable  NETBIOS  support.  To do so, run DVSETUP inside DESQview.
        Select  "Advanced  Setup",  and  press  "N"  for "Network".  Then
        enter  "Y"  under  "NETBIOS"  and  press return twice to save and
        exit.  


        5.3 Novell         

        NetBios  support  on  Novell networks is provided by a TSR called
        "NETBIOS".  You must install this TSR before running any KSP-HOST
        software.   (Lantastic  networks  already  have  NetBios  support



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      19


        built into the basic system.) 



















































        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      20


                        APPENDIX 1 - HOW TO REACH US     


        The  Key Software Products BBS/FAX number (415-364-9847) operates
        24   hours   a   day,  7  days  a  week.   Software  at  our  end
        automatically  determines whether an incoming call is data or FAX
        and will operate accordingly.  

        If  you have access to electronic mail, you can send us a message
        via any of the following: 

        On COMPUSERVE, send mail to:

                >Internet:tech.support@ksp.com

        On PRODIGY, send mail to: VGDC59A

        On Internet, UUCP, or Bitnet, send mail to:

                tech.support@ksp.com

        On Fidonet, address mail to "UUCP" at nearest fidonet site which
        provides a gateway to Internet, such as 1:105/42.

                1st line of message: To: tech.support@ksp.com



























        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      21


                APPENDIX 2 - GETTING UPDATES VIA THE INTERNET    


        The  main  distribution  file  is KSPHST??.ZIP, where "??" is the
        version  number.  You can retrieve this file via anonymous ftp at
        "scizzl.scu.edu",  directory "ksp".  Please note that there is no
        "e" at the end of "scizzl".  

        This  file  is also available from the KSP BBS, either by calling
        in   and   downloading,   or  via  e-mail  using  the  "LISTSERV"
        capabilities of the BBS.  

        To  use  LISTSERV,  you  must  send  a  message  addressed to the
        Internet  address  listserv@ksp.com.  The message must contain an
        LISTSERV  command  entered  as a single line of text, and it must
        be  the first line in the message. The LISTSERV commands that are
        supported include: 

        Command: HELP tlbmm-l
        Purpose: Returns an text file with help information about LISTSERV.

        Command: DIR tlbmm-l
        Purpose: Returns an e-mail message listing all of the file 
                 directories on the BBS by number and description.

        Command: LIST tlbmm-l 1
        Purpose: Returns an e-mail message listing all of the files in
                 directory #1 of the BBS.

        Command: GET tlbmm-l KSPHST12.ZIP
        Purpose: Returns an e-mail message containing a uuencoded version of
                 the file KSPHST12.ZIP.  To extract the file, you must save
                 the message as a file on your system, edit out the e-mail
                 header at the beginning of the file, and then use a program
                 called UUDECODE (commonly available on Unix) to convert the
                 uuencoded version back to the original ZIP format, and then
                 (finally) use PKUNZIP to extract the contents of the file.















        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 11, 1996           KSP-HOST (tm) v1.2                      22


                         APPENDIX 3 - LEGAL STUFF       


                                LIMITED WARRANTY

        This  software  is provided 'as is' without warranty of any kind,
        either  expressed  or  implied, including, but not limited to the
        implied   warranties   of   merchantability  and  fitness  for  a
        particular  purpose.   The  entire  risk  as  to  the quality and
        performance of the program is with you.  

        Some  states do not allow the exclusion of implied warranties, so
        the  above  exclusions may not apply to you.  This warranty gives
        you  specific  legal  rights  and  you may also have other rights
        which vary from state to state.  

        Key  Software  Products  has  taken  due  care  in  preparing the
        documentation  and  software  included  in   to  ascertain  their
        correctness  and  effectiveness.   However, Key Software Products
        does  not  warrant  that  operation  of  this  software  will  be
        uninterrupted  or  error  free.   In  no event shall Key Software
        Products  be  liable  for  incidental or consequential damages in
        connection  with  or  arising out of the furnishing, performance,
        or use of this software.  


                                     LICENSE

        You  MAY  use  this software on any computer or computers in your
        possession.   The licensed version is registered for use on up to
        a  fixed  number of BBS nodes running on multiple machines and/or
        multiple multi-tasking processes.  

        You  MAY  copy this software into any machine readable or printed
        form  for  backup or modification purposes in support of your use
        of the software.  

        You  MAY  distribute  the original unmodified, unlicensed version
        of  this  software,  but you may not charge a fee exceeding $5.00
        to  cover  the  cost of duplicating, shipping, and handling.  You
        may NOT distribute a licensed version of this software.  

        You  may  NOT  use,  copy, modify, sublicense, assign or transfer
        this  software  and  its license, or any copy or modification, in
        whole  or  in  part,  except  as  expressly  provided for in this
        license.  






        Copyright (C) 1995-96, Key Software Products. All Rights Reserved