KSP SLIP (tm)

                     A SLIP Door for Bulletin Board Systems










                                   Version 3.4










                              Copyright (C) 1995-96
                               All Rights Reserved


                                       by


                              KEY SOFTWARE PRODUCTS

                                440 Ninth Avenue
                        Menlo Park, California 94025-1802
                              BBS/FAX: 415-364-9847



                KSP SLIP is a trademark of Key Software Products.
                 PCL4C is a trademark of MarshallSoft Computing.
                     WATTCP is a trademark of Erick Engelke.
                     Power C is a trademark of Mix Software.
                     Multi-C is a trademark of Mix Software.
             DESQview is a trademark of Quarterdeck Office Systems.
                   Lantastic is a trademark of Artisoft, Inc.
                      Novell is a trademark of Novell Corp.
                   Banyan Vines is a trademark of Banyan Inc.




        



                                TABLE OF CONTENTS



        CHAPTER 1 - INTRODUCTION        ...........................    1
           1.1  Compatibility with BBS Software     ...............    2
           1.2  Hardware Requirements       .......................    2
           1.3  Software Requirements       .......................    2
           1.4  Other KSP Software      ...........................    3
              1.4.1  KSP Telnet       .............................    3
              1.4.2  KSP FTP       ................................    3
              1.4.3  KSP Mail       ...............................    3
              1.4.4  KSP HOST       ...............................    3
              1.4.5  So Many CD's      ............................    4

        CHAPTER 2 - INSTALLATION        ...........................    5
           2.1  Packet Driver Shims for Novell    .................    5
           2.2  Packet Driver Shim for Novell w/Token-RingSNAP   ..    6
           2.3  Packet Driver Shims for Lantastic    ..............    6
              2.3.1  Changes to CONFIG.SYS      ...................    6
              2.3.2  Changes to PROTOCOL.INI      .................    7
           2.4  Packet Driver Shims for Banyan Vines   ............    8
           2.5  Other Things to Configure     .....................    8

        CHAPTER 3 - THE WATTCP CONFIGURATION FILE     .............    9
           3.1  Multiple Nodes and the "include" Directive   ......   10
           3.2  Using a BOOTP Server     ..........................   10
           3.3  Manual Configuration       ........................   10
              3.3.1  The PC's Host Name     .......................   11
              3.3.2  The PC's Domain Name     .....................   11
              3.3.3  The PC's IP Address     ......................   11
              3.3.4  The Name Server's IP Address    ..............   12
              3.3.5  The Router's IP Address     ..................   12
              3.3.6  The PC's Network Mask     ....................   12
           3.4  TCP/IP Parameters (optional)      .................   12
              3.4.1  Timeouts        ..............................   13
              3.4.2  Maximum Segment Size (MSS)     ...............   13
           3.5  SLIP Operating Parameters      ....................   13
              3.5.1  Dynamic Parameters       .....................   14
              3.5.2  Blocking Access to Certain Sites    ..........   14
              3.5.3  Allowing Access to a Limited Set of Sites ....   15
              3.5.4  Session Time Limit      ......................   15
              3.5.5  Session Reserve Time      ....................   15
              3.5.6  Inactivity Limit       .......................   16
              3.5.7  Minimum Baud Rate      .......................   16
              3.5.8  Operating Hours       ........................   16
              3.5.9  Startup Message       ........................   17
              3.5.10  Minimum Baud Rate Message     ...............   17
              3.5.11  Operating Hours Message      ................   17
              3.5.12  User Session Logging      ...................   17
              3.5.13  SLIP Packet Monitor      ....................   18
              3.5.14  Non-Standard Port/Fossil Break Detect     ...   18



        



                                TABLE OF CONTENTS


              3.5.15  Eliminating the Startup Count-Down     ......   18
              3.5.16  Silencing the BBS console bell    ...........   18
              3.5.17  Disabling the Local Screen     ..............   19

        CHAPTER 4 - INSTALLING THE SLIP DOOR COMMAND    ...........   20
           4.1  Command Line Parameters      ......................   20
              4.1.1  The /MAXMINS Parameter      ..................   20
              4.1.2  The /CONFIG Parameter      ...................   20
              4.1.3  KSP-SLIP.EXE Exit Codes      .................   21
              4.1.4  Checking Packet Counts (PKTCOUNT.EXE)     ....   21

        CHAPTER 5 - INSTALLING YOUR ACCESS KEY     ................   22

        CHAPTER 6 - CUSTOMIZING THE DISPLAY FILES     .............   23
           6.1  PCBoard Display Macros      .......................   23
           6.2  Macros Unique to KSP SLIP    ......................   23
           6.3  Justification and Spacing      ....................   23
              6.3.1  No Justification       .......................   24
              6.3.2  Left Justification       .....................   24
              6.3.3  Center Justification       ...................   24
              6.3.4  Right Justification       ....................   24
           6.4  The DISPLAY Program      ..........................   25

        APPENDIX 1 - HOW TO REACH US     ..........................   26

        APPENDIX 2 - GETTING UPDATES VIA THE INTERNET    ..........   27

        APPENDIX 3 - LEGAL STUFF       ............................   28
























        




        Feb 20, 1996           KSP SLIP (tm) v3.4                       1


                        CHAPTER 1 - INTRODUCTION        


        Many  BBS's  now offer E-Mail access to the Internet.  But few if
        any  offer  a real TCP/IP connection.  As compared to mere E-Mail
        access,  providing a TCP/IP connection opens up a large number of
        new  possibilities  to  callers,  such  as  the ability to remote
        login  to Internet hosts in foreign countries using Telnet, or to
        access  files  on  those  hosts  using  FTP,  or  to  search  for
        information   using   Gopher,  Archie,  and  the  new  multimedia
        hypertext browser, Mosaic.  

        KSP  SLIP  establishes  a  logical two-way connection between the
        user's serial line and the Internet: 

                            +----------+     |
               User's       |          |     | Local Area Network
               Modem <----->| KSP SLIP |<----+ connected to the
                            |          |     | Internet
                            +----------+     |
                            BBS Machine

        As  indicated,  the  physical  connection between the BBS machine
        and  the  Internet  is  usually  by  means  of  an  Ethernet card
        attached  to  a  local  area  network  that  is  attached  to the
        Internet.   However,  this  connection  could instead be simply a
        separate   modem  connection  to  a  commercial  Internet  access
        provider, such as NETCOM.  

        TCP/IP  encapsulates  data in packets and transfers those packets
        according  to  a  specific  communication  protocol.  Data on the
        serial  line  between  the  BBS  and  the  caller  must obey this
        protocol;  KSP  SLIP  does  this  using a popular protocol called
        SLIP  (Serial Link Internet Protocol).  Of course the caller must
        also  be using software at his end that also supports SLIP; there
        are  several  shareware products for this purpose, available from
        the Key Software Products BBS.  

        KSP SLIP meets the following BBS-specific needs: 

             1.  Terminates  the  BBS session when user's time limit
                     expires.  
             2.  Terminates the BBS session when user hangs up.  
             3.  Terminates   when   there's   no   activity  for  a
                     sysop-specified period of time.  
             4.  Records the SLIP session in a log file.  
             5.  Provide  colorized  or  parameterized  messages  to
                     user.  




        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                       2


             6.  Restrict users by baud rate.  
             7.  Restrict hours of operation.  

        KSP   SLIP   is  shareware.   The  unlicensed  version  is  fully
        functional  except  that it imposes a maximum of five minutes per
        SLIP  session.   Once  licensed,  the user is limited only by the
        amount of time remaining in his BBS session.  

        KSP  SLIP  was  implemented  using  Erick  Engelke's Waterloo TCP
        library,  MarshallSoft  Computing's PCL4C Personal Communications
        library,   and  Mix  Software's  Power  C  compiler  and  Multi-C
        multi-threaded code library.  


        1.1 Compatibility with BBS Software      

        KSP  SLIP is compatible with any BBS software that can generate a
        DOOR.SYS  file.   It  works  with  a  BBS  configured  to use the
        standard  COM1  through  COM4 ports, or will automatically detect
        and use a Fossil driver.  


        1.2 Hardware Requirements        

        KSP  SLIP  inherently  requires  that  the  PC  running  your BBS
        software  have  a  physical  connection  to  a  TCP/IP  network -
        normally  the  Internet.  Ideally, this connection is by means of
        an  adapter  card  connected  to  an  Ethernet at your company or
        school (and then through a "gateway" to the Internet).  

        It  is  also  possible  to  connect  to  the  Internet  through a
        commercial  Internet  Access  Provier  via a dial-up SLIP (Serial
        Line  Internet  Protocol)  connection.   This approach requires a
        second  serial  port, modem, and telephone line dedicated to this
        purpose.   Information on finding such a provider is available on
        the KSP BBS.  


        1.3 Software Requirements        

        KSP  SLIP  runs  on  top  of  another  piece of software called a
        "packet  driver".  The packet driver presents a standard software
        interface  to  KSP  SLIP,  regardless  of  the  type  of hardware
        interface  that  connects  the  PC to the network.  Public domain
        packet drivers exist for SLIP links and most Ethernet cards.  

        If  your  BBS  uses  a  multi-tasking  operating  system  to  run
        multiple  nodes  on  a  single  PC,  then you will need a "packet
        multiplexer".   A  packet  multiplexer  designed specifically for



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                       3


        use   with   KSP  network  products  running  under  DESQview  is
        available  as  a  freeware  package  distributed  as KSPMUX*.ZIP,
        where  the  "*"  is  the  version  number.   KSP SLIP is DESQview
        "aware"   to   provide   better  performance  in  a  multitasking
        environment.  

        If  your  PC  is  connected  to  a non-TCP/IP proprietary network
        (such  as  Novell  or Lantastic), you will probably need a packet
        driver "shim".  

        KSP  SLIP  does  NOT  require that you purchase a separate TCP/IP
        package,  such  as  that  sold  by Novell, Artisoft, or IBM.  KSP
        SLIP   should   happily  coexist  with  any  of  these  packages,
        however.  

        An  assortment of public domain packet drivers, multiplexers, and
        shims are available on the KSP BBS.  


        1.4 Other KSP Software       

        Key  Software  Products  offers  a  number  of other products for
        BBS's: 


        1.4.1 KSP Telnet        

        A   door  program  that  allows  callers  to  connect  to  remote
        computers  anywhere  on the Internet via your BBS.  Available now
        on our BBS.  


        1.4.2 KSP FTP        

        A  door  program  that  allows  callers to transfer files to/from
        remote computers anywhere on the Internet via your BBS.  


        1.4.3 KSP Mail        

        A  Multi-Threaded  Server  for  SMTP  Mail  and NNTP Usenet news.
        Replaces  UUCP,  its  monthly  fees,  and slow transfer rates! No
        more  unwanted  newsgroups!  Instant  mail  without  waiting  for
        scheduled  events!   Works  with  any BBS software that presently
        uses  UUCP.   Requires a 24hr TCP/IP Internet connection. Can now
        receive NNTP news feeds! 






        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                       4


        1.4.4 KSP HOST        

        An  inbound  Telnet  server  for  MS/DOS  Bulletin Board Systems.
        Every  node  can  answer both telnet and modem calls!  Requires a
        fossil  driver  on  each node, a 24 hour TCP/IP connection to the
        Internet,  and a local area network that supports NetBios such as
        Novell or Lantastic.  


        1.4.5 So Many CD's       

        A  PCBoard PPE to handle off-line CD-Roms.  Seamlessly integrated
        into  PCBoard.   Users  post requests for off-line files and have
        then  returned  as  attachments to messages. Configurable message
        pack-out  dates  automatically  keep  your hard disk from getting
        cluttered.  Available now on our BBS.  




































        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                       5


                        CHAPTER 2 - INSTALLATION        


        Before  installing  KSP  SLIP  as  a  BBS  door,  you  must first
        install: 

             1.  The network interface hardware.  
             2.  A corresponding packet driver.  
             3.  A packet driver shim (if needed).  
             4.  A packet multiplexer (if needed).  

        Detailed  directions for these preliminary steps are available in
        separate   documentation   that   comes  with  the  corresponding
        hardware or software.   

        It's  most  common  that multi-node BBS's are interconnected with
        Ethernet  and  either  Lantastic or Novell.  Unfortunately, these
        two  network  operating  systems  were  designed  using their own
        proprietary  protocols  rather than the TCP/IP protocol and their
        own  proprietary  software  rather than packet drivers to talk to
        their  Ethernet  interface  cards.   However, a piece of software
        called  a packet driver "shim" can be used to let both TCP/IP and
        their proprietary protocol coexist.  


        2.1 Packet Driver Shims for Novell     

        Novell's  network  software is installed in layers as TSRs in the
        order  shown  below.   These commands are usually found either in
        the  AUTOEXEC.BAT  file  or  in another batch file in a directory
        typically called C:\NWCLIENT.  

             LSL
             NE2000  }-- specific to your interface card
             IPXODI
             VLM

        The  packet driver shim (ODIPKT) logically sits on top of IPXODI,
        providing  a  packet  driver  interface  for software such as KSP
        SLIP: 

             LSL
             NE2000 +--- Frame Type (0-3)
             IPXODI |
             ODIPKT 2 97  }--- The packet driver shim
             VLM       |
                       +----- Packet Vector Interrupt (96-127)
                              (See comment below about hex vs. decimal)




        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                       6


        The  ODIPKT  command  line parameters may vary according to which
        version  of  the  software  you  have  and  how  your hardware is
        configured.   The "Frame Type" parameter should correspond to the
        position  of  ETHERNET_II  among  the  frame  types  specified in
        NET.CFG;  zero  (0)  selects  the  first  frame type, one (1) the
        second,  and  so  on. The "Packet Vector Interrupt" number should
        correspond  to  an  unused  interrupt  vector.   Note  that older
        versions  of  ODIPKT  insist that this number be given in decimal
        (96-127)  rather  than  in hex (0x60-0x7F).  The necessary packet
        driver  shim can be downloaded from the Key Software Products BBS
        as file ODI-SHIM.ZIP.   


        2.2 Packet Driver Shim for Novell w/Token-RingSNAP    

        Another  shim  called  ODITRPKT  exists for Novell that should be
        used  if the underlying network is Token-Ring_SNAP.  Installation
        is  similar  to  ODIPKT as described above, except that the first
        command  line  parameter  must  correspond to the Token-Ring_SNAP
        frame  type  in NET.CFG, and starts at "1" rather than "0".  This
        shim  can  be  downloaded  from  the Key Software Products BBS as
        file TKN-SHIM.ZIP.  


        2.3 Packet Driver Shims for Lantastic     

        Using   a   packet  driver  shim  with  Lantastic  requires  that
        Lantastic  be  installed  using  NDIS  (Network  Driver Interface
        Specification)  Support.  The necessary packet driver shim can be
        downloaded   from   the   Key   Software  Products  BBS  as  file
        DIS-SHIM.ZIP.  

        NDIS   allows  you  to  stack  multiple  protocols  on  a  single
        adapter.   This  lets  you use multiple protocol drivers (such as
        LANtastic  and  TCP/IP)  on  the  same adapter.  You can also use
        NDIS  to  include  third-party adapters that have NDIS drivers in
        your   LANtastic   network.    Supported  adapter  types  include
        Ethernet,  Token-Ring  and ARCNET (R) adapters.  The software and
        documentation  necessary  to  add  NDIS  support  to  an existing
        Lantastic network is available free of charge from Artisoft.  

        Once  you  have NDIS installed and working with Lantastic, adding
        the  shim is a simple matter of editing PROTOCOL.INI (part of the
        NDIS support) and CONFIG.SYS.  








        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                       7


        2.3.1 Changes to CONFIG.SYS       

        With  NDIS  installed,  there  will be two device driver lines in
        your CONFIG.SYS file that look something like the following: 

             DEVICE=C:\LANTASTI\PROTMAN.DOS /I:C:\LANTASTI
             DEVICE=C:\LANTASTI\AEXNDIS.DOS

        The  file  listed  in  the  second line may differ if you are not
        using  Artisoft's  interface  card; in that case, this file would
        typically  be  replaced  by  a  NDIS  driver supplied by the card
        manufacturer.  

        The  packet  driver  shim  itself  is installed as a third device
        driver after the first two, as in: 

             DEVICE=C:\LANTASTI\PROTMAN.DOS /I:C:\LANTASTI
             DEVICE=C:\LANTASTI\AEXNDIS.DOS
             DEVICE=C:\DRIVERS\DIS_PKT.DOS  }--- The packet driver shim


        2.3.2 Changes to PROTOCOL.INI       

        The  PROTOCOL.INI  file  is  a  text file created (usually in the
        C:\LANTASTI  directory) as part of the NDIS installation.  Before
        adding  the  packet  driver  shim,  it  typically  looks like the
        following,  but  with  the  "iobase"  and  "interrupt" parameters
        changed   according   to   your  hardware,  or  with  the  entire
        "[AEXNDIS_NIF]"   section  replaced  if  you  are  not  using  an
        Artisoft interface card.  

             [PROTMAN]
               DRIVERNAME = PROTMAN$
               DYNAMIC = YES

             [AEXNDIS_NIF]
               DRIVERNAME = AEXNDS$
               IOBASE = 0x300
               INTERRUPT = 15

        Adding  the packet driver shim requires adding another section to
        the PROTOCOL.INI file: 

             [PROTMAN]
               DRIVERNAME = PROTMAN$
               DYNAMIC = YES






        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                       8


             [AEXNDIS_NIF]               <---+
               DRIVERNAME = AEXNDS$          |
               IOBASE = 0x300                |
               INTERRUPT = 15                | These names must match!
                                             |
             [PKTDRV]                        |
               DRIVERNAME = PKTDRV$          |
               BINDINGS = AEXNDIS_NIF    <---+
               INTVEC = 0x61
               CHAINVEC = 0x66
               NOVELL = Y

        Note  that the name "AEXNDIS_NIF" must exactly match the spelling
        used  as  the  title of the previous section, "[AEXNDIS_NIF]"; if
        you  are not using Artisoft interface cards, then both occurences
        will  use  some  other identifier.  The "INTVEC" parameter may be
        anything  from  0x60  to 0x80; you may have to experiment to find
        an unused interrupt number.  


        2.4 Packet Driver Shims for Banyan Vines    

        Although  Key  Software  Products  has  never  used  it, and thus
        cannot  offer help on its installation, a packet driver shim does
        exist  for  Banyan  Vines  and  can  be  downloaded  from the Key
        Software Products BBS as file BAN-SHIM.ZIP.  


        2.5 Other Things to Configure      

        Once  your  network  is  up and running with a packet driver or a
        packet driver shim, there are basically two additional steps: 

             1.  Create a WATTCP.CFG configuration file.  
             2.  Configure KSP SLIP as a BBS door.  

        As  discussed  in the next chapter, you may not need a WATTCP.CFG
        configuration file if you have a BOOTP server.  

        There  is  a  useful  program called TCPINFO available on the KSP
        BBS.   If  you have no WATTCP.CFG file, it will tell you (after a
        maximum  of 30 seconds) if it was able to automatically configure
        itself  via  a  BOOTP  server.  If you have a WATTCP.CFG file, it
        will  determine  whether  or  not  you  have configured that file
        properly.  







        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                       9


                 CHAPTER 3 - THE WATTCP CONFIGURATION FILE     


        In  order  to  run, KSP SLIP needs to know some information about
        your  network,  and  tries  to  find this in a configuration file
        called  WATTCP.CFG.   KSP  SLIP  looks  in  three  directories to
        locate  this  file.  First, it checks for an environment variable
        called  WATTCP.CFG  that  specifies  the  directory.   Second, it
        looks  in  the  current (default) directory.  Third, if still not
        found,  it  looks  in  the directory that contains the executable
        (KSP-SLIP.EXE).  

        The  following  example  may  be  helpful  for  those  using  the
        environment  variable  approach:  If you place WATTCP.CFG in your
        PCB  directory,  then  your  AUTOEXEC.BAT file should contain the
        following command: 

                              set WATTCP.CFG=C:\PCB

          Note that there is no trailing "\" after the directory name!

        If  KSP  SLIP  still  can't  find the configuration file, it will
        attempt  to  automatically  configure  itself  by  looking  for a
        "BOOTP"  server  on  your network.  (BOOTP is a standard protocol
        that  obtains  your "IP address" and other information about your
        PC  from  a  BOOTP  server.)   If there is no BOOTP server, or if
        your  PC  is not registered in its database, then you must create
        a configuration file.  

        The  configuration  file  contains  one entry per line.  A sample
        configuration  file  is  included  in  this distribution, but the
        values  MUST  be  modified to suit your particular environment or
        else KSP SLIP will not work!   

        The syntax of every entry follows the following format: 

           [ directive = [ "data" | data] ] [ # comment | ; comment ]

        I.e.,  if  a  directive is not followed by data, the directive is
        ignored.   Similary,  lines  without directives are ignored.  The
        directive is NOT case sensitive; the data IS case sensitive.   

        e.g.,   netmask=255.255.252.0
                domainslist=ksp.com    ; Our domain

        Whitespace  is normally removed from data; data containing blanks
        must  be  surrounded by quotes.  An unquoted '#' or ';' marks the
        beginning of a comment.  




        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      10



        3.1 Multiple Nodes and the "include" Directive    

        There  must  be  one WATTCP.CFG file for each BBS node since each
        node  has  to  be  configured  with  a  unique  hostname  and  IP
        address.   All  other configuration parameters are usually set at
        the  same  values  for  all nodes.  Rather than duplicating these
        common  entries  in each WATTCP.CFG file, you can set-up a master
        configuration   file   that   gets  "included"  in  each  of  the
        node-specific   files.    For  example,  the  node-specific  file
        (WATTCP.CFG) might look like: 

                include=c:\ksp\master.cfg
                hostname=ourbbspc
                myip=125.283.210.17

        This  makes it much easier to make changes since you only have to
        modify a single file (MASTER.CFG).  


        3.2 Using a BOOTP Server      

        It's  always  a good idea to have a configuration file whether or
        not   you   use   a  BOOTP  server.   If  you  choose  to  use  a
        configuration  file  and want to tell it to use the BOOTP server,
        this  option  allows  you  to specify your the IP address of your
        BOOTP server.  


                Example: bootp=129.255.0.128 

        You  should  specify the domain name manually as described in the
        next  section  since  the  BOOTP  protocol  doesn't  provide that
        information.  

                Example: domainslist=ksp.com 

        NOTE:  An  "IP  address"  is  a logical addressing scheme used on
        TCP/IP  networks  such  as the Internet.  Each computer connected
        to  the  Internet  is  assigned  a unique IP address.  Your local
        network  "guru"  or access provider should be able to provide you
        with those IP addresses you need.   

        IMPORTANT:  The  IP  addresses  given  in  this document are only
        examples.   Do  NOT  attempt to use them - they will NOT work and
        your network administrator will probably get VERY upset! 






        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      11


        3.3 Manual Configuration        

        If  you  don't  have  a  BOOTP  server,  or  if  your  PC  is not
        registered  with  a BOOTP server, then you must use the following
        directives   to   configure   KSP  SLIP.   The  values  of  these
        parameters   are  important,  and  KSP  SLIP  will  NOT  function
        properly  without  the  proper  values.   If you are not familiar
        with  the terminology, or if you are unsure of the proper values,
        please consult with your network access provider.  


        3.3.1 The PC's Host Name      

        This  is  the network name of the PC that runs your BBS (and thus
        KSP  SLIP).   If  your  BBS  is implemented by a network of PC's,
        then each PC should have its own unique host name.  

                Example: hostname=bbs 

        Note  that  the  host  name  does  not  include  the  domain name
        suffix.   For  example, the hostname of machine '"bbs.ksp.com" is
        simply "bbs".  


        3.3.2 The PC's Domain Name      

        This  is  the  network  name  of the subnet to which your PC (and
        possibly others) are connected.  

                Example: domainslist=ksp.com 

        Note  that  the  domain  name  does  not  include  the  host name
        prefix.   For  example, the domain name of machine '"bbs.ksp.com"
        is "ksp.com".  


        3.3.3 The PC's IP Address      

        This is the unique IP address assigned to your PC.  

                Example: my_ip=100.2.37.4  

        Your  local  network  "guru" or access provider should be able to
        provide  you  with  the  proper IP address of your PC.  Note that
        you  should  have  a  different  IP address for each node in your
        BBS.  

        Note:  As  an  alternative, you may also set the IP address using
        an environment variable, as in: 



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      12



                              set ksp-ip=100.2.37.4


        3.3.4 The Name Server's IP Address     

        This  is  the  unique  IP  address  assigned  to  a  network name
        nerver.   You  may  specify more than on nameserver by using more
        than one "nameserver" line.  

                Example: nameserver=111.21.108.110 

        Your  local  network  "guru" or access provider should be able to
        provide  you  with the proper IP addresses of appropriate network
        name servers.  


        3.3.5 The Router's IP Address      

        This is the unique IP address assigned to the network router.  

          Syntax: gateway = ipaddr [ , subnet [ , subnet_mask ] ] 

                Examples: gateway=129.97.176.1
                          gateway=129.97.176.2, 129.97.0.0
                          gateway=129.97.176.2, 129.97.0.0, 255.255.0.0

        Usually  the  (destination)  subnet  and  subnet mask need not be
        specified,  and  is  used to create a "default".  The other forms
        are  used  to  specify  one or more other gatewaya for particular
        subnets.  

        Your  local  network  "guru" or access provider should be able to
        provide you with the proper IP address of the network router.  


        3.3.6 The PC's Network Mask      

        Network  masks  are  used to distinguish destination IP addresses
        that  are  on  the  local  subnet  from those that are not.  This
        option may not be required, depending on your network topology.  

                Example: netmask=255.255.254.0 

        Your  local  network  "guru" or access provider should be able to
        provide you with the proper netmask if needed.  






        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      13


        3.4 TCP/IP Parameters (optional)       

        KSP  SLIP  will  work without using the following parameters, but
        they are provided if you wish to change them.  


        3.4.1 Timeouts         

        Most  network  operations (such as establishing a connection to a
        remote  host)  have a maximum time before a timeout error occurs.
        The  default  value is 30 seconds; a smaller value is unwise, but
        larger   values   may   be   necessary   for   particularly   bad
        connections.  

                Example: sockdelay=40 


        3.4.2 Maximum Segment Size (MSS)      

        The  default  value  of  MSS  is  1400.  If you know what maximum
        segment  size  means  and know what size you want, you can change
        it: 

                Example: mss=512 

                Note:  Some  Internet  access  providers  configure their
                dial-up  slip  and ppp accounts with a very small segment
                size.   You  may  need  to  set mss as low as 212 if your
                Internet connection is through such a connection.  


        3.5 SLIP Operating Parameters       

        The  remaining  parameters in WATTCP.CFG are operating parameters
        for  KSP  SLIP  that define limits and display files needed while
        KSP SLIP is running.  Each follows the format: 

                ksp-slip.<parameter>=<value> 

        where   <parameter>  and  <value>  are  replaced  by  appropriate
        strings.  

        Some  operating  parameters have counterparts in other members of
        the  KSP  family  of  network  application programs.  Rather than
        have   multiple   entries   in   the  WATTCP.CFG  file  for  each
        application,  such parameters can be specified globally using the
        format: 

                ksp.<parameter>=<value> 



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      14



        This  global setting can be overridden for a specific application
        by  using  the  application-specific form at a subsequent line in
        WATTCP.CFG.  


        3.5.1 Dynamic Parameters        

        Configuration  file  parameters  can  be  made  "dynamic".   Such
        parameters  are ignored unless activated by an associated command
        line option: 

                /CONFIG=<number> 

        where  "<number>"  is  a non-zero integer.  Dynamic configuration
        parameters  are  those that specify a number in square backets as
        in: 

                ksp-slip[<number>].<parameter>=<value> 

        The  number  specified  in the configuration parameter must match
        that  in  the  command  line  option  or  else  the configuration
        parameter will be ignored.  

        This also works for dynamic global parameters of the form: 

                ksp[<number>].<parameter>=<value> 


        3.5.2 Blocking Access to Certain Sites     

         Syntax: ksp-slip.blocked_ip_list=<pathspec> 

        Example: ksp-slip.blocked_ip_list=c:\ksp\blocked.lst 

        Purpose: Specifies  the  name of a text file containing a list of
                 blocked  IP  addresses.  No user access to sites on this
                 list will be allowed.  

           Note: Packets  addressed  to  blocked  IP  addresses  are  not
                 forwarded  to  their  destination; however KSP-SLIP does
                 return  a  type 3 ("host unreachable") ICMP error packet
                 to  the  caller's slip client software, with explanation
                 code   10   ("communication  with  destination  host  is
                 administratively  forbidden").   Although  the  caller's
                 client   software  may  present  a  corresponding  error
                 message  to  the  user,  some  (such as Trumpet Winsock)
                 will  simply  ignore  such  ICMP packets.  In the latter
                 case,  the  user  may  not  understand  why  there's  no



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      15


                 response   from   the   remote   host,   and  thus  some
                 explanation  (such  as  a  posted  bulletin)  should  be
                 provided on the BBS.  


        3.5.3 Allowing Access to a Limited Set of Sites  

         Syntax: ksp-slip.allowed_ip_list=<pathspec> 

        Example: ksp-slip.allowed_ip_list=c:\ksp\allowed.lst 

        Purpose: Specifies  the  name of a text file containing a list of
                 IP   addresses   to  which  the  users  are  allowed  to
                 connect.   No user access to sites not on this list will
                 be allowed.  

           Note: Packets   addressed   to  other  IP  addresses  are  not
                 forwarded  to  their  destination; however KSP-SLIP does
                 return  a  type 3 ("host unreachable") ICMP error packet
                 to  the  caller's slip client software, with explanation
                 code   10   ("communication  with  destination  host  is
                 administratively  forbidden").   Although  the  caller's
                 client   software  may  present  a  corresponding  error
                 message  to  the  user,  some  (such as Trumpet Winsock)
                 will  simply  ignore  such  ICMP packets.  In the latter
                 case,  the  user  may  not  understand  why  there's  no
                 response   from   the   remote   host,   and  thus  some
                 explanation  (such  as  a  posted  bulletin)  should  be
                 provided on the BBS.  


        3.5.4 Session Time Limit       

         Syntax: ksp-slip.max_mins=<number> 

        Example: ksp-slip.max_mins=30 

        Purpose: Overrides  the  time  remaining as specified in DOOR.SYS
                 if  lower.  If omitted, time remaining is that specified
                 by DOOR.SYS.  












        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      16


        3.5.5 Session Reserve Time       

         Syntax: ksp-slip.reserve_mins=<number> 

        Example: ksp-slip.reserve_mins=3 

        Purpose: Reduces  the  time available in the door so that if time
                 runs  out,  the  user  still  has a small amount of time
                 left  on  the BBS.  This is useful, for example, if your
                 BBS  offers  a  Time  Bank  so  that users can use it to
                 withdraw extra time.  


        3.5.6 Inactivity Limit        

         Syntax: ksp-slip.idle_mins=<minutes> 

        Example: ksp-slip.idle_mins=10 

        Purpose: Establishes  an  upper limit on how long the session can
                 remain  inactive  before  it is terminated.  If omitted,
                 no inactivity limit is imposed.  


        3.5.7 Minimum Baud Rate       

         Syntax: ksp-slip.minbaud=<baudrate>[,<security>] 

        Example: ksp-slip.minbaud=9600 

        Example: ksp-slip.minbaud=9600,100 

        Purpose: Specifies  a  minimum  baud  rate  required  to  use the
                 gateway,  and  an  optional  security  level required to
                 override  the minimum baud rate.  If omitted, no minimum
                 baud rate will be required.  


        3.5.8 Operating Hours        

         Syntax: ksp-slip.ophours=<hh:mm-hh:mm> 

        Example: ksp-slip.ophours=21:00-23:00 

        Purpose: To  establish  the  hours  of operation for the gateway;
                 attempts  to  use  the  gateway  at  other times will be
                 disallowed.    Times   must  be  specified  in  24  hour
                 format.   If  omitted,  the  gateway  may be used at any
                 time.  



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      17



        Note: If  start  time  is  after  the  stop  time,  the  hours of
              operation  will  be  interpreted  as  all  but those in the
              window  specified.   I.e.,  setting  ophours to 03:20-03:00
              will allow operation anytime except 03:00-03:20.  


        3.5.9 Startup Message        

         Syntax: ksp-slip.startup_msg=<filespec> 

        Example: ksp-slip.startup_msg=c:\ksp-slip\startup.msg 

        Purpose: Specifies  the  location  of  a display file sent to the
                 user  when  the  gateway is initialized.  If omitted, no
                 display file is sent.  


        3.5.10 Minimum Baud Rate Message      

         Syntax: ksp-slip.minbaud_msg=<filespec> 

        Example: ksp-slip.minbaud_msg=c:\ksp-slip\minbaud.msg 

        Purpose: Specifies  the  location  of  a display file sent to the
                 user  if the his baud rate is less than that required by
                 the  "ksp-slip.minbaud"  option (described earlier).  If
                 omitted, no display file is sent.  


        3.5.11 Operating Hours Message       

         Syntax: ksp-slip.ophours_msg=<filespec> 

        Example: ksp-slip.ophours_msg=c:\ksp-slip\ophours.msg 

        Purpose: Specifies  the  location  of  a display file sent to the
                 user  if  the  he  attempts  to use the gateway at other
                 than  the  hours  specified  by  the  "ksp-slip.ophours"
                 option  (described  earlier).   If  omitted,  no display
                 file is sent.  


        3.5.12 User Session Logging       

         Syntax: ksp-slip.log_dir=<pathspec> 

        Example: ksp-slip.log_dir=c:\ksp-slip 




        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      18


        Purpose: Specifies  the  name  of a directory where a log of user
                 sessions   will  be  kept.   The  log  files  are  named
                 KSP-SLIP.???, where "???" is the BBS node number.  


        3.5.13 SLIP Packet Monitor       

         Syntax: ksp-slip.status=<method> 

        Example: ksp-slip.status=direct 

        Purpose: Enables  local console display of SLIP packet counts and
                 selects  output method.  Options are "direct" (fastest),
                 "bios",  and  "ansi"  (slowest).   If  running  under  a
                 multi-tasker,  you may need to specify "ansi" or "bios";
                 otherwise use "direct".  


        3.5.14 Non-Standard Port/Fossil Break Detect      

         Syntax: ksp-slip.serial_port=<adr>,<irq> 

        Example: ksp-slip.serial_port=3F8,5 

        Purpose: Used  to  override serial port and IRQ values implied by
                 "COMx"    in    DOOR.SYS    to    support   non-standard
                 configurations  that  are  NOT  using  a  fossil driver.
                 Also  used  WITH  a  fossil  driver  to add serial break
                 detection  as  required to return to BBS without hanging
                 up.  

                 The  port  address  <adr>  must be specified in hex, and
                 the   interrupt   request  line  number  <irq>  must  be
                 specified in decimal.  


        3.5.15 Eliminating the Startup Count-Down      

         Syntax: ksp-slip.countdown=<yes|no> 

        Example: ksp-slip.countdown=no 

        Purpose: Used  to  eliminate the default "Press any key to begin"
                 message  and  nine-second countdown at startup.  Default
                 is 'yes'.  







        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      19


        3.5.16 Silencing the BBS console bell     

         Syntax: ksp-slip.local_bell=<option> 

        Example: ksp-slip.local_bell=disabled 

        Purpose: Used to silence the bell on the local BBS console.  


        3.5.17 Disabling the Local Screen      

         Syntax: ksp-slip.local_screen=<option> 

        Example: ksp-slip.local_screen=disabled 

        Purpose: Used  to  disable  painting  of  the local (BBS) screen,
                 thus  improving  screen  painting  speed for the caller.
                 This  option  does  not  affect  status  displays on the
                 local console.  

































        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      20


                CHAPTER 4 - INSTALLING THE SLIP DOOR COMMAND    


        Install  KSP  SLIP  as  you  would any other door program on your
        BBS.   Be  sure  you  setup the BBS to create a DOOR.SYS file for
        KSP  SLIP  when  it  runs.   (KSP  SLIP  does not need a USER.SYS
        file.)   If you are running multiple BBS nodes accessing a single
        copy  of  the  file  KSP-SLIP.EXE, then don't forget to make that
        file  (and  the  *.MSG  display  files)  read-only  using the DOS
        ATTRIB command in order to avoid sharing conflicts.  

        Most  BBS's  use  a  batch  file  to run a door.  For example, on
        PCBoard  systems you might create a door batch file called "SLIP"
        containing simply: 

                C:\KSP\KSP-SLIP 
                BOARD 

        Do  NOT  change  directories  within  this  batch file!  KSP SLIP
        expects  to  find  the  DOOR.SYS  file in whatever is the default
        directory  at  the  moment it starts to run.  That's why the name
        of  the  program  is preceeded by the name of the directory where
        it is located.  

        Of  course, you must also configure your BBS so it knows where to
        find this batch file (SLIP).  


        4.1 Command Line Parameters       

        4.1.1 The /MAXMINS Parameter       

        The  /MAXMINS  parameter  is an alternative to the same parameter
        that  appears  in  the  WATTCP.CFG  file.   It  provides  another
        mechanism  for  limiting  the maximum time a caller is allowed in
        the door.  The syntax is: 

                /MAX_MINS=<minutes> 

        where "<minutes>" is replaced by a number, as in: 

                KSP-SLIP /MAX_MINS=60 


        4.1.2 The /CONFIG Parameter       

        The  /CONFIG  parameter  is  used  in  conjunction with "dynamic"
        configuration  parameters  to  enable  or  disable  them.   For a
        complete  description  of  this  feature,  please see the section



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      21


        called "Dynamic Parameters".  


        4.1.3 KSP-SLIP.EXE Exit Codes       

        At  the  end of execution, KSP-SLIP exits with an errorlevel that
        indicates the reason for termination: 

                0       User never got past startup screen 
                1       Carrier lost (user hung up) 
                2       Break detected (intentionally sent by user) 
                3       Inactivity timeout 
                4       Session timeout 
                255     Some sort of program error condition 


        4.1.4 Checking Packet Counts (PKTCOUNT.EXE)      

        At  the  end  of execution, KSP-SLIP writes a one-line ascii text
        file  containing three numbers.  For example, the line might look
        like: 

        1534  1647 35
          |     |   |
          |     |   +--- number of bad packets received from user
          |     +------- number of good packets received from user
          +------------- number of packets transmitted to user

        The  content  of  this  file  is  overwritten  each  time you run
        KSP-SLIP.   A  companion  program  called  PKTCOUNT.EXE  has been
        provided  to  read  and  exits  with  one of these numbers as its
        errorlevel  (limited  to  255);  this  program can be used in the
        batch  file  that  runs the door for various accounting purposes.
        For  example,  you  may  not  wish  to charge a user if they were
        having  configuration  problems  with their slip client software,
        usually  indicated by lots of bad packets received and only a few
        good ones.  

        The PKTCOUNT program requires one command line argument: 

                PKTCOUNT <option>

        where  "<option>"  is  one  of "SENT", "GOOD", or "BAD".  Running
        the  program  with  no command line argument will produce a short
        usage summary.  







        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      22


                   CHAPTER 5 - INSTALLING YOUR ACCESS KEY     


        The  unlicensed version of KSP SLIP limits each user to a maximum
        of  five  minutes  per  session.   To remove this limit, you must
        purchase  an  access  key and install it as described below; once
        installed,  users will be limited only by their time remaining on
        the BBS.  

        There  are  three  parameters  that  must  be  specified  in  two
        environment  variables called "KSP-ID" and "KSP-SLIP" in order to
        install  your access key; the access key will not be validated if
        any parameter is missing.  

        The  environment  variable  "KSP-ID"  is used to specify your BBS
        name, as in: 

                      set ksp-id=Key Software Products BBS

        The  environment  variable  "KSP-SLIP"  is  used  to  specify the
        number  of BBS nodes and your access key separated by a semicolon
        as in: 

                             set ksp-slip=2;12345678

        The  access  key  is  derived  from  the name of your BBS and the
        number   of   BBS  nodes.   The  specified  key  must  match  the
        combination  of BBS name and nodes.  If not, or if you invoke KSP
        SLIP  on a node whose node number is greater than indicated, then
        the caller will be limited to five minutes per session.  






















        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      23


                 CHAPTER 6 - CUSTOMIZING THE DISPLAY FILES     


        The distribution package includes three sample display files: 

           OPHOURS.MSG     Displayed during off hours
           STARTUP.MSG     Displayed on start of gateway session
           LOSPEED.MSG     Displayed if baud rate is too low

        These   files   have  been  customized  by  the  use  of  certain
        predefined  "macros".  Some of these macros are a subset of those
        supported by PCBoard, while others are unique to KSP SLIP.  


        6.1 PCBoard Display Macros       

        The  following  PCBoard  display  macros,  plus  all of PCBoard's
        "@X##"  color control macros, may be used within KSP SLIP display
        files.   For  a  description of what they represent, refer to the
        PCBoard documentation.  

                    @BEEP@          @CLREOL@        @CLS@
                    @FIRST@         @MINLEFT@       @SECURITY@
                    @SYSDATE@       @SYSTIME@       @USER@
                    @POS:#@


        6.2 Macros Unique to KSP SLIP     

        The  following  additional display file macros are also supported
        by KSP SLIP.  

                @SLIPIP@                The IP address of the BBS node
                @SLIPNAME@              The SLIP node's network name
                @DCESPEED@              Current DCE (carrier) speed
                @DTESPEED@              Current DTE (PC-Modem) speed
                @EXPIRETIME@            Expire time in HH:MM format
                @IDLEMINS@              Maximum inactivity time
                @MINDCESPEED@           Minimum DCE (carrier) speed
                @OPHOURS@               Hours of operation
                @OVERRIDE@              Override security for mindcespeed


        6.3 Justification and Spacing       

        Any  of  the text insertion macros used in KSP SLIP display files
        can  appear  in  one  of four forms as discussed in the following
        paragraphs.    These  options  allow  you  to  precisely  control
        spacing,  and  allow  you  to  draw a box around a message - even



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      24


        when replacement text within a line has a varying length.  


        6.3.1 No Justification        

         Syntax: @<keyword>@ 

        Example: @USER@ 

        Purpose: Inserts  the  replacment  text, using as many columns as
                 are necessary.  


        6.3.2 Left Justification        

         Syntax: @<keyword>:<number>@ 
             or: @<keyword>:<number>L@ 

        Example: @USER:15@ 
             or: @USER:15L@ 

        Purpose: Insert  the  replacement text, left justifying it within
                 a   field   whose  width  is  specified  by  the  number
                 following  the colon.  If more columns are required than
                 provided  in  the  field  width,  the field is expanded.
                 macro.  


        6.3.3 Center Justification        

         Syntax: @<keyword>:<number>C@ 

        Example: @USER:15C@ 

        Purpose: Insert  the  replacement  text,  centering  it  within a
                 field  whose  width is specified by the number following
                 the  colon.   If more columns are required than provided
                 in the field width, the field is expanded.  


        6.3.4 Right Justification        

         Syntax: @<keyword>:<number>R@ 

        Example: @USER:15R@ 

        Purpose: Insert  the replacement text, right justifying it within
                 a   field   whose  width  is  specified  by  the  number
                 following  the colon.  If more columns are required than



        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      25


                 provided in the field width, the field is expanded.  


        6.4 The DISPLAY Program       

        Included  among  the distribution files is DISPLAY.EXE, a program
        that  helps  design  a  display  file by allowing it to be viewed
        offline.  The command line syntax is: 

                          DISPLAY [-g] [-7] <filespec>

        Where:  <filespec>   Is the name of the display file.
                             The filename extension defaults
                             to ".MSG" if omitted.

                []           Denotes an optional argument.

                -g           Enables (color) graphics and
                             ANSI control sequences; requires
                             ANSI.SYS to be installed.
                             Default is disabled.

                -7           Replaces 8-bit graphics characters
                             with suitable 7-bit alternatives.




























        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      26


                        APPENDIX 1 - HOW TO REACH US     


        The  Key Software Products BBS/FAX number (415-364-9847) operates
        24   hours   a   day,  7  days  a  week.   Software  at  our  end
        automatically  determines whether an incoming call is data or FAX
        and will operate accordingly.  

        If  you have access to electronic mail, you can send us a message
        via any of the following: 

        On COMPUSERVE, send mail to:

                >Internet:tech.support@ksp.com

        On PRODIGY, send mail to: VGDC59A

        On Internet, UUCP, or Bitnet, send mail to:

                tech.support@ksp.com

        On Fidonet, address mail to "UUCP" at nearest fidonet site which
        provides a gateway to Internet, such as 1:105/42.

                1st line of message: To: tech.support@ksp.com



























        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      27


                APPENDIX 2 - GETTING UPDATES VIA THE INTERNET    


        The  main  distribution  file  is KSPSLP??.ZIP, where "??" is the
        version  number.  You can retrieve this file via anonymous ftp at
        "scizzl.scu.edu",  directory "ksp".  Please note that there is no
        "e" at the end of "scizzl".  

        This  file  is also available from the KSP BBS, either by calling
        in   and   downloading,   or  via  e-mail  using  the  "LISTSERV"
        capabilities of the BBS.  

        To  use  LISTSERV,  you  must  send  a  message  addressed to the
        Internet  address  listserv@ksp.com.  The message must contain an
        LISTSERV  command  entered  as a single line of text, and it must
        be  the first line in the message. The LISTSERV commands that are
        supported include: 

        Command: HELP tlbmm-l
        Purpose: Returns an text file with help information about LISTSERV.

        Command: DIR tlbmm-l
        Purpose: Returns an e-mail message listing all of the file 
                 directories on the BBS by number and description.

        Command: LIST tlbmm-l 1
        Purpose: Returns an e-mail message listing all of the files in
                 directory #1 of the BBS.

        Command: GET tlbmm-l KSPSLP34.ZIP
        Purpose: Returns an e-mail message containing a uuencoded version of
                 the file KSPSLP34.ZIP.  To extract the file, you must save
                 the message as a file on your system, edit out the e-mail
                 header at the beginning of the file, and then use a program
                 called UUDECODE (commonly available on Unix) to convert the
                 uuencoded version back to the original ZIP format, and then
                 (finally) use PKUNZIP to extract the contents of the file.















        Copyright (C) 1995-96, Key Software Products. All Rights Reserved



        Feb 20, 1996           KSP SLIP (tm) v3.4                      28


                         APPENDIX 3 - LEGAL STUFF       


                                LIMITED WARRANTY

        This  software  is provided 'as is' without warranty of any kind,
        either  expressed  or  implied, including, but not limited to the
        implied   warranties   of   merchantability  and  fitness  for  a
        particular  purpose.   The  entire  risk  as  to  the quality and
        performance of the program is with you.  

        Some  states do not allow the exclusion of implied warranties, so
        the  above  exclusions may not apply to you.  This warranty gives
        you  specific  legal  rights  and  you may also have other rights
        which vary from state to state.  

        Key  Software  Products  has  taken  due  care  in  preparing the
        documentation  and  software  included  in   to  ascertain  their
        correctness  and  effectiveness.   However, Key Software Products
        does  not  warrant  that  operation  of  this  software  will  be
        uninterrupted  or  error  free.   In  no event shall Key Software
        Products  be  liable  for  incidental or consequential damages in
        connection  with  or  arising out of the furnishing, performance,
        or use of this software.  


                                     LICENSE

        You  MAY  use  this software on any computer or computers in your
        possession.   The licensed version is registered for use on up to
        a  fixed  number of BBS nodes running on multiple machines and/or
        multiple multi-tasking processes.  

        You  MAY  copy this software into any machine readable or printed
        form  for  backup or modification purposes in support of your use
        of the software.  

        You  MAY  distribute  the original unmodified, unlicensed version
        of  this  software,  but you may not charge a fee exceeding $5.00
        to  cover  the  cost of duplicating, shipping, and handling.  You
        may NOT distribute a licensed version of this software.  

        You  may  NOT  use,  copy, modify, sublicense, assign or transfer
        this  software  and  its license, or any copy or modification, in
        whole  or  in  part,  except  as  expressly  provided for in this
        license.  






        Copyright (C) 1995-96, Key Software Products. All Rights Reserved