FOSSIL driver over TCP/IP rlogin/telnet protocols.
                                 Version 1.2

        RLFOSSIL   is   an   implementation   of   multi-line   serial  port
  driver corresponding to Fido/Opus/Seadog level 5 specification and  simple
  HAYES-compatible modem emulator in one. It allow to use many  applications
  usually worked through serial lines and modems in Internet space, or in
  IP-based local net. RLFOSSIL provide emulation of HAYES-modem and FOSSIL
  driver from application's direction, and rlogin/rlogind or telnet/telnetd
  emulation (more exactly - rlogin & telnet compatible handshake ) using IP
  services numbers 513 & 23 for IP-based net's direction. Number of emulated
  channels (ports & modems): 4. RLFOSSIL tolerate combined work with other
  FOSSIL drivers (X00,BNU etc.). RLFOSSIL support as incoming as outgoing
  calls. This programm is NOT A TSR, what more easy to unload.

        Possible use: for provide access of any terminal emulators to
  IP-based net, for provide work of any mailers & communication script
  through IP-based net, for provide access to MS-DOS based BBS-es from
  MS-DOS and UNIX users through IP-based net (using same emulator or rlogin
  or telnet from any TCP packet, for ex. PC/TCP, CUTCP Telbin, Kermit etc.).
  You can use as ethernet as SLIP interface (only Class 1).

  Required:
          IBM-PC XT/AT 8086 and above
          MS-DOS 3.3 and above
          Packet driver class 1 (Ethernet).

  *) For information. You can get Ethernet paket drivers free, using
     anonymous ftp to:
       oak.oakland.edu                      /SimTel/msdos/pktdrvr
       ftp-ns.rutgers.edu                   /pub/msdos/packet-drivers
     SLIP Class 1 driver (EtherSLIP) you can get using anonymous ftp to:
       owl.nstn.ns.ca                       /pub/pc-stuff/packet/etherslip

  Supported multitaskers:
          TopView
          DesqView
          Windows 3.1, and 3.11 (for Workgroups).

  Driver was test with follow communication software:
          Terminate     1.41g
          TeleMate      4.0
          UUPC          5.0
          FrontDoor     2.02
          Remote Access 1.01
          Maximus       2.0
          T-Mail        2.0
          Kermit        3.13,3.14

  Usage:
    RLFOSSIL.EXE start_portn ports progname [idname]

  where: start_portn - number of first serial port what will emulated
                       (0 - COM1:, 1 - COM2: etc).
         ports       - number of ports what will be emulated ( 1 - 4 ).
         progname    - programm name what will be launched after start of
                       driver, when this programm will be terminated, driver
                       will unload. This parameter can include arguments for
                       launched programm. In such case it must be placed 
                       in "".
         idname      - your default login name for outgoing calls
                       (if parameter missed, idname will get from WATTCP.CFG).

  examples of usage:
  Usage Telemate with 1 virtual modem on COM1:
    RLFOSSIL.EXE 0 1 TM.EXE

  Usage Telemate script file with 1 virtual modem on COM3: , and default
  login name "guest"
    RLFOSSIL.EXE 2 1 "TM.EXE SCRIPT.TMS" guest

  Usage Maximus with 1 virtual modem on COM5:
    RLFOSSIL.EXE 4 1 "MAX.EXE -W"

  Usage multiline BBS under WINDOWS with 4 virtual modems on COM5: - COM8:
    RLFOSSIL.EXE 4 4 WIN.COM
  <Files BBS.BAT must be placed in STARTUP window>

  Usage multiline BBS under DV with 4 virtual modems on COM5: - COM8:
    RLFOSSIL.EXE 4 4 DV.COM
  <Files BBS.BAT must be launched from STARTUP script>

  Driver X00 or BNU for real modems must be started early and ports of
  virtual modems must be choosed different with real modems.

  commands of virtual modem:
  ATDP 192.168.5.5
    outgoing connection to 192.168.5.5
  ATDP 192,168,5,5
    the same as previous (for compatibility with phone numbers)
  ATDP machine.my.net
    outgoing connection to machine.my.net (nameserver must be defined in
    wattcp.cfg).
  ATDP guest@192.168.4.9
    outgoing connection to 192.168.4.9 as user "guest"
  ATDP root@xserv
    outgoing connection to xserv (domain name will get from WATTCP.CFG) as
    user "root"
  ATA
    answer on incoming calls (only after "RING")
    all other commands beginning with AT - answer OK but do nothing.
  ATS<reg>=<val>
    where <reg> - number from 0 to 15 (now used only first 5).
          <val> - decimal value (0-65535).
    set regisrer <reg> value to <val>.
    Registers:
      0 - autoanswer. Non-zero value enable autoanswer, zero value disable
          it.
      1 - IP service port number for incoming calls. (default value for
          rlogin - 513, for telnet - 23, 0 - allow both).
      2 - delay between "ATA" & "CONNECT 9600/TCP/IP" in 55ms. ticks.
      3 - delay between connection lost & "NO CARRIER" in 55ms. ticks.
      4 - handshake mode. 0 - no handshake (simple socket to socket
          connection), 1 - rlogin handsahke, 2 - telnet handshake,3 -
          auto choose.
      5 - IP service port number for outgoing calls. (default value for
          rlogin - 513, for telnet - 23).
  ATZ
    re-init socket. Recommended after change of register values.

  Combined strings like as "ATS1=23S4=2Z" are permitted.

  virtual modem messages:
  NO DIALTONE - cannot resolve hostname (may be wrong nameserver?)
  NO CARRIER  - host or service not available, or no route to host,
                (after ATDP), or connection closed by programm or
                another host (after connection), or ATA was entered
                not after RING.
  CONNECT 9600/TCP/IP - connection established (after ATDP or ATA).
  RING        - incoming connection established, but you must enter
                ATA to confirm it.
  OK          - Standard modem answer on most commands.

  maximal transfer speed:
    limited only by processor's power & inreface card.
  Internal buffers, FOSSIL level:
    1024Bytes -TX, 1024Bytes -RX
  Internal buffers, TCP level:
    2048Bytes -TX, 2048Bytes -RX
  config file:
    wattcp.cfg - see inside

  History:
  1.0 - first distributed release (after one month of testing).
  1.1 - never was distributed.
  1.2 - current version. Corrected some bugs. Modified algoritm of
        virtual modem. Now it work with T-MAIL & Maximus. Added S and Z
        commands of virtual modem. Autoanswer implemented. Change of
        IP port number implemented. Telnet emulated now!!! Dynamic channel
        map. Only 3Kb more than previous version.

  Special thanx to: Ernest Seleznyov, Fyodor A. Evseev,Daryl Collins,
                    Madis Kaal, Roma Kuzmin, John Fluharty, Markus Bank
                    for his remarks.

  All remark allowed to Andrew Sapozhnikov (Sapa),
                        root@hq.icb.chel.su.