Stomper  3.21
                       
                       
                       
                       

                       
                  Modemsharing-Software for Novell or Netbios
                                based networks
                       
                       
                       
                                 DOS/Windows
                       
                       
                       
                       
                       
                      (C) 1994,1995 Pflug Datentechnik.
                       


Hardware and software requirements for
installation:

-   network, preferably Personal NetWare,
    Novell NetWare lite, NetWare >=3.11 or
    Netbios network (Lantastic)
-   minimum DOS 3.3
-   Windows 3.1 if available
-   1 serial interface per modem server, if
    possible FIFO buffered (UART 16550)
-   Processor depending on number of modem
    servers on one computer, minimum AT
    (80286)


1 The Concept
1.1 What is a modem-/ISDN-server?
1.2 Server-Client Operation
2 Installation
2.1 fast installation
2.2 Complete Installation
 2.2.1 The Queuemanager
 2.2.2 The modem server
 2.2.3 The Client
 2.2.4 Windows-Modemsharing
 2.2.5 The ISDN server
 2.2.6 The ISDN-client
3 Select Specific Modemservers By Different Ports
4 the Cooperative Mode
5 Queue Management
6 The Monitor
7 Programs Using INT 14 (BIOS)
8 Stomper And Windows For Workgroups / Windows 95
8.1 Microsoft Network
8.2 Novell Network
9 Installation On A Netware Fileserver (NLM-Version)
10 Applying Access Rights
Appendix A Suitable Programs
Appendix B NETINFO.EXE
Appendix C Tips
 1. Telemate
 2. Terminate
 3. Telix For Windows
 4. pcAnywhere
Appendix D Troubleshooting
Appendix E What is a FOSSIL driver?
Appendix F What is a network fossil driver?
Appendix G How to order
Appendix H Support




1   The Concept
~~~~~~~~~~~~~~~

1.1 What is a modem-/ISDN-server?
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

The modemserver is a small program, that accesses the device directly, that
should be made available throughout the network.
There may be more than one modemserver (or ISDN-server) on one computer
oder there may be several servers spread over the whole network.
When a client accesses a modemserver, all communication between
communication software (terminal, fax, ...) and the modem is directed
through the network.
Stomper is responsible for repacking the data suitable for the network, to
send it and to convert it back. It appears to the user as if the modem was
attached directly to his local workstation.
Often the modemserver is compared to a printerserver. This is not quite
correct. The main difference is, that the printer server is "batch-driven".
This means, that a print job is placed into a temporary file, which is
read by the printer server whenever it is ready and the contents then are
sent to the printer.
A modemserver works online. All data is sent to the device immediately.
Additionally all line-control information is passed on.




1.2 Server-Client Operation
~~~~~~~~~~~~~~~~~~~~~~~~~~~

As soon as a client requests an available modem or an ISDN-adapter (this
happens automatically, when your communications software is started),
the client-program (NETFOS, NFCAPI, ...) searches for a modemserver and
initiates a session.
From this moment on, the server is not available for other stations. It is
reserved for this one client.
At the end of the session, the server will get released.



2   Installation
~~~~~~~~~~~~~~~~

2.1 fast installation
~~~~~~~~~~~~~~~~~~~~~


First of all, the queue manager

    STMGR

is loaded on any available workstation in the network. This could be a
computer not integrated in the modem sharing, or a modem server.
If you intend to run Stomper in a Novell Netware 3.11 or higher network, we
strongly recommend to install STMGR.NLM on the fileserver rather than
installing the queuemanager on a DOS station. Refer to chapter Installation
on a NetWare fileserver (NLM-version) on page 28.
Please read chapter 4, waiting queue administration, in this context.


1.  Modemsharing
~~~~~~~~~~~~~~~~

     To install a modemserver, load

          STOMPER /Px    (x = number of the port ; 1 = COM1)

     To install a modem client, load:

          NETFOS /Px     (x = number of the port)

          NETFOS now serves all applications, that use a FOSSIL
          driver. For BIOS-INT14 or Windows-COMM.DRV,
          read the next chapter.

2. ISDN-Sharing
~~~~~~~~~~~~~~~

To install an ISDN-server, load:

    STISDN

To install an ISDN-client, load:

    NFCAPI

Now your ISDN-applications can access NFCAPI(CAPI v1.1)



2.2 Complete Installation
~~~~~~~~~~~~~~~~~~~~~~~~~

Stomper either works with the IPX- or the Netbios protocol. In Novell
networks IPX is loaded already, so nothing else has to be done.
Others (for example Lantastic: AILANBIO), however, require the installation
of the Netbios driver. Most network types (NetWare/NetWare Lite,
Lantastic...) supply Netbios. With the use of Netbios Stomper becomes
independent of the available network.



2.2.1    The Queuemanager
~~~~~~~~~~~~~~~~~~~~~~~~~

The Queuemanager performs the following tasks:

1.  "Tracker", observes the status of all modem servers installed in the
    network, containing the following information: Status of the modem
    server (busy/free), the Client (Netfos) which is presently served,
    number of bytes transmitted in a session.
    This information is analysed and displayed for example by STMON, the
    monitor program.

2.  "Queue manager", allocates free modem servers to the clients. In order
    to avoid chaos, the queue manager can only exist once in the network.
    When STMGR is loaded for a second time in the network, only the tracker
    part will be loaded automatically.

3.  IPX routing. The transmitter must always know the destination network in
    order to transport IPX packets over several network segments. STMGR
    therefore gives his address to all routers in the network (the file
    server can also work as a router and therefore adds this address to its
    bindary). Stomper identifies this address by ordering it form the nearest
    router. When the queue manager allocates a modem server to a client, the
    network address of stomper is supplied to the client.

4.  Logging. If the option /L is specified, a log file will be generated,
    that logs all actions.

5.  Stationrestrictions (only STMGR.NLM) See Chapter Applying access rights.



Command line parameters

If you intend to run Stomper in a Novell Netware 3.11 or higher network, we
strongly recommend to install STMGR.NLM on the fileserver rather than
installing the queuemanager on a DOS station. Refer to chapter Installation
on a NetWare fileserver (NLM-version) on page 28.


    STMGR [/F] [/U] [/L.....] [/A]

    /U   is given to remove an installed STMGR from the memory

    /F   the queue manager uses netbios, even if IPX is loaded

    /L  generates a logfile.
        examples:

        STMGR /LSTOMPER.LOG       generates STOMPER.LOG in the directory, in
                                  which STMGR.COM resides.

        STMGR /LC:\TEMP\ST.LOG    generates C:\TEMP\ST.LOG

    /A  Allow "autoattach". See also: NETFOS /A

please note, that if you wish to create a logfile in a desired directory,
you must specify a complete path!



2.2.2    The modem server
~~~~~~~~~~~~~~~~~~~~~~~~~

The modemserver accesses the modem (or another device connected to the
RS-232-port).
Apart from the application data, the line-condition will be updated whenever
necessary. This condition includes DCD (Data Carrier Detect), DTR (Data
Terminal Ready), RI (Ring Indicator), DSR (Data Set Ready), RTS (Ready To
Send) and CTS (Clear To Send).

For DOS there are 2 variants of the modemserver:

ú   STOMPER.COM              accesses the serial port directly
ú   STOMPERF.COM             uses a FOSSIL driver to communicate with the
                             hardware

Using the latter, makes it possible to share any communications-hardware in
the network, as long as there is an apropriate FOSSIL driver available
(like CFOS for ISDN).


For information on how to install a modemserver on a NetWare fileserver,
refer to chapter Installation on a NetWare fileserver (NLM-version)


Command line parameters


STOMPER [/Px] [/Na] [/Lxxxxxx] [/U] [/F] [/Qxx] [/Bxxxx] [/Caaa...] [/R]

The parameters are optional:

    /P   selects the COM port for the modem,
         for example /P2 for COM2. If omitted,
         COM1 is selected automatically.

    /U   is given to remove any already
         installed STOMPER from the memory.
         This is only possible while Stomper
         is not active.

    /F   STOMPER is told to use Netbios
         exclusively (even if IPX is loaded)

    /Q   for unconventional IRQs. /Q7 => IRQ7

    /B   for unconventional ports. /B3E8  =>
         Port 3E8

    /C   Cooperative mode: see chapter 3,
         Cooperative mode

    /L   Lock Baud. Independent of the bps
         rate chosen by the application
         (terminal program,...), Stomper
         always selects automatically the bps
         rate of this parameter, for example

         /L57600 (locked).

         Attention: Windows applications
         ignore this parameter!

    /N   one single character is added to this
         option (for example one letter or one
         digit), giving the modem server an
         individual identification. Each modem
         server has to be identified
         individually (several modem servers
         on one computer have individual
         characters).

    /R   ensures RTS/CTS data flow control.
         This is very helpful, for example if
         you encounter problems when sending
         with Winfax. Normally this option
         does not influence any other
         applications.

    /Z   16550 FIFO buffer control
                /Z0 FIFO off
                /Z1 FIFO on 1 byte threshold
                /Z4 FIFO on 4 byte threshold
                /Z8 FIFO on 8 byte threshold (default)
                /Z14FIFO on 14 byte threshold

It is not recommended to use this parameter!
Stomper normally selects an 8 byte threshold for the FIFO buffer, which
causes the least potential errors.
On very slow PCs (286 - 6 MHz), it may be necessary to use /Z1.



2.2.3    The Client
~~~~~~~~~~~~~~~~~~~

The modem client provides access to a modemserver. All applications that
can use a FOSSIL driver or BIOS-INT14 (option /I) can use it to access a
network modem.

Command line parameters


NETFOS [/Px] [/U] [/I] [/F] [/Naaa...] [/A|/A+]

    /P   specifies which COM port will be
         redirected, for example. /P2 for
         COM2. COM1 is chosen automatically
         when this parameter is not used.

    /U   is given to remove an installed
         NETFOS from the memory.

    /I   This parameter is necessary to
         redirect programs which communicate
         using the BIOS-INT-14. With this
         parameter given, Netfos finds out if
         an application is able to serve a
         fossil interface, and reacts
         accordingly.

         Without this parameter Netfos can
         only serve Windows programs or
         programs which support a fossil
         driver.

    /F   Netfos uses Netbios (even if IPX is
         loaded)

    /N   All modem servers wanted in the
         network are listed here. When for
         example. /N123 is given, the
         queuemanager selects the first
         available modem server from the list.
         The priority is from left to right,
         so that the queuemanager selects
         STOMPER /N2 when STOMPER /N1 is
         occupied.
         This option is invalid (and
         meaningless) In the 1-server version.

    /A   "Autoattach"-mode. When a modemserver
         is assigned to a user after he was
         placed in the queue (waiting for a
         modemserver to become available),
         this option suppresses the message
         "Connected to modemserver". So the
         connection will be established
         without interaction. For both /A and
         /A+ STMGR must have been loaded with
         the option /A as well!

    /A+  Same as /A, but additionally the user
         will be placed into the waitingqueue
         automatically, in case there is no
         modemserver available. This mode runs
         completely unattended.

Note that the parameter /Px does not have to be identical for the two
drivers. For Stomper /Px defines the interface which is physically connected
with the modem. For Netfos /Px defines only the interface which is addressed
by the terminal program.



2.2.4    Windows-Modemsharing
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

In the file SYSTEM.INI (Windows directory) change the following line in
the [boot]-section:

comm.drv=comm.drv

change into

comm.drv=stcomm.drv

Make sure that there is only one line of comm.drv=...!!

Attention!
After Winfax installations comm.drv is usually changed into wfxcomm.drv.
This can be replaced without problems.

STCOMM.DRV  should be placed on a DOS path or in a windows directory.
Alternatively, the whole path can be given.



2.2.5 The ISDN server
~~~~~~~~~~~~~~~~~~~~~

The ISDN server (STISDN) makes a CAPI accessible by the clients (NFCAPI).
An STISDN can only serve one client at a time. To let more than one client
access the CAPI at the same time, STISDN has to be loaded multiple times.
These can use the same CAPI, depending on how many applications this CAPI
can support (usually 2 to 4).

Command line parameters


STISDN [/Na] [/U] [/F] [/M...] [/Kn]


    /U   is given to remove any already
         installed STISDN from the memory.
         This is only possible while STISDN is
         not active.

    /F   STISDN is told to use Netbios
         exclusively (even if IPX is loaded)

    /N   one single character is added to this
         option (for example one letter or one
         digit), giving the modem server an
         individual identification. Each ISDN
         server has to be identified
         individually (several ISDN servers on
         one computer have individual
         characters).

    /M...    defines, how much memory is
             reserved for communications. The
             default is 16384 Bytes. Values from
             4000-65500 Bytes are accepted.
             The optimum depends on the software
             you will be using and the number of
             concurrent ISDN-connections. The
             default value usually is enough for 1
             application with channel-bundeling or
             two concurrent applications using
             each a single ISDN-connection.

    /Kn  Tells STISDN to use ISDN-adapter number n.
         If no adapter number is given, 0 is assumed
         (first adapter)


2.2.6  The ISDN-client
~~~~~~~~~~~~~~~~~~~~~~

The ISDN cclient (NFCAPI) provides applications with a virtual CAPI v1.1-
interface. Up to 4 applications can be serviced by the same NFCAPI.


Command line parameters


NFCAPI [/U] [/F] [/Naaa...] [/A|/A+]

    /U   is given to remove an installed
         NFCAPI from the memory.

    /F   NFCAPI uses Netbios (even if IPX is
         loaded)

    /N   All ISDN servers wanted in the
         network are listed here. When for
         example, /N123 is given, the
         queuemanager selects the first
         available ISDN server from the list.
         The priority is from left to right,
         so that the queuemanager selects
         STISDN /N2 when STISDN /N1 is
         occupied.
         This option is invalid (and
         meaningless) In the 1-server version.

    /A  "Autoattach"-mode. When a ISDN server
         is assigned to a user after he was
         placed in the queue (waiting for a
         ISDN server to become available),
         this option suppresses the message
         "Connected to ISDN server". So the
         connection will be established
         without interaction. For both /A and
         /A+ STMGR must have been loaded with
         the option /A as well!

    /A+  Same as /A, but additionally the user
         will be placed into the waitingqueue
         automatically, in case there is no
         ISDN server available. This mode runs
         completely unattended.


3   Select specific modemservers by different ports
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

Example:

You have 5 modem-/ISDN-servers installed in your network:

ú   three modems with IDs 1, 2 and 3
ú   two ISDN-lines with IDs 4 and 5

Of course you will want to use an ISDN-line, when you need an ISDN-line
and a modem line, when you need a modem line. You can do this by simply
entering the following command line:

NETFOS /P1(123) /P2(45)

When your Application addresses COM1, you will get connected to
modemserver 1, 2 or 3, whichever is available. When your application uses
COM2, one of th ISDN lines will be selected.

Note that there is no option /N specified, since this is completely replaced
by the values in brackets. You can specify up to 4 ports.

Of course you can use this method to distinguish different modemtypes as
well - ISDN was chosen as a typical example of different transport media.



4   The Cooperative Mode
~~~~~~~~~~~~~~~~~~~~~~~~


This mode - under certain circumstances - enables the use of another
software (for example a mailbox) on the modem server - sharing the port
cooperatively with Stomper.

Parameter: /Cxxxxx

xxxxx stands for any modem command. At the end of a session this command is
sent to the modem in order to re-initialize it. CR/LF is added to this
string (for example. ATZ), automatically.

Thus the modem server can run a mailbox, which will be stopped automatically
when a client in the network demands the modem. While a caller is logged
into the mailbox, Stomper is inactive.

In order to avoid fatal failures on the computer, please read the following
lines even if this sounds a bit technical:

For safety reasons a network-modem demand is rejected, when the CD signal
is active, for example, when someone is logged into the mailbox. Stomper
will also be blocked for another 60 seconds after the last ring.
This mode has to be handled with care, as it is quite rude to block an
application just like that, but this can be done for example with FrontDoor
and Remote Access.

As during the blocking of the modem the bps-rate could be changed, at the
end of such a session Stomper sends an optional command (see above, "/Caaa")
to the modem in order to set the correct bps rate. For this, the modem must
have an automatic baudrate identification.

In the cooperative mode Stomper MUST NOT BE LOADED in the high memory
area(UMB), due to the following:

The computer will be stopped at an appropriate time, that is in the moment
of a timer interrupt (produced by the computer 18 times per second).

"Appropriate" means:

1.  there is no hard disk or disk access
2.  Windows is inactive
3.  The program interrupted is placed in the memory above stomper and
    under the high memory area from A000:0000 on.

No. 3 ensures that no IPX routine has been interrupted.
As Stomper depends on IPX, it would not dare to touch this without being
affected personally. As Stomper needs the IPX (or Netbios) drivers, they
are normally placed in a lower memory section or in an UMB. But if Stomper
has also been loaded in the high memory area, there is no certainty where
the network drivers are placed related to Stomper.

It is possible that the interrupt does not appear. This happens for example.
when the command line in DOS is used, which is mainly executed in
COMMAND.COM (below Stomper) or in BIOS (>A000). The use of the interface is
not affected in this case.





5   Queue Management
~~~~~~~~~~~~~~~~~~~~


In order to enable a precise access to one or several modem servers in the
network, the program

STMGR.COM

has to be loaded on one computer (any) in the network. STMGR.COM should
already be active in the network, before a Client (Netfos) or modem server
(Stomper) is loaded. Preferably this program should be installed on a
modem server. If you are working with Novell Netware, the best choice will
be the Fileserver (STMGR.NLM)

This program operates completely in the background and does not require
much memory.


The queue manager's strategies

When a client demands a modem server, the queue manager tries to allocate
a free modem server which is selected by NETFOS /Naaa...(from left to right).
In case all modem servers are busy, the client computer receives the
following message:

No modemserver available. Queue in?       Y/N

After confirming Y, the following message appears:

Queued in. Wait in foreground?         Y/N

Now there are two possibilities:

1.  "Wait in the background" (N) tells the application that no fossil
    driver is installed (not recommended for pure BIOS INT14 applications).
    The computer can be used and as soon as a modem server is free, the
    following message appears:

    Connected to modem server    (ENTER)

The queue manager marks the modem server as "reserved". The user has
1,5 minutes to start his application and to use the modem server.


2.  While waiting in the foreground, the following message appears

    Waiting for modem server...    (ESC)

    In the meantime the computer cannot be used for other applications.

Under windows this process is executed accordingly, but only the
application in use is paused.





6   The Monitor
~~~~~~~~~~~~~~~

The monitor (STMON.EXE) provides an overview over the modem servers
installed in the network and the proceedings can be observed. The monitor is
started by loading

STMON

As STMON displays the information obtained from the tracker, it depends on
STMGR.COM being loaded. If STMGR is not already in memory, the monitor will
load it automatically. For this, however, STMGR.COM must be either

    -   in the same directory as STMON.EXE or
    -   in the DOS path.

Attention: The monitor must not be started in a DOS box under windows!

The monitor displays ten sections on the screen, each containing information
of an individual modem server.

Field identifications:

-   Network address - individual address in the network which is preset by
    the network adaptor. In order to obtain a better overview, a file called

    NODES.LST

    can be created, in which names are allocated to the network addresses.
    An example for such a file:

    924e32a  John's abacus
    80ca23e5 venus

    ... allocating the names "John's abacus" and "venus" to the according
    network addresses. John's abacus and venus will replace the cryptic
    address names on the monitor.

-   Served interface - the serial interface served by the modem server
    or CAPI

-   Status - status of the modem server.
    Possible states:

    - free           the modem server is available at the moment
    - Ser. <Client>  the modem server is just serving the client named
                     <Client>
    - Res. <Client>  the modem server is presently reserved for the client
                     <Client>.
    - locally in use The modem server is presently used locally in the /"C"
                     mode         (for example a user in the mailbox)

-   Sent / received bytes - number of bytes transmitted in the current
    session. This information will be held until the start of a new session.

-   Identification - the identification of the modem server (/Na).




7   Programs Using INT 14 (BIOS)
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~


The fossil driver is to be understood as an extension to the BIOS-INT 14
interrupt. However, Stomper expects that the software used initializes the
fossil driver (not necessary with BIOS routines).
For programs only using BIOS-INT 14, NETFOS has to be loaded with the
parameter /I.
With pure INT 14 applications, Stomper always switches to RTS/CTS data flow
control.

Approximately 20 seconds after the end of an "INT-14 program" the modem
server becomes available for others again.

When using fax software, which communicates via INT 14, it is absolutely
necessary to lock Stomper on an appropriate rate. The ideal bps rate depends
on the modem used.
Standard modems transmit faxes with a rate of up to 14400 bps, or 19200 bps
on the phone line. In this case the bps rate has to be locked on 19200 bps.
Most modems accept a higher rate, for example 57600 bps, when transmitting
faxes.

For modems with a maximum baud rate of 9600 bps, Stomper should be locked
on 9600 bps (see parameter /L on page 6).



8   Stomper and Windows for Workgroups / Windows 95
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

A "real" Windows 95 version should be available december 95



WfW and Windows 95 normally load their own network drivers. This means, in
these cases, there are no network protocols available prior to loading
Windows.
In case you are running Netware or any network with DOS-drivers, you can
skip this chapter.

Create the file WINSTART.BAT in your Windows-directory, like

-----------------------------------
NETFOS /P1
-----------------------------------

The batchfile WINSTART.BAT will be executed by Windows after all
system-drivers have been loaded (including network drivers).

STCOMM.DRV should be loaded as described in chapter "Complete Installation"

Be aware that this version of Stomper only supports 16-bit applications!
New 32-bit software uses a different driver.


8.1 Microsoft Network
~~~~~~~~~~~~~~~~~~~~~

Make the following changes to your Windows network setup:

Defaultprotocol:   NetBEUI

NCBS=255

NetHeapSize=20


8.2 Novell Network
~~~~~~~~~~~~~~~~~~

Make the following changes to your Windows network setup:

Defaultprotocol:   IPX/SPX

SPX Connections = 60



9   Installation on a NetWare fileserver (NLM-version)
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~


Copy STMGR.NLM and STOMPER.NLM to the SYS:SYSTEM directory.

To install STMGR.NLM on the fileserver, enter

load STMGR

at the console.

To install a modemserver, you will need to install an asynchonous
I/O-driver first. This requires the module AIO.NLM and any AIO-driver.
The appropriate AIO-driver for standard RS232 is AIOCOMX.NLM. You can
download AIO-drivers from Compuserve NOVLIB or from our BBS. Several
AIO drivers for Hostess, Digiboard, etc. are available.

For available commandline options recognized by STOMPER.NLM and STMGR.NLM,
refer to chapter Complete Installation on page 6.

Note the different format of STOMPER-option /P for port selection:

/P<hardwaretype>,<boardnumber>,<portnumber>

The three values are shown when you load the AIO-driver. If you are not
sure what to type, you can load STOMPER.NLM without the /P-option.
Stomper will let you select the desired port and then display the
appropriate commandline you should use in future.

If you posess a multi-modemserver version of Stomper, you can load
STOMPER.NLM multiple times.

If you type

unload stomper

at the system console, you will disable all running modemservers.

Caution!!

-   There is a bug in the Netware 3.x / 4.0x (not 4.1) -
    SPX-protocol. This bug known to STOMPER.NLM and
    Stomper tries hard to avoid problems that might
    arise.
    But wo do strongly advise you to install the
    following Novell-patches:

    PATCHMAN.NLM
    SPXDDFIX.NLM
    SPXFIX2.NLM

    These three modules are contained in the
    archive STRTL3.EXE, that can be downloaded free
    from Compuserve NOVLIB or from our support BBS.

-   If you have problems loading AIO.NLM,
    STOMPER.NLM and STMGR.NLM, and you get a
    message like

    "Public symbol IsColorMonitor not found",

    then you have an old version of CLIB.NLM
    (Netware 3.11). Just install an updated
    version, that is part of the archive
    LIBUP4.EXE (Compuserve NOVLIB or our support
    BBS)

-   When loading AIOCOMX, do not use the
    option "node=..." if possible

-   You should use AIOCOMX >= 2.11. It should
    be loaded with the maxrate-option:

    load aiocomx [...] maxrate=115200

-   The use of a FIFO (16550)-serial UART is
    strongly recommended.



10  Applying access rights
~~~~~~~~~~~~~~~~~~~~~~~~~~

STMGR.NLM provides a mechanism to refuse access to all or specific
modemservers by username, stationaddress and/or network.

This mechanism is activated, as soon as STMGR.NLM finds a file named
QMREST.LST in the same directory, STMGR.NLM is contained in. If this file
is not present, no restrictions apply.

This file could look like this:


             [stations]
             928485
             80A23E42     12Q

             [nets]
             1000002
             1000003       1

             [names]
             supervisor
             Peter         24


Rules:

-   there are 3 possible sections: [stations], [nets] and [names]
-   you can omit particular sections. There will be no restrictions for
    these sections.
-   if a section is present, it defines  objects (stationaddresses,
    usernames or networkaddresses), that have access to modemservers. All
    objects of this sectiontype, that are not defined, will not have access
    to any modemserver.
-   if only the object is entered in a line, it receives access rights to
    all modemservers throughout the network. If you additionally enter a
    list of modemserver-ids - separated by spaces or tabs from the objects
    designation - the object will only have access to the specified
    modemservers.
-   access rights are combined by logical and, which means, the user must
    qualify by station, network and username (in case restrictions apply
    respectively)

Typically the file QMREST.LST will only contain
a [names] or [nets] section.



Appendix A    Suitable Programs
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~


All windows programs, using the functions (API) (provided by windows
COMM.DRV) for the interface addressing, are supported.

DOS:

Not every terminal program supports a fossil driver. An example for a
program with FOSSIL support is Telemate (In Options / Terminal, FOSSIL can
be selected)

For the use of Telemate note the following: in order to work with the dial
list, for each listing the fossil driver has to be selected individually.
To select the fossil support in Telemate, first the baud rate has to be
set to a maximum of 38400bps. Otherwise fossil will be ignored!

A short list of programs which have been tested with Stomper:

Name            Operating       Comments
                system
------------------------------------------------------------------
Telemate        DOS             extensive and comfortable

FX-Term         DOS             Very easy to handle GUI, works with
                                RoboBoard.

Terminate       DOS             extensive (similar to Telemate). IEMSI
                                support

Dos/CIS         DOS             Compuserve information manager

Terminal        Windows         Terminal program included in windows packet

GoCIS           Windows         Offline Compuserve navigator

NavCIS          Windows         Offline Compuserve navigator

WinCIS          Windows         Compuserve information manager

PowerCom        Windows         terminal program

Telix for       Windows         extensive and comfortable terminal program
Windows

Transend        DOS/Windows     terminal / fax

RemoteAccess    DOS             BBS software

Frontdoor       DOS             Fido mailer

Binkley         DOS             Fido mailer

Crosspoint      DOS             Fido / Z net / UUCP - point system

Winfax          Windows         fax software

Bitfax          Windows         fax software

Unicom          Windows         comfortable terminal program



Most of these programs are available are available as shareware on our
Support BBS (see end of Document).




Appendix B    NETINFO.EXE
~~~~~~~~~~~~~~~~~~~~~~~~~

This a small diagnostic tool added to the packet, giving some information of
the network environment (received from netbios), for example


Permanent name:                         0000C0039A79   ; network address
Jumper:                                 40
POST result:                            00 
Version:                                0.1
Minutes up:                             0
Number of CRC errors:                   0
Number of alignment errors:             0
Number of collisions:                   0
Number of aborts:                       1
Number of transmitted packets:          6
Number of received packets:             10
Number of retransmits:                  4
Number of out-of-buffer-counts:         0
Free NCBs:                              10
Max. NCBs:                              12
Active sessions:                        32
Max. packet size:                       1024
Names:                                  1
NFOSMPX1                                0


Attention! This tool can only be useful when Netbios is actually installed.
Otherwise no useful information will be displayed here! This information
is of no use for IPX.


Appendix C    Tips
~~~~~~~~~~~~~~~~~~


1.  Telemate
~~~~~~~~~~~~

Before you select FOSSIL, be careful to set the speed to not more than
38400 bps. Otherwise Telemate will reject the FOSSIL-Setting (without
displaying a message).
In case even this fails, the safest way is to edit TM.CFG manually. Just
change

Connection=Modem

to

Connection=Fossil

and make sure that the entry Port= is correct.

Also, FOSSIL has to be selected for every entry in the Dial-List.


2.  Terminate
~~~~~~~~~~~~~
Early versions of Terminate (<3.x) had a problem identifying a FOSSIL 
driver that does not support all serial ports at once, like does NETFOS. 
If you have Terminate 3.x or higher, you don't have to read on.
The first time Terminate is set up for FOSSIL, it expects that a FOSSIL
driver is installed on COM1. This, of course, is not always given (e.g.
NETFOS installed on COM2).
It may result in a system-crash.

Workaround:

either use NETFOS on COM1 or

the first time, you switch Terminate to FOSSIL, do it with a regular FOSSIL
driver (like BNU or X00) installed. From then on you can use NETFOS.

If you don't have a FOSSIL driver handy, load

NETFOS /P1() /P2()

This installs NETFOS on both COM1 and COM2.


3.  Telix For Windows
~~~~~~~~~~~~~~~~~~~~~

Use the COM-Setting, not FOSSIL! In Windows it is always recommended to use
STCOMM whenever possible.
Apart from that, the FOSSIL support of early versions of TfW is buggy.


4.  pcAnywhere
~~~~~~~~~~~~~~

Use the plain INT14-Setting and do not set higher speeds than 9600 bps.
Otherwise pcAnywhere will not be able to initialize the port.
To achieve higher speeds, refer to the modemserver switch /L.

Appendix D    Troubleshooting
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

Problem              possible source             solution / remarks

The terminalprogram  The terminalprogram might   If provided by the terminal
doesn't react - no   address the hardware        software, switch to Fossil
characters are       directly                    or INT 14.
transmitted                                      In case the software doesn't
                                                 support a software inter-
                                                 face,
                                                 there is no way of
                                                 redirecting port usage.

                     The terminalprogram is set  Call NETFOS /I when using
                     to INT-14, but Netfos       BIOS-INT14-routines.
                     wasn't loaded with the /I-
                     option.

                     the wrong port is being     set the com-port settings of
                     addressed.                  the terminal software to the
                                                 value specified in the
                                                 commandline of Netfos.

Characters are lost  A non-buffered serial       Use a buffered serial device
during transmission  hardware is used            (UART 16550). Such can
                                                 be obtained for a small fee
                                                 in most computer stores.
                                                 Stomper relies on buffered
                                                 communications devices
                                                 more than other COM-
                                                 software, since it has to
                                                 deal with many interrupt
                                                 types at once (timer,
                                                 network and serial).

                     no handshaking active       Usually you have to specify
                                                 the type of handshaking you
                                                 want to use in the setup of
                                                 your communications
                                                 software. In most cases it's
                                                 best to set hardware
                                                 handshaking (RTS/CTS) to
                                                 on and software
                                                 handshaking (XON/XOFF) to
                                                 off.

Stomper hangs in     Stomper was loaded in       Stomper cannot be loaded in
cooperative mode     high memory                 high memory when driven in
                                                 cooperative mode.

It works with DOS    STCOMM.DRV wasn't           Make sure, the line
but not with Windows installed or wasn't         comm.drv=stcomm.drv is
                     installed correctly         placed in the [boot]-section
                                                 of you SYSTEM.INI-file and
                                                 that there is only one
                                                 occurence of a line
                                                 beginning with "comm.drv="

Fax-sending causes   You are using a DOS-Fax-    In this case, Stomper sets
problems             software that uses the      the handshake-method to
                     Bios-INT 14 interface.      "Hardware". Fax
                                                 transmission with class 2
                                                 expects software flow
                                                 control. make sure that your
                                                 modem is set to hardware
                                                 flowcontrol explicitly


                     XON/XOFF handshaking        start Stomper with the
                     doesn't function properly   commandline option /R





Appendix E    What is a FOSSIL driver?
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

There are various possibilities for a DOS program to address serial
interfaces of a PC:

There is the hardware related method, communicating directly with the
interface components. This method is used very often because it's quick and
uncomplicated for the program user - no unnecessary thoughts about a
fossil driver and its implementation.

"Polite" programs use the 4 functions provided by the computer BIOS (INT 14):
Baud rate setting, character transmission, character receive and fetching
the interface status. This method has the advantage of being hardware
independent (only BIOS has to have the information how to communicate with
the hardware - the programmer isn't troubled with that). Big and decisive
disadvantage: under DOS, BIOS allows max. 9600 bps, which is out of date
today. Furthermore BIOS routines are generally quite slow.

Another possibility is the fossil driver, combining the advantages of the
solutions mentioned above - speed and hardware independence - troubling the
user with only one installation.

The fossil driver offers buffered interface communication as an additional
function to the BIOS, emulating the interface functions of BIOS. Data
arriving at the interface needn't be handled immediately by the software,
but are stored in a ring buffer. A program using BIOS for example, has to
handle every single character before the next arrives in order to avoid a
loss of data. With a fossil driver the data can be fetched and handled in
blocks.


Appendix F    What is a network fossil driver?
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~


It's easy to exploit the advantage of a hardware independent program with
the use of a fossil driver. A suitable driver can pretend any digital
communication element against such a hardware independent program, for
example as COM2. The programm doesn't care how this works, as long as the
driver handles the mass of data.

Stomper uses this circumstance. A modem server is installed on a network
integrated computer linked to a modem. The modem server waits for a network
fossil driver connection, which again bluffs to be communicating with a
serial interface. At the same time a lot of instruction data and other data
are passed over the network, but don't worry, a normal network is hardly
concerned with that.


Appendix G - How to order
~~~~~~~~~~~~~~~~~~~~~~~~~

We have registration sites in many countries. Run the program

ORDER.EXE

to get information on pricing and registration sites. You will be prompted
to select your country.



Appendix H    Support
~~~~~~~~~~~~~~~~~~~~~

You can determine your local support site by running ORDER.EXE.
Pflug Datentechnik can be contacted via


Fax          49 / 7156 - 939005
e-mail       100340.1047@compuserve.com
Compuserve   Pflug 100340,1047
Fido         2:246/1009 (per Crashmail only, please!)

Mailbox  (see below)

Current Stomper versions and several shareware/PD software can be
downloaded from our mailbox:

+49 / 7156 - 939006


Internet FTP sites:

ftp.u-net.com                   /com/acl/stomper
cyberstation.net                /pub/silvrado/stomper
ftp.dyson.brisnet.org.au        /pub/clarion/stomper

WWW:
ftp://www.acl.co.uk/com/acl/stomper
http://dyson.brisnet.org.au/~cugq/stomper.html

Compuserve:

GO PCCOM oder GO PCPRO