Amateur Radio Packet Door
                                  v.  1.31

                 Land-Line BBS to Packet Radio Access System

                              Copyright 1994-95
                                      by

                          Pass - the - Buck SoftWare
                              Independence, Mo.

                                   (W4KGU)


    Files included in this package:

    ARPD.EXE
    ARPD.DOC
    CONFIG.TNC
    DEFAULTS.TNC
    HELP.TNC
    INIT.TNC
    INTRO.TNC
    TNCNODE.TNC
    USERS.TNC
    HISTORY.TXT
    ARPD_OS2.TXT


         Please  be  sure  all files are included when  you  install  this
    software.    Please  DO NOT distribute this program if ANY  files  are
    missing.

         Refer  to  HISTORY.TXT  for  changes  to  system  parameters  and
    operation.

         The  A.R.P.D.    program  was developed and tested  on  land-line
    Bulletin Board Systems using the following hardware / software:

              386/40 IBM clone
              8250 / 16550 UART serial cards
              PPI 14,400 / 28,800 modems
              RemoteAccess BBS software
              (running under MS Windows)
              MFJ-1270B / 1274C
              Kenwood TM-2530A

         While  no two systems are alike,  one similar to the above should
    offer few problems in setting up and running A.R.P.D.

         Of  course,   you MUST have a working knowledge of  packet  radio
    operation, your TNC and your BBS software.  Some setup is required and
    the more your system differs from the above,  the more will have to be
    done.

         From  the users standpoint,  operation is very simple.   Just hit
    the  key  to access the door,  wait for the TNC to be initialized  and
    then operate just as if they were using it from their computer.   This
    will  require  that you screen the users to be sure they are  familiar
    with  the  operation of your make/model TNC.   If the user panics  and
    drops  carrier  on  the door (many will!),  the system  will  NORMALLY
    recover properly.

         Under  some  circumstances the system may feel "All is not  well"
    and  will  make  itself unavailable to other users till reset  by  the
    SysOp.    The  logic  involved  in  this  is  very  simple  but  quite
    intelligent.    When  accessed,  the system writes a file in the  ARPD
    directory called TNCB.USY.   At exit from the door the system attempts
    to  reset the TNC to defaults,  checks the status of the serial  port,
    the phone line,  the temperature and humidity, etc.   If all goes well
    in  this process the system will delete this semaphore file.   At  any
    point  where the system suspects a problem it will exit with the  file
    still in place.

         When  the  door is accessed with the TNCB.USY file still  in  the
    directory it will display a screen to the user which explains that the
    TNC is not available and to try again at a future time.  The door will
    exit  back  to  the  BBS.    This makes it possible  to  run  ARPD  on
    multi-line Bulletin Board Systems.  Only one node at a time may access
    the  TNC without concern about the BBS software handling multiple user
    conflicts.

         ARPD  also makes a semaphore file to prevent a multiline BBS from
    attempting  simultaneous  access to the CONFIG.TNC file.   While  this
    file  could be left in place under certain extreme conditions,  it  is
    self clearing and will not cause the BBS to hang.   The worst that can
    happen is that a user attempting access would be shown a "Waiting Node
    Access" string for about ten seconds before the process completes.

         Under  normal  conditions,  when two nodes attempt access to  the
    TNC,  one will be successful, the other will be told to try again in a
    while.

         The  TNCB.USY semaphore file serves another purpose in the normal
    operation of your station.  It allows you to share it with your users.
    A  dedicated packet station is beyond the ability (or willingness)  of
    most  BBS SysOps to supply for their users.   By calling your favorite
    packet  operating software from a batch file such as the one below you
    can take control of the TNC at any time and the users will be informed
    that the TNC is not available for their use.

         The  batch  includes a safeguard so that you can't try to  access
    the  TNC  if  it is in use by a BBS caller.   (Handy when  running  in
    Windows!)

    REM *** Sample batch to call local packet program
    REM *** Allows use of equipment without BBS user
    REM *** conflict
    @echo off

    if exist d:\ra\arpd\tncb.usy goto nocando
    REM *** If TNCB.USY exists local packet program will not be called

    copy d:\ra\arpd\tncnode.tnc d:\ra\arpd\tncb.usy
    REM *** Makes a copy of the 1 byte file as TNCB.USY so users
    REM *** will not compete for the serial port

    kgucomm.exe
    REM *** Call local packet program

    del d:\ra\arpd\tncb.usy goto end
    REM *** This command runs after packet program exits and clears
    REM *** the file so users will have access again

    :nocando
    echo Sorry, the TNC is currently in use on the BBS.
    REM *** Displays TNC not available message to YOU!

    pause
    :end


         If  this  batch refuses to operate locally and you know that  the
    door  is  not in use at the moment,  it means that the system has  not
    reset  properly  and  the door is also not available  to  your  users.
    Delete the TNCB.USY file from the ARPD directory and log on to the TNC
    and  check the parameters.   Change any that require changing and then
    exit.

         If  you  are not running a multiline BBS and not running under  a
    multi-tasking environment where you could not possibly have a conflict
    with  two programs attempting to use the TNC at once,  you may  delete
    the TNCNODE.TNC file from the ARPD directory.  IF THE TNCNODE.TNC FILE
    IS NOT IN THE ARPD DIRECTORY - TNCB.USY WILL NOT BE CREATED.

         Some  SysOps have taken steps to ensure that the TNCB.USY file is
    always  deleted.    Such as adding a line in the calling .BAT file  to
    delete  it.    In earlier versions of ARPD this file could  cause  the
    system to refuse access to users under conditions which didn't warrant
    such  extreme  measures.   Version 1.20 and later will not  have  this
    problem and SysOps should allow ARPD to handle the maintenance of this
    file.    If  you have a problem in your system with this file  causing
    users  to  be locked out of the door you may then take whatever  steps
    necessary  to prevent this from happening.   Please consider the logic
    involved when dealing with multi-tasking environments or multiline BBS
    software.

         You  may  also use the door while logged on to the  BBS  locally,
    just as any user can.  You may prefer the look and feel of the door to
    your  present  program,   especially if you are using  a  simple  dumb
    terminal program.

         In normal operation,  if the user has ANSI activated on your BBS,
    the screen will be printed in 'DEFCOLOR'  on black until a connect has
    been made.  When a connect has been made the screen will be printed in
    'CONCOLOR'  on black.   The color of the screen indicating the connect
    status of the TNC.   If the user does not have ANSI active on your BBS
    then no color codes are sent.

         A  user  actually in the door will time out after the  length  of
    time  specified in the CONFIG.TNC file OR the system time left to  him
    on the BBS, whichever comes first.   In the door, there is no keyboard
    time-out.  The opening and closing screens have a keyboard time-out of
    three  minutes  with a warning beep at two minutes.   If  no  keyboard
    entry takes place within the allotted time, the door will exit back to
    the BBS.

         A user dropping carrier will cause the system to attempt to reset
    the  TNC and return to the BBS for normal exit.   It is at this  point
    that  problems may occur.   Encourage your users to NOT hang up on the
    system  if at all possible,  ESPECIALLY if the TNC is connected at the
    time.    Exiting the door in ANY way while the TNC is in the connected
    state  may lead to abnormal program termination.   Use of the CTRLCBRK
    command  in  the CONFIG.TNC if it is applicable to your TNC will  help
    insure the proper resetting of the TNC and normal program termination.

    Features:

         A.R.P.D.    is  designed to make life easier for a BBS SysOp  who
    wishes  to  make  on air packet available to system users.    Ease  of
    operation was a prime consideration as was low maintenance.

         Once   installed  A.R.P.D.    requires  little  attention.    All
    operations  are  handled  automatically by  an  intelligent  operating
    system requiring little specialized knowledge on the part of the SysOp
    or the user.

         When  a  user  accesses the door,  the call sign of  the  TNC  is
    changed to that of the user.   This allows him to log on to packet BBS
    stations  and  receive traffic as he would from his own home  station.
    The  call sign is changed back to that of the System Operator on  exit
    from  the  door.    This  has an added advantage of  making  the  user
    responsible for his own actions on the air.

         In the event that a station has connected to your TNC from the RF
    end,   a user will not be permitted to enter the door.   Changing  the
    callsign  of the TNC would leave the connected station in limbo.   The
    connect  status  at  door  entry is determined by the  status  of  the
    carrier detect line from the TNC.   Your TNC will,  therefore, need to
    be  set so that DCD reflects the connect status.   On some models this
    is a software setting and a jumper setting on others.  See your manual
    if users get rejected at log-on because of an "external" user.

         All  operations are logged in an ASCII text file called  ARPD.LOG
    as well as individual logs for each of the authorized users.

         As  the door is accessed the TNC clock is checked and updated  to
    keep  it correct according to system time.   This is also handy in the
    event of a power failure when TNC time might be lost completely.

         No SysOp intervention is necessary to tell the A.R.P.D.   program
    or the BBS software that the TNC is off line or powered down.   If the
    TNC is not powered on or is not connected to the serial port, the user
    is notified and the door exits to the BBS.  This off-line condition is
    determined by the condition of the DSR (Data Set Ready)  line from the
    TNC.    DSR MUST be true at log-on.   If you are using a TNC or RS-232
    cable that does not allow this status to be properly reported, you may
    strap  DSR  high  at  the connector and fool the  program.    I  don't
    recommend  this  but  we  are hams and prone  to  experiment.    Since
    A.R.P.D.    now  supports software flow control it should be  possible
    though I haven't tried it.

         Any  changes made to TNC settings by you in a local session or by
    the  user  in the door should be canceled on entry/exit to  the  door.
    This  assures  that the system will remain well behaved in both  modes
    whether attended or not.  It also assures that the system is always in
    the same condition the user is familiar with when he logs in.

         This  operation  is  handled  automatically by  the  software  if
    properly configed.   On entry to the door, the file INIT.TNC is fed to
    the  TNC  as if written line for line from the keyboard.    This  file
    should  contain  parameters that you would normally change in a  local
    packet  session.   It is particularly handy if you have a local packet
    program  that  loads the TNC with settings optimized for  a  different
    type of operation.

         On  exit  from the door,  a COMPLETE set of parameters should  be
    loaded  into the TNC.   This will assure that anything changed in  the
    system  by  a creative user will not be held over for you or the  next
    user.   The file DEFAULTS.TNC is sent to the TNC on exit from the door
    just as though typed from the keyboard line for line.

         If you use your TNC on HF or RTTY, several of the settings may be
    changed.    Each of the changed settings should be re-set by INIT.TNC.
    If  you're  not  sure  which settings may be  changed  in  your  local
    operation, you may copy the DEFAULTS.TNC file to the INIT.TNC file and
    do a complete reconditioning of the TNC on both entry and exit.

         A.R.P.D.    has  a  feature which was not documented  in  earlier
    versions, though it has been there all along.  Using the <F3> function
    key,   you may enable the local keyboard while a user is online.   The
    user is notified that the SysOp is online in HELP mode.

         With  this option you may take a new packet user by the hand  and
    lead  him  through  the  operation  of the TNC  and  even  join  in  a
    conversation   he  is  having  while  connected  to  another  station.
    Pressing  the <F3> key once again will cancel the HELP mode and inform
    the user that you are no longer with him.

         The <F4> key will put you in CHAT mode with the user.  He will be
    informed  of  your  presence and if he has ANSI enabled will  see  the
    print  change  to 'SYSCOLOR'  on black.   Keystrokes from him and  the
    local keyboard are displayed on both terminal screens but are not sent
    to the TNC.   TNC output is inhibited (buffered) during this CHAT.  If
    you  chat  long enough the circular buffer structure of  the  A.R.P.D.
    program will allow the contents of the buffer to be overwritten.  This
    is  usually  not a problem unless the user is connected and reading  a
    long ASCII text file.  Again, pressing the <F4> key a second time will
    cancel CHAT mode and return the system to normal operation.

         The <F3> and <F4> functions are mutually exclusive.  Entering the
    other  mode will cancel the first.   You need not exit CHAT mode to go
    directly to HELP mode.   Just press the key of the option you wish and
    the transition will take place seemlessly.


    Technical Stuff:

         While the A.R.P.D.   was written around the RemoteAccess (r)  BBS
    software  package,  the only thing actually necessary is that the  BBS
    software  write  an  RA style DORINFO1.DEF file.   This  is  a  fairly
    standard drop file and available with most BBS packages.   If your BBS
    uses  another  drop  file  there are utilities to  change  the  format
    available on most large support BBS's.

         A.R.P.D.  runs in a very small amount of memory and it is usually
    not necessary for the BBS software to swap itself out of memory except
    on extremely small systems.   This allows faster loading/unloading for
    the user online.

         In  RA a TYPE 7 exit is used to call a batch file.   This is done
    to allow the batch to change the current working directory to the ARPD
    directory.  The menu call in RA is : *C /c d:\ra\arpd.bat

         ARPD.BAT is simple:

    REM *** Batch file to run A.R.P.D.
    cd d:\ra\arpd
    arpd.exe
    cd d:\ra

         You  will,   of  course,  have to change the paths to  suit  your
    system.

         In  order  for  your  system to process the batch  file  and  for
    A.R.P.D.  to perform DOS functions the call from the BBS software will
    have it initiate a new instance of COMMAND.COM.  See your BBS software
    documentation to be sure of the procedure for your system.

         All of the files supplied with this package are necessary for the
    proper operation of A.R.P.D.  They are :

    CONFIG.TNC

         ASCII text file describing your system.

         SETTING                            |         COMMENT
         ----------------------------------------------------------------
         BBS d:\ra                          | Path to DORINFO1.DEF
         BBSNAME The HamShack BBS           | Name of the BBS
         DLPATH d:\archive\logfiles         | Path to download directory
         BAUD 9600                          | TNC to CPU baud rate
         TNCPORT 3                          | Comm port for TNC
         TNCINT 7                           | Interrupt used by TNC
         PROTOCOL 8N1                       | TNC/CPU mode
         RTSHIGH                            | Required for recent MFJ's
         KAM                                | Required for some KanTronics
         XFLOW                              | XON/XOFF flow control
         NEWLINE 13                         | Specify c/r character
         CTRLCBRK                           | Use 'BREAK' to return CMD:
         DEFCOLOR WHITE                     | Color of normal print
         CONCOLOR LTGREEN                   | Color of connected print
         SYSCOLOR YELLOW                    | Chat mode print color
         TIMELIMIT 60                       | Max time in door
         MYCALL W4KGU                       | TNC call setting command
         MYALIAS HSBBS                      | TNC alias setting command
         MYMCALL W4KGU-1                    | TNC mailbox setting command
         CONNSTRING *** CONNECTED           | TNC connect string
         DISCONNSTRING *** DISCONNECTED     | TNC disconnect string

         Only  the left hand portion of the file is included in the actual
    file.  Comments are not allowed in the file.

         These  commands may appear in any order and case is not critical.
    The  DLPATH  statement  is  the path to a directory  where  users  may
    download files.   A log of each stations activities are placed in this
    directory  with  the format CALL.LOG.   Mine would be W4KGU.LOG.    It
    would probably be best to allow only participating operators access to
    this directory to keep their files private.  If you don't wish to make
    user  logs  available  online you may make this line the path  to  the
    ARPD directory.  All logs will be written in that area for your review
    or file attaching to the user on a quarterly basis.

         The  BAUD,  TNCPORT,  TNCINT and PROTOCOL settings are for use in
    initializing  the  serial port in the computer and have no meaning  as
    far as the RADIO end of the TNC circuit.  PLEASE be sure that the comm
    port  and  interrupt  agree!    Any port from 1 thru 4  is  valid  and
    interrupts  3  thru  7 are valid.   This allows you some  latitude  in
    setting A.R.P.D.  up on a system with non-standard interrupts.

         The RTSHIGH is required by late model MFJ TNC's.  If the RTS line
    is pulled low during operation of these units,  no output will be sent
    to the terminal.  If you are using an MFJ and can send to it but don't
    see  anything back,  try adding this line to the CONFIG.TNC file.   If
    you don't need it - don't use it.

         KAM tells the system that the TNC is a KANTRONICS.   This will be
    required  on some systems using this equipment.   The best way to tell
    is cycle the power on the TNC and enter the door.  If the DATE/TIME is
    not properly set, add this line to the CONFIG.TNC.

         XFLOW  tells  the  system  that you wish  to  use  XON/XOFF  flow
    control.    There  are no parameters,  if it is there,  software  flow
    control  is  enabled.   Hardware flow control is assumed if it is  not
    there.    Not  having XFLOW available was an initial problem for  some
    system operators.  Having it seems to be a greater problem for others.
    PLEASE  BE  SURE  THAT BOTH THE TNC (ALL RELEVANT COMMANDS)   AND  THE
    SERIAL  PORT AGREE ON THE PROTOCOL TO USE TO COMMUNICATE.   THEY  MUST
    _BOTH_ BE SET FOR ONE OR THE OTHER!!

         NEWLINE  xx  allows you to change the character sent to  the  TNC
    when  the  <ENTER>  key is pressed.   This value MUST be  in  decimal.
    Either  11  or  13  are valid.   If the line is  not  present  in  the
    CONFIG.TNC 13 ($0D) is used.

         CTRLCBRK  will  cause ARPD to send a modem-break  signal  (serial
    spacing  condition for about 3/4 second)  to return control of the TNC
    in place of the $03 character normally sent by CONTROL-C.  On many TNC
    models  this is a SURE way of regaining control whether in converse or
    transparent  mode without regard to timing.   CTRLCBRK is active if it
    is included in the CONFIG.TNC file.   If not present, the ^C character
    is  sent.   With CTRLCBRK active it is not necessary to use the ^C key
    more than one time to return to command mode from any other mode.

         DEFCOLOR  - CONCOLOR - SYSCOLOR are the print color configuration
    commands.  Any of these parameters not included in the CONFIG.TNC file
    will  cause  that particular function to use the default value.    The
    command should be followed by a color string from the following list:

         BLACK
         RED
         GREEN
         BROWN
         BLUE
         VIOLET
         CYAN
         WHITE
         GRAY
         LTRED
         LTGREEN
         YELLOW
         LTBLUE
         LTVIOLET
         LTCYAN
         LTWHITE

         You may have to experiment with these color strings as I am color
    blind  and don't know if the names are exactly correct or not.   I can
    only guarantee that each is a different color.

         DEFCOLOR is normal terminal mode print color.
         CONCOLOR is connected mode print color.
         SYSCOLOR is SysOp Chat Mode print color.

         The  TIMELIMIT  parameter  is the maximum time the user  will  be
    allowed in the door.  If this time is greater than the time allowed on
    the  system  as reported in the DORINFO1.DEF file it will be  ignored.
    If  it is less than system time left,  the user will have to exit  the
    door  after  this  length of time.   A.R.P.D.   will  allow  users  to
    re-enter the door after exiting.   If you wish to prevent multiple use
    in a 24 hour period, you will have to do it with the BBS software.

         MYCALL, MYALIAS and MYMCALL are commands which must be recognized
    by the TNC.  The strings following the commands are sent character for
    character to the TNC as if typed from the keyboard.

         CONNSTRING  and DISCONNSTRING are the strings reported by the TNC
    at  connect  and  disconnect.    The strings  MUST  be  character  for
    character  as they would appear on the screen.   A.R.P.D.   uses these
    strings  in conjunction with carrier detect to determine the status of
    the TNC.

         This  file is space delimited.   That means that the command name
    and  the parameter must be separated by a space.   No other characters
    are  allowed  to appear in the file.   Everything after the  space  is
    assumed to be part of the parameter and passed to the TNC.



    INTRO.TNC

         File  that is displayed to the user after the initial LOGO screen
    that  is hard coded into the program.   This allows you to personalize
    the program to your system.

    HELP.TNC

         ASCII  text  file that is displayed to users when the TAB key  is
    pressed.  The file will be scrolled 23 lines at a time with a familiar
    "More?  (Y/n)" prompt on the 24th line.

    TNCNODE.TNC

         A  one  byte file which is used to create the TNCB.USY  semaphore
    file.    Nothing  magic about this file.   Just a space inside a  text
    wrapper.    If it gets lost you can recreate it easily.   If the  file
    does  not  exist the TNCB.USY file will not be created.   Delete  this
    file at your own risk.

    INIT.TNC

         A  subset  of TNC parameters in an ASCII text file used to  clear
    any changes you may normally make in a "local"  packet session.   This
    file  loads  as  the door is accessed to relieve you of  the  task  of
    resetting  the  changes  at the end of a local session.   Be  sure  to
    include any parameters you might change even occasionally.

         This file is passed character for character to the TNC,   just as
    if  you  had typed the commands from the command line.    Any  command
    valid for your TNC may be included here.

    DEFAULTS.TNC

         Same as the INIT.TNC file but more complete.  This file loads the
    TNC  with  a complete set of parameters to undo any  possible  changes
    made  online  by a user.   If the user gets upset and sets the TNC  to
    beacon  every  ten seconds with rude comments about your  family  tree
    this file will clear it.  Be sure it is a COMPLETE set of parameters.

         This  file is passed character for character to the TNC,  just as
    if  you  had typed the commands from the command line.    Any  command
    valid for your TNC may be included here.


    USERS.TNC

         This  is  a list of users who have access to the door.   If  this
    information is missing in this file,  users will not be able to access
    the TNC even if their security level and flag settings allow access to
    the  door.    Users who gain access to the door but are not listed  in
    this file will be shown a screen explaining that they must contact the
    SysOp for complete access to the door.

         This file is white space delimited.   That means that you may use
    a space or TAB character(s) between the strings on each line.   It has
    the following format:

    LOGON NAME          CALLSIGN            LICENSE CLASS       ACCESS
    ------------------------------------------------------------------
    (example)

    Dave Perry          W4KGU-2             EXTRA               FULL
    Craig WA0WPJ        WA0WPJ-4            EXTRA               FULL

         Use  of the TAB character will keep the file looking neat but one
    space is all that is really necessary:

    Dave Perry W4KGU-2 EXTRA FULL
    Craig WA0WPJ WA0APJ-4 EXTRA FULL

    would also work.

         Please  note the use of the SSID in the callsign field.   This is
    will  prevent the users home station from responding at the same  time
    should  it  be on the same frequency.   Have your users pick  an  SSID
    number  that  will  not conflict with any presently in  use  on  other
    transmitters.

         At  this  time only the first two fields are in use  by  A.R.P.D.
    but  the  others  are  included for planned future  expansion  of  the
    program.   With radios becoming more and more computer aware it may be
    possible  in  the  future that users online can pick  frequencies  and
    bands.   It will then be necessary to insure that only those valid for
    a given user are allowed.

         If you turn the power off to the TNC,  A.R.P.D.   will sense this
    and inform the user that the TNC is not available for use and ask them
    to  please  try  at a later time.   You do not have to  change  access
    levels or flags when taking the TNC off line.

         The  TNC clock is updated at each access to the door.   This will
    keep the TNC time in agreement with the system clock.

         A.R.P.D.    uses a direct control method of serial port operation
    both  on the BBS and the TNC ports.   If a FOSSIL driver is present in
    the system it is ignored for the time the door is in operation.   This
    communications driver has been in use and improved over 5 years as the
    basis  for  all  door programs written by PTB SoftWare and in  use  by
    other  software authors for remote system access.   It works very well
    in DOS, Windows and in a DOS box under OS/2.

         In  the  ALPHA test machine here the port is set at 9600 for  TNC
    operations and at 57,600 for the 28.8kb modem.   Internal buffering in
    the program and the TNC are sufficient for handling 28.8 user connects
    to  300 baud connects at the radio port with no loss of data in either
    direction under normal keyboarding conditions.

    Installation:

         Installation  is  simple.   Just make a directory under your  BBS
    software directory and place all the files included in this directory.

         Using  an ASCII text editor,  edit each of the files as necessary
    for your installation.

         Make  a menu selection on your BBS that will allow the system  to
    shell out to the A.R.P.D.  program.

         Write a batch file to change the current working directory to the
    ARPD directory and call the program.

         Remember  that the comm port and interrupt settings are  hardware
    settings.    Changing  the  comm  port and interrupt  numbers  in  the
    CONFIG.TNC file won't make it so.  These are just pointers to hardware
    that must exist on your system when installed.

         The  Land-Line  comm port MUST have RTS/CTS  DSR/DTR  handshaking
    enabled.    You DO NOT have the option of XON/XOFF protocol for the LL
    port.    Some  of  your users may have improperly  configured  modems.
    About   15%  of  the  users  on  my  system  have  pass-thru  XON/XOFF
    configured.    Most  users aren't aware that they can change that  and
    many  of those will not be up to the task once made aware.   Pass-thru
    XON/XOFF  should not be a problem in the door.   It may however  cause
    some problems on entry and exit.  Users having problems at these times
    need to be informed that modems usually come with manuals.

         For  ARPD.EXE to work the first time,  it MUST be able to talk to
    the  TNC.   If the parameters you have set in CONFIG.TNC do not  match
    the modem parameters (protocol - handshaking - etc.), the program will
    not  initialize  the TNC.   Use a favorite packet or comm  program  to
    "condition"   the TNC.   Usually it is best to put in BBRAM in the TNC
    the values that will be used in the DEFAULTS.TNC file.

         If your TNC does not recognize the command strings:

         MYCALL
         MYALIAS
         DA xxxxxxxx

    then it will NOT work with this version of ARPD.EXE.

         I  write better programs than documents.   All of the information
    you  need to install and use the program is here,  it just may not  be
    formatted  to your taste.   Read the entire document carefully and you
    should be able to install and use it in short order.


    LEGAL Stuff:

         This program is copyrighted software with a limited license to be
    used  for  its intended purpose without charge.   It may not be  sold,
    altered or included in any software or hardware package for any reason
    without the express written consent of the author.   (This will insure
    you have the latest version!)

         The  author can accept no liability for the use or the misuse  of
    this  program  or any damage resulting from such use.   If you  cannot
    accept  the  terms of this condition and use this program at your  own
    risk then DO NOT USE THIS SOFTWARE.

         You  MUST  be  a  licensed Amateur Radio  Operator  to  use  this
    software.   Use of this program to control on air transmissions may be
    a violation of Federal Law.  You should check with the FCC for planned
    operation  on certain bands/frequencies.   The author cannot guarantee
    that  under  certain  circumstances  and conditions the  use  of  this
    program  on bands/frequencies where unattended operation is prohibited
    will not result in a citation for violation.  The author can accept NO
    responsibility for such operation.  Please check with your closest FCC
    office if you have any question.

         FCC rules and regulations Part 97.5(e) require the posting of the
    station license at the transmitter sight.  It would be prudent to have
    each  user  supply  a  photocopy/fax of  their  license  for  posting.
    Remember,   when the user logs onto the system the callsign is changed
    to his and becomes his transmitter for the duration of use.   The user
    is  in effect using his own station under wire-line remote control  as
    permitted by FCC regulations.

         There is no charge for this program.  I would appreciate a QSL or
    netmail  to know that you are using it.   I would also appreciate  any
    feedback you may have on its operation and,  of course, the inevitable
    bug reports.   I cannot guarantee to update the software and accept no
    obligation for future releases.  This is FREE, you know!

         If you are using this program in a system substantially different
    from the one outlined above, I would appreciate a note letting me know
    of any special steps or settings you have made to make it function for
    you.    I will pass these along to others who may have similar systems
    or problems with particular pieces of hardware/software.

    Kantronics(r) users please note:

         This  software is NOT compatible with Kantronics(r)  products and
    the  manufacturer has refused to cooperate in supplying specifications
    to  enable  me  to make it so.   I will not be able  to  support  this
    program for users who have the Kantronics(r)  KPC(r)  line of Terminal
    Node Controllers.   Don't even bother to ask.  I was treated so rudely
    by  this company on the telephone that I have absolutely NO desire  to
    support the use of their products.

         All  Hardware and Software products mentioned in this document by
    name are the sole exclusive property of their manufacturers.


         You may reach me at any of the following addresses:

    sysop@f19.n280.z1.fidonet.org                     InterNet

    Dave Perry                                        FidoNet
    1:280/19

    Dave Perry                                        SnailMail
    W4KGU
    Current Callbook Address



                                     -73-