ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³ ±±±ÜÜ±±±Ü ±±±±±±Ü ±±Ü ±±Ü     A QWK-compatible mail door for RBBS-PC  ³
  ³ ±±Û±±Û±±Û ±±Ûß±±Û ±±Û ±±Û     Copyright (C) 1991-93  Makai Software   ³ Û
  ³ ±±Û ßß±±Û ±±±±±±Û ±±Û ±±Û               All rights reserved           ³ Û
  ³ ±±Û   ±±Û ±±Ûß±±Û ±±Û ±±Û                                             ³ Û
  ³ ±±Û   ±±Û ±±Û ±±Û ±±Û ±±±±±±Ü       Version 1.36 - June 20, 1993      ³ Û
  ³  ßß    ßß  ßß  ßß  ßß  ßßßßßß                                         ³ Û
  ³           ±±±ÜÜ±±±Ü ±±±±±±Ü ±±±ÜÜ ±±Ü ±±±±±±Ü ±±±±±±Ü ±±±±±±Ü ±±±±±±Ü ³ Û
  ³           ±±Û±±Û±±Û ±±Ûß±±Û ±±Û±±Û±±Û ±±Ûß±±Û ±±Ûßßßß ±±Ûßßßß ±±Ûß±±Û ³ Û
  ³           ±±Û ßß±±Û ±±±±±±Û ±±Û ß±±±Û ±±±±±±Û ±±Û±±±Ü ±±±±±Ü  ±±±±±Ûß ³ Û
  ³           ±±Û   ±±Û ±±Ûß±±Û ±±Û   ±±Û ±±Ûß±±Û ±±Û ±±Û ±±Ûßßß  ±±Ûß±±Ü ³ Û
  ³           ±±Û   ±±Û ±±Û ±±Û ±±Û   ±±Û ±±Û ±±Û ±±±±±±Û ±±±±±±Ü ±±Û ±±Û ³ Û
  ³            ßß    ßß  ßß  ßß  ßß    ßß  ßß  ßß  ßßßßßß  ßßßßßß  ßß  ßß ³ Û
  ³                                                                       ³ Û
  ³ Makai Software        Support boards: 301-843-5732  1:109/806         ³ Û
  ³ 870 Golden Drive                      318-345-1955  1:380/14          ³ Û
  ³ Newark, OH 43055                      916-546-7002  8:919/20          ³ Û
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ Û
    ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

                            TABLE OF CONTENTS

       Introduction . . . . . . . . . . . . . . . . . . . . . . .  1
       Warranty, distribution, & registration (or lack thereof) .  2
       Features & limitations . . . . . . . . . . . . . . . . . .  3
       Checklist of requirements  . . . . . . . . . . . . . . . .  5
       * Before you begin, READ THIS! * . . . . . . . . . . . . .  6
       Upgrading from a previous version  . . . . . . . . . . . .  7
       Installing Mail Manager from scratch . . . . . . . . . . .  9
          Locked BPS rates and the [CBAUD] variable . . . . . . . 13
       Debugging your setup, and running in local mode  . . . . . 14
       Sysop-configurable text files  . . . . . . . . . . . . . . 17
       DESQview, networks, and multiple nodes . . . . . . . . . . 21
       Working with a FOSSIL driver . . . . . . . . . . . . . . . 23
       Utility programs included with Mail Manager  . . . . . . . 24
       Security features of Mail Manager  . . . . . . . . . . . . 25
       Additional features  . . . . . . . . . . . . . . . . . . . 27
       Mail Manager's main menu . . . . . . . . . . . . . . . . . 30
            C)onfigure  . . . . . . . . . . . . . . . . . . . . . 30
            D)ownload . . . . . . . . . . . . . . . . . . . . . . 34
            E)xpedite!  . . . . . . . . . . . . . . . . . . . . . 34
            Q)uit . . . . . . . . . . . . . . . . . . . . . . . . 34
            H)elp . . . . . . . . . . . . . . . . . . . . . . . . 34
            I)nformation  . . . . . . . . . . . . . . . . . . . . 34
            M)essage number (lowest) to extract in each conf. . . 35
            U)pload your replies  . . . . . . . . . . . . . . . . 35
            W)ho's online to RBBS-PC? . . . . . . . . . . . . . . 35
            X)pert toggle . . . . . . . . . . . . . . . . . . . . 36
       Appendix A: Common problems  . . . . . . . . . . . . . . . 37
       Appendix B: Contacting the authors . . . . . . . . . . . . 38
       Appendix C: How to get the latest version  . . . . . . . . 39
       Appendix D: Suggestions since the initial release  . . . . 40
       Appendix E: Acknowledgements . . . . . . . . . . . . . . . 41
       Appendix F: For TRULY curious types only . . . . . . . . . 43
       Appendix G: Mail Manager's file formats (for programmers)  44



                               INTRODUCTION                             Page 1
                               ------------

        The 'QWK' format, developed by Mark Herring, has been around for 
        some time now (on bulletin board systems other than RBBS-PC), and is 
        intended as a standardized way to transfer mail, news, and bulletins
        to and from your bulletin board, and your users.

        Mail Manager was conceived as a way to handle RBBS-PC message bases
        offline via this 'QWK' format. QWK mail packets may read by popular
        mail readers such as EZReader, SLMR, JABBER, OFFLINE, OLX, and many
        others.

        This type of mail transfer is normally a four-step process:

            1) The users call your BBS, open the QWK-style mail door, and
               download their *.QWK mail packets.

            2) The users then log off the BBS, and use any number of QWK-
               compatible offline mail readers to read and reply to messages
               contained in the mail packets.  When they exit their mail
               readers, any messages entered in that session are packed up
               into what is termed as "reply packets".

            3) The users then call your BBS back up, open the QWK-style mail
               door, and upload their reply packets (*.REP).

            4) The QWK-style mail door then processes the reply packet, and
               inserts the new messages into the proper message base(s).

        Enter RBBS-PC and Mail Manager.

        The original purpose was to create a small, secure, functional door 
        for the 3-node RBBS-based system we were running at the time, but
        has since expanded quite a bit beyond what we had originally
        intended (to put it mildly).

        We acknowledge that there are at least two other established QWK
        mail doors for RBBS-PC (with a 3rd just now appearing):

               JIMMER by Jim Goodenough,
               TQM by Tom Collins, and now
               Mail Manager +Plus+! (see next page)

        JIMMER popped up during development of Mail Manager's initial
        release, and TQM followed a few months later.

        If Mail Manager isn't what you're after, maybe one of these others
        are.

        Just for the record, Mail Manager has been in nearly continuous
        development since late January of 1991.



                    WARRANTY, DISTRIBUTION, & REGISTRATION              Page 2
                    --------------------------------------

        Mail Manager v1.36 is NOT guaranteed in any way, shape, or form.
        Although we have worked very hard to keep Mail Manager compatible
        with a wide variety of possible RBBS configurations, we are forced
        to deal with two very important aspects of your RBBS-PC: your USERS
        files, and your MESSAGES files.  While it works just fine here,
        there may be differences in your setup that can cause problems with
        the Mail Manager/RBBS-PC combination.  THEREFORE:

                      RUN MAIL MANAGER AT YOUR OWN RISK!

        Mail Manager v1.36 may be distributed freely (in un-modified form),
        to the far corners of the earth.  The one thing that you *CAN'T* do
        is charge anything for it.

        If you are a shareware distributor/dealer, a normal disk copying and
        postage charge is permitted, provided that the amount required to do
        so does not exceed the REAL costs.  ($5.00 ought to be plenty, in
        our opinion).

        Mail Manager v1.36 continues to be distributed as SysopWare, meaning
        that a registration fee is neither required nor requested once you
        have determined that the program meets your needs.

                     ---*** BLATANT ADVERTISEMENT ***---

        Mail Manager v1.36 is our basic QWK mail door package.  For those
        wishing more features, there is now an enhanced version of Mail
        Manager, "Mail Manager +Plus+", which is released as uncrippled,
        fully functional shareware.

        To put it as simply as possible, the amount of time and money
        required to properly support the widespread use of our door has
        turned out to be far greater than we ever imagined.  We will
        continue to support the "free" Mail Manager as we have in the past,
        and will continue with any bug fixes and/or modifications for
        compatibility with future releases of RBBS-PC, but features and
        enhancements beyond what you find in the current release of Mail
        Manager will be available only in Mail Manager +Plus+.

        Mail Manager +Plus+ has a $25.00 registration fee.  We're not
        attempting to get rich here, just trying to cover some of the cost
        of support.  As a sysop, you already know what it costs for any LD
        connect time at all...

        Please see ENHANCED.DOC for more information about what is currently
        available in Mail Manager +Plus+.



                          FEATURES/LIMITATIONS                          Page 3
                          --------------------

        The length of this list has gotten ridiculous.  So, we'll only list
        the MAJOR stuff that you might be interested in:

        þ Can use a FOSSIL for communications.

        þ Supports both DESQview and NetBIOS file & record locking schemes,
          as well as file sharing under NetBIOS, and supports Novell
          networks.

        þ Mail packets can be downloaded in either text or QWK format.  Both 
          types of mail packets can, at the option of the sysop, contain all 
          sorts of additional stuff such as bulletins, news, new file 
          listings, etc.

        þ Supports the optional multiple message headers that were 
          introduced in RBBS-PC v17.4.

        þ Supports both types of RBBS-PC message bases, fixed-length and 
          'elastic'.  (Your message bases are 'elastic' if you have 
          configured them to GROW as messages are added).  Can handle a mix 
          of both 'fixed-length' and 'elastic' message bases.

        þ Multi-node support (up to 36 nodes) via DORINFOx.DEF and separate 
          subdirectories for each node (built by Mail Manager on-the-fly).

        þ Up to 250 conferences can be configured.

        þ Up to 1,000 messages can be extracted & downloaded in any one mail
          packet.  Subsequent downloads will extract any additional waiting 
          messages.  (1,000 messages means at least a 300K compressed mail 
          packet).

        þ BPS rates up to 38,400, and COM ports 1-4 are supported.

        þ Support for non-standard communication ports & IRQ's via FOSSIL,
          MAILMGR.PRO, and batch files.

        þ X, Y, and Zmodem for file transfers via Forsberg's DSZ, or you can
          use our implementation of PROTO.DEF (MAILMGR.PRO) and configure a
          number of different protocols.

        þ "(R)", when found at the beginning of the subject field of
          extracted messages, is stripped from the field.  This allows
          offline readers to group related messages together, rather than
          into one group with "(R)" and one without.

        þ *FAST* message extracting and handling of ".REP" uploads.

        þ High/low ASCII can be allowed or stripped in each conference.

        þ ANSI can be allowed or stripped in each conference.



                          FEATURES/LIMITATIONS                          Page 4
                          --------------------

        þ Mail reader tearlines in uploaded messages can be altered (for
          possible FIDO compatibility) from "---" to "   ", or left alone
          for each conference.

        þ Extensive security checks.

        þ Supports RBBS template variables, including [CBAUD].



                       CHECKLIST OF REQUIREMENTS                        Page 5
                       -------------------------

   [ ] DOS 3.10 or above.

   [ ] Un-damaged RBBS-PC message bases.  (Not all are!)

   [ ] Separate RBBS-PC users files for each conference/subboard.

   [ ] DORINFOx.DEF for remote operation.

   [ ] A recent version of DSZ.COM (one that supports the "handshake slow"
       command) *IN A DOS PATH!*, or the external protocols of your choice
       via MAILMGR.PRO (our implementation of RBBS-PC's PROTO.DEF).

   [ ] The environment variable of your choice set to indicate where Mail
       Manager is to look for "XFER-[node].DEF" (where [node] is the node
       number).  XFER-x.DEF is no longer required to be in the default 
       directory.

   [ ] The file compression/extraction programs of your choice in a DOS
       path, or wherever you specified them in Mail Manager's list of 
       archivers (MAILMGR.ARL).

   [ ] At least 300K free memory, maybe more.



                           BEFORE YOU BEGIN                             Page 6
                           ----------------

   *PLEASE READ THIS!!!!!! *********************************************

   RBBS-PC has the unique ability to create, read, and manipulate its own
   corrupted message bases, without ever telling you that anything's wrong.

   Mail Manager is not as forgiving, and requires that your message bases be
   in good condition.  It is therefore STRONGLY suggested that you run some
   type of a checkout/repair utility against your message bases BEFORE 
   installing Mail Manager.  We've included an alternate utility to 
   repair/purge your message bases named MailFix, which you can try out as 
   an alternative to CONFIG.EXE's repair and purge functions.

   MailFix is compatible with RBBSMail'ed, MsgToss'ed, and OverMail'ed 
   message bases (which have differently-formatted message headers), as well 
   as RBBS-standard message bases.  This is in contrast to RBBS-PC's CONFIG 
   option #185, which simply will not properly handle a message base that 
   has been manipulated by any of these mail processors.

   *PLEASE* take a few minutes to read MailFix's documentation before you
   attempt to utilize this program!

   In any event, you really SHOULD check out the integrity of your message
   bases before attempting to install Mail Manager.



                    UPGRADING FROM A PREVIOUS VERSION                   Page 7
                    ---------------------------------

   If you are installing Mail Manager for the first time, read the section
   entitled "Installing Mail Manager from scratch".

   If you are upgrading from Mail Manager v1.35, you should do the 
   following:

       [ ] Replace your existing MAILMGR.EXE and MAILCFG.EXE programs with  
           the ones included in this package.

   If you are upgrading from Mail Manager v1.30 thru v1.34, you should do
   the following:

       [ ] Replace your existing MAILMGR.EXE and MAILCFG.EXE programs with
           the ones included in this package.

       [ ] If you are using a fossil with your comm port locked at high
           speed, and if you are using RBBS 17.4 or an earlier RBBS version
           which has been modified to support the [CBAUD] variable, change
           your DOORS.DEF entry and the batch file you use to load MAILMGR
           to utilize [CBAUD].  See the "Locked BPS Rates"  section of this
           document for further details.

       [ ] (Optional) - Run MAILCFG.EXE once against your existing
           MAILMGR.CFG file, and save your setup (without making any
           changes).  All this does is update the version number in your
           configuration file.

   -----------------------------------------------------------------------

   If you are upgrading from v1.20 through 1.24, you should do the following
   IN THIS ORDER:

       [ ] Copy the supplied UPDATE.EXE to your Mail Manager directory, and
           run it once from DOS.  This updates your existing MAILMAN.CFG
           file to the new format.   After doing this, you can discard
           UPDATE.EXE.

       [ ] Make sure you're in your Mail Manager directory, and rename
           MAILMAN*.* to MAILMGR*.*.  You can do this easily by typing the
           following from the DOS command line:

               REN MAILMAN*.* MAILMGR*.*

       [ ] Replace files with the ones included in the imbedded MAILMGR.ZIP
           as needed:

              - MAILMGR.EXE  (must)
              - MAILCFG.EXE  (must)
              - *.HLP        (optional - wording changes)
              - *.MNU        (optional - wording changes)

       [ ] If you'd like to include ANSI color welcome and exit screens for
           your users who are configured as such in RBBS-PC, create a
           PRELOGC.RBS and/or EPILOGC.RBS, and place them in Mail Manager's
           directory.

       [ ] Run MAILCFG.EXE, and set these additional options:

           - Whether or not to modify the date/time stamp on uploaded
             replies.
           - Location (City, State) of your BBS.
           - Phone number of your BBS.



                    UPGRADING FROM A PREVIOUS VERSION                   Page 8
                    ---------------------------------

       [ ] If you are using a fossil with your comm port locked at high
           speed, and if you are using RBBS 17.4 or an earlier RBBS version
           which has been modified to support the [CBAUD] variable, change
           your DOORS.DEF entry and the batch file you use to load MAILMGR
           to utilize [CBAUD].  See the CBAUD section of this document for
           further details.

   -----------------------------------------------------------------------

   If you are upgrading from a version older than v1.20, you should do the
   following IN THIS ORDER:

      [ ] Back up your entire Mail Manager subdirectory, in case you need
          anything additional from it later.

      [ ] Delete everything from it, EXCEPT the following files:

           MAILMAN.USR  (Mail Manager's internal user file)
           MAILMAN.CFG  (Mail Manager's binary configuration file)
           MAILMAN.BUL  (or whatever you named it, if it exists)
           *.RBS        (the prelog and epilog screens)
           *.MNU        (the main menu)
           *.PRE        (Mail Manager's prelog screen)

          Almost everything else about Mail Manager has changed from
          previous versions of the program.

      [ ] Copy UPDATE.EXE to your Mail Manager subdirectory, and run it once
          from DOS to update the format of your configuration file.  When
          finished, you can discard UPDATE.EXE.

      [ ] Make sure you're in your Mail Manager directory, and rename
          MAILMAN*.* to MAILMGR*.*.  You can do this easily by typing the
          following from the DOS command line:

              REN MAILMAN*.* MAILMGR*.*
      
      [ ] De-compress the embedded MAILMGR.ZIP to your Mail Manager
          subdirectory.

      [ ] Read the section in MAILMGR.DOC entitled "SYSOP-CONFIGURABLE TEXT 
          FILES", and update your files as needed.  Most notably:

                MAILMGR.ARL
                MAILMGR.PRO
                MAILMGR.BUL

      [ ] Run MAILCFG.EXE, and insure that everything is set properly.
          MOST NOTABLY the additional options for:

          - type of network to use in local mode,
          - type of flow control (handshaking),
          - path/filename of the list of new bulletins,
          - path/filename of your FMS directory (if you were using NEWFILES),
          - path/filename of MAILMGR.PRO,



                   UPGRADING FROM A PREVIOUS VERSION                    Page 9
                   ---------------------------------

          - path/filename of the list of archivers,
          - environment variable to use (DSZLOG or equivalent), and
          - whether or not to modify date/time stamp on uploaded replies.
          - Location (City, State) of your BBS.
          - Phone number of your BBS.

       [ ] If you are using a fossil with your comm port locked at high
           speed, and if you are using RBBS 17.4 or an earlier RBBS version
           which has been modified to support the [CBAUD] variable, change
           your DOORS.DEF entry and the batch file you use to load MAILMGR
           to utilize [CBAUD].  See the CBAUD section of this document for
           further details.

   This should be sufficient to get you up and running with this release of
   Mail Manager, but if you run into trouble, you'll want to carefully study
   the following section of this document.

                     INSTALLING MAIL MANAGER FROM SCRATCH
                     ------------------------------------

   For the purposes of this document, we'll assume that you named your Mail
   Manager directory \MAILMGR off the root.

   If for some reason these instructions are not clear to you, or this is
   your first attempt at installing a door in your RBBS-PC, there's really
   not much that can take the place of RBBS-PC's documentation.

   With that said...

   Check your environment variables (type "SET" at the DOS prompt).  Both
   RBBS-PC and Mail Manager use the log file "XFER-x.DEF", where "x" is the
   node number.  Mail Manager needs an environment variable to determine
   where this file is located on your system.  Most of us seem to be using
   Forsberg's DSZ for file transfers, so there should be a line referencing
   "DSZLOG", which would look something like this for node 1:

      DSZLOG=C:\RBBS\XFER-1.DEF

         or...

      DSZLOG=XFER-1.DEF

   If Mail Manager cannot find "XFER-x.DEF", it will report that all file 
   transfers have failed.

   In any case, make a note of the environment variable name (in this case 
   DSZLOG), since you'll need it later.

   Once you're past this, you can get on to the actual installation.

   Create a subdirectory just for Mail Manager.  Stick it anywhere you want, 
   and name it anything you want, just be sure that it is a drive and
   directory specificially meant for Mail Manager.  From here on we'll just
   refer to it as the \MAILMGR directory.



                   INSTALLING MAIL MANAGER FROM SCRATCH                 Page 10
                   ------------------------------------

   De-compress the imbedded archive "MAILMGR.ZIP" to the directory you just
   created.

   Change to it (making it the current directory).

   Before you run Mail Manager's configuration program (MAILCFG.EXE), look
   for seven files in your Mail Manager directory:

        - PRELOG.RBS (and PRELOGC.RBS)
        - EPILOG.RBS (and EPILOGC.RBS)
        - MAILMGR.BUL
        - MAILMGR.ARL
        - MAILMGR.PRO

   These are all text files, and should be edited to pertain to your
   particular RBBS-PC!  To take them individually:

       - PRELOG.RBS is the welcome message that your users will see when
         they first fire up their mail reader against one of Mail Manager's
         QWK's.  Probably the most common thing that you'd want to put here
         would be a copy of your RBBS-PC prelog or welcome screen, but this
         is entirely up to you!  (PRELOGC.RBS is an ANSI color version).

         --------------------------------------------------------------

       - EPILOG.RBS is the signoff message that the users will see just as
         they exit your QWK packet from their mail reader.  You might want
         to put an adaption of RBBS-PC's EPILOG.DEF here.  (EPILOGC.RBS is
         an ANSI color version).

         --------------------------------------------------------------

       - MAILMGR.BUL is the list of bulletin path/filenames that you'll want 
         to include in your user's QWK's.  Edit this file to pertain to your 
         system bulletins, (and/or any other text files that you'll want to 
         include in your users' QWK packets), and if any of them are newer 
         than the user's last call to RBBS-PC, the user will get them 
         included in his/her QWK packet.  The users have the option of 
         turning "off" new bulletin listings, so if you have any that you 
         ALWAYS want included in the mail packets (if they have been 
         updated), precede them with a double-asterisk:

              c:\bulet1       (optional)
              **c:\bulet2     (mandatory for inclusion)

         You can choose the path\name of this file in the configuration
         program.  C:\MAILMGR\MAILMGR.BUL is simply the default name.

         --------------------------------------------------------------

       - MAILMGR.ARL is the list of archivers available to your users.  This
         is a "template" file, similar in structure to RBBS-PC's PROTO.DEF.
         This file is well-commented, and you should be able to follow  what
         it does fairly easily.  If you do not intend to make a variety of
         archivers available to your users, simply delete all compression



                   INSTALLING MAIL MANAGER FROM SCRATCH                 Page 11
                   ------------------------------------

         types except your default, and the users will be unable to select
         any other type of file compression.  Be sure to adjust the path to
         the archiver, if it is not included in your DOS path.

         You can choose the path\name of this file in the configuration
         program.  C:\MAILMGR\MAILMGR.ARL is simply the default name.

         --------------------------------------------------------------

       - MAILMGR.PRO is an adaption of RBBS-PC's PROTO.DEF file, to list the
         file transfer methods available to your users.  You should be able
         to use your own PROTO.DEF file here, provided that the very last
         protocol option begins with the letter "N", for "None".  Mail
         Manager is able to use quite a few of the PROTO.DEF options, such
         as whether or not a reliable connection is required, the factor to
         determine transfer times, and all of the "template" variables, such
         as [FILE], [PORT#], [BAUD], etc.

         You'll want to insure that the proper DOS path to the file
         protocols are listed in the "send" and "receive" arguments, as well
         as insuring that you have an external X) and Y)modem configured.
         (Mail Manager cannot use RBBS-PC's internal X and Ymodem).  Consult
         the RBBS-PC documentation for more particulars regarding PROTO.DEF.

         You can choose the path\name of this file in the configuration 
         program.  C:\MAILMGR\MAILMGR.PRO is simply the default name.

   (These five are also covered in the section regarding "SYSOP- 
   CONFIGURABLE TEXT FILES" elsewhere in this manual).

   Run MAILCFG.EXE, and inform Mail Manager about your system.  You'll find
   that it asks a lot of questions!  All should be fairly self-explanatory,
   but you'll want to read MAILCFG.DOC if you have any questions.

   When done, Mail Manager's configuration file (MAILMGR.CFG) will be
   created, and thereafter you can edit it anytime by re-running
   MAILCFG.EXE.

   Follow standard procedure for adding a new door to your system.  On a 
   'normal' RBBS-PC this would entail:

       - Editing MENU5* (or whatever you have named your door menu) and
         adding the word " MAILMGR ".

       - Creating a MAILMGR.BAT file, and sticking it where RBBS can find
         it.  Your batch file that calls Mail Manager is very important, and 
         must logically do the following:

            * Change to the Mail Manager directory,
            * Copy RBBS-PC's DORINFOx.DEF to that directory,
            * Run MAILMGR.EXE, passing the NODE NUMBER as the ONLY command
              line parameter (such as MAILMGR 1 for node 1), and
            * Change back to RBBS directory when finished.



                   INSTALLING MAIL MANAGER FROM SCRATCH                 Page 12
                   ------------------------------------

         With that in mind, your batch file should look something like this:

           cd\mailmgr
           copy \rbbs\dorinfo%1.def
           mailmgr %1
           cd\rbbs

   If you're running the "DOORS.DEF" method that RBBS-PC provides, here's an
   example line to implement Mail Manager:

        MAILMGR,5,,D,"MAILMGR.BAT [NODE]",N,,

   This line tells RBBS-PC the following:

        1) The name of the door is MAILMGR.
        2) Security level 5 and above can access the door.
        3) No questionnaire is to be invoked.
        4) Exit to this door.  (Mail Manager requires a lot of RAM)
        5) The name of the batch file to invoke is MAILMGR.BAT.
        6) RBBS-PC is to pass the node number to the batch file.

           * NOTE - Type the word "[NODE]" as shown above, and RBBS-PC will 
                    replace it with the true node number when it calls the 
                    batch file.  If you are running a single-node system,
                    and find this confusing, you can instead pass the node
                    number directly, but it isn't necessary to do it this
                    way.  This would make your DOORS.DEF line look something
                    like this:

                    MAILMGR,5,,D,"MAILMGR.BAT 1",N,,

        7) Don't ask for a password when returning back to RBBS-PC.
        8) Don't display a text file when the door closes.
        9) Use the time limit from RBBS-PC as the time allowed in the door.

   And that's all that's needed.



                  LOCKED BPS RATE AND THE [CBAUD] VARIABLE             Page 13
                  ----------------------------------------

   If you have your communications port locked higher than what the user's
   actual connect speed is going to be, you will find that Mail Manager
   will not report the correct BPS rate, nor will it estimate the amount of
   time required for file transfers properly.  This is due to RBBS-PC
   passing the locked BPS rate to the door in the DORINFOx.DEF file,
   instead of true connect speed.

   With the advent of the CBAUD merge, a new RBBS template variable [CBAUD] 
   became available.  This has now been incorporated into RBBS-PC 17.4.  If 
   you are running a system which supports the [CBAUD] variable, you can use 
   this to inform Mail Manager 1.36 of the actual connect rate.  The
   following will work *ONLY* with RBBS-PC v17.4 and up (or with copies of
   RBBS-PC compiled with the CBAUD merge):

   Change the DOORS.DEF example mentioned on page 12 to read:

        MAILMGR,5,,D,"MAILMGR.BAT [NODE] [CBAUD]",N,,

   Then, in your batch file that loads the door:

        mailmgr %1 /CBAUD%2

   If the door is called on node 2 of your system, and the user's connect
   rate is 2400 BPS, the above line will look like this to Mail Manager:

        mailmgr 2 /CBAUD2400

   With this done, your basic door installation is finished, and the time
   has come to plan your interface for the users, and to configure the door
   for your system.



             DEBUGGING YOUR SETUP, AND RUNNING IN LOCAL MODE            Page 14
             -----------------------------------------------

   Assuming (again) that your Mail Manager directory is named \MAILMGR:

   Change to the \MAILMGR directory, and run MAILMGR.EXE with no command
   line to bring the door up in local mode.

   NOTE - Depending on how many conferences you've entered, Mail Manager may
          take a while to come up.  Mail Manager attempts to find the user 
          in each and every conference as soon as it loads to determine 
          which conferences the user has and has not joined.  The more 
          conferences you have, and the slower your hard disk, the longer 
          this will take.  This is required by the security measures 
          mentioned in the 'features' section.

   If this is a first-time installation, Mail Manager should say that you're
   a new user and walk you through the user setup.

   We think it is necessary to mention Mail Manager's own running scenario,
   since it is important for you as the sysop to understand this for any
   debugging purposes on your end.

     You created   +-- Work directories created & maintained by Mail Manager.
            |      |
        \MAILMGR   |
                   |
        \MAILMGR\LOCAL
                \NODE1
                \NODE2
                ...etc.

   Mail Manager changes to these work directories as it runs, and changes
   back to the parent directory just as it exits.

   Two files that absolutely MUST be in the directory that you created:

      MAILMGR.EXE, and RBBSQWK.BAT.

   Don't rename RBBSQWK.BAT!!!

   You can edit RBBSQWK.BAT if you are familiar with the format of the
   CONTROL.DAT file that is included in all .QWK packets, and/or want to
   modify what the users will receive in their QWK's.  This is not for the 
   faint of heart, requires some knowledge of how things work in QWK land, 
   and simply isn't necessary.  RBBSQWK.BAT is run each time that Mail 
   Manager creates a QWK packet for the user to download, and doesn't do 
   anything at all if you are using MAILMGR.ARL.

   FOR A FIRST-TIME INSTALLATION, WE RECOMMEND YOU DON'T MODIFY RBBSQWK.BAT!

   An important consideration is what to do with your own personal QWK's and
   REP's created locally.  Configure your offline reader to use the
   \MAILMGR\LOCAL directory for all .REP's and .QWK's, since that's where
   Mail Manager will manipulate your mail in local mode.



             DEBUGGING YOUR SETUP, AND RUNNING IN LOCAL MODE            Page 15
             -----------------------------------------------

   To stick a .REP packet into your message bases, just U)pload while in
   local mode, and select any protocol other than N)one.  If your .REP
   packet is in the \MAILMGR\LOCAL directory, it will be processed as if 
   you'd uploaded the file remotely.

   It is important to make you aware that there is a sysop-only menu option 
   "I" (Info), which isn't listed in either the command prompt, or the menu
   itself.  This menu option is available only to those with sufficient
   security to read ALL messages, or greater.  If the user does not have at
   least this security level, they will see the familar "Command not
   recognized", instead.

   If you have set yourself up with sufficient security to use this option,
   pressing "I" at Mail Manager's main menu will greet you with something 
   like this:

      SYSOP INFORMATION:

      Mail Manager version ............: v1.36
      Mail Manager path ...............: C:\MAILMGR
      MailMGR's operating environment .: LANtastic v4.00 (NetBIOS)
      DOS version .....................: 5.00
      DOS SHARE detected? .............: Yes
      Flow control method .............: Local mode
      Free string space ...............: 23624
      Non-string array avail ..........: 373408
      Available stack space ...........: 1738
      MAIN message base ...............: E:\RBBS\MAINM.DEF
      MAIN users file .................: E:\RBBS\MAINU.DEF
      Highest message # in MAIN .......: 6132
      Last msg # YOU read in MAIN .....: 6131
      Filename of protocol definitions : C:\MAILMGR\MAILMGR.PRO
      Filename of list of archivers ...: C:\MAILMGR\MAILMGR.ARL
      Filename of FMS directory .......: E:\RBBS\MASTER.DIR
      RBBS-PC semaphore file ..........: E:\RBBS\IBMFLAGS
      MailMGR semaphore file ..........: MMFLAGS
      RBBS-PC semaphore file size (6) .: 6
      MailMGR semaphore size size (3) .: 3

   These 20 are all of the possible lines that can be shown to you.  The
   last four will be displayed only if your environment is NetBIOS.

   Some of the more important information in here:

     Mail Manager path should reflect the drive and directory that you have 
     installed the program in.  If it doesn't, your batch file is probably
     not changing to the proper directory prior to running MAILMGR.EXE.

     Mail Manager's operating environment should reflect what you've told 
     Mail Manager to use.  If it doesn't, there's definitely a problem!

     DOS version must be 3.10 or above in order for Mail Manager to operate 
     properly.



             DEBUGGING YOUR SETUP, AND RUNNING IN LOCAL MODE            Page 16
             -----------------------------------------------

     DOS SHARE must be detected if you are operating in a NetBIOS 
     environment.  The only exception is if you are running under a NOVELL
     network, in which case SHARE checking is bypassed.

     Flow control method can report one of five things:  Local mode, FOSSIL,
     RTS/CTS, XON/XOFF, or NONE.  This is a great way to find out for sure
     (when calling remotely) if Mail Manager properly detected your FOSSIL 
     driver.  If it didn't, it will show one of the other flow control 
     options.

     Free string space is pretty darned important, too.  This should really 
     be up around 6000 or higher at all times when you display this screen.  
     It could conceivably be less than that if you have an extremely large 
     number of conferences, and/or have a very long path name to all of your 
     conferences, and/or are running Mail Manager in very tight RAM.  If the 
     number you get here is less than 6000, we want to hear about it!

     Non-string array available should be approximately the amount of free 
     DOS memory that is available to Mail Manager, and this number is
     roughly what is available for DSZ and your file compression/extraction
     programs.  If this number is less than 200K, you are likely to run into
     trouble, and should check to make sure that you are EXITING, (NOT 
     SHELLING!) from RBBS-PC to Mail Manager.  This is the only way that we 
     can think of that would cause you to have less than 200K available on 
     today's 640K+ PC's.

     MAIN message base and user file names must match what is true for your
     MAIN area.  If not, you don't have MAIN as your 1st conference listed,
     and Mail Manager will NOT operate properly.

     Highest message number in MAIN, and highest message # that you read in
     main should be accurate.  If they're not, then Mail Manager didn't
     properly find you in the MAIN users file, and/or it wasn't able to 
     correctly access the MAIN message file.

     Filename of list of protocol definitions should match what you told 
     MAILCFG to use for MAILMGR.PRO.

     Filename of list of archivers should match what you told MAILCFG to 
     use.  (If this file does not exist, Mail Manager will use the default
     type of compression that you chose, and will require said archiver to
     be in a DOS path!)

     Filename of FMS directory should match what is true for your system if 
     you are using an RBBS-PC FMS directory, or "NONE" otherwise.

     The last four lines will only be shown to you if you are running under
     NetBIOS, and they are described in better detail elsewhere in this
     manual.

     If, after following these instructions, you continue to have trouble, 
     take a look at the "COMMON PROBLEMS" section of this manual.



                     SYSOP-CONFIGURABLE TEXT FILES                      Page 17
                     -----------------------------

    (All in Mail Manager's directory)

    MAILMGR.HLP    - The online help file that will be displayed to the 
                     users.  You can customize it if need be, but should be
                     pretty much OK as-is.

    MAILMGR.PRE    - The initial screen displayed when Mail Manager loads.  
                     Again, you might want to customize it for your own
                     individual system, but it is generic enough as-
                     distributed that you may not need to.

    MAILMGR.MNU    - Mail Manager's main menu, displayed to the users just 
                     before the command prompt.

    PRELOG.RBS     - The welcome message that your users will see when they
                     first fire up their mail reader against one of Mail 
                     Manager's QWK's.  Probably the most common thing that 
                     you'd want to put here would be a copy of your RBBS-PC 
                     prelog or welcome screen, but this is entirely up to 
                     you!

    EPILOG.RBS     - The signoff message that the users will see just as 
                     they exit your QWK packet from their mail reader.  You 
                     might want to put an adaption of RBBS-PC's EPILOG.DEF 
                     here.

    MAILMGRC.HLP   \
    MAILMGRC.PRE    \
    MAILMGRC.MNU     > Color/ANSI versions of the above.
    PRELOGC.RBS     /
    EPILOGC.RBS    /


    MAILMGR.BUL - The list of bulletin path/filenames that you'll want to
                  include in your user's QWK's.  Edit this file to pertain
                  to your system bulletins, (and/or any other text files
                  that you'll want to include in your users' QWK packets),
                  and if any of them are newer than the user's last call to
                  RBBS-PC, the user will get them included in his/her QWK
                  packet.

                  Bulletins preceded with a double-asterisk are considered
                  mandatory for inclusion in the user's mail packets, and if
                  new, they will be included regardless of whether or not
                  the user has configured Mail Manager to send new
                  bulletins.

                  Example:

                     c:\bulet1
                     c:\bulet2
                     **c:\bulet3

                  bulet1 and bulet2 are optional, bulet3 will always be
                  included.



                     SYSOP-CONFIGURABLE TEXT FILES                      Page 18
                     -----------------------------

                     (NOTE - The path\filename of MAILMGR.BUL is
                             sysop-configurable in MailCFG.EXE.)

    MAILMGR.PRO - A copy of the RBBS-PC PROTO.DEF that you intend to have
                  Mail Manager use.  Mail Manager can use all of
                  RBBS-PC's "template" variables in here, such as [NODE],
                  [PORT#], [BAUD], etc.  Refer to the RBBS-PC
                  documentation for information on these "template"
                  variables.

                  For Mail Manager's purposes, it is important that you
                  configure "N)one" as the last protocol in this file!
                  You will also need to configure an external X)modem and
                  Y)modem, since Mail Manager obviously cannot use
                  RBBS-PC's internal X and Y that are probably listed in
                  your existing RBBS-PC PROTO.DEF.

                  The supplied MAILMGR.PRO will use X, Y, and Zmodem in
                  the same fashion as previous versions of Mail Manager,
                  requiring DSZ.COM to be in a DOS path.

                  (NOTE - The path/filename of MAILMGR.PRO is
                          sysop-configurable in MAILCFG.EXE).


                 HANDLING NON-STD PORTS VIA MAILMGR.PRO
                 --------------------------------------

    In order to support a nonstandard port address in MAILMGR, have your 
    MAILMGR.PRO specify a custom batch file, rather than a direct call to
    the protocol executable itself.  Your custom batch file can then send
    the correct commands to the protocol, depending on which port is
    involved.

    Here's what an entry in the MAILMGR.PRO file might look like. This
    should all be on one line, of course, but is split here for clarity):

       "Z)modem (Batch)",0,S,8,,B,1024,,0.95,,1=E,
       "X:\ZMODEM.BAT S [PORT#] [BAUD] [FILE]",
       "X:\ZMODEM.BAT R [PORT#] [BAUD] [FILE]"

    With drive X: of course being whatever drive\directory you want.

    Then the ZMODEM.BAT file could look something like (assuming that you
    have ports 1 and 2 at standard addresses, and port 3 at non-standard
    address 3e8, irq 5):

       @ECHO OFF
       : --------------------------------------
       : 1st arg is either S or R,
       : 2rd arg is comm port number
       : 3rd arg is bps rate, and
       : 4th arg is filename being transferred.
       : --------------------------------------



                     SYSOP-CONFIGURABLE TEXT FILES                      Page 19
                     -----------------------------


       IF (%1)==(S) GOTO SEND
       IF (%1)==(R) GOTO RECEIVE
       GOTO END

       :SEND
         IF NOT (%2)==(3) dsz port %2 speed %3 sz -m %4
         IF     (%2)==(3) dsz portx 3e8,5 speed %3 -m sz %4
         GOTO END

       :RECEIVE
         IF NOT (%2)==(3) dsz port %2 speed %3 rz %4
         IF     (%2)==(3) dsz portx 3e8,5 speed %3 rz %4
 
       :END

    This could, of course, be refined into a single batch file that handles
    all protocols, not just Zmodem, but it should serve to illustrate the
    principle.  Or a separate batch file could be set up for each protocol.

    We leave it to you to adapt to protocol drivers other than DSZ.


    MAILMGR.ARL - The list of archivers that are available to your users 
                  through Mail Manager.  MAILMGR.ARL is a "template" file,
                  similar in structure to MAILMGR.PRO.

                  The supplied copy of MAILMGR.ARL allows the use of ARC, 
                  ARJ, LZH, and ZIP compression methods, which the user can 
                  pick and choose from to suit their own preference.  You 
                  can configure fewer or additional archivers as you see
                  fit.  Format of each line:

                  Name, EXT, Compress, Extract

                      Name = The name of the archiver, as shown to the user.
                       EXT = The three-letter extension that this archiver
                             creates by default for compressed files.
                  Compress = The line to send to DOS to compress the mail
                             packets.
                   Extract = The line to send to DOS to extract the uploaded
                             reply packets that the user uploads.

                  "Template" variables that can be included in the Compress 
                  and Extract lines (Mail Manager will convert these to
                  their true values):

                     [FILE]  - Compressed file to create, or extract from.
                     [INC]   - All files that Mail Manager normally
                               includes in the downloadable archive.
                     [REPLY] - Reply file that Mail Manager expects to be
                               contained within the compressed upload.
                     [NODE]  - Current RBBS-PC node number.



                     SYSOP-CONFIGURABLE TEXT FILES                      Page 20
                     -----------------------------

   See the supplied MAILMGR.ARL for an example implementation of this file.

   (NOTE - The path/filename of MAILMGR.ARL is sysop-configurable in
           MAILCFG.EXE).



                  DESQVIEW, NETWORKS, AND MULTIPLE NODES                Page 21
                  --------------------------------------

    Operating in a multitasking environment or on a network is a special
    case, worthy of further explanation!

    First off, Mail Manager can automatically detect the following 
    conditions:

      - Is DOS SHARE installed?
      - Is DESQview present?
      - Is Artisoft's LANtastic present?
      - Is Novell present?

    What Mail Manager detects will be used as the basis for initially
    determining the operating environment, which will be:

      - DESQview, if it is present, regardless of whether or not SHARE is 
        installed.

      - NetBIOS, if DESQview is not present, and SHARE is installed, or
        Novell is detected.

      - Good ole' normal DOS if neither of the above is true.

    Mail Manager will then use the appropriate file locking technique for 
    the type of environment that was detected.  At this point, the only file 
    being accessed is Mail Manager's own configuration file, so your RBBS 
    files are quite safe even if this is not the same environment that you 
    have specified for RBBS to use.

    Once the program has progressed far enough to have read what network 
    type that you told it to use (from DORINFOx.DEF if operating remotely, 
    or MAILMGR.CFG if operating in local mode), Mail Manager will, if
    necessary, switch to your specified type of network.

    With that out of the way, let's talk about the three possible types of
    environments, and what they mean from Mail Manager's standpoint:

    DESQview - Mail Manager will use the same file & record locking scheme
               that RBBS-PC itself uses.  In fact, it uses the very same
               assembler source, which was written by Jon Martin in 1988.
               Therefore, the DESQview semaphore locking routines used by
               Mail Manager are copyrighted by Jon Martin, and are in fact
               available to anyone who has a copy of RBBS-PC's source code.
               Look for RBBSDV.ASM in RBBS-PC's assembler source.
    --------------------------------------------------------------------------

    NetBIOS/ - This is a special case, and requires that physical file and
    Novell     record locking take place.  RBBS-PC uses what is termed as a 
               "semaphore" file, to control access to what Mail Manager is 
               concerned with:  Your USERS file(s), your MESSAGES file(s), 
               and your FMS file (if any).



                  DESQVIEW, NETWORKS, AND MULTIPLE NODES                Page 22
                  --------------------------------------

               This is done with the hard-coded filename "IBMFLAGS", which 
               will exist in the same directory as your MAIN message base.  
               If you're already running RBBS-PC under NetBIOS, look for 
               it... it should already be there.  IBMFLAGS is 6 bytes in 
               length, and contains nothing but three empty 2-byte records, 
               which are controlled by RBBS-PC (and now Mail Manager) to
               limit access to USERS and MESSAGES files.

               Under NetBIOS, Mail Manager will create and maintain its own 
               "semaphore" locking file, using the same principle as 
               IBMFLAGS.  Mail Manager's semaphore file is named MMFLAGS, 
               and will be created in your Mail Manager directory.  MMFLAGS
               will be 3 bytes in length, and manipulated by all nodes of 
               Mail Manager.

               It is also noteworthy to mention that all files will be 
               opened in a SHARED fashion under NetBIOS, which is the nature 
               of the beast.

               If you are running under Novell Netware, Mail Manager will 
               detect it, and will not check for the installation of DOS 
               SHARE.  If Novell is not detected, yet NetBIOS is specified 
               as the environment, Mail Manager will check for DOS SHARE 
               before allowing itself to continue.
    --------------------------------------------------------------------------

    DOS      - Gee, isn't it nice when you don't have to worry about all 
               this?  Under good 'ole DOS, none of the above is meaningful, 
               and all files will be opened normally, with no locking
               mechanisms in place.

    If you happen to be running in an environment that does NOT match any of 
    the above three methods, AND you are sharing the same set of RBBS
    message bases and users files between nodes, you will want to consider
    having DOS SHARE loaded, and configure both RBBS-PC and Mail Manager to
    use NetBIOS as the operating environment.

    Or, if file sharing is not a concern, just configure Mail Manager to use
    DOS as its environment.

    You should NOT set up a separate Mail Manager configuration for each
    node unless your network drive letters are different on each one:

    (C:\MAINM.DEF on one, D:\MAINM.DEF on another).

    Why you'd set your network up that way we don't know, but it isn't our
    place to, is it?  Mail Manager always operates out of a unique work
    directory for each node, and can handle up to 36 nodes with a single
    configuration.



                            WORKING WITH A FOSSIL                       Page 23
                            ---------------------

    Starting with version 1.10, Mail Manager does support a FOSSIL driver.  
    If you told RBBS-PC to use a FOSSIL, Mail Manager will also.  Versions 
    1.10 and up have been tested successfully with both BNU v1.70 and X00 
    v1.2x FOSSILs.

    PLEASE NOTE that some door converters & programs that 'launch' doors for
    you may not correctly set the FOSSIL argument in DORINFOx.DEF!!!!

    The very last line of your DORINFOx.DEF (line #13) should be either a
    zero or minus one (0 or -1).  -1 indicates that the FOSSIL is active in
    RBBS-PC, and tells the door that it too should use a FOSSIL.

    To keep you from having to dig up the RBBS-PC documentation, here's what
    Mail Manager expects from DORINFOx.DEF:

        WORLD'S BEST BBS         <- BBS name (ignored by Mail Manager)
        MAJOR                    <- Sysop's first name
        EGO                      <- Sysop's last name
        COM1                     <- Communications port
        2400 BAUDD,N,8,1         <- Communications parameters
         6                       <- Network type (4=DV, 6=NetBIOS)
        JOE                      <- User's first name
        USERNAME                 <- User's last name
        NEWARK, OH               <- User's city/state
        2                        <- User's graphics preference (2=ANSI)
        10                       <- User's security level
        30                       <- Number of minutes remaining
        -1                       <- FOSSIL in use (0=no, -1=yes)

   * NOTE - The second "D" in "BAUDD" is a bug in RBBS-PC 17.3C, and does
            not affect Mail Manager's operation.

   It is possible to configure Mail Manager to ALWAYS check for a FOSSIL
   driver, regardless of the setting in DORINFOx.DEF.  This is done in the
   MAILCFG program, by setting the flow control method to "F".  In this
   case, Mail Manager will ALWAYS try to use a FOSSIL for communications.  
   See MAILCFG.DOC for further details.



               UTILITY PROGRAMS INCLUDED WITH MAIL MANAGER              Page 24
               -------------------------------------------

   We include two supplemental programs with Mail Manager:

            MAILCFG.EXE  - The configuration program, which is required to 
                           create Mail Manager's configuration file,
                           MAILMGR.CFG.  Once created, MAILMGR.CFG can be
                           edited anytime by re-running this program.

            MAILFIX.EXE  - A handy little program to check/repair/purge/ 
                           re-size/renumber your message bases.  It is
                           compatible with RBBSMail, OverMail, and MsgToss,
                           as well as RBBS-PC itself, and can handle both
                           fixed-length and 'elastic' message bases.  
                           Version 4.0 of this utility is included with 
                           this package.  As later versions become are 
                           issued, they will be available separately.

    These utilities are explained in further detail in the their individual
    documentation (MAILCFG.DOC, and MAILFIX.DOC).



                           SECURITY FEATURES                            Page 25
                           -----------------

    Mail Manager has extensive built-in security functions.  We hope you
    agree that it does make for a pretty secure mail door.

    We want to make you aware of the importance of the security level that
    you configured in the MAILCFG program for the ability to read ALL
    messages.  This security level is checked for all of the sysop functions
    that Mail Manager performs, and should be set to either sysop or
    co-sysop level.  Some of the more important things that users with this
    security level or higher can do:

       - Use the sysop-only function I)nfo from the main menu (which shows
         where everything that pertains to your Mail Manager setup is
         located).

       - Upload a message under a name other than the one that they use on 
         the BBS.

       - Read everybody's mail, regardless of whether it's marked as private
         or password-protected.

    You get the idea.

    ------------------------------------------------------------------

    Conferences are configured with two minimum security levels:  One for
    the ability to read, and the other for the ability to post.

    User can only extract mail from conferences that they have joined from
    the BBS.

    Mail Manager will not add a user to a conference in any case.

    Mail Manager bypasses all killed messages.

    Only conferences which the user has joined are shown in the QWK packets
    that the user downloads.

    Password-protected messages are only extracted and downloaded to users
    with an exact name match in the "TO" or "FROM" fields, or to those with
    sufficient security to read ALL messages.

    Only users with sufficient security to read ALL messages are permitted
    to upload messages under a name other than the one they use on the BBS.

    Users cannot upload messages to conferences that they have not joined.



                           SECURITY FEATURES                            Page 26
                           -----------------

    Mail Manager posts a private message (in the MAIN area) to the sender's 
    true name whenever a security violation regarding an uploaded reply
    occurs.  This can be triggered by:

        - Uploading a message with the "FROM" name not matching the user's
          name on the BBS.

        - Uploading a message to a conference that the user has not joined.

        - Uploading a message to a conference that the user does not have 
          sufficient security to post a message in.

        - Uploading a message to a conference number that does not exist.



                          ADDITIONAL FEATURES                           Page 27
                          -------------------

   CHAT MODE:  While Mail Manager is waiting for a keystroke (preferably at
     [F10]     the MAIN MENU), the Sysop can press [F10] to jump into a no-
               frills chat mode with the user that's currently online.

               When finished with the chat, either one of you can type
               "/QUIT" to return to Mail Manager.
   ----------------------------------------------------------------------
   DOS SHELL:  While Mail Manager is waiting for a keystroke (preferably
     [F2]      at the MAIN MENU), the Sysop can press [F2] to jump to DOS.
               When finished, type EXIT to return to Mail Manager.  
               Naturally, this works only from the local keyboard.  Mail
               Manager will automatically return to the proper drive and
               directory when you type "exit" to return from the DOS shell.
   ----------------------------------------------------------------------
   TIME LIMIT: This is passed to Mail Manager from RBBS-PC in DORINFOx.DEF.
               It will be either the amount of time remaining on your
               RBBS-PC, or whatever time limit that you specified in
               DOORS.DEF, otherwise.  In local mode, the time limit is
               always 120 minutes.
   ----------------------------------------------------------------------
   KYBD IDLE:  If Mail Manager has to wait more than 180 seconds for the
               user to press a key, it will exit back to the BBS.  The user
               will get a beep and a warning message after 90 seconds, and
               every 30 seconds thereafter, until keyboard time expires.
   ----------------------------------------------------------------------
   CARRIER DETECT:  If the user drops carrier, Mail Manager will report to
               you as such, write this info to the appropriate log file, and
               return to the BBS.  RBBS-PC will see that no carrier detect
               is present, re-cycle itself, and wait for the next caller.
   ----------------------------------------------------------------------
   DOWNLOAD & EXIT:  Although the E)xpedite! option is documented
              elsewhere in this manual, we didn't make it clear as to the
              best way to automate this from RBBS-PC's standpoint.

              RBBS-PC 17.3C and above allow you to specify "/G" after the 
              name of the door, which allows the user to be logged off
              immediately after returning to RBBS-PC.  Therefore, the users
              could type:

                               d mailmgr /g

              Then, from within Mail Manager, select E)xpedite!, and the
              user will be logged completely off the BBS after downloading
              their mail.
   ----------------------------------------------------------------------



                          ADDITIONAL FEATURES                           Page 28
                          -------------------

   NEW FILES: If you are running a standard RBBS-PC FMS directory, you
              should be able to use this built-in capability.  If you are
              not running a standard FMS, and the path/name of your FMS
              directory is set to "NONE" in the MAILCFG program, Mail
              Manager will not attempt to include a new file listing in the
              user's mail packets.

              It should be noted here that the users do have the ability to 
              turn this feature "off", if they do not desire a file listing
              in their mail packets.

              Here's what is required of your FMS directory:

                - No 'special' lines contained within it (semi-private 
                  filenames preceded with an asterisk (*) before the
                  filename, special comment lines, etc).

                - Oldest files listed at the top of the FMS, and most recent 
                  files listed at the bottom.

             If yours fits all of the above, NEWFILES should work fine.

             Here's the way NEWFILES works:

             1) Finds the date that the user last checked the file listing 
                (from the RBBS-PC main users file).  If user never listed
                your file directories, the user's last date into the Mail
                Manager door is used, instead.

             2) Grabs the very first line of your FMS, to determine the line 
                length, since this can vary depending on how you set things 
                up via RBBS-PC's CONFIG.  HOWEVER, all lines in your FMS are 
                expected to be the same length as the first line listed!

             3) After determining line length, moves to end of file, grabs 
                the very last line of your FMS, and checks the date stamp 
                against the user's "last check" date.

             4) If the last file's date is the same as, or newer than, the 
                user's date that they last listed your files, NEWFILES steps
                through your FMS in reverse order, pulling out filenames & 
                extended descriptions until the date stamp is earlier than 
                the user's last check.  The file created (NEWFILES.DAT) is 
                then included in the user's QWK mail packet, and can be 
                viewed easily within his mail reader.

             If the last file's date is older than the user's last check, 
             NEWFILES figures no new files, and doesn't include a 
             NEWFILES.DAT in the QWK packet.

             PRIVATE UPLOADS TO THE SYSOP are listed ONLY in the sysop's own
             mail packets.  These files (and their extended descriptions)
             are skipped for everyone else.



                          ADDITIONAL FEATURES                           Page 29
                          -------------------

             If you use chained FMS directories, or any of the "\FMS" 
             directives, NEWFILES will stop searching when it reaches that 
             line of your FMS.  Why?  The line won't be an extended
             description  ("  ." as the last three characters on the line),
             and won't have a file date in the proper positions on the line.
             In this case, NEWFILES will consider the file date to be
             00-00-00, and will quit searching your FMS directory.



                              THE MAIN MENU                             Page 30
                              -------------

    Although we hope that you'll find Mail Manager to be pretty self- 
    explanatory, a complete run-down on everything that you can do with this 
    door follows.

    A shorter version of this is available to the user, in the online help
    file MAILMGR.HLP and MAILMGRC.HLP.

    The menu itself looks like this:

                        MAIL MANAGER Main Menu:

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ C)onfigure Mail Manager.                           ÃÄ¿
         ³ D)ownload new mail from your selected conferences. ³ ³
         ³ E)xpedite!  (Download new mail and return to RBBS) ³ ³
         ³ Q)uit (return to bbs)                              ³ ³
         ³ H)elp!                                             ³ ³
         ³ M)essage number (lowest) to extract in each conf.  ³ ³
         ³ W)ho's online to RBBS-PC?                          ³ ³
         ³ U)pload your replies.                              ³ ³
         ³ X)pert toggle (this menu on/off)                   ³ ³
         ÀÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
           ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

    Your choice, Username <C,D,E,Q,H,M,W,U,X,?>?

    MAIN MENU commands are as follows:

    C - Configure Mail Manager.

       Allows you to select your personal options, and change your selected 
       conferences from which to extract new mail.  Please note that you 
       must J)oin the conference from the BBS before you can extract mail 
       via this door. Otherwise, Mail Manager will not find you as a valid
       conference user, and will not access the conference for you.

       You'll be presented with a screen that looks something like this:

       ----------------------------------------------------------------------



                              THE MAIN MENU                             Page 31
                              -------------

         Configuration options:

         A - Select conferences to extract and download.
         B - Download messages in Q)WK or T)ext format..........: Q
         C - Msgs addressed to ALL marked as personal (QWK only): No
         D - Extract ONLY your personal mail ...................: No
         E - Extract messages written by YOU ...................: Yes
         F - Abort packet if no messages .......................: No
         G - Send updated bulletins ............................: Yes
         H - Send new file listings ............................: Yes
         I - Ask before sending packet .........................: No
         J - Type of file compression to use ...................: ZIP
         K - Default file transfer protocol ....................: Z
         L - Tell RBBS that you've read your downloaded messages: Yes
         T - Use 'TurboKeys' (act on 1-character commands) .....: No
             -----------------------------
         Q - Quit.  (Finished configuring)

         Enter your choice(s), UserName <A,B,C,D,E,F,G,H,I,J,K,L,Q> ->
       -----------------------------------------------------------------------

         A - Select conferences to extract and download.

               You'll be presented with a list of conferences that you are 
               able to access, which will look something like this:

               ---------------------------------------------------------------
               You may select any conference which is shown in UPPER CASE.
               Confs you've marked as active are surrounded in brackets '[]'.
               Confs shown in lower case must first be joined from the BBS.
               Confs marked as --- are not available.

                  1 - [MAIN   ] 11 -  TEEN     21 - [RSYS   ]
                  2 - [4SALE  ] 12 - [PRIVATE] 22 - [BITS   ]
                  3 - [MS-DOS ] 13 - [SYSOP  ] 23 - [POL    ]
                  4 -  BBS      14 - [USER   ] 24 - [CRES   ]
                  5 -   ---     15 -   grafx   25 - [WINB   ]
                  6 - [CODE   ] 16 -   arj     26 - [MAILMGR]
                  7 - [DEBATE ] 17 -   ---
                  8 - [HAM    ] 18 - [QB     ]
                  9 -  HUMOR    19 - [RBBS   ]
                 10 - [IBM    ] 20 - [DEV    ]

               Enter conference number(s) to toggle on/off, or [ENTER] to quit.
               ->
               ---------------------------------------------------------------

               In this example, all conferences that are available to you 
               are flagged as active, except BBS (conference 4), HUMOR
               (conference 9), and TEEN (conference 11).



                              THE MAIN MENU                             Page 32
                              -------------

               If you wanted to mark those three as active, you'd enter:

                     4 9 11

               at the above prompt.

               Conferences #5 and 17 are unavailable, meaning that the user 
               either has insufficient security to access them, or you (the 
               Sysop) have "reserved" these conference numbers in the
               MAILCFG program, for future use.

               Conferences #15 and 16 are active conferences, but the user
               must join them from the BBS before they will be available to 
               them via Mail Manager.


         B - Download messages in Q)WK or T)ext format

                Set to text if you want to use Mail Manager as a simple
                "extract and download" system (all messages in a single
                continuous ascii file).

                Set to QWK if you want to read and reply offline using a 
                QWK-compatible mail reader like SLMR.

         C - Msgs addressed to ALL marked as personal (QWK only)

               If set to "Y", Mail Manager will add messages addressed to 
               "ALL" to your personal index.  This applies to QWK packets
               only.

         D - Extract ONLY your personal mail

               If set to "Y", Mail Manager will not extract a message unless 
               it is addressed to you.  (Will also extract msgs addressed to
               "ALL" if you have option C set to "Y".)

         E - Extract messages written by you

               If set to "NO", Mail Manager will not include messages from
               you in your packet.

         F - Abort packet if no new messages

               You might not want to do this if you would still like to 
               receive new file listings or updated system news or
               bulletins.



                              THE MAIN MENU                             Page 33
                              -------------

         G - Send updated bulletins

               If set to "No", any updated bulletins which the sysop has 
               designated as mandatory will still be included.

         H - Send new file listings

               If you select this option, a listing of newly-uploaded files
               will be included in your mail packet.

               This option may not be operational on all systems.

         I - Ask before sending packet

               If set to "Yes", will cause Mail Manager to prompt you 
               whether or not you want to receive the mail packet that it 
               just created for you.  Will otherwise go right into the 
               download when finished extracting.

         J - Type of file compression to use

               If the Sysop has activated this option, you can choose from 
               the file compression utilities offered on this system (ZIP,
               ARC, etc.).

         K - Default file transfer protocol

               Choose from the protcols offered by your sysop (Xmodem, 
               Zmodem, etc.).  If set to N)one, Mail Manager will prompt you
               for which protocol to use at each file transfer.

         L - Tell RBBS that you've read your downloaded messages

               If this is set to NO, both RBBS and Mail Manager will think 
               that you haven't read the messages that you've downloaded. 
               (Mail Manager will extract them again your next time in).

         T - Use 'TurboKeys' (act on 1-character commands)

               Works like RBBS-PC's toggle of the same name.  If set to Yes, 
               Mail Manager will not wait for [ENTER] when asking you for 
               input.

         Q - Quit. (Finished configuring)

               (Or just press [ENTER] to accomplish the same thing).

       After this screen, you'll be asked to save your current choices.  You 
       MUST answer "Y" if you want your changes to be saved for subsequent
       visits to the Mail Manager door.

       (If this is your first time into the door, your changes will be saved
       automatically).

   --------------------------------------------------------------------------



                              THE MAIN MENU                             Page 34
                              -------------

   D - Download new mail.

       Will find and extract all new mail from your selected conferences, in 
       the format that you told Mail Manager to use (Text or QWK).

       Mail Manager will then compress the file(s) in your selected file 
       compression format.

       Unless your file protocol is set to N)one, Mail Manager will then 
       send you the mail packet.  If your default protocol is set to N)one, 
       you'll be asked for the transfer protocol of your choice.  If you 
       choose "N", the file will not be sent to you, and you'll be returned 
       to the main menu.  Otherwise Mail Manager will do its best to send a 
       compressed version of the mail to you via your selected choice.

   ---------------------------------------------------------------------------

   E - Expedite!

       Same as Download (above), except automatically exits back to the main
       bulletin board when finished.

   ---------------------------------------------------------------------------

   Q - Quit (return to BBS).

       This one should be pretty self-explanatory.

   ---------------------------------------------------------------------------

   H - (Or '?') Display help file.

       Displays an abbreviated version of these command descriptions.

   ---------------------------------------------------------------------------

   I - Sysop Information

       This command is not shown in the online help file, is not displayed 
       in the command prompt, and is not shown in the menu itself.

       Only those with sufficient security to read ALL messages will be able 
       to activate this command.  Everyone else will get the familiar
       "Command not recognized".

       The purpose of this command is to assist you in debugging your setup, 
       and it is covered in detail elsewhere in this manual under "DEBUGGING
       YOUR SETUP".

   --------------------------------------------------------------------------



                              THE MAIN MENU                             Page 35
                              -------------

   M - Message number (lowest) to extract in each conference.

       Mail Manager will normally download mail based on the last message 
       that you've read in each conference.  Since you can read mail both 
       online AND offline, and have the option of telling Mail Manager NOT
       to update your last message read markers, you might want to use this
       option to reset them to what you want.

       Requirement for using this option:

           - You must have already joined the conference from the main board
             (as with all conferences that you manipulate via this door).

       If you get an error while changing your message markers, try going
       back through the C)onfigure option, saving your settings, and try
       again.

   ---------------------------------------------------------------------------

   U - Upload your replies.

       Works with QWK-compatible mail reader/repliers only. Your uploaded
       file is expected to be compatible with the .REP format used by
       popular mail readers such as SLMR.  Mail Manager will look for the
       REP packet after the upload and attempt to place your replies into 
       the proper message bases.

       If your default protocol is set to N)one, you'll be asked for the 
       protocol that you wish to use.  If you select N)one, you'll be
       returned to the main menu.

       If you're in local mode as the Sysop, place the .REP file in the 
       \MAILMGR\LOCAL directory, and choose this option.  This is covered
       further in the section regarding "DEBUGGING YOUR SETUP".

   ---------------------------------------------------------------------------

   W - Who's online?

       Displays a list of who's online to all nodes of this RBBS-PC.  (Much
       like RBBS's command of the same name).

       Those with sufficient security to read ALL messages will have the 
       following displayed:

           - User's name, 
           - City/State, and
           - Baud rate.



                              THE MAIN MENU                             Page 36
                              -------------

           If a node is inactive, the last user's information is displayed,
           and will be reported as "Last call".

       All other users will have the following displayed:

           - User's name, and
           - baud rate.

           If a node is inactive, "Waiting for next caller" is displayed.

   ---------------------------------------------------------------------------

   X - Expert toggle.

       Turns the main menu on or off.  (Much like RBBS's command of the same
       name).

       This setting is saved for the user's next time into the door.



                      APPENDIX A - COMMON PROBLEMS                      Page 37
                      ----------------------------

Problem :  Not finding the Sysop in any conferences.

Solution:  Double-check your setting of "Remote Sysop Name" on the first 
           screen of the MAILCFG program.  This setting must be the name
           that you use to log onto your system remotely, NOT your name as
           you are known to your users.

--------------------------------------------------------------------------

Problem :  Shows "Error finding new message" when trying to extract your
           first mail packet.

Solution:  Run MAILFIX.EXE against the message base in question (using the
           proper command line switches).  Re-read the section of this
           document entitled "Before you begin".

--------------------------------------------------------------------------

Problem :  Always showing Sysop name when operating remotely.

Solution:  Probably not copying the correct DORINFOx.DEF file to the Mail
           Manager directory prior to loading the door.  Drop to DOS, and
           take a look at the DORINFOx.DEF that was in use at the time.

        /------------------[ v1.20 to v1.24 ]---------------------\

         The authors spent the majority of the development time on v1.30
         extensively tracking a problem that exists only when Mail Manager
         is executed on a system that has a math co-processor installed.

         Weird problems prevailed, including:

            - Freezing at the "Checking conferences:" prompt,
            - Looping back to "Initializing Mail Manager:" after checking
              conferences, and THEN freezing,
            - Runs ok sometimes, sometimes locks the CPU.

         We have spent weeks trying to track this down, and could not find
         anything in Mail Manager that could cause such a thing to happen.

         The problem was FINALLY traced to floating point implementation
         when running on a co-processor or 486.

         We have worked out replacement routines that eliminate *ALL*
         floating point calculations from Mail Manager.  With the releases
         of v1.30 and up, we believe these problems are a thing of the
         past.  (Crossing fingers and knocking on wood)


                       APPENDIX B - CONTACTING THE AUTHORS              Page 38
                       -----------------------------------
         Up through this release, Mail Manager +Plus+ has been a joint effort
         of Chip Morrow and Doug Wilson (SysOp and Co-SysOp of Mail Manager's
         original home bbs).  Personal time commitments are forcing serious
         cutbacks on Chip Morrow's involvement in future Mail Manager
         development, and the closing of Mail Manager's home BBS.

         But, Doug Wilson is continuing under the new banner of Makai
         Software, and both of us are continuing to provide support.
         Comments, ideas, suggestions, and whatever else you want to throw
         our way are always appreciated and should be directed to any of
         the following:

         Good ole' US Mail:
                             Makai Software
                             870 Golden Drive
                             Newark, OH 43055

         Bulletin boards:
         
            Three RBBS-PC boards have agreed to jump in as official Support
            Sites in the wake of the closing of Mail Manager's original home
            board.  All three have the latest versions of Mail Manager, Mail
            Manager +Plus+, MailFix, MNET, and any other RBBS-related software
            we may develop.  The sysops have committed to making these files
            available to first time callers, bypassing the usual new user
            registration hassles, when they log on with the special
            username/password combinations shown below:
            
            Board:        BRODMANN'S PLACE   HOTLine Co-op   THE DOG HOUSE
            Location:     Waldorf, MD        Monroe, LA      Kings Beach, CA
            Sysop:        Dave Brodmann      Eddie Rowe      Kip Gies
            Phone:        301-843-5732       318-345-1955    916-546-7002
            Modem:        HST/v.32bis        v.32bis         v.32bis
            Username:     FREE GUEST         HOTLINE BBS     MAILMGR LATEST
            Password:     USER               GUEST           VERSION
            Net Address:  Fido 1:109/806     Fido 1:380/14   RBBS 8:919/20
                          Rime ->BRODMANN
            
            In addition, a local (to us) BBS that we both check into on a near-
            daily basis is:

               THE MOTHER BOARD (WildCat!)
               Buckeye Lake, OH
               Michael Graham, Sysop
               Data line: 614-928-2259
               Modem: HST/v.32bis
               Fido: 1:226/1400

               Fido netmail sent to The Mother Board or messages left there
               directly will probably get the fastest response.


                       APPENDIX B - CONTACTING THE AUTHORS              Page 39
                       -----------------------------------

            We check into all of these boards on a regular (but not necessarity
            daily) basis, and will answer questions left on or netmailed to any
            of them.  The Mother Board, being a local call, gets the most
            attention and is probably the place to get the fastest response.
            Please leave messages as PUBLIC so that whichever of us calls first
            will be able to see them.  The sysops of the three Support Boards
            are all experienced with Mail Manager, and may be able to handle
            some of your questions without help from Chip or me.
            
         Computer network conferences:
            
            We will also continue to monitor the following computer network
            conferences.  If you don't have access to Fido netmail, these may
            be your best bet for obtaining support in a timely fashion:

                                RIME:  RBBS-PC and RBBSQWK
                                FIDO:  RBBS-PC and OFFLINE

         We're sorry, but we simply do not have the time or resources to make
         voice calls to help with debugging your individual Mail Manager setup.
         On the other hand, we'd like to see you in any of the above echo
         conferences, where you can get help from others as well as ourselves,
         and where questions/answers/reports/release notices get a much wider
         audience, and can benefit more people.



             APPENDIX C - SUGGESTIONS SINCE INITIAL RELEASE             Page 40
             ----------------------------------------------

  We've had a slew of 'em.  Keep 'em coming!  We can't get better without
  your input.

  Most frequent suggestions:

     - Easier/faster setup for MANY conferences      : done  v1.04
     - New bulletins included in QWK's               : done  v1.04
     - New NEWS file included in QWK's               : done  v1.04
     - Less screwing around with RBBSQWK.BAT         : done  v1.04 & v1.10
     - NEWFILES.EXE supporting extended descriptions : done  v1.04
     - Non-standard IRQ and address support          : via FOSSIL & PROTO.DEF
     - File/Record locking                           : done  v1.10
     - Desqview awareness                            : done  v1.10
     - FOSSIL support                                : done  v1.10
     - Add new bulletins/news to TEXT packets        : done  v1.10
     - Allow configurable type of file compression   : done  v1.20
     - Allow configurable transfer protocols         : done  v1.20
     - Support FIDO-style conferences as well as RBBS: *
     - Ability to join conferences from within MMGR  : *
     - Support for conferences allowing aliases      : *
     - Select "personal only" for individ. confs.    : *
     - Support for more than 250 conferences         : *
     - Support "net-status" packets from other BBSs  : *
     - Convert "smart text" in news, bulletins       : *
     - Use individual conference security levels     : *
     - Ability to use text editor to modify config.  : *
     - Editor for MAILMGR user file                  : *
     - Support "net status" QWK packets              : *

               * Implemented in Mail Manager +Plus+

  



                     APPENDIX D - ACKNOWLEDGEMENTS                      Page 41
                     -----------------------------

  Microsoft, Crescent Software, DSZ, PKZIP, LHARC, ARJ, LZEXE, PKLITE,
  Jimmer, TQM, LANtastic, DESQview, BNU, X00, RBBSMAIL, MSGTOSS, OVERMAIL,
  PDQ, PDQCOMM, QuickBASIC, RBBS-PC, SLMR, JABBER, OFFLINE, and OLX (did we
  miss any?) are all trademarks or copyrighted in some way by somebody, and
  are mentioned throughout our documentation for clarity only.

  Special thanks to:

      Mike Ervin, who tested early beta versions on his system and verified
      that it really worked in an environment other than our own.

      Tom Craver, who tested the very last beta version prior to the initial
      release of v1.01b, and helped us get 38,400 bps taken care of.

      Craig Gagner, who actually sent us an exact sample of the error
      message reported when opening the communications port under DESQview.
      Had LOTS of reports on this one.

      Glenn Rossi, who first suggested adding extended file description
      support, wrote his own converter to handle them, pointed us in the
      right direction for DESQview, and tested a late beta of v1.10 under
      DESQview for us.

      Jon Martin, who was nice enough to supply the world with assembler
      source for DESQview resource locking.

      Joe Tailleur, who tested several beta versions for us under DESQview.

      Michael Lurie, who put up with seemingly never-ending system crashes
      while testing beta copies.  Michael, you're a patient individual!

      Gregg Snyder who was the first brave soul to try non-standard port
      addresses.

      Don Smith, who tested a few late beta versions of v1.24 for us under
      Novell.

      Doug Azzarito, current co-author of RBBS-PC, who thinks enough of our
      door to run it on his own system, and offer beta-testing.

      Dave Brodmann, who's 486 was used as a guinea pig for the floating
      point problem, and other experiments.  Yet another patient individual!

      Benny Carr, who also has a math co-processor system that was abused by
      beta copies.

  And thanks to everyone else who commented & offered suggestions, help, and
  beta testing.  We honestly cannot remember all of the names, and do
  apologize for that!



                     APPENDIX D - ACKNOWLEDGEMENTS                      Page 42
                     -----------------------------

  I must express one HUGE debt of gratitude to Chip Morrow, who poured his
  heart and soul into the development of Mail Manager for over two years,
  and who has been an absolute joy to work with.  Without Chip, there would
  be no Mail Manager.  Period.  If there is anyone out there who better
  exemplifies the Spirit of RBBS as defined by Tom Mack, I have yet to meet
  him.

  We are frankly astounded at Mail Manager's quick success and wide
  distribution (we've had file requests from Nova Scotia to Taiwan), and
  hope we can continue to provide everyone with a truly useful piece of 
  software for your RBBS-PC.

                                       Doug Wilson
                                       Makai Software



               APPENDIX E - FOR TRULY CURIOUS-TYPES ONLY!               Page 43
               ------------------------------------------

     For the few who have been curious enough to ask, Mail Manager is a
     multiple-module, modern-dialect BASIC program, compiled & linked using
     Microsoft's QuickBASIC, and Crescent Software's PDQ and PDQComm.  (We
     speculate that Mail Manager may have the world's record for the largest
     PDQ/PDQComm-specific program to date...  <grin>...).

     The source code for Mail Manager is available upon request, for those 
     who would like to see how it works.  The commerical PDQ and PDQComm 
     libraries ARE required to use this code, and rewriting to eliminate
     them would be exhaustive at best, and impossible at worst.  To receive
     a copy of the source code, send a formatted diskette of your chosen
     format and a self-addressed mailer with sufficient postage affixed to:

                          Makai Software
                          870 Golden Drive
                          Newark, OH 43055

     SIDE NOTE REGARDING COMPRESSED EXECUTABLES:
     --------------------------------------------------------------
     We're distributing the executables in non-compressed format.  You'll
     find that our .EXE's will compress quite nicely with utilities like
     PKLITE and LZEXE.  We leave it up to you to use the compression utility
     of your choice, or run as-is.
     --------------------------------------------------------------



                 APPENDIX F - MAIL MANAGER'S FILE FORMATS               Page 44
                 ----------------------------------------

    Just in case someone out there has an inkling to write a utility program
    or two for use with their Mail Manager setup, here are the formats for
    Mail Manager v1.36's two binary system files, MAILMGR.CFG and
    MAILMGR.USR.

    +-------------------------------------------------------------------------+
    | MAILMGR.USR - Mail Manager's internal users file.                       |
    |               One 884-byte record per user.  Each 884-byte record is    |
    |               broken down as follows:                                   |
    |-------------------------------------------------------------------------|
    | Start  Stop  Length  Record Type   Description                          |
    |=========================================================================|
    |     1    31      31    STRING      The user's name, in upper case,      |
    |                                    left-justified, padded with ASCII 32s|
    |-------------------------------------------------------------------------|
    |    32   281     250    STRING      Conference-active flags. ASCII 1 if  |
    |                                    flagged as active, ASCII 255 if not. |
    |                                    1 flag for each of the 250 possible  |
    |                                    conferences.                         |
    |-------------------------------------------------------------------------|
    |   282   781     500    STRING      UNUSED - This field is now redundant,|
    |                                    and will be removed entirely in a    |
    |                                    future release.                      |
    |-------------------------------------------------------------------------|
    |   782   782       1    STRING      User's QWK preference.  Either "Q"   |
    |                                    or "T".  (QWK or TEXT).              |
    |-------------------------------------------------------------------------|
    |   783   783       1    STRING      User's flag for whether or not to    |
    |                                    update last message read in the RBBS |
    |                                    user files (after downloading pkts). |
    |                                    ASCII 1 for true, 255 for false.     |
    |-------------------------------------------------------------------------|
    |   784   784       1    STRING      Letter of the user's default file    |
    |                                    protocol choice, in upper case.      |
    |-------------------------------------------------------------------------|
    |   785   785       1    STRING      Messages addressed to "ALL" marked   |
    |                                    as personal in QWK packet?  ASCII 1  |
    |                                    for true, 255 for false.             |
    |-------------------------------------------------------------------------|
    |   786   786       1    STRING      Xpert toggle on or off (ASCII 1, 255)|
    |-------------------------------------------------------------------------|
    |   787   787       1    STRING      Bit flag byte for other user options.|
    |                                    Currently used:  0 = Send own msgs   |
    |                                                     1 = Send bullets    |
    |                                                     2 = Send newfiles   |
    |                                                     3 = Abort if no msgs|
    |                                                     4 = Ask before send |
    |                                                     5 = Only pers mail  |
    |                                                     6 = Turbokey toggle |
    |-------------------------------------------------------------------------|
    |   788   790       3    STRING      User's choice of archiver (ZIP, ARC, |
    |                                    etc.)                                |
    |-------------------------------------------------------------------------|
    |   791   796       6    STRING      "YYMMDD" that user last used the     |
    |                                    door. ("911223" = 23 Dec 91)         |
    |-------------------------------------------------------------------------|
    |   797   884      88    STRING      Reserved for future use.             |
    +-------------------------------------------------------------------------+



                 APPENDIX F - MAIL MANAGER'S FILE FORMATS               Page 45
                 ----------------------------------------

    +-------------------------------------------------------------------------+
    | MAILMGR.CFG - Mail Manager's configuration file.                        |
    |               Consists of one 556-byte header, followed by a number of  |
    |               334-byte conference configuration records.                |
    |                                                                         |
    |                           HEADER RECORD:                                |
    |-------------------------------------------------------------------------|
    | Start  Stop  Length  Record Type   Description                          |
    |=========================================================================|
    |     1    35      35     STRING     Name of the BBS (in proper case).    |
    |-------------------------------------------------------------------------|
    |    36    66      31     STRING     Remote logon name of the sysop (left-|
    |                                    justified, in upper case, padded with|
    |                                    ASCII 32 blanks).                    |
    |-------------------------------------------------------------------------|
    |    67    81      15     STRING     Sysop's public first name.           |
    |-------------------------------------------------------------------------|
    |    82    96      15     STRING     Sysop's public last name.            |
    |-------------------------------------------------------------------------|
    |    97    98       2    INTEGER     Security level to read ALL messages. |
    |-------------------------------------------------------------------------|
    |    99   100       2    INTEGER     Security level to use in local mode. |
    |-------------------------------------------------------------------------|
    |   101   102       2    INTEGER     Local sysop's graphic preference.    |
    |                                    2 = ANSI, 1 = ASCII, 0 = None.       |
    |-------------------------------------------------------------------------|
    |   103   163      61     STRING     Default tagline for all conferences. |
    |-------------------------------------------------------------------------|
    |   164   165       2    INTEGER     Number of 334-byte conference        |
    |                                    configuration records that follow    |
    |                                    this header record.                  |
    |-------------------------------------------------------------------------|
    |   166   173       8     STRING     First 8 characters of extract file   |
    |                                    name to use (this is the "*" of      |
    |                                    *.QWK, *.REP, *.ZIP, etc.).          |
    |-------------------------------------------------------------------------|
    |   174   176       3     STRING     3 upper case characters designating  |
    |                                    the default file compression type    |
    |                                    (ZIP, ARC, ARJ, or LZH)              |
    |-------------------------------------------------------------------------|
    |   177   216      40     STRING     Full path/filename of the NEWS file. |
    |-------------------------------------------------------------------------|
    |   217   256      40     STRING     Full path/filename of the list of    |
    |                                    bulletins (MAILMGR.BUL).             |
    |-------------------------------------------------------------------------|
    |   257   257       1     STRING     Network type to use in local mode.   |
    |                                    D)os, N)etbios, desQ)view.           |
    |-------------------------------------------------------------------------|
    |   258   258       1     STRING     Handshake method to use, upper case. |
    |                                    R)ts, X)on, N)one, or F)ossil.       |
    |-------------------------------------------------------------------------|



                 APPENDIX F - MAIL MANAGER'S FILE FORMATS               Page 46
                 ----------------------------------------

    |   259   260       2    INTEGER     Version number (1.36 = 136).         |
    |-------------------------------------------------------------------------|
    |   261   300      40     STRING     Path/filename of MAILMGR.PRO         |
    |-------------------------------------------------------------------------|
    |   301   340      40     STRING     Path/filename of FMS directory.      |
    |-------------------------------------------------------------------------|
    |   341   380      40     STRING     Path/name of list of archivers.      |
    |-------------------------------------------------------------------------|
    |   381   395      15     STRING     Name of environment variable to check|
    |                                    path/name of XFER-x.DEF log file.    |
    |-------------------------------------------------------------------------|
    |   396   396       1     STRING     Modify uploaded messages date & time |
    |                                    stamp to the current system time?    |
    |                                    (Y or N)                             |
    |-------------------------------------------------------------------------|
    |   397   427      31     STRING     City/State where BBS is located.     |
    |-------------------------------------------------------------------------|
    |   428   439      12     STRING     Phone number of BBS. "xxx-xxx-xxxx"  |
    |-------------------------------------------------------------------------|
    |   440   556     117     STRING     Reserved for future use.             |
    +-------------------------------------------------------------------------+


    +-------------------------------------------------------------------------+
    |                    CONFERENCE CONFIGURATION RECORD:                     |
    |-------------------------------------------------------------------------|
    | Start  Stop  Length  Record Type   Description                          |
    |=========================================================================|
    |     1     7       7    STRING      Name of the conference, upper case.  |
    |-------------------------------------------------------------------------|
    |     8    87      80    STRING      Path/name to USERS file.             |
    |-------------------------------------------------------------------------|
    |    88   167      80    STRING      Path/name to MESSAGES file.          |
    |-------------------------------------------------------------------------|
    |   168   168       1    STRING      Allow ANSI in REPs?  "Y" or "N".     |
    |-------------------------------------------------------------------------|
    |   169   169       1    STRING      Allow high/low ASCII in REPs? Y, N.  |
    |-------------------------------------------------------------------------|
    |   170   171       2   INTEGER      Security level needed to join.       |
    |-------------------------------------------------------------------------|
    |   172   173       2   INTEGER      Security level needed to post.       |
    |-------------------------------------------------------------------------|
    |   174   234      61    STRING      Tagline for this conference.         |
    |-------------------------------------------------------------------------|
    |   235   235       1    STRING      Fido-style tearlines?  ("Y" or "N"). |
    |-------------------------------------------------------------------------|
    |   236   236       1    STRING      Fixed-length message base? (Y, N).   |
    |-------------------------------------------------------------------------|
    |   237   334      98    STRING      Reserved for future use.             |
    +-------------------------------------------------------------------------+