This document describes how to do multiple outbound forwards.  The
normal mode is only one outbound forward which was the same mode as
before this feature was added.  If you are not using this feature then
the only difference will be that some of the prefixes on the messages
will be changed.

Groups
------

Forwarding is now done in groups.  There are a maximum of ten groups
numbered 0 to 9. The number of groups is set by the parameter
'MAXIMUM_FORWARD_GROUP' in PARMS.BB.  The default is 0 which means you
have only one group and the system behaves as it did without this
feature.

The number of groups is the MAXIMUM number of simultaneous forwards that
can be done.  Each group will need at least 20K of memory.

Ports
-----

Each port is assigned to a group using the 'FORWARD_GROUP' parameter in
PARMS.BB.  This parameter appears in the port section for each port.

All ports in a group will contend for forwarding.  If you have

    Group 1  -- Port A and Port B
    Group 2  -- Port C

then Group1 can forward either port A or port B but not both
simultaneously.  Port C can forward anytime without regards to ports A
and B.

Group 0 and Wakeup
------------------

The wakeup actions are run in group 0. If you want to be able to forward
out a port while a wakeup action is in progress, don't put that port in
group 0. In fact, I recommend no ports in group 0.

Command changes
---------------

The "X" commands now have a group number.

   X[n] [path] [PORT p] [FORCE] [CONNECT]

       Start a forward.

         n -- optional group number.  The highest group number is
              assumed if it is omitted.

         path -- optional path pattern.  If specified, forward to
              the paths specified.  Wildcards can be used.

         PORT p -- option port pattern.  If specified, forward to
              only the ports specified.  Wildcards can be used.

         FORCE -- Force a connect to even if there are no messages
              waiting.

         CONNECT -- Allow a connect to even if this station is connected
              on another channel/port.

       Examples:

          X
          X3
          X2 PORT B*
          X3 WB6* CONNECT
          X  WW6L FORCE CONNECT


   X[n]STOP [ALL]

       Stop forwarding

         n -- optional group number.  The highest group number is
              assumed if it is omitted.

         ALL -- indicates that this will affect all groups.

       Examples:

          XSTOP
          X1STOP
          XSTOP ALL

Using WAKEUP to get more forwarding
-----------------------------------

Since the WAKEUP commands now run independent of the forward commands,
you can use WAKEUP to start forwarding.  Since you can define groups
with no ports, these are useful for extra forwarding.  A line like

931203/1437 ==/==/== +01:00 X5 WW6L

Will cause group 5 to forward to WW6L every hour independent of what the
other groups are doing.

There are some interesting possibilites with this feature.