The  following  are the known patches for DOUBLEDOS version  4.0.  You 
should  always work with a copy of the file and not the original.  The 
DEBUG  program should be available via path or be  called  explicitly. 
The patch dialog would be something like the following: 

C:\dirname\>DEBUG DOUBLED2.PGM (could also be DOUBLEDO.PGM)
-       enter changes as specified in patch
-W
writing xxxx bytes
-Q

----------------------------------------------------------------------
Revert to version 'V'
COPY A:DBLDVPGM.DRV C:\dirname\DOUBLEDO.PGM
note: this isn't a permanent change. reinstalling the program will 
restore it to version 4.0
----------------------------------------------------------------------
HP Vectra (old model)                                          1/14/87
-E 85D5 F5          (old value BA)
note: will not work with International Quartz laptop after this patch.
----------------------------------------------------------------------
IBM P/S 2 model 30                                             4/28/87
-E 9075 BA 42 21    (old values 47 FE 45)
-E 9829 09 71       ( "    "    E0 F8)
-E 982E AF 3A 58 A9 ( "    "    47 87 3D D0)
note: fixes screen problem.
----------------------------------------------------------------------
Sanyo MBC-990                                                   7/2/87
-E 99DB 12 09
note: removes an I/O word read that fails on this machine.
----------------------------------------------------------------------
HP Vectra (ES & CS)                                           12/22/87
-E 84C6 09 84 42    (old values 8E AA FF)
-E 99D1 48 24       ( "    "    3A 55)
note: will only work on systems with three 8259's after this patch.
----------------------------------------------------------------------
IBM DOS 3.3                                                    4/24/87
-E 2130 20          (old value 10)
-E 878C C0 A1       ( "    "   41 81)
-E 8B7D 03 50       ( "    "   6C 4C)
-E 9487 7F FF B7 6E 20 80 C2
                    ( "    "   A7 E0 C5 32 0B 33 FF)  
note: will not work with any other operating system after this patch.
----------------------------------------------------------------------
Columbia DOS 3.20
-E 8B7D CE          (old value 6C)
note: will not work with any other operating system after this patch.
----------------------------------------------------------------------
HP Vectra DOS 3.2                                             12/22/87
-E 8B7D F6          (old value 6C)
note: will not work with any other operating system after this patch.

----------------------------------------------------------------------
very slow printing w/clock or interrupt
-E 116 EA 83        (old values 6E B0)
-E 24A9 21 90       ( "    "    E8 BD)
note: only use with clock or interrupt when very slow printing occurs.
----------------------------------------------------------------------
Drives with volumes larger than 32 megabytes
-E 4E3A 5F B8       (old value  5C F8)
----------------------------------------------------------------------
COMx=BOTTOM
-E 1237 1F          (old value 1B)
-E 1256 1F          ( "    "   1B)
note: caused junk to be written to random locations in memory.
----------------------------------------------------------------------
REMM.SYS and other expanded ram drivers                         8/4/87
-E 1AA1 83 E3 E0 38 D2 9C A0 56 0D
                    (old values 23 19 E8 C6 3A 81 B8 01 93)
-E 2366 63 81 95 43 10 AF 12 FD
                    ( "    "    47 81 FC D0 31 2E 7C 96)
note: the symptom is that the system will not work correctly with the 
driver installed, but fine without it.
----------------------------------------------------------------------
Function E074 failure                                           9/3/87
-E 6715 AB          (old value 9E)
-E 6718 30          ( "    "   CC)
note: this function fails only when using DISPLAY=LONG.
----------------------------------------------------------------------

   *4B01* patches
----------------------------------------------------------------------
Changing memory sizes                                           9/9/87
-E 0116 C7 C0       (old value CB 17)
-E 92F8 0F          ( "    "   03)
-E 92FC 63 7D       ( "    "   03 77)
-E 9300 2B E3 05 E1 EB
                    ( "    "   89 10 F3 D7 1C)
-E 9A66 17 C3 9E 20 81 37 18 A7 39 DF
                    ( "    "   A6 B1 03 F4 7D 38 DF C8 E6 03)
-E 9A70 02 10 6E 20 F7 13 47 08 07 24 12 1D
                    ( "    "   F4 66 FB B5 8E AF 03 0E 3E 83 80 47)
-E 9A7D 06 1C 7C 07 01 8E 86 37 03 0E 3E 83 08
                    ( "    "   9B 81 07 1F C1 04 06 4C 7C 07 FF FE F5)
-E 9A8C 81 13 1F C1 ( "    "   8E 6F AF DF)
-E 9A91 BF 61 BE    ( "    "   65 38 3E)
-E B50F FF BF DB    ( "    "   DF EF FB)
note: disks produced after 9/15/87 have been patched already.
----------------------------------------------------------------------