Serial Communications
                               Diagnostic Program
                                   NOISE.COM
                              Created 11-DEC-1988
                               Richard B. Johnson
                        PROGRAM EXCHANGE (719) 548-0540

          General.
          This program is meant to be executed as a "live program"
          from a BBS system and as an "external protocol" from a
          remote-user's communications program. It will display in-
          formation concerning the quality of the transmission channel
          existing between the remote user and the BBS system. It may
          be helpful in obtaining better quality service from the
          telephone company.

          Now to install this program.
          If you are a BBS system operator, you create a batch file
          containing the following information:

          REM * Noise Program Batch file *
          D:\PATH\NOISE/PORT=2/MODE=MIRROR
          |     |     |      |           |____ Execute in mirror mode
          |     |     |      |________________ COM port (1-4)
          |     |     |_______________________ Program name
          |     |_____________________________ Path to program
          |___________________________________ Drive name

          You then define this as a "live program" (DOOR) in your BBS
          system software configuration.

          If you are a remote-user, using a communications program
          like TELIX or PCPLUS, you create a batch file containing the
          following information:

          REM * Noise Program Batch file *
          D:\PATH\NOISE/PORT=2
          |     |     |      |
          |     |     |      |________________ COM port (1-4)
          |     |     |_______________________ Program name
          |     |_____________________________ Path to program
          |___________________________________ Drive name

          You then define this batch file as an "external protocol"
          DOWNLOAD utility. In TELIX, you use ALT-O to get to the cor-
          rect menu. You can use "NOISE" as the protocol name. Tell
          TELIX that you do NOT wish to be prompted for a file name.

          How to use this program.
          Find a BBS system that has this line-noise live program
          "door" installed. Execute the live program from your com-







                                     - 1 -
          




          munications program just as though you were going to execute
          any other live-program. When the BBS system advises that you
          execute your local NOISE.COM program, just hit the "down-
          load" key (PgDn for TELIX) and select "NOISE". The program
          should begin execution and keep a running tabulation of the
          amount of data sent and received, the number of bad bytes
          and the percentage error-rate.

          When you wish to exit the program, just hit control-break or
          control-C. Control-break is "cleaner" because it doesn't
          mess up your screen with a "^C" echo and cause the screen to
          be overwritten.

          You can also execute this program from the DOS command line.
          If you were executing a communications program, you could
          "shell" to DOS and execute the same command-line that you
          used within the batch file. If your program exists within
          the current path, you need not type the path and drive on
          the command line. If the communications adapter port in use
          in COM1, you need not enter anything on the command line. In
          this case, "NOISE", entered at the DOS prompt or from the
          batch file, is sufficient.

          Other usage:
          NOISE has two modes of operation. The default mode is to
          send a string of bytes to a remote location and record any
          errors in the string being echoed back. The other mode, the
          "mirror" mode, simply echoes any characters received. It
          functions as though you put a connection between pins 2 and
          3 of a RS-232C connector to immediately echo any bytes re-
          ceived on the RX line back to the TX line. The only differ-
          ence between NOISE in the "mirror" mode and a piece of wire
          is that if NOISE receives a ^C, it aborts. You can see from
          this that NOISE can be very useful in debugging local RS-
          232C connections as well as monitoring line-noise.

          NOISE.ARC contains the complete source-code and documenta-
          tion. The source code shows how to operate the UARTs used in
          IBM-compatible computers in interrupt-mode. Interrupt-mode
          operation is necessary if you intend to use these UARTs at
          speeds much in excess of 2400 baud for communications. In
          particular, the code shows how to:

          (1)   Set up the required interrupt vectors.
          (2)   Set up the UART
          (3)   Set up the interrupt controller.
          (4)   Operate both transmit and receive in interrupt-mode.
          (5)   Trap ^C and control-break so vectors may be restored.
          (6)   Restore interrupt vectors before program exit.
          (7)   Restore interrupt-controller mask program before exit.
          (8)   Restore saved UART parameters before program exit.








                                     - 2 -
          




          Restoring the machine-state before the program exits is very
          important. The major failing of many, otherwise excellent,
          home-made communications programs has been that the program
          may exit without restoring the machine state. The next time
          a program is executed, the system will crash if the machine
          state has not been correctly restored.

          If you use these routines for a tutorial, remember that it
          is seldom necessary to operate the UART in interrupt-mode
          for transmit, only for receive. Operation of the UART in
          interrupt-mode during transmit will accomplish nothing use-
          ful in a communications program since the program must wait
          until the host receives the characters, processes them, and
          sends back a response, before the interactive user sends
          more characters. Operation in interrupt-mode for receive is
          important so that no incoming characters are ever lost even
          if the user is typing at the keyboard, reading from a file,
          etc.

          How the program works.
          The program sends a string of all the ANSI characters (with
          ^C missing) to the remote computer. The remote computer
          simply echoes these characters back.

          The program then compares the characters sent with those
          received. If they are the same, the block-number and byte-
          count is updated on the screen and the cycle continues. If a
          byte is missing or garbled, the program records this fact,
          calculates a running error-rate, and then continues. The
          process continues until aborted by the user or until the
          modem carrier fails.

          If the user aborts, a string of ^C characters are sent to
          the remote computer to cause the remote program to abort
          also. In case of an abort for any reason, the machine-state
          is restored before the program terminates.

          Warranty.
          This program is supplied "as-is" with no warranty whatso-
          ever. The complete source-code is provided so the users may
          determine for themselves if the program may serve a useful
          purpose.

          - finis -















                                     - 3 -