>>> STARTING RAID <<<





     RAID is started the same way as DEBUG. Type RAID followed by 
an optional program name followed by optional arguments. The only 
difference  between RAID and DEBUG command lines is that the file 
extension must be specified.


            To run RAID enter:

                         RAID


            To debug foo.com enter:

                         RAID FOO.COM


            To debug myfile.exe with apple as an argument enter:

                         RAID MYFILE.EXE APPLE



     If  a file is found with the same name as the program to  be 
debugged  with a .SYM extension it is automatically  loaded  into 
the symbol table.


     Raid  may be loaded resident so it may be used  anytime.  To 
call  up raid after it's been loaded resident and exited use  the 
<5> key on the numeric pad without numlock.  Note:  When raid  is 
resident it keeps interrupts 0,  1,  3,  6, 8, 9, 20, 21, 22, 23, 
and 24 vectored to itself.  Avoid running programs that also trap 
these. There will also be about a 48k reduction in free ram.


            To load RAID resident enter:

                         RAID +R

            Note: A filename and arguments may follow the +r.
.pa
                           >>> Commands <<<





     Raid  commands  are  available after  typing  <F1>.  Several 
commands  that  are  commonly used are definded  as  control  and 
function  keys.  The function and control key definitions are  in 
the command summary section.

     Commands  are selected using a nested  tree  structure.  The 
escape  key will remove you from the command tree.  Or if not  in 
the  command  tree will display the function key settings on  the 
second display line.

     Once the <F1> has been depressed the first display line will 
show  a  list  of subjects.  The second line will  show  all  the 
subject's options.  To select a different subject use the  cursor 
keys  or  the space bar.  Once the subject wanted is  highlighted 
press  the return key.  If the selection is already  know  simply 
enter  the first letter of the subject.  This may go on for  many 
levels  until  a specific command is reached.  At this point  the 
second line will display a brief description of what action  will 
take place.

     Some  commands require data from the user.  In this case the 
user  will be prompted on the first line with the description  on 
the  second line of the display.  After the prompt arguments  are 
entered they must be followed by a return.  Commands that require 
multiple  arguments must have arguments seperated by a  space  or 
comma.

.pa
                         >>> WINDOWS <<<





     Raid uses windows for viewing and modifing various data. The 
windows are named BREAKPOINT, CPU, DATA, PROGRAM, STACK, SYMBOLS, 
and 6301. Only one window may be active at a time. To change from 
window to window use the <F4> key. To go directly to a window use 
the following:

          <F1> W C B     -or-      CTRL-B      for BREAKPOINT
          <F1> W C C     -or-      CTRL-C      for CPU
          <F1> W C D     -or-      CTRL-D      for DATA
          <F1> W C P     -or-      CTRL-P      for PROGRAM
          <F1> W C S     -or-      CTRL-S      for STACK
          <F1> P S L                           for SYMBOL
          <F1> W C 6     -or-      CTRL-P <F4> for 6301



     When  a  window is active the window name is highlighted  in 
reverse video. The current item in the window is also highlighted 
in  reverse video.  To change the current selected item  use  the 
cursor keys. To scroll the window a line at a time use the cursor 
keys. To scroll the window a page at a time use the PgUp and PgDn 
keys. 



     To set the window orgin address (start address of window) to 
a  desired  value enter the value followed by the <F2>  key.  The 
orgin may also be changed by the <F1> W A command.



     To change from data or text in the DATA window use the  <F3> 
key. Or to change the stack direction in the STACK window use the 
<F3> key. In all other windows <F3> will be ignored.



     To  change  data  in a window simply type the new  data  and 
press the return key.



     Raid  displays  all windows on one screen except the  symbol 
window.  The  SYMBOL window requires a screen of it's  own.  When 
viewing  the SYMBOL window as escape key will return you  to  the 
others.  The  6301 window will be available only if the  computer 
model is a KAYPRO 2000 (The Flexy).


          BREAKPOINT window:

          The  breakpoint window displays the status and  setting 
     of  the permanet breakpoints.  It also allows the setting of 
     breakpoints.  The breakpoints are numbered 0:  thru 9:.

          The  breakpoint viewed in the window may be selected  by 
     entering  the   breakpoint  number  and  pressing  <F2>   or       
     with  the <F1> W A command.  To scroll thru the  breakpoints 
     use the PgUp and PgDn or cursor keys.

          If  a 'D' follows the breakpoint number the  breakpoint 
     is disabled.  The address,  count, type and condition of the 
     breakpoint  is  also  displayed.  If the breakpoint  is  not 
     assigned then 'CLEAR' is displayed in the window. 

          The  address is displayed as segment:offset.  The count 
     is displayed as a word hex value.  Count of 1 means break on 
     the  first  time.  The type is displayed as 'Stop',  'Enable 
     #', 'Disable  #', or 'Call segment:offset'. The condition is 
     displayed as  it was entered. (Such as AX<>0).

          When  a breakpoint is encountered the BREAKPOINT window 
     will select that breakpoint.  For example if breakpoint 7 is 
     used then the window will display breakpoint 7.  Breakpoints 
     reached in a programs or breakpoint numbers used in commands 
     will cause this action.

          To set a breakpoint enter the specification followed by      
     return. (See BREAKPOINT section for more information).


.pa
          CPU window:

          The  CPU  window  displays all  machine  registers  and 
     flags.  To  change  the value position the current item over 
     the  register  or  flag  value  to  be  changed,  enter  the 
     expression to be placed and press return.

          Values  entered  in the flags must be  0  or  1.  Since 
     conditional  expressions generate these they can be used  to 
     set  flags.  For example:  AX<>CX would set a flag if AX was 
     not equal to CX,  else if they were equal the flag would  be 
     reset.  Expressions can also generate 0 or 1 and can even be 
     used to copy flags. For example: FLC&FLI would set a flag if 
     the  carry and interrupt flags were on,  else the flag would 
     be  reset.  If  values other than 0 and 1 are  attempted  an 
     error is issued.

          The  CPU  window  will not accept an orgin  address  or 
     scroll.  If  an attempt is made to move the item out of  the 
     window wraparound will occur.  Scroll keys are  ignored.  An 
     attempt to set an orgin address will result in an error.
.pa
          DATA window:

          The  DATA  window  displays  40 bytes of  memory  in  a 
     specified format and the ascii text.  If the ascii character 
     cannot be displayed then a diamond is displayed insted.  The 
     format of the data displayed defaults to bytes.  This can be 
     changed by using the following commands:


               <F1> F D A     Display data in address form.

               <F1> F D B     Display data in byte form.

               <F1> F D L     Display data in long form.

               <F1> F D W     Display data in word form.


          Data  entry  may  be done  in  hexadecimal  (addresses, 
     bytes,  long,  or words) or ascii. To change from one to the 
     other use the <F3> key.  In either mode to select an item to 
     be changed position the highlight over it. Then if using the 
     ascii mode enter the ascii characters to be stored  followed 
     by  a return.  If using the hexadecimal mode enter a list of 
     Addresses,  bytes,  long  intergers,  or words.  A  list  is 
     defined  as  one or more expressions seperated by commas  or
     spaces followed by a return.


          List examples:

               Address format: cs:145,2378,1256:76c9

               Byte format:    12,d4,'a','b',12*3,al,{si}

               Long format:    1234:5678 (Means 12345678)
                               Long  intergers must be entered  in 
                               address form.

               Word format:    1234,'sd','a',132*4,ax,[es:bx]


          As  things  in  memory  change  the  DATA  window  will      
     reflect  the  change real time.  For example  set  the  DATA      
     window  address  to  40:40 and watch  the  timer  tic.  When      
     setting the DATA window to the video display area the screen      
     will  look  very 'noisy'.  This is from the video ram  being           
     access during the trace and is normal.

          On  a  break  the  DATA window  will  show  DS:0.  When 
     specifing  a new address for the DATA window if the  segment 
     is omitted DS will be assumed.

.pa
          PROGRAM window:

          The  program window displays the  disassembled  program 
     and allows inline assembly. To change an item in the program 
     window  position  the  highlight  over  the  instruction  to 
     change.  Then enter the new assemble instruction followed by 
     a return.

          Instructions  that  are  'abnormal' will  be  shown  in 
     brown.  Instructions  that  are breakpoint will be shown  in 
     blue. Symbolic labels will be shown in red and followed by a 
     colon. An arrow preceding the address means this instruction 
     will  be executed next (Instruction Pointer).  An  asterisks 
     following the address means this is a temporary breakpoint.

          When   an   instruction  that  references   memory   is 
     highlighted the effective address and contents is  displayed 
     on the second line.

          When  the  size  of  an  operand  is  not  obvious  the 
     disassembler will use 'BYTE PTR' and 'WORD PTR' prefixs. The 
     assembler accepts these prefixs.  If the operand size is not 
     obvious and a prefix is not used 'BYTE PTR' is assumed. When 
     immediates  are  used 2 hexadecimal digits refer to  a  byte 
     while four refer to a word.

          Segment  overides  are disassembled on a seperate  line 
     and must be entered as such with the assembler.

          The   mnemonic  for  a  far  return   is   RETF.   Jump 
     instructions  are coded SHORT,  NEAR,  and FAR automatically 
     but may be overode using SHORT, NEAR, or FAR prefixes.

          String  instructions  must  specify  the  size  in  the 
     mnemonic.  MOVS cannot be used,  MOVSB for byte or MOVSW for 
     word can.

          Addresses (even symbolic ones) are always displayed  in 
     brackets.  The assembler expects this syntax.  If an address 
     is  not  placed  in  brackets it will be  interpeted  as  an 
     immediate value by the parser.

          All opcode synonyms are supported by the assembler. The 
     disassembler  however  will  chose which  one  to  use.  The 
     disassembler uses the following:  SHL,  REPNZ,  REPZ, LOOPZ, 
     LOOPNZ,  JO,  JNO,  JC,  JNC, JZ, JNZ, JBE, JA, JS, JNS, JP, 
     JNP, JL, JGE, and JLE.

          The  exchange AX with AX instruction is  assembled  and 
     disassembled  as  NOP.   Of  course  XCHG  AX,AX  will  also 
     assemble as NOP.

          Undefined  instructions  will disassemble as DB  or  DW 
     depending if 1 or 2 bytes are invalid.

          The following mnemonics are recognized by Raid:



                        >>>>>  Instructions <<<<<


               AAA       AAD       AAM       AAS       ADC
               ADD       AND       CALL      CBW       CLC
               CLD       CLI       CMC       CMP       CMPSB
               CMPSW     CWD       DAA       DAS       DEC
               DIV       ESC       HLT       IDIV      IMUL
               IN        INC       INT       INTO      IRET
               JA        JAE       JB        JBE       JC
               JCXZ      JE        JG        JGE       JL
               JLE       JMP       JNA       JNAE      JNB
               JNBE      JNC       JNE       JNL       JNLE
               JNG       JNGE      JNO       JNP       JNS
               JNZ       JO        JP        JPE       JPO
               JS        JZ        LAHF      LDS       LEA
               LES       LOCK      LODSB     LODSW     LOOPE
               LOOPNE    LOOPNZ    LOOPZ     MOV       MOVSB
               MOVSW     MUL       NEG       NOP       NOT
               OR        OUT       POP       POPF      PUSH
               PUSHF     RCL       RCR       REPE      REPNE
               REPNZ     REPZ      RET       RETF      ROL
               ROR       SAHF      SAL       SAR       SBB
               SCASB     SCASW     SHL       SHR       STC
               STD       STI       STOSB     STOSW     SUB
               TEST      WAIT      XCHG      XLAT      XOR



                      >>>>>  Segment overides <<<<<


                         CS:    DS:    ES:   SS:



                         >>>>>  Registers <<<<<


               AX, BX, CX, DX, BP, DI, SI, SP, SS, CS, DS, ES
               AH, AL, BH, BL, CH, CL, DH, DL



                          >>>>> Prefixes <<<<<


                 SHORT, NEAR, FAR, BYTE PTR, WORD PTR



               The  radix of immediate values disassembled may be 
     changed  by  the <F1> F R x commands where x refers  to  the 
     radix.   Binary,  decimal,  hexadecimal,  or  octal  may  be 
     selected. The following shows each command:

                    <F1> F R B     Display in binary

                    <F1> F R D     Display in decimal

                    <F1> F R H     Display in hexadecimal

                    <F1> F R O     Display in octal


               Symbol  types  are looked at  during  disassemble. 
     Symbols defined as byte will be disassembled (For the symbol 
     length)  as DBs.  Symbols defined as constants will  replace 
     any immediate value.  Symbol defined as labels or  addresses 
     will replace any reference or address.

               Disassemble to disk can be done using the <F1> D D 
     command.  (See Disk section).

               The CTRL-N key will set the Instruction Pointer to 
     the current selected item in the PROGRAM window.
.pa
          STACK window:

          The STACK window displays the contents of the stack and 
     allows  changes  to the stack contents.  To change  a  stack 
     value position the highlight over the item to change,  enter 
     the new value and press return.

          The stack order may be reversed by using the <F3>  key. 
     From incrementing to decrementing and vice versa.

          An arrow before the address indicates the stack pointer.

          The stack upon a program break starts at SS:SP.

          The  stack window could be used as another data  window 
     for words only but on a program break will return to a stack 
     display.  To do this use <F1> W A or <F2>, the <F3> key also 
     so the addresses are incrementing.
.pa
                       >>> EXPRESSIONS <<<






     Raid  values  may  be entered as hexadecimal  values  or  as 
expressions. Expressions contain operands and operators. Operands 
may be constants(binary, decimal, hexadecimal, or octal), machine 
register mnemonics, machine flag mnemonics, memory contents (byte 
or word),  quoted characters,  or symbols.  Operators are  unary, 
conditional, arithmetic, or logical.



     Expressions  may be evaluated by the <F1> E command followed 
by  the  expression  to evaluate.  The  expression  may  also  be 
evaluated  if followed by the <F8> key.  The evaluated expression 
is displayed on the 2nd display line in binary,  decimal,  octal, 
and hexadecimal.



     Conditional  expressions are helpful in breaking  a  program 
under  a  certain  circumstance.  For example break  if  ds:[123] 
changed, or when the carry flag goes on, ect...



     Nesting  of parenthesis may be done.  They may be nested  16 
levels   deep.   Expression  are  processed  left  to  right   so 
parenthesis are often needed. If the parenthesis mismatch then an 
error will be issued.



     Division  by  zero is not allowed.  If this occurs an  error 
will  be  issued.  If  a division by zero is done  in  a  running 
program it will be trapped by Raid and an error issued.



          Examples of expressions:

                    AX

                    SI+BX/7

                    123*(BX/3)

                    FLC|FLO=0

                    [DS:BX+SI-18]<>SYMBOL

          Unary operators:

               +         Positive
               -         Negitive  (2's complement)
               ~         Complement (1's complement)



          Conditional operators:

               =         Equal to
               <>        Not equal to
               >         Greater than
               <         Less than
               >=        Greater than or equal to / Not less than
               <=        Less than or equal to / Not greater than



          Arithmetic operators:

               +         Addition
               -         Subtraction
               *         Multiplication
               /         Division
               %         Remainer



          Logical operators:

               &         And
               |         Or
               \<        Shift left
               \>        Shift Right
               ()        Precedence



     Notes:

          Using  operator combinations many useful functions  can           
     be  derived.  Operators  may be mixed in  any  fashion.  The 
     following would be used to complete the boolean functions:


               NAND      ~(<opr1>&<opr2>)

               NOR       ~(<opr1>|<opr2>)

               EXOR      ~((<opr1>&<opr2>)|~(<opr1>|<opr2>))

               EXNOR     (<opr1>&<opr2>)|~(<opr1>|<opr2>)


          Hexadecimal constants:

               Hexadecimal constants may be entered as is without 
          a   leading zero even if the leading digit  is  between 
          'a'  and  'f'.  This can be troblesom if a  symbol  for 
          example  is named 'face'.  In this case 0face would  be 
          used  for a constant and face for the symbol.  Entering 
          long constants (double words) must be done as  entering 
          an  address.  For example 12345678 would be entered  as 
          1234:5678.



          Binary constants:

               Binary constants must be preceeded by a '^B'.  For 
          example ^B1101 would enter 0dh.



          Decimal constants:

               Decimal constants must be preceeded by a '^D'. For 
          example ^D13 would enter 0dh.



          Octal constants:

               Octal  constants must be preceeded by a '^O'.  For 
          example ^O15 would enter 0dh.



          Machine register mnemonics:

               All 16 bit registers are supported:

                    AX, BX, CX, DX, SI, DI, BP, SP

               All segments registers are supported:

                    CS, DS, ES, SS

               Control registers are supported:

                    IP and FL
                    (Instruction Pointer and FLag register)

               All 8 bit registers are supported:

                    AL, AH, BL, BH, CL, CH, DL, DH



          Machine flag mnemonics:

               FLT       Trap flag
               FLA       Aux carry flag
               FLC       Carry flag
               FLP       Parity flag
               FLS       Sign flag
               FLZ       Zero flag
               FLD       Direction flag
               FLI       Interrupt flag
               FLO       Overflow flag



          Quoted characters:

               ASCII  values may be specified in  quotes.  Single 
          quotes  may be placed in double quotes and vice  versa. 
          If  2  charaters are specifed for a word they  will  be 
          reversed (as normal) when hi/lo bytes are stored.



          Memory contents:

               The  contents of memory locations are specified by 
          placing  the  address in brakets(for  word  values)  or 
          braces(for   byte   values).   The  address   may   use 
          expressions. If the address segment is omitted then the 
          data segment value is used.

                    {1234}              ;Byte at DS:[1234]

                    {es:bx+si}          ;Byte at ES:[BX+SI]

                    [ss:34]             ;Word at SS:[34]



          Symbols:

               Symbols  are  used  as addresses  when  placed  in 
          brakets  or  braces unless the symbol is defined  as  a
          constant.  If  this  occurs then ds:  is used  for  the 
          segment  and  the constant value as  the  offset.  When 
          symbols  are used as constants and not defined as  such 
          then  the symbols offset is used.  Symbol names are not 
          restricted so care must be taken not to define a symbol 
          as a cpu register mnemonic,  ect... Also if a symbol is 
          defined  as  a hexadecimal number then a  leading  zero 
          must  be  used to distingish the two  (See  Hexadecimal 
          numbers).



          Conditional expressions:

              A condition is said to be true if it equates to not 
          zero.  When  using  conditional operators  they  return           
          zero if false or one if true.


                    FLC       True if carry flag is set

                    AX        True if AX <> 0

                    [SI]=123  True if word at ds:[si] = 0123

                    FLA|FLC   True if aux carry or carry set

                    FLA&FLC   True if aux carry and carry set



          Notes:

               Logical   operations  can  be  used  in  math   or 
          relations.

                    ((AX&8000h)=0)&FLO

               The  above  is true if AX sign bit is off and  the 
               overflow flag is set.
.pa

                          >>> BREAKPOINT <<<





     Raid  has extremly powerful breakpoint facilitys.  There are 
up  to  ten  permanent  breakpoints  and  up  to  ten   temporary 
breakpoints.  The  temporary breakpoints are used simply to  stop 
the  program at a given point.  The permanent breakpoints allow a 
user to select what condition the break should be taken and  what 
action  should be done.  Such as stop the program when the  carry 
flag is set at point cs:1245.

     Once a breakpoint is taken all the temporary breakpoints are 
removed. (That's why there called temporary).

     Once  a  permanent  breakpoint is taken it  is  disabled  so 
execution  may  continue.   Disabled  means  all  the  breakpoint 
specifications are 'remembered' but the breakpoint is not active. 

     To  enable a permanent breakpoint once disabled use the <F1> 
B E command.  To disable a permanent breakpoint use the <F1> B  D 
command.

     Temporary breakpoints are set by positioning the item in the 
program window to the instruction where the breakpoint should  be 
set.  Then  issue  a <F1> B T command or press  <F10>.  Temporary 
breakpoints are flaged in the program window by an asterisks  (*) 
following  the  address.  If a temporary breakpoint needs  to  be 
removed do the same. These commands toggle the breakpoint not set 
it.

     To  set  a  permanent  breakpoint the <F1> B  S  command  or 
selecting the BREAKPOINT window may be used.

     To clear a permanent breakpoint use the <F1> B C command. To 
clear all permanent breakpoints use the <F1> B I command.

     Permanent breakpoints may have a count specified. This means 
the breakpoint will not be active until executed count times. The 
default count is 1 (The first time).

     Permanent breakpoints may be conditional.  A condition given 
to  a breakpoint must be true for the breakpoint to  break.  (See 
conditional expressions in the expressions section).

     Permanent breakpoints have an action specified.  The default 
action  is STOP.  Other functions are ENABLE another  breakpoint, 
DISABLE another breakpoint, or CALL a user routine.

     The  user routine for permanent breakpoints should end  with 
an IRET instruction.


          <F1> Breakpoint Clear command:

          The  <F1> B C command removes a  permanent  breakpoint. 
     Breakpoints  can be disabled without removal with the <F1> B 
     D  command.  To clear(remove) all permanent breakpoints  use 
     the <F1> B I command.

          The user will be prompted:

               'Enter breakpoint number to clear:'

          The response must be a valid breakpoint number (0  thru 
     9). If not no action will occur and an error will be issued.



          <F1> Breakpoint Disable All command:

          The  <F1>  B  D A command will  disable  all  permanent 
     breakpoints.   They   will  remain  inactive  until  enabled      
     with <F1> B E command. Note: Breakpoints can also be enabled 
     by other breakpoints. Disabled breakpoints are flaged in the  
     BREAKPOINT window by a 'D' following the breakpoint number.



          <F1> Breakpoint Disable Single command:

          The  <F1>  B  D S command will  disable  one  permanent 
     breakpoint. The breakpoint will remain inactive until a <F1> 
     B  E command is issued or another breakpoint enables  it.  A 
     'D'  will  be shown in the BREAKPOINT window  following  the 
     breakpoint number to indicate it's disabled.

          The user will be prompted:

               'Enter breakpoint number to disable:'

          The  response must be a valid breakpoint number (0 thru 
     9). If not no action will occur and an error will be issued.



          <F1> Breakpoint Enable All command:

          The  <F1>  B  E  A command will  enable  all  permanent 
     breakpoints.  To  disable  a  breakpoint use the  <F1>  B  D 
     command.  To enable specific breakpoints use the <F1> B E  S 
     command.


.pa
          <F1> Breakpoint Enable Single command:

          The  <F1>  B  E  S  command  will  enable  a  permanent 
     breakpoint.   The  breakpoint  will  then  be  active  until 
     disabled by a <F1> B D command or the breakpoint is taken.

          The user will be prompted:

               'Enter breakpoint number to enable:'

          The  responce must be a valid breakpoint number (0 thru 
     9).  If  not  no action will be taken and an error  will  be 
     issued. Press return only for breakpoint 0.



          <F1> Breakpoint Initialize command:

          The  <F1>  B I command removes (clears)  all  permanent 
     breakpoints.  To disable all breakpoints insted of  clearing 
     use the <F1> B D A command.  To set breakpoints use the <F1> 
     B S command.




          <F1> Breakpoint Set command:

          The   <F1>  B  S  command  is  used  to  set  permanent 
     breakpoints.  To  disable a set breakpoint use the <F1> B  D 
     command.  To  clear  (remove) a breakpoint use the <F1> B  C 
     command.  To  set temporary breakpoints (or remove them) use 
     the <F1> B T command or the <F10> key.


          Upon entering <F1> B S the user will be prompted:

              'Enter brkpnt number [,addr [,count [,type [,cond]]]]:'


          The responce must be a valid breakpoint number (default 
     is  breakpoint  0) from 0 thru 9.  


          The address (default is highlighted address in  PROGRAM 
     window)  is  entered as segment:offset.  If the  segment  is 
     omitted then CS:  is used. If the address is does not matter 
     and  a certain condition is what is wanted use the <F1> P  T 
     command.


          The  count  (default  is 0001) is entered  as  a  word. 
     Meaning  a value from 0001h to 0ffffh.  The count refers  to 
     how  many times the address must be reached before an action 
     is taken. If zero is specified then 0001 will be used.
          The  type  (default  is Stop) is entered  as  a  single 
     character. The options are Disable, Call, Enable, and Stop.

          The  Disable  type  must be followed  by  a  breakpoint 
     number to be disabled upon break.

          The Call type must be followed by an address of a  user 
     routine to be called upon break.

          The Enable type must be followed by a breakpoint number 
     to be enabled upon break.

          The Stop type simply stops the program upon break.


          The  condition  (default is none) may be  specified  so 
     that  the  breakpoint  will  do  it's  action  only  if  the 
     specified  condition is true.  See condition expressions  in 
     the expressions sections for details.



          <F1> Breakpoint Temporary command:

          The   <F1>   B  T  command  will  toggle  a   temporary 
     breakpoint.  The current highlighted address in the  PROGRAM 
     window  will  be  toggled  set and  reset.

          If  a temporary breakpoint is set an asterisks (*)  will 
     be displayed to the right of the address.

          The <F10> key has the same function.

          When  a breakpoint  (permanent or  temporary is  taked) 
     all temporary breakpoints are reset.

          Up to ten temporary breakpoints may be set at a time.
.pa
                              >>> DISK <<<





          Raid has extensive disk commands.  Disk I/O can be done 
     using physical sectors,  logical sectors or files.

          Features  to  load  a   program   for   debugging   and 
     disassembling a file to disk are also included.


          File  specification may include full path specification 
     except for the disk disassembler.


          Sectors may be specified as relative or as head, track, 
     and sector.  Relative is refers to as logical.  Head, track, 
     and sector is a physical specification.


          Extensive  error  trapping  is used incase  of  an  I/O 
     error.  Hardware  problems  are  displayed  in  an  easy  to 
     understand  manner.  Software problems or DOS  failures  are 
     displayed in the following form:

               <error that occured> failure occured at <address>
               Interrupt xxh, function xxh
               Device: x:, Device header is at <address>

               Abort, Ignor, or Retry?

          In responce to the above:

               Abort:    Return to raid
               Ignor:    Continue with error
               Retry:    Try function again


          Use  the <F1> D G and <F1> D P commands for sector disk 
     I/O.   These   commands  use  logical  or  physical   sector 
     numbering.


          For file I/O use the <F1> D N command to specify a file 
     and <F1> D R to read and <F1> D W to write it.


          To load a(nother) program for debugging use the <F1>  D 
     L command.


          To disassemble a file to disk use the <F1> D D command.
          <F1> Disk Disassemble command:


          The  <F1> D D command disassembles a program to a  disk 
     file.


          If  symbols  are  defined  they  will be  used  in  the 
     disassemble.


          See  program window in the windows sections  for   more      
     details on the disassembler.


          The user will be prompted:

               'Enter filename.ext [,starting address [,count]]:'

          Enter  a file specification for the output to be named. 
     Paths are not accepted.

          The  starting address (default is CS:IP) is  where  the 
     disassemble   will   start.   The  address  is  entered   as 
     segment:offset.  If the segment is omitted then CS:  will be 
     used.

          The count is entered as a word from 1 to 0ffffh. If the 
     count is omitted then the count will default to the size  of 
     the last file loaded for debugging.

          It  is possible for a few more bytes to be disassembled 
     than specified. If the byte count is reached mid-instruction 
     then the count will go over because that instruction will be 
     completly disassembled.


               (Example output)
.pa
          <F1> Disk Get Logical command:
          
          The  <F1> D G L command will read one or  more  sectors 
     from  the disk into memory.


          For  disk editing sectors can be read in,  edited using 
     the  DATA  window,  and  wrote back using the  <F1>  D  P  L 
     command.


          If specifing head,  track, and sector is more desirable 
     use the <F1> D G P command.


          The user will be prompted:

               'Enter address, sector, count, drive:'

          The  address  is  entered  as  segment:offset.  If  the 
     segment is not specified then DS: is used.

          The sector is a 'relative sector' number.  Meaning that 
     all sectors on the disk are numbered sequential. For example 
     physical  sector:  track  0,  sector 1,  head 0 is  relative 
     sector: sector 0.

          The count is a word that refers to how many sectors are 
     to be sequentially read into memory.

          The  drive is entered as a single character  optionally 
     followed by a colon refering to the drive name. For example: 
     A:.



          <F1> Disk Get Physical command:

          The  <F1>  D G P command will read one or more  sectors 
     from the disk into memory.


          This  command  is identical to the <F1> D G  L  command 
     except that sectors are specified by head, track, and sector 
     rather that relative sectors.


          The user will be prompted:

          'Enter address, head, track, sector, count, drive:'

          The syntax is the same as the <F1> D G L command except 
     the head and track values must be entered.


          <F1> Disk Load command:

          The  <F1>  D L command load a file for  debugging.


          If a .SYM file is found in the same path with the  same 
     filename  then  it is loaded into the symbol table.  If  the 
     .SYM file is not a RAID .SYM file it may cause problems.  To 
     remove an invalid .SYM file use the <F1> P S I command.


          Path and drive specifications are valid.


          Extentions (Even if .COM or .EXE) must be specified.


          .EXE  files are detected by a valid .EXE format not the 
     extention name itself.


          The  size  of the file is saved for the  default  count 
     when using the <F1> D W command.


          The  file specification is saved for the  default  name 
     used  for  the <F1> D R and <F1> D W commands.  This can  be 
     changed with the <F1> D N command.


          Window pointers are set  to:  BREAKPOINT=0,  DATA=DS:0, 
     PROGRAM=CS:IP, and STACK=SS:SP.


          For .COM files IP=0100h,  SP=0FFFEh, CS=DS=ES=SS, and 0 
     is pushed on the stack.


          For  .EXE files all values are passed from the  linker. 
     Ones  that  are not are computed so the .EXE file  will  run 
     properly  under  raid.  All relocation is taken care  of  as 
     well.


          A program segment prefix is always built.


          The user will be prompted:

               'Enter file specification to load:'

          A  file  specification (paths may be included) must  be 
     entered.  If  the file is not found or an error  occurs  the 
     user will be informed.

          <F1> Disk Name command:

          The  <F1>  D  N  command  is used  to  specify  a  file 
     specification  to  be used with the <F1> D R and  <F1>  D  W 
     commands.

          Full  path specification may be used or a device  name. 
     For example: lpt1

          If the file is not found it is created.



          <F1> Disk Put Logical command:

          The  <F1> D P L command will write one or more  sectors 
     from memory to disk.

          USE EXTREME CAUTION USING THIS COMMAND ANY PLACE ON THE 
     DISK MAY BE DESTROYED IF THE USER WRITES IN THE WORNG PLACE!

          The user will be prompted:

               'Enter address, sector, count, drive:'

          The  address  is  entered  as  segment:offset.  If  the 
     segment is omitted then DS: is assumed.

          The sector is a relative sector number. (See <F1> D G L 
     command for the definition of a relitive sector).

          The count refers to a word that specifies the number of 
     sectors to be written.

          The  drive is entered as a single character  optionally 
     followed by a colon refering to the drive name. For example: 
     A:.



          <F1> Disk Put Physical command:

          The  <F1> D P P command will write one or more  sectors 
     from the disk into memory.

          The  command  is  identical to the <F1> D P  L  command 
     except that sectors are specified as head, track, and sector 
     rather than relative sectors.

          The user will be prompted:

          'Enter address, head, track, sector, count, drive:'

          The syntax is the same as the <F1> D P L command except 
     the head and track values must be entered.
          <F1> Disk Read command:

          The  <F1> D R command reads data into memory from a DOS 
     file.

          The file specification to read must have been specified 
     using the <F1> D N command.  If no previous <F1> D N command 
     has  issued  then  the name of last read or loaded  file  is 
     used. If no file has been loaded or read then 'RAIDFILE.COM' 
     is used.  Device input is doe if a device was specified with      
     the <F1> D N command.

          The user is prompted:

               'Enter address [, count [,offset]]:'

          The  address  is  entered  as  segment:offset.  If  the 
     segment is omitted then CS: is assumed.

          The  count is a word that refers to how many bytes  are 
     to be read.  If the count is not specified then the file  is 
     completly read.

          The  offset is a word that refers to the starting  byte 
     number to be read. The default is 0 (begining of file).



          <F1> Disk Write command:

          The  <F1> D W command writes data from memory to a DOS 
     file.

          The file specification to write must have been specified 
     using the <F1> D N command.  If no previous <F1> D N command 
     has  issued  then  the name of last read or loaded  file  is 
     used. If no file has been loaded or read then 'RAIDFILE.COM' 
     is used.  Device output is done if a device was specified in 
     the <F1> D N command.

          The user is prompted:

               'Enter address [, count [,offset]]:'

          The  address  is  entered  as  segment:offset.  If  the 
     segment is omitted then CS: is assumed.

          The  count is a word that refers to how many bytes  are 
     to be write. If a count is not specified then the numbers of 
     bytes last read or loaded is used. If no file has previously 
     been  loaded  or read and no count is specified then a  file 
     with length of 0 will be written.

          The  offset is a word that refers to the starting  byte 
     number to be written. The default is 0 (begining of file).
                            >>> EVALUATE <<<





          Raid   has   a   built  in  facility   for   evaluating 
     expressions.

          Enter  an expression followed by the <F8> key  and  the 
     result will be displayed.


          <F1> Evalute command:

          The <F1> E command is used to evaluate expressions.

          The user will be prompted:

               'Enter expression to evaluate:'

          The  expression  then  must be entered  followed  by  a 
     return.


          The   result   is   displayed   in   binary,   decimal, 
     hexadecimal, and octal.

          For more information see the expressions section.
.pa
                           >>> FORMAT <<<




          Raid  has  several formats available for ease  in  use. 


          Formats  are  divided into Data and Radix  types.


          The  Data types effect the data window display  format. 
     The  data in the window can be shown  as  addresses,  bytes, 
     long  intergers,  or  words.

               Forms:    Address   7856:3412
                         Byte      12 34 56 78
                         Long      78563412
                         Word      3412 7856


          The  Radix  types  effect the  disassembler  output  of 
     immediate  operands.  Immediate operands can be displayed in 
     binary, decimal, hexadecimal, or octal.



          <F1> Format Data Address command:

          The  <F1> F D A command changes the data window  format 
     to display and accept data in address form.



          <F1> Format Data Byte command:

          The  <F1> F D B command changes the data window  format 
     to display and accept data in byte form.



          <F1> Format Data Long command:

          The  <F1> F D L command changes the data window  format 
     to  display  and  accept data in long  interger  form.  Data 
     must be entered as addresses under this format.



          <F1> Format Data Word command:

          The  <F1> F D W command changes the data window  format 
     to display and accept data in word form.


          <F1> Format Radix Binary command:

          The  <F1>  F  R B command  causes the  disassembler  to 
     display immediate operands in binary.  Note:  Due to leading 
     zero  supression size of operand must be determined by bytes 
     disassembled.



          <F1> Format Radix Decimal command:

          The  <F1>  F  R D command causes  the  disassembler  to 
     display immediate operands in decimal.  Note: Due to leading 
     zero  supression size of operand must be determined by bytes 
     disassembled.



          <F1> Format Radix Hexadecimal command:

          The  <F1>  F  R H command causes  the  disassembler  to 
     display immediate operands in hexadecimal.  Byte values will 
     be  displayed as two digits and words will be  displayed  as 
     four digits.



          <F1> Format Radix Octal command:

          The  <F1>  F  R O command causes  the  disassembler  to 
     display immediate operands in octal.  Note:  Due to  leading 
     zero  supression size of operand must be determined by bytes 
     disassembled.
.pa
                              >>> IO <<<





          Raid  allows the user to input from and output to any 8 
     or  16  bit port.  

          Raid  also  allow  a user to input from  and  output  a 
     device.  To do device I/O specify a device (LPT1,  COM2,...) 
     with  the  <F1> D N command.  To output to a device then use 
     the <F1> D W command.  To input from a device use the <F1> D 
     R command. Note: NO colon follows the device name!



          <F1> Io Input command:

          The  <F1>  I I command allows a user to  read  16  bits 
     ports.  Is a count is  specified  the starting port  address 
     is  displayed followed by the port contents and the contents 
     of  every  successive  port  address  for  the  count.   The 
     information will be displayed on the display line.

          The user will be prompted:

               'Enter I/O port address, optional count:'

          The  I/O  port address is a hardware I/O  port  address 
     between 0 and 0ffffh.

          The  optional  count defaults to 1.  If  the  specified 
     count is too large to fit on the display line the data  will 
     be truncated.



          <F1> Io Out command:

          The  <F1>  I  O  command  writes  words  to  successive 
     addresses. Or of course a word to an address.

          The user will be prompted:

               'Enter I/O port address, word list:'

          The  I/O  port address is a hardware I/O  port  address 
     between 0 and 0ffffh.

          The word list is the data to be output to the port(s).

               Example:
                       27,34c7        ;port 27=34c7
                       38,1234,565d   ;port 38=1234, port 3a=565d
          <F1> Io Read command:

          The  <F1>  I R command allows a user to  read  8  bits 
     ports.  Is a count is  specified  the starting port  address 
     is  displayed followed by the port contents and the contents 
     of  every  successive  port  address  for  the  count.   The 
     information will be displayed on the display line.

          The user will be prompted:

               'Enter I/O port address, optional count:'

          The  I/O  port address is a hardware I/O  port  address 
     between 0 and 0ffffh.

          The  optional  count defaults to 1.  If  the  specified 
     count is too large to fit on the display line the data  will 
     be truncated.



          <F1> Io Write command:

          The  <F1>  I  W  command  writes  bytes  to  successive 
     addresses. Or of course a byte to an address.

          The user will be prompted:

               'Enter I/O port address, byte list:'

          The  I/O  port address is a hardware I/O  port  address 
     between 0 and 0ffffh.

          The byte list is the data to be output to the port(s).

               Example:

                       27,34      ;port 27=34
                       38,12,56   ;port 38=12, port 39=56


.pa
                          >>> MEMORY <<<




          Raid  has  facilitys for dealing directly with  memory. 
     The features include clearing a portion of memory (<F1> M  C 
     command),  finding  a pattern in memory (<F1> M F  command), 
     moving  a  block of data in memory (<F1> M M  command),  and 
     setting a pattern in memory (<F1> M S command).



          <F1> Memory Clear command:

          The <F1> M C command clears a range of memory. Starting 
     at  a specfied address all bytes are set to 0 for the  count 
     specified.

          The user is prompted:

             'Enter starting address, number of bytes to clear:'

          The starting address is the byte to be cleared.

          The number of bytes to clear is just that.

               Example:
                         100,100 would clear 100h thru 1FFh



          <F1> Memory Find command:

          The  <F1>  M  F command finds a specific byte  or  byte 
     pattern in memory.

          The user is prompted:

               'Enter starting address, count, data byte(s):'

          The  starting address specifies the first  location  to 
     look for the pattern.

          The count is how many successive locations to search.

          The  data bytes is a byte list refering to the  pattern 
     to be found.

               Example:
                         100,1000,'t','e','s','t',0d,0a

                         Searches   for  'test'  followed  by   a 
                         carriage  return-line  feed starting  at 
                         address 100h for 1000h bytes.
          <F1> Memory Move command:

          The  <F1> M M command copies a block of data  from  one 
     section  of memory to another.  Care must be taken that  the 
     blocks  do  not overlap unless a repeated pattern is  to  be 
     stored. If that is the case use the <F1> M S command.

          The user will be prompted:

          'Enter source address, count, destionation address:'

          The  source address is specified as segment:offset.  If 
     the segment is omitted it will default to DS:.

          The count is the number of bytes to be copied.

          The    destionation    address    is    specified    as 
     segment:offset.  If  the  segment is  omitted  then  DS:  is 
     assumed.

               Example:
                         1000,3cb,4500
                    3cbh bytes will be copied from 1000h to 4500h.



          <F1> Memory Set command:

          The  <F1>  M  S  command  sets a  range  of  memory  to 
     specified byte pattern.

          The user will be prompted:

               'Enter starting address, count, data byte(s):'

          The  starting address specifies what address  to  start 
     placing   the   specified   pattern.   It  is   entered   as 
     segment:offset.  If  the  segment is ommitted  then  DS:  is 
     assumed.

          The count specifies how many times the pattern is to be      
       stored.

          The  data byte(s) refers to a byte list that  specifies 
     the pattern to be stored.
.pa
                         >>> PROGRAM <<<




          Raid  has  various  way of  executing  a  program.  The 
     program  can  be started at a specified address (<F1> P  G). 
     The program can be (re)started at the current CS:IP (<F1>  P 
     R). The program can be traced instruction at a time or until 
     a specified condition has occured (<F1> P T). Or the program 
     can  be proceeded thru (<F1> P P).  Proceeding is just  like 
     tracing except CALLs, INTerrupt, LOOPs, ect are not traced.

          There  is also a facility  for entering  arguments to  a 
     program to use as if they were entered on the command line.

          There  is  a  symbol submenu for  manipulating  program 
     symbols.



          <F1> Program Arguments command:

          The <F1> P A command is used to enter a command line to 
     the program.  This line should be entered as arguments  that 
     would  normally follow the program name.  Program  arguments 
     may  be specified after the program name to load in the raid 
     command line.

          The command line is placed at DS:0080.  and FCBs 5C and 
     6C are set.

          The user will be prompted:

               'Enter command line:'

          The  command  line  should be  entered  followed  by  a 
     return.



          <F1> Program Go command:

          The  <F1>  P G command starts a program executing at  a 
     specfied address.

          The user will be prompted:

               'Enter starting address:'

          The starting address refers to where program  execution 
     is to begin.  The address is specified as segment:offset. If 
     the segement is omitted then CS: is assumed
.pa
          <F1> Program Proceed command:

          The   <F1>  P  P  command  will  trace  a  program  one 
     instruction at a time.  The difference from this and tracing 
     is  that  certain  intructions  are  skipped.   This  avoids 
     stepping  thru a loop several times or thru a call  that  is 
     known to work.

          The following instructions are skipped:

                    CALL
                    INT
                    LOOP
                    LOOPNZ / LOOPNE
                    LOOPZ / LOOPE
                    REP (and following intruction)
                    REPZ / REPE (and following instruction)

          The <F6> key has the same function as <F1> P P.



          <F1> Program Restart command:

          The  <F1>  P  R  command restarts the  program  at  the 
     current instruction pointer (CS:IP). When a program is first 
     loaded  this  command  can be used to execute  it  from  the 
     starting address.

          The <F7> key has the same function as <F1> P R.



          <F1> Program Symbol Add command:

          The  <F1>  P S A command adds a symbol  to  the  symbol 
     table.  Once  a  symbol is added it will be honored  by  the 
     disassembler and may be used in expressions.

          If  the symbol already exist it will be replaced by the 
     new values entered.

          The user will be prompted:

               'Enter symbol name, address [,type [,size]]:'

          The  symbol  name  is  any character string  (Up  to  9 
     characters). Note: all characters are valid except ',' and a 
     space.

          The  address  is  entered  as  segment:offset.  If  the 
     segment is omitted then CS: is assumed.

          The  type is an optional single character  refering  to 
     what type of symbol is to be defined.  The default is Label. 
          Symbol types:

               B    For byte DB
               C    For constant EQU
               L    For label x:
               T    For text DB 'x'
               W    For word DW

               Note:  The  disassembler takes types into  account 
                      for a more acurate disassemble.


          The  size is a word that refers to how long the  symbol 
     field is.

               Examples:

                    FOO,CS:1234         ;Label FOO: at CS:1234

                    APPLE,27,B,10       ;APPLE at CS:27 is data
                                        ;in bytes for 10 bytes



          <F1> Program Symbol Initialize command:

          The  <F1>  P S I command initializes the symbol  table. 
     All symbols are erased.



          <F1> Program Symbol List command:

          The <F1> P S L command displays the symbol table. To do 
     this  the normal raid windows will be replaced by  a  symbol 
     window. The escape key will bring them back.

          Symbols are displayed in alphabetic order.

          The  PgDn  and  PgUp  keys may be used  to  scroll  the 
     window.  The  display can be positioned to the first  symbol 
     starting with a specified letter by typing the letter.

          If  more  than 23 symbols are defined the  symbols  are 
     displayed in two columns.

               Display example:

                    FOOBAR    1EC5:023B Label
                    FOODATA   1EC5:43CB Byte  Length=12
.pa
          <F1> Program Symbol Read command:

          The  <F1>  P  S R command reads a .SYM  file  into  the 
     symbol table.  The .SYM file must have been created with the 
     <F1> P S W commands or the MAP2SYM utility.

          Any  existing  symbols  in  the symbol  table  will  be 
     detroyed when the symbol file is loaded.

               The user will be prompted:

                    'Enter file name:'

               A   file  name  must  be  specified.   Full   path 
     specification  may be used.  A symbol file does not have  to 
     have a .SYM extension so extension must be specified even if 
     it's .SYM.

               If  a  .SYM file exist with the same name  as  the 
     program loaded for debugging it is automatically loaded into 
     the symbol table.



          <F1> Program Symbol Write command:

          The  <F1>  P S W command write the symbol  table  to  a 
     file.  The specified extension should be .SYM so the symbols 
     will  automatically be loaded in future debugging  sessions. 
     The  symbol  file  can  be reloaded using the  <F1>  P  S  R 
     command.

          The user will be prompted:

               'Enter file name:'

          A file name must be specified.  Full path specification 
     may be used.

          If the file already exist it will be overwritten.
.pa
          <F1> Program Symbol Trace command:

          The <F1> P S T command traces a program one instruction 
     at  a  time.  It  can also execute  a  specified  number  of 
     instructions   before  breaking  execution.   Optionally   a 
     condition may be specified to break execution on.

          The <F5> key will trace one instruction at a time.

          When  the <F5> key is used and the screen is in  update 
     mode there may be a flicker.  The screen will flicker if the 
     instruction to be executed could possibly effect the screen. 
     If not no flicker will occur.

          When  a  condition is specified you have an  option  of 
     'watching  the  program run'.  To do this put the screen  in 
     nonupdate mode.  All program output will overwrite the  raid 
     screen.  When  command  mode is resumed press the  <F9>  key 
     twice if the display needs to be restored.

          When a program is being traced the escape key will stop 
     program tracing.

          When tracing for a condition the screen update flag can 
     be toggled using the <F9> key. This is NOT advised.

          The screen mode (update/nonupdate) can be set using the 
     <F1> S U and <F1> S N commands respectivly.


          The user will be prompted:

               'Enter number of instructions to execute [,cond]:'

          If  just return is pressed one instruction is exectued. 
     The   <F5>  key  is  recommended  for   single   instruction 
     execution.

          The  number of instructions to execute is just that.  A 
     word from 0 to 0ffffh may be specified.

          The cond is what condition the program is stop at. If a 
     conditional trace feature is needed use for example: CX<>CX.
     This  condition will never occur so only the count  will  be 
     valid but conditional features may be used.  For information 
     on  condition see conditional expressions in the expressions 
     section.
.pa
                            >>> QUIT <<<





          When  leaving raid all memory is freed,  all  interrupt 
     vectors   are  restored,   and  the  application  screen  is 
     restored.

          If  raid was invoked with a '+r' option then all memory 
     will  be  freed  except for what raid  needs  and  interrupt 
     vectors are NOT restored.


          <F1> Quit No command:

          The <F1> Q N command cancels the exit of raid to DOS in 
     case the user really does not want to exit.



          <F1> Quit Yes command:

          The <F1> Q Y command exit from raid to DOS.
.pa
                         >>> SCREEN <<<





          Raid  keeps  the application screen seperate  from  its 
     own.  If  two screens are available raid can run on one  and 
     the  application  program on the other.  If using  only  one 
     screen   it   will  be  shared  by  multiplexing  raid   and 
     application screens. There is also a faciltiy for saving the 
     application screen as a BLOAD (BASIC command) file.



          <F1> Screen Application command:

          The <F1> S A command displays the application screen to 
     return  to the raid screen press any  key.  The  application 
     will  be updated as the program runs if the screen update is 
     on (<F1> S U).

          The <F9> key has the same function.



          <F1> Screen Color command:

          The  <F1>  S  C  command forces raid  to  use  a  color 
     display.



          <F1> Screen Monochrome command:

          The  <F1> S M command forces raid to use  a  monochrome 
     display.



          <F1> Screen Nonupdate command:

          The  <F1> S N command causes raid not to keep track  of 
     screen  changes made by the program currently running.  This 
     is useful for the <F1> P T command or if raid is for example 
     using the color display and the application the monochrome.



          <F1> Screen Save command:

          The  <F1> S S command writes the application screen  to 
     disk in a format so it can be load from BASIC with the BLOAD      
     command.

          <F1> Screen Update command:

          The  <F1> S U command causes raid to keep track of  the 
     changes  made  to  the application  screen.  During  tracing 
     instructions  that could effect the screen there will  be  a 
     short  flicker.  To view the application screen use the <F9> 
     key or the <F1> S A command.
.pa
                           >>> TRACE <<<





          Raid  has a facility for tracing  interrupts.  Normally 
     interrupts are not traced. With the trace facility ranges of 
     interrupts may be set to trace. Interrupts 0, 1, 3, 6, 8, 9, 
     and 20 cannot be traced because raid takes these over.  When 
     tracing interrupt 21 (DOS call) there will be an extra  step 
     checking  for an exit function.  After this interrupt 21  is 
     vanilla.



          <F1> Trace Clear command:

          The  <F1> T C command disables an interrupt or range of 
     interrupts to trace.

               The user will be prompted:

                    'Enter low INT range [, high INT range]:'

               In  response  the  user may  enter  a  hexadecimal 
          number of an interrupt not to trace,  or two values may 
          be  entered to specify a range of interrupts not to  be 
          traced.



          <F1> Trace Disable command:

          The  <F1> T D command disables all  interrupt  tracing. 
     The is raids default.  To trace a particular interrupt range 
     use  the <F1> T S command.  To enable all interrupt  tracing 
     use the <F1> T E command.



          <F1> Trace Enable command:

          The  <F1>  T E command enables all  interrupt  tracing. 
     Except of course the ones that cannot be traced.  To disable 
     a  certain interrupt or range of interrupts use the <F1> T C 
     command.  To disable all interrupt tracing use the <F1> T  D 
     command.
.pa
          <F1> Trace Set command:

          The  <F1>  T S command enable an interrupt or range  of 
     interrupts to trace.

               The user will be prompted:

                    'Enter low INT range [, high INT range]:'

               A  hexadecimal value may be entered to  enable  an 
     interrupt.  Two values may be specified to enable a range of 
     interrupts.  Interrupts specified that are not allowed to be 
     traced  will be ignored.  If for example '2,5' were  entered 
     interrupts 2,  4, and 5 would be enabled. Not 3 because raid 
     uses it for breakpoints.
.pa
                         >>> WINDOW <<<





          Information  on windows is in the windows chapter.  The 
     following are descriptions of the window commands.



          <F1> Window Address command:

          The  <F1>  W A command sets the orgin  address  of  the 
     current window.  An address entered followed by the <F2> key 
     has the same effect.

               The user will be prompted:

                    'Enter address:'

               In  the  DATA,  PROGRAM,  and STACK  windows  full 
          memory  address  may be specified.  If the  segment  is 
          omitted DS, CS, and SS are used respectivly.

               In  the BREAKPOINT window a breakpoint number must 
          be specified.

               In  the  CPU window this command issues  an  error 
          message.



          <F1> Window Change Breakpoint command:

          The  <F1>  W  C B command makes the  BREAKPOINT  window 
     active. CTRL-B has the same effect. For more information see 
     the breakpoint window section in the windows chapter.



          <F1> Window Change Cpu command:

          The  <F1>  W C C command makes the CPU  window  active. 
     CTRL-C  has  the effect.  For more information see  the  cpu 
     window section in the windows chapter.



          <F1> Window Change Data command:

          The  <F1> W C D command makes the DATA  window  active. 
     CTRL-D  has  the same effect.  For more information see  the 
     data window section in the windows chapter.

          <F1> Window Change Program command:

          The <F1> W C P command makes the PROGRAM window active. 
     CTRL-P  has the same effect.  For more information  see  the 
     program window section in the windows chapter.



          <F1> Window Change Stack command:

          The  <F1> W C S command makes the STACK window  active. 
     CTRL-S  has  the same effect.  For more information see  the 
     stack window section in the windows chapter.



          <F1> Window Exchange command:

          The  <F1> W E command will change from  hexadecimal  to 
     text  mode in the DATA window.  In the STACK window it  will 
     reverse  the  direction.   In  other  windows  this  has  no 
     function. The <F3> key has the same effect.
.pa
                      >>> SUMMARY OF COMMANDS <<<





     Command                       Description
     =======                       ===========

     Breakpoint Clear              Clear a breakpoint

     Breakpoint Disable All        Disable all breakpoints

     Breakpoint Disable Single     Disable a breakpoint

     Breakpoint Enable All         Enable all breakpoints

     Breakpoint Enable Single      Enable a single breakpoint

     Breakpoint Initialize         Clear all breakpoints

     Breakpoint Set                Set a breakpoint

     Breakpoint Temporary          Toggle temporary breakpoint

     Disk Disassemble              Disassemble program to a file

     Disk Get Logical              Read a logical sector

     Disk Get Physical             Read a physical sector

     Disk Load                     Load a program for debugging

     Disk Name                     Specify a file name

     Disk Put Logical              Write a logical sector

     Disk Put Physical             Write a physical sector

     Disk Read                     Read a file

     Disk Write                    Write a file

     Evaluate                      Evaluate an expression

     Format Data Address           Data in address format

     Format Data Byte              Data in byte format

     Format Data Long              Data in long format

     Format Data Word              Data in word format

     Format Radix Binary           Display operands in binary

     Format Radix Decimal          Display operands in decimal

     Format Radix Hexadecimal      Display operands in hex

     Format Radix Octal            Display operands in octal

     I/o In                        Read word(s) from port(s)

     I/o Out                       Write word(s) to port(s)

     I/o Read                      Read byte(s) from port(s)

     I/o Write                     Write byte(s) to port(s)

     Memory Clear                  Clear range of memory

     Memory Find                   Find pattern in memory

     Memory Move                   Copy a memory block

     Memory Set                    Place a pattern in memory

     Program Arguments             Enter command line

     Program Go                    Execute start at an address

     Program Proceed               Trace, skipping loops

     Program Restart               Continue execution

     Program Symbol Add            Add a symbol to the table

     Program Symbol Initialize     Clear symbol table

     Program Symbol List           Display symbol table

     Program Symbol Read           Read symbol table from disk

     Program Symbol Write          Write symbol table to disk

     Program Trace                 Execute a single instruction

     Quit No                       Cancel quit command

     Quit Yes                      Exit from raid to DOS

     Screen Application            Display application screen

     Screen Color                  Use color display

     Screen Monochrome             Use monochrome display

     Screen Nonupdate              No application screen update

     Screen Save                   Save user screen to a file
     Screen Update                 Update application screen

     Trace Clear                   Disable range of interrupt
                                   tracing

     Trace Disable                 Disable all interrupt tracing

     Trace Enable                  Enable all interrupt tracing

     Trace Set                     Set range of interrupt tracing

     Window Address                Set orgin address of window

     Window Change Breakpoint      Select breakpoint window

     Window Change Cpu             Select cpu window

     Window Change Data            Select data window

     Window Change Program         Select program window

     Window Change Stack           Select stack window

     Window Exchange               Select other window function

     <ESC>                         Display funtion key setting or
                                   exit from command tree.

     <F1>                          Issue a command

     <F2>                          Set window address

     <F3>                          Window exchange

     <F4>                          Change window

     <F5>                          Execute single intruction

     <F6>                          Trace, skipping loops

     <F7>                          Continue execution

     <F8>                          Evaluate expression

     <F9>                          Show application screen

     <F10>                         Toggle temporary breakpoint

     CTRL-B                        Select breakpoint window

     CTRL-C                        Select cpu window

     CTRL-D                        Select data window

     CTRL-E                        Display last error message
     CTRL-N                        Set IP to current item address

     CTRL-P                        Select program window

     CTRL-S                        Select stack window

     <5> on pad (no numlock)       Break program execution

.pa
                         >>> MESSAGES <<<





          ? Access denied

                    This  is a DOS error meaning the wanted  file 
               cannot be accessed.


          ? Attempt to divide by zero

                    An  expression was entered that attempted  to 
               divide  by zero.  For example if BX=0 and SI/BX is 
               entered as an expession.


          Bad FAT image

                    A bad File Allocation Table was detected on a 
               disk.


          Bad req strc len

                    A bad request structure length was specified.


          ? Bad sector - CRC failed

                    The  CRC for a sector was wrong.  This  means 
               the data in the sector is not valid.


          *** BREAKPOINT x ***

                    This message is issued when raid is restarted 
               after  a program breakpoint is reached.  The x  is 
               replaced  by  the breakpoint number or  ?  if  the 
               breakpoint reached was not defined by raid.


          Bytes read from disk = x

                    After  a disk read this message displays  the 
               number of bytes read in hexadecimal.


          Cannot find pattern in memory

                    When  using the <F1> M F command the  pattern 
               was not found.

          ? Cannot set breakpoint

                    A  breakpoint was attempted to be set in  ROM 
               or  non-existent memory.  This error can  also  be 
               caused by faulty memory.


          ? Cannot use register twice in address

                    An  attempt  to assemble a  memory  reference 
               that  used  an index register twice.  This can  be 
               done  in expressions but not assembled  since  the 
               8086 processor does not support this.


          Character device error

                    A   ROM   error   occured  when   trying   to 
               communicate to a character device. (lpt, com,...).


          ? Close failed - dir entry lost

                    A  DOS error occured when trying to  close  a 
               file.  If  this  occurs the file written will  not 
               contain any new information.


          >>> Condition true: x <<<

                    A waited for condition occured.  This will be 
               displayed when tracing a program till a condition.


          ? Condition truncated - Too big

                    The   condition   entered   was   too   long. 
               Conditional  breakpoint conditions are limited  to 
               15 characters.


          ? CPU flags must be 0 or 1 only

                    An  attempt was made to enter a  value  other 
               than 0 or 1 in a CPU flag field.


          ? CPU window has no address

                    An  attempt was made to set the orgin address 
               of the CPU window which has no addresses.

.pa
          Data error

                    The  ROM  detected a data error  while  doing 
               I/O.


          ? Disk controller failed

                    The ROM detected a disk controller failure.


          ? Disk is write protected

                    An attempt to write on a write protected disk 
               was made.


          ? Disk seek failed

                    A seek error occured while reading or writing 
               a disk sector.


          ? Disk timed out

                    The disk prematurly timed out.


          ? Divide overflow, Interrupt 0

                    The  8086  processor attempted to  divide  by 
               zero or a divide overflow occured.


          Drive not ready

                    The drive is not ready to be used.  The  door 
               is not closed, ect...


          ? File not found

                    The  specified  file  was not  found  in  the 
               directory.


          Found pattern at location: xxxx:xxxx

                    The  <F1> M F command found the pattern.  The 
               program window's address is set to the location.

.pa
          ? Free disk space exhasted

                    All free space on the disk has been used.  In 
               other words the disk is full.


          ? Garbage after expression

                    An  expression entered was valid  except  for 
               'junk' entered after it.


          ? General disk I/O failure

                    A  ROM  error  that means the last  disk  I/O 
               failed.


          General error

                    A ROM error that means the last I/O failed.


          ? Immediate value out of range

                    An immediate value was specified that was out 
               of  range.  Example:  MOV AL,3000 will cause  this 
               error  because the largest number AL can  hold  is 
               0FFh.


          ? Insufficient free memory

                    This  message  is  issued when there  is  not 
               enough RAM to load a program.


          ? Invalid address list

                    The   entered   address  list   contains   an 
               improperly formatted entry.


          ? Invalid breakpoint number

                    A  breakpoint number was specified  that  was 
               not valid. Valid breakpoint numbers are 0 thru 9.


          ? Invalid breakpoint type

                    A  breakpoint  type was specified other  that 
               Call, Disable, Enable, or Stop.


          ? Invalid byte list

                    The entered byte list contains an  improperly 
               formatted entry or an entry that exceeds 0ffh.


          ? Invalid doubleword list

                    The   entered  doubleword  list  contains  an 
               improperly formatted entry.


          ? Invalid op code

                    An  unrecognized op code was attempted to  be 
               assembled.


          ? Invalid operand specified

                    The  operand  specified for the  op  code  is 
               invalid.   Note:   8087/80287  op  codes  are  not 
               supported,   they   must  be  entered  as   escape 
               sequences.


          ? Invalid path

                    The  path  specified in a file  specification 
               was not found.


          ? Invalid symbol type

                    A  symbol  type other  than  Byte,  Constant, 
               Label, Text, or Word was specified.


          ? Invalid word list

                    The entered word list contains an  improperly 
               formatted entry.


          *** Manual break from keyboard ***

                    The <5> key without numlock was pressed while 
               a  program  was  running.  Doing  this  interrupts 
               program execution.

.pa
          ? Missing closing brace }

                    An  opening  brace was encountered without  a 
               closing brace.


          ? Missing closing bracket ]

                    An opening bracket was encountered without  a           
               closing bracket.


          ? Missing closing parenthesis )

                    An  opening parenthesis was encounted without 
               a closing parenthesis.


          ? Missing closing quote

                    A  literal  was  entered  without  a  closing 
               quote.


          ? Missing operand

                    The  op  code to be assembled  required  more 
               operands then were specified.


          ? No directory space available

                    The  directory is full and can hold  no  more 
               file entrys.


          Out of paper

                    The printer is out of paper.


          >>> Please wait for disk access(es) <<<

                    Raid is accessing disk.


          >>> Please wait for memory access(es) <<<

                    Raid is accessing RAM.


          * PROGRAM ABORT - Fatal error *

                    A fatal DOS error was encounter and the Abort           
               option was entered.
          * Program loaded *

                    The   specified   program  was   successfully 
               loaded.


          * Program terminated normally *

                    The program terminated with a normal exit.


          Raid vx.x at your service...

                    Raid and optional files are loaded and  ready 
               for use.


          Read fault

                    ROM detected a read fault.


          ? Relative address out of range

                    A  relative address was entered that was  out 
               of the -128 to +128 byte range.


          ? Sector not found

                    The  specified sector does not exist or could 
               not be found.


          Seek error

                    The  ROM  detected a disk  seek  error  while 
               trying to read or write a sector.


          ? Symbol table empty

                    An attempt was made to display a non-existant           
               symbol table.


          ? Symbol table full

                    The symbol table is full and can hold no more           
               entries.

.pa
          ? Syntax error

                    A general syntax occured. This happens when a           
               sequence is expected to be entered and is not.


          *** TEMPORARY BREAKPOINT ***

                    This  is displayed when the program breaks on 
               a temporary breakpoint.


          ? Too many temporary breakpoints

                    An  attempt was made to define more than  ten           
               temporary breakpoints.


          *** TRACE ***

                    This means the program broke after  executing 
               a trace.


          ? Undefined OPcode, Interrupt 6

                    The  80286  attempted to execute  an  invalid           
               instruction.


          Unknown command

                    ROM returned an unknown command error.


          Unknown media

                    ROM returned an unknown media error.


          Unknown unit

                    ROM returned an unknown unit error.


          Write fault

                    ROM returned a write fault error.


          Write protected

                    ROM returned a write protect error meaning an  
               attempt  was  made to write on a  write  protected 
               disk.