SETDIR   Use to restore the current directory

SETDIR sets the environment string 'CURDIR' with the current directory. Once 
this has been done it is very simple to restore the current directory after it 
has been changed. To restore the current directory, simply issue the following 
command: 
  
                  CD %CURDIR%

This technique has distinct advantages over other techniques that create files
(i.e. CD >CURDIR.FIL) or modify the interupt vector (PUSHDIR/POPDIR from PC 
magazine and PC OUTLINE). It is much faster, creates no files, cannot be 
impacted by programs that modify the interrupt vector, and requires only 
one very small program.

If you desire setting another environment variable, use the following:

                 SETDIR
                 SET name=%CURDIR%

Note that due to limitations in DOS, the errorlevel can be 0 even if
SETDIR fails due to lack of environment space. Errorlevels 1 and 2
are for SETDIR errors. Errorlevel=1 means the DOS release is not at least 2. 
Errorlevel=2 means that the directory string was too long to return.