Dear Above Board PS/PC User:

This diskette contains an alternate program for setting and 
loading the Above Board PS/PC clock, ABCLOCK.  

Above Board user Dr. E. Michael Perdue developed ABCLOCK and 
placed it in the public domain.  ABCLOCK is useful in situations 
where the Intel CLOCK.SYS device driver does not work.  For 
example, ABCLOCK allows fractional second time increments from 
the system clock.  Some graphics programs, keyboard utilities, 
and data acquisition software requires fractional seconds.

USING ABCLOCK WITH THE INTEL ABOVE BOARD PS/PC:
1. Remove CLOCK.SYS from the config.sys file.
   {ABCLOCK will not work if the Intel CLOCK.SYS device driver is 
   loaded.}  

2. Copy the file ABCLOCK.COM from this diskette to your system 
   disk root directory.

3. Add the command ABCLOCK to your autoexec.bat file

SETTING THE DATE AND TIME WITH ABCLOCK: 
Enter the following command from the DOS prompt

ABCLOCK /TIME=HH:MM:SS/DATE=MM-DD-YY

This sets the date and time on the Above Board clock.  It is also 
possible to set only the time or date by using just one parameter 
on the command line.

Because ABCLOCK was developed outside Intel, we do not cover it 
with our product warranty.   Our thanks to Dr. Perdue for 
creating this program and allowing us to distribute it.

ABCLOCK (c) 1986 by E. M. Perdue  
Clock Utility for Intel Above Board PS/PC    All rights reserved

Dr. E. Michael Purdue 
School of Geophysical Sciences  
Georgia Institute of Technology, 
Atlanta, GA  30332