DISK.EXE
         
         
         
                                      ver 1.1 
         
         This software is a help to perform some of the calculations
         described in a book:
         
                      ROARK'S FORMULAS FOR STRESS AND STRAINS
                     by  Warren C. Young, Mc Graw Hill, 6th ed.
         
         It is not my purpose to reproduce the book, or even to make any
         comment.
         I just want to put in the user's hands a program which will
         perform the rather intricate calculations involved in a
         particular paragraph of a particular chapter. That is, chapter
         10, table 24, and not all of that table is dealt with.
         I don't think it is safe to use the program, without the book,
         and I strongly advise against.
         
         2 Remarks
         
         I will not be considered as responsible for any damage arising
         from either errors in the book, or even in the program, as no
         program can really be bug free. It is up to the user to make his
         own verifications. There are many reasonable ways to do it.
         It is up to the user to convince himself that the formulas are
         applicable, and that he may safely neglect for instance, shear
         stresses (see book: paragraph 10.3).
         The formulas are given without too many explanations as to where
         they come from, and as to their limitations. I am not going to
         improve on this, but may I point out that the disk should "look"
         like a disk? Comparing the formulas and the results will readily
         show that the hole should be a real hole, that the disk should
         not be too thick, etc
         It is intentionally that I don't give more precise warnings. Some
         are quoted in the book, some are not. It is obvious, that the
         corrections for shear not being implemented, the zone of
         applicability of these corrections should be considered as a zone
         of limited validity for the main formulas (and for this program).
         
         I know that all fire of inferno will in time punish those who did
         not implement the Horner's scheme whenever possible. I tried: in
         this case, it does not bring any speed advantage. But it
         certainly makes the listing unreadable. I choose inferno.
         
         3 Verifications
         
         Table 23 has been used in a small program built from a copy of
         the block of functions used to generate them in the actual
         program, to be certain that both blocks are identical. No copy of


DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                      1




         





         this document is available, as it was considered as an auxiliary
         comparison.
         On the right hand part of table 24, under the heading "special
         cases" there is a simplified set of equations. I have put into a
         spreadsheet (Quattro) the relations given for case 1 (a to l), 2
         (a to l) and then some more in cases 3,  5. Cases higher than 5
         are not treated.
         A hundred of these verifications have been performed.
         Case 2, a,b,c have been compared to results given by case 2 of
         the program, the rest has been treated with program case 3.
         The sketch appears correctly on an EGA screen. It works on a VGA
         screen and should work correctly on CGA and on screens for which
         Borland provided a driver, as no absolute coordinate has been
         used, and all drivers loaded.
         
         4 Description
         
         Copy the program on a working diskette, or on the hard disk.
         Then, when the DOS prompt appears (A:> or C:>, possibly with some
         more information), type disk and return.
         You are requested to feed in the metallurgical and geometrical
         properties.
         Most tests have been performed with:
         Modulus of elasticity E=1.1E7
         Poisson's ratio nu=.3
         Outer radius a=20
         Inner radius b= sequence of 2-6-10-14-18
         Thickness t=1
         
































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                      2




         





         
         Load q or w=10, M=100.
         Then, you are given a choice between three load options, and no
         more.
         Option 1 will implement case nø1, with precisely the formulas used
         by the author of the book. The ring is divided in 50 elementary
         rings to build arrays for deflections, moments etc.
         Case 2 is similar to case 2 of the book, but has been treated
         another way:
         The load is converted in an equivalent array of equal linear
         loads, acting on 20 elementary rings, starting at r0 (same
         convention as the book). Solving the problem  boils down to
         iterating 20 times the solution given for case 1.
         Case 3 is designed as case 2, except that you feed each
         individual load value (as a local pressure, the program performs
         the conversion in linear loads). You may feed in a moment, but
         not precisely at the edge, by making it equivalent to two opposed
         linear forces. By using large forces, you may simulate a moment
         at the edge reasonably well. But it is left to you to convert the
         linear force into pressure, remembering that the ring between r0
         and a will be divided into 20 parts.
         Of course, that double iteration is going to take some time.
         At that stage, you are left with a screen full of informations:
         the same as those described in the book (the last load is the
         value of q in the book). You will get a calculation note by
         making a hard copy of the screen.
         Pressing any key will bring you a sketch, which will be helpful
         in finding input mistakes. This kind of information is
         incorporated in more general notes, coming from a word processor.
         Usually, you get with the word processor a "capture" software,
         which is the best way if you want a copy of the graphic screen.
         
         5 Restraints
         
         Some conditions are imposed to the inner and outer edges of the
         ring. They fall under categories a to l. It is left to the user
         to take care of the compatibility of these with the load (a
         vertical load right at a support may give erroneous results,
         because the method used may move the load slightly off, or worse,
         an error "division by zero" in the graphic part of the program).
         
         case: Outer edge:             Inner edge:
                                       
         
         a     simply supported        free
                                       
         
         b     simply supported        guided
                                       
         
         c     simply supported        simply supported
                                       
         
         d     simply supported        fixed
                                       
         
         e     fixed                   free
                                       
         
         f     fixed                   guided
                                       
         
         g     fixed                   simply supported
                                       
         











DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                      3




         





         h     fixed                   fixed
                                       
         
         i     guided                  simply supported
                                       
         
         j     guided                  fixed
                                       
         
         k     free                    simply supported
                                       
         
         l     free                    fixed
                                       
         
         6 Units
         
         No consideration has been given to units. Therefore, all is well
         if and only if a consistent system is used: SI may take you into
         uneasy situations: E in Pascal gives terrific figures. If you are
         considering a manometer diaphragm, the diameter and thickness may
         have to be fed in meters!.
         
         7 Funny figures
         
         You will often see very small and funny figures appear where you
         would expect a zero. Although doubles have been used, the method
         leads to piling up small errors. It is very easy to set up a
         procedure which brings down to zero any small enough value before
         sending it to the output. But I rather left them, so that you
         have an idea of what went on. I also think that if these values
         are not at least three orders of magnitude smaller than the non
         nil values, there is a problem somewhere.
         





































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                      4




         





         
         
         8 Compiling.
         
         The program is compiled with Borland Turbo C++ compiler, huge
         model, 8086 set, simulated coprocessor if none present. The whole
         thing has been compressed with PKLITE, well known compression
         software.
         All the work has been done on an IBM AT 286 computer, with a
         coprocessor, 1 Mo memory (actually, no extended or expanded
         memory is used while running).
         
         9 Registration
         
         May I call it registration ? My address is:
         
                                     R.Hirschel
                                16, Avenue Boffrand
                                    54000 NANCY
                                       France
         
         Send 20 $ (checks only please). Although there is nothing in it
         to be proud of, I am giving the listing of the program (disk.c).
         If, for some reason you want a 360 ko 5"1/4 diskette (formatted
         with PcTools 6) with a new copy of the software, and an output of
         the Quattro verification (in .wkq or wq1 format) please send an
         additional 10$ (that will just cover expenses). The graphic
         screen will be free of my reference. I do not have a 3" drive.
         
         10 Developments
         
         If you are more than a few to encourage, I could implement a unit
         conversion routine. I can also do the same kind of job for the
         rest of table 24, and possibly some other parts of the book. I
         could also put the number of individual loads at the customer
         disposal. Up to now, I have thought that 20 was accurate enough,
         and more would be boring to enter.
         
         11 Revisions
         
         Revisions are numbered according to an "x.y" system:
         Variations in y denotes minor modifications: changes in displays,
         for instance. A new y does not give different calculated values.
         Variations in x denotes more fundamental corrections: bugs fixed,
         change in scope (cases added), new edition of the book taken into
         consideration...
         
         First revision 1.0 March 4th 1991.
         Second revision 1.1 Aug 27 Th 1991 Addition of listing and
         verifications to the doc, recompiling with Borland C++.
         
         12 Screen copies
         
                                                                                        
                               ROARK'S FORMULAS FOR STRESS AND STRAINS                  





DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                      5




         





                           by Warren C. Young, Mc Graw Hill editor, 6th ed              
                                  Table 24, program disk, ver 1.0                       
                                                                                        
                                  case nø: 3 -- restraints case:a                       
          E= 1.10e+07       nu= 0.30                                                    
          a= 2.00e+01  b= 1.00e+01 t=5.00e-01                                           
                                                                                        
                   Mt        Mr         Q            y         theta                    
          a     +2.41e+02  -1.51e-15  -3.69e+01  -1.46e-18   +4.20e-02                  
          b     +5.23e+02  +0.00e+00  +0.00e+00  -4.34e-01   +4.57e-02                  
                                                                                        
           Maximum Moment    =+5.23e+02, Minimum moment    =-1.67e-15                   
           Maximum deflection=+4.97e-18, Minimum deflection=-4.34e-01
         















































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                      6




         





                    
         
         
         
         13 Listing
         
          #include <graphics.h>
          #include <stdio.h>
          #include <conio.h>
          #include <math.h>
          #include <string.h>
          #include <stdlib.h>
          #include <ctype.h>
         
         #define max(a,b)    (a>b) ? a:b
         #define min(a,b)    (a<b) ? a:b
         
         double
         w,dr,r0,rr0,a,b,t,E,nu,D,ya,yb,Qa,Qb,Mmr,Mra,Mrb,th,thetaa,thetab
         ;
         double
         maxload,minload,maxy,miny,maxMr,minMr,maxMt,minMt,maxM,minM,maxQ,
         minQ;
         double C1,C2,C3,C4,C5,C6,C7,C8,C9; double L3,L6,L9;
         double G3,G6,G9;
         double F1,F2,F3,F4,F5,F6,F7,F8,F9;
         double rr[51];
         double def[51],Mr[51],Mt[51],Q[51],theta[51];
         double r[21],ww[21];
         double x1,y1;
         
         char cas,name[4];
         int n,aa,bb,load_case,RR,xx,yy;
         
         void auxil_calc_draw2(void);
         void comp (void);
         void csa(void);void csb(void);void csc(void);void csd(void);void
         cse(void); void csf(void);void csg(void);void csh(void);void
         csi(void);void csj(void); void csk(void);void csl(void);
         void draw(void);
         void drawload(void);
         void drawLefty(double,double,double *u);
         void drawLeftQ(double,double,double *u);
         void drawRightMt(double,double,double *u);
         void drawRightMr(double,double,double *u);
         void drawdisk(int);
         void drawax(int,int);
         













DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                      7




         





         
         double Ff1 (double x ,double y ,double z); double Ff2 (double y,
         double z);
         double Ff3 (double y, double z); double Ff4 (double x, double y,
         double z);
         double Ff5 (double y, double z); double Ff6 (double y, double z);
         double Ff7 (double x, double y, double z); double Ff8 (double x,
         double y, double z);
         double Ff9 (double x, double y, double z);
         void metallurgy (void);
         void geometry (void);
         void initial(int,int);
         void load_case1(void); void load_case2(void); void
         load_case3(void);
         void load(void);
         void out(void);
         void print(void);
         void restraints (void);
         void restrain(void);
         int  scalex (double); int scaley (double,double);
         void setgraph (void);
         
           13.1 main ()
         
           {
           clrscr();
           printf("\n                     ROARK'S FORMULAS FOR STRESS AND
           STRAINS"); printf("\n                  by Warren C. Young, Mc
           Graw Hill editor, 6th ed");
           printf("\n                         Table 24, program disk, ver
           1.1"); printf("\n");
           metallurgy();
           geometry();
           load();
           restrain();
           comp ();
           out();
           }
         
           13.2 void auxil_calc_draw2()
         
           {
           char val[40];
           int x1,y1;
           xx=getmaxx();
           yy=getmaxy();
           aa=xx/2;
           bb=.025*yy;
           initial(aa,bb);
           drawax(aa,yy);
           drawdisk(yy);
           strcpy(name," Mr");
           drawRightMr(maxM,minM,Mr);
  
         






DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                      8




         





           strcpy(name," Mt");
           drawRightMt(maxM,minM,Mt);
           strcpy(name,"  y");
           drawLefty(maxy,miny,def);
           drawload();
           x1=.207*xx;
           y1=.8*yy;
           sprintf (val," Mra       = %+2.2le",Mr[50]);
           outtextxy(x1,y1,val);
           x1+=textwidth(val);
           sprintf (val,"   Mrb       = %+2.2le",Mr[0]);
           outtextxy(x1,y1,val);
           y1+=textheight(val);
           x1=.207*xx;
           sprintf (val," maximum M = %+2.2le",maxM);
           outtextxy(x1,y1,val);
           x1+=textwidth(val);
           sprintf (val,"   minimum M = %2.2le",minM);
         










































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                      9




         





         
           outtextxy(x1,y1,val);
           x1=.207*xx;
           y1+=textheight(val);
           sprintf (val," sigma maxi= %+2.2le",6.0*maxM/t/t);
           outtextxy(x1,y1,val);
           x1+=textwidth(val);
           sprintf (val,"   sigma mini= %+2.2le",6.0*minM/t/t);
           outtextxy (x1,y1,val);
           y1+=textheight(val);
           x1=.207*xx;
           sprintf(val," y maxi    = %+2.2le", maxy);
           outtextxy(x1,y1,val);
           x1+=textwidth(val);
           sprintf(val,"   y mini    = %+2.2le", miny);
           outtextxy(x1,y1,val);
           x1=.5*xx; 
           y1=.95*yy;
           settextstyle(0,0,1);
           setusercharsize(3,5,2,5);
           sprintf(val,"Robert Hirschel, disk.exe ver 1.0");
           outtextxy(x1,y1,val);
           settextstyle(0,0,1);
            getch();
           closegraph();
           }
         
           13.3 void comp(void)
         
           {
           int i,j;
           for (j=0;j<n;j++)
             {
             w=ww[j];
             r0=r[j];
             L3=Ff3(r0,a);
             L6=Ff6(r0,a);
             L9=Ff9(nu,r0,a);
             restraints();
             for  (i=0;i<=50;i++)
               {
               RR=(rr[i]>r0);
               G3=Ff3(r0,rr[i])*RR;
               G6=Ff6(r0,rr[i])*RR;
               G9=Ff9(nu,r0,rr[i])*RR;
               F1=Ff1(nu,b,rr[i]);
               F2=Ff2(b,rr[i]);
               F3=Ff3(b,rr[i]);
               F4=Ff4(nu,b,rr[i]);
               F5=Ff5(b,rr[i]);
               F6=Ff6(b,rr[i]);
               F7=Ff7(nu,b,rr[i]);
  
         







DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     10




         





               F8=Ff8(nu,b,rr[i]);
               F9=Ff9(nu,b,rr[i]);
           
           def[i]+=yb+thetab*F1*rr[i]+Mrb*rr[i]*rr[i]/D*F2+pow(rr[i],3)/D*
           (Qb*F3-w*G3);
           maxy=max(def[i],maxy);miny=min(def[i],miny);
           th=thetab*F4+Mrb*rr[i]/D*F5+rr[i]*rr[i]/D*(Qb*F6-w*G6);
           theta[i]+=th;
           Mmr=thetab*D/rr[i]*F7+Mrb*F8+Qb*rr[i]*F9-w*rr[i]*G9;
           Mr[i]+=Mmr;
           maxMr=max(Mr[i],maxMr); minMr=min(Mr[i],minMr);
         

















































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     11




         





         
           Mt[i]+=th*D*(1-nu*nu)/rr[i]+nu*Mmr;
           maxMt=max(Mt[i],maxMt); minMt=min(Mt[i],minMt);
           Q[i]+=Qb*b/rr[i]-w*r0/rr[i]*RR;
           maxQ=max(Q[i],maxQ); minQ=min(Q[i],minQ);
               }
             }
            maxM=max(maxMt,maxMr);   minM=min(minMt,minMr);
            }
         
           13.4 /* Values at the edges. */
         
              13.4.1  void csa(void) 
         
              {
              Mrb=0.0;Qb=0.0;ya=0.0;Mra=0.0;
                   yb=-w*a*a*a/D*(C1*L9/C7-L3);
                   thetaa=w*a*a/D*(C4*L9/C7-L6);
                   thetab=w*a*a/D/C7*L9;
                   Qa=-w*r0/a;
               }
         
              13.4.2 void csb(void)
         
              {
              thetab=0.0;Qb=0.0;ya=0.0;Mra=0.0;
                   yb=-w*a*a*a/D*(C2*L9/C8-L3);
                   thetaa=w*a*a/D*(C5*L9/C8-L6);
                   Mrb=w*a/C8*L9;
                   Qa=-w*r0/a;
               }
         
              13.4.3  void csc(void)
         
               {
              yb=0.0;Mrb=0.0;ya=0.0;Mra=0.0;
                   thetab=-w*a*a/D*(C3*L9-C9*L3)/(C1*C9-C3*C7);
                   Qb=w*(C1*L9-C7*L3)/(C1*C9-C3*C7);
                   thetaa=thetab*C4+(Qb*C6-w*L6)*a*a/D;
                   Qa=Qb*b/a-w*r0/a;
               }
         
              13.4.4  void csd(void)
         
               {
              yb=0.0;thetab=0.0;ya=0.0;Mra=0.0;
                   Mrb=-w*a*(C3*L9-C9*L3)/(C2*C9-C3*C8);
                   Qb=w*(C2*L9-C8*L3)/(C2*C9-C3*C8);
                   thetaa=Mrb*a/D*C5+Qb*a*a/D*C6-w*a*a/D*L6;
                   Qa=Qb*b/a-w*r0/a;
               }
         
              13.4.5  void cse(void)
         
               {
     
         




DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     12




         





              Mrb=0.0;Qb=0.0;ya=0.0;thetaa=0.0;
                   yb=-w*a*a*a/D*(C1*L6/C4-L3);
                   thetab=w*a*a/D*L6/C4;
                   Mra=-w*a*(L9-C7*L6/C4);
                   Qa=-w*r0/a;
               }
         
              13.4.6  void csf(void)
         
               {
              thetab=0.0;Qb=0.0;ya=0.0;thetaa=0.0;
                   yb=-w*a*a*a/D*(C2*L6/C5-L3);
                   Mra=-w*a*(L9-C8*L6/C5);
                   Mrb=w*a*L6/C5;
                   Qa=-w*r0/a;
               }
         
              13.4.7  void csg(void)
         
               {
              yb=0.0;Mrb=0.0;ya=0.0;thetaa=0.0;
                   thetab=-w*a*a/D*(C3*L6-C6*L3)/(C1*C6-C3*C4);
                   Qb=w*(C1*L6-C4*L3)/(C1*C6-C3*C4);
                   Mra=thetab*D/a*C7+Qb*a*C9-w*a*L9;
                   Qa=Qb*b/a-w*r0/a;
               }
         
              13.4.8  void csh(void)
         
               {
              yb=0.0;thetab=0.0;ya=0.0;thetaa=0.0;
                   Mrb=-w*a*(C3*L6-C6*L3)/(C2*C6-C3*C5);
                   Qb=w*(C2*L6-C5*L3)/(C2*C6-C3*C5);
                   Mra=Mrb*C8+Qb*a*C9-w*a*L9;
                   Qa=Qb*b/a-w*r0/a;
               }
         
              13.4.9  void csi(void)
         
               {
              yb=0.0;Mrb=0.0;thetaa=0.0;Qa=0.0;
                   ya=-w*a*a*a/D*(C1/C4*(r0*C6/b-L6)-r0*C3/b+L3);
                   thetab=-w*a*a/D/C4*(r0*C6/b-L6);
                   Mra=w*a*(C7/C4*(L6-r0*C6/b)+r0*C9/b-L9);
                   Qb=w*r0/b;
               }
         
              13.4.10  void csj(void)
         
               {
              yb=0.0;thetab=0.0;thetaa=0.0;Qa=0.0;
                   ya=-w*a*a*a/D*(C2/C5*(r0*C6/b-L6)-r0*C3/b+L3);
                   Mra=w*a*(C8/C5*(L6-r0*C6/b)+r0*C9/b-L9);
     
         






DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     13




         





                   Mrb=-w*a/C5*(r0*C6/b-L6);
                   Qb=w*r0/b;
               }
         
              13.4.11  void csk(void)
         
               {
              yb=0.0;Mrb=0.0;Mra=0.0;Qa=0.0;
                   ya=-w*a*a*a/D*(C1/C7*(r0*C9/b-L9)-r0*C3/b+L3);
                   thetaa=-w*a*a/D*(C4/C7*(r0*C9/b-L9)-r0*C6/b+L6);
                   thetab=-w*a*a/D/C7*(r0*C9/b-L9);
                   Qb=w*r0/b;
               }
         















































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     14




         





         
         
              13.4.12  void csl(void)
         
               {
              yb=0.0;thetab=0.0;Mra=0.0;Qa=0.0;
                   ya=-w*a*a*a/D*(C2/C8*(r0*C9/b-L9)-r0*C3/b+L3);
                   thetaa=-w*a*a/D*(C5/C8*(r0*C9/b-L9)-r0*C6/b+L6);
                   Mrb=-w*a/C8*(r0*C9/b-L9);
                   Qb=w*r0/b;
               }
         
           13.5  void drawax(int,int)       /* Draws a vertical axis of
           symetry */
         
           {
           int s;
           setlinestyle(4,20462,1);
           s=gety()*2.5;
           line(aa,s,aa,yy*.7);
           setlinestyle(0,1,1);
           }
         
           13.6  void drawdisk(int)              /* Draws the disk */
         
           {
           setfillstyle(3,7);
           bar3d(scalex(-a),yy/2+t*xx/a/2,scalex(-b),yy/2-t*xx/a/2,0,0);
           bar3d(scalex(b),yy/2+t*xx/a/2,scalex(a),yy/2-t*xx/2/a,0,0);
           line (scalex(-b),yy/2-t*xx/a/2,scalex(b),yy/2-t*xx/a/2);
           line (scalex(-b),yy/2+t*xx/a/2,scalex(b),yy/2+t*xx/a/2);
           setlinestyle(4,20462,1);
           line(0,yy/2,xx,yy/2);
           setlinestyle(0,1,1);
           }
         
           13.7  void drawload()
         
           {
           int i;
            maxload=fabs(maxload-minload);
             for (i=0;i<=n;i++)
               {
               moveto(scalex(-r[i]),yy/2);
               linerel(0,-ww[i]*50/maxload);
               if (i==0)
                  { 
                  linerel(.02*xx,-.05*yy);
                  outtext(" load");
                  }
               }
            }
         
           13.8  void drawLefty (double maxYY,double minYY,double *u)
  
         





DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     15




         





           /*prints diagram on graphic screen*/
         
           {                                           /* left side y  */
           int i;
           double dif;
           settextjustify(0,0);
           moveto(scalex(-rr[0]),yy/2);
           dif=max(fabs(maxYY),fabs(minYY));
           for (i=0;i<=50;i++)
              {
              lineto(scalex(-rr[i]),scaley(dif,*u++));
         

















































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     16




         





         
              if (i==30)
                 {
                 moveto (.10*xx,.25*yy);
                 outtext(" y");
                 }
              }
           lineto(scalex(-rr[50]),yy/2);
           settextjustify(0,0);
           }
         
           13.9  void drawRightMr (double maxYY,double minYY,double *u)/*
           prints diagrams on graphic screen */
         
            {                                            /* right side Mr
           */
           int i;
           double dif;
           settextjustify(0,0);
           moveto(scalex(rr[0]),yy/2);
           dif=max(fabs(maxYY),fabs(minYY));
           for (i=0;i<=50;i++)
              {
              lineto(scalex(rr[i]),scaley(dif,*u++));
              if (i==10)
                 {
                 moveto(.6*xx,.25*yy);
                 outtext (" Mr");
                 }
              }
            lineto(scalex(rr[50]),yy/2);
           }
         
           13.10  void drawRightMt (double maxYY,double minYY, double
           *u)/* prints diagrams on graphic screen */
         
            {                                            /* right side Mt
           */
           int i;
           double dif;
           settextjustify(0,0);
           moveto(scalex(rr[0]),yy/2);
           dif=max(fabs(maxYY),fabs(minYY));
           for (i=0;i<=50;i++)
              {
              lineto(scalex(rr[i]),scaley(dif,*u++));
              if (i==30)
                 {
                 moveto(.9*xx,.25*yy);
                 outtext(" Mt");
                 }
              }
            lineto(scalex(rr[50]),yy/2);
  
         






DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     17




         





           }
         
           13.11 /* F,C,L,G Functions generation. */
         
              13.11.1  double Ff1 (double x,double y,double z)
         
               {
              return((1.0+x)/2.0*y/z*log(z/y)+(1.0-x)/4.0*(z/y-y/z));
               }
         



















































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     18




         





         
         
              13.11.2  double Ff2 (double y, double z)
         
               {
              return(.25*(1.0-y/z*y/z*(1.0+2.0*log(z/y))));
               }
         
              13.11.3  double Ff3 (double y, double z)
         
               {
              return(.25*y/z*((y/z*y/z+1.0)*log(z/y)+y/z*y/z-1));
               }
         
              13.11.4  double Ff4 (double x, double y, double z)
         
               {
              return(0.5*((1.0+x)*y/z+(1.0-x)*z/y));
               }
         
              13.11.5  double Ff5 (double y, double z)
         
               {
              return(0.5*(1.0-y/z*y/z));
               }
         
              13.11.6  double Ff6 (double y, double z)
         
              {
              return(y/z/4.0*(y/z*y/z-1.0+2.0*log(z/y)));
               }
         
              13.11.7  double Ff7 (double x,double y, double z)
         
               {
              return(0.5*(1.0-x*x)*(z/y-y/z));
               }
         
              13.11.8  double Ff8 (double x, double y, double z)
         
               {
              return(0.5*(1.0+x+(1.0-x)*y/z*y/z));
               }
         
              13.11.9  double Ff9 (double x, double y, double z)
         
               {
              return(y/z*((1.0+x)/2.0*log(z/y)+(1.0-x)/4.0*(1.0-y/z*y/z)))
              ;
               }
         
           13.12  void  geometry()            /* Enter geometric
           characteristics */
         
           {
           int i;
  
         



DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     19




         





           printf("\n Outer radius: ");
           scanf("%lf", &a);
           printf(" Inner radius for annular plate: ");
           scanf("%lf",&b);
           printf(" Plate thickness: ");
           scanf("%lf", &t);
           if ((a<=0)||(b<0)||(t<=0))
               {
               printf("\n   Inacceptable values for a,b,t \n");
               geometry();
               }
            if (a<b)
         
















































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     20




         





         
               {
               printf("\n   a must be greater than b, \n");
               geometry();
               }
            D=E*t*t*t/12.0/(1.0-nu*nu);
            C1=Ff1(nu,b,a);
            C2=Ff2(b,a);
            C3=Ff3(b,a);
            C4=Ff4(nu,b,a);
            C5=Ff5(b,a);
            C6=Ff6(b,a);
            C7=Ff7(nu,b,a);
            C8=Ff8(nu,b,a);
            C9=Ff9(nu,b,a);
            for (i=0;i<=50;i++)
              {
              rr[i]=b+i*(a-b)/50;      /* define the step size */
              }
           }
         
           13.13  void initial(int aa,int bb)     /* Prints title on
           graphic screen */
         
           {
           char string1[20];
           strcpy(string1,"Table 24, case:");
           setpalette (0,BLUE);
           settextstyle (0,0,1);
           moveto(aa,bb);
           settextjustify(CENTER_TEXT,TOP_TEXT);
           outtextxy(aa,bb,"Roark's Formulas for stress and strains, by
           W.C. Young");
           moveto(aa,bb+textheight("R")+10);
           outtextxy(aa,bb+textheight("R")+10,"Mc Graw Hill, 6th
           edition");
           strcat(string1,&cas);
           outtextxy(aa,bb+2*textheight("R")+20,string1);
           settextjustify(0,0);
            }
         
           13.14  void load(void)
         
           {
           char ch[1];
           printf("\n Load case number: ");
           ch[0]=getche();
           load_case=atoi(ch);
           if (!((load_case==1)||(load_case==2)||(load_case==3)))
               {
               printf("\n There are only 3 possible
           cases:1,2,3,default=3");
               load_case=3;
  
         






DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     21




         





               }
           printf("\n Radial location of unit line loading or start of
           distributed load:");
           scanf("%lf",&rr0);
           if ((rr0<b)||(rr0>a))
              {
              printf("\n Abnormal value for r0");
              load();
              }
            switch(load_case)
                  {
                  case 1:load_case1();break;
                  case 2:load_case2();break;
                  case 3:load_case3();break;
         














































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     22




         





         
                  default:load();
                  }
           }
         
           13.15 /* Load cases */
         
              13.15.1  void load_case1(void)
         
              {
              double load;
              printf(" Load value (w):");
              scanf("%lf",&load);
              n=1;
              r[0]=rr0;
              ww[0]=load;
              maxload=load;
              minload=0.0;
              }
         
              13.15.2  void load_case2(void)
         
              {
              int i;
              double load;
              n=20;             /* n points :limits of intervals */
              printf(" Load value (q):");
              scanf("%lf",&load);
              dr=(a-rr0)/n;
              for (i=0;i<n;i++)/*|_v__|_v__|_v__|_v__| n intervals=n
              loads=n+1 points*/
                  {
                  r[i]=rr0+dr/2+i*dr;
                  ww[i]=dr*load;
                  }
              maxload=load; minload=0.0;
              }
         
              13.15.3  void load_case3(void) /*Divide the loaded area in
              20 zones, ask for the local equivalent load */
         
              {
              int i;
              double load;
              n=20;
              dr=(a-rr0)/n;
              r[0]=rr0+dr/2;
              printf(" Local linear load w at radius r0= : %3.2lf :
              ",r[0]);
              scanf("%lf",&load);
              ww[0]=load*dr;
              maxload=max(maxload,load);
              minload=min(minload,load);
              for (i=1;i<n;i++)
     
         





DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     23




         





                {
                r[i]=rr0+dr/2+i*dr;
                printf("                                     %3.2lf :
              ",r[i]);
                scanf("%lf",&load);
                ww[i]=load*dr;
                maxload=max(maxload,load);
                minload=min(minload,load);
                }
              }
         


















































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     24




         





         
         
           13.16  void  metallurgy()                 /* Enter E and nu */
         
           {
           printf("\n Poisson's ratio: ");
           scanf("%lf", &nu);
           printf(" Modulus of elasticity (in pressure units): ");
           scanf("%lf", &E);
           if ((nu<0)||(nu>.7)||(E<=0))
              {
              printf(" nu <0 or >.7, or negative value for E\n");
              metallurgy();
              }
            }
         
           13.17  void out( )             /* subroutine for i/o */
         
           {
           print();
           setgraph();
           auxil_calc_draw2();
           }
         
           13.18  void print()           /* prints a small calculation
           note */
         
           {
           clrscr();
           printf("\n                     ROARK'S FORMULAS FOR STRESS AND
           STRAINS");
           printf("\n                  by Warren C. Young, Mc Graw Hill
           editor, 6th ed");
           printf("\n                         Table 24, program disk, ver
           1.1");
           printf("\n");
           printf("\n                         case nø: %d -- restraints
           case: %c",load_case,cas);
           printf("\n E= %2.2le       nu= %2.2lf",E,nu);
           printf("\n a= %2.2le  b= %2.2le t=%2.2le",a,b,t);
           printf("\n");
           printf("\n          Mt        Mr         Q            y           é
           ");
           printf("\n a     %-+#2.2e  %-+#2.2le  %-+#2.2le  %-+#2.2le
           %-+#2.2le ",Mt[50],Mr[50],Q[50],def[50],theta[50]);
           printf("\n b     %-+#2.2e  %-+#2.2le  %-+#2.2le  %-+#2.2le
           %-+#2.2le ",Mt[0],Mr[0],Q[0],def[0],theta[0]);
           printf("\n"); printf("\n  Maximum Moment    =%-+#2.2le, Minimum
           moment    =%-+#2.2le ",maxM,minM);
           printf("\n  Maximum deflection=%-+#2.2le, Minimum
           deflection=%-+#2.2le ",maxy,miny);
             getch();
           }







DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     25




         





         
           13.19  void restrain(void)  /* beginning of choice of
           restraints*/
         
           {
           printf(" Edge restraints case ");
           cas=tolower(getch());
           printf("%c",cas);
           printf("                       Please wait...");
           }
         
           13.20  void restraints ()/* 2nd step :to avoid infinite looping
           of default*/
         
           {
           switch (cas)
                  {
                  case 'a':csa();break;
                  case 'b':csb();break;
                  case 'c':csc();break;
         








































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     26




         





         
                  case 'd':csd();break;
                  case 'e':cse();break;
                  case 'f':csf();break;
                  case 'g':csg();break;
                  case 'h':csh();break;
                  case 'i':csi();break;
                  case 'j':csj();break;
                  case 'k':csk();break;
                  case 'l':csl();break;
                  default:restrain();
                  }
           }
         
           13.21 /* Scaling */ 
         
              13.21.1 int scalex(double x)         /* scaling along x axix
              */
         
              {
              return(xx/2*(x/a+1)) ;
              }
         
              13.21.2  int scaley(double x,double y) /*scaling along y
              axis */
         
              {
              return(yy/4*(-y/x+2));
              }
         
           13.22  void setgraph()              /* usual graph verif
           routine */
         
           { /* request auto detection */
           int gdriver = DETECT, gmode, errorcode;
           /* register a driver that was added into graphics.lib */
           errorcode = registerfarbgidriver(EGAVGA_driver_far);
           
           errorcode = registerfarbgidriver(CGA_driver_far);
           
           /* report any registration errors */
           if (errorcode < 0)
              {
              printf("Graphics error: %s\n", grapherrormsg(errorcode));
              printf("Press any key to halt:");
              getch();
              exit(1); /* terminate with an error code */ }
              }
           /* initialize graphics and local variables */
              initgraph(&gdriver, &gmode, "");
           /* read result of initialization */
              errorcode = graphresult();
            if (errorcode != grOk)  /* an error occurred */
               {
  
         





DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     27




         





               printf("Graphics error: %s\n", grapherrormsg(errorcode));
               printf("Press any key to halt:"); 
               getch();
               exit(1); /* terminate with an error code */
               }
           }
         
         14 Table of verifications
         
         ok : shows a good agreement between the two methods, not much
         more than one digit in the last of the figure.
         

















































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     28




         





         
         o : shows a larger discrepancy, explained or acceptable.
         Actually, all these are attributable to a poor accuracy of the
         tabulated results in the book itself: the author is right, there
         is no reason to try and find an accurate figure for anyway
         negligible stresses or strains, but in this instance, it becomes
         impossible to rely on these values to check the software.
         
         a=20                r0=b (except when indicated otherwise)
                             
         
         b=2,6,12,14
         
         E=11000000
         
         t=1  nu=0.3  D=1007326
         
         q=10
         
         M=100   w=10
         
         14.1 case 1a                                          
                                                               
         
                       ok    ok        ok        ok        ok
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb               -3.640E-02-1.266E-01-1.934E-01-1.927E-01-9.380E-02
                                                           
         
         Ktetaa          4.180E-02 1.664E-01 3.573E-01 6.119E-01 9.237E-01
                                                           
         
         Kthetab        3.710E-02 2.047E-01 4.262E-01 6.780E-01 9.532E-01
                                                           
         
         Kmtb              3.374E-01 6.210E-01 7.757E-01 8.814E-01 9.638E-01
                                                           
         
                                                           
         
         yb=               -2.891E-03-1.005E-02-1.536E-02-1.530E-02-7.449E-03
                                                           
         
         thetaa          1.660E-04 6.608E-04 1.419E-03 2.430E-03 3.668E-03
                                                           
         
         thetab          1.473E-04 8.128E-04 1.692E-03 2.692E-03 3.785E-03
                                                           
         
         Mtb=              6.748E+01 1.242E+02 1.551E+02 1.763E+02 1.928E+02
                                                           
         
         14.2 case 1 b                                         
                                                               
         
                       ok    ok        ok        ok        o
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb               -2.690E-02-4.170E-02-2.520E-02-7.200E-03-3.000E-04
                                                           
         
         Kthetaa        3.610E-02 7.630E-02 6.840E-02 3.420E-02 4.700E-03
                                                           
         
         Kmrb              2.555E-01 4.146E-01 3.944E-01 2.736E-01 9.810E-02
                                                           
         
                                                           
         
         yb=               -2.136E-03-3.312E-03-2.001E-03-5.718E-04-2.383E-05
                                                           
         
         thetaa          1.433E-04 3.030E-04 2.716E-04 1.358E-04 1.866E-05
                                                           
         
         Mrb=              5.110E+01 8.292E+01 7.888E+01 5.472E+01 1.962E+01
                                                           
         
         14.3 case 1c                                          
                                                               
         


















DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     29




         





                       ok    o         ok        ok        ok
                                                           
         
            b/a    0.1                 0.5                 0.7
                                                           
         
             r0/a  0.5       0.7       0.7       0.9       0.9
                                                           
         
         Kymax           -1.020E-02-1.130E-02-2.300E-03-1.700E-03-5.000E-04
                                                           
         
         Kthetaa        2.780E-02 3.880E-02 1.200E-02 1.220E-02 5.500E-03
                                                           
         
         Kthetab       -4.440E-02-4.200E-02-1.650E-02-9.800E-03-4.800E-03
                                                           
         
         KMtb             -4.043E-01-3.891E-01-3.010E-02-1.780E-02-6.300E-03
                                                           
         
         KMr0              1.629E-01 1.689E-01 1.161E-01 7.880E-02 6.620E-02
                                                           
         
         KQb                2.941E+00 2.478E+00 8.114E-01 3.376E-01 4.145E-01
                                                           
         
                                                           
         
         ymax=           -8.101E-04-8.974E-04-1.827E-04-1.350E-04-3.971E-05
                                                           
         
         thetaa=        1.104E-04 1.541E-04 4.765E-05 4.845E-05 2.184E-05
                                                           
         
         thetab=       -1.763E-04-1.668E-04-6.552E-05-3.891E-05-1.906E-05
                                                           
         
         Mtb=             -8.086E+01-7.782E+01-6.020E+00-3.560E+00-1.260E+00
                                                           
         
         Mr0                3.258E+01 3.378E+01 2.322E+01 1.576E+01 1.324E+01
                                                           
         
         Qb                  2.941E+01 2.478E+01 8.114E+00 3.376E+00 4.145E+00
                                                           
         
         14.4 case 1d                                          
                                                               
         
                       ok    ok        ok        o         o
                                                           
         
            b/a    0.1                 0.5                 0.7
                                                           
         
             r0/a  0.5       0.7       0.7       0.9       0.9
                                                           
         
         Kymax           -6.600E-03-8.200E-03-1.000E-03-1.000E-03-3.000E-04
                                                           
         
         Kthetaa        1.940E-02 3.080E-02 5.600E-03 8.400E-03 3.400E-03
                                                           
         
         KMrb             -4.141E-01-3.911E-01-1.172E-01-6.920E-02-5.190E-02
                                                           
         
         KQb                3.362E+00 2.876E+00 1.070E+00 4.901E-01 5.972E-01
                                                           
         
                                                           
         
         ymax=           -5.242E-04-6.512E-04-7.942E-05-7.942E-05-2.383E-05
                                                           
         
         thetaa=        7.704E-05 1.223E-04 2.224E-05 3.336E-05 1.350E-05
                                                           
         
         Mrb               -8.282E+01-7.822E+01-2.344E+01-1.384E+01-1.038E+01
                                                           
         
         Qb                  3.362E+01 2.876E+01 1.070E+01 4.901E+00 5.972E+00
                                                           
         
         14.5 case 1 e                                         
                                                               
         
                       ok    ok        ok        o         ok
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb               -1.430E-02-3.300E-02-2.330E-02-7.100E-03-3.000E-04
                                                           
         



























DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     30




         





         Kthetab        2.540E-02 8.250E-02 7.760E-02 3.730E-02 4.800E-03
                                                           
         
         KMra             -5.280E-02-1.687E-01-2.379E-01-2.124E-01-9.110E-02
                                                           
         
         Kmtb              2.307E-01 2.503E-01 1.412E-01 4.840E-02 4.800E-03
                                                           
         
                                                           
         
         yb=               -1.136E-03-2.621E-03-1.850E-03-5.639E-04-2.383E-05
                                                           
         
         thetab=        1.009E-04 3.276E-04 3.081E-04 1.481E-04 1.906E-05
                                                           
         
         Mra               -1.056E+01-3.374E+01-4.758E+01-4.248E+01-1.822E+01
                                                           
         
         Mtb                4.614E+01 5.006E+01 2.824E+01 9.680E+00 9.600E-01
                                                           
         
         14.6 case 1 f                                         
                                                               
         
                       o     ok        ok        ok        ok
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb               -9.700E-03-1.260E-02-6.800E-03-1.900E-03-1.000E-04
                                                           
         
         KMrb=            1.826E-01 2.469E-01 2.121E-01 1.396E-01 4.910E-02
                                                           
         
         KMra=           -4.770E-02-1.143E-01-1.345E-01-1.101E-01-4.580E-02
                                                           
         
                                                           
         
         yb=               -7.704E-04-1.001E-03-5.400E-04-1.509E-04-7.942E-06
                                                           
         
         Mrb=              3.652E+01 4.938E+01 4.242E+01 2.792E+01 9.820E+00
                                                           
         
         Mra=             -9.540E+00-2.286E+01-2.690E+01-2.202E+01-9.160E+00
                                                           
         
         14.7 case 1 g                                         
                                                               
         
                       ok    ok        o         o         o
                                                           
         
            b/a    0.1                 0.5                 0.7
                                                           
         
             r0/a  0.5       0.7       0.7       0.9       0.9
                                                           
         
         Kymax           -5.300E-03-4.100E-03-1.200E-03-4.000E-04-2.000E-04
                                                           
         
         Kthetab=     -2.620E-02-1.660E-02-9.200E-03-2.300E-03-1.800E-03
                                                           
         
         KMrb             -2.388E-01-1.513E-01-1.670E-02-4.200E-03-2.300E-03
                                                           
         
         KMr0=            1.179E-01 7.660E-02 8.200E-02 2.080E-02 2.860E-02
                                                           
         
         KMra=           -8.930E-02-1.244E-01-6.640E-02-6.740E-02-5.210E-02
                                                           
         
         KQb=              1.915E+00 1.050E+00 5.658E-01 8.850E-02 1.784E-01
                                                           
         
                                                           
         
         ymax=           -4.209E-04-3.256E-04-9.530E-05-3.177E-05-1.588E-05
                                                           
         
         thetab=       -1.040E-04-6.592E-05-3.653E-05-9.133E-06-7.148E-06
                                                           
         
         Mrb=             -4.776E+01-3.026E+01-3.340E+00-8.400E-01-4.600E-01
                                                           
         
         Mr0=              2.358E+01 1.532E+01 1.640E+01 4.160E+00 5.720E+00
                                                           
         



























DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     31




         





         Mra=             -1.786E+01-2.488E+01-1.328E+01-1.348E+01-1.042E+01
                                                           
         
         Qb=                   19.152    10.495     5.658     0.885     1.784
                                                           
         
         14.8 case 1 h                                         
                                                               
         
                       ok    o         ok        o         o
                                                           
         
            b/a    0.1                 0.5                 0.7
                                                           
         
             r0/a  0.5       0.7       0.7       0.9       0.9
                                                           
         
         Kymax           -3.800E-03-3.300E-03-6.000E-04-3.000E-04-1.000E-04
                                                           
         
         KMrb=           -2.792E-01-1.769E-01-8.560E-02-2.160E-02-2.520E-02
                                                           
         
         KMra=           -7.100E-02-1.128E-01-4.040E-02-6.080E-02-4.220E-02
                                                           
         
         KMr0=            1.071E-01 7.950E-02 5.860E-02 2.400E-02 2.900E-02
                                                           
         
         KQb=              2.409E+00 1.363E+00 8.509E-01 1.603E-01 3.118E-01
                                                           
         
                                                           
         
         ymax=           -3.018E-04-2.621E-04-4.765E-05-2.383E-05-7.942E-06
                                                           
         
         Mrb=             -5.584E+01-3.538E+01-1.712E+01-4.320E+00-5.040E+00
                                                           
         
         Mra=             -1.420E+01-2.256E+01-8.080E+00-1.216E+01-8.440E+00
                                                           
         
         Mr0=              2.142E+01 1.590E+01 1.172E+01 4.800E+00 5.800E+00
                                                           
         
         Qb=                2.409E+01 1.363E+01 8.509E+00 1.603E+00 3.118E+00
                                                           
         
         14.9 case 2 a                                         
                                                               
         
                       ok    ok        ok        ok        ok
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb               -6.870E-02-7.610E-02-6.240E-02-3.250E-02-4.800E-03
                                                           
         
         Ktetaa          9.860E-02 1.120E-01 1.201E-01 1.041E-01 4.770E-02
                                                           
         
         Kthetab        4.360E-02 1.079E-01 1.321E-01 1.130E-01 4.910E-02
                                                           
         
         Kmtb              3.965E-01 3.272E-01 2.404E-01 1.469E-01 4.970E-02
                                                           
         
                                                           
         
         yb=               -1.091E-01-1.209E-01-9.911E-02-5.162E-02-7.624E-03
                                                           
         
         thetaa=        7.831E-03 8.895E-03 9.538E-03 8.267E-03 3.788E-03
                                                           
         
         thetab=        3.463E-03 8.569E-03 1.049E-02 8.974E-03 3.899E-03
                                                           
         
         Mtb=              1.586E+03 1.309E+03 9.616E+02 5.876E+02 1.988E+02
                                                           
         
         14.10 case 2 b                                        
                                                               
         
                       ok    ok        ok        o         
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb               -5.750E-02-3.140E-02-1.030E-02-1.500E-03-2.000E-05
                                                           
         



























DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     32




         





         Kthetaa        9.190E-02 6.450E-02 3.060E-02 7.800E-03 3.200E-04
                                                           
         
         Kmrb              3.003E-01 2.185E-01 1.223E-01 4.560E-02 5.050E-03
                                                           
         
                                                           
         
         yb=               -9.133E-02-4.987E-02-1.636E-02-2.383E-03-3.177E-05
                                                           
         
         thetaa          7.299E-03 5.122E-03 2.430E-03 6.195E-04 2.541E-05
                                                           
         
         Mrb=              1.201E+03 8.740E+02 4.892E+02 1.824E+02 2.020E+01
                                                           
         
         14.11 case 2 c                                        
                                                               
         
                       ok    ok        ok        o         
                                                           
         
            b/a    0.1       0.3       0.5       0.7       
                                                           
         
         Kymax=         -6.000E-03-2.900E-03-8.000E-04-1.000E-04
                                                           
         
         Kthetab       -2.640E-02-1.530E-02-5.500E-03-1.200E-03
                                                           
         
         Kthetaa        1.980E-02 1.190E-02 4.700E-03 1.100E-03
                                                           
         
         KMtb             -2.401E-01-4.630E-02-1.010E-02-1.500E-03
                                                           
         
         KMrmax          7.080E-02 5.520E-02 3.000E-02 1.100E-02
                                                           
         
         KQb                1.887E+00 6.015E-01 3.230E-01 1.684E-01
                                                           
         
                                                           
         
         ymax             -9.530E-03-4.606E-03-1.271E-03-1.588E-04
                                                           
         
         thetab         -2.097E-03-1.215E-03-4.368E-04-9.530E-05
                                                           
         
         thetaa          1.572E-03 9.451E-04 3.733E-04 8.736E-05
                                                           
         
         Mtb               -9.604E+02-1.852E+02-4.040E+01-6.000E+00
                                                           
         
         Mrmax            2.832E+02 2.208E+02 1.200E+02 4.400E+01
                                                           
         
         Qb                  3.774E+02 1.203E+02 6.460E+01 3.368E+01
                                                           
         
         14.12 case 2 d                                        
                                                               
         
                   ok        ok        ok        o         
                                                           
         
            b/a    0.1       0.3       0.5       0.7       
                                                           
         
         Kymax=         -4.000E-03-1.400E-03-4.000E-04-4.000E-05
                                                           
         
         Kthetaa        1.470E-02 7.000E-03 2.600E-03 5.600E-04
                                                           
         
         Kmrb             -2.459E-01-9.390E-02-3.930E-02-1.257E-02
                                                           
         
         KQb                2.138E+00 7.533E-01 4.096E-01 2.126E-01
                                                           
         
                                                           
         
         ymax             -6.353E-03-2.224E-03-6.353E-04-6.353E-05
                                                           
         
         thetaa          2.335E-02 1.112E-02 4.130E-03 8.895E-04
                                                           
         
         Mrb               -9.836E+02-3.756E+02-1.572E+02-5.028E+01
                                                           
         



























DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     33




         





         Qb                  4.275E+02 1.507E+02 8.192E+01 4.252E+01
                                                           
         
         14.13 case 2 e                                        
                                                               
         
                       ok    ok        ok        o         o
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb               -1.660E-02-1.320E-02-5.300E-03-9.000E-04-1.000E-05
                                                           
         
         Kthetab        1.590E-02 2.560E-02 1.490E-02 4.000E-03 1.600E-04
                                                           
         
         KMra             -1.246E-01-1.135E-01-8.000E-02-3.610E-02-4.700E-03
                                                           
         
         KMtb              1.448E-01 7.780E-02 2.710E-02 5.200E-03 1.600E-04
                                                           
         
                                                           
         
         yb                 -2.637E-02-2.097E-02-8.418E-03-1.430E-03-1.588E-05
                                                           
         
         thetab          1.263E-03 2.033E-03 1.183E-03 3.177E-04 1.271E-05
                                                           
         
         Mra               -4.984E+02-4.540E+02-3.200E+02-1.444E+02-1.880E+01
                                                           
         
         Mtb                5.792E+02 3.112E+02 1.084E+02 2.080E+01 6.400E-01
                                                           
         
         14.14 case 2 f                                        
                                                               
         
                       ok    ok        ok        o         ok
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb               -1.370E-02-6.800E-03-2.100E-03-3.000E-04 0.000E+00
                                                           
         
         KMrb              1.146E-01 7.670E-02 4.070E-02 1.490E-02 1.670E-03
                                                           
         
         KMra             -1.214E-01-9.660E-02-6.010E-02-2.520E-02-3.160E-03
                                                           
         
                                                           
                                                           
         
         yb                 -2.176E-02-1.080E-02-3.336E-03-4.765E-04 0.000E+00
                                                           
         
         Mrb                4.584E+02 3.068E+02 1.628E+02 5.960E+01 6.680E+00
                                                           
         
         Mra               -4.856E+02-3.864E+02-2.404E+02-1.008E+02-1.264E+01
                                                           
         
         14.15 case 2 g                                        
                                                               
         
                       o     o         o         o         
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kymax           -2.500E-03-1.200E-03-3.000E-04 0.000E+00 0.000E+00
                                                           
         
         Kthetab       -1.350E-02-7.300E-03-2.700E-03-6.000E-04 0.000E+00
                                                           
         
         KMtb              1.226E-01 2.210E-02 4.800E-03 7.000E-04 0.000E+00
                                                           
         
         KMra             -6.340E-02-4.620E-02-2.620E-02-1.020E-02-1.200E-03
                                                           
         
         KQb                1.159E+00 3.989E-01 2.262E-01-1.221E+03 3.830E-02
                                                           
         
                                                           
         
         ymax             -3.971E-03-1.906E-03-4.765E-04 0.000E+00 0.000E+00
                                                           
         



























DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     34




         





         thetab         -1.072E-03-5.798E-04-2.144E-04-4.765E-05 0.000E+00
                                                           
         
         Mtb                4.904E+02 8.840E+01 1.920E+01 2.800E+00 0.000E+00
                                                           
         
         Mra               -2.536E+02-1.848E+02-1.048E+02-4.080E+01-4.800E+00
                                                           
         
         Qb                  2.318E+02 7.978E+01 4.524E+01-2.442E+05 7.660E+00
                                                           
         
         14.16 case 2 h                                        
                                                               
         
                       o     o         o         o         
                                                           
         
            b/a    0.1       0.3       0.5       0.7       
                                                           
         
         Kymax           -1.800E-03-6.000E-04-2.000E-04 0.000E+00
                                                           
         
         KMrb             -1.433E-01-5.700E-02-2.470E-02-8.100E-03
                                                           
         
         KMra             -5.400E-02-3.470E-02-1.870E-02-7.000E-03
                                                           
         
         KQb                1.413E+00 5.414E-01 3.084E-01 1.650E-01
                                                           
         
                                                           
         
         ymax             -2.859E-03-9.530E-04-3.177E-04 0.000E+00
                                                           
         
         Mrb               -5.732E+02-2.280E+02-9.880E+01-3.240E+01
                                                           
         
         Mra               -2.160E+02-1.388E+02-7.480E+01-2.800E+01
                                                           
         
         Qb                  2.825E+02 1.083E+02 6.168E+01 3.300E+01
                                                           
         
         14.17 case 2 i                                        
                                                               
         
                       ok    ok        ok        ok        o
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kya               -5.430E-02-3.690E-02-1.220E-02-1.700E-03-2.000E-05
                                                           
         
         Kthetab       -1.096E-01-9.950E-02-4.330E-02-9.600E-03-3.400E-04
                                                           
         
         KMra              1.368E-01 1.423E-01 9.850E-02 4.120E-02 4.910E-03
                                                           
         
         KMtb             -9.971E-01-3.018E-01-7.880E-02-1.250E-02-3.500E-04
                                                           
         
                                                           
         
         ya                 -8.625E-02-5.861E-02-1.938E-02-2.700E-03-3.177E-05
                                                           
         
         thetab         -8.704E-03-7.902E-03-3.439E-03-7.624E-04-2.700E-05
                                                           
         
         Mra                5.472E+02 5.692E+02 3.940E+02 1.648E+02 1.964E+01
                                                           
         
         Mtb               -3.988E+03-1.207E+03-3.152E+02-5.000E+01-1.400E+00
                                                           
         
         14.18 case 2 j                                        
                                                               
         
                       ok    ok        ok        ok        o
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kya               -3.430E-02-1.230E-02-3.000E-03-4.000E-04 0.000E+00
                                                           
         
         KMrb             -7.892E-01-2.978E-01-1.184E-01-3.590E-02-3.510E-03
                                                           
         



























DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     35




         





         KMra              1.146E-01 7.670E-02 4.070E-02 1.490E-02 1.670E-03
                                                           
         
         ya                 -5.448E-02-1.954E-02-4.765E-03-6.353E-04 0.000E+00
                                                           
         
         Mra                4.584E+02 3.068E+02 1.628E+02 5.960E+01 6.680E+00
                                                           
         
         Mrb               -3.157E+03-1.191E+03-4.736E+02-1.436E+02-1.404E+01
                                                           
         
         14.19 case 2 k                                        
                                                               
         
                       ok    ok        ok        ok        o
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kya               -1.115E-01-1.158E-01-8.260E-02-3.780E-02-5.100E-03
                                                           
         
         Kthetab       -1.400E-01-2.026E-01-1.876E-01-1.340E-01-5.150E-02
                                                           
         
         Kthetaa       -1.082E-01-1.404E-01-1.479E-01-1.188E-01-4.980E-02
                                                           
         
         KMtb             -1.273E+00-6.146E-01-3.414E-01-1.742E-01-5.210E-02
                                                           
         
                                                           
         
         ya                 -1.771E-01-1.839E-01-1.312E-01-6.004E-02-8.101E-03
                                                           
         
         thetab         -1.112E-02-1.609E-02-1.490E-02-1.064E-02-4.090E-03
                                                           
         
         thetaa         -8.593E-03-1.115E-02-1.175E-02-9.435E-03-3.955E-03
                                                           
         
         Mrb               -5.094E+03-2.458E+03-1.366E+03-6.968E+02-2.084E+02
                                                           
         
         14.20 case 2 l                                        
                                                               
         
                       ok    ok        ok        ok        ok
                                                           
         
            a/b    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kya               -7.570E-02-3.180E-02-8.600E-03-1.100E-03 0.000E+00
                                                           
         
         KKthetaa     -8.680E-02-5.120E-02-2.070E-02-4.600E-03-1.700E-04
                                                           
         
         KMrb             -9.646E-01-4.103E-01-1.736E-01-5.410E-02-5.300E-03
                                                           
         
                                                           
         
         ya                 -1.202E-01-5.051E-02-1.366E-02-1.747E-03 0.000E+00
                                                           
         
         thetaa         -1.379E-01-8.132E-02-3.288E-02-7.306E-03-2.700E-04
                                                           
         
         Mrb               -3.858E+03-1.641E+03-6.944E+02-2.164E+02-2.120E+01
                                                           
         
         14.21 case 3 a                                        
                                                               
         
                       ok    ok        ok        ok        o
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb               -3.170E-02-3.060E-02-2.310E-02-1.140E-02-1.600E-03
                                                           
         
         Ktetaa          4.820E-02 4.700E-02 4.540E-02 3.680E-02 1.610E-02
                                                           
         
         Kthetab        1.860E-02 4.180E-02 4.830E-02 3.960E-02 1.660E-02
                                                           
         
         Kmtb              1.690E-01 1.269E-01 8.790E-02 5.140E-02 1.680E-02
                                                           
         



























DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     36




         





                                                           
         
         yb=               -5.035E-02-4.860E-02-3.669E-02-1.811E-02-2.541E-03
                                                           
         
         thetaa          3.828E-03 3.733E-03 3.606E-03 2.923E-03 1.279E-03
                                                           
         
         thetab          1.477E-03 3.320E-03 3.836E-03 3.145E-03 1.318E-03
                                                           
         
         Mtb=              6.760E+02 5.076E+02 3.516E+02 2.056E+02 6.720E+01
                                                           
         
         14.22 case 3 k                                        
                                                               
         
                       ok    ok        ok        ok        ok
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kya               -8.300E-02-8.260E-02-5.740E-02-2.580E-02-3.400E-03
                                                           
         
         Kthetab       -9.820E-02-1.413E-01-1.293E-01-9.120E-02-3.460E-02
                                                           
         
         Kthetaa       -8.340E-02-1.019E-01-1.035E-01-8.120E-02-3.350E-02
                                                           
         
         KMtb             -8.937E-01-4.286E-01-2.354E-01-1.186E-01-3.500E-02
                                                           
         
                                                           
         
         ya                 -1.318E-01-1.312E-01-9.117E-02-4.098E-02-5.400E-03
                                                           
         
         thetab         -7.799E-03-1.122E-02-1.027E-02-7.243E-03-2.748E-03
                                                           
         
         thetaa         -6.623E-03-8.093E-03-8.220E-03-6.449E-03-2.661E-03
                                                           
         
         Mtb               -3.575E+03-1.714E+03-9.416E+02-4.744E+02-1.400E+02
                                                           
         
         14.23 case 5 a                                        
                                                               
         
                       o     o         o         o         o
                                                           
         
            b/a    0.1       0.3       0.5       0.7       0.9
                                                           
         
         Kyb                4.178E-01 5.447E-01 7.147E-01 8.742E-01 1.026E+00
                                                           
         
         Ktetaa         -7.914E-01-9.866E-01-1.502E+00-2.881E+00-1.014E+01
                                                           
         
         Kthetab       -2.220E-01-7.246E-01-1.465E+00-3.017E+00-1.041E+01
                                                           
         
         Kmtb             -2.020E+00-2.198E+00-2.667E+00-3.922E+00-1.053E+01
                                                           
         
                                                           
         
         yb=                1.659E-02 2.163E-02 2.838E-02 3.471E-02 8.151E-02
                                                           
         
         thetaa         -1.571E-03-1.959E-03-2.982E-03-5.720E-03-4.026E-02
                                                           
         
         thetab         -4.408E-04-1.439E-03-2.909E-03-5.989E-03-4.134E-02
                                                           
         
         Mtb=             -2.020E+02-2.198E+02-2.667E+02-3.922E+02-2.105E+03
                                                           
         
         15 Acknowledgments
         
         IBM is a trademark of International Business Machines.
         PcTools is a trademark of Central Point Software.
         Quattro and Turbo C++ are under copyright of Borland
         International, Inc 1987,1990. All rights reserved. Licensed

























DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     37




         





         material-program property of Borland International, Inc, 1800
         Green Hills Road, PO Box 660001,SCOTTS VALLEY, CA 95067-0001.
         Unauthorized use, duplication, or distribution is strictly
         prohibited by federal laws.
         PKLITE is published by PKWARE, Inc 7545 North Port Washington
         Road, Suite 205, Glendale, WI 53217-3422, USA.
         





















































DISK: Circular pierced plates (Roark's formulas for stress and strains,
by Warren C. Young
                                                                                     38