POP-CAL                                    Leo Forrest
          Command                                    1986/No. 17

          ______________________________________________________

          Purpose:  Pops up a calendar window for any month from
                    January, 1583 to December, 9999.

          Format:   POP-CAL          (loads command into memory)
                    Alt-C                Toggles calendar on/off
                    Right-Arrow                Advance one month
                    Left-Arrow                    Back one month
                    Up-Arrow                    Advance one year
                    Down-Arrow                     Back one year

          Remarks:  POP-CAL is a memory-resident utility and
                    should be loaded into memory before you call
                    up any applications programs.  Normally, you
                    would simply enter POP-CAL as one line in
                    your AUTOEXEC.BAT file.

                    POP-CAL takes the current month and year as
                    its initial value.  It subsequently remembers
                    your last-used calendar, facilitating
                    repeated references.

                    Notes:

                    1.   You can use DEBUG to change the default
                         Alt-C toggle key by replacing the
                         Alt-key scan code value at offset :014B.
                         The default value is 2E, which will
                         appear, followed by a period, in
                         response to the E command shown below.
                         Enter only the new scan code, not the
                         2E.  Thus, to change the program to use
                         Alt-Q (scan code 10) you would enter:
                            DEBUG POP-CAL.COM
                            E 14b 10
                            W
                            Q

                         The hex values for the various scan
                         codes are given in Appendix E of the IBM
                         BASIC manual (3.0) and also in the "Scan
                         Code Value Table" in connection with
                         SLASHBAR.COM.

                    2.   While POP-CAL has been tested for
                         compatibility with a number of other
                         memory-resident programs, there is
                         always the possibility of a conflict
                         with other TSR (Terminate-Stay-Resident)
                         programs.