SMOUSE.SYS and SMOUSE.COM allow the tablet to operate like a Microsoft(R) mouse.
SMOUSE.SYS is a system file that can be used in your config.sys file.
SMOUSE.COM is a TSR (Terminate and Stay Resident) program, that can be run
from the DOS command prompt or from a batch file, including the autoexec.bat.
SMOUSE.SYS and SMOUSE.COM should  NOT  be loaded at the same time.

Usage:    DEVICE=SMOUSE.SYS [Com Port] [Tablet Type] [Pointing Device]
       or
          SMOUSE.COM [Com Port] [Tablet Type] [Pointing Device]

Where:    Com Port = 1   for Com Port 1
                     2   for Com Port 2
                     3   for Com Port 3, PS/2 models only
                     4   for Com Port 4, PS/2 models only

       Tablet Type = T2  for SummaSketch 12"x12" (MM1201)
                     T2  for SummaSketch 12"x18" (MM1812)
                     T9  for SummaSketch 9"x6" (MM961)

   Pointing Device = C3  for three button cursor
                     C4  for four button cursor
                     CP  for stylus