ORBITAL MECHANICS PROGRAM
                              Version 1.0   2-16-86
                                  By Don Thayer
        
        
            This  program will  calculate the  major  orbital  parameters
        associated with  two astronomical  objects when one orbits around
        the other.
        
           When the program is first started, the GRAVITATIONAL PARAMETER
        (GP) will be requested.
        
            Whenever  this parameter is required, you can either enter it
        directly or press the <CR> key to get a list of possible choices.
        Selections  1   through  11  are  common  solar  system  objects.
        Selection 12  lets  you  enter  the  parameter  directly.    With
        selection 13  you can combine any two of the choices from 1 to 11
        and selection 14 will show the GPs for black holes.
        
            Once  the GP  is entered,  you will  be required to enter the
        object's diameter.   Again  you can  either  enter  the  diameter
        directly or press the <CR> key to get a listing.  If you selected
        a GP  for a  black hole,  the option  13 will  select a  diameter
        equivalent to  the EVENT  HORIZON diameter.   Selecting option 13
        when a black hole GP was not chosen will enter a very small value
        which will  force any  major astronomical  object to  simulate  a
        black hole.
        
            After  initially entering the GP and diameter a menu of input
        options will  be displayed.  Before the orbital parameters can be
        computed, you  must select  option <2>,  <3>, <4>,  <5> or <6> to
        enter final necessary information.
        
            Selecting  option <2>  from this menu will allow you to input
        the SEMIMAJOR  AXIS and  the ECCENTRICITY  of the orbit.  Both of
        these options  can be  either entered  directly or  from  a  list
        provided when  the <CR>  key is  pressed in  lieu of  entering  a
        number.
        
        NOTE: Only  selections <1>  and <2>  will give  you the option of
        selecting from  a list.   Selection numbers <3>, <4>, <5> and <6>
        will require  direct input  of  the  values.    Option  <7>  when
        available, will give a range that can be used.
        
            Selecting  option <3>  will allow  you to input the RADIUS at
        APOGEE and the RADIUS at PERIGEE.
        
            VELOCITY at APOGEE and PERIGEE are the orbital velocities and
        can be entered from option <4> on the main menu.
        
            The  PERIOD of  ROTATION in option <5> is the time in seconds
        required for  the orbiting  object to  revolve  around  the  main
        object.



            Selecting  option <6> will allow you to define an orbit given
        your PRESENT  RADIUS (or  distance to  the object), your VELOCITY
        and the  ATTACK ANGLE.   An  angle of  90 degrees  will define an
        orbit at  a right  angle to  your velocity  vector and  the  main
        object.   Selecting an  angle of "0" degrees may be disastrous to
        both you  and the  program as  it will direct you straight at the
        main object.   Choosing  too high  of a  velocity may  exceed the
        escape velocity  and a warning will be shown at the bottom of the
        screen.   No orbit  can be  computed if  this happens.    If  the
        velocity is too small, your orbit will intersect the object.
        
           Option <7> will not be available until after an orbit has been
        calculated.  This option allows you to enter the distance you are
        from the  object (orbital  radius) and show data relative to your
        position on the orbit.
        
            Option  <X> will  toggle between full scientific notation and
        mixed notation  where only  large numeric values above 1x10E6 and
        very small numbers will be shown in scientific notation.
        
           Option <Q> quits the program.
        
        
                   ----------------------------------------
        
           Once data has been entered by using options <2>, <3>, <4>, <5>
        or <6>,  the orbital data will be displayed and you will be given
        a chance  to print  the data  on a printer.  Type a "Y" or "y" if
        you want a printout otherwise type "N" or "n" for no printout.
        
            A  command line  will appear at the bottom of the screen that
        will allow  you change  any of  the input  sets of data.  You can
        enter options  1, 2, 3, 4, 5, 6, 7, 8, X, Q which are the same as
        those on  main menu  or you  can select option "M" to display the
        main menu  again.   You can  see a  graphic representation of the
        orbit by  selecting  the  "G"  option  if  you  have  an  IBM  or
        equivalent graphics card.
        
            If  you change the GP & diameter by selection option <1>, the
        new orbit  data will be computed from the existing semimajor axis
        and eccentricity.
        
            When  you select  options <6>  or <7> from either the command
        line or  the main  menu, data  in addition  to the normal orbital
        statistics will be shown on the screen.
        
        
                               THE GRAPHIC SCREEN
        
            When  you choose  then graphic display your orbit will shown.
        If the eccentricity is near 1.0000, then the orbit will appear as
        a straight  line and if the eccentricity was 0.000, a circle will
        be displayed as the orbit.  Values in between will produce orbits
        of varying ellipses.
        
            A  small cross will mark the center of the main object at the
        focal point  of the  orbital ellipse.   If possible, the relative
        size of  the main  object will  also be  shown as  a solid circle
        about the  objects center.   This  will  occur  if  the  relative
        diameter of  the object is more than four pixles across and if it
        is not greater than size of the screen.
 

        
           If a black hole was selected from the GP & diameter option, it
        will be  shown as  broken line  orbit if its relative size can be
        shown on the screen.
        
            When options <6> or <7> are selected, the graphic screen will
        also show  your relative  position on  the orbit in the form of a
        larger cross.
        
        
                                ENTERING NUMBERS
        
           Sometimes when a number is entered, the data will be requested
        again or  the computer  will beep  and display  another  question
        mark.   When this  happens, you  have either  entered an  illegal
        string of characters such as 3q23 or the value you entered is not
        acceptable for  the input  such as  trying to  enter 0.00 for the
        semimajor axis.
        
            Many  times the  value you are to enter is very large or very
        small, for  example: 200000000 (2 with eight zeros following it).
        This number  can be  entered   as 2.0E8  or 2.0E+8  in scientific
        notation.  Very small number such as 0.00000123 should be entered
        as 1.23E-6 in the scientific format.
        
        
                                   DEFINITIONS
        
        Gravitational Parameter:   This  is the  gravitational attraction
           between two  objects and  is the  result  of  the  gravitation
           constant multiplied  by the mass of the object and is measured
           in miles cubed per second squared.
        
        Diameter of Object: The diameter of the main object in miles.
        
        Event Horizon:   The  radius of  a black hole at which the escape
           velocity is  equal to the speed of light.  This is measured in
           miles.
        
        Semimajor Axis:   The  greatest distance  from the  center of the
           orbital ellipse to the orbit and is measured in miles.
        
        Eccentricity: A measure of the out of roundness of the orbit.  An
           eccentricity of  "0" will  produce a  perfect  circular  orbit
           while  a  value  of  0.9999  will  produce  a  very  flattened
           elliptical orbit.
        
        Radius at  Apogee:   The greatest  distance between  the orbiting
           object and the center of the main object as measured in miles.
        
        Radius at  Perigee:   The closest distance between the centers of
           two objects in miles.
        
        Velocity at  Apogee:  The orbital velocity in miles per second at
           the furthest distance between the two objects.
        
        Velocity at  Perigee:   The velocity at the nearest point between
           the objects in miles per second.
        
        Period of  Rotation:   The time  in  seconds  for  an  object  to
           complete one orbital revolution.



        
        Escape Velocity:   The  minimum velocity  for which no orbit will
           exist at a given orbital position.
        
        Gravitational Force:   The force in gee's exerted on the orbiting
           object by the main object.  Note: This is also the centrifugal
           force induced  by  the  orbiting  object  thus  canceling  the
           gravitational force and results in "free fall" if the orbiting
           object is a space vessel.
        
        Tidal Force:   The  force in  gee's at  one foot from the orbital
           path.   In normal orbital mechanics this value is too small to
           bother with,  however, if  a space  vessel should  approach  a
           black hole  or neutron star, this can become very great.  This
           is how  a space vessel too close to such an object can be torn
           apart.
        
        
                                 SAMPLE PROBLEM
        
           Many objects have been placed in a stationary orbit around the
        earth in  order for them to remain in one relative position above
        our planet.  These satellites  are in  what is  called an  earth-
        synchronous orbit.   Since the earth rotates about its axis every
        24 hours,  this means that a satellite must also make its orbital
        rotation in 24 hours.
           
           To determine a earth-synchronous orbit for a satellite, either
        start the  program or  if already started, select option <1> from
        the main menu.
           
           When asked for the Gravitational Parameter, press the <CR> key
        to get a listing and select item #4 for the earth.
           
           The program  will now  ask for  a diameter, press the <CR> key
        again and select item #4 on that list.
           
           Now select  option <5>  to enter  the period  of rotation  and
        eccentricity.   When the  program prompts  you for  the Period Of
        Rotation, enter 86400 (24 hrs * 3600 sec/hr).
           
           When asked  for the  eccentricity, enter a small value such as
        0.01 since we want the satellite's orbit to nearly round.
           
           The program  will now  show you  the orbital statistics for an
        earth-synchronous orbit.   Answer  the printout  question  appro-
        priately and if you have a graphics board select option "G" for a
        graphic display of the orbit.
           
           Once the  data is  back on  the screen, try experimenting with
        different orbital parameters or select option <7> and see some of
        the other orbital data.
           
           Another Example:  On October 4, 1957 the Soviet Union launched
        the first  artificial satellite.   It's  orbit ranged between 584
        miles and  143.5 miles.   Add  these values  to the radius of the
        earth  to get the approximate values of 4540 miles and 4100 miles
        respectively.   Select the  GP and  Diameter for the earth if you
        haven't already  done so  and then select option <3>.  Enter 4540
        for the  Radius at  Apogee and  then enter 4100 for the Radius at
        Perigee.


           
           
                                 ABOUT THIS PROGRAM
           
           The initial  idea started  out as  a mere curiosity when I ran
        across some  interesting equations  on black  holes.  This led to
        more in-depth  studying of  orbital mechanics.  The first program
        was written  for a  Hewlett-Packard  67  programable  calculator.
        When more  memory came  available in  form  of  an  HP-41CV,  the
        program was expanded.  Boy, this was really great!  A whole 3K of
        memory.
           
           Then came  the PC  with its free basic and later a compiler to
        speed things  up a  bit.   This final(?) version has been written
        with Borland's  Turbo Pascal with thanks to Michael Covington for
        his movable window procedure.
           
           
           The formulas  used in  this program  are mostly  basic orbital
        mechanics methods  and cannot  possible give exact results.  Also
        in orbital  systems, there  are many  massive objects  that  also
        influence the  orbit.   Our own solar system contains at least 10
        major bodies  all interacting  with each other while this program
        only deals with the "two-body problem".
           
           Every precaution  I can  think of  has been taken to keep this
        program on-line,  however, when dealing with astronomical values,
        the figures themselves become astronomical and can cause floating
        point overflow  which will  abort the  program.   I wouldn't  try
        determining the data for orbiting  galaxies.