This is the documentation file for the MODROM procedure. This procedure
will modify the 8mhz AT rom dated 11/15/85 to eliminate speed problems
with faster crystals or compatible clones running faster than 8mhz.

The problem occurs because IBM put a speed check in the 8mhz BIOS
to prevent faster crystals from being installed. At loaction 05A3
in the unmodified BIOS is the following code:

         .
         .
         .
; -----  VERIFY SPEED/REFRESH RATES  ( ERROR = 1 LONG AND 1 SHORT BEEP )

         XOR     BL,BL           ; CLEAR REFRESH CYCLE REPEAT COUNT
         XOR     CX,CX           ; INITIALIZE SPEED RATE REGISTER
         EVEN                    ; PLACE ON EVEN WORD BOUNDARY
C34:
         IN      AL,PORT_B       ; READ REFRESH BIT REGISTER
         TEST    AL,REFRESH_BIT  ; MASK FOR BIT
         LOOPZ   C34             ; DECREMENT LOOP COUNTER TILL ON
C35:
         IN      AL,PORT_B       ; READ REFRESH BIT REGISTER
         TEST    AL,REFRESH_BIT  ; MASK FOR BIT
         LOOPNZ  C35             ; DECREMENT LOOP COUNTER TILL OFF

         DEC     BL              ; DECREMENT REFRESH CYCLE REPEAT COUNT


         JNZ     C34             ; REPEAT TILL CYCLE COUNT DONE
         CMP     CX,RATE_UPPER   ; CHECK FOR RATE BELOW UPPER LIMIT
         JAE     C36             ; SKIP ERROR BEEP IF BELOW MAXIMUM

C36E:
         MOV     DX,0101H        ; GET BEEP COUNTS FOR REFRESH ERROR
         CALL    ERR_BEEP        ; CALL TO POST ERROR BEEP ROUTINES
         HLT                     ; HALT SYSTEM - BAD REFRESH RATE
C36:
         CMP     CX,RATE_LOWER   ; CHECK FOR RATE ABOVE LOWER LIMIT
         JA      C36E            ; GO TO ERROR BEEP IF BELOW MINIMUM
         .
         .
         .
What we need to do is make the JAE  C36 an unconditional jump, JMP C36,
and the JA C36E a NOP (no operation), NOP NOP.
This completely eliminates speed checking from the diagnostics (POST).

Some machines get a 108 POST error. Here the bios post routines are
checking the timer channel that drives the speaker. There is a short
code segment as follows:

         .
         .
         .
         OUT     TIMER+2,AL      ; WRITE TIMER 2 COUNT - MSB
         JMP     $+2             ; I/O DELAY
         IN      AL,TIMER+2      ; GET THE LSB
         .
         .
         .
After this code fragment is a test for AL containing the proper values.
At 6 or 8mhz most machines have no problem, but, with the short delay
inserted by the JMP $+2, at 10mhz the data doesn't have time to settle
on the bus, so an incorrect value is read. To eliminate this bug we
must change the JZ D7_D to to JMP D7_D. I've been running this way for
months with no problem. If your speaker works, the timer channel is
ok.

To acomplish all this we must run a series of programs included here.
First we must get the AT rom to disk. ROMSAVAT.EXE will do this. When
run on an IBM AT, the BIOS rom is written to disk. Next we must
modify the saved BIOS image. We will use DEBUG to do it with the
command file provided. Next we must calculate a new checksum and
split the BIOS image into the ODD and EVEN bytes. The AT has a 16 bit
bus and needs 2 27256 EPROMS (200 ns or faster reccommended), one
for each byte fetched. We will use CHKSUM64.EXE to do this step.
Now burn ATROM.EEE (EVEN bytes) in one EPROM and ATROM.OOO (ODD BYTES)
in the other. Now replace your current ROMS with the new EPROMS and
no more speeding tickets!

Remember - This works ONLY on the AT BIOS dated 11/15/85 !!!!!!!!!

To run the procedure do the following:

1. Use ONLY an IBM AT with a BIOS dated 11/15/85
2. Copy DEBUG onto the diskette with the files provided.
3. Place the diskette in drive A:
4. Make A: the default drive
5. enter the command "MODROM"
6. Sit back and wait for a while, CHKSUM64 takes a while to run.
7. Burn your new EPROMS and put them in your machine.
   if they don't work, swap them. The ODD and EVEN sockets vary from
   machine to machine and the EPROMS won't work in the wrong sockets.

The IBM BIOS won't work on SOME clones. I don't know why, but they won't