1610

Date: 11-15-88 (14:10)              Number: 1610 (Echo)
  To: SHOEL PERELMAN                Refer#: NONE
From: MIKE MEYER                      Read: NO
Subj: SPINRITE AND THE WD-27X       Status: PUBLIC MESSAGE

SP>I just got spinrite and it wont reformat my hd with the 27x cuz it
SP>"lies" to the system by saying the st238 has 939 cyliders and 17
SP>sectors, but it really has 614 cyls and 26 sectors. I read in the
SP>readme.now that there is a way to re-jumper the 27x so it doesnt "lie"
SP>about that. Does anyone know the jumper to change?

The manual  has a very clear picture on page 37 of which jumper to move,
depending on whether you have the 1002-27X or 1002A-27X.  Be prepared to
re-low-level your hard disk, though.
---
 * QDeLuxe 1.00 #134s  Have you hugged a PC today?  Did you get shocked?

 * QNet 1.03á2: Sound Of Music. Oceanside, NY.


Scanning HardDisk (1) .

Date: 11-15-88 (11:14)              Number: 1611 (Echo)
  To: SHOEL PERELMAN                Refer#: NONE
From: JAMES ARNOLD                    Read: NO
Subj: SPINRITE AND THE WD-27X       Status: PUBLIC MESSAGE

Western Digital's User's Guide for the 27x says that to disable sector
translation, close jumper S1-6 and open S1-5 and W-9.

 * QNet 1.03á2: SmartNet: The Tool Shop þ Phoenix AZ <Home of ProDoor>

(H)elp, End of Message Command? t

(Ctrl-K) or (Ctrl-X) Aborts, (Ctrl-S) Suspends.

Scanning HardDisk (1) .

Date: 11-16-88 (02:19)              Number: 1614 (Echo)
  To: SHOEL PERELMAN                Refer#: NONE
From: TONY BOROWIEC                   Read: NO
Subj: SPINRITE AND THE WD-27X       Status: PUBLIC MESSAGE

Shoel,

Try calling Western Digital at 800-847-6181.  They will give you the
info that you need.  However, you'll need Disk Manager or Speedstor to
low level format the drive.  Spinrite won't do it for you.  I
encountered the same problem with my ST-238 and WD1003A-RA2 controller,
but decided not to do it.  I just backup with Fastback Plus more
frequently.

- Tony
---
 * Via Qwikmail 2.02á.  I Love to Fly my Hauppauge 386 on TGIF

 * QNet 1.03á2: The Invention Factory Multi-user BBS, New York, N.Y.


Scanning HardDisk (1) ..

Date: 11-24-88 (08:31)              Number: 1648 (Echo)
  To: SHOEL PERELMAN                Refer#: NONE
From: SYSOP                           Read: NO
Subj: SPINRITE AND THE WD-27X       Status: PUBLIC MESSAGE

Shoel,
Rather than worry about Spinwrite, leave the 27x in the translation mode
if you want it to give you the full capacity of the ST238 drive. 
Your jumper settings should be as follows
      S1-1     S1-2    S1-3    S1-4      Jumpers for:
0     Close    Close   Close   Close    981 Cyl 5 Heads
1     Open     Close   Open    Close    987 Cyl 7 Heads
2     Close    Open    Close   Open     612 Cyl 4 Heads
3*    Open     Open    Open    Open     615 Cyl 4 Heads

      S1-5     S1-6   Jumpers for:
      Close    Close  RLL - 17 Sectors per Track (W9 ON )
      Open*    Close* RLL - 26 Sectors per Track (W9 OFF)
      Close    Open   RLL - 17 Sectors per Track (W9 OFF)
      Open     Open   RLL - 17 Sectors per Track (W9 OFF)
 
W9 controls firmware enabled or disabled. Hope this answers your 
(H)questions about jumpering.
 
---
 * Via ProEdit 2.8á


Scanning HardDisk (1) ....................
Sorry, no mail found to read ...

Message Text Search Terminated ...

Thread Read Terminated ...