PC/XT Switch Settings

Switch Block 1 (FARTHEST FROM POWER SUPPLY)

S1		DISKETTE DRIVE

OFF		(NOT USED)

S2		MATH COPROCESSOR

ON		NO MATH COPROCESSOR
OFF		MATH COPROCESSOR INSTALLED

S3	S4	MEMORY 256K XT		MEMORY 640K XT		PC

OFF	ON	128K INSTALLED		256K INSTALLED		NA
ON	OFF	192K INSTALLED		512K INSTALLED		NA
OFF	OFF	256K INSTALLED		640K INSTALLED		NORMAL - USE SB2

S5	S6	DISPLAY MODE

OFF	ON	CGA 40X25 COLOR
ON	OFF	CGA 80X25 COLOR
OFF	OFF	MDA OR DUAL MONITOR
ON	ON	NO DISPLAY

S7	S8	NUMBER OF FLOPPY DRIVES INSTALLED

ON	ON	1 FLOPPY DRIVE
OFF	ON	2 FLOPPY DRIVES


Switch Block 2 (CLOSEST TO POWER SUPPLY, PC ONLY)

MEMORY INSTALLED

S1	S2	S3	S4	S5	

ON	ON	ON	ON	ON	 64K
ON	OFF	ON	ON	ON	128K
ON	ON	OFF	ON	ON	192K
ON	OFF	OFF	ON	ON	256K
ON	ON	ON	OFF	ON	320K
ON	OFF	ON	OFF	ON	384K
ON	ON	OFF	OFF	ON	448K
ON	OFF	OFF	OFF	ON	512K
ON	ON	ON	ON	OFF	576K
ON	OFF	ON	ON	OFF	640K