INSTRUCTIONS FOR INSTALLING HP LASERJET  PLUS DRIVERS (1-2-3 Rel 2)
       ======================================================

    BEFORE YOU BEGIN:

      -  Download  the   files  HPPLUS.BAT,  LAS11.DRV,   LASR2.DRV  and
         LASR4.DRV using XMODEM protocol.

      -  Run the HPPLUS.BAT file by typing HPPLUS at a DOS prompt in the
         same drive and directory that you've downloaded the above files
         into.  This will rename  LAS11.DRV to HPLAS11.DRV, LASR2.DRV to
         SHP2LASR and LASR4.DRV to SHPLASR.DRV.

    The 3 driver files for using  1-2-3 Release 2 with the Hewlett Packard
    Laserjet PLUS are:

            HPLAS11.DRV,  for text printing
            SHP2LASR.DRV, for printing graphics in low density
            SHP4LASR.DRV, for printing graphics in high density


   To use the Laserjet PLUS drivers, perform the following steps:

    1.  Copy the files HPLAS11.DRV  and SHP2LASR.DRV and SHP4LASR.DRV onto
        your Install  Library Disk or to  the directory on your  hard disk
        where your 1-2-3 files reside.

        For a two-disk system:
        Put  the disk  with  the files  HPLAS11.DRV  and SHP2LASR.DRV  and
        SHP4LASR.DRV in drive A, and your Install Library Disk in drive B.
        At the DOS A prompt, type
        COPY HPLAS11.DRV B: and press RETURN.  Then type
        COPY SHP2LASR.DRV B: and press RETURN.  Then type
        COPY SHP4LASR.DRV B: and press RETURN.

        For a hard-disk system:
        Put  the disk  with  the files  HPLAS11.DRV  AND SHP2LASR.DRV  and
        SHP4LASR.DRV in drive A.  At a DOS A prompt, type
        COPY HPLAS11.DRV C:\pathname and press RETURN.  Then type
        COPY SHP2LASR.DRV C:\pathname and press RETURN.  Then type
        COPY SHP4LASR.DRV C:\pathname and press RETURN.

        For pathname, use the name  of your 1-2-3 directory.  For example,
        if your 1-2-3 files are in a directory called LOTUS, type
        COPY (filename) C:\LOTUS

    2.  Get into the INSTALL program  as described in your Getting Started
        manual.

    3.  Once  in  INSTALL, choose  Advanced  Options,  Add New  Driver  to
        Library.

    4.  Follow  the screen  instructions and  press RETURN  when prompted.
        The HP  2686 Laserjet Plus Drivers  will now be listed  in INSTALL
        when picking Text and Graphics Printers.