ÛÛÛÛÛÛÛÛÛÛ
				   ÛÛÛÛÛÛÛÛÛÛÛÛÛÛ
				  ÛÛÛ ú ÛÛÛÛ ú ÛÛÛ
				   ÛÛÛÛÛÛÛÛÛÛÛÛÛÛ
				   ÛÛÛÛÛÛ  ÛÛÛÛÛÛ
				    ÛÛÛÛÛÛÛÛÛÛÛÛ
				      ÛÛÛÛÛÛÛÛ
				     ÛÛ³³³³³³ÛÛ
				      ÛÛÛÛÛÛÛÛ
				  ÛÛÜ          ÜÛÛ
				   ßÛÛÜ      ÜÛÛß
				     ßÛÛÜ  ÜÛÛß
				       ßÛÛÛÛß
				       ÜÛÛÛÛÜ
				     ÜÛÛß  ßÛÛÜ
				   ÜÛÛß      ßÛÛÜ
				  ÛÛß          ßÛÛ

				   ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿
				   ³ BLACKBEARD ³
				   ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ

			       User Supported Software



				    VERSION LOG
			       BLACKBEARD FORMATTER

	 version  remarks
	 ------------------------------------------------------------------
	 2.4      Added underlining capability feature

	 2.3      C compiler compatible version. 3-87

	 2.2      Latest BB 6.45 distribution version.  2-9-87.
		  Multi-line footer commands

	 2.1      Bold start & end sequences added.

	 2.0      New C Compiler used. Output command added.

	 1.7      Bold function to insert special bold sequences

	 1.6      Require function added to allow merging of files.

	 1.5      Title does not skip spaces when using multi-line titles.

	 1.4      File terminated with FF CR LF

	 1.3      Fixed bug that truncated first line to the length of the
		  title.

	 1.2      Multi-line titles (upto 10)

	 1.1      Added sections and table of contents feature and include
		  file.

	 1.0      First release version of the formatter.


	 INTRODUCTION

	    Printing out documents is an essential associated task of a
	 text processing system. Blackbeard performs the editing tasks
	 very well. An available text formatter/printer was not
	 available. Programs like Microsoft Word (R) are so word
	 processing oriented that simplicity is often compromised. The
	 Blackbeard formatter is a simple to use, do what I tell you, text
	 processor.  It takes any text file and produce a cleaned up
	 printed output.  It is also a powerful formatter for producing
	 technical documents.  A design constraint was that the initial
	 version be compatible with DEC's DSR (R) as much as possible.

	    This manual describes how to use the formatter.

	 RUNNING BLACKBEARD FORMATTER

	    To run Blackbeard formatter type:

	       BBF

	    or

	       BBF {filename}

	    BBF does not include a pop-up directory of files to format
	 yet (available real soon now). BBF will then format your
	 document and write it to the standard output device (the
	 screen). To send the output to the printer run Blackbeard with
	 the command:

	       BBF {filename} >prn

	    This redirects output to the printer. You could also
	 redirect the output to a filename if you want by substituting a
	 filename for prn.

	 The default format is to print 2 blank lines at the top of the
	 page, the filename (used for the title), 2 more blank lines,
	 text lines as they appear in the file (no formatting is done,
	 except for tabs are converted to spaces, fonts are replaced if
	 enabled and spaces are insert if a left margin is used), 2 blank
	 lines, a page number, and a form feed.


	 COMMANDS

	    The nature of the format can be altered by embedding
	 formatter commands (often known as dot commands) in your text.
	 The general format is:

	 .command parameter1 parameter2 text

	 The following is a description of the available commands.

	 .bold c string
	    Sets up a bold charater indicator.  When the bold
	    character is first encountered in the text, all subsequent
	    characters are duplicated and the string is inserted between
	    the duplicated characters until a terminating bold character
	    is encountered.  Example:

	    .bold @ &a+
	    abc@def@ghi

	    formats to:

	    abcd&a+de&a+ef&a+fghi

	 .bs c string
	 .be c string
	    Sets up a bold charater indicator.  When the bold character is
	    first encountered in the text, all subsequent characters are
	    duplicated and the string designated with .bs is inserted
	    between the duplicated characters and the string designated
	    with .be is inserted after the duplicated character until a
	    terminating bold character is encountered.  Example:

	 .bs  &a-67H
	 .be  &a-5H

	 is the sequence to perform bolding on the HP Laserjet+ with the
	 standard 10CPI font. For:

	    XYZ

	    the string:

	    X&a-67HX&a-5HY&a-67HY&a-5HZ&a-67HZ&a-5H

	    is produced.  The HP laserjet+ perform the following
	 operations when receiving this sequence.  An X is printed then
	 the jet is moved "horizontally backward" 67 decipoints (i.e.,
	 just less than the character width of 72 decipoints), the
	 character X is printed again, and the jet is moved "horizontally
	 backward" 5 decipoints, which is the compensation for not having
	 moved back 72 originally.  So the character appears bold having
	 been printed once and the offset printed again.
	    This formatting command can cause your document to become
	 uneditable since lines can get very long.  Essentially each
	 bolded charater becomes equivalent to 15 characters (in this
	 example).  So if you have a line of 20 bolded characters, that
	 line is now 300 characters long! The max line length the
	 Blackbeard formatter can currently accomodate is 4096
	 characters.  So for this example that is a line of 273
	 characters.

	 .dump string
	    Dumps a string to the file designated by the file command.

	 .enable c
	    Set the font character as the character c. For example:

	    .enable 

	 .file filename
	    This command causes the formatter to place all header numbers
	    and titles in the specified file.  This functions as a table
	    of contents.

	 .fm before-title after-title before-footer after-footer
	    Specify the page layout:

	   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
	   ³        before-title            ³
	   ³    Title line                   ³
	   ³       after-title              ³
	   ³    This is a sample text line.  ³
	   ³    This is a sample text line.  ³
	   ³<-> This is a sample text line.  ³
	   ³lm  This is a sample text line.  ³
	   ³    This is a sample text line.  ³
	   ³    This is a sample text line.  ³
	   ³    This is a sample text line.  ³
	   ³    This is a sample text line.  ³
	   ³    This is a sample text line.  ³
	   ³    This is a sample text line.  ³
	   ³    This is a sample text line.  ³
	   ³    This is a sample text line.  ³
	   ³       before-footer            ³
	   ³    Footer line                  ³
	   ³       after-footer             ³
	   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

	   The number of blank spaces at the top and bottom of the text.
	 Default is 2 2 2 2.

	 .fo [n] text
	    Running footer at the bottom of page.  A # in the footer text
	    represents the page number.  Multiple line footers can be
	    designated by preceding the footer with a number between 0 and
	    9.  For example to get a two line footer use the commands:

	    .fo 0 First footer line
	    .fo 1 Second footer line

	    To create a blank header line you must set "display tabs" on
	    in Blackbeard (using the options menu) and put a few spaces
	    after the .fo command. This tells BBF that you still want
	    the header but that it is clear. This anomoly will be
	    changed in version 2.3 when it becomes available.

	 .hl n
	    This is the header level command. It allows you to create
	    relocatable sections and produce automatic numbering like
	    1.2.4.6.

	    Example:

	    .hl 1 Section 1
	    .hl 2 Section 1.1
	    .hl 3 Section 1.1.1
	    .hl 2 Section 1.2
	    .hl 1 Section 2

	 .include filename
	    This will emplace a file -- as is -- in the file you are
	    currently formatting.  This command includes graphics as well
	    as ASCII files.

	 .le
	    This is a list element. It allows you to create a numbered
	    list.

	 .ls
	    List start. Starts (and ends) an itemized list.

	 .lm n
	    Left margin. Default is 0.

	 .nmlv header-level number
	    Reset header level numbering.

	 .nmpg n
	    Reset page number.

	 .output s
	    Outputs the string s without considering it as text. This can
	    be used to reset the printer, e.g., landscape to portrait
	    mode.
	 .pg
	    New page.

	 .ps n
	    Page size with n in lines per page. Default is 66.

	 .req filename
	    This will emplace a file and reformat as required in the file
	    you are currently formatting.  This command can be nested, but
	    only ten files can be required at any one time.

	 .ti [n] text
	    Running title on top of page.  A # in the title text
	    represents the page number.  Multiple line titles can be
	    designated by preceding the title with a number between 0 and
	    9.  For example to get a two line title use the commands:

	    .ti 0 First title line
	    .ti 1 Second title line

	    To create a blank header line you must set "display tabs" on
	    in Blackbeard (using the options menu) and put a few spaces
	    after the .ti command. This tells BBF that you still want
	    the header but that it is clear. This anomoly will be
	    changed in version 2.3 when it becomes available.

	 .ul c string
	    Sets up a underline charater indicator.  When the
	    underline character is first encountered in the text,
	    all subsequent characters are followed by the
	    underline string until a terminating underline
	    character is encountered.  Example:

	    .ul € _
	    abc_def_ghi

	    formats to:

	    abcd_e_f_ghi



	 FONTS

	    The formatter can also perform font translation.  It does
	 this by recognizing font designators in your text file.  A
	 font designator begins with the ASCII font character such as
	  followed by another ASCII character for the font number
	 such as  for the first font.

	    When fonts are enabled (see the .enable command) the font
	 designations are replaced by the escape sequenced required for
	 the printer defined in the Blackbeard font file. When the
	 formatter starts up it looks for a font file. Blackbeard looks
	 in the current subdirectory for a file named BB.FNT.  This file
	 defines the font to escape sequence relationship.  If there is
	 not a file named BB.CFG in the current subdirectory, Blackbeard
	 will look in the DOS environment for the symbol BBFNT, if it is
	 found it will use the filename supplied with the symbol.  This
	 will let you keep one font file and use Blackbeard from any disk
	 or directory.  To set BBFNT place this command or one similar in
	 your autoexec.bat file

		  SET BBFNT=C:\BB.FNT

	 The font file looks like the following:

	 0  18             18       ( normal = 10 CPI)
	 1  27,45,1        27,45,0  ( underline)
	 2  27,69          27,70    ( bold )
	 3  27,69          27,70    ( italic)
	 4  27,69          27,70    ( subscript)
	 5  27,69          27,70    ( superscript)
	 6  15             18       ( compressed)
	 7  14             20       ( double)
	 8  27,58          27,58    ( 12 CPI)

	 The first number is the font number. The second set of numbers
	 define the "ON" sequence for that font number. The third set of
	 numbers define the "OFF" sequence for that font number. The
	 rest of the line is ignored and can be used for comments.
	 A comma separates numbers of a set. Spaces separates sets from sets.

	 To use a font enclose your text between font designators as
	 follows:

	       "127""1"abcdef"127""1"

	    "127" and "1" stand for the ASCII characters 127 and 01.
	 This can be done using the insert special character feature of
	 Blackbeard. When this file is formatted, these font designators
	 will be replaced so they will look like (using the sample font
	 file):

	       "27""45""1"abcdef"27""45""0"

	    There are several font files included on your Blackbeard
	 distribution diskette. The following is a descriptive list of
	 these files.

	 Filename    Description
	 ----------  ----------------------------------------------------
	 TP351.FNT   Fonts for the TOSHIBA P351
	 BB.FNT      The Blackbeard standard font file (÷ TP351.FNT)
	 EMX80.FNT   Epson MX 80 font file