Rapid Contour Plots By Bilinear Patch


     In this technique, the points of the original data array are viewed as
     being samples of a function that is continuous, with piecewise
     continuous partial derivatives.  This function is presumed to be
     bilinear within the squares delineated by the data points.  In order
     to prepare the contour plot of the entire region, we merely prepare a
     contour plot of each square "patch" delineated by four adjacent data
     points.  There is one potential problem with this method, and that is
     if a contour value is exactly equal to one of the data values (one of
     the values exactly on the corner of a patch), then the plot becomes
     ill-conditioned.  In the software example provided, this is readily
     prevented.  The data values take on only integer values, while the
     contour levels are floating point.  We simply prevent any contour
     value from taking on an exact integer value by adding a small number
     (constant called epsilon) if we determine that the contour value is an
     exact integer.

     Once this conditioning problem is resolved, it may readily be seen
     that within a single patch, for a specified contour level, exactly
     three possibilities exist:  no contour line crosses the patch,
     determined if the contour level is either less than the minimum of the
     four corner values or greater than the maximum of the corner values;
     one contour line crosses the patch; or two contour lines cross the
     patch.  In the case where one contour line crosses the patch, the
     bilinear equation is solved for the endpoints of the contour line and
     the line is plotted.  In the case where two contour lines cross the
     patch, we determine the four endpoints, and then must decide which
     pairs of endpoints to match to draw the appropriate contour lines.
     Define the bilinear coefficients for the patch in a coordinate system
     local to the patch, so that the x value ranges from 0 to 1 and the y
     value ranges from 0 to 1, and let the bilinear equation be:

     value(x,y) = ax + by + cxy +d.

     If we now attempt to parametrize the contour line in x in terms of y
     we find:

     x = (value - contour level - by - d)/(a + cy).

     We then see, that because of the nature of the local coordinate
     system, one of the contour lines must have the y value of both of its
     endpoints greater than -a/c, and the other contour line must have both
     of its endpoints less than -a/c.  (It should be noted that because of
     the non-integral nature of the contour level, we cannot have two
     contour lines in a patch when c=0).  This means that if we simply sort
     the four endpoints in increasing value of their y-values, that the two
     endpoints with the lowest y-values form a pair for one contour line
     and the two endpoints with the highest y-values form a pair for the
     other contour line.

     In the software example provided, contour lines are approximated by
     drawing straight lines from one edge of the bilinear patch to the
     other.  In cases where the number of data points are large relative to
     the screen pixel density (say 20 x 20 data points for an EGA display),
     this is adequate for reasonable contour plots.  If the data are









     sparse, it may be desirable to plot the contour line more accurately
     within the patch, using the parametrized equation above.

     The software example provided consists of three modules and one main
     program.  The first module is c_defs.pas and contains the definitions
     used for the contour plotting software, the pointers to the data array
     and the contour level array, and a procedure for allocating memory to
     these arrays.  The data array is called data_array_pointer, which
     points to longint data points, via:  data=data_array_pointer^[x]^[y],
     with 0<=x<max_x_size and 0<=y<max_y_size.  The contour level array
     points to type float (currently set to be single for speed with
     coprocessors), and is accessed via:  contour level = contours^[i],
     with 0<=i<max_contours.  These data arrays are allocated via a call to
     init_array.

     The second module is video.pas and contains the routines necessary for
     manipulating the display.  These procedures are:  init_graphics, which
     loads the BGI driver for the graphics display (this procedure requires
     that the Borland BGI driver file for the display be in the default
     directory); close_graphics, which returns the display to text mode;
     and make_line, which plots a single contour line through a single
     patch.  It should be noted, that as written make_line takes as an
     argument the contour number.  The color of the contour line is
     specified by this contour number, so that on EGA and VGA displays, the
     contour plot is color-coded to make it easier to interpret.

     The third module is contour.pas and contains the routines necessary
     for contour plotting.  The only procedure available for external
     calling is contour_plot, which performs the entire plot function.

     The test program, test.pas, is a skeleton of a general user program
     employing the contour plot modules.  It performs the operations
     minimally necessary for operation.  First, it calls init_array to
     allocate storage.  Then, it fills the data array.  In this example,
     the data array consists of a sum of two two-dimensional Gaussians plus
     noise.  The contour level array is then filled with values (which need
     not be in any particular order).  Init_graphics is called to set the
     display to graphics mode, contour_plot is called to perform the plot,
     and finally close_graphics is called to return the display to text
     mode.

     The test package is compiled using the Borland command-line compiler,
     version 5.0, by:  tpc /B test.pas.  All modules internally use
     compiler options $N+ to compile with IEEE floating point and $E+ to
     include the emulator, so that the test program will exhibit identical
     behavior whether a coprocessor is present or not (except for speed).