!FAST! !FAST! !FAST! !FAST! !FAST! !FAST! !FAST! !FAST! !FAST! !FAST! !FAST!

  File: FastDate.DOC
Author: David N.Dubois
  Date: 1988.04.16

CountDays is a !FAST! routine which tells how many days it has been since a
specific date. It is written in assembly language, and conforms to the far
call conventions of TurboPascal 4.0.

It's somewhat cryptic, and filled with magic numbers, but it is fast.

Here's how it works.

Lines 35 .. 36   Standard procedure prologue for Turbo 4.0

Lines 38 .. 40   Gets the Year. Make sure that it is positive.  Let me
                 explain. The procedure does not work with negative years.
                 There are three reasons for this. First, I figured it was
                 useless, particularly if you consider that the Gregorian
                 calender has only been in effect since 1583. Secondly,
                 signed arithemetic would have slowed the procedure
                 slightly, and I didn't think it was worth it. Thirdly,
                 there is no year 0. Year 1 A.D. was preceded by 1 B.C. So
                 should 1 B.C. be represented by 0 or by -1? It's better to
                 un-ask the question. When a negative, or zero, year is
                 used, the function returns MaxLongInt.

Line  42         Copy Year into BX. Now there are two copies, one in AX and
                 one in BX.

Lines 44 .. 46   Get the Month. Check to see if the month is March or
                 beyond. The idea here, is that you want to count leap days
                 for months after February on a leap year, or months upto
                 February on the year after. Comparing the Month to 3 sets
                 the carry flag if the Month is February or less. Doing an
                 SBB (subtract with carry) will decrement AX if the Month is
                 March or beyond. I will call this value Zeller's Year,
                 since I understand that Mr. Zeller first thought of it.
                 Now we have two different years. The actual year is in BX
                 and Zeller's year is in AX.

Line  47         Store Zeller's year for later.

Lines 48 .. 49   Shifting right twice divides Zeller's year by 4. This tells
                 us how many leap years have passed since the (alledged)
                 year 0.

Lines 51 .. 55   Now we find out how many days have been eaten up by the
                 months that have passed. This uses the DaysIntoYear table
                 shown on line 31. First, we set DI to the position of the
                 table. Actually it is set to 2 bytes before the start of
                 the table. This is because the first month, January, is
                 stored as a 1 rather than 0. Recall that CL contains the
                 month. Its still there after it was loaded in line 44.
                 Since the table is of words, we multiply the Month by two,
                 by shifting left, to find the index into the table. We
                 clear CH (by XORing it with itself) so that now CX contains
                 2*Month. Adding that to the start of the table (less 2)
                 gives us the actual offset of the number we want. The table
                 is stored in the code segment, so we use a segment over-
                 ride when looking up the number. This number is added to
                 AX. So now, AX contains the number of leap days, plus the
                 number of days in the preceding months of this year.

Lines 57 .. 58   Now we add on the days into the month. Recall that CH is
                 still cleared from line 39, so loading CL with the month is
                 like load CX with the month. We add into CX this time. Now
                 CX contains the sum of: the days into the year, plus all
                 the leap days. AX has been freed for other use.

Lines 60 .. 61   Now we ask, how many days have passed since the
                 (hypothetical) year 0, if we count just the normal 365 days
                 per year. Recall that BX contains the actual year that was
                 placed there in line 42. Setting Ax to 365 and MULtiplying
                 leaves the product in the DX:AX pair.

Lines 62 .. 63   We add the value in CX to this. The ADC is necessary since
                 this number will probably be larger than 16-bits.

Lines 65 .. 68   Now we almost have our answer. All we have to do now is
                 take into account those pesky years that are multiples of
                 100. Recall that multiples of 100 are not leap years,
                 except for multiples of 400. This requires a time-consuming
                 division operation, so I wanted to avoid it if possible. I
                 figured that most calls on the function would have years in
                 the 20th and 21st century, and since there were none of
                 these strange leap years during the period 1901 .. 2099, I
                 figured I could skip the division in these years, and make
                 up for it somewhere else.

                 Remember Zeller's Year? That was stored in SI on line 47.
                 These lines check Zeller's Year, skipping to the end
                 (Magic) if the year is in the 20th or 21st century.
                 Otherwise we have to adjust for the 100's.

Lines 70 .. 71   Our answer so far, stored in DX:AX is transferred to CX:DI
                 while we do our division.

Lines 72 .. 73   We are going to divide Zeller's Year by 100. We transfer
                 the year, in SI, to the DX:AX pair. DX will always be zero.

Lines 74 .. 76   Divide Zeller's Year by 100. This will give us the number
                 of multiples of 100 that we have already counted as leap
                 years, even though they may not be. This is stored in BX
                 while we make a final adjustment.

Lines 77 .. 78   By dividing that number by 4 (by shifting twice), we find
                 out how many years have been multiples of 400.

Lines 79         Adding 15 takes into account the fact that we are ignoring
                 years in the range of 1901 .. 2099. Had we done this
                 calcualtion for those years, we would have ended up
                 subtracting 15, so instead we add 15 here.

Line  80 .. 81   By adding the multiples of 400, and subtracting the
                 multiples of 100, we have adjusted for the strange leap
                 years. CWD quickly clears out DX for next operation.

Line  82 .. 83   Recall that the original un-adjusted count was stored
                 temporarily in CX:DI in lines 70 and 71. Now we add that
                 onto the adjustment, leaving the result back in DX:AX.

Line  84         Merge back into the main stream.

Lines 86 .. 88   As I explained above, I didn't want to handle negative
                 years. If Year is less than or equal to zero, the function
                 returns MaxLongInt.

Lines 90 .. 91   These lines add on a magic number. I'm going to keep the
                 ORIGIN of this number secret.

Lines 93 .. 94   Result of function is stored in DX:AX. These lines are the
                 standard post-logue for the Pascal calling sequence.