Fast Fourier Transform
                               
                               by
                        Michael F.Griffin

             Childrens Hospital Research Foundation
                     Division of Cardiology
                Biomedical Engineering Laboratory
                     Elland & Bethesda Aves
                      Cincinnati,Ohio 45229


     


     The Fast Fourier Transform (FFT) is a computationally efficient 
algorithm  to compute the discrete fourier transform.  
     
     There  are two methods that are commonly used to compute the 
FFT:  Decimation in Time and Decimation in Frequency.  The author 
chooses to use the decimation in time.

     The FFT programs written by the author assume that the  user 
has some background knowledge.  

     The FFT programs require that the number of data points be a 
power  of two.  Some modifications would be needed to transform a 
length  other than a power of two.  Please contact the author  if 
you are interested in the modifications.

     If  you are using real data the computational efficiency can 
be further improved by modifying the transform to remove some  of 
statements referring to the imaginary portion of the input.

 
     
        List of some Fourier Analysis Programs available
        ------------------------------------------------

FFT.PAS        - Turbo Pascal version of a complete FFT program
                 with data input from files and data output to 
                 either files or printer.
                 The program works but could use a little work
                 on the input and output sections.
                 It does not know if an output file already 
                 exists and could write over another data file.

FFT.COM        - Compiled version of the above.

PROCFFT.PAS    - Turbo Pascal FFT 'procedure'. 

FFT.EXE        - Compiled Basica FFT.

FFT.BAS        - Source code for FFT.EXE.

DFT.EXE        - Discrete Fourier Transform - Compiled Basica

DFT.BAS        - Source code for DFT.EXE


Data gathering for the Turbo Pascal FFT's

GETDATA.PAS     - Crude program to enter complex data into a 
                  random access file.  This program was written 
                  to enter test data. Although it is crude, it
                  works. In most cases the data will be gathered 
                  from a source and dumped into a random access 
                  file  that  can  be read  by  the  program.  If 
                  entering  data by hand is  desired,  this  file 
                  needs   to  be  modified  so  that  an  editing 
                  capability is added.


     Hopefully,  the author will find time to modify some of  the 
problems mentioned above.   If not,  you are more than welcome to 
modify  them yourselves.   If you do modify the programs,  please 
download them to the Biomedical Engineering RBBS.


                  List of some future programs
                  ----------------------------

Chirp  Z Transform   - Evaluating the Fourier Transform  along  a 
                       different contour.

Two Dimensional FFT  - FFT for image data.

Complex Cepstrum     - Log Spectrum.


     Please send any corrections,  modifications, suggestions, or 
ideas  to the address listed or leave a message on the RBBS.   If 
you  are having any problems,  feel free to call between 9am  and 
6pm on weekdays.

Biomedical Engineering RBBS
---------------------------
data/voice: 513-559-8599
RBBS hours: 1800-0900 weekdays
          : 24 hours weekends
          : Eastern Standard Time