Chirp Z-Transform

                               by
                   Phuong Tran & Mike Griffin

             Children's Hospital Research Foundation
                     Division of Cardiology
                Biomedical Engineering Laboratory
                     Elland & Bethesda Aves
                      Cincinnati,Ohio 45229






	The  Chirp  Z-Transform  is a  computationally  efficient 
algorithm  to compute the z Transform along a spiral  contour  in 
the z domain.  If the contour is the unit circle, then this would 
be  equivalent  to  computing the Fast Fourier  Transform  but  a 
little slower. 



System requirements: 

        IBM-PC w/128k
        8087 coprocessor	
        Hercules Mono Graphics Board

Program Requirements:

 	This  program  requires the following files to reside  on 
the same disk as the program:

	4x6.fon
	error.msg

Program  Description:
	
	The  program allows inputs from either the keyboard or  a 
sequential  data  file  (data is assumed to have  both  real  and 
imaginary parts).  If a file is specified,  it must have a '.DAT' 
extension.

	The output can be routed to a file,printer or screen.  If 
the  printer  or  screen  is  specified,  the  data  points  will 
be printed from left to right. If a file is specified, it will be
stored on a disk file with a '.DAT' extension.

	Regardless  of output routing,  the magnitude  and  phase 
will be plotted on the screen.

	The phase output is plotted from pi/2 to -pi/2.




	The input parameters are as follows:

     1. Number of complex paired input points 
     2. Number of complex paired output points 
     3. Sample rate of the data in Hertz
     4. Initial Sigma value of CZT contour in Hertz
     5. Initial Omega value of CZT contour in Hertz
     6. Increment in Sigma along the CZT contour in Hertz
     7. Increment in Omega along the CZT contour in Hertz


Files:

	The following files are included in this library:

	CHIRPZ.COM     -  program
	4X6.FON        -  required for graphics
	ERROR.MSG      -  required for graphics 
	CHIRPZ.DOC     -  this file
        PROCWRIT.PAS   -  procedure to write data into a file

       A version for the color monitor is also available.

              Source code is available on request.

References:

	1. Programs for Digital Signal Processing
	   IEEE Press, 1979

	2. Theory & Application of Digital Signal Processing
	   L.R.Rabiner,B.Gold,Prentice Hall,1975

     Please  send  any  problems,suggestions,  or  ideas  to  the 
address listed or leave a message on our RBBS. If your having any 
problems and would like to contact us, feel free to call from 9am 
to 6pm on weekdays.

Biomedical Engineering RBBS
---------------------------
data/voice: 513-559-8599
RBBS hours: 1800-0900 weekdays
          : 24 hours weekends
          : EST 

4/26/85