9













9                               _P_T_C _i_m_p_l_e_m_e_n_t_a_t_i_o_n _n_o_t_e

                                         by

                                    Per Bergsten

                               Holistic Technology AB
                                   Grona Gatan 59
                                  414 54 Gothenburg
                                       Sweden













          This note describes the implementation of  ptc,  a  Pascal  to  C
          translator.   The program was developed by Per Bergsten of Holis-
          tic Technology AB, Gothenburg, Sweden.  The paper is intended  to
          provide  a  guide  for  those  who need to transport ptc to a new
          environment, it describes how Pascal constructs are mapped onto C
          constructs.



















9



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          _1.  _B_a_c_k_g_r_o_u_n_d

          The aim was originally to provide a simple tool for  transporting
          finished  applications  to systems lacking Pascal compilers.  The
          first versions,  constructed  in  about  1984,  were  capable  of
          translating  simple  Pascal  programs.   It was never intended to
          become a released product, however, as time went by, programs and
          ambitions grew to the point where nearly the full Pascal language
          was supported.  Thus the program as it stands today  has  a  long
          ancestry  but  it has never been redesigned (which it should have
          been).

          _2.  _P_a_s_c_a_l _v_s _C

          To anyone familiar with the two languages it is obvious that they
          are very similar in structure.  The major features may be summar-
          ised as follows:

                     Pascal                            C

          Block-structured                Block-structured
          - multiple declaration levels   - single declaration level
          Statically scoped               Statically scoped
          Strongly typed                  Weakly typed
                                          - allows unbounded pointers
          Call by value                   Mostly call by value
          - and call by reference
          Highly independent              Highly integrated
          - of host system                - with system
          Self contained                  Allows external definitions.


          On the syntactic level the languages differ only in  minor  ways,
          mostly  in  the  order in which keywords and other symbols occur,
          and of course in that the languages uses  different  symbols  for
          the  same  purposes.   The  only complication is that C prohibits
          nested subroutine declarations.

          On the semantic level the situation is worse.  C  has  the  pecu-
          liarity  that  array variables are treated differently from other
          variables, this forces us to adopt some  general  way  to  handle
          array variables.  Furthermore, since Pascal offers nested subrou-
          tine declarations it becomes necessary to simulate  part  of  the
          activation  record  mechanism in the translated code, in one case
          it is extremely difficult to completely  do  this.   It  is  also
          clear  that  the  C  typedef mechanism has some shortcomings that
          preclude an easy translation of Pascal types.











9



9                                        - 1 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          _3.  _M_a_p_p_i_n_g _P_a_s_c_a_l _t_o _C

          In this part of the paper we briefly illustrate how to  translate
          Pascal code into equivalent C code.

          _3._1.  _P_r_o_g_r_a_m_s

          A minimal Pascal program:

                  program p;
                  begin
                  end.

          translates to the C equivalent:

                  extern void exit();
                  main()
                  {
                          exit(0);
                  }


          It should be noted here that the  translator  does  not  actually
          require  a  complete  Pascal  program, the implementation is such
          that any consistent set of declarations can be translated.

          _3._2.  _L_e_x_i_c_a_l _i_s_s_u_e_s

          The C language uses ASCII as a carrier, almost all of the availi-
          ble  characters  are  used.  The Pascal definition uses a smaller
          set of characters.  Since few features of the languages depend on
          the  underlying character set this does not introduce much diffi-
          culties.

          One serious problem does occur.  Both language definitions states
          that  comments have no meaning and no clear place in the language
          syntax.  Furthermore, the Pascal definition states that a comment
          is  equivalent  to  a blank character.  This implies that if com-
          ments are handled accurately the translator should also  be  able
          to  collect and classify each blank character in a Pascal program
          and to generate a C program with the same number of blank charac-
          ters  in the corresponding positions.  This implication conflicts
          with the fact that the languages have different syntax rules,  it
          is not obvious what the "corresponding positions" would be.

          Since comments have no defined meaning a user is free  to  inter-
          pret  them  in any way and, in particular, to associate them with
          the surrounding code in any way s/he  chooses.   Although  humans
          usually are able to deduce what bearing a comment has on the sur-
          rounding program code there are no formal rules  for  how  to  do
          this.   Therefore  there  is no _a _p_r_i_o_r_i correct way to translate
          comments and the translator described here ignores comments alto-
          gether.   If/when  a  reasonable  _a_d  _h_o_c  solution is found that
          feature may be incorporated.

          _3._3.  _D_e_c_l_a_r_a_t_i_o_n_s

          The program may introduce local declarations which are handled as
          follows.




                                        - 2 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          _3._3._1.  _L_a_b_e_l_s


                  program p;

                  label 9;

                  begin
                  9:
                          goto 9
                  end.

          which we simply translate into:

                  extern void exit();
                  main()
                  {
                  L9:
                          goto L9;
                          exit(0);
                  }


          If the label is reached from an inner procedure:

                  program p;

                  label 100;

                          procedure q;

                          begin
                                  goto 100
                          end;

                  begin
                  100:
                  end.

          a more complicated translation must be used:


















9



9                                        - 3 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9
                  # define Line __LINE__
                  void Caseerror();
                  # include <setjmp.h>
                  static struct Jb { jmp_buf jb; } J[1];

                   void
                  q()
                  {
                          longjmp(J[0].jb, 100);
                  }

                  main()
                  {
                          if (setjmp(J[0].jb))
                                  goto L100;
                  L100:
                          exit(0);
                  }


          We assume the existence of the standard  _s_e_t_j_m_p()  and  _l_o_n_g_j_m_p()
          library  functions.   Jumpbuffers  are  statically  allocated  as
          needed depending on the number of declarationlevels in  the  pro-
          gram.

          _3._3._2.  _C_o_n_s_t_a_n_t_s

          Constant declarations are treated in two different ways.  Numbers
          aliases  etc  are simply # _d_e_f_i_n_e'd but string constants are con-
          verted to static character arrays in order to  avoid  unnecessary
          duplication of string-constants in the object code, thus:

                  const
                     p  = 3.14;
                     pie   = '3.14';

          translates to:

                  # define pi 3.14
                  static char pie[] = "3.14";


          _3._3._3.  _T_y_p_e_s _a_n_d _v_a_r_i_a_b_l_e_s

          Types and variables are mostly easy to translate:












9



9                                        - 4 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9
                  program p;

                  const length   = 15;

                  type
                     struct      = 0 .. length;
                     vect     = array [ struct ] of struct;
                     color    = (red, blue, ada, yellow);
                     pointer  = ^ recd;
                     recd     = record
                              r  : pointer;
                              case b : boolean of
                                false: (c : color);
                                true:  (v : vect);
                             end;

                  var   SP    : pointer;

                  begin
                     new(SP, true);
                  end.

          becomes

                  typedef char    boolean;
                  # define false (boolean)0
                  # define true (boolean)1
                  extern char *Bools[];
                  # define Unionoffs(p, m) (((long)(&(p)->m))-((long)(p)))
                  extern char *malloc();
                  # define length 15
                  typedef unsigned char C47_struct;
                  typedef struct { C47_struct A[length + 1]; } vect;
                  typedef enum { red, blue, ada, yellow } color;
                  typedef struct S57 *pointer;
                  typedef struct S57 {
                     pointer  r;
                     boolean  b;
                     union {
                        struct {
                           color    c;
                        } V1;
                        struct  {
                           vect  v;
                        } V2;
                     } U;
                  }  recd;
                  pointer  sp;

                  main()
                  {
                     sp = (struct S57 *)malloc((unsigned)
                        (Unionoffs(sp, U.V2.v) + sizeof(sp->U.V2)));
                     exit(0);
                  }

          The rationale is as follows:
9



9                                        - 5 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          Identifiers in the Pascal program which conflicts  with  reserved
          words  in  C are renamed by adding a unique prefix Cnnn where nnn
          is a number.

          We also note here that uppercase letters in identifiers and  key-
          words   are  translated  to  lowercase.   Pascal  specifies  that
          upper/lower case is insignificant whereas  C  (for  the  present)
          separates  the two.  This fact is used to advantage by the trans-
          lator as all subroutines and macros  defined  by  the  translator
          have an initial uppercase letter which prevents confusion.

          -    The type _b_o_o_l_e_a_n is a predefined Pascal  type,  when  it  is
               used  the  translator emits code which defines boolean to be
               the smallest convenient type: _c_h_a_r.  The constants _f_a_l_s_e and
               _t_r_u_e  are  defined  and  the vector _B_o_o_l_s will contain text-
               strings for output if needed.

          -    The predefined types _i_n_t_e_g_e_r and _r_e_a_l  are  likewise  mapped
               directly  onto the standard C types _i_n_t and _d_o_u_b_l_e through a
               typedef declaration.

               Integer subranges are  mapped  onto  standard  C  arithmetic
               types  according  to  a  short table in the translator.  The
               table is scanned from top to bottom until an enclosing range
               is found and the corresponding type-name is emitted.

          -    C-arrays have peculiar semantix.  To unify the treatment  of
               arrays and other datatypes we always encapsulate an array in
               a struct, thus an array always becomes a _s_t_r_u_c_t with a  sin-
               gle member named A.

          -    Records and their variants are translated into C _s_t_r_u_c_t  and
               _u_n_i_o_n  definitions.   Since  C requires all union members to
               have a name we must supply artificial names for  all  record
               variants.  A record with variants will therefore always con-
               tain one field with the name U which have  sub-fields  named
               Vnnn where nnn is a positive number.

               When allocating dynamic storage for a record  with  variants
               naming the desired variant

                       new(sp, true)

               we face the problem of  determining  the  amount  of  memory
               needed.

               _C _d_o_e_s _n_o_t _p_r_o_v_i_d_e _a _s_a_f_e _w_a_y _t_o _c_o_m_p_u_t_e _t_h_e _s_i_z_e _o_f  _a
               _p_a_r_t_i_c_u_l_a_r _s_t_r_u_c_t _v_a_r_i_a_n_t.

               The strategy adopted to cope with this problem is to attempt
               to compute the offset of a fieldmember in the variant match-
               ing the constant and then to add the size  of  the  variant.
               The  offset  computation is expressed as a macro, _U_n_i_o_n_o_f_f_s,
               which uses rather foul typecasting  to  achive  the  result.
               The only availible alternative would be to use the same size
               of all variants.  This  method,  while  being  safe,  wastes
               memory  when  many  small  and few large records of the same
               type are created dynamically.
9



9                                        - 6 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          -    Pascal enumeration types are converted directly  to  C  _e_n_u_m
               types.

          -    Pascal pointer types are translated into  C  pointer  types.
               Pascal allows the programmer to construct recursive types as
               pointer types need not be fully defined until the end of the
               declaration-section  where  the  pointer  type  is used.  In
               practice this is only used to introduce record  types  which
               contain  pointers  to themselves.  This problem is partially
               solved by introducing a name for the record type.  Hence

                       type
                          ptr   = ^ node;
                          node  = record
                                next  : ptr;
                                info  : integer
                               end;

               becomes

                       typedef struct S56 * ptr;
                       typedef struct S56 {
                          ptr      next;
                          integer     info;
                       } node;

               we note in passing that the  problem  cannot  be  completely
               solved since

                       type  pureptr  = ^ pureptr;

               which is valid Pascal, cannot be expressed in C.

          -    A pascal set-type does not have any direct counterpart in C.
               The C language does however have a adequate set of operators
               for bit manipulation.  We use these to  implement  a  Pascal
               set as an array of _s_e_t_w_o_r_d.  So:

                       type
                          s  = set of 1 .. 100;

                       var
                          ss : s;

               is translated into:

                       typedef unsigned short setword;
                       typedef struct { setword S[8]; } s;

                       s  ss;

               The situation is slightly complicated by the fact that  Pas-
               cal  has a set constructor which permits the construction of
               arbitrary large sets, for example:

                       s := [ 50 .. maxint ] * [ 1 .. 80 ]

               for that reason the first member in the array of words gives
               size  of  the  set  (in words).  In the example above s.S[0]




                                        - 7 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9               would have the value 7, and s.S[1] through s.S[7] would hold
               the  bits.   The number 7 is computed on the assumption that
               the type _u_n_s_i_g_n_e_d _s_h_o_r_t on the target host  is  sufficiently
               large  to  holds  16  bits.  The set operators of Pascal are
               implemented as C functions returning pointers to  arrays  of
               setwords, the intermediary results are held in a static area
               of fixed size.

          -    Pascal files are implemented using the standard i/o  package
               availible  in  most C implementations.  Since Pascal has the
               requirement that the next element of a file  is  visible  in
               the  filebuffer  before it is read, and the requirement that
               linemarkers in textfiles are given special treatement we are
               forced  to  extend  the  _F_I_L_E  type  provided  in <_s_t_d_i_o._h>.
               Hence:

                       var   f  : text;

               becomes

                       typedef struct {
                          FILE  *fp;
                          unsigned short
                                eoln:1,
                                eof:1,
                                init:1,
                                out:1,
                                :12;
                          char  buf;
                       }  text;
                       text  f;

               where _b_u_f is our filebuffer and _e_o_l_n, _e_o_f and _i_n_i_t are flags
               giving the state of the file.  All Pascal i/o operations are
               implemented using macros that maintain  the  flags  and  the
               buffer  variable.  The actual reading and writing of data is
               deferred to the standard i/o package.

          _3._3._4.  _P_r_o_c_e_d_u_r_e_s _a_n_d _f_u_n_c_t_i_o_n_s

          Pascal  procedures  and  functions  are  somewhat  difficult   to
          translate to C.  The main problems lie in nested declarations and
          procedural parameters.  Nested declarations are  handled  in  the
          following manner:

               -    If procedure B is declared in procedure  A,  then  pro-
                    cedure  B is emitted before A and A is forward declared
                    before B.

               -    Any constants and types declared in A is moved  to  the
                    global scope, this may force renaming of those objects.

               -    Any variable declared in A _a_n_d _u_s_e_d _i_n _B  is  converted
                    to  a  pointer  and  moved  to  the  global scope.  The
                    pointer value is saved  and  re-initialized  upon  each
                    entry of A and restored upon exit from A.


9



9                                        - 8 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          Hence:

                  procedure A;

                  const limit = 20;

                  type  loctyp   = 0 .. limit;

                  var   i, j  : loctyp;

                     procedure B(k : loctyp);

                     begin
                        j := k + 2
                     end;

                  begin
                     B(i)
                  end;

          becomes

                  typedef unsigned char   loctyp;
                  loctyp   *G56_j;

                  void a();

                   void
                  b(k)
                     loctyp  k;
                  {
                     (*G56_j) = k + 2;
                  }

                   void
                  a()
                  {
                  # define limit 20
                     loctyp  i, j;
                     loctyp  *F57;

                     F57 = G56_j;
                     G56_j = &j;
                     b(i);
                     G56_j = F57;
                  }

          we see that references to _j inside procedure _b  are  replaced  by
          the  pointer  _G_5_6__j  which points to the local variable _j in pro-
          cedure _a.  In order to preserve the proper semantix in  the  face
          of  recursion  the value of the pointer need also be saved in the
          local variable _F_5_7 during the invocation of _a.

          -    Procedure parameters offer little  problems.   We  translate
               Pascal  value-parameters into ordinary C parameters and Pas-
               cal var-parameters are treated as pointers.


9



9                                        - 9 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          -    Procedural parameters appear at first to be easy to  handle.
               The ordinary program:

                       program p;

                       procedure pp(procedure q(i : integer));

                       begin
                          q(2)
                       end;

                       procedure qq(i : integer);
                       begin
                       end;

                       begin
                          pp(qq)
                       end.

               becomes

                       extern void exit();
                       typedef int integer;

                        void
                       pp(q)
                          void  (*q)();
                       {
                          (*q)(2);
                       }

                        void
                       qq(i)
                          integer i;
                       {
                       }

                       main()
                       {
                          pp(qq);
                          exit(0);
                       }

               which looks simple enough.
               However, Pascal requires  that  the  scope  of  a  procedure













9



9                                       - 10 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9               _r_e_m_a_i_n_s _u_n_c_h_a_n_g_e_d throughout its lifetime.  Consider:

                       program demo(output);

                       var   i  : integer;

                          procedure p(procedure q);

                          var   j  : integer;

                             procedure qq;

                             begin
                                writeln(j)
                             end;

                          begin
                             j := i;
                             q;
                             if i < 1 then
                               begin
                                i := i + 1;
                                p(qq)
                               end
                          end;

                          procedure dummy;
                          begin
                          end;

                       begin
                          i := 0;
                          p(dummy)
                       end.

               When _p is first invoked it assigns the local variable _j  the
               value  0.   This  variable  is  accessible  from _q_q which is
               passed as a parameter in  the  recursive  call  of  _p.   The
               second  invocation  of  _p then sets _i_t_s variable _j to 1, and
               calls _q which is bound to the  first  instance  of  _q_q,  and
               should  therefore  print the number _0.  _S_a_d_l_y, _t_h_e _c_o_d_e _p_r_o_-
               _d_u_c_e_d _b_y _t_h_e _t_r_a_n_s_l_a_t_o_r _f_a_i_l_s _t_o _d_o  _t_h_i_s.   It  is  obvious
               that  the  program  above calls for a complete simulation of
               the activation record mechanism of Pascal to work correctly.

               A workable but unpractical solution would be:

               1)   When qq is used as parameter  we  call  a  function  q1
                    which saves the environment for qq (i.e. the address of
                    j) in a well known place and returns a pointer to q2.

               2)   When qq is later called (under the name q)  the  actual
                    target  will be q2 which sets up the proper environment
                    calls qq.

               The problem is that this requires a save-area for _e_a_c_h  pro-
               cedural parameter which can hold the intresting parts of its
               environment for _e_a_c_h of its  invocations.   In  the  example
               above  we need one are which holds the address of i for each




                                       - 11 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9               instance of qq (say N instances,  where  N  depends  on  the
               run-time  behaviour  of  p).  It also requires a set of dif-
               ferent procedures to perform the work  of  q2  (N  different
               procedures   which   sets  up  the  environment  for  the  N
               instances).  _T_h_i_s _r_e_q_u_i_r_e_s _m_u_c_h _t_o _m_u_c_h _w_o_r_k _t_o _i_m_p_l_e_m_e_n_t _s_o
               _t_h_e  _p_r_o_b_l_e_m  _i_s  _l_e_f_t _u_n_s_o_l_v_e_d, this is hardly a problem in
               practice since humans rarely write such code  but  _i_t  _c_o_u_l_d
               _i_n_t_r_o_d_u_c_e _p_r_o_b_l_e_m_s in machine generated Pascal code.

               It should be noted that the translator accepts  the  keyword
               _e_x_t_e_r_n_a_l  in  place  of  the  Pascal  _f_o_r_w_a_r_d  directive and
               assumes that the so declared procedure is defined elsewhere.














































9



9                                       - 12 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          _3._4.  _S_t_a_t_e_m_e_n_t_s.

          Pascal statements are comparatively easy to translate to C.   The
          only parts that require special care are non-local _g_o_t_o, _w_i_t_h and
          _f_o_r statements.  The code

                  program p(output);

                  type
                     msgtyp   = packed array [ 1 .. 12 ] of char;

                  var
                     a  : array [ 1 .. 10 ] of
                           record
                              r  : real
                           end;
                     i  : integer;
                     ok : boolean;

                     procedure fatal(m : msgtyp);

                     begin
                        writeln('Fatal error: ', m)
                     end;

                  begin
                     while true do
                       repeat
                        ok := false;
                        i := 1;
                        for i := i + 1 to i + 10 do
                           if i > 10 then
                              fatal(' 10 exceeded')
                           else
                             with a[i] do
                              if r > 9.99e+38 then
                                 ok := true
                              else
                                 writeln(r)
                       until ok
                  end.

















9



9                                       - 13 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          becomes

                  typedef char boolean;
                  # define false (boolean)0
                  # define true (boolean)1
                  typedef int integer;
                  typedef double real;

                  typedef struct { char A[12 - 1 + 1]; } msgtyp;
                  typedef struct { struct S57 {
                     real  r;
                  }  A[10 - 1 + 1]; }  T56;
                  T56      a;
                  integer  i;
                  boolean  done;

                   void
                  fatal(m)
                     msgtyp   m;
                  {
                     (void)fprintf(output.fp, "Fatal error: %.12s", m.A),
                                 Putchr('\n', output);
                  }

                  main()
                  {
                     while (true)
                       do {
                        done = false;
                        i = 1;
                        {
                          integer      B1 = i + 1, B2 = i + 10;

                          if (B1 <= B2)
                           for (i = B1; ; i++) {
                              if (i > 10)
                                 fatal(*((msgtyp *)" 10 exceeded"));
                              else {
                                 register struct   S57 *W3 = &a.A[i - 1];

                                 if (W3->r > 9.99e+38)
                                    done = true;
                                 else
                                    (void)fprintf(output.fp, "% 20e", W3->r),
                                       Putchr('\n', output);
                              }
                              if (i == B2) break;
                           }
                        }
                       } while (!(done));
                     exit(0);
                  }

          for the following reasons:

          _3._4._1.  _B_e_g_i_n

          The compound statements are very similar in the two languages and
          need no further explanation.




                                       - 14 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          _3._4._2.  _I_f

          Pascal if-statements have the same structure and  semantix  as  C
          if-statments.

          _3._4._3.  _C_a_s_e

          Pascal case-statements have the same structure and semantix as  C
          switch-statements  provided  that a _b_r_e_a_k is always added to each
          entry.

          The translator supports a common  Pascal  extension  in  that  it
          recognizes  the keyword _o_t_h_e_r_w_i_s_e to signify a default entry in a
          case-statement.

          _3._4._4.  _L_a_b_e_l_s

          Pascal labeled statements and labels have the same structure  and
          semantix  as  C  labeled statements except that Pascal labels are
          numbers where C labels are identifiers, this difference is solved
          by simply prefixing the labels with the letter _L.

          _3._4._5.  _G_o_t_o

          Pascal goto-statements have the same structure as C  goto  state-
          ments  but  the  semantix  differ in that Pascal allows a goto to
          lead out of the current procedure.  This is implemented using the
          _s_e_t_j_m_p/_l_o_n_g_j_m_p library functions of C as described earlier.

          _3._4._6.  _W_i_t_h

          The with-statement of Pascal has no  counterpart  in  C.   It  is
          translated into nested compund statements where pointervariables,
          referencing the corresponding records, are declared and  initial-
          ized.   Within  the  scope  of the with-statement, the accessible
          record fields are renamed to include the pointer.  The effect  of
          this  is  that the record address is evaluated once as the Pascal
          standard requires.

          _3._4._7.  _F_o_r

          The for-statement of Pascal has a structure that  is  similar  to
          the  C  for-statement but the semantix differ completely.  Pascal
          requires that a loop be exited when  the  upper  bound  has  been
          reached,   Pascal  also  requires  that  the  loop-boundaries  be
          evaluated exactly once.  The standard C for-loop is  exited  when
          the  loop-condition  becomes  false.  This implies that it is not
          always true that

                  for (i = 0; i <= e; i++) ;

          behaves in the same manner as

                  for i := 0 to e do ;

          since (in most implementations) the C version becomes an infinite
          loop  if  _e  equals _m_a_x_i_n_t or if _e is the expression _i.  For that
          reason Pascal for-statments are translated into  compound  state-
          ments  where  the  upper/lower bounds of the for-loop are held in




                                       - 15 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          local variables.  It is  also  necessary  to  add  a  conditional
          break-statement at the end of the loop.  It is possible to obtain
          the  more  relaxed  translation  by  configuring  the  translator
          appropriately (see "Tuning" below).

          _3._4._8.  _W_h_i_l_e

          The while-statement behaves exactly the same in both languages.

          _3._4._9.  _R_e_p_e_a_t

          The repeat-statement of Pascal matches the do-while statement  of
          C  except  for  the  trivial  difference  that  Pascal  permits a
          statement-list where C permits a single statment in the loop.

          _3._4._1_0.  _E_m_p_t_y

          The empty statement has (of course) the same structure and seman-
          tix in both languages.

          _3._5.  _E_x_p_r_e_s_s_i_o_n_s _a_n_d _a_s_s_i_g_n_m_e_n_t_s

          In most cases Pascal expressions can be literally translated into
          equivalent C expressions.

          identifiers    Except where identifiers clash with reserved words
                         or  with  other  identifiers  declared in the same
                         scope, they may simply be printed.  In some  cases
                         the  translator is forced to rename identifiers or
                         to invent new identifiers.

          operators      The operators +, -, * _d_i_v and _m_o_d when applied  to
                         real  or  integer operands have exact counterparts
                         in C and are therefore easy to handle.  The opera-
                         tor  for real division, /, corresponds to the same
                         C  operator  except  that  the  operands  may   be
                         integers.  In that case a cast is necessary.  When
                         the operands are sets the expression is  converted
                         into a function call.

                         The operators <, <=, >, >=,  =  and  <>  all  have
                         exact  counterparts  in  C  for  integer  and real
                         operands.  Most C implementations  disallows  _e_n_u_m
                         operands,  the  translator  therefore  casts  such
                         operands to _i_n_t.  Comparisons on structures  (i.e.
                         strings  or  sets)  are  converted  into  function
                         calls.

          assignments    Assignments are straightforward  to  handle  since
                         arrays are encapsulated in structures.  Therefore:

                                 a := b

                         becomes

                                 a = b

                         _u_n_l_e_s_s b is a string or a set, in which  case  the
                         assignment is converted into a function call.




                                       - 16 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          indexing       Given  the  translation  for  array   declarations
                         (described above) we are forced to translate

                                 a[i]

                         into

                                 a.A[i - c]

                         where _c is the lower bound for the index type.

          selection      Given the translation for  records  with  variants
                         (described above) the translation of

                                 a.b

                         becomes

                                 a.b

                         _o_r, if b is declared in a variant,

                                 a.Vxxx.b

                         where Vxxx is a name manufactured by the  transla-
                         tor for the particular variant.

          dereferencing  Pointer references and _v_a_r-parameters are  handled
                         by  prefixing the expression with an asterisk, but
                         the special case dereferencing followed by  selec-
                         tion is also recognized, so:

                                 p^ := q^.f

                         becomes

                                 *p = q->f


          miscellanea    The boolean operators _a_n_d, _o_r and _n_o_t  are  simply
                         translated  into  their  C  counterparts.  The set
                         contructors [], and ..  and the  operator  _i_n  are
                         converted to function calls.















9



9                                       - 17 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          _4.  _I_m_p_l_e_m_e_n_t_a_t_i_o_n

          The general strategy is to convert the Pascal source program into
          a  parsetree.   The tree is then traversed by a set of procedures
          that perform some necessary transformations.  The tree is finally
          traversed  by  a set of procedures that print the corresponding C
          constructs.  The translator consists of  three  major  procedures
          that  perform these actions.  They are augmented by a set of pro-
          cedures that maintain a symbol table that holds information about
          identifiers found in the source, and by a procedure that initial-
          izes all internal datastructures.

          There are three major datastructures that interact in complicated
          ways:

          1)   a store for identifiers and strings

          2)   a multilevel symbol table

          3)   a parse-tree.

          The identifier and string store, _s_t_r_s_t_o_r is in principle an array
          of  characters  that  grow  in  increments  of  one string block.
          Exactly one copy of each identifier  is  stored  in  that  array.
          Whenever  an identifier is found in the input stream the array is
          scanned to see if that identifier has been seen before.  In order
          to  speed  up the search all identifiers are represented by nodes
          which are chained together such that all nodes  in  a  particular
          chain have the same hashvalue as determined by the function _h_a_s_h.
          Each _i_d_n_o_d_e holds an index to  strstor  where  the  corresponding
          identifier text is stored.  The start of the hashchains are found
          in the global variable _i_d_t_a_b.

          idtab
          +----+
          |  |  chain of idnodes with same hashvalue
          +----+  +--------+  +--------+
          |  |----->|     |----->|     |idnode representing
          +----+  |     |   index=2|     |identifier "demo"
          |  |  +--------+  +--------+

             strstor
          +------------ - --------+
          |  |  |     |  |
          +------------ - --------+|
            |

          +--------------------------------
          |  |  |d |e |m |o |/ |
          +--------------------------------   first idblock
                 |^
                index=2


          So: the global representation of the identifier "demo" is a  par-
          ticlular idnode; whenever the lexical analysis routine recognizes
          the identifier "demo" it returns a pointer to that idnode.

9



9                                       - 18 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          In order to represent different identifiers with the same name we
          need  to  be  able to distinguish between identifiers declared in
          different scopes.  This is accomplished  by  the  _s_y_m_n_o_d_e  struc-
          tures.   When an identifier is first encountered in a given scope
          it is "declared", meaning that a  new  symnode  is  created  that
          references the identifier.  Occurrences of the same identifier in
          that scope are then represented in the  parse-tree  by  treenodes
          referencing the same symnode.


















































9



9                                       - 19 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          The program:

                  program p;

                  var   demo  : integer;

                  begin
                     demo := 3
                  end.

          yilds the following structure:

             top

             +----------------+treenode representing
              npgm|           |the program
             +----|-----|-----|-----+
                |  | |^| |^
                |  | || +-----------------------------+
                |  | |+----------------------------+ |
                |    |                     | |
                | +-----|-------+treenode representing| |
                |  nvar|      |the var-declaration|
                | +---|----|-----+        +---------------|---+treenode repr.
                |  | |^|            nassign|           |assignment
                |  | |+-------> to type+----|---------|-----+
          symtab|    |                 |^     |^
          +----+  | +-----|---+treenode repr.+-------|---+ +-----|-------+
          |  |<------+  nid|   |occurrence ofnid|     |  ninteger|      |
                  +--|-----+id. "demo" +----|-----+ +------|-----+
          |  |     | |^               |        | |^
          +----+     | |+--------------------+        | |
          |  |       |                          |
          +----+  +-------|-------+symnode representing+-------|------+
          |  |----->    lidentifier|        |identifier "demo" linteger|       |
          +----+  +----|---------+in the current scopelinum=3|       |
                   |                       +-----------+
          idtab    +------------+
          +----+              |
          |  |
          +----+  +--------+  +--------+
          |  |----->|     |----->|     |idnode representing
          +----+  |     |   index=2|     |identifier "demo"
          |  |  +--------+  +--------+

             strstor
          +------------ - --------+
          |  |  |     |  |
          +---|----------- - --------+
            |

          +--------------------------------
          |  |  |d |e |m |o |/ |
          +--------------------------------   first idblock
                 |^
                index=2

          We see that the two occurrences  of  the  identifier  "demo"  are
          represented  by  two  _t_r_e_e_n_o_d_e_s  of  variant  _n_i_d  that both have




                                       - 20 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          pointers to the same  _s_y_m_n_o_d_e  representing  the  declaration  of
          "demo".   All  symnodes  at  a given declarationlevel are chained
          together (in the same manner as the idnodes) and the  chains  are
          attached  to the global variable _s_y_m_t_a_b.  In order to find out if
          an identifer is declared in the current scope we scan  the  chain
          of symnodes starting from symtab, and check if any of them refer-
          ences the idnode we are looking  for.   A  symnode  also  have  a
          pointer  to  the  treenode which defines the symbol.  The _s_y_m_t_a_b_s
          themselves are also chained, the  chain  implements  a  stack  of
          declarationlevels.  The symtab which is created when the scope of
          a procedure is entered is also attached to that procedure.   When
          a  procedure  is entered we create a new symtab, push it onto the
          stack, parse the procedure and pop the stack.  The  symbols  then
          visible are those that still can be reached from the stack.

          The parse-tree consists of _t_r_e_e_n_o_d_e_s representing  each  declara-
          tion,  statement,  expression etc.  Each node except the nprogram
          node has a pointer to its immediate father (giving  the  defining
          point),  to its children (if it has any) and to its right brother
          (if it is a member of a list).  The top of the tree is  found  in
          the global variable _t_o_p.

          In order to find the defining point for  the  identifier  in  the
          assignment,  we  follow pointers from the nassign-treenode to the
          nid-treenode, to the lidentifier-symnode,  and  then  up  to  the
          nid-treenode  in the declaration.  If we want to know the type of
          the identifier we proceed up to the nvar-treenode and  then  down
          to  the  node  giving the type in the declaration (in our example
          that node would also be a nid-treenode  referencing  a  linteger-
          symnode  that  represents  the identifier "integer").  There is a
          function _t_y_p_e_o_f that performs exactly this  operation.   It  will
          return  a  pointer  to  a  npredef-,  nsubrange-, nscalar-, nptr-
          narray-, nrecord-, nfileof- or nsetof-treenode.  In  those  cases
          where  the  translator  pays attention to types it uses a pointer
          (obtained from typeof) as representation of a type.

          Given the parse-tree and the layered symbol table it is not  hard
          to see how the translations described earlier are performed.  The
          one place where the code becomes more  than  usually  complex  is
          when  a  _w_r_i_t_e  statement  with  format  specifications  is to be
          translated into a call to _f_p_r_i_n_t_f.

















9



9                                       - 21 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          _5.  _T_u_n_i_n_g

          The behaviour of the translator may be modified  for  some  cases
          simply by changing constants.  These constants are all located at
          the top of the program text.

          output      The translator will copy the source during  input  if
                      the  constant _e_c_h_o is true.  The copy is preceeded by
                      the line

                              # ifdef PASCAL

                      and ended by the line

                              # else

                      and then follows the translated code and finally

                              # endif

                      This may be used to hold both Pascal and C source  in
                      the  same  file.  If the Pascal part is changed the C
                      part may be updated through:

                                 cpp -P -DPASCAL < orig > tmp
                                 ptc < tmp > new
                                 move new orig

                      assuming that _e_c_h_o is true and that _c_p_p is the  stan-
                      dard C preprocessor.

                              Default value:

                                 echo     = false;


          comments    The translator recognizes both (* and  {  as  comment
                      delimiters.   They are treated as different, allowing
                      1 level nested comments, if the constant  _d_i_f_f_c_o_m  is
                      true.

                              Default value:

                                 diffcomm = false;


          symbols     The  translator  accepts  default  entries  in  case-
                      statements  provided that the keyword defined through
                      _o_t_h_e_r_s_y_m is used in place of the constant list.

                              Default value:

                                 othersym = 'otherwise ';

                      substitute for

                                 othersym = 'otherwise%';

                      if that feature is undesired.




                                       - 22 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9                      The translator accepts externally declared procedures
                      and  functions  provided  that  the directive defined
                      through _e_x_t_e_r_n_s_y_m is used in  place  of  the  keyword
                      _f_o_r_w_a_r_d.

                              Default value:

                                 externsym   = 'external  ';


          sets        Sets are implemented as arrays of _w_o_r_d_t_y_p_e.  The type
                      is assumed to hold _s_e_t_b_i_t_s + _1 bits numbered from 0.

                              Default value:

                                 wordtype = 'unsigned short';
                                 setbits  = 15;


          files       The implementation of files uses  a  flag-word  which
                      has  the  type  given as _f_i_l_e_b_i_t_s which is assumed to
                      hold _f_i_l_e_f_i_l_l + _4 bits.

                              Default value:

                                 filebits = 'unsigned short';
                                 filefill = 12;


          stmts       If the Pascal source is known to be "normal"  in  the
                      sense  that for-loops always have an upper bound that
                      is less than the maximum value of  the  type  of  the
                      loop-variable,  and in the sense that the upper bound
                      doesn't change by computations inside the loop,  then
                      the  translator  may  generate  a  more natural code.
                      I.e:

                              for i := 1 to 10 do ;

                      becomes

                              for (i = 1; i <= 10; i++) ;

                      Since the requirements cannot be  determined  by  the
                      translator itself this kind of code is generated when
                      the constant _l_a_z_y_f_o_r is true.

                              Default value:

                                 lazyfor  = false;








9



9                                       - 23 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9          new         The second and following parameters to the  procedure
                      _n_e_w  will  be  ignored  if  the  constant _u_n_i_o_n_n_e_w is
                      false.

                              Default value:

                                 unionnew = true;


          strings     All identifiers and strings are stored in the  trans-
                      lator  with  the special character having the ordinal
                      value _n_u_l_l as endmarker.  Hence, that  character  can
                      not occur in strings in the Pascal source.

                              Default value:

                                 null     = 0;


          types       The names of predefined types are given by  the  con-
                      stants: _i_n_t_t_y_p, _c_h_a_r_t_y_p, _f_l_o_a_t_t_y_p, and _d_o_u_b_l_e_t_y_p.

                              Default value:

                                 inttyp      = 'int';
                                 chartyp  = 'char';
                                 floattyp = 'float';
                                 doubletyp   = 'double';

                      The typename for real variables and functions defined
                      by the user is given by the constant _r_e_a_l_t_y_p.

                              Default value:

                                 realtyp  = doubletyp;

                      The typename for procedures is given by the  constant
                      _v_o_i_d_t_y_p.

                              Default value:

                                 voidtyp  = 'void';


          i/o         The default fieldwidths for integer and  real  values
                      written  on  textfiles  are  given  by  the constants
                      _i_n_t_l_e_n and _f_i_x_l_e_n.

                              Default value:

                                 intlen   = 10;
                                 fixlen   = 20;


          types       A table in the translator gives the mapping from Pas-
                      cal  integer  subrange  types  to C arithmetic types.
                      The table is initialized by code located at  the  end
                      of  procedure _i_n_i_t_i_a_l_i_z_e giving the following default
                      configuration:




                                       - 24 -



9

          Holistic Technology AB         PTC            HD870410-1 Rev: 1.6

9                      Low bound     High bound   Selected type

                                0          255   unsigned char
                             -128          127   char
                                0        65535   unsigned short
                           -32768        32767   short
                      -2147483647   2147483647   long



















































9



9                                       - 25 -



9