{ Qinit.doc - documentation for QWIK Qinit                  ver 4.1, 05-01-88 }
{                                                                             }
{ Qinit initializes all the variables needed for the Q- procedures.  And      }
{ specifically checks for ALL IBM video equipment including dual monitors.    }

  This file will help you figure out how the new IBM PS/2 systems are config-
  ured as well as original equipment.  First, it is helpful to have a list of 
  all the possible Alphanumeric (A/N or text) modes.  QWIK was not designed 
  for the All Points Addressable (APA or graphics) modes.  Qinit detects dual 
  monitors and saves both the active and alternate display device codes.

            TABLE 1:  Hardware Specific Video Mode Characteristics
Mode Format Segment Display Box  MDA CGA EGA MCGA VGA PCjr PCC 3270 HGC MaxPage
---- ------ ------- ------- ---- --- --- --- ---- --- ---- --- ---- --- -------
0,1  40x25  B800:0  320x200 8x8       x   x   x    x   x    x              7
                    320x350 8x14          x        x                       7
                    320x400 8x16              x                            7
                    360x400 9x16                   x                       7
2,3  80x25  B800:0  640x200 8x8       x                x    x              3
                    640x200 8x8           x        x                       7 *
                    640x350 8x14          x        x                       7 *
                    640x400 8x16              x                            7
                    720x350 9x14                                x          0+
                    720x400 9x16                   x                       7
7    80x25  B000:0  720x350 9x14  x                         x   x    x     0 
                    720x350 9x14          x        x                       7 *
                    720x400 9x16                   x                       7
                    640x200 8x8                             x              3

Legend:
  Format  - Characters per row by the number of rows in the data area.
  Segment - Address of the first character on page 0 of the display buffer.
  Display - The pixel resolution for the data area excluding the border, 
            horizontal by vertical.
  Box     - The pixel resolution for each character, horizontal by vertical.
  MDA     - Monochrome Display and Printer Adapter
  CGA     - Color Graphics Adapter 
  EGA     - Enhanced Graphics Adapter
  PGC     - Professional Graphics Controller
  MCGA    - Multi-Color Graphics Array
  VGA     - Video Graphics Array
  PCjr    - PC Junior
  PCC     - PC Convertible
  HGC     - Hercules Graphics Cards - HGC, HGC Plus, and InColor Card
  3270    - All IBM 3270 PC adapters
  MaxPage - 0-based highest page number; e.g. 7 means there are 8 pages.
  MD      - 5151 Monochrome Display
  CD      - 5153 Color Display
  ECD     - 5154 Enhanced Color Display

Notes:
  1. The 0 and 2 modes suppress color burst only on composite displays (not 
     RGB) only for CGA and EGA.
  2. The PS/2 model 25 and 30 have an integrated MCGA.  The model 50 and 
     above have an integrated VGA.
  3. The 8514 High Content Color Display along with the 8514/A adapter 
     produces a superset of the VGA for APA, but there is no differences in 
     the A/N modes to the VGA when the adapter is in "VGA" mode.  See IBM 
     documentation for Advanced Function Mode.
  4. Reduced MaxPage to 3 if EGA only has 64K graphics memory installed for 
     modes marked "*".  MaxPage of 7 is for 128K or more.
  5. The PCC can have either an alternate MDA or CGA.  The LCD (model 5140) 
     can emulate either the MDA or CGA modes, but the MDA mode is 640x200.
  6. I currently have no information on the PGC.
  7. To relieve cursor routine programming due to the multiple character box 
     sizes, the VGA has a cursor emulation mode.  Qinit turns on the mode 
     if PS/2 equipment is detected.  See CURSOR.DOC for emulation notes.
  8. On the 3270 PC, dual monitors are not possible as they use the same 
     physical buffer space.  Qinit will determine if more than just page 0 
     is available for color displays.  Unless there is a special adapter, 
     there is only page 0.

  Display Combination Code (DCC) - The PS/2 video BIOS has a new function 
  that simplifies equipment detection called the Read/Write Display 
  Combination Code.  Using interrupt $10 with AH = $1A00, the call will 
  return the Active Display Device in BL and the Alternate Display Device in 
  BH.  If the function is supported, it also returns $1A to AL.  The possible 
  Display Device codes (as assigned by IBM) are: 

     TABLE 2:  Display Combination Code
     CODE  DESCRIPTION                       QWIK41 Constant
     ----  --------------------------------  ---------------
     $00   No display                        NoDisplay
     $01   MDA with 5151 monochrome display  MdaMono
     $02   CGA with 5153/4 color display     CgaColor
     $03   reserved                          DCC3
     $04   EGA with 5153/4 color             EgaColor
     $05   EGA with 5151 monochrome          EgaMono
     $06   PGC with 5175 color               PgcColor
     $07   VGA with analog monochrome        VgaMono
     $08   VGA with analog color             VgaColor
     $09 to $0A - reserved                   DCC9,DCC10
     $0B   MCGA with analog monochrome       McgaMono
     $0C   MCGA with analog color            McgaColor
     $0D to $FE - reserved                   n/a
     $FF   unknown                           Unknown

  Conforming to DCC - No results are obtained for the DCC on anything other 
  than PS/2 equipment.  However, to be consistent, Qinit was reprogrammed 
  to conform to the DCC for ALL equipment.  To see if a CGA is in use, 
  simply check to see if ActiveDispDev=CgaColor.  Qinit only sets the 
  parameters for the active display.  Although the alternate display device 
  code is saved, it is only for testing purposes.  If you change text modes 
  in a running program, Qinit should be executed again. 

  HavePS2 - Qinit sets HavePS2 to true if the DCC is supported.  This means 
| that the program has detected a PS/2 video card whether it is a standard 
  Model 30, a PS/2 Display Adapter on an IBM XT, or the like.  It also 
  means that either MCGA or VGA is present, but not necessarily active.  To 
  know which, just check the DCC.

  Have3270 - If Qinit detects 3270 PC equipment/software, this variable is 
  set to true.  In addition, the ActiveDispDev is either MdaMono or 
  CgaColor.  Note: There may or may not be graphics capability in either 
  case; Qinit is not meant to detect graphics.  ActiveDispDev3270 may be 
  one of the following:

     TABLE 3:  3270 PC Display Combination Code
     CODE  MONITOR        ADAPTER                    QWIK41 Constant
     ----  -------------- -------------------------  ---------------
     $00   5151 or 5272   for 5151 or 5272           
     $01   3295           for 3295
     $02   5151 or 5272   for 5151 or 5272 plus
                           XGA graphics
     $03   5279           3270 PC G 
     $04   5379 C01       3270 PC GX 
     $05   5379 M01       3270 PC GX 
     $06   Reserved
     $07   Reserved
     $FF   Unknown, not a 3270 PC                    Unknown

  EGA Switches - By checking the value of this byte, you can determine the 
  monitor connected to the EGA, the alternate video system, and the start 
  up default.  The byte is a copy of how the dip switches are set on the 
  card where on=0 and off=1.  The primary is the default.  When the ECD is 
| set for 640x200, it is emulating the CD including the cursor mode.  Qinit 
| now directly tests for the alternate device rather than assuming it.

       TABLE 4: EGA dip switch configuration     
       SWITCH  VALUE  PRIMARY               SECONDARY
       ------  -----  --------------------  -------------------
       0000    0      MDA + MD              EGA + CD - 40x25   
       0001    1      MDA + MD              EGA + CD - 80x25   
       0010    2      MDA + MD              EGA + ECD (640x200)
       0011    3      MDA + MD              EGA + ECD (640x350)
       0100    4      CGA + CD - 40x25      EGA + MD           
       0101    5      CGA + CD - 80x25      EGA + MD           
       0110    6      EGA + CD - 40x25      MDA + MD           
       0111    7      EGA + CD - 80x25      MDA + MD           
       1000    8      EGA + ECD (640x200)   MDA + MD           
       1001    9      EGA + ECD (640x350)   MDA + MD           
       1010   10      EGA + MD              CGA + CD - 40x25   
       1011   11      EGA + MD              CGA + CD - 80x25   

  EGA Information - The byte located at $0040:$0087 has the following 
  information when the EGA (or VGA) is present:

       TABLE 5: EGA information
       BITS  DESCRIPTION
       ----  -------------------------------------------------
       7     (0) Clear, (1) Keep video data after mode set
       6,5   (00) 64k, (01) 128k, (10) 192k, (11) 256k, memory
       4     Reserved
       3     (0) EGA active, (1) EGA not active
       2     (0) Disable,    (1) Enable wait-for-display
       1     (0) CD/ECD,     (1) MD attached
       0     (0) Active,     (1) Inactive CD emulation

  PCC Exceptions - Since the PCC also does not support the DCC, a separate
  code is used.  If the 5140 LCD is used in mode 7, the Active Display 
  Device is set to MdaMono which is close enough.  This set up can be 
  verified by testing if MaxPage=3.  The alternate display is found by using 
  interrupt $10 with AH=$15.  The result is saved in AltDispDevPCC.  Of 
  course the variable is undefined if a PCC is not used.  The possible types 
  are:

     TABLE 6: PC Convertible Alternate Display Adapters
     VARIABLE        MODEL  DESCRIPTION
     -------------   -----  --------------------
     AltDispDevPCC = $   0   No alternate adapter
                   = $5140   LCD
                   = $5153   CGA type
                   = $5151   Monochrome type

  Dual Monitors - Qinit makes an attempt to detect for a second monitor by 
| several means.  If no alternate cards like EGA or VGA are found, an 
| alternate 6845 video chip (CGA, MDA, or Hercules) is checked.  If the 
| chip is found, then further tests are made to find which card it could 
| be.  The chip existence test is highly reliable.  If no alternate display 
| device is found, then AltDispDev=NoDisplay.

| Hercules - Hercules cards are also detected.  If either the active or 
| alternate DCC is MdaMono, which is found by verifying a responsive 6845 
| video chip at the mono register port, then an attempt is made to find if 
| any Hercules card is attached.  If no Hercules card is found, then 
| HercModel=NoHerc; it is then assumed that just an MDA card is attached.  
| This test is only run once, even if Qinit is executed again, because the 
| test can take up to 1/3 of a second on slower computers.  The tests for 
  the Hercules cards are the ones recommended by Hercules Computer 
  Technology, which also admits that sometimes the tests will fail during 
  multi-tasking activity.  Hercules clones may not be detected by these 
  test, but the DCC will be correct.

     TABLE 7:  HercModel - Hercules Model Code
     CODE  DESCRIPTION                       QWIK41 Constant
     ----  --------------------------------  ---------------
      0    No Hercules card                  NoHerc
      1    HGC                               HgcMono
      2    HGC Plus                          HgcPlus
      3    Hercules InColor Card             HercInColor

  System Identification - To get both the model and submodel, you must use 
| interrupt $15 with AH=$C0 which only works on some computers.  The code 
| was modified to properly exit on AT&T, Leading Edge, and other clones 
| which have BIOS inconsistencies.  If the carry flag is set on exit, then 
  that interrupt is not supported, because there's no submodel number.  The 
  alternative is to get the basic computer model by directly accessing the 
  byte in memory at $F000:$FFFE.  The possible values are:


     TABLE 8:  System Identification Codes
     SysID Sub-Model  SYSTEM              
     ----- ---------  ---------------------------
      $FF    n/a      IBM PC
      $FE    n/a      IBM PC XT
      $FD    n/a      IBM PCjr
      $FC    n/a      IBM PC AT (6 MHz, 01/10/84)
             $00      IBM PC AT (6 MHz, 06/10/85)
             $01      IBM PC AT (8 MHz, 11/15/85)
             $02      IBM PC XT (286)
             $04      IBM PS/2 model 50
             $05      IBM PS/2 model 60
      $FB    $00      IBM PC XT (256/640)
      $FA    $00      IBM PS/2 model 30
             $01      IBM PS/2 model 25
      $F9    $00      IBM PC Convertible
      $F8    $00      IBM PS/2 model 80 (16 MHz)
             $01      IBM PS/2 model 80 (20 MHz)

| CPU Identification - A CPU detection routine has been included for Intel  
| processors.  This routine is independent of QWIK and is useful for clones 
| that do not recognize IBM's system ID scheme.  The idea came from Juan 
| Jimenez as it appeared in Jan/Feb '88 Turbo Technix magazine.  The 
| routine has been simplified for reduced code (only 42 bytes) and allows 
| use of simple constant identifiers.  Therefore, this routine is optional 
| to  QWIK and may be deleted from the initialization in QWIKxx.PAS if 
| desired.

|    TABLE 9:  Intel CPU Identification
|    INTEL CPU MODEL NUMBERS  QWIK41 Constant
|    -----------------------  ---------------
|    Intel 8086/8088          Cpu8086
|    Intel 80186/80188        Cpu80186
|    Intel 80286              Cpu80286
|    Intel 80386              Cpu80386

  The essential variables set by Qinit are:

    VARIABLE      DESCRIPTION
    ------------  ---------------------------------------------------------
    Page0seg      Segment for the base page, page 0.  This value may be
                    changed for multi-tasking environments.
    Qseg          Segment for Q writing which is altered when changing
                    pages.
    Qsnow         Wait-for-retrace (snow) while Q writing.
    MaxPage       Maximum possible 0-based page number.

  The other variables set or located by Qinit are for your reference to 
  help make decisions in your programs:  

    VARIABLE      DESCRIPTION
    ------------  ---------------------------------------------------------
    VideoMode     Directly accesses the video mode code.
    VideoPage     Directly accesses the video page number.
    EgaRows       0-based number of rows on the screen for EGA or VGA.
    EgaFontSize   1-based number of horizontal scan lines per character for
                    EGA or VGA.
    EgaInfo       (Described above)
    EgaSwithces   (Described above)
    CRTcolumns    1-based number of CRT columns for any card or video mode.
    CRTcols       Global variable equal to CRTcolumns.
    CRTrows       1-based number of CRT rows for any card or video mode.
|   QnextOfs      0-based offset where next Q*More procedure will write.
    HavePS2       Detects the presence of IBM PS/2 video equipment.
    Have3270      Detects the presence IBM 3270 PC equipment/software.
    CardSeg       Video buffer address the video "card".
    CardSnow      Requirement for wait-for-retrace for the video "card".
    SystemID      Code for the IBM computer in use.
    SubModelID    Code for the sub-model of the IBM computer in use.
|   CpuID         Intel CPU identification code.
    ActiveDispDev Code for the Active Display Device.
    AltDispDev    Code for the Alternate Display Device.
    AltDispDevPCC Code for the Alternate Display adapter on the PC 
                    Convertible.
    ActiveDispDev3270 Code for the Active Display Device on the 3270 PC.
    
  CGA Snow - A recent discovery has shown that CGA cards do not need wait-
  for-retrace in 40 column modes 0 and 1.  Qinit was programmed to 
  accommodate this.  For other hardware, you can change Qsnow to suit your 
  needs, but CardSnow should be left unchanged to save what Qinit detected. 

  References - For more information on the new IBM PS/2 system, you can get 
  the "IBM BIOS Interface Technical Reference Manual".  Other references 
  include:
    
     IBM Personal System/2 Seminar Proceedings:
       Volume 5, Number 2, Displays and Adapters, publication # G360-2678.
       Volume 5, Number 4, Models 50, 60, 80, VGA, BIOS and Programming 
          Considerations, publication # G360-2747.

  For more information on the IBM 3270 PC, you can get the the following 
  publications:
 
    "3270 PC Application Development Considerations"
    "IBM 3270 Personal Computer Programming Guide", Pub # SA23-0221
    "IBM 3270 Personal Computer Control Program Reference", Pub # GA23-0232

  As always, the above information is subject to change without notice per 
  IBM.  IBM is the trademark for International Business Machines Corp. (but 
  you already know that!)