*****************************************************
           * TPATCH: Turbo File Patching Utility, Version 2.00 *
           *****************************************************

             (C) Copyright 1987 Brian Foley, TurboPower Software
                           CompuServe 76317,3247

    This program is released into the public domain for personal,
    non-commercial use only. It may be freely copied and distributed so
    long as no fee is charged, either for the program itself or the
    distribution of it.

What TPATCH does
================
TPATCH.COM is a utility for programs compiled with Turbo Pascal (PC-DOS,
versions 3.00B-3.02A). It allows you to examine the status of certain
settings--colors, mIn and mAx heap, display mode, etc.--and, if requested,
to change them without recompiling. It also allows you to make a few
simple patches to Turbo compilers. Here is the output that would be
generated by entering

     TPATCH tpatch

at the command line (I've added the numbers to the left, in parentheses):

      TPATCH, Turbo File Patching Utility, Version 2.00
      (C) Copyright 1986 by Brian Foley
      Examining TPATCH.COM
 (1)  Compiled with Turbo Pascal version 3.01A (plain vanilla)
 (2)  Monochrome
 (3)    NormVideo        $0F (White on Black)
 (4)    LowVideo         $07 (Light Gray on Black)
      Black & white
        NormVideo        $0F (White on Black)
        LowVideo         $07 (Light Gray on Black)
      Color
        NormVideo        $0E (Yellow on Black)
        LowVideo         $07 (Light Gray on Black)
 (5)  Display mode       $FF "Default display mode"
 (6)  Device checking  {$D+}
 (7)  ^Break checking  {$C+}
 (8)  ^C checking      {$U-}
 (9)  Code size        $0564 paragraphs
(10)  Data size        $003D paragraphs
(11)  mIn stack        $0400 paragraphs
(12)  mAx stack        $2000 paragraphs
(13)  Input buffer     (N/A)
(14)  Output buffer    (N/A)

-P and -O options
=================
If you want to change some of these items, use the "-P" (Patch Mode) option and
you will be prompted for new settings. By default, any changes you request
will be made directly to the COM file itself. If you want to play it safe,
you can have TPATCH write a new version of the program that incorporates
the changes by using the "-O" (Output file) option and specifying a
filename. If the "-O" option is specified, Patch Mode is selected
automatically.

Items displayed, Making changes
===============================
     (1) Version: The version of the Turbo compiler that was used to
         generate the executable file. TPATCH recognizes the runtime
         library for most DOS versions of the Turbo compiler, from 1.00A up
         to 3.02A. However, it will only report the default settings for,
         and permit changes to, programs compiled with PC-DOS Turbo 3.00B
         and higher (including BCD and 8087 versions).
     (2) Monochrome (Black & white, Color): The runtime library keeps three
         sets of video attributes--one for monochrome adapters, one for
         composite black and white monitors attached to color cards, and
         one for color monitor-adapter combinations.
     (3) NormVideo: The video attribute used for NormVideo (aka HighVideo),
         the default. If you aren't familiar with video attributes, but
         want to change them, here's a simple Pascal function that takes
         foreground and background colors as parameters, and returns a
         video attribute (with the blink bit masked out):

         function Attribute(Foreground, Background : Byte) : Byte;
         {-Translates foreground and background colors into video attributes.
           "And 127" masks out the blink bit. Add 128 to the result to set it.}
         begin
           Attribute := ((Background shl 4)+Foreground) and 127;
         end;

         You may change NormVideo for any or all of the three sets of
         attributes. Number must be in the range 0-$FF (enter in decimal or
         hex, either one).
     (4) LowVideo: The video attribute used for LowVideo. You may change
         LowVideo for any or all of the three sets of attributes. Number
         must be in the range 0-$FF (enter in decimal or hex, either one).
     (5) Display mode: A Turbo compiler fresh out of the package will have
         $FF (= default display mode) here, which is what it should be.
         If you need to change this, the valid entries are:

              0 : b/w   display 40x25
              1 : Color display 40x25
              2 : b/w   display 80x25
              3 : Color display 80x25
              7 : Monochrome display
            $FF : Default display mode

         The string that goes with this byte is shown in quotation marks.
         If you alter the mode, TPATCH supplies the corresponding string.
         Enter the appropriate number in decimal or hex, either one.
     (6) Device checking: Default is D+. You may change this by entering
         '-' (just the minus) for $D- or '+' (just the plus) for $D+. This
         option does nothing unless the program uses DOS standard I/O. If
         $D- is used, all I/O is buffered, no matter what.
     (7) ^Break checking: Default is $C+. You may change this by entering
         '-' (just the minus) for $C- or '+' (just the plus) for $C+.
         Affects only the *initial* setting for CBreak (the well-known
         global variable), which determines whether break checking is on.
     (8) ^C checking: Default is $U-. You may change this by entering '-'
         (just the minus) for $U- or '+' (just the plus) for $U+. When you
         set $U+ (anywhere in your program, but normally at the top), the
         compiler fills your program with breakpoint instructions (INT
         3's), and sets a flag telling the runtime library to install an
         interrupt handler to trap INT 3 and check for a ^C at *every*
         breakpoint. TPATCH lets you determine whether that interrupt
         handler gets installed or not by setting the flag on or off. You
         can thus speed up the execution of a program compiled with $U+ (a
         bit), since the default INT 3 handler will *usually* point to a
         simple IRET. Or you can simulate a selective $U+ by inserting
         "Inline($CC);" statements into your code at strategic locations
         (as opposed to everywhere) and use TPATCH to see that the
         interrupt handler gets installed.
     (9) cOde size: There is no reason for changing this unless you are
         using chain files. If you are, you'll know what this is good for;
         if not, don't worry. You may enter *any* integer value here (the
         number of 16-byte paragraphs), either in decimal or in hex, so be
         careful.
    (10) Data size: Ditto.
    (11) mIn heap: mIn will usually be $400 paragraphs (16K bytes). You
         may enter any integer value in the range $40-$B000 (paragraphs)
         here, either in decimal or in hex.
    (12) mAx heap: mAx will usually be set to $A000 paragraphs (640K
         bytes), insuring that all available memory gets allocated for your
         program. You may enter any integer value in the range $40-$B000
         (paragraphs) here, either in decimal or in hex.
    (13) Input buffer: The size of the buffer created with the $G (Get)
         compiler directive, used to permit redirected input. "(N/A)" is
         displayed if the buffer size is 0, indicating that redirection is
         not enabled. This value cannot be changed. (At least not in this
         version--I'm not sure it's safe.)
    (14) Output buffer: The size of the buffer created with the $P (Put)
         compiler directive, used to permit redirected output. "(N/A)" is
         displayed if the buffer size is 0, indicating that redirection is
         not enabled. This value cannot be changed. (Again, not sure it's
         safe.)

-I and -A options
=================
New in TPATCH 2.00 are the -I and -A options, which give you an easy way
to do nothing except reset mIn (-I) and mAx (-A) heap settings. If you use
CED, you may want to define a synonym such as

  minmax syn 'tpatch %1 -i $%2 -a $%3'

If you're one of the six people who don't, you could also construct a
batch file to accomplish the same thing. These options can also be used to
reset the default mIn/mAx on Turbo compilers. (See the discussion of the
-S option, below.)

-C option
=========
Those are the settings that are shown ordinarily. If you select the "-C"
option, however, things look a little different. This option activates
"Colors Only Mode". It is selected automatically if the .COM file being
examined is a Turbo compiler. If Colors Only Mode is activated, items (6)
through (14) are not shown. Instead, two more attribute settings are
displayed for each of the three sets: "Marked blocks" (the attribute used
to display marked blocks inside the Turbo editor) and "Error messages" (the
attribute used to display error messages both in the editor and in the
compiler--the kind that require you to press the Escape key to continue).
These are displayed and changed in the same manner as NormVideo and
LowVideo. In addition, the status of the "Snow checking" flag is shown
(TINST asks if your display "flickers when it scrolls"--not quite
accurate). (All of the extra items are in the runtime libraries of programs
compiled with Turbo, but they aren't used.) Entering [Y] turns Snow
Checking on, [N] turns it off.

If you use plain vanilla Turbo 3.01A and you enter

     TPATCH turbo

at the command line, this is what the display will look like:

      TPATCH, Turbo File Patching Utility, Version 2.00
      (C) Copyright 1987 by Brian Foley
      Examining TURBO.COM
      This is Turbo Pascal version 3.01A (plain vanilla)
      Monochrome
        NormVideo        $0F (White on Black)
        LowVideo         $07 (Light Gray on Black)
        Marked blocks    $07 (Light Gray on Black)
        Error messages   $70 (Black on Light Gray)
      Black & white
        NormVideo        $0F (White on Black)
        LowVideo         $07 (Light Gray on Black)
        Marked blocks    $07 (Light Gray on Black)
        Error messages   $70 (Black on Light Gray)
      Color
        NormVideo        $0E (Yellow on Black)
        LowVideo         $07 (Light Gray on Black)
        Marked blocks    $07 (Light Gray on Black)
        Error messages   $4F (White on Red)
      Snow checking       ON
      Display mode       $FF "Default display mode"

Although the "-C" option is intended mainly for Turbo compilers, it is
perfectly acceptable to use it with your own programs. (See the
discussion of the -F option, below.)

-S option
=========
Also new in TPATCH 2.00 is the -S option, to Show all compiler options
(well, all that TPATCH knows about). This allows you to examine the
default settings for mIn and mAx heap, as well as the more common compiler
directives. After displaying the usual compiler information discussed
above, TPATCH will ask you to press a key to continue, then display the
following:

      mIn stack        $0400 paragraphs
      mAx stack        $A000 paragraphs
      I/O checking     {$I+}
      Range checking   {$R-}
      Break checking   {$C+}
      ^C checking      {$U-}
      Stack checking   {$K+}
      Type checking    {$V+}
      Device checking  {$D+}

As with compiled programs, these settings can be changed if Patch Mode
(-P) is in effect. Before changing any of these, be sure to consider
carefully the consequences, especially if you are in the habit of
distributing the source code for your programs.

-F option
=========
Selects the Fast screen update option, which installs the alternate ConOut
driver from my CONOUT.PAS. By default, this option must be selected each
time you run the program. However, if you wish, you can patch TPATCH to
install the driver automatically. To do so, run TPATCH on itself in Colors
Only Mode by entering

     TPATCH tpatch -C -P [-O newfile]

Press [Enter] at all the prompts except the "Snow checking" one--for it,
answer [N]. The alternate driver will then always be installed, and the -F
option ignored. Try the -F option first before making the patch. (Please
don't distribute altered versions of TPATCH.)

Default extension
=================
TPATCH always assumes that the extension for a filename passed to it as a
parameter is .COM -- you can include it or omit it, doesn't matter.

Feedback
========
That's it. Let me know if you have any comments, complaints, bug reports,
etc. As noted above, I can be reached via CompuServe [76317,3247].