ASM48 Version 1.3 
       Cross Assembler for the Intel 8748 Microcontroller
                       By Vance Navarrette

Introduction:


     The ASM 48 assembler was intended to be a simple, easy to 
use assembler for the person who only intends to assemble one or 
two programs for personal use in a hacker type project. This 
person does not want to spend $200-300 for a professional 
product, but rather just needs something simple to get him by.
     The source file is written using any editor that will 
generate an ascii file (Wordstar, or even (Gag!) Edlin) and is 
processed using the ASM48 program to produce an assembled object 
file.


Changes for version 1.3:

     Version 1.3 is now in compiled format using Borland's Turbo 
Basic. This speeds up the execution by a factor of 8. On a 
4.77MHz IBM PC, a 1K object file would have taken approximately 
20 minutes to assemble, depending on the number of comments and 
errors in the source file. This will now take a little over 3 
minutes, and on AT class machines the execution time will be 
measured in seconds, not minutes.
     The error messages for version 1.3 have been reworked, so 
that additional kinds of errors are flagged that previously would 
have gone unflagged (object code generation was still correct, 
but certain kinds of errors resulted in the source line in which 
the error occurred to be ignored).

To use the program:

The program is now much faster than before, but it is impossible 
to modify to suit your needs unless you have the turbo-basic 
compiler. Such is the tradeoff for speed. The program can be 
invoked by typing ASM48 <Enter>. After the program loads, it 
will immediately execute, and will prompt:

"Name of file to assemble?"

     The user types the name of the source listing file. A sample 
file name would be "A:Test"<Enter>. Note that the program assumes no 
extension is present in the file name. If an extension is 
present, an error will be generated.
     The program will then prompt:

"Do you want to print the assembler listing (Enter=YES)?"

     The user would type a "N"<Enter> at this point if no hardcopy 
was wanted, or if there is no printer available for the system. 
If the assembler is unable to find a printer, or if the printer 
is not ready, the file will be generated but not printed, and 
execution will terminate with an error message.	It is strongly 
recommended that a listing be used to de-bug any assembly errors. 
     Assuming the file to be assembled is be found, the assembler 
then responds :


"BEGINNING PASS 1
Press F1 key to abort assembly"

     The assembler then decodes the listing, looking for opcodes 
and errors. During this time, a temporary file is created on the 
disk for use by the assembler to store the partially assembled 
code listing. For this reason, it is recommended that there be 
plenty of disk space for large files to assemble. The file will 
be created on the same disk that the source listing resides.

     After some time (depending on the amount of code to be 
assembled), the assembler prints:

"BEGINNING PASS 2"

and continues to assemble the source. During the second pass, 
absolute addresses are assigned to labels and branches. Because 
this assembler produces absolute code, a linker or locator is not 
required. After assembly is complete, an assembler listing is 
produced (if requested) and is sent to the list device (printer). 
In addition to the listing, a label table is dumped to aid in 
debug, and the number of errors is shown.
     The object code is placed in a file called <filespec>.OBJ, 
and the listing, if requested is also placed in a file called 
<filespec>.LST. The assembler then prints on the CRT screen:

"ERRORS THIS ASSEMBLY: XX"

and assembly is complete.



Syntax of the source file:

     It is assumed that the user is familiar with assembly 
language programming, and understands it's elements. For a 
listing of the Intel mnemonics, see the MCS-48 User's Manual, 
available from Intel.
     The structure of a typical source code line is:

LABEL       OPCODE  VARIABLE       ;COMMENT <Enter>

     Note that the above elements may appear in any combination, 
but only in the order shown. In other words, a label is optional, 
but if present, must appear before the opcode. The opcode is not 
needed for a comment to be legal, but must appear BEFORE the 
comment if present on a line.
     The assembler uses a FREE FIELD format, that is as long as 
spaces are used as delimiters, the spacing of the various 
language elements is irrelevant.

     A source file might look like this:
                                             

                                            

                ; this is a test file for asm48
                ;it includes comments and a few sample opcodes
                                               
label1          MOV P4,A                        ;COMMENT
                DEC R1
                RR A                            ;ANOTHER COMMENT
                INC A
LABEL2          XRL A,#  label1                                
		ORL P2,#00                      
                ORL BUS,# 0F                    
		ADD A,# 55                          
		ORG 000F			; ORG PSEUDO OP
		DS 05				; SAVE 5 BYTES
		DB 00,FF,88			; DEFINE 3 BYTES
ASIC		EQU 00
ASID            EQU ASIC
labelxyz        JMP LABEL2         
		XRL A,#FA			;TEST FOR HEX 
		NOP
		CALL label1
		JMP 0187			;TEST FOR GOOD JMP
		DT  HELLO, DEVO!
ARCANE		EQU   LABEL2
                                                ; END OF TEST






Object Code:

     The object code is placed in an Intel compatible ascii HEX 
listing file. The basic format of the hex dump is:

:BBAAAA00B1B2B3B4B5B6B7B8B9BABCBDBE...B(N)SS
:BBAAAA00B1B2B3B4B5B6B7B8B9BABCBDBE...B(N)SS
               .
               .
               .
:0000000000

     Where:
           BB=Number of bytes in the record (max=255)
           AAAA=Absolute load Address for this record
           00=Always two 0s.
           B1, B2,....B(N)=Object code (Hexadecimal)
           SS=Two's compliment Check Sum of BB, AAAA, and B1-
                B(N).



     The last record (line) will be all zeroes. Note that NO 
BINARY OBJECT FILE IS PRODUCED. Thus, the output of this 
assembler cannot be loaded directly and executed. This was deemed 
un-necessary, since the target system is a controller, and not 
the host microprocessor. If you need a straight binary file, the 
INHEX subroutine in the basic listing (If you have it) may be 
modified to produce one.



     Points to Remember!:

          a. The assembler is case sensitive (i.e. "a" does NOT 
               equal "A")
          b. All mnemonics must be in caps (labels need not be).
          c. All comments start with ";".
          d. The vertical bar "|" is a reserved character. Do not 
               use it! The results are unpredictable.
          e. All numbers are to be in hex. Binary and decimal 
               numbers are not supported.
          f. No math operators (+, -, etc.) are supported.
          g. The file to be assembled must be an ascii coded text 
             file. No special control codes are allowed. If you 
             use a word processor like "Word Star" to edit the 
             file, be sure to use the non-document mode or else 
             do a ^QU command in the non document mode to insure 
             that the assembler won't get confused. You will get 
             error messages with nothing (apparently) wrong in the
             listing file when you try to debug your source code 
             if you fail to observe this rule.
	  h. All Hexadecimal number must have two characters, even 
		if they are both zeros.
	  i. The ^C and the ^Scroll Lock keys are NOT supported. Use
		F1 key to terminate assembly prematurely.
Pseudo Opcodes:

     In addition to the standard Intel mnemonics, several pseudo 
opcodes are supported to control the flow of the assembler and 
aid in producing code with a minimum of fuss. Pseudo opcodes
produce no hexadecimal output, and take up no space in the 
assembled code, although they will show up in your listing and 
will show an "address" in the listing. They are:

               DB  	"define byte"
               DT 	"define Text"
               EQU	"equals"
               ORG 	"Set Origin"
               DS 	"Define space"

     DB: Used to define a byte or bytes of code, using 
hexadecimal. Note that hex notation is always assumed, and that 
multiple bytes are delimited with a single space or comma. Do not 
use an "H" to designate hex, as it is assumed. It is also 
permissible to define a constant using the "EQU" opcode, and then 
use the label previously defined as a variable.
     DT: Used to define text. This generates the ascii code for 
each letter in a text string. Delimiters are not necessary.
     EQU: Sets the label on the left equal to the variable on the 
right. The variable on the right may be hex or a previously 
defined label.
     ORG: This sets the address counter used for assembly to the 
value of the hex variable or label on the right of the pseudo-op. 
The ORG opcode forces the assembly of subsequent code to begin at 
the address given by the variable used for ORG. May be used with 
hex or a previously defined label.
     DS: This allocates space in memory immediately following the 
opcode. The amount of space is defined by the variable used. The
Variable may be Hex or previously defined Label.


     Error Messages:
     The following error messages are generated during assembly, 
and are fatal (i.e. object code would have been incorrect, so the 
object file was deleted). The error messages will appear as com-
ments in the listing (.LST file). While the original comment will
appear to have been erased and the error message substituted, the 
original comment is in fact still present in the source file. 
Correcting the cause of the error and reassembling the source 
file will cause the original comment to appear in the listing 
file.


ILLEGAL VARIABLE: A non-hexadecimal character was found where 
only 0-9 or A-F characters were expected, or a label was used as 
a variable and was not previously defined. This error message 
will also be generated if an attempt is made to define a variable 
that is too large (>FFF hexadecimal) or use a variable larger 
than 0FF hex in a branch instruction that expects a single byte 
variable (i.e. using a variable larger than 0FF in any branch 
instruction other than JMP or CALL). 

UNKNOWN OPCODE: An opcode was used that is not legal, or an 
opcode is missing, resulting in a variable being interpreted as 
an opcode. Another possible cause is using lower case letters for 
an opcode (all opcodes must be in CAPS). Also note that embedded 
spaces in opcodes are considered significant, and must be present 
if defined by INTEL mnemonics.

MISSING VARIABLE: A variable was not found following an opcode  
that requires a variable. Also used when a DT pseudo op is used, 
and there is no text, or when there are no variables following a 
DB pseudo op.

LABEL TOO LONG: A label was encountered that was longer than 10 
characters. If a label is too long and subsequently used as a 
variable, an ILLEGAL VARIABLE error message will result.

DUPLICATE DEFINITION: A label that was previously defined was 
re-defined subsequent to the original definition. The label will 
appear twice in the label table, but only the first definition 
will be used in the assembly.

PAGE ERROR: The 8748 uses certain jump instructions that are only 
valid in a paged memory scheme (this is done for the sake of 
compactness and speed. Most branches in a typical assembly 
program jump to locations that are close by...).An attempt was 
made to cross a page boundary (Address in the range of X00-XFF 
hex) using a branch instruction that only supports branching 
within the page in which that branch instruction occurs. The 
assembler has generated code that will result in a jump to an 
incorrect address.
     This error is not necessarily even possible to see while 
writing the source code. The simplest way to correct the problem 
is to substitute a JMP instruction, but it is possible to simply 
move the offending subroutine inside the addressing page where 
the error occurred.

     A word on debugging the source code:
     
     It is possible for more than one error to occur on a given 
line of source code. ONLY THE MOST RECENT ERROR MESSAGE WILL 
APPEAR. Thus it is possible to have an "unknown opcode" error 
message appear, to then correct the opcode error and reassemble, 
only to have a "Illegal Variable" error message appear.
     To save time, it is therefore prudent to examine each 
flagged source line for other mistakes that might have occurred 
during assembly. The error count given at the close of assembly 
will not match a physical count of the error messages under these 
circumstances, and should be taken as an indication of multiple 
errors on single source lines. It is also possible that correcting 
one error will generate another. For instance, the following 
line:

TLABEL         ORg       5G            ;Comment.....

     Will first result in the "Unknown Opcode" message. After the 
line is corrected:

TLABEL         ORG       5G            ;Comment.....

     It will generate an "Illegal Variable" Error, since 5G is 
not a legal hex number.



     BASIC error messages:

     Several errors can arise that are not part of the assembler 
flow itself, but are generated by BASIC as a result of 
unexpected conditions during the execution of the assembler 
program. They are:

PRINTER IS OUT OF PAPER OR IS OFF LINE:
     A listing was requested, but the print device is 
unavailable. 

DISK DRIVE IS FULL:
     The disk drive that the source file was found on has 
insufficient space to allow the assembler to complete assembly. 
There are several options to correct this:

     1. Copy the source file to a floppy or Hard disk that has 
          more room, and re-assemble the file.
     2. Request that no list file be generated. This will greatly 
          reduce the space (and time) required to assemble the 
          file. (It will also make it nearly impossible to 
          debug. The total error count will appear on the 
          screen at the close of assembly.)
     3. Create a copy of the source file, and edit it to 
          eliminate all comments, blank lines, etc. Then proceed 
          to assemble the new source file.


DISK DRIVE NOT READY:
     The disk drive named for use by the assembler is unavailable 
to the system. Usually caused by an open door on the disk drive 
or a write protected file or disk.


SOURCE FILE NOT FOUND:
     The file specified for assembly is not on the specified disk 
drive, or is mis-spelled. This is a non fatal error, and can be 
recovered by retyping the file specification, including the disk 
drive. Be sure to include the name of the sub-directory that the 
file may be located in. Example: A:\SRCFILES\TEST

     Additional error messages may be generated by turbo-basic 
that are not found here. These will appear as error code numbers. 
Consult your BASIC manual to correct the error conditions, using 
the error code number that  appears on the screen. Be careful if
you do not have access to a Borlan Turbo-Basic manual. While the
error codes are in the vast majority of cases identicle, there can
be subtle differences in the definition of the error code.