POOL
                         A Pool Water Balancing Program

                                       by
                                  Joe McDaniel
                                 209 Oak Avenue
                               Baltimore, MD 21208

        Purpose
             POOL is designed to aid in the management of a swimming pool 
        by  performing  the  calculations to achieve a  "balanced"  pool. 
        Balancing  a pool is desirable for several reasons:  the Ph  will 
        remain much more stable, the pool itself (whether lined, painted, 
        or  plastered) and the filtering equipment will last  longer  and  
        filter  runs (between backwashing or cleaning of filters) will be 
        longer.  In  general,  balancing requires only a  relatively  few 
        dollars  and  results in great savings of  time,  chemicals,  and 
        money.

        Testing the Water
             To  use the POOL program,  it will be necessary to have  the 
        ability  to perform tests on your pool for free  chlorine,  total 
        chlorine,  Ph,  total alkalinity,  calcium hardness, and cyanuric 
        acid (or stabilizer) levels. The  Taylor Chemicals, Inc. test kit 
        model 2000 with the 2001 - Total Alkalinity Test Pack, the 2002 - 
        Cyanuric  Acid Test Pack,  and the 2003 - Calcium  Hardness  Test 
        Pack  is  very suitable.  Other companies make similar test  kits 
        which  will also work.  The cheap test kits sold at Murphy  Mart, 
        etc. are not suitable!

             Perform all the necessary tests,  following the instructions 
        with your test kit.  Record the readings for entry into the  POOL 
        program.  POOL  will also ask for your pool temperature.  A  pool 
        thermometer is desirable but a guess is sufficient.

        Using the POOL Program
             POOL  is  run by entering the command:  BASIC POOL with  the 
        POOL program on the same disk as BASIC.  If you have gotten  this 
        far (by getting POOL from a BBS) you should be able to figure out 
        how to run POOL under other circumstances.

             POOL  will prompt you to enter all required readings.  After 
        entry,  POOL  will perform the calculations necessary to  balance 
        your  pool  water.  The  recommended  actions  should  always  be 
        examined for reasonableness.  If the amounts of water to pump out 
        or  the  chemicals to add seem wrong,  recheck the input  to  the 
        program, redo the tests, or consult your pool manual. (The Taylor 
        test  set  comes  with a very handy  reference  manual  for  pool 
        management.)  The  possibility of errors in the POOL  program  is 
        always present.

             If  one  of the actions is to drain some of  the  water  and 
        refill,   do  not  add  any  other  chemicals  before  refilling, 
        retesting, and running POOL again.



                                        1




        Disclaimers, References, Etc.
             POOL  started out as a program published by Olin Corporation 
        in  their POOLIFE magazine.  (Mailed to all pool owners  free  of 
        charge.  Address is Poolife,  120 Long Ridge Road,  Stamford,  CT 
        06904-1355)  The original program has been modified and  enhanced 
        for my own needs and to remove somewhat the use of only HTH brand 
        (sold  by Olin) chemicals.  The original program used some rather 
        gross estimates for some values and the Taylor figures have  been 
        integrated  where there are any differences.  The suggested doses 
        have  been computed for HTH brand and generic chemicals  in  most 
        cases.

             For initial balancing, large amounts of Calcium Chloride and 
        Sodium  Bicarbonate  will be needed (if you have a  large  pool). 
        Using  HTH  or  any other brand chemicals is a  waste  of  money, 
        generally. Go to a local chemical supplier (most in Baltimore, MD 
        where  I  live  seem  to sell cleaning supplies)  and  buy  large 
        quantities  of these two chemicals.  I buy by the 100 pounds  and 
        the costs are about $20 per 100 pounds of each.

              Cyanuric Acid may be available as a generic rather than  as 
        a branded version. In any case, only a few (up to 20 pounds) will 
        generally be needed although the cost is high (per pound).

             Chlorine  is  quite expensive as  Calcium  Hypochlorite.  By 
        stabilizing  (using Cyanuric Acid) you can reduce the  quantities 
        needed considerably.  Also,  the use of stabilized chlorine (also 
        know  as  tri-chlor and hundreds of other names) will reduce  the 
        quantities  needed  (on a poundage basis) although the  cost  per 
        pound  is higher.  The savings will usually be greater than  when 
        using Calcium Hypochlorite (HTH,  for instance).  Again,  generic 
        tri-chlor is available.

             I  have  had  good  success for the  last  two  years  using 
        Potassium  Monopersulfate  instead of "shock" treating  my  pool. 
        This  chemical  reacts  with the  chloramines  to  oxidize  them, 
        releasing  the  chlorine into the water for reuse.  The  standard 
        treatment  for  chloramines  is  to  superchlorinate  by   adding 
        something  like  10  ppm  of  chlorine.  This  is  expensive  and 
        injurious to solar covers,  etc.  The Potassium Monopersulfate is 
        cheap and very effective.  The only drawback so far has been that 
        the  DPD type test kits (like the Taylor) are not compatible (for 
        total chlorine,  at least) with potassium monopersulfate. This is 
        not  too  much  of a problem since the need  for  total  chlorine 
        testing is largely eliminated by having the chemical in the water 
        and oxidizing chloramines continuously.  I bought my supply  from 
        Leslie's (a mail order pool supplier) and have used only about 20 
        pounds  a  year - far less than the amount of  chlorine  chemical 
        that would have been required.

             The  adjustments  suggested by the POOL program for  Ph  are 
        better  determined by use of the Taylor test kit's acid and  base 
        demand  reagents.  The  Taylor method is to add drops of acid  or 
        base reagents to determine how much acid or base will be required 
        to  achieve the correct Ph directly rather than  by  calculation. 


                                        2




        This technique is more accurate than a calculated method. If your 
        test kit has this feature, it is a better way to maintain Ph than 
        by using the POOL program's calculations.

             I  use  an  automatic  feeder for  my  chlorine  (stabilized 
        trichlor).  This has the advantage of maintaining a more constant 
        level  of chlorine in the water,  thereby reducing  the  chlorine 
        usage and problems with algae, bacteria, etc. The floating feeder 
        types are also effective and very cheap - they just can't be used 
        with solar covers.

             The  prices  in the Leslie's catalog are often  better  than 
        those  from  local stores,  even with the costs of United  Parcel 
        Service  added  in.  I have found that some  local  stores,  when 
        confronted with the catalog in hand,  will match the prices  from 
        Leslie's.  One  claim  from the stores is that their  product  is 
        better  than the generic one from Leslie's (other companies  also 
        sell by mail order and have similar pricing). I believe that this 
        claim  is generally without foundation.  I haven't  investigated, 
        but  I'll bet that virtually all the companies buy from only  one 
        or two manufacturers and that the final products differ mostly in 
        packaging.  In any case,  I have had no problems with the generic 
        chemicals  offered by Leslie's or by my local store when  pressed 
        to match the price from Leslie's.

             My  pump  motor  recently  had  to  be  replaced.  (Age  and 
        occasional  immersions  from  being below ground and  pool  level 
        killed  it.)  The  prices  from  the  pool  companies  (including 
        Leslie's) were about $120.  I called a local industrial  electric 
        motor  repair  company  (Electric  Motor in  Baltimore)  and  got 
        estimates of $50 to $80! Again, if you are willing to do a little 
        work  to  bypass the middlemen such as the pool company (or  even 
        Leslie's), you can save a lot.

             Buy  a  winterizing  cover if your pool is large  enough  to 
        justify  the  costs.  The  cost of the cover  will  be  recovered 
        quickly  in  lower  costs  for  balancing  chemicals  (especially 
        Cyanuric Acid) and water (and sewage) charges.  In the fall,  you 
        cover  your  pool  after lowering the water level  to  below  the 
        skimmer.  The cover keeps out leaves and dirt. In the spring, you 
        clean  off  the cover and remove it.  Your pool  water  may  look 
        cloudy,  etc.  but with the filter running and some vacuuming, it 
        will  be  sparkling in about a day.  Once you have  refilled  the 
        pool,  do  the  tests and run the POOL program to  rebalance  the 
        water.  The amounts of Calcium Chloride,  Sodium Bicarbonate, and 
        Cyanuric  Acid  will  be relatively small since all you  need  to 
        balance  is  the  water just used to  refill  back  to  operating 
        levels,  not  the entire water quantity.  A side benefit is  that 
        some  pools will pop right out of the ground if emptied where the 
        water level is high.

             I  offer this program and these notes without claiming to be 
        an expert or that there are no errors, omissions, faults, etc. My 
        own pool (18 by 42 feet,  concrete construction,  painted,  40000 
        gallons)  has  been  better managed using this  program  and  the 


                                        3




        techniques  and sources mentioned above.  When I'v had  problems, 
        Taylor Chemical,  Leslie's,  Poolife,  and my local chemical  and 
        pool  stores have been of value.  I have been operating the  pool 
        for 6 seasons now and the above are the results of my experiences 
        and  mistakes.  I now believe that my knowlege of pool management 
        and  of  sources  for  answers is sufficient  enough  so  that  I 
        purchase on price,  not level of support.  (This is analogous  to 
        buying  your computer by mail order.) My costs for operating  the 
        pool have been lower each year, even with inflation.