@x1CB





     
     
     
     
     
                         The Microcom MNP Library
                      (Microsoft QuickBASIC Version)
     
     
     
                           PROGRAMMER'S MANUAL
     
     
     
     
     
     
     
     
     
     
     
     
     
     
                                Version 1.0
     
                             December 15, 1987
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
                              Microcom, Inc.
                          1400 Providence Highway
                            Norwood, MA 02062






     
     
     The Microcom MNP Library and MNP are trademarks of Microcom, Inc.
     Microsoft and MS-DOS are trademarks of Microsoft Corporation.  IBM is a
     registered trademark of International Business Machines.
     
     
     This manual is not subject to copyright and may be freely copied.
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     Questions relating to the Microcom MNP Library should be directed to
     Microcom at:
     
                              Microcom, Inc.
                       15303 Ventura Blvd., Suite 900
                          Sherman Oaks, CA 91403
                               (818)986-4212






     
     1. INTRODUCTION
     
          The Microcom MNP Library is a set of subroutines which implement the
     stream mode of the link protocol in Microcom Networking Protocol (MNP).
     This mode of the MNP link protocol is appropriate for interworking with MNP
     error-correcting modems or with other software implementations which use
     the Microcom MNP Library or other compatible software.
     
          This version of the library provides a set of assembly language
     routines which are designed to be easily integrated into an application
     program written in BASIC and compiled using the Microsoft QuickBASIC
     compiler (version 1.02 or 2.0).  Through the use of these routines, an
     application is able to perform error-free data communications over a
     physical-connection, such as one established on the public switched
     telephone network.
     
          These MNP Library subroutines are especially for the IBM Personal
     Computer family (and compatibles) under PCDOS (MS-DOS).  Hardware
     facilities for asynchronous communications are required.






     2. LIBRARY MODULES
     
          The Microcom MNP LIbrary is supplied in one of two forms, object
     library only and object library with source.  The source version is de-
     scribed in more detail in a manual addendum supplied as part of the source
     version distribution.
     
          In the case of the object library only form, the distribution diskette
     contains one file, mnpb.lib, which includes the various object modules
     which make up the MNP Library.
     
          When building the executable form of a particular application, the
     mnpb.lib file should be specified if the application calls any MNP sub-
     routine described in this document.  The manner in which library modules
     are specified for inclusion varies according to the linkage editor employed
     in building the application program run module.






     3. LINK MANAGEMENT
     
          In general, the MNP link follows the life of the normal physical-
     connection.  Immediately after the physical-connection is made (e.g. after
     a modem first reports carrier detected), the application must attempt the
     establishment of the Link via the MNPCONNECT subroutine.  MNP-capable
     modems which answer the incoming telephone call, for example, must receive
     the Link establishment sequence within 4 seconds of physical-connection
     establishment.  If a link is not attempted within this period, such modems
     may fall back to a normal connection and it will not be possible to provide
     a reliable connection on that particular call.
     
          Link termination, performed via the MNPDISCONNECT call, should
     immediately precede termination of the physical-connection, i.e. right
     before hanging up the telephone.  Note that the Link is active for the
     entire duration of the physical-connection.
     
          During the data phase of the Link (i.e. after establishment but before
     termination), the Link must be kept running by allowing the Link code to
     execute periodically.  Any of the data phase calls, namely MNPSEND,
     MNPRECEIVE, MNPSTATUS, and MNPBREAK, will accomplish this.  One of these
     routines must be called every 250ms or so which means that the Link code
     gets a chance to run about 4 times per second.  The absolute interval is
     not critical and it may be possible to reduce the frequency as well and
     still get reasonable performance.  Polling the Link code, however, must
     occur with a predictable frequency otherwise the Link may be lost.  When
     the Link is lost, an MNP error-correcting modem may clear the call.
     
          When a Link is in progress, all line I/O is performed via the
     appropriate MNP call rather than by using the BASIC COM file mechanism.
     The BASIC COM file, however, must remain open.
     
          Data sent and received on the Link will be "chunked" depending on the
     number of bytes which happen to be sent in a single data message.  The
     maximum amount in a single message is 64 bytes.  This "chunking" is not
     noticeable to the sender but can be perceived by the data receiver.
     Strings of data may be split over more than one data message and some
     messages may have to be sent more than once when there is noise on the
     connection.  Retransmission can be seen by the application as an
     interruption, possibly in the middle of some data string.  The application
     should be examined to see if there are any cases involving timing
     dependencies which could be adversely effected by this kind of irregularity
     in the data flow.






     4. LINK INTERFACE SUBROUTINES
     
     4.1  Link Establishment - MNPCONNECT
     
          MNPCONNECT is used to establish a Link.  It is called after the
     physical-connection has been established.  It can take up to 5 seconds for
     an MNPCONNECT call to complete.
     
          MNPCONNECT has the following parameters:
     
               RATE - an integer which indicates the speed of the
                      physical-connection, as follows:
     
                          1 = 110 bps
                          2 = 300 bps
                          3 = 1200 bps
                          5 = 2400 bps
     
                      [Note: Other speeds are not supported in this
                       version of the Microcom MNP Library.]
     
               FORMAT - an integer which indicates the data format,
                        as follows:
     
                         0 = 8 data bits, no parity
                         1 = 7 data bits, even parity
                         2 = 7 data bits, odd parity
                         3 = 7 data bits, mark parity
                         4 = 7 data bits, space parity
     
                      [Note: In this Library version, once the Link
                       is established, it is not possible to change
                       format.]
     
               PORT -  an integer which indicates the communications
                       port, as follows:
     
                         1 = COM1
                         2 = COM2
     
                      [Note: This Library version does not support
                       other comm ports.  Also, COM2 cannot be speci-
                       fied if no COM1 is present in the system.]
     
               MODE - an integer which indicates the role in link
                      establishment, as follows:
     
                         0 = link initiator (caller)
                         1 = link accepter (answerer)
     






               RETCODE - an integer returned to the caller which
                         indicates the result of the link
                         establishment attempt, as follows:
     
                         0 = success (link established)
     
                         -64 - failure, no additional info
                         -65 - failure, timeout (no remote response)
                         -66 - failure, physical-connection lost
                               (carrier lost)
                         -70 - failure, incompatible MNP
                         -72 - failure, remote protocol error
     
                      [Note: -70 and -72 should never occur.]
     
     
          MNPCONNECT is called as follows:
     
              CALL MNPCONNECT(RATE,FORMAT,PORT,MODE,RETCODE)






     4.2  Link Termination - MNPDISCONNECT
     
          MNPDISCONNECT has two functions, to send the appropriate protocol
     message to the other side to indicate Link termination and to reset the PC
     interrupt environment.  MNPDISCONNECT must always be called if MNPCONNECT
     had been called previously.  This is so even for establishment failure or
     for loss of the physical-connection (i.e. carrier lost).
     
          MNPDISCONNECT has no parameters.  It is called as follows:
     
                            CALL MNPDISCONNECT






     4.3  Send Data - MNPSEND
     
          MNPSEND is called to copy data to be sent on the Link from the
     application into the MNP transmit buffer.
     
          MNPSEND has parameters as follows:
     
               SNDBUF$ - the BASIC string from which transmit data
                         is to be copied.
     
               BUFLEN - an integer which indicates the maximum
                        number of data bytes which can be copied
                        from SNDBUF$.
     
               RETCODE - an integer returned to the caller which
                         indicates the number of bytes copied from
                         SNDBUF$ or a Link error condition, as follows:
     
                         positive int = number of bytes copied from
                                        SNDBUF$.  0=no bytes copied
     
                         -64 = link terminated, retransmission limit
                               exceeded
                         -65 = link terminated, unable to send
                         -66 = link terminated, carrier lost
                         -67 = link terminated, remote disconnected
     
          MNPSEND is called as follows:
     
                  CALL MNPSEND(SNDBUF$,BUFLEN,RETCODE)






     4.4  Receive Data - MNPRECEIVE
     
          MNPRECEIVE is called to copy data received on the Link into the
     application.  MNPRECEIVE transfers all available data up to the size of the
     application buffer.  MNPRECEIVE returns immediately if no data is
     available.
     
          MNPRECEIVE has the following parameters:
     
               RCVBUF$ - the BASIC string into which received
                         data is to be copied.  This string must
                         be created by the application to be as
                         long as the value of BUFLEN.
     
               BUFLEN - an integer which indicates the maximum
                        number of data bytes which can be copied
                        into RCVBUF$
     
               RETCODE - an integer returned to the caller which
                         indicates the number of bytes copied into
                         RCVBUF$ or a Link error condition, as follows:
     
                         positive int = number of bytes copied into
                                        RCVBUF. 0=no bytes available.
     
                         -64 = link terminated.  retransmission limit
                               exceeded
                         -65 = link terminated, unable to send
                         -66 = link terminated,  carrier lost
                         -67 = link terminated, remote disconnected
     
          MNPRECEIVE is called as follows:
     
                  CALL MNPRECEIVE(RCVBUF$,BUFLEN,RETCODE)






     4.5  Link Status - MNPSTATUS
     
          MNPSTATUS is called to return to the application the status of the
     Link and to read parameters which indicate the availability of received
     data or the ability to enqueue data for transmission.
     
          MNPSTATUS has parameters as follows:
     
               PSTATUS - an integer which indicates the condition of
                         the physical-connection, as follows:
     
                         0 = not connected (carrier not present)
                         1 = connected (carrier present)
     
               LSTATUS - an integer which indicates the condition of
                         Link, as follows:
     
                         0 = link not established (i.e. link
                             terminated)
                         1 = link established
     
               SCOUNT - an integer which indicates the number of
                        bytes free in the Link send buffer.  This is
                        the number of bytes which can be completely
                        copied to the Link transmit code via an
                        MNPSEND call.
     
               RCOUNT - an integer which indicates the number of
                        received data bytes which are available to
                        be copied into the application via MNPRECEIVE
     
               ALLSENT - an integer which indicates whether or not
                         all data passed to the Link code has been
                         successfully sent and acknowledged, as
                         follows:
     
                         0 = all data not sent
                         1 = all data sent
     
     
          MNPSTATUS is called as follows:
     
           CALL MNPSTATUS(PSTATUS,LSTATUS,SCOUNT,RCOUNT,ALLSENT)






     4.6  Send Signal - MNPBREAK
     
          MNPBREAK is called to send a signal to the remote DTE.  When the
     remote side is an MNP error-correcting modem, an MNPBREAK call causes the
     remote modem to send a break signal (continuous spacing) to its attached
     DTE.
     
          MNPBREAK employs the MNP Link Protocol's reliable attention
     mechanism in 'destructive mode'.  That is, when MNPBREAK is called, the
     Link is reset and any data pending transmission on the link is discarded as
     is any received data which has not been read via the MNPRECEIVE subroutine.
     Data may also be discarded at the remote side of the Link.
     
          MNPBREAK has one parameter as follows:
     
               RETCODE - an integer returned to the caller which
                         indicates the result of the MNPBREAK call
                         or a Link error condition, as follows:
     
                         0 = break initiated
     
                         -64 = link terminated, retransmission limit
                               exceeded
                         -65 = link terminated, unable to send
                         -66 = link terminated, carrier lost
                         -67 = link terminated, remote disconnected
                         -75 = break not supported (remote did not
                               negotiate attention support for this
                               Link)
                         -76 = previous break still in progress
     
     
          MNPBREAK is called as follows:
     
                          CALL MNPBREAK(RETCODE)
     
     
     
          [Note that the MNP Library does not support receipt of the MNP
     attention message and hence it is assumed that MNPBREAK will only be
     employed when the remote side of the connection is an MNP error-correcting
     modem.]






     5. SAMPLE PROGRAM
     
          A demonstration program is provided on the distribution diskette in
     the file testb.exe.  A listing of this program follows in the next pages.
     
     '==========================================================================
     '
     '       MNP INTERFACE TEST PROGRAM
     '
     '       This test program is a simple terminal emulator which
     '       exercises the assembly language routines which interface
     '       QuickBASIC to the MNP library.
     '
     '             - G. Pearson, September 1986
     '
     '==========================================================================
     
     '----- Data declarations
     defint a-z
     
     '----- Initialize
     rbuflen=80                              ' make receive buffer be a
     rcvbuf$=string$(rbuflen,32)             '   a blank string of right
                                             '   length
     
     '----- Display herald screen
     cls                                     ' clear screen
     print "-------------------------------------------------------------------"
     print
     print "                     MNP Link Demonstration Program"
     print
     print "        This simple terminal emulation program demonstrates the use"
     print "        of the Microcom MNP Library to provide error-free data"
     print "        com munications."
     print
     print
     print "        Hit any key to begin..."
     print
     print "-------------------------------------------------------------------"
     
     startloop:
         if inkey$="" then goto startloop
     print
     
     '----- Get user parameter selections
     ' Comm port number...
     parms:
         input "Enter comm port number (1/2)";port$
         if (port$="1" or port$="2") then goto parms1 _
         else goto parms
     






     ' Port speed...
     parms1:
         input "Enter port speed (300/1200/2400)";spd$
         if (spd$="300" or spd$="1200" or spd$="2400") then goto parms2 _
         else goto parms1
     
     ' Telephone number...
     parms2:
         input "Enter telephone number of MNP remote";number$
         if number$="" then goto parms2
     
     '----- Open comm file
     opncom:
         open "com"+port$+":"+spd$+",n,8,1,cs,ds,cd" as #1
     
     '----- Initialize modem (Hayes 2400-compatible assumed)
     a$=""
     print #1,"ATE0Q0V0"                     ' no cmd echo,result codes,
                              '   numeric codes
     for i=1 to 1000:next i                  ' let cmds get out...
     close #1                 ' trash modem response
     open "com"+port$+":"+spd$+",n,8,1,cs,ds,cd" as #1     ' re-open modem
     
     '----- Dial MNP-capable remote and wait for connect
     print                                   ' inform user
     print "dialing "+number$+"..."
     print #1,"ATDT"+number$                 ' send dial string to modem
     print "-- waiting for physical-connection establishment..."
     connwait:                               ' wait for modem or user abort
         if (inkey$<>"") then goto xitpgm    ' any user input will abort...
         if loc(1)=0 then goto connwait
         a$=input$(1,#1)                     ' get modem response code
         if (a$<>"1") then goto connwait     ' wait till connect or user abort
         print "physical-connection established."
     
     '----- Initiate Link
     startlink:
         for i=1 to 10000:next i             ' let line settle...
         print "-- starting link..."         ' pass line speed
         rate=5                              ' assume 2400 bps
         if (spd$="1200") then rate=4        ' adjust for other speeds...
         if (spd$="300") then rate=2
         format=1                            ' assume 7 bits, even parity
         if (port$="1") then port=1 else port=2 ' pass comm port number
         mode=0                              ' caller is link initiator
         call mnpconnect(rate,format,port,mode,retcode) ' try for link
         if retcode<>0 then goto xitpgm     ' just quit if failure
     
     '----- Link established. Notify user and wait to continue.
     print
     print "***** Link established.  Hit any key to continue... *****"






     '----- Now wait for user input before starting terminal emulation.
     ' Note that the application must poll the link code while waiting
     ' in order to keep the link alive.
     startwait:
         call mnpstatus(pstatus,lstatus,scount,rcount,allsent)
         if pstatus=0 then print "carrier lost":goto xitpgm
         if lstatus=0 then print "link lost":goto xitpgm
         if inkey$="" then goto startwait
     
     '----- Start terminal emulation with a clear screen and tell the
     ' user how to terminate the program.
     cls
     print "Begin terminal emulation.  A slash (/) will exit program."
          
     '----- Data phase of Link
     mainloop:
         retcode=0
         call mnpstatus(pstatus,lstatus,scount,rcount,allsent)
         if (pstatus=0) then print "carrier lost":goto xitpgm
         b$=inkey$
         if (b$="") then goto getcomm
         if (b$="/") then goto xitpgm
     
     sndagain:
         call mnpsend(b$,len(b$),retcode)
         if (retcode<0) then _
          print "link failed on send": _
          goto xitpgm
         if (retcode<>len(b$)) then goto sndagain
         retcode=0
     
     getcomm:
         if (rcount>0) then call mnpreceive(rcvbuf$,rbuflen,retcode)
         if (retcode<0) then _
          print "link failed on receive": _
          goto xitpgm
         if (retcode>0) then print using "&";left$(rcvbuf$,retcode);
         goto mainloop
     
     '----- Exit
     xitpgm:
         print
         print "-- disconnecting link..."
         call mnpdisconnect
         print
         print "end of test program"
         close
         system