LPTPORT                                 John Dickinson
          Command                                         No. 15

          _______________________________________________________

          Purpose:  Permits alternate use of two parallel
                    printers (e.g., letter- and draft-quality
                    units) with software that is normally limited
                    to using LPT1:.

          Format:   LPTPORT

          Remarks:  Certain software, e.g., the PC-DOS Shift-
                    PrtSc routine, does not recognize a command
                    such as

                    A>MODE LPT1:=LPT2:

                    To use such software with two different
                    printers normally requires changing physical
                    connections.

                    LPTPORT.COM provides a software toggle that
                    interchanges the internal DOS I/O addresses
                    of LPT1: and LPT2:.  After entering the
                    LPTPORT command, a second printer, connected
                    to LPT2:, will receive program output
                    nominally directed to LPT1:.  Entering the
                    LPTPORT command a second time restores the
                    original port assignments.

                    Notes:

                    1.   Certain internal print-spooling
                         programs, such as those supplied with
                         add-on memory board cards, read the port
                         address assignments at boot-up time and
                         do not thereafter look at the low-memory
                         area of DOS to find them.  With such
                         programs you will have to run LPTPORT
                         before the print spoolers are loaded in
                         order to change the effective port
                         assignments.