AUTOBOOT


Description:
-----------

AUTOBOOT.EXE is a small TSR designed to force a boot at a specified time of
day.

Originally designed to boot gateway servers to overcome a bug in their
software causing sessions to hang when users powered off their machines while
their lines were still active -- since our network is basically idle during
the night, we use this program to boot the servers (unattended) each morning
at 4 a.m., cleaning all lines up by the time people start logging in.  Can
also be used to clear things up (like putting Procomm Host Mode to sleep), or
for security measures if you leave your machine running "sensitive" stuff
when you go home (or go to work).

The program uses 3920 bytes of memory and chains to the timer interrupt (1Ch).
It is also an old main-framer's 3rd Turbo-C program as part of his migration
from big iron (forgiving) to little iron (very stubborn, but popular).


Usage:
-----

Command line format: AUTOBOOT HH:MM x
                        where HH = hour of the day,
                              MM = minute of hour,
                              x  = optional "W" or "C" (anycase),
                                   W forces warm boot, C forces cold boot.
     
HH max is 23, MM max is 59, colon ":" is required between HH and MM.  If the
optional "x" field is not supplied, the program defaults to a "cold" (power-
up) type of boot.  To conserve space the program only sets Errorlevel when
an input error occurs, as the following sample autoexec.bat file illustrates.

Examples: (to warm boot at 11 p.m.): AUTOBOOT 23:00 w
          (to cold boot at 1 a.m.):  AUTOBOOT 01:00 C or AUTOBOOT 01:00
      
Sample AUTOEXEC.BAT file to boot at 04:00:

@echo off
PATH=C:\DOS;C:\PROGS;C:\BAT;C:
echo Installing Auto-Boot Package...
AUTOBOOT 04:00
if errorlevel 1 goto nogood
echo Auto-Boot Package Installed Successfully.
goto done
:nogood
echo Input Error -- Auto-Boot NOT Installed.
:done
prompt $P$G
\mouse1\mouse
menu


--------------------------------------------------------------------------------
Placed in Domainican RePublic (free, grin), by Dave Durnbaugh, June 1989
                                               Eden Prairie,  Muskeetasota