FAKEY

                          Keyboard Phantom Typist

                                Version 1.0



(C) COPYRIGHT 1986 by System Enhancement Associates; ALL RIGHTS RESERVED



FAKEY is used to fake sequences of keystrokes.  It is especially useful in 
batch files, where it can be used to "pre-load" input for programs.  It is 
faking it at the point where BIOS is called.  It will not affect programs 
that bypass BIOS for their input.  FAKEY can fake keyboard input for almost 
any program, except for certain resident utilities.  


FAKEY takes one or more arguments, separated by spaces.  Each argument can 
be any one of the following:

1)  A text literal enclosed in quotes.  See below.

2)  A decimal number, indicating the ASCII value of a character.

3)  A hexadecimal number of up to four digits, preceeded by an ampersand.  

4)  A mnemonic value indicating a particular keystroke.

None of these are case sensitive, except literal text in quotes.  Hex 
digits, mnemonics, and so forth can be entered in any combination of upper 
and lower case.  

If an argument indicates a character value, then the character value is 
filled out to include a scan code value.  Where more than one scan code is 
possible (such as Backspace or Ctrl H), the more "conventional" choice is 
made (ie. Backspace instead of Ctrl H, top row instead of number pad, etc.) 

A text literal is enclosed in quotes, and may contain special sequences.  
The special sequences currently defined are: 

1)  An uparrow followed by a character from A to Z (in this case really "at 
    sign" to "underline"), indicating the equivalent control key.  

2)  An exclamation mark followed by a digit or a character from A to Z,
    indicating the equivalent alter key.

3)  A backslash followed by another character.  Defined uses are:

    a)   \r   for a return or enter
    b)   \t   for a tab
    c)   \b   for a backspace
    d)   \e   for an escape
    e)   \anything else, for a literal character.  Thus \" is a quote, \\ 
         is a backslash, \! is an exclamation mark, etc.


A mnemonic can be an uparrow, exclamation mark, or backslash followed by a 
character, in which case it means the same thing as in a text literal.  The 
following additional mnemonics are also defined: 

    Standard ASCII mnemonics:

         NUL SOH STX ETX EOT ENQ ACK BEL 
         BS  HT  LF  VT  FF  CR  SO  SI
         DLE DC1 DC2 DC3 DC4 NAK SYN ETB 
         CAN EM  SUB ESC FS  GS  RS  US
         SP  DEL

    Cursor movement keypad mnemonics:

         UP DOWN LEFT RITE HOME END PGUP PGDN

    Function key mnemonics:

         Fn   for normal
         Sn   for shifted
         Cn   for control
         An   for alter

              Where "n" is a number from 1 to 10.  Ie. A10 means Alt F10.

    Special mnemonics:

         TOSS      Causes all previous pending keystrokes to be thrown 
                   away.  Does not affect the sequence being defined.

         WAIT <n>  Causes a pause for <n> seconds in the input stream.  
                   Keystrokes will not appear to be available for the 
                   duration of the wait.  The maximum wait is 255 seconds.  

         BOOT      Causes a warm system boot, as if the user had typed 
                   "Ctrl-Alt-Del".


Notes on special mnemonics:

    The TOSS mnemonic takes effect at the point where FAKEY is run.  It 
    serves to discard faked keystrokes which an earlier program didn't use.  

    The other special mnemonics take effect at the point where they are 
    first scanned by the operating system.  This is not always when you 
    might think.  DOS (along with many applications programs) scans the 
    keyboard buffer to see if anything is pending at many points, so things 
    may take effect sooner than you would expect.  For example, if your 
    batch file contained: 

         fakey ^C
         myprog

    then "myprog" would not be run.  DOS would check the keyboard after 
    running FAKEY and before running the next program, and see the pending 
    control C.  Your batch file would stop while DOS asks: 

         Terminate batch file (y/n)?

    You probably don't want that.  So instead, you should say:

         fakey wait 1 ^C
         myprog

    This would cause a one second delay before the control C shows up in 
    the keyboard buffer.  

    If this doesn't make sense, then don't worry too much.  This is all 
    meant to address a few special cases which don't normally arise.  


Example:

    Here's an example of a batch file to delete all of the files in a 
    directory, without waiting for DOS to ask for confirmation: 

         fakey "y\r"
         del %1
         fakey toss

    Assuming you named the file ZAPDIR.BAT, then typing ZAPDIR X would give 
    the DOS command "del X".  When DOS stops to ask "Are you sure?", it 
    will think you pressed "y", and continue.  

    In this example we ended the file with "fakey toss".  This is so that 
    if DOS doesn't ask for confirmation (maybe X is a file instead of a 
    directory), the "y" won't be left hanging around.  



Hexadecimal literals:

    These can be used to fake any keystroke whatsoever.  Use the table 
    following to pick out the keystroke you want.  For example, a shifted 
    keypad 5 would be: 

         fakey &4C35

    A table entry of "--" means you can't get that combination out of BIOS.



    BIOS keystroke codes, hexadecimal

    Key      Normal         Shift          Control        Alter

    Esc      011B           011B           011B            --
    1!       0231 '1'       0221 '!'        --            7800
    2@       0332 '2'       0340 '@'       0300           7900
    3#       0433 '3'       0423 '#'        --            7A00
    4$       0534 '4'       0524 '$'        --            7B00
    5%       0635 '5'       0625 '%'        --            7C00
    6^       0736 '6'       075E '^'       071E           7D00
    7&       0837 '7'       0826 '&'        --            7E00
    8*       0938 '8'       092A '*'        --            7F00
    9(       0A39 '9'       0A28 '('        --            8000
    0)       0B30 '0'       0B29 ')'        --            8100
    -_       0C2D '-'       0C5F '_'       0C1F           8200
    =+       0D3D '='       0D2B '+'        --            8300
    BkSpc    0E08           0E08           0E7F            --
    tab      0F09           0F00            --             --
    q        1071 'q'       1051 'Q'       1011           1000
    w        1177 'w'       1157 'W'       1117           1100
    e        1265 'e'       1245 'E'       1205           1200
    r        1372 'r'       1352 'R'       1312           1300
    t        1474 't'       1454 'T'       1414           1400
    y        1579 'y'       1559 'Y'       1519           1500
    u        1675 'u'       1655 'U'       1615           1600
    i        1769 'i'       1749 'I'       1709           1700
    o        186F 'o'       184F 'O'       180F           1800
    p        1970 'p'       1950 'P'       1910           1900
    [{       1A5B '['       1A7B '{'       1A1B            --
    ]}       1B5D ']'       1B7D '}'       1B1D            --
    enter    1C0D           1C0D           1C0A            --
    Ctrl      --             --             --             --
    a        1E61 'a'       1E41 'A'       1E01           1E00
    s        1F73 's'       1F53 'S'       1F13           1F00
    d        2064 'd'       2044 'D'       2004           2000
    f        2166 'f'       2146 'F'       2106           2100
    g        2267 'g'       2247 'G'       2207           2200
    h        2368 'h'       2348 'H'       2308           2300
    j        246A 'j'       244A 'J'       240A           2400
    k        256B 'k'       254B 'K'       250B           2500
    l        266C 'l'       264C 'L'       260C           2600
    ;:       273B ';'       273A ':'        --             --
    '"       2827 '''       2822 '"'        --             --
    `~       2960 '`'       297E '~'        --             --
    l shift   --             --             --             --
    \|       2B5C '\'       2B7C '|'       2B1C            --
    z        2C7A 'z'       2C5A 'Z'       2C1A           2C00
    x        2D78 'x'       2D58 'X'       2D18           2D00
    c        2E63 'c'       2E43 'C'       2E03           2E00
    v        2F76 'v'       2F56 'V'       2F16           2F00
    b        3062 'b'       3042 'B'       3002           3000
    n        316E 'n'       314E 'N'       310E           3100
    m        326D 'm'       324D 'M'       320D           3200
    ,<       332C ','       333C '<'        --             --
    .>       342E '.'       343E '>'        --             --
    /?       352F '/'       353F '?'        --             --
    r shift   --             --             --             --
    PrtSc    372A '*'        --            7200            --
    Alt       --             --             --             --
    spacebar 3920 ' '       3920 ' '       3920 ' '       3920 ' '
    CapsLock  --             --             --             --
    F1       3B00           5400           5E00           6800
    F2       3C00           5500           5F00           6900
    F3       3D00           5600           6000           6A00
    F4       3E00           5700           6100           6B00
    F5       3F00           5800           6200           6C00
    F6       4000           5900           6300           6D00
    F7       4100           5A00           6400           6E00
    F8       4200           5B00           6500           6F00
    F9       4300           5C00           6600           7000
    F10      4400           5D00           6700           7100
    NumLock   --             --             --             --
    Scroll    --             --             --             --
    7 Home   4700           4737 '7'       7700            --
    8 up     4800           4838 '8'        --             --
    9 PgUp   4900           4939 '9'       8400            --
    grey -   4A2D '-'       4A2D '-'        --             --
    4 left   4B00           4B34 '4'       7300            --
    5         --            4C35 '5'        --             --
    6 right  4D00           4D36 '6'       7400            --
    grey +   4E2B '+'       4E2B '+'        --             --
    1 End    4F00           4F31 '1'       7500            --
    2 down   5000           5032 '2'        --             --
    3 PgDn   5100           5133 '3'       7600            --
    Ins      5200           5230 '0'        --             --
    Del      5300           532E '.'        --             --