JRCONFIG Version 2.14

        This  device  driver  will  make  the configuration during the boot
        process quick and easy for an IBM PCjr.

        If you use this program, please send a contribution of $10 to

                Larry Newcomb
                9210 Adelaide Dr.
                Bethesda, Md.  20817

        This contribution will encourage me  to  continue  to  enhance this
        program, and  to write other programs for the PCjr. If you have any
        suggestions for future enhancements or other utility programs, send
        me a letter and I will consider them.

          New to version 2.15:

        1 In STATLIN,  the screen blanker is now optional; ie, you must use
          the -b option to activate the screen blanker.
          Also there is a new option (-a) to specify if you want to use the
          software or hardware method for blanking the screen.

        2 In  STATLIN,  there  is  a  new  option (-g) to toggle the Nickel
          Express into and out of Turbo mode.

          New to version 2.14:

        1 Fixed bug in JRCONFIG that caused the system  to lock  up if the-
          v option was used with a value less than -v16.

        2 Fixed bug in STATLIN that caused STATLIN to disable itself if the
          -s option in JRCONFIG was less than the default value. Although it
          is not a bug, STATLIN can cause problems if the -v option is used
          in JRCONFIG with a value less than -v8.

          New to version 2.13:

        1 -a & -b will move the screen to the left or right.

        2 The -x option will allow the step rate to be selectable. Useful if
          you have a 3.5 inch drive.

        3 The  -p  and  -q  options  have  been  removed.  The print screen
          function was causing problems, so I removed it.  I may  make it a
          separate program and put it in a future release of JRCONFIG.

        4 -f will set the boot screen color.

          New to version 2.12:
                Note: This  version was  never intended  to be released. It
                contains several bugs, one of which resulted in the removal
                of the print screen function.







        1 A device driver to access the ramdisk allocated by JRCONFIG.NRD.

        2 Both versions (.DSK and .NRD) install INT 60. If you use a program
          that also installs INT 60, it is likely to cause a problem. I do not
          know  of  any  programs  that  use  INT  60. If anyone knows of a
          program that uses INT 60, please let me know.

        3 The selective print screen will now save to a disk file.

        4 -q will enable a help line for the selective print screen function.

        5 -n will disable color for monochrome monitors.

        6 STATLIN.COM will display information on line 26.

          New to version 2.11:

        1 I have included the patch to INT 9  that is  supposed to  fix the
          incompatibility with MS QuickBasic. I do not have QuickBasic, so I
          have not tested its effectiveness.

        2 -j will fix the incompatibility problem  that some communications
          programs have with the jr's internal COM port.

        3 -m will turn off the internal speaker.

        4 -g will read a battery backed clock and set the time in DOS.

        5 Install 2 different Version 1.4 of the jrSynchro cartridge.

        6 -p the selective printscreen function has been changed slightly. It
          now checks to make sure it  is in  a compatible  mode. The screen
          attributes are  saved in  a buffer  in the  second text page, and
          restored after printing.

          New to version 2.10:

        1 I have changed the names of the two versions to clear up  some of
          the confusion over which version does what. Also the defaults for
          all options now work the same for both versions.
                JRCONFIG.DSK -    the .DSK signifies a ramDiSK and replaces
                                  the old .SYS extension
                JRCONFIG.NRD -    the   .NRD   signifies   No  RamDisk  and
                                  replaces the old CONFIGJR.SYS

        2 There are  some  programs  that  needed  to  have  MODE  CO80 run
          before they would display boarder colors properly. I believe I have
          fixed the -t3 option so this will no longer be necessary.

        3 -x option to fix the step  rate in  DOS 3.x;  this will  make the
          diskette drives run quieter.

        4 -e option to change the number of entries in the directory of the
          ramdisk.







        5 -y option to install the jrSynchro cartridge if you have it plugged
          in.

        6 -p adds a printer online check for shift-print screen, and will allow
          selection of lines to print.

        7 -h will force the top of DOS user RAM to a given amount.

        8 The DEBUG session for RAM.SYS has  instructions for  changing the
          number of entries you can have in the ramdisk directory.

        9 The check for the PCjr ROM BIOS has been removed.


        You MUST have at least 256K of memory to use this program.

        To use  this driver put the file JRCONFIG.DSK on a bootable DOS 2.1
        disk. On the same disk put the following line as the FIRST  line of
        your CONFIG.SYS file. Then re-boot.

           device=jrconfig.dsk -t2

        This will:
        Install your expansion memory (256K to 640K).
        Install a  91K ramdisk  in your  internal memory (first 128K). This
          ramdisk will take the first available letter after  your physical
          drives (starting with C:). If you only have one drive, drive B: will
          still be a phantom drive. By filling up your first 128K, DOS will be
          forced to  load your  programs into  your expansion memory, which
          will cause your programs to run faster.
        Put your screen in 80 column, low intensity, black & white.

        Options:
        (-a -b -c -d -e -f -g -h -j -k -l -m -n -s -t -v -w -x -y)

        -a      will move the screen n positions to the left, use -an where n
                is from 1 to 7.
        -b      will move the screen n positions to the right, use -bn where
                n is from 1 to 7.
                Note: Both -a &  -b MUST  come after  the -t  option on the
                      command line  in CONFIG.SYS.  If the  -t option comes
                      after either -a or -b, there effect will be cancelled.

        -c      will turn on the keyboard click.

        -d      will cause DOS to  recognize extra  floppy drives,  use -dn
                option, where n is 1 to 4.

        -f      will set the screen color at boot time and when the mode is
                changed. Use -fnnn where nnn is from 0 to 255.

        -e      will set the number of  directory  entries  allowed  on the
                ramdisk. The default is 16 entries. Use -en where:






                      -e1 will allow  32 entries
                      -e2 will allow  64 entries
                      -e3 will allow 128 entries
                Each  entry  uses  32  bytes  of  the  RAM reserved for the
                ramdisk.

        -g      will read the time and date from a battery backed clock and
                set  the  time  and  date  in  DOS.  This was written for a
                JRCAPTAIN with  the clock  chip at  address (37D  hex - 893
                decimal). If  you have changed the jumper to set your clock
                chip at (27D hex - 637 decimal) then use -g637.
                If you have another type of clock board, this option may or
                may not  work for you. If your clock is at another address,
                use -gnnn  where nnn  is the  decimal address  of the clock
                chip.
                If there is a problem reading the clock chip, JRCONFIG will
                beep and give the general error message about  "the options
                list in  CONFIG.SYS". If you are sure that nothing is wrong
                with your clock chip, then it is either at another address or
                it is incompatible with the code in JRCONFIG.

        -h      is not  designed for the average user. I use it for testing
                programs I  want to  put outside  the DOS  user area. -hnnn
                will put  nnn as the top of ram, regardless of how much ram
                you actually have; ie, -h512 will set the top of ram to 512K.
                If you  don't have that much ram, your system will probably
                crash. You should NOT use this  option and  -l at  the same
                time.

        -j      will put  the address  for the  COM port on the motherboard
                into the BIOS data  area  for  COM2.  This  will  solve the
                problem that  some communications  programs have when using
                the COM port on  the  motherboard  and  an  external modem.
                When you specify COM2, the program will now find it; and it
                will use the correct hardware interrupt.

        -k      will set Caps-Lock (Note:  If you  have a  keyboard with an
                indicator light for Caps-Lock, the light will not be turned
                on.)

        -l      will look for extra RAM, starting at 640K and will  stop at
                736K,  and  give  it  to  DOS. (Note: 640K is where the ROM
                stops testing RAM and 736K is  where video  ram "logically"
                starts.)  This option will only perform a superficial check for
                RAM. You will need to use  a ramtest  program to  check for
                bad chips above 640K.

        -m      will turn off the jr's internal speaker. If you run a program
                that turns the speaker back on, it will probably stay on.

        -n      will  prevent   color   modes   for   monochrome  monitors.
                JRCONFIG will  intercept a  call to change to CO40 or CO80,
                and make a call for BW40 or BW80. It will have no effect on
                graphics modes.







        -s      sets the size of the ramdisk, use -sn where n is the number
                of K bytes you  want the  ramdisk to  be. The  ramdisk size
                may    be a little larger than the value you put in, because
                of video page boundaries. The default size is 91K for DOS 2.1
                and 79K  for DOS  3.1. (10K is the smallest ramdisk you can
                have, because that is how much  room is  left on  the video
                page  where  IBMDOS.COM  is  loaded  with DOS 2.1, and this
                space can not be  used for  anything else  anyway. With DOS
                3.1  you  get  about  15K, because IBMDOS.COM is larger and
                video ram must be moved to a higher  video page).  There is
                no upper  limit on  the size of the ramdisk (other than the
                amount of RAM you have in your computer).

        -t   will set the video display mode, use -tn where n is:

          Alpha Modes
          0 for 40 X 25 B/W  (Default)
          1 for 40 X 25 Color
          2 for 80 X 25 B/W
          3 for 80 X 25 Color
          Graphics Modes                        You  can   get  some  funny
        looking
          4 for 320 X 200  4 Color              screens when you boot up in
        a
          5 for 320 X 200  B/W 4 Shades   graphics    mode    because   DOS
        expects
          6 for 640 X 200  B/W 2 Shades   to be in Alpha mode.
          7 is not a valid mode
          Extended Graphics Modes
          8 for 160 X 200  16 Color
          9 for 320 X 200  16 Color
         10 for 640 X 200  4  Color

        -v      will reserve video ram, where n is 4 to 96. Normally 16K is
                set aside for video ram, you can either decrease or increase
                this amount with this option. Using -v4  will reserve 4K for
                video, giving you an extra 12K of user ram, but you must not
                use any  graphics modes  or a  program that uses text pages
                other than the first test page. If you  are concerned about
                speed, you may not want to use this option with a value less
                than 16. The extra RAM that you get this way will be in the
                video page,  and that  will be in the first 128K. Any other
                device drivers  and COMMAND.COM  will load  into this area.
                Unless you  have some large device drivers, the regular DOS
                programs you run will start in this low RAM. Don't be fooled
                by the size of the files on the disk. JRCONFIG is over half
                initialization code, the resident portion is less than 2K. Only
                about  3K  of  COMMAND.COM  will  load into low memory, the
                rest is the transient  portion that  is at  the top  of DOS
                memory. High  values are  used for reserving ram to be used
                for high-res graphics (32K) or extra video pages.

        -w      will put a clockwise spinning character in on the top row of






                your screen, use -wnn where nn is the column you want it to
                appear in.

        -x      will set the proper step motor rate in  DOS 3.x,  this will
                make the disk quieter. Note: this will not take effect until
                after you see the initialization message.
                The default step rate for the PCjr is 13; which is the best
                rate for most 5.25 inch drives. If you want to make it some
                other value, use -xnn where nn is from 1 to 15. If you have
                a 3.5  inch drive  that is noisy, using n = 14 may quiet it
                down; although it may make the 5.25 drive slightly noisier.
                You may  need to  experiment with  different values for the
                best value for your combination of drives. If the step rate is
                set wrong  for your  drive it  can become noisy and you may
                have read/write errors, so use this options carefully. Note, if
                you do not specify a step rate, the default value is used.

        -y      will install the jrSynchro cartridge if you have it in a slot.
                If you are not familiar with this cartridge. It replaces the
                keyboard and floppy disk interrupts, and allows the keyboard
                to be used while the disk drive is being accessed. It seems to
                work fine  with DOS  2.1, but  there are some problems with
                DOS 3.1.
                It also will give you a 47 character buffer (DOS gives you 15
                characters) if you install the buffer in the first 64K of RAM.
                Unfortunately, this is very restrictive if you want to force
                your  programs  into  expansion  RAM.  This  is the primary
                reason I install it in JRCONFIG. I allocate the buffer inside
                JRCONFIG, which is always in the first 64K. If you want the
                47  character   buffer,  you   can  put   JRSYN47  in  your
                AUTOEXEC.BAT. I  have used three versions of the cartridge,
                1.2 and two marked 1.4.

                Use  -yn where n is:
                   0      for version 1.2
                   1 or 3 for version 1.4 with parity check
                   2 or 4 for version 1.4 with no parity check

                There are at least 2 versions of 1.4. The version I have used
                for  n=1&2  came  from  PC  Enterprises.  The one for n=2&4
                came from Dave Cox and was  combined in  the same cartridge
                with jrVideo.
                If you have another version, try using one of the available
                options anyway. If you  see  JRSYNC  in  the initialization
                message  that  JRCONFIG  prints,  then  JRCONFIG  found the
                cartridge.  If  your  computer   locks  up,   you  have  an
                incompatible version.

        Cartridge Basic compatibility:
          Cartridge  Basic  is  written  to  run  in  the low RAM of an un-
          expanded PCjr. If you have a copy of  JBASIC.COM, you  can run it
          to enter  Cartridge Basic when using expansion RAM. It is a short
          program that sets up an environment for Cartridge Basic to run in.
          One of the things it does, is to get information from the ramdisk






          device driver about low memory and the video  page. JRCONFIG will
          give it the information it needs to set up the proper environment.
          If you use  JRCONFIG.NRD,  then  you  can  use  LOWRD.SYS  to get
          the  necessary  information  (see  below).  It  also checks for a
          hardware register that is on a MS Booster. If it can not find this
          register, it will abort. Below is a printout of a DEBUG session that
          will remove the check for the  MS Booster,  and change  the drive
          that it  expects the  ramdisk to be. If JRCONFIG is drive C:, you
          can ignore the 2 lines that change the  drive from  C: to  D:. If
          JRCONFIG is  E: then  change the 03 to 05. The forth to last line
          changes  the  name  that  DEBUG  uses  to  DBASIC.COM,   so  that
          DEBUG  will  write  a  new  file.  I  chose  the  name DBASIC.COM
          because this new modified program will work when  JRCONFIG is D:.
          The  6797  at  the  beginning  of  most  lines will probably be a
          different number for your DEBUG session.

        A>debug jbasic.com                start debug session
        -u108b                            un-assemble code
        6797:108B BA3F02    MOV  DX,023F  hardware address on booster
        6797:108E B091      MOV  AL,91
        6797:1090 EE        OUT  DX,AL
        6797:1091 BA3D02    MOV  DX,023D  hardware address on booster
        6797:1094 B05A      MOV  AL,5A    write a byte to the register
        6797:1096 EE        OUT  DX,AL
        6797:1097 EC        IN   AL,DX    read a byte from the register
        6797:1098 3C5A      CMP  AL,5A    compare read to written byte
        6797:109A 750E      JNZ  10AA     jump if they are different
        6797:109C BA070B    MOV  DX,0B07
        6797:109F BB0300    MOV  BX,0003  drive C:
        6797:10A2 B004      MOV  AL,04    read function
        6797:10A4 B444      MOV  AH,44    I/O control
        6797:10A6 CD21      INT  21       get information from ramdisk
        6797:10A8 7306      JNB  10B0     jump if read is successful
        -e1097
        6797:1097  EC.90                  replace read instruction with NOP
        -e10a0                            examine ramdisk drive letter
        6797:10A0  03.04                  change from  C: to D:
        -ndbasic.com                      change name of file
        -w                                write new file
        Writing 15AF bytes
        -q                                quit and return to DOS


        JRCONFIG.NRD (formerly called  CONFIGJR.SYS)  is  the  version that
                will  not  install  a  ramdisk. This version will not cause
                problems with hard disk drivers that insist on being drive C:.
                All the  defaults are  the same as they are in JRCONFIG.DSK
                (incuding the -s option). If you want your hard disk device
                driver  to  load  into  external  memory, do not use the -s
                option. This will waste some of your internal RAM, but your
                hard disk  driver will  run faster.  If you  DO NOT want to
                waste any of your RAM, use -s1 to  make all  RAM usable. If
                you  have  one  of  the  hard  disks that have a ROM on the
                controller, you may still experience some increase in speed






                by  sacrificing  your  internal  memory, because all device
                drivers and COMMAND.COM  will  load  into  external memory.
                You should  experiment to  see if it makes a difference for
                your configuration.

        LOWRD.SYS (LOW  RamDisk) is  a device  driver that  will access the
                ramdisk  allocated  by  JRCONFIG.NRD.  When JRCONFIG.NRD is
                installed, it installs the  code to  operate a  ramdisk and
                allocates memory for it. But since it is a character device
                driver, it can not be operated as a ramdisk (a block device).
                LOWRD.SYS   will    access   the   ramdisk   allocated   in
                JRCONFIG.NRD, but the  drive  letter  will  be  assigned to
                LOWRD.SYS.
                I use  INT 60  to pass  information between  the two device
                drivers. I am not aware of any other programs that  use INT
                60, but  if you have one it could cause problems. LOWRD.SYS
                only uses INT 60 during initialization.  If another program
                installs INT 60 after LOWRD.SYS is installed, it should not
                cause a problem.
                Just add the line

                      device=lowrd.sys

                to  your  CONFIG.SYS.  It  can  be  anywhere  in CONFIG.SYS
                except the first line, and will be assigned the next free drive
                letter by DOS.



        EXAMPLE:
                device=jrconfig.dsk -d2 -t3 -c

        will:
          Tell DOS you have two floppy disk drives.
          Boot up in 80 column color mode.
          Turn on the keyboard click.



        STATLIN.COM is a program that will display a status line on line 26
                of your display. This program uses RAM that is in the second
                test page;  therefore, you  must not  use the  -v option in
                JRCONFIG with a value less than -v6.
                On the left of this line will be the status of your Caps Lock,
                Num Lock, and Scroll Lock keys. A hyphen  will be displayed
                after the key name if in the unlock position and an up arrow
                for the lock position. (I also put the status of the Insert key
                in STATLIN,  but I removed it because some programs did not
                use the keyboard flag to get the status of the  Insert key.
                COMMAND.COM is one of these programs.)
                On the right of the screen will be date and time.
                In  the  center  will  be  the  status  for  the ramdisk in
                JRCONFIG  and  the  ramdisk   RAM.SYS.   When   STATLIN  is
                installed, it  uses INT 60 to tell both ramdisks to display






                there spinning characters in the status line. If you have not
                activated this  function in JRCONFIG with the -w option, it
                will not be displayed in the status line.

          options ( -a -b -c -d -e -f -g )

          -a    determines the type of screen blanker used (see -b option).
                The default type (-a0) is to set all the color attributes to
                black on black. This will  work  only  for  80  column text
                modes. The  attributes are  saved in  the second video text
                page, and restored when  a key  is depressed.  You must not
                use the  -v option with a value less than -v8; a value less
                than -v8  will  probably  cause  your  system  to  lock up.
                Interrupt 10 is monitored to determine when the screen is in
                80 column text mode, and disable the screen blanker when it
                is not.  If a program changes the screen into graphics mode
                directly, you can get a strange looking screen.

                -a1  will  cause  the  hardware  blanking  to  occur.  This
                manipulates the video chip registers to turn the video signal
                off and on. This will work in all video modes;  however the
                bug described in option -b will occasionally occur.

          -b    will blank the screen after a period of inactivity. There are
                18.2 ticks of the  timer every  second (except  during disk
                reads and  writes). Use  -bnnn where  nnn is  the number of
                ticks to count before blanking the  screen (between  32 and
                32000). Whenever the keyboard interrupt (INT 9) or the video
                interrupt (INT 10) is executed, the tick counter will be reset.
                If you run a program that writes directly to the screen, the
                number of ticks will not be reset. This can cause the screen
                to go blank even though something is being written to it. If
                the screen has been blanked, I suggest you  use one  of the
                shift keys to re-display it, because they are "safe" keys to
                touch.

         CAUTION:     If you use the -a1 option. There is an elusive bug in
                      the  screen  blanker.  Sometimes,  when the screen is
                      blank and I press a key to reactivate  it, the screen
                      becomes  all   green  (I  have  a  green  phosphorous
                      monitor). The system is OK, except that the screen is
                      solid green. If I wait until the screen blanks again, it
                      will  appear  when  I  press  a   key.  This  happens
                      infrequently and  I have given up trying to fix it. I
                      believe it may be a  peculiarity  of  the  jr's Video
                      system, and may not be fixable. If I continue to type
                      when the screen is green, everything will work, I just
                      can't see  what I'm typing. If I am at the DOS prompt
                      and type CLS, the screen is reset, and  everything is
                      OK.

          -c    the default  color gives a shade of green that I like on my
                green phosphorous monochrome monitor. If you don't like this
                color,  use   -cnnn  where  nnn  is  the  color  you  want.






                COLOR.COM will show you the color options available. If you
                make an error in the -c parameter, you will get the default
                color.

          -d    will disable the spinning character in RAM.SYS.

          -e    will disable the spinning character in JRCONFIG.

          -f    will speed up the repeat key function.
                -f2   decreases the default delay  between  repeat  keys by
                      about one third.
                -f1   decreases  the  default  delay between repeat keys by
                      about two thirds.
                The status line will be disabled whenever a program is using
                a graphics  mode or any text page other than page one. This
                is not true for  the spinning  characters displayed  by the
                ramdisks. The  -d and  -e options will disable the spinning
                characters in  the  ramdisk  regardless  of  how  they were
                originally installed, because the device drivers are altered by
                INT 60.  Although  it  is  very  clumsy,  you  can  use TRS
                management   programs   such   as  INSTALL  and  REMOVE  to
                remove STATLIN from  memory  and  then  re-install  it with
                different options.  If you do remove STATLIN, the number of
                display lines  will not  be reset  to 25.  However, the DOS
                command CLS will erase what is displayed on line 26.

          -g    If you have a Nickel Express, this option will allow you to
                toggle into and out  of Turbo  mode from  the keyboard, and
                display the status on line 26. Use -gnn where nn is the sum
                of  the  following  numbers  you  want  for  the  "hot  key
                combination".

                 1 right shift key
                 2 left shift key
                 4 Ctrl key
                 8 Alt key

                For example:  use -g3  to toggle the mode by using both the
                left and right shift key

                If you want to  be  able  to  change  modes  from  inside a
                program, use INT 60 with AH set to 08. The AL register will
                return 00 if the result of the toggle is normal mode, or a 01
                of in  Turbo mode. For example: the following piece of code
                could be used to make sure that Turbo mode is set on.

                TOP:  MOV   AH,08       ;toggle function
                      INT   60          ;toggle the Nickel Express
                      CMP   AL,01       ;is it in Turbo mode
                      JNE   TOP         ;no, toggle it again

                I have included 3  programs that  will allow  you to change
                modes in batch files.
                      TOGGLE.COM






                      TB-ON.COM
                      TB-OFF.COM



        FOR BEGINNERS:
        Here is  a quick and easy way to start using this program. Format a
        new disk using the /s parameter. This makes the new disk a bootable
        disk.  Refer  to  the  DOS  manual  if you have not used the FORMAT
        command. Then copy JRCONFIG.DSK to  the  new  disk.  Then  type the
        following three lines from the DOS prompt:

        copy con config.sys
        device=jrconfig.dsk -t3 -c 
        ^Z

        The first line tells DOS to copy from the keyboard to a file called
        CONFIG.SYS. The second line is what is put  into the  file, you can
        add any other options to this line you want. The third line is the end
        of file marker, DOS will add this to the file  if you  press the F6
        function key.


        I hope this is as useful to others as it has been to me. If anyone has
        any questions about this device driver, or if you think there is a bug,
        you  can  write  me  at  the  address  at  the  beginning  of  this
        documentation, or you can leave me  a  message  on  the      jr BBS
        301-468-0984.  This  bulletin  board  is operated by the METRO PCjr
        USER GROUP.



        I have included another program that  I  find  useful.  I  get very
        annoyed  at  the  DOS  message  to  insert  a disk with COMMAND.COM
        and press a key. I think that putting  COMMAND.COM on  all my disks
        a poor answer. I got this program from a bulletin board, and it has
        made my life much easier.

        COMSPEC.COM  -  If  you   put  the   following  3   lines  in  your
        AUTOEXEC.BAT,   you   will   always   have   COMMAND.COM   on  your
        ramdisk that is created with JRCONFIG.DSK.

        1. set comspec=c:\command.com   -  this  line  uses  the  DOS 'set'
                                        command to  tell DOS  where to find
                                        COMMAND.COM;  however,  there  is a
                                        bug  in  DOS  and this doesn't work
                                        by itself.

        2. comspec c:\command.com       - this  line  executes  the program
                                        COMSPEC.COM,   which   causes   DOS
                                        to recognize the 'set' command

        3. copy command.com c:          - this line  copies  COMMAND.COM to
                                        the ramdisk







        NOTE: The  numbers at  the beginning  of the  3 lines  do not go in
        AUTOEXEC.BAT they are only there for  easier reading.If  you have 3
        or 4 floppy drives, then the ramdisk will be D: or E:


        I modified  RAM.SYS to have a spinning character in the upper right
        corner of the screen. It is 2 spaces  to the  right of  the one for
        JRCONFIG.DSK  and  spins  counter  clockwise.  For those of you who
        don't already have it, add the following line to your CONFIG.SYS

          device=ram.sys

        This will install the  device  driver.  You  then  run  the program
        SETRAM.EXE.

          setram d n

        Where d is the drive specifier and n is the number of K bytes to use
        for the ramdisk. The ramdisk will  take the  next available letter;
        therefore, if you have three floppy drives (A: B: C:), JRCONFIG.DSK
        will be drive D:, and RAM.SYS will be E:. You may want  to add this
        line  to  your  AUTOEXEC.BAT.  You  can have RAM.SYS installed more
        than once in CONFIG.SYS, each occurrence  will take  the next drive
        letter.

        You can remove the ramdisk at any time by running

          setram d

        This will free up the ram used by the ramdisk. NOTE: you will loose
        any files that were on it. You can then recreate the ramdisk at any
        time, because the device driver is still installed.

        If you  want to  move the  spinning character  to the left, you can
        change the  position  using  DEBUG.COM.  You  can  also  change the
        number of  directory entries. The following is what a DEBUG session
        will look like. The hyphens are the DEBUG prompt and  are not typed
        in.

          debug ram.sys           This starts the program.
          -e29b             If you want to move the spinning character.
          XXXX:029B   9E.nn DEBUG  responds  with  everything  on this line
                            except the  nn. This will be the  new offset of
                            the  spinning   character.  Subtract  two  from
                            hexidecimal 9E to move one space to the left; ie,
                            nn can be any even number from 0 to 9E.

          -e11f             If you  want to  change the number of directory
                            entries
          XXXX:011F   40.nn Replace 40 (64 decimal) with nn,  the number of
                            entries you  want. I  suggest you only use even
                            multiples of 10 (16 decimal). 80 (128 decimal) is
                            probably as high as you will want to use. Every






                            10 (16 decimal) entries  will use  512 bytes of
                            memory. 
          -w                      This will cause the modified program to be
                                  written to the disk.
          Writing 01EA bytes      The message from DEBUG.
          -q                      Ends the debug session.