Last Rev 1/11/86   

                 UPGRADE YOUR IBM PCjr from 256K to 640K

If you have upgraded your IBM PCjr to 256K with IBM's 128K memory 
sidecar you are in luck.  IBM designed the 128K memory board to 
support both 64K DRAMs and 256K DRAMs although this fact is 
undocumented.  The upgrade requires replacing the 64K DRAM chips 
with 256K DRAM chips, cutting a jumper trace and adding a jumper 
wire.  We, Turning Point Logic Corporation, have upgraded two IBM 
PCjr's from 256K to 640K via this method with excellent results.  
If you are interested in upgrading the directions are given 
below.


WARNING: THIS UPGRADE IS FAIRLY DIFFICULT AND SHOULD ONLY BE 
         ATTEMPTED BY THOSE WITH SUBSTANTIAL SOLDERING AND CHIP 
         REMOVAL EXPERIENCE.  IN ADDITION THIS IS NOT AN IBM 
         SUPPORTED OR ACKNOWLEDGED UPGRADE AND THEREFORE THIS 
         UPGRADE IS PERFORMED AT THE USER'S OWN RISK.


UPGRADE DIRECTIONS

 1.  Tools needed (if you do not have these tools then please do 
     not proceed, this procedure is very delicate and it is VERY 
     EASY to DAMAGE the board).
 
     a.  Small screwdriver
     b.  A good pair of side cutters
     c.  A good soldering iron
     d.  Solder
     e.  A good solder extractor
     f.  An X-acto knife
     g.  A small pair of needle nose pliers or tweezers.
 
 2.  Parts needed.
    
     a.  16 - 16 pin low profile solder tail sockets (sockets are 
         not necessary but are advantageous if a memory chip 
         is bad or found bad).
     b.  16 - 16 256K DRAMs 150 ns
     c.  A small piece of 28 or 30 AGW wire (1" is more than 
         adequate).

 3.  Power down the PCjr and disconnect the power cable.
 4.  Remove the IBM 128K memory option sidecar.
 5.  Completely unscrew the four mounting screws.
 6.  Remove the interior sidecar panel with a small screwdriver.  
     The panel is held in by eight tongs; four on the top, four 
     on the bottom.
 7.  Remove the printed circuit board from the sidecar case.
 8.  Using a pair of side cutters (we highly recommend purchasing 
     a good pair of side cutters, if you do not have a pair, 
     before attempting this step. They cost about $10 and can 
     make the difference between success and failure of this 
     project) completely cut legs of all of the installed 64K 
     DRAM chips.  There are 16 of them.  Do not attempt to 
     salvage the 64K chips.  Cut the legs at the edge closest to 
     the DRAM chip, NOT by the board.
 9.  With good electrical solder, re-tin the solder pad at each 
     cut leg.  This step may seem a waste but makes the overall 
     job of removing the cut legs and solder much, much easier.  
     Please take the time of performing this step - we did not 
     with our first upgrade and it took eight hours to complete 
     compared to two hours for the second upgrade.
10.  With a pair of needle nose pliers or tweezers and a 
     soldering iron, remove each cut leg.  Apply the heat of the 
     soldering iron from the component side or the back side if 
     two people are working.  Grip the leg to be removed with as 
     little contact of the pliers as possible.  The pliers become 
     a heat sink and the less surface contact of the pliers with 
     the leg the less heat drawn off by the pliers.  This goes a 
     lot faster if two people are working, one with the soldering 
     iron and one removing the legs. 
11.  Again re-tin all of the solder pads with a fair amount of 
     clean solder.  Taking this step make take a longer amount of 
     time in the short run but can save a significant amount of 
     time and headache in the long run.
12.  Remove all of the solder from the holes with a solder iron 
     and solder extractor.
13.  With a lightly tinned soldering iron apply enough heat to 
     each hole so the remaining solder melts around the edge of 
     plated through hole and solder pad.
14.  Scan the bare solder holes and surrounding area for lose 
     pieces of solder.  This lose solder can be a killer for it 
     can cause intermittent shorts which are near impossible to 
     locate once the sockets have been soldered in.  Use the 
     soldering iron or an X-acto knife to remove the excess 
     solder.
15.  Solder in the 16 low profile solder tail sockets.
16.  With the component side of the board facing you there is a 
     set of three plated though holes to the right of the big 
     chip (SN74S409N DRAM Controller) with a white rectangle 
     drawn around them.  This is a jumper which determines 
     whether 64K or 256K DRAMs are used.  Currently there is a 
     foil on the component side which connects the left and 
     center hole together.  Completely cut the foil which 
     connects the two holes with an X-acto knife.  Then solder a 
     wire between the center hole and the right hole.  The 
     diagram below should give a better idea where the jumper is
     located.
    __________  __________  ________
                                  _____
     _________________________  -[o-o o]-  <--- Foil Jumper
    |                         |   
    |  SN74S409N              |    
    |_________________________|

17.  Install the 16 256K DRAM chips into their sockets.  Be sure 
     each chip is oriented properly (the notch indicating pin 1 
     should match the printing on the board.  On mine it was 
     toward the connector.)

18.  Set all four DIP switches on the rear board to their on 
     position (OPEN).
19.  Reinstall the PCB back into the sidecar case.  Note that in 
     one of our upgrades we found that the pins of the DIP switch 
     were shorted with the strip of gold "fingers" located in the 
     sidecar case.  The purpose of the gold fingers is to ensure 
     contact between the PCB and the sidecar case.  It may be 
     advisable to place a small piece of electrical tape over the 
     8 pins of the DIP switch on the foil side of the board.
20.  Reinstall the sidecar onto the PCjr.
21.  Reconnect the power cable.
22.  Turn on the PCjr and verify that power-on diagnostics find 
     640K of memory with no errors.
23.  It is then advisable to run the special diagnostics (CTL ALT 
     INS) for several hours.  If the special diagnostics do not 
     find any errors then the memory should be usable.
24.  If you have a Microsoft Booster you can set all switches off 
     (0k position shown in the instruction book) and remove the 
     memory chips to minimize heat and power.

The Following Message Was Taken From Turning Point Logic's BBS On 5-25-86


#205 22 21 May 86  04:49:32  
From: Bert Stark
To:   All
Subj: IBM SIDE CAR UPGRADE

              ATTENTION ! Anyone attempting
         an IBM 128k upgrade to 512k! I
         have found a problem with the
         upgrade file for the IBM sidecar.
         It appears that IBM has made an
         upgrade to its sidecars and its
         later versions (probably dated
         late `83 or `84) .These particular
         boards have a chip missing on the
         board.  This chip is in the first
         horizontal row of chips and four to
         the left of the configuration switch.
              The chip that is missing was
         originally a (74-HC32).  I have
         modifide several boards without
         any trouble but recently have
         encountered 2 with the chip
         missing and a lot of wiring
         changes.  I am appealing to
         anyone that can help with any
         ideas as to how to configure
         the boards.  Desperately need
         a schematic of the old and the
         new boards.please leave a note
         or call collect 512-680-5867 if
         you can help in any way.  Thanks
         !!!  Bert Stark