SUPERCOMM
                  IBM PC Communications drivers
                       (C) Copyright 1986
                          Doctor Debug
                         Pittsburgh, Pa
                       All Rights Reserved

****************************************************************
*                                                              *
*         As  with all the Doctor's software,  SUPERCOMM       *
*         has  been tested and by all indications  works       *
*         as described under all reasonable  conditions.       *
*         However, the good doctor cannot be responsible       * 
*         for damages,  heartbreak,  outbreaks of war or       *
*         acts  of  God  caused  by  the  use  of   this       *
*         software.    As   it   is   FreeWare,   *free*       *
*         distribution  is  encouraged  so long  as  the       *
*         programs  and  documentation  are   unaltered.       *
*         Please  read  the contribution information  at       *
*         the end of this document.                            *
*                                                              *
****************************************************************

     Anyone  who has attempted to use the BIOS Int 14  to  access 
the  IBM's Communications ports knows that these routines are the 
pits.   They  allow  absolutely  no  flexibility,   and  also  no 
interrupt-driven  means  of reading the ports.  SUPERCOMM  is  an 
answer to that problem.

     Running  the  program  SUPER.COM  is  necessary  to   access 
SUPERCOMM.  This  program  can easily be placed in your  AUTOEXEC 
file if you wish.  Part of the program stays resident,  replacing 
Interrupt 14. 

     After  SUPER.COM has been run,  the following functions  are 
available  to the new interrupt 14.  As with the BIOS  interrupt, 
select the function by loading AH with the function number.

Function 0 - set Communications status
     Unchanged from the BIOS Int 14. Does not activate SUPERCOMM. 
This is really just kept for compatability sake.

Function 1 - Transmit Byte
     A  bug  which  caused this function not to  work  with  some 
modems has been fixed, but otherwise this function is the same as 
the BIOS function.

Function 2 - Receive Character
     Removes  a  character  from the circular  input  buffer  and 
returns  it in AL.  If no character is available a timeout occurs 
(bit 7 of AH will be set.)

Function 3 - Port Status
     Unchanged.

Function 4 - Clear Buffer
     Empties  Communications input buffer.  (The buffer is 4K  in 
length)

Function 5 - Block Receive
     Requests a block of data be read from the comm port.
     ENTRY:    DX   =    Port (0 or 1)
               CX   =    Size of block in bytes
               ES:BX=    address to which data will be written

     RETURN:   CX   =    16 bit checksum of data read
               AL   =    Error codes (as in original Int 14)

Function 6 - Block Send
     Sends a block of data over the comm line
     ENTRY:    DX   =    Port (0 or 1)
               CX   =    Size of block in bytes
               ES:BX=    Address of block

     RETURN:   AL   =    Error codes (as in original Int 14)

Function 7 - Buffer Status
     Number of bytes waiting in the buffer returned in BX

Function 8 - Get Character
     Equivalent  of  INKEY from keyboard.  Gets a byte  from  the 
input  buffer if one is waiting.  Byte is returned in AL.  If  no 
byte  was waiting,  AL will have 0.  Don't use this function  for 
data which might be 0.

Function 9 - Set Port
     Port in DX (0 or 1) will be buffered and used by  SUPERCOMM. 
The other will be handled by the old BIOS routines.

Function 12 - Open SUPERCOMM port
     Load  registers  as in old Interrupt 14's Function  0.  Port 
specified in DX becomes active SUPERCOMM port.  System  interrupt 
speed  is kicked up to 4550 times/sec for goof-proof buffering of 
incoming  data.  This function must be called before any  of  the 
input  or output functions are.  While the SUPERCOMM port is open 
overall system speed may lag as much as 35%,  so be sure to close 
the  port (using function 13) when you are through.  Leaving  the 
port  open  at the end of a user program may cause a  crash  when 
another program is loaded.

Function 13 - Close SUPERCOMM port
     Simply load the port (0 or 1) into DX and call this routine. 
System  interrupt  speed is returned to normal and  SUPERCOMM  is 
deactivated until the next Function 12.

Function 14 - Peek buffer
     This  handy function returns the next character in the input 
buffer in AL,  but does not remove the character from the buffer. 
This  means you can look ahead one char into the  buffer.  If  no 
characters are waiting AL will return with a 0.

     SUPERCOMM  returns error codes in AH and AL (unless they are 
returning other information).  These error codes will be the same 
as  those returned by the standard Input/Output routines  of  the 
old Interrupt 14. 

     All this is pretty complicated, which is why I have included 
the file SUPERCOM.PAS, which contains turbo Pascal routines which 
access  these functions.  DUMBTERM.PAS is a demonstration program 
which  is  essentially a plain vanilla  comm  program.  Examining 
these  programs  will  provide some insight  into  how  SUPERCOMM 
works. Be sure to compile any Turbo programs using SUPERCOMM to a 
.COM file before using!  DUMBTERM.COM has been included for those 
out  there  without  a Turbo Pascal Compiler.  Also  included  is 
DUMB.ASM  and DUMB.COM,  which are essentially the same thing  as 
DUMBTERM.PAS only in 8086 assembler.

                         Pascal Routines
                     (Found in SUPERCOM.PAS)

These routines are meant to be called by user programs. The
SUPER.COM Interrupt 14 driver must have been installed to
use any of these routines. Use of these routines without proper
installation of SUPER.COM will produce unpredictable results.
It should be relatively simple to translate these turbo routines
into C or most any other language.

The integers InError and OutError will always contain the error
conditions after every receive or transmit. The bits of these
values are defined as:

     Bit 7 (128)        Timeout
     Bit 3   (8)        Framing Error
     Bit 2   (4)        Parity Error
     Bit 1   (2)        Overrun Error

If the value of InError[port] is 0, then you can be sure that the
last character was received without error.

The value or Port is always 1 or 2.

     Procedure InitPort(port,Baud,Parity,data_bits,stop_bits)
          Baud: integer 300-9600
          Parity: char, E(ven),O(dd),N(one)
          Data_bits: integer, 7 or 8
          Stop_bits: integer, 1 or 2

          This routine initializes the communications port
          to the parameters specified and activates SUPERCOM
          for that port. All of the following functions will
          use the port specified here.

     Function PortStatus(port)

          This function returns the line status and modem control
          status of the comm port specified. The bits returned are
          defined as:

          Bit 15 (negative)  Time out (no device connected)
          Bit 14 (16384)     Transmission shift register empty
          Bit 13 (8192)      Transmission holding register empty
          Bit 12 (4096)      Break detect
          Bit 11 (2048)      Framing error
          Bit 10 (1024)      Parity error
          Bit 9  (512)       Overrun error
          Bit 8  (256)       Data ready
          Bit 7  (128)       Received line signal detect
          Bit 6  (64)        Ring indicator
          Bit 5  (32)        Data set ready
          Bit 4  (16)        Clear to send
          Bit 3  (8)         Delta receive line signal detect
          Bit 2  (4)         Trailing edge ring detector
          Bit 1  (2)         Delta data set ready
          Bit 0  (1)         Delta clear to send

     Procedure XmitCh(ch)

          This Procedure sends the character in ch out the port
          specified.

     Procedure XmitBlk(string)

          This procedure sends the entire string out the comm port.

     Procedure XmitLn(string)

          This is identical to XmitBlk, but adds a CR/LF to the
          end of the block.

      Procedure RecCh(ch)

          This procedure waits until a character is available over
          the comm line and then returns it in ch. If the system times
          out ch will contain a nul (Ascii 0).

     Procedure RecLn(string)

          This is the equivalent of ReadLn over the comm port.
          Be sure to check the InError variable to make sure the
          operation did not time out (no CR was received.)

     Procedure RecBlk(number,String)

          The number of characters specified by number will be
          placed into the string. Be sure to check the InError
          variable to assure that the operation did not time out
          before sufficient characters were received.

     Procedure GrabCh(ch)

          If a character is waiting in the receive buffer it will
          be returned in ch otherwise ch will contain a nul character.

     Procedure PeekBuff(ch)

          Identical to GrabCh but the character is not removed
          from the buffer.

     Procedure ClearBuff

          Empties the receive buffer

     Procedure ClosePort

          Closes the comm port and deactivates SUPERCOMM until the
          next InitPort.

     Function Rlen

          Returns the number of characters currently available in the
          receive buffer.


                             Summary
         (How to use SUPERCOMM in a few semi-easy steps)

1)  Make  sure that SUPER.COM has been run so that  SUPERCOMM  is 
resident. It is very difficult for software to work properly when 
in is not in the computer's memory.

2)   Your program should first issue an Interrupt 14 with AH  set 
to 12 (opens the port with SUPERCOMM) and the other registers set 
as  in the old BIOS Interrupt 14 Function 0.  This  assures  that 
SUPERCOMM is humming away,  busily checking comm activity on  the 
port specified in DX  some 4500 times a second. 

3)    Now  you can use functions 1 through 8 to input  of  output 
all the happy data over that comm port. 

4) Before exiting the program,  issue an Interrupt 14 with AH set 
to  13 (close SUPERCOMM port).  This assures that all is back  to 
normal for any programs which you run later.

     Believe  me,  using  it  is a great deal  more  simple  than 
writing it was!

     If you have questions,  comments, suggestions or criticisms, 
you can reach me on the Neverboard,  (412) 733-4842 1200/8/N.  If 
you find SUPERCOMM useful, a donation of, say, $15 may be sent to 
the doctor's office:

               Doctor Debug
               1 Windsor Road B-6
               Pittsburgh, PA  15239

     If you use these routines in a commercial product, the above 
donation  is **not** optional.  The donation will make sure  that 
you  are  informed of upgrades and other pieces of  the  doctor's 
software.