V2.01 22-Mar-1985
 
                           Burnout II Documentation
                           ------------------------
 
        Function
        --------
        Burnout is an enhanced version of the old screen blanking
        program of the same name; its primary purpose is to blank out
        your video display after a specified length of time.  This new
        version is signifcantly enhanced over the older program; not
        only does it allow you better control over its operations, but
        it is written as a virtual device driver so that you can control
        it directly from your own programs.
 
 
        V2.01 Notes
        -----------
        The status report has been changed to be consistent with the
        format of input parameters.  The new status report is:
 
                count,reset,B,C+,V+,H+
 
        Note that count and reset have been reversed.  This makes it
        possible to reset burnout's parameters by passing its own report
        back to it, beginning with the first character of the reset
        count.  (The "B" will be ignored because it's not a valid
        parameter.)
 
        There is also a burnout "R" command which was present but not
        documented in version 2.00.
 
        There was an error in the V2.00 documentation, in which it was
        stated that you must send a "#" to BRNDEV to prepare it for a
        status request.  This is not correct; the "@" flush character is
        sufficient.  This error also cause the first BASIC demo program
        in the TRICKS section to malfunction.  Line 40, which was
 
                40 PRINT #1,"@#";
 
        should have been
 
                40 PRINT #1,"@";
 
 
        Installation
        ------------
        To install burnout, follow two steps: place the file BURNDEV.SYS
        in the root directory of your boot diskette or hard disk, and
        modify the CONFIG.SYS file to include the statement
        "device=burndev.sys".
 
        In case you are not familiar with CONFIG.SYS: this is a small
        text file which DOS reads when booting.  It contains various
        pieces of information which DOS and other programs can use when
        setting themselves up.  Look in the root directory of your boot
        disk for the file CONFIG.SYS.  If no such file exists, just
        type:
 
                copy con \config.sys<Enter>
                device=burndev.sys<Enter>
 
        Then press Ctrl-Z (you'll see "^Z") and <Enter>, and you're
        done.
 
        If you already have a CONFIG.SYS file (which is likely), you
        must edit it to include the statement "device=burndev.sys".  Do
        this using your text editor or word processor in text mode (or
        Edlin, heaven forbid).  Retain all existing information, and add
        the new line.
 
        WARNING: version 2.0 is experimental.  Don't install burnout on
        your only bootable disk.  There's always a chance something will
        go wrong go wrong go wrong, and you can't delete the CONFIG.SYS
        or BURNDEV.SYS files unless you can boot the machine.
 
        Now reboot your machine.  If all goes well, it will boot as
        usual.  There will be no indication that anything has happened.
        However, the screen should blank out after about ten minutes of
        inactivity.
 
 
        Burnout parameters
        ------------------
        There are several ways in which you can alter the operation of
        burnout.  There is a demo program called BURNOUT.COM which you
        can use for this purpose.  Its syntax is as follows:
 
                burnout [count] [V+-] [H+-] [C+-]
 
        The parameters are as follows:
 
        COUNT: changes the number of clock ticks until the screen
        blanks (this is called the "reset count").  For example,
 
                burnout 5000
 
        sets the reset count to 5000.  This means that if burnout
        observes no keyboard or video activity within 5000 clock
        ticks, it will blank the screen.  On the IBM PC, there are
        about 18.2 ticks per second, so this means that the screen will
        clear after about 5000/18.2 seconds (275 seconds, or about four
        and a half minutes).  (The default value on powerup is 10800
        ticks, or about 10 minutes).  You can set the reset count
        anywhere from 1 tick (not highly recommended) to 65535 ticks
        (about an hour).
 
        If you set the reset count to 0, burnout will be effectively
        "deinstalled" (equivalent to the old BURNOUT /Q) until you set a
        new nonzero count.  This is useful for programs that don't get
        along with the screen blanker.
 
        V: This stands for Video, and tells burnout whether you want it
        to monitor video activity in adddition to keyboard activity.
        You can set either "V+" (monitor video), or "V-" (don't).  Thus,
 
                burnout 5000 V-
 
        sets the program to reset to 5000 ticks, and not to monitor
        video.  Why would you not want to monitor video?  Primarily
        because some programs continuously update the display (e.g.,
        with a ticking clock) even when they're not doing anything.  If
        you set V+, the screen would never blank.  The powerup default
        setting is V+. (V- is equivalent to the old "BURNOUT /K"
        command).
 
        H: This stands for Hardware, and tells burnout whether you want
        it to blank the screen by manipulating the hardware (i.e., by
        turning off the video signal), or by software (which it does by
        temporarily changing screen attributes to black-on-black, or
        nondisplay).  Some explanation is in order.
 
        The preferred method of blanking the screen is to do it by
        manipulating the PC's video controller.  This method is very
        fast and in general has fewer problems than the software method.
        However, it does have two problems.  First, it is nonportable:
        it doesn't work with all PC-compatibles.  Second, there have
        been reports that this method can PHYSICALLY DAMAGE a few
        non-IBM video adapters, notably the Hercules monochrome graphics
        adapter.
 
        DO NOT USE H+ IF YOU ARE USING A HERCULES VIDEO ADAPTER!!!  YOU
        HAVE BEEN WARNED!!!
 
        If you are NOT using a Hercules card, try H+, with a setting of
        about 10 seconds, to make sure it works:
 
                burnout 180 H+
 
        The screen should blank in about 10 seconds.  If it does not,
        you will have to use H- (which is the powerup default setting).
        Reset burnout to some reasonable period of time, of course,
        after you have tested.
 
        C: This stands for Continuous Clear.  If you are using H+, you
        can skip this one, because it is ignored in hardware blanking
        mode.  As mentioned above, software blanking is achieved by
        simply changing all video attributes to nondisplay
        (black-on-black).  Now, if you are running in V- mode (not
        monitoring video), or if you are running a program which
        achieves video output by writing data directly to screen memory,
        new data will begin to appear on the screen, even though it is
        blanked.  Continuous Clear attempts to remedy this by simply
        resetting all the attributes to black-on-black every time the
        clock ticks (18 times per second).  The new data will flash on
        the screen and disappear immediately.  Powerup default is C-.
        Note that C- is equivalent to the old "BURNOUT /N" command.
 
        The burnout parameters can be entered in any order; illegal
        parameters, capitalization, and separators are ignored.  Thus,
        the following are all equivalent:
 
                burnout 5000 V+ H-
                burnout 5000,V+,H-
                burnout v+h-5000
                burnout H+, V-, 5000
                burnout 5000H-V+
                burnout h-5000v+
 
        If you enter a count greater than 65535, you're on your own.
        You won't get what you expect.  If you don't like the way
        BURNOUT.COM works, you're free to "roll your own"; see the next
        section.
 
        When BURNOUT has completed, it will display the current device
        status.  For example:
 
                Status: 09994,10000, ,C-,V+,H+
 
        The format of the status line is:
 
                Status: nnnnn,nnnnn,B,C+-,V+-,H+-
 
        The first number is the current number of clock ticks remaining
        till the next screen blank; the second is the reset count (in
        this case, the two numbers will be very close).  The "B", if
        present, indicates that the screen is currently Blanked (you
        won't see this after running BURNOUT).  The "C", "V", and "H"
        flags indicate the current status of Continuous Clear, Video
        monitoring, and Hardware clearing.  If the parameter is active,
        the indicator will be followed by a plus sign (+), otherwise a
        minus sign (-).  In the above example, then, the current count
        is 09994, the reset count is 10000, the screen is not blanked
        (naturally), Continous Clear is off, and Video monitoring and
        Hardware clearing are on.
 
        Unspecified parameters are not changed; thus, if you run burnout
        without any parameters, it will simply display status without
        changing anything.
 
        You can also include any of these parameters in the config.sys
        file so that they will be set immediately when you boot.  For
        example,
 
                device=burndev.sys 8000 H+ V-
 
 
        Burnout command
        ---------------
        Burnout has one command, the "R" (reset) command.  When the
        burnout device receives an R in its input stream, it performs
        two actions: it restores the screen if it is current blanked,
        and it resets the current count to the reset count.  The R
        command's primary purpose is to allow other applications to
        force a burnout device reset, as described below.
 
 
        Using the BRNDEV device
        -----------------------
        As mentioned above, the screen blanker is implemented as a
        virtual device.  The advantage to this is that it can be
        interrogated or controlled very easily, from the DOS command
        line or from your own programs.  In fact, BURNOUT.COM is a very
        simple program which takes your command line parameters, sends
        them to the burnout device, reads the current status back from
        the device, and displays the results.  This section explains how
        to do this.
 
        When DOS finds the "device=burndev.sys" line in config.sys, it
        loads and installs the burndev.sys program as a virtual device.
        What this means, practically speaking, is that there is now a
        new "device" attached to your PC. You already have several
        devices installed: CON, PRN, COM1 and COM2, AUX, your disk
        drives, and possibly a RAM (or virtual) disk if you have
        installed VDISK.SYS or another disk emulator.
 
        The new device is known to DOS by the name "BRNDEV" (note: this
        is NOT "BURNDEV", it's "BRNDEV", no U). Like other devices, you
        can write (send information) to the device, and you can read
        (receive information) from the device.  BRNDEV is designed to
        accept certain very specific information (the burnout
        parameters) when it is written to, and to return certain very
        specific information (the burnout status) when it is read from.
 
 
        Writing to BRNDEV
        -----------------
        How do you "write" to BRNDEV?  There are many ways.  The
        simplest is to do it right from the keyboard, at the DOS prompt:
 
                copy con brndev<Enter>
                @8000 V-#<Enter>
                ^Z<Enter>
 
        The "copy con brndev" command instructs DOS that you want to
        copy input from the console device to the BRNDEV device.  The
        console input "@5000 V-#<Enter>" is copied to the burnout device
        when you hit the Ctrl-Z (end of copy) and <Enter> (execute)
        keys.  To prove it worked, type "burnout" and look at the new
        parameters; they should reflect a reset count of 8000 and no
        video monitoring.  (The significance of @ and # will be
        explained shortly.)
 
        Another way to write to the device would be to copy a small
        textfile to BRNDEV.  As an example, type
 
                copy con brndemo.txt<Enter>
                @10000V+#<Enter>
                ^Z<Enter>
 
        You should now have a small textfile, the contents of which are
        "@10000V+#".  To sen it to BRNDEV, just type
 
                copy brndemo.txt brndev
                        or
                type brndemo.txt > brndev
 
        Run burnout to prove that the parameters have changed.
 
        The purpose of the "@" at the beginning of the output to BRNDEV
        is to tell the device to flush or rewind its I/O buffers.
        BRNDEV just sees a sequence of characters coming from DOS; it
        has no particular way to know when it is getting a new sequence
        of command characters.  The "@" tells it to get rid of any old,
        leftover junk and to start fresh.  Make a habit of prefixing all
        BRNDEV commands with an @ symbol.  "@" also has a second
        purpose, which will be covered below.
 
        The "#" is the "execute" character.  It tells BRNDEV that it has
        received the whole parameter list.  Only when BRNDEV sees the #
        will it examine the parameter list and execute the commands.
        Thus, "#" should be at the end of all BRNDEV commands; something
        like "@5000 C+H-" will have no effect at all.  The one exception
        is that it is NOT necessary to send a "#" to execute a "@".
        That is, the "@" is a live character; it is not buffered for
        later execution.
 
        It is also possible, of course, to send commands to BRNDEV from
        high level languages or from assembler programs.  Here's a BASIC
        example:
 
                10 OPEN "BRNDEV" FOR OUTPUT AS #1
                20 PRINT #1, "@5000 C+ H-#";
                30 CLOSE 1
 
        And C (this is C86); you'd want to add some error detection:
 
                {
                FILE *burnout, *fopen();
                static char command[] = "@5000 C+ H-#";
 
                        burnout = fopen("BRNDEV","w");
                        fwrite(command, 1, strlen(command), burnout);
                        fclose(burnout);
                }
 
        For an 8086 assembler example, see the source for BURNOUT.COM
        (BURNOUT.ASM), which is included in the burnout library.
        Basically, you have to open the device (filename=BRNDEV, fomode
        0 or 2), and use function 40H (FWRITE) to write bytes to the
        device using the returned handle.
 
        Note that application programs can use the R command to force a
        burnout device reset:
 
                1000 ' SUBROUTINE TO RESET BURNOUT AND RESTORE SCREEN
                1010 OPEN "BRNDEV" FOR OUTPUT AS #1
                1020 PRINT #1,"@R#";
                1030 CLOSE 1
                1040 RETURN
 
 
        Reading from BRNDEV
        -------------------
 
        Unfortunately, reading from BRNDEV is not quite as simple as
        writing to it.  There's no way that I can think of to do it from
        the command line; you really need a program (I suppose you could
        CTTY BRNDEV and then reboot when the machine went crazy [just
        kidding, don't try it]).  Also, there is a bug in DOS 2.x which
        prevents you from using BASIC for this purpose (fixed under 3.0,
        however).  Under 3.0, the BASIC program would be:
 
                10 OPEN "BRNDEV" FOR OUTPUT AS #1
                20 PRINT #1, "@";      ' Note "#" not necessary here
                30 CLOSE 1
                40 OPEN "BRNDEV" FOR INPUT AS #1
                50 BSTAT$ = INPUT$(22,1)
                60 CLOSE 1
                70 PRINT "Burnout status is "; BSTAT$
 
        Note that we always write an "@" to the device before reading
        its status.  The @'s function is described as above, to flush
        any unfinished I/O from BRNDEV's buffers.  Of considerable
        importance here, however, is that the @ also tells BRNDEV to
        prepare for a status request.  When BRNDEV sees the @, it
        examines its current status and puts the data into a buffer,
        from which it will be retrieved when it gets the request.
        Without the preparatory @, you'll get old data.
 
        The significance of the "22" in the INPUT$ statement is that the
        BRNDEV status report is 22 characters long.
 
        Here's a C example:
 
                {
                FILE *burnout, *fopen();
                static char command[] = "@";
                char status[30];
 
                        burnout = fopen("BRNDEV","rw");
                        fwrite(command, 1, strlen(command), burnout);
                        fread (status, 1, 255, burnout);
                        fclose(burnout);
                        printf("Burnout status is %s\n", status);
                }
 
        Note that we requested 255 characters.  DOS, in general, will
        halt a device read when it encounters a carriage return from the
        input stream.  BRNDEV makes a habit of sending a CR after the
        last byte of the status report, so this will terminate the read
        automatically; no need to worry about the true length of the
        report.  BASIC, however, will just keep reading until it
        accumulates the requested number of characters, so you do have
        to be watchful there.  The same trick (requesting too many
        characters) will also work in assembler programs (again, see
        BURNOUT.ASM).
 
        Now, about that bug in DOS 2.x.  It turns out that DOS will mess
        up if you ever request a single byte from an installed character
        device, which is what BRNDEV is.  (Technically: EOF is set on
        the device, and you will not be able to do any further reads
        unless you mess with IOCTL and explicitly reset EOF.)  Thus, the
        following assembler code will NOT work under 2.x:
 
                mov cx,22         ; Loop for 22 bytes
        Label:
                push cx           ; Save loop count
                mov ah,3FH        ; Read from file
                mov bx,BHandle    ; BRNDEV file handle (from FOPEN)
                mov cx,1          ; One byte at a time
                mov dx,offset buf ; Where to put the data
                int 21H           ; Perform read
                (do something with the byte)
                pop cx            ; Recover loop count
                loop label        ; Loop till 19 bytes read
 
        The first byte will be read OK, but no further input will be
        received.  You MUST read at least 2 bytes at a time.
 
        This bug can be overcome in assembler and C by simply requesting
        the full status report in one read.  However, it appears that
        BASIC requests only one byte at a time, even if you use
        something like INPUT$(22,n).  Reading the second byte then
        results in a READ PAST EOF error.
 
 
        Tricks
        ------
        You can do neat stuff like waiting for the screen to burn out,
        then turning it back on:
 
                1  REM DEMO PROGRAM TO WAIT UNTIL SCREEN BLANKS
                2  REM
                10 OPEN "BRNDEV" FOR OUTPUT AS #1
                20 OPEN "BRNDEV" FOR INPUT AS #2
                30 WHILE NOT BURNED.OUT
                40    PRINT #1,"@";
                50    A$ = INPUT$(22,2)
                60    BURNED.OUT = (MID$(A$,13,1) = "B")
                70 WEND
                80 BEEP: PRINT "Burned out!"
                90 CLOSE 1: CLOSE 2
 
        The 13th character of the status report, "B", will appear in the
        report only when the screen is blanked.
 
        Also, your programs can cancel burnout totally, if desired:
 
                1  REM DEMO PROGRAM TO DISABLE BURNOUT
                2  REM
                10 OPEN "BRNDEV" FOR OUTPUT AS #1
                20 PRINT #1,"@0#";
                30 CLOSE 1
 
        (I am not a BASIC programmer, so if any of these demo BASIC
        programs are dumb, someone tell me.)
 
        Naturally, it would be possible (and friendly) to read in the
        burnout parameters, modify them while your program is running,
        and restore the original parameters when you are done.
 
        If you use Seaware's Extended Batch Language, you can even test
        whether or not BRNDEV is installed from within a batch:
 
                bat stateof BRNDEV
                bat if %r = 0 type BURNOUT IS INSTALLED | goto -A1
                bat type BURNOUT IS NOT INSTALLED
                bat -A1
 
        If you have a one-floppy machine, you can trick DOS and BAT into
        not checking the second logical drive (and stopping the batch to
        ask you to "Insert diskette for drive B") by using
 
                bat stateof A:BRNDEV
 
        DOS apparently doesn't care if you prefix a device name with a
        drive ID.
 
 
        Incompatibilities and Problems
        ------------------------------
        I am aware of only a few problems and interactions with other
        programs.  In order for burnout to "see" keyboard and video
        activity, active programs must use ROM BIOS (or DOS, which
        itself uses BIOS) for their keyboard input and video output.
        A few progams use neither; hence burnout never sees their
        activity, and the screen will be irrevocably blanked.  These
        programs are mostly word processors; two that I know of are
        XYWrite and WordVision.  You must disable burnout before using
        either of these ("BURNOUT 0" will do the trick).  Most people do
        this in a batch:
 
                burnout 0
                wv
                burnout 10000
 
        There are also problems with some communications programs if you
        use software blanking.  If you are performing an extended length
        file transfer the screen may blank during the transfer.
        Software blanking takes a little time, and communications input
        can be lost while it is being accomplished.  This, of course,
        messes up the transfer.  And Continuous Clear is even worse.
        The solution is either to use hardware blanking or to disable
        burnout while transfers are taking place.  You MAY be able to
        get away with leaving burnout enabled, but disabling Continuous
        Clear (C-).
 
        Note that the word "BRNDEV" becomes a reserved word to DOS.  You
        cannot name any file BRNDEV (or even BRNDEV.TXT, or whatever).
        DOS won't let you do that.  If you do succeed, you won't be able
        to erase it.  This is why the driver is stored in a file named
        BURNDEV.SYS rather than BRNDEV.SYS.
 
 
        Tick chart
        ----------
        To save wear and tear on your calculator, here are some
        approximate tick counts:
 
                Minutes   Count
                -------   -----
                   1       1100
                   2       2200
                   3       3275
                   4       4375
                   5       5450
                   6       6550
                   7       7650
                   8       8725
                   9       9825
                  10      10920
                  20      21850
                  30      32760
                  40      43680
                  50      54600
                  60      65520
 
 
 
        The Usual Suspects
        ------------------
        The author accepts no responsibility for this software
        whatsoever.  It might work, it might not.  In particular, he
        accepts no responsibility for any result of the use of the
        software, even if it results in damage to your hardware.
 
        The burnout device driver (BURNDEV.SYS) and all demonstration
        programs are placed in the public domain and may be freely used
        by any individual.  You may not use them commercially.  You may
        copy and distribute the software and documentation to any other
        individual, PROVIDED that you do not charge for this.
        Recognized users' groups may, however, charge a small fee for
        postage and materials.
 
        I am interested in comments or suggestions on the usability of
        the burnout system, especially by programmers.  Contact me via
        CompuServe if possible.
 
 
                      All software and documentation are
 
                             Copyright (c) 1985 by
                            Christopher J. Dunford
                           10057-2 WIndstream Drive
                           Columbia, Maryland 21044
                           CompuServe ID 76703,2002