Documentation for:
-------------------
LZEXE.EXE v0.91 (á-release) (c) 1989 Fabrice BELLARD
Compressor for EXE files.


This program is in the public domain (FREEWARE), and you can therefore
use, copy and distribute it freely.  You can also utilize it commercially,
i.e. you can use it on programs you intend to sell.  However, the sale of
LZEXE.EXE itself is forbidden.


Requirements:  PC and compatibles.  80286 or 80386 microprocessors are
recommended  for greater execution speed.
Memory requirements: 128K minimum are needed to run LZEXE.


1-Introduction
--------------

This utility compresses EXE files, namely executable files.
You know that there are many other compressors for such files, such as
the excellent PKZIP or LHARC.  This uniqueness of the present method
consists in the fact that the compressed files can be run directly!
For almost all EXE files the decompression time is so short that it is
negligible ! In addition the decompression does not use any extra space
on disk or in RAM.  It simply uses the amount of RAM normally allocated
for the uncompressed file.  The compressor algorithm has been optimized
not only for speed but also for efficiency:  EXE files are reduced almost
to the size of their ZIPped counterparts.  I am working on future releases
which I hope will be even better.

2-Using LZEXE
-------------

Usage is very simple: just enter the command line

		 LZEXE filename

where filename is the EXE file to be compressed.  The extension .EXE is
implied by default. "path" is optional: it refers to the directory where
the compacted file and the temporary working file LZTMP.EXE are to be
located.

Warning!  Certain files are EXE only by name! For DOS it is not the
extension EXE that characterizes an 'EXE' file, but the presence of a header
with the letters "MZ" followed by information on the length of the file
the space occupied in RAM, etc...  Thus if you change the COM extension to
EXE, LZEXE will refuse to process the file.

There is a way to force LZEXE to accept a COM file: just use COMTOEXE by the
same author.  It works like EXE2BIN in reverse.

For greater safety LZEXE does not erase the original EXE file, but it renames
it with the extension .OLD.  In addition it creates the temporary file
LZEXE.TMP which is renamed with the name of the original program only at the
end of the compression process.

3-Usage tips
------------

Certain files can not be compressed for various reasons:

-  The file is not a true EXE file.  Solution: use COMTOEXE.EXE.
-  The relocation table is too large. To understand this you need to know
   the internal structure of an EXE file: such a file can occupy several
   segments unlike COM files.  Thus it must contain a table specifying where
   to branch and where to call subprograms, etc... And if the program is
   rather large  it may confuse the compressor.  I have provided for a table
   with up to 16,000 relocation addresses, which should suffice for almost
   all EXE files.
-  The file you wish to compress has already been compressed by LZEXE.
   Notice that there exists another compressor:   Microsoft's EXEPACK.EXE,
   which however is far less efficient than LZEXE.  LZEXE can further
   compress an EXEPACKed file, if you use UPACKEXE to unpack what EXEPACK
   has done.
-  Sometimes the compression factor is not significant.  This may happen with
   very small files (less than 2K).  Normally the compression is quite
   substantial.


-  A more serious problem: certain compressed EXE file may hang the system:

    -  If the program checks its size (like Turbo Debugger for example).
    -  If it checks for its integrity on disk.
    -  If it uses overlays, which must be loaded later and thus must occupy
       occupy fixed position in the file.  LZEXE 0.91 warns you of the
       presence of such overlays.
    -  Programs that require Microsoft's Windows:  they are not true EXE
       and will not work properly if compressed with LZEXE.
    -  This list may grow, since I have not experimented with all types
       of EXE files.


-  A less serious problem: Certain programs use configuration options that
   modify the code (Turbo  Pascal, for example).
   In this case, first configure the program, then compress it.  (Always
   keep an uncompressed version for safety.)


4-Some technical notes
----------------------

    The compression algorithm used is based on the Ziv Lempel method,
uses a circular (ring) buffer, and a tree-lile method for finding byte
sequence repeats.  The encoding of the position and length of the repeating
sequences is optimized via an auxiliary algorithm based on the Huffman
method.  Uncompressed bytes are kept unchanged since any further method
(such as Adaptive Huffman, as in LHARC, or Shanon-Fano trees, as in PKZIP)
would have entailed a much longer decompression time, and above all, a much
more complex and larger decompressor, which would have decreased excessively
the compression factor.

    The decompressor is located at the end of the compressed EXE file
and is 330 bytes long (in version 0.91). Its functions are:

-  Check the CRC to ensure that the file has not be tampred with (useful
   against viruses).  If the test files, the message  "CRC Error" is
   displayed.  However, I've removed this from version 0.91 because it
   increased the size of the file and the time spent i decompressing.  Further,
   the crc check was only done on the decompressor.
-  Locate itself in high RAM, then move the compressed code in order to
   leave sufficient room to the EXE file.
-  Decompress the code, checking that it is correct, and adjust the sgments
   if more than 64K (this was a hard problem, in terms of speed!).
-  Decompress the relocation table, and update the relocatable addresses
   of the EXE file.  Improvements have been made in this version to getter
   better compression.
-  Run the program, updating the CS,IP,SS,SP registers.

That's all!!!

    This decompressor is by itself a little jewel of 8086 assembler
programming. It goes without saying that it was hard work.  But the
compressor was not much easier, particularly with regard to the updating
all the pointers that the decompressor needs in order to function.


5-LZEXE and the other compressors
---------------------------------

PKARC (latest version):  LZEXE	is much better:  "crunching" (alias
Shrinking for PKZIP) is outdated...

PKZIP v0.92: LZEXE is better in most cases.

PKZIP v1.02: better than LZEXE with large files due to "imploding", since this
algorithm is a subset of mine, but the decompressor is slower than mine.  On
smaller files the difference is minimal.

LHARC v1.01:  better than LZEXE due to "freezing", but same remark as
for PKZIP v1.02.

LARC: LZEXE is better.

Important notes:

- One can not truly compare LZEXE with these other products. since the
files compressed with my method contain a decompressor which runs the
programs by itself.  It is true that the other compressor can create
"self-extracting" files, but they do so on disk, are slow and add sveral
scores of K to the compressed files (except for PKARC and LHARC, which add
only 1 or 2K., but only decompress to disk, unfortunately.)
- In almost all cases. the compressors mentioned can not further compress
a file already compressed with LZEXE, which demonstrates the high
efficiency of thismethod.


6-The future...
---------------

- I want to develop soon a decompressor which allows the recreation of the
original EXE file from the compressed one.  Its usefulness is questionable,
- I intend to optimize further the decompressor for speed,  and the
compressor for efficiency, by further reducing the relocation table, for
example (I already have a few ideas...);  adding a password system, and
creating an 80836 version which should speed things quite abit.
- I intend to develop a decompressor for  Microsoft's EXEPACKed files, which
is interesting because my compressor works better on files which have not
been treated with EXEPACK.
- I am also thinking of an automatic document-decompressor of the LIZEMOI.COM
or LIST.COM type, which should be very handy.
- Finally, I hope to create a "universal" compressor, like PKZIP or LHARC,
slower than LZEXE in decompression, but better than the existing ones.



7-Warnings...
-------------

I hope that LZEXE and the files it can create may become very popular...
a good incentive for further work.

I shall not be responsible in any way for any loss of data caused by LZEXE,
But rest assured: the algorithms are reliable and I do not believe there
are many bugs. If the EXE program created by LZEXE functions properly the
first time, then it will always do so!

Warning!  I advise against compressing and distributing commercial software
protected by copyright.  The authors may not like it...

But if you create a piece of FREEWARE or SHAREWARE,  or even a commercial
product,  nothing prevents you from compressing it with LZEXE.	In fact, I
urge youto do so:

- Your EXE files will be smaller and people may even think you programmed
them in assembler.  Your competitors will be amazed by your software, which
does what their does butis 30% smaller.
In addition you will have more space on your floppy and hard disks.  Space
is always at a premium...
-  Compressed programs are always less vulnerable to viruses, since any
interference will cause the "CRC error" to appear or the system to hang.
-  The compression constitutes an excellent encryption system, preventing
unscrupulous  people  from  hacking your messages or examining your algo-
rithms.  The only way would be to disassemble the decompressor, which is 
not going to be easy, I tell you!


    That's it!  I hope you enjoy this utility.  Please remember it is
still in its á-state!


    Fabrice.

    If you would like more information on the algorithms used, or in case of
difficulties, here is my address:

    Fabrice BELLARD
    451 chemin du mas de Matour
    34790 GRABELS  (FRANCE)

	Changes in v0.91:
	----------------
	-The dash, "-", is now acceptable character in file names.
	-LZEXE now points out the presence of internal overlays
	-LZEXE indicates if the file has been packed with EXEPACK
	-A bug under v0.90 has been fixed.  It made programs occupy too
	 much memory when running.
	-The relocation table has been improved
	-CRC control has been removed
	-The compression tail's size has been reduced from 385 to 330 bytes.