UnShrinking
-----------

Shrinking is a Dynamic Ziv-Lempel-Welch compression algorithm 
with partial clearing.  The initial code size is 9 bits, and 
the maximum code size is 13 bits.  Shrinking differs from 
conventional Dynamic Ziv-lempel-Welch implementations in several 
respects:

1)  The code size is controlled by the compressor, and is not 
    automatically increased when codes larger than the current 
    code size are created (but not necessarily used).  When 
    the decompressor encounters the code sequence 256 
    (decimal) followed by 1, it should increase the code size 
    read from the input stream to the next bit size.  No 
    blocking of the codes is performed, so the next code at 
    the increased size should be read from the input stream 
    immediately after where the previous code at the smaller 
    bit size was read.  Again, the decompressor should not 
    increase the code size used until the sequence 256,1 is 
    encountered.

2)  When the table becomes full, total clearing is not 
    performed.  Rather, when the compresser emits the code 
    sequence 256,2 (decimal), the decompressor should clear 
    all leaf nodes from the Ziv-Lempel tree, and continue to 
    use the current code size.  The nodes that are cleared 
    from the Ziv-Lempel tree are then re-used, with the lowest 
    code value re-used first, and the highest code value 
    re-used last.  The compressor can emit the sequence 256,2
    at any time.



Expanding
---------

The Reducing algorithm is actually a combination of two 
distinct algorithms.  The first algorithm compresses repeated 
byte sequences, and the second algorithm takes the compressed
stream from the first algorithm and applies a probabilistic 
compression method.  

The probabilistic compression stores an array of 'follower 
sets' S(j), for j=0 to 255, corresponding to each possible 
ASCII character.  Each set contains between 0 and 32 
characters, to be denoted as S(j)[0],...,S(j)[m], where m<32.  
The sets are stored at the beginning of the data area for a 
Reduced file, in reverse order, with S(255) first, and S(0) 
last.  

The sets are encoded as { N(j), S(j)[0],...,S(j)[N(j)-1] }, 
where N(j) is the size of set S(j).  N(j) can be 0, in which 
case the follower set for S(j) is empty.  Each N(j) value is 
encoded in 6 bits, followed by N(j) eight bit character values 
corresponding to S(j)[0] to S(j)[N(j)-1] respectively.  If 
N(j) is 0, then no values for S(j) are stored, and the value 
for N(j-1) immediately follows.

Immediately after the follower sets, is the compressed data 
stream.  The compressed data stream can be interpreted for the 
probabilistic decompression as follows:


let Last-Character <- 0.
loop until done
    if the follower set S(Last-Character) is empty then
	read 8 bits from the input stream, and copy this
	value to the output stream.
    otherwise if the follower set S(Last-Character) is non-empty then
	read 1 bit from the input stream.
	if this bit is not zero then
	    read 8 bits from the input stream, and copy this
	    value to the output stream.
	otherwise if this bit is zero then
	    read B(N(Last-Character)) bits from the input 
	    stream, and assign this value to I.
	    Copy the value of S(Last-Character)[I] to the 
	    output stream.
	
    assign the last value placed on the output stream to 
    Last-Character.
end loop


B(N(j)) is defined as the minimal number of bits required to 
encode the value N(j)-1.


The decompressed stream from above can then be expanded to 
re-create the original file as follows:


let State <- 0.

loop until done
    read 8 bits from the input stream into C.
    case State of
	0:  if C is not equal to DLE (144 decimal) then
		copy C to the output stream.
	    otherwise if C is equal to DLE then
		let State <- 1.

	1:  if C is non-zero then
		let V <- C.
		let Len <- L(V)
		let State <- F(Len).
	    otherwise if C is zero then
		copy the value 144 (decimal) to the output stream.
		let State <- 0

	2:  let Len <- Len + C
	    let State <- 3.
    
	3:  move backwards D(V,C) bytes in the output stream 
	    (if this position is before the start of the output 
	    stream, then assume that all the data before the 
	    start of the output stream is filled with zeros).
	    copy Len+3 bytes from this position to the output stream.
	    let State <- 0.
    end case
end loop


The functions F,L, and D are dependent on the 'compression 
factor' (see FORMAT.DOC), 1 through 4, and are defined as follows:

For compression factor 1:
    L(X) equals the lower 7 bits of X.
    F(X) equals 2 if X equals 127 otherwise F(X) equals 3.
    D(X,Y) equals the (upper 1 bit of X) * 256 + Y + 1.
For compression factor 2:
    L(X) equals the lower 6 bits of X.
    F(X) equals 2 if X equals 63 otherwise F(X) equals 3.
    D(X,Y) equals the (upper 2 bits of X) * 256 + Y + 1.
For compression factor 3:
    L(X) equals the lower 5 bits of X.
    F(X) equals 2 if X equals 31 otherwise F(X) equals 3.
    D(X,Y) equals the (upper 3 bits of X) * 256 + Y + 1.
For compression factor 4:
    L(X) equals the lower 4 bits of X.
    F(X) equals 2 if X equals 15 otherwise F(X) equals 3.
    D(X,Y) equals the (upper 4 bits of X) * 256 + Y + 1.