FASTPLOT

                                by Ryan Software

                                  Version 1.10




                                  Ryan Software
                                  P.O. Box 1150
                              Twin Peaks, CA  92391









                       Copyright (c) 1987 by Ryan Software
                               All Rights Reserved



























                                  REGISTRATION

        Shareware  is a term for software that can be freely  copied  and 
        shared.  The term describes copyrighted software which the author 
        supports and encourages people to copy and share.

        The concept is based upon these principles:

           1. People need to try programs to see if they are useful.

           2. Software authors can be supported directly by users.

           3. Copying and networking of programs can be encouraged.


        We  encourage  you to register your copy of FASTPLOT for  $25.00.  
        Registration has a number of benefits to you:


           1. You   will  receive the most current version of the program  
              if the one you register is not the most current.

           2. You will receive a current manual if the one you registered 
              is not the most current.

           3. You will encourage us to develop more useful programs.



                      Other Programs Available from Ryan Software

        EXTRACT

        EXTRACT is a utility program which will extract points, lines and 
        text from any given layer and write it to an ASCII file or to the 
        screen  for  use by other programs.  EXTRACT can extract all  the 
        layer  names  in a drawing file in case you want  a  quick  list. 
        EXTRACT is hundreds of times faster than producing a DXF file and 
        reading it from another program. DXB files might suffice for many 
        applications except that DXB cannot handle text.


        CHLAYER  is a utility program will change the layer names in  any 
        DXF  file.  The  old names and new names are contained in a  file 
        called CHLAYER.INF.  The names are entered in matched pairs  with 
        the  first name being the name to be changed and the second entry 
        is the name to be changed to.













        1. Introduction

           FASTPLOT is an off line plotting program which runs on any IBM 
           or  compatible computer running DOS 2.1  or  higher.  FASTPLOT 
           plots any file  which  can to be sent to a plotter in XON/XOFF 
           or   hardware  handshaking  mode.  It therefore  supports  any 
           plotter which AutoCAD would normally support.  A few of  these 
           plotters include:

           Calcomp 906/907/PCI controllers

           Hewlett Packard 7220, 7470, 7475, 7550, 7580, 7585, 7586,
                           ColorPro, DraftPro and DraftMaster

           Houston Instruments DMP-7, 8, 29, 40, 41, 42, 51, 52, 52, 
                               and 56

           Ioline LP 3700 and 4000

           Numonics



        2. Benefits of FASTPLOT

           FASTPLOT will run your plotter at full speed.  It makes use of 
           the plotter's internal buffer if it has one. 

           The   program  is completely interrupt driven which allows  it  
           to  communicate   quickly  with the plotter and  without   any  
           fear  of losing  any  drawing vectors as might happen with the 
           use of  the COPY or PRINT commands.

           It  does not permanently take any memory from your system   as  
           do other resident spooler programs.

           FASTPLOT   can  be  used on a second computer to  do   nothing  
           but plotting thus freeing up the main CAD system.

           Plots files can be kept and replotted at any time.

           A   plot   file can be generated for another type  of  plotter  
           which may reside in a remote location and FASTPLOT can be used 
           to  plot it on that plotter if FASTPLOT supports that plotter.













                                        1





        3. Running FASTPLOT 

           a. From AutoCAD

              You   need   to save your plot as a plot  file.   This   is  
              done  after you select the PLOT command in  AutoCAD.   When  
              AutoCAD asks if you want to plot to a file,   answer with a 
              "Y".  You will  then  need to supply a file name.  For  the  
              following  example   assume  that  the plot file  name  you  
              supplied    was  BRIDGE.   AutoCAD  creates  a  file  named 
              BRIDGE.PLT.

              To run FASTPLOT just type: 

                                  FASTPLOT BRIDGE.PLT

              FASTPLOT   will  use  all the  plotting  parameters   (baud  
              rate,  parity,  etc.) that you have previously set.  If you 
              want to set of reset the parameters and plot then you  need 
              to type:

                                       FASTPLOT

              This will start the program from the main menu.



           b. From Another Program

              FASTPLOT   can   plot most plot files from  programs  which  
              can generate them.  You will need to save the plot file and  
              use FASTPLOT to replot it. 

              You   should   remember to always use the same   parameters  
              in  FASTPLOT  that  you may have selected in  your  program  
              which  generated the plot.   This is necessary because many 
              programs  include a few of the parameters in the  beginning 
              of the plot file.


















                                        2





        4. Program Options
                 
           If  you  type FASTPLOT,   without the filename on the  command  
           line, you will get the main menu as shown below.




                                      FASTPLOT

                                    Version 1.10
                                Copyright June 1987
                                   Ryan Software

            Select Main Menu Option

            1 - Set Communications Parameters
            2 - Set File Name < >
            3 - Send Plot File

            5 - Exit to DOS


            XON/XOFF   COM1   9600 baud   1 stop bits   8 data bits   parity = none




           The   bottom   line   is  a status  line   which   shows   the  
           current communication options in effect.



            a. Set Communications Parameters

               There  are  six parameters to be set  for  communications. 
               These are the baud rate,  communication port,  stop  bits, 
               data bits,  parity,   and type of handshaking. The current 
               value is shown in brackets, < >.

               The sub-menus are shown below:

                    Select desired baud rate <9600>
                      
                    1  -   300 baud
                    2  -   600 baud
                    3  -  1200 baud
                    4  -  2400 baud
                    5  -  4800 baud
                    6  -  9600 baud






                                        3






                    Select desired communications plot <COM1>

                    1  -  COM1
                    2  -  COM2


                    Select number of stop bits <1>

                    1  -  1 stop bit
                    2  -  2 stop bits


                    Select number of data bits <8>

                    1  -  7 data bits
                    2  -  8 data bits


                    Select the type of parity <none>

                    1  -  No parity
                    2  -  Odd parity
                    3  -  Even parity


                    Select desired handshaking mode <XON/XOFF>

                    1  -  XON/XOFF
                    2  -  Hardware


               All   the   communication   options are saved in  a   file  
               named FASTPLOT.INF.


            b. Set File Name

               This  menu option options allows you to specify  the  plot 
               file  name   for   plotting.   You will need to  do   this  
               before  you select Main Menu Option 3.

            c. Send Plot File

               This will cause the file name given in Main Menu Option  2 
               to  be  sent to the selected communication port  (COM1  or 
               COM2).

               While   the  file is being plotted you may abort the  plot  
               by  hitting  the ESCAPE key.   This will only work if  the 
               computer  and   plotter   are  correctly  connected    and  
               handshaking  has begun.




                                        4






        5. Debugging

           The   program   does have some provisions for  debugging  plot  
           files and plotters.

           Add  2  (two)  to  the value of  the  handshaking  option  and  
           debugging will be turned on (i.e. 3 for XON/XOFF).

           A   "W"  or  "S"  will be displayed in the upper  left  corner  
           to indicate  if  the program is "W"aiting for the plotter   to  
           request more data or "S"ending data to the plotter. 

           The   program will display each character in hex format as  it  
           is sent to the plotter. 

           When   the  transmission is complete the program will  display  
           the total number of characters transmitted to the plotter.






































                                        5






        6. Miscellaneous

           FASTPLOT   has  been  tested  on over 20  plotters   including  
           the Hewlett Packard and Houston Instruments plotters.

           HP   and   HI  plotters run equally  fast  in   XON/XOFF   and  
           hardware handshaking.   

           Calcomp   plotters  run much faster in  hardware   handshaking  
           mode.  Calcomp   plotters  will require that you  consult  the 
           manual  to  set  the  correct connector in  the  rear  of  the 
           plotter,  set the correct dip switch settings,  and select the 
           correct  settings on the front panel.   If  you want  hardware 
           handshaking  then XON/XOFF  will  be off.   Remember  to   use  
           the  same  sync  codes  and  values   as   the  program  which 
           generated the plot file would have used.

           It   is  possible  that  FASTPLOT may not work  with  all  the  
           plotters supported by AutoCAD.  This is because of the encoded 
           information  in   the   beginning of the plot  file  that  may  
           disagree  with  the selected parameters from FASTPLOT.

           Most  communications  problems are due to incorrect   cabling.  
           If  you   are using the same cable that you normally use   for  
           AutoCAD with XON/XOFF protocol then the problem could be  with 
           FASTPLOT. 

           Hardware   handshaking  requires special cabling.   In general  
           the diagram given below will work with most plotters.


                      Computer_End          Plotter_End
                            1 ____________________ 1
                            2 ____________________ 3
                            3 ____________________ 2
                            5 ____________________ 20
                            6 ___|
                            7 ____________________ 7



            If you have a Calcomp plotter the cabling below should be used:


                      Computer_End          Plotter_End
                            1 ____________________ 1
                            2 ____________________ 2
                            3 ____________________ 3
                            4 ____________________ 4 
                            5 ____________________ 5
                            6 ____________________ 6
                            7 ____________________ 7



                                        6





        7. Special Problems.

           If   you   cannot   resolve your problem you  may   submit   a  
           problem  report.     Describe    the   problem   clearly   and  
           please    include  information  about your  type  of  computer 
           system,   plotter type and model number and,   if possible,  a 
           small sample plot file on 5-1/4 inch   or 3-1/2 inch diskette.  
           We  will try to review the problem and if there is  a  program 
           problem will include a fix in the  next version.















































                                        7









                             FASTPLOT REGISTRATION FORM


        Name________________________________________________

        Company_____________________________________________

        Address_____________________________________________

        City, State, Zip____________________________________

        Daytime telephone___________________________________


        To  register,  send  $25.00  (money order,  or personal  
        check  -  California residents add 6% sales tax) to:

        Ryan Software
        P.O. Box 1150
        Twin Peaks, CA 92391

        Likes, dislikes, features wanted, problems?  List below:


        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________





                                        8