LICENSE AGREEMENT

       Menumaker is copyrighted but a limited license is 
       granted under the following conditions:
   

     You MAY:
     
     1. Use Menumaker as much as you like.  

     2. distribute and copy Menumaker freely, as long as the 
        associated files are kept together with the main 
        program. 

     4. send IntelliCADD any amount of money for all of there 
        hard work on this phenomenal software. (see system
        information on the Menumaker utility menu)


     You may NOT: 
  
     1. distribute Menumaker in MODIFIED form. That includes 
        executable, help, documentation and all other files
        associated with Menumaker.
  
     2. charge any fee for Menumaker itself.
  
     3. remove, change or alter in any way the copyright notices.


     By using Menumaker and it associated software you are 
     accepting and agreeing with the two terms below.
 
     1. THERE ARE NO WARRANTIES EITHER EXPRESSED OR  IMPLIED, 
        INCLUDING  BUT NOT LIMITED TO, IMPLIED WARRANTIES  OF 
        MERCHANTABILITY OR FITNESS FOR A PARTICULAR  PURPOSE, 
        AND   ALL   SUCH   WARRANTIES   ARE   EXPRESSLY   AND 
        SPECIFICALLY DENIED.
 
     2. Liability.  You hereby agree that, regardless of  the 
        form  of claim, the liability of IntelliCADD for  any 
        damages or loss by you shall not exceed the  original 
        license   fee   paid.  INTELLICADD   SHALL   NOT   BE 
        RESPONSIBLE    FOR   ANY   INDIRECT,   SPECIAL,    OR 
        CONSEQUENTIAL DAMAGES OR LOST PROFITS.
 


   * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *
         Menumaker is not BEGGERware but:
         If you find this program useful, and would like
         a complete working copy, a manual, and program
         binder. Please send $30.00 to the above address.
         If you would like to send us less than $30.00 we
         will gladly accept any contribution for our hard
         work, but we will not be able to send you back
         any of the above.
   * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

IntelliCADD
256 Witherspoon way Suite H
El Cajon CA. 92020
(619) 460-6030
BBS (619) 460-1568






                               Trademarks
                Autocad is a trademark of Autodesk, Inc.
          Norton Commander is a trademark of Norton Utilities.
             Sidekick is a trademark of Borland Engineering.


                            Copyright Notice
             Copyright (c) IntelliCADD, 1987, 1988, 1989.  
                          All rights reserved.
       





 


 
 
                             Menumaker
 
                         Reference Manual















                       Table of Contents
 
Chapter 1  INTRODUCTION TO MENUMAKER
       1.1  What is Menumaker
       1.2  How to use this Manual and Software
       1.3  Discussion on making Custom Menus
 
Chapter 2  STARTING MENUMAKER
       2.1  General
       2.2  System Requirements
       2.3  Installing Menumaker
       2.4  Existing Menus
 
Chapter 3  Getting a Fast Start (Tutorial)
       3.1  So you want to get started quick
       3.2  Submenu Directory Editor
       3.3  Submenu Statement
       3.4  Command Entry
       3.5  Command Description
       3.6  Prompt Entry
       3.7  Custom Entry
       3.8  Writing Your New Menu
 
Chapter 4  CREATING MENUS
       4.1  General
       4.2  Help Menus
       4.3  The Main Menu of Menumaker
       4.3a  Editing Auxiliary Buttons
       4.3b  Editing Mouse Buttons
       4.3c  Editing Icon-Boxes (Rel.9)
       4.3d  Editing Pull Down Menus (Rel.9)
       4.3e  Editing Screen Submenus
       4.3f  Editing Tablet Menus
       4.3g  Utilities
       4.3h  Quit Menumaker
 
Chapter 5  PROMPT ENTRY
       5.1  General
       5.2  Prompt Entry
       5.3  Prompt Entry Editing Notes
 
Chapter 6  CUSTOM ENTRY
       6.1  General
       6.2  Custom Entry
       6.3  Custom Entry Editing Notes
 
Appendix A  IF DISASTER OCCURS
Appendix B  ARCHIVING FILES
Appendix C  TEMPLATE MAKER
 






1.1   What is Menumaker.
___________________________________________________________
The Menumaker software allows you to easily create and  edit
your own Autocad menus customized to your individual  needs.  
Once  installed,  Menumaker guides you through  the  various 
steps in the creation of your menus.  Along the way,  pop-up 
Help  windows are available to assist you with the  required 
commands and all of the Autocad commands you will be using.
 
In  addition,  Menumaker supports the customization  of  the 
pull-down  windows in Release. 9+, and the  configuration  of 
the buttons on your input device.
 
Menumaker  also  allows  for the inclusion of  all  of  your 
favorite Lisp and other macro program commands.  
 
Menumaker  allows you to read in any existing menu which  is 
in  an .MNU format for editing purposes.   Upon  completion, 
Menumaker will produce the new .MNU file ready for use  with 
your Autocad drawing.
 

1.2   How to use this manual and software
___________________________________________________________
This manual has been written to act as a reference guide for 
use  with  the Menumaker software package.  We  must  assume 
that the user has a little experience using Autocad and  DOS 
commands.  An individual chapter in this book is devoted  to 
each  of  the  three  major  Menumaker  processes  for   the 
customization  of  your menus.  Chapters 4  through  6  each 
correspond to one of these applications.
 
Menumaker  makes  extensive  use  of  pop-up  Help   windows 
throughout  the customization process.  The help offered  in 
these  areas will provide general assistance with  Menumaker 
commands  while  this  manual  will  provide  the   detailed 
instruction along with specific examples.
 
In addition, Menumaker supplies Help windows for all of  the 
Autocad commands.  The windows you will see are the same  as 
if  you were in an Autocad drawing and requested help for  a 
specific  command.   At  the bottom  of  each  Autocad  Help 
window, Menumaker will refer you to the specific chapter  in 
the  Autocad reference manual for additional details.   This 
manual  does  not  contain  help  on  the  specific  Autocad 
commands.
 
 
1.3  Discussion on making custom menus.
___________________________________________________________
Either  by modifying an existing menu or creating your  own, 
Menumaker offers both the beginner and the expert alike  the 
required  tools  to complete the process  easily.   Included 
with  Menumaker  is  a sample menu  (EXAMPLE.MNU),  for  the 
purposes  of providing you with both a place to start and  a 
detailed example of a completed menu.  It is suggested  that 
you  use  this menu together with the tutorial  to  practice 
with, prior to working with one of your existing menus.
 
When  you begin Menumaker for the first time, the  "EXAMPLE" 
menu  will automatically be loaded ready for  editing.   Now 
that  you have an existing menu to experiment with, you  can 
make  small  changes  in order to see the  results  both  in 
Menumaker and within an Autocad drawing.
 
Menumaker  allows tremendous flexibility in the creation  of 
your menus.  Because you are able to add, delete and  change 
any  number of times, it is suggested that you build a  menu 
gradually  rather than a complicated one all at  once.   The 
key  to  a good customized menu is repeated testing  of  the 
finished product.
 
Menumaker  allows you to program a change between  menus  as 
many times as you want.  This is important.  Even though you 
may have a very large menu, several smaller menus will allow 
you much faster access time in both Menumaker during editing 
and Autocad while you are drawing.
 


CHAPTER 2  Getting Started
 
2.1  General
____________________________________________________________
We suggest that you take a few minutes to read this  chapter 
in  order  to  completely  familiarize  yourself  with   the 
installation  procedure.   During the  installation  process 
Menumaker  creates  its own sub-directory, checks  for  your 
Autocad  files,  creates batch files and transfers  to  your 
hard disk.
 
2.2  System Requirements
___________________________________________________________
In general the system requirements are the same as  Autocad.  
You should have the following minimum system configuration:
 
       IBM PC, PC/XT or AT or compatible
       At least 512K of free memory
       1 Double sided 360K floppy disk drive
       1 hard disk drive with at least 1.5 MB of free space
       Compatible Printer (optional)
       DOS 2.0 or higher

Menumaker requires that your CONFIG.SYS file in your  "Root" 
Directory  have the following minimum requirements in  order 
to function properly:
 
       BUFFERS=20
       FILES=20
 
If  your  CONFIG.SYS  does not have  these  minimum  values, 
consult  your  DOS manual or use any asci editor  to  change 
them.
 
Please  note: The running of resident memory  programs  (ie. 
Norton  Commander,  Sidekick,  etc.)  may  have  some  minor 
effects on Menumaker.
 
Menumaker  will  create  a separate  sub-directory  of  your 
choice  as part of the installation process for  its  files. 
It will also automatically transfer your completed menus  to 
the  sub-directory you have designated where you  will  work 
with your drawings in Autocad.
 
From  time to time there will be changes to this manual  and 
updates to the software.  Please type the "README.DOC"  file 
for  this  additional information.
 

2.3  Installing Menumaker
___________________________________________________________
The Menumaker installation process is automatic the first 
time that you run Menumaker. You may want to put Menumaker
in it's own sub-directory (ie "MENUMAKR"). 

To start Menumaker, type the following:
 
       C:\MENUMAKR> MENUMAKR   <RETURN>

During  the  installation  process  you will  be  asked 
the  name  of  the Sub-directory you  would  like  to  place 
Menumaker  in  and  the location of  your  Autocad  program. 
Finally,  you  will  be asked which printer  port  you  have 
connected.
 
Every  time you begin a new editing session, Menumaker  will 
check  to make sure that all files required are present  and 
in good condition.  This will help prevent the  frustrations 
of  a "crash" during the session should the necessary  files 
be  missing.  Should files be missing, Menumaker  will  tell 
you  which ones the are.

You can re-run the install portion or Menumaker by using a
"/R" at the DOS prompt. Like this:

       C:\MENUMAKR> MENUMAKR /R  <RETURN>
 
 
2.4  Existing Menus
_____________________________________________________________
Menumaker also allows for the modification of existing menus 
you  are currently using with your Autocad drawings.  PLEASE 
NOTE: they must be in the uncompiled format designated as an 
.MNU file, not an .MNX file.  Those menus you wish to modify 
should be moved to the Menumaker subdirectory using the COPY 
command  from  DOS.  After editing a  menu,  Menumaker  will 
automatically  transfer  your  new  menu  to  your   Autocad 
subdirectory.   When  this is done the old   .MNU  file  (if 
there  is one) will be renamed as a .BAK file  for  archival 
purposes.  Details for this process are provided in  Chapter 
4.3e.
 

Chapter 3  Getting A Fast Start
 
3.1  So you want to get started quick.....
____________________________________________________________
At  this point we know you are anxious to get  started  with 
the customization of your own menus.  So we will take a  few 
moments  and walk you through a short tutorial in  order  to 
give a small idea of the power awaiting you.  All we ask  in 
return  is that you take the time to read the rest  of  this 
manual as there are a lot of very powerful editing tools  to 
numerous to mention here.
 
In  this quick tutorial we will take a look at a part  of  a 
the  menu you received with your original Autocad  software, 
make a few changes, then use it in a drawing.  In order  not 
to  confuse the menus, the part of the Autocad menu we  will 
use has been renamed to SAMPLE.MNU.  During the installation 
procedure  it  was transferred to your  Menumaker  directory 
ready to use.
 
The  first step is to start your computer, move to  whatever 
drive and subdirectory Menumaker was installed on and enter:
 
C:\MENUMAKR> MENUMAKER     <RETURN>
 
Please  note that Menumaker will display only  the  function 
keys available with each editor at the bottom of the screen. 
As you move between editors, this list of available function 
keys will change with each type of editing screen.
 
Type an "R" to Read-in an existing menu.  Menumaker will ask 
you to enter the name of the menu to read in.  Type the word 
"SAMPLE"  and  press  <RETURN>.  The menu  "SAMPLE"  is  now 
translated  into  a format to be used in Menumaker  and  you 
have  been  returned to the Utility Menu. Please  note  that 
this  process must be done to all existing menus  which  are 
designated  with the .MNU extension.  Press <X> OR  <escape> 
to return to the Main Menu.
 
Please note: Although you have translated "SAMPLE.MNU"  into 
a  Menumaker format, it is still not the current Menu  being 
edited.  The current menu being edited is noted in the upper 
left  corner as being "EXAMPLE".  To change this, press  <C> 
while on the main menu, type "SAMPLE" as the name of the new 
current  menu and press <RETURN>.  The menu "SAMPLE" is  now 
the  current menu being edited and is so noted in the  upper 
left corner of the screen.
 
In  order to edit the individual Submenus that make  up  the 
Menu  "SAMPLE"  we  need to move to  the  Submenu  Directory 
Editor.   To  do this, press <E> on the Main  Menu. 
 
 
3.2  Submenu Directory Editor
____________________________________________________________
You  should  now have the Submenu Directory Editor  on  your 
screen  as shown above.  PLEASE NOTE!!! This screen shows  a 
list  of  the titles of all of the Submenus (listed  at  the 
right)  that  make up the Menu "Example" (as  noted  in  the 
upper left corner of the screen.)
 
It  is important that you realize that a Submenu  represents 
what  you will see on your drawing screen at any  one  time, 
and  that all of these different Submenus (screens) make  up 
the menu you are currently working with.

Also  note that the first submenu at the top of the list  is 
called the Master Submenu (in this case MASTER).  It is  the 
submenu  that first appears on your screen when you start  a 
drawing   in   Autocad.    Also,  for   purposes   of   this 
demonstration,  less  than 5% of the Autocad menu  is  being 
used  in the file "SAMPLE.MNU".  You may read in the  entire 
menu later if you like.
 
You can move the cursor through the list of submenus (screen 
displays) to the one you want to edit.  The up, down, Pg Up, 
Pg  Dn, Home and End keys will move you through  this  list. 
You  may also type the first letter of the  Submenu  desired 
and  Menumaker will take you to the first  Submenu  starting 
with that letter.
 
Our  purpose for editing this menu is to add a  new  Submenu 
called  "Practice" right after the Master  Submenu  "MASTER" 
and  place  the  commands to draw  parking  islands,  insert 
handicap   symbols  in  the  parking  spaces  and   make   a 
combination of these two commands.
 
To accomplish this, we first need to create the new  Submenu 
"Practice" and place it after the Master Submenu "S".   Make 
sure   the  marker  is  at  the  Master  Submenu   "MASTER", 
(Menumaker  places  the  new  Submenu  after  the   "marked" 
Submenu)  and press [F5].  Menumaker will ask you  to  enter 
the new Submenu Name.  Type the new submenu name  "PRACTICE" 
and press <RETURN>. Menumaker will create the blank  Submenu 
"practice" and place it after the Master Submenu MASTER.
 
Next  we  want to go into the Master  Submenu  "MASTER"  and 
insert  a  command which will take you to this  new  Submenu 
called  "Practice".  With the marker at the  "MASTER"  press 
[F2]. 
 
Your  screen now displays the Master Submenu "MASTER".   You 
should  recognize the left-hand column as what you see  when 
you start an Autocad drawing.  In the right-hand column  you 
will see a brief description of the commands entered.  Since 
you  have Read-in an existing menu, the command  description 
for each line simply says that there is an existing  command 
that  was already there.
 
In  order to create a menu command to go to our new  submenu 
"Practice",  we  must first create a space  for  it  between 
"Plot"  and "Utility".  To do so, first press  the  <Insert> 
key  to turn on the Insert toggle at the top of the  screen. 
Then move the <Cursor> to "Utility" and press <RETURN>  (The 
up and down arrow keys will move you on this list).
 
Menumaker  has  inserted  a space (or Return)  in  front  of 
"Utility" moving everything down the page, while making room 
for  your new command.  The cursor remains at the new  space 
ready for your new entry.
 
Entering  a Submenu item is a two step process.   The  first 
being  to  type  the statement you want  to  appear  on  the 
drawing  screen.   The  second is the actual  editing  of  a 
command,  which  can  be done one of  three  ways;   Command 
Entry, Prompt Entry or Custom Entry.  We will explore  each; 
one at a time.
 

3.3  Submenu Statement
____________________________________________________________
With  the cursor at its present location on line 14  between 
"Plot"  and "Utility", type in the Statement you would  like 
to  appear  on  your  drawing screen.   In  this  case  type 
"PRACTICE".   Notice that you are limited by Autocad  to  no 
more  than 8 characters in the Statement.  You may type  any 
combination  of characters and Autocad will display them  on 
your drawing screen.
 

3.4  Command Entry
____________________________________________________________
In order to create the command, we must first choose a  form 
of editing to insert the command.  In this case we will  use 
Command  Entry to create the command to change the  menu  on 
the  screen to our new Submenu "PRACTICE".  To do so,  while 
the   cursor  is  still  on  line  14  with  the   statement 
"Practice",  press  [F10]. 
 
Notice  that  a list of Menumaker and Autocad  commands  has 
appeared at the right side of your screen.  You may move the 
cursor  through the list using the Up Arrow, Down Arrow,  Pg 
Up, Pg Dn, Home and End keys.  If you know what command  you 
are going to use, you may also type the first letter of  the 
command which will move you directly to that portion of  the 
list.  For now we are going to the first item on the list; -
SUBMENU-.   This is the command used most often because  you
need  it  to change the Submenu displayed  on  your  drawing
screen  from  one to another. With the marker  at  -SUBMENU-
press [F2].
 
Each of the commands chosen from the Command Entry list will 
display a Command Window with a list of options available to 
you.   They do not include all of the possibilities, but  do 
incorporate enough to cover most situations.  More extensive 
possibilities  exist in Prompt Entry and Custom Entry.   You 
can move the option window up or down with the arrow keys to 
choose  the  one  you want.  Since we are  working  with   a 
"screen" Submenu, place the marker in front of "SCREEN"  and 
press <RETURN>.

If  you  required  additional assistance with  this  or  any 
other  specific command, a Help Window is  always  available 
for  the  command  you are working with  while  the  Command 
Window is on the screen by pressing [F1].
 
Menumaker will now ask you for the new Submenu name you want 
this command to display on the screen. IMPORTANT: This  must 
be  exactly the same name (without the numeric value at  the 
end  of  it) of one of the submenus listed  on  the  Submenu 
Directory  Editor.  Type in "PRACTICE" and  press  <RETURN>. 
Menumaker will store the correct command sequence and return 
you  to the Submenu Editor with the description included. 
 
A more detailed explanation of Command Entry, including  all 
of the options available, is given in Chapter 4.3b.
 

3.5  Command Description
____________________________________________________________
Next we would now like to move to our new Submenu "PRACTICE" 
and create a new menu item that will draw a parking  island. 
To  do  so,  we must first save the  changes  made  to  this 
Submenu  by  pressing [F2].  Menumaker has  now  saved  your 
changes  for the Submenu "S" and moved back to  the  Submenu 
Directory  Editor.  If we had not wanted to save all of  our 
changes we would have pressed <ESCAPE> to abort the  editing 
session.
 
To move to your new Submenu "Practice", move the marker down 
the  list to "Practice" and press [F2].  This will move  you 
to  the Editor for our new Submenu "Practice".  Notice  that 
since we have just created it, there are no commands listed.
 
Our  first step in working on this new Submenu might  be  to 
write a statement which will tell us while in a drawing what 
this  Submenu  is without including a command.  To  do  this 
simply  type "PRACTICE" on line 1.  We could just  leave  it 
like this and it would appear on our drawing screen, but  we 
want to place a description on it so we know what it is  for 
future  editing.   To  do  so,  we  will  edit  the  command 
description. With the cursor still on line 1, press [F4].
 
Inside the Command Description Editor you may type  whatever 
comments  you  would like to be displayed.  This  will  only 
appear in Menumaker and does not affect the menu when it  is 
used  in  a  drawing.  For instance,  type  in  "INFORMATION 
STATEMENT" and press <RETURN>.  Notice that your description 
has  been placed next to line 1.  This becomes a  convenient 
tool for keeping notes as your menus become longer and  more 
complicated.   If you were to press [F8] you would see  that 
no Autocad command string exists.  You can always put one in 
later should you need it.
 
 
3.6  Prompt Entry
____________________________________________________________
Next  we  would like like to create a menu  item  that  will 
create  our  parking island by drawing two  different  lines 
connected  by an arc between them.  Knowing that we will  be 
using  several  Autocad commands together as a  single  menu 
item, we choose to create this menu item with Prompt Entry. 
Please notice that we are unable to press the "pick"  button
on our input device (ie. mouse), so we have substituted  the
<INSERT>  key.  Therefore, every time we want  Menumaker  to
have your menu stop and wait for input from your device,  we
will  press the <INSERT> key.  If we would have  wanted  our
menu to pause for input from the keyboard instead, we  would
press the <DELETE> key.  We will try this combination later.
 
The  first  step is to move to a line we want to  use,  (say 
line  5) and type in the statement we want to appear on  the 
drawing  screen.  In this case we are going to use  the  new 
menu item to draw parking islands.  So we type "P ISLAND" on 
line  5. Then in order to use Prompt Entry, we  press  [F9].
 
Menumaker  will  now  emulate Autocad.  And  as  you  type, 
will combine  all  of  your commands and responses  into  one
command string  for line 5.  Just as  you would in a drawing,
respond  to the prompts as follows:
 
Command: LINE                       (Press the <RETURN> key)
From point: <Pick>                  (Press the <INSERT> key)
To point: <Pick>                    (Press the <INSERT> key)
To Point:                           (Press the <RETURN> key)
Command: ARC                        (Press the <RETURN> key)
Center/<Start point>:               (Press the <RETURN> key)
End point: <Pick>                   (Press the <INSERT> key)
Command: LINE                       (Press the <RETURN> key)
From point:                         (Press the <RETURN> key)
To point: <Pick>                    (Press the <INSERT> key)
To point:                           (Press the <RETURN> key)
Command:
 
Another  editing tool Menumaker displays, is the  length  of 
the command string.  Notice the length of this string is  27 
characters and is designated in the upper left corner of the 
Prompt  Entry  window.   As you  enter  commands  and  their 
responses, Menumaker will continue to update that length  as 
you  go. Remember, each line on the Submenu is limited to  a 
total length of 150 characters.
 
You have now finished our  command string which will draw  a 
line,  continue with an arc and finish with another line  to 
be  used in drawing our parking island.  Next we  will  save 
this  string on our Submenu by simply pressing  [F2].   Then 
Menumaker  will place the comment "* Prompt Entry *" as  the 
description  of our line so that we will know by what  means 
we created this command.
 
Before you move on, let's look at what you have created.  To 
do  so, we leave the cursor on line 5 and press  [F8].  

Menumaker has displayed the Custom Entry format, but we just 
want  to review our command.  Since we do not want  to  make 
any changes at this time, press <ESCAPE> to abort the Custom 
Entry.
 
Next,  we  will add another command using  Prompt  Entry  to 
make  a layer called "HANDICAP", set the color to blue,  set 
the  linetype to continuous and make "HANDICAP" the  current 
layer.   It will also insert a block called "HCSYMBOL" at  a 
scale to be determined in our drawing from the keyboard  and 
a rotation to be designated by your input device.  (Be  sure 
to  create  a  block  called  "HCSYMBOL"  in  your   drawing 
directory in order to allow this command to work).
 
The  first  step is to move to a line you want to  use  (say 
line  6) and type "HCSYMBOL" for the statement you  want  to 
appear  on the drawing screen.  Then press [F9]  for  Prompt 
Entry.   Now that you are in Prompt Entry, imagine that  you 
are  in  an  Autocad drawing.  Now  type  in  the  following 
commands to create your string:
 
Command: LAYER                                      <RETURN>
Make/Set/New/On/Off/Color/Ltype/Freeze/Thaw: MAKE   <RETURN>
New current layer<default>: HANDICAP                <RETURN>
Make/Set/New/On/Off/Color/Ltype/Freeze/Thaw: C      <RETURN>
Color: BLUE                                         <RETURN>
Layer name(s) for color (color): HANDICAP           <RETURN>
Make/Set/New/On/Off/Color/Ltype/Freeze/Thaw: L      <RETURN>
Linetype ( or ? )<default>: CONTINUOUS              <RETURN>
Layer name(s) for Linetype <default>:               <RETURN>
Make/Set/New/On/Off/Color/Ltype/Freeze/Thaw:        <RETURN>
Command: INSERT                                     <RETURN>
Block name (or ?): HCSYMBOL                         <RETURN>
Insertion point: <pick>                             <INSERT>
X scale factor <1> / Corner / XYZ: <keyboard>        <DEL>
Y scale factor (default = X):                       <RETURN>
Rotation angle <0>: <pick>                          <INSERT>
Command:
 
Please note that Autocad supports several different ways  of 
responding  to  any given statement.   Menumaker  will  also 
support  these  variations even though we can  not  describe 
them all here.  After you have completed the above  sequence 
press  [F2] to save them and return to the  Submenu  Editor. 

 
3.7  Custom Entry
____________________________________________________________
We  would  now  like to explore more of  the  editing  tools 
available  to us.  As you become more comfortable  with  the 
creation  of  your  own menus, you  will  probably  want  to 
explore  the format of the actual command string as  Autocad 
will  execute it in a drawing.  Custom Entry  displays  this 
command string used in an Autocad  menu item and allows  you 
to  modify  it.
 
To  demonstrate  this we can use our present  example.   Our 
goal in the creation of our next menu item is to create  one 
that  will insert the same handicapped symbol on a  drawing. 
But  this time we want to put it on a layer called  "SYMBOL" 
instead of "HANDICAP".
 
Now,  since  we already created most of the command  in  the 
line  above, we should re-use what we can in order  to  save 
time.   To  do this, we need to copy line 6 to  line  7  and 
change  the  statement and then modify the  command  string. 
The first step is to move the cursor to the line we want  to 
copy and press [F5] to mark this line as a block for editing 
purposes.  The second step is to move the cursor to the line 
we want to place the new item on (say on line 7) and type in 
a statement (say "ALT SYMB").
 
We can now either move or copy the "marked" block to the new 
location (line 7).  In this case we only want to copy it  so 
press [F6] and Menumaker will place a copy of line 6 on line 
7.   Next retype the statement for line 7, changing it  from 
"HCSYMBOL" to "ALT SYMB".
 
Finally  we could redo the command using Prompt  Entry,  but 
for  purposes  of this demonstration let's change  it  using 
Custom  Entry.  To do so press [F8] with the cursor on  line 
7.  The Custom Entry window will appear showing the  command 
string  as it was inputted on line 6.  We may now  move  the 
cursor  to the word "HANDICAP" and retype the word  "SYMBOL" 
over  the top of it. (the <DELETE> key will erase the  extra 
letters.   

Once you are satisfied with your changes, press <RETURN>  to 
save  it and return to the Submenu Editor.  Please note  the 
letters  "CE"  now appear at the end of the  Description  to 
denote that this line was edited using Custom Entry.
 
Please  note  that  our demonstration  of  Custom  Entry  is 
limited  for  purposes of this tutorial.  You  are  able  to 
modify  any  command as much as you want and  see  what  the 
results  will be in your drawings.  But be  careful.   Every 
character  has its purpose in the command string.  We  would 
suggest  that you make several different items  and  observe 
what happens and then modify  one item at a time.  Remember, 
the options are limitless.
 
Before  we  finish, we need to add a command to one  of  the 
existing  lines.   We  want each of the lines  to  tell  the 
screen  menu  to return to the Master submenu after  it  has 
completed  its command.  To do this we move the cursor  back 
up  to the line we want to add it to and press [F10] to  get 
to  Command Entry.  Menumaker will tell us that there  is  a 
command already existing and ask if we want to append to  or 
replace  it.   Since we want to add to it press "A"  and  we 
will go on to the Command Editor.
 
The  sequence for changing a submenu is the same as  before.  
Once  there  the sequence is the same as before.   With  the 
cursor  at -SUBMENU- press [F2] and then <return>  with  the 
marker  adjacent  to Screen because we are  dealing  with  a 
screen  menu.   When  asked for a Submenu to go  to  we  can 
either type in "S" or simply press <RETURN> since it was the 
previous menu.
 
Notice that the Command Description now has two pluses  (++) 
after * Prompt Entry *.  This tells us that we have added to 
it.  You may add to a line as many times as you like,  being 
only limited to a total of 150 characters.  The only way you 
can  delete from inside a command string is  through  Custom 
Entry.   Take  the time and add the command  description  to 
return to the Master Submenu "S" to the other lines.
 
Now that we are finished we must save our Submenu and return 
to the Submenu Directory by pressing [F2].
 

3.8  Writing Your New Menu
____________________________________________________________
Now  that we have a modified menu, it's time to try it in  a 
drawing.   To  do  so  we need to get  out  of  the  Submenu 
Directory  Editor  and return to the Main Menu  by  pressing 
<ESCAPE>.   Then we need to move to the Utilities  directory 
to  write  out our menu in an Autocad format.   To  do  this 
press "U". 
 
Please  note  the name of the Menu that  you  are  currently 
working  with at the top left corner of the screen (in  this 
case SAMPLE).  When you write out a menu, it is the one that 
is  designated that will be written out.  If you had  wanted 
to  write out a different one, you would have entered a  "C" 
on  the main and changed the name of the current menu  being 
edited.  Press "W" and Menumaker will ask what name you want 
to  write out your current menu under.  Type in a  name  you 
would  like  to  use.   We would  suggest  that  you  use  a 
different  name (ie. test) while you are testing a  menu  as 
your  new menu replaces the menu in your Autocad  directory. 

That way you would be able to recover your original,  should 
changes  be made to your new menu that you don't  want.   As 
the  menu  is written out it will scroll up the  screen  and 
when finished will return you to the Utility menu.
 
Now  that you have written out your new menu, press  "X"  or 
<ESCAPE>  to  return to the Main Menu.  From  here  you  may 
continue with other editing or press "Q" to leave Menumaker. 
Once  outside  Menumaker  you  can  move  to  your   Autocad 
directory where your new menu is already been placed,  ready 
to  use.   At this point you may want to edit a  drawing  to 
test your menu.  Once inside a drawing type "MENU" and  then 
the name of you new menu.
 
This concludes the quick tutorial.  We have not covered  the 
programming  of pull-down windows or buttons as the  command 
editing  is  the  same as with  the  Submenus.   A  detailed 
explanation  for these areas is contained in the next  three 
chapters.
 

Chapter 4
 
Creating Menus
___________________________________________________________

4.1  General
____________________________________________________________
Menumaker  provides  both the beginner and  the  expert  the 
necessary  tools to customize their own personalized  menus. 
This  chapter provides the backbone around  which  Menumaker 
provides the most assistance in the creation of your  menus. 
The creation of each command is prompted with the  extensive 
use of windows displaying all of the possibilities available 
as you progress.
 

4.2  Help Windows
____________________________________________________________
Throughout Menumaker on-screen help is only one button away.  
Just press the [F1] key and help with the screen you are  on 
will  appear.   In  addition, when you are  working  with  a 
specific  Autocad  command simply press the [F1] key  and  a 
help  window for that Autocad command will appear.   At  the 
bottom of each help window, reference is made to the chapter 
in   the  Autocad  Reference  Manual  where  more   detailed 
assistance is available.
 

4.3  The Main Menu
____________________________________________________________
You   may  enter  Menumaker  either  from  within  its   own 
subdirectory   by  typing  "MENUMAKR"  or  from  your   root 
directory by typing "MM" and pressing  <RETURN>.  The  paths 
to  both Menumaker and for your edited menus going  to  your 
Autocad directory were established during the  Installation. 
 
Menumaker  will  display this is as the main menu  and  will 
always  return to it prior to exiting to DOS.  At the  upper 
left of the screen is information concerning your version of 
Menumaker and your Serial Number.  Below this is the name of 
the current menu you are working with.
 
On-Screen  Help  is  available for this  or  any  window  or 
command by pressing [F1].


4.3a  Edit Auxiliary Buttons
____________________________________________________________
Menumaker  allows  for the customization of the  buttons  on 
your auxiliary button device.  Currently Menumaker  supports 
up to 16 buttons which is the same as Autocad.  In order  to 
edit  your  buttons,  enter an "A" at the  main  menu.   
 
Each  line  above  corresponds  with  the  button  on   your 
auxiliary   device.    Although  up  to   16   buttons   are 
programmable,  please  note the number of  buttons  on  your 
auxiliary device in order not to exceed the number you have. 
If you accidentally edit more buttons than you have on  your 
auxiliary device, it will make no difference other than  you 
will not be able to use those extra commands.
 
Entering a Command
____________________________________________________________
Editing  a command for an auxiliary button follows much  the 
same format as a command on the Submenu.  Notice that  there 
is  no place to make a statement because there is no  screen 
to  show  you what the commands are.  In order  to  edit  an 
auxiliary  button move the marker up or down on the list  to 
the number you want to work with and press <RETURN>.
 
Please  notice  that  if  a  command  was  already   present 
Menumaker will not ask if you want to append or replace  it. 
Because  of the complexity of the commands  associated  with 
buttons,  Menumaker  will always replace the command  if  it 
already  exists.  Therefore, the list of commands  available 
will immediately appear at the right of the screen.

You may now tie a specific command to your auxiliary button.  
To do so, move the marker to the appropriate command and use 
either  Custom, Prompt or Command Entry to create  your  new 
item.

Once  you have completed the editing of your  buttons  press 
[F2] to save your changes and return to the Main Menu.
 
Special Editing Tools
____________________________________________________________
Menumaker  also  provides two function  keys  as  additional 
tools that can be used during the editing of your menus.   A 
description of these are:
 
  [F4] Command Description
       Menumaker  allows you to edit the description of  the 
       button you have indicated with the marker.  This DOES 
       NOT  change the command associated with  the  button. 
       To  do  so, move the marker adjacent  to  the  button 
       number  and  press [F4].  If  Menumaker  had  already 
       placed  a description there, it would appear and  you 
       will  be  able to edit it.  Type whatever  notes  are 
       helpful  and  when finished  press  <RETURN>.   These 
       notes will appear but not effect the command.
 
  [F8] Custom Entry
       Because  there  may  be  unique  situations  in  your 
       individual  menu requirements, Menumaker  allows  you 
       edit  the actual entry for an individual button.   To 
       do  this,  move  the marker adjacent  to  the  button 
       number to be edited and press [F8].  The Custom Entry 
       Window  will  appear  showing  the  existing  command 
       string  ready  for  your editing.   Custom  Entry  is 
       discussed in detail in Chapter 6.
 
 [F10] Command Entry
       Command   Entry  guides  you  through  the   possible 
       commands  in  the  same way it does  in  the  Submenu 
       Editor.   In  order  to  enable  the  Command   Entry 
       function  of Menumaker, move the cursor to  the  line 
       you  wish to edit using this method and press  [F10]. 
       Command Entry is discussed in detail in Chapter 4.
 


4.3b  Edit Mouse Buttons
____________________________________________________________
Menumaker  also allows for the customization of the  buttons 
on your input device (mouse).  Currently Menumaker  supports 
up to 10 buttons which is the same as Autocad.  In order  to 
edit  your  buttons,  enter a "B" at  the  main  menu.  

Each  line above corresponds with the button on  your  input 
device.  Although up to 10 buttons are programmable,  please 
note the number of buttons on your input device in order not 
to  exceed  the number you have.  If you  accidentally  edit 
more  buttons  than you have on your input device,  it  will 
make  no difference other than you will not be able  to  use 
those extra commands.
 
Entering a Command
____________________________________________________________
Editing  a command for an input device button  follows  much 
the  same format as a command on the Submenu.   Notice  that 
there  is no place to make a statement because there  is  no 
screen to show you what the commands are.  In order to  edit 
an  input  device button move the marker up or down  on  the 
list to the number you want to work with and press <RETURN>.
 
Please  notice  that  if  a  command  was  already   present 
Menumaker will not ask if you want to append or replace  it. 
Because  of the complexity of the commands  associated  with 
buttons,  Menumaker  will always replace the command  if  it 
already  exists.  Therefore, the list of commands  available 
will immediately appear at the right of the screen. 
 
You  may  now tie a specific command to  your  input  device 
button.   To  do  so, move the  marker  to  the  appropriate 
command  and use either Custom, Prompt or Command  Entry  to 
create your new item.

Once  you have completed the editing of your  buttons  press 
[F2] to save your changes and return to the Main Menu.
 
Special Editing Tools
____________________________________________________________
Menumaker  also  provides two function  keys  as  additional 
tools that can be used during the editing of your menus.   A 
description of these are:
 
  [F4] Command Description
       Menumaker  allows you to edit the description of  the 
       button you have indicated with the marker.  This DOES 
       NOT  change the command associated with  the  button. 
       To  do  so, move the marker adjacent  to  the  button 
       number  and  press [F4].  If  Menumaker  had  already 
       placed  a description there, it would appear and  you 
       will  be  able to edit it.  Type whatever  notes  are 
       helpful  and  when finished  press  <RETURN>.   These 
       notes will appear but not effect the command.
 
  [F8] Custom Entry
       Because  there  may  be  unique  situations  in  your 
       individual  menu requirements, Menumaker  allows  you 
       edit  the actual entry for an individual button.   To 
       do  this,  move  the marker adjacent  to  the  button 
       number to be edited and press [F8].  The Custom Entry 
       Window  will  appear  showing  the  existing  command 
       string  ready  for  your editing.   Custom  Entry  is 
       discussed in detail in Chapter 6.
 
 [F10] Command Entry
       Command   Entry  guides  you  through  the   possible 
       commands  in  the  same way it does  in  the  Submenu 
       Editor.   In  order  to  enable  the  Command   Entry 
       function  of Menumaker, move the cursor to  the  line 
       you  wish to edit using this method and press  [F10]. 
       Command Entry is discussed in detail in Chapter 4.
 


4.3c  Editing Icon Boxes (Rel.9+)
____________________________________________________________
In  order  to begin editing the Icons on your  current  menu 
type an "I" at the main menu and you will move to the  Icon-
Box Editor.
 
Shown above is the Icon-Box Editor.  On the left side of the 
screen  is a list of the various commands available for  the 
manipulation of your Icons.  At the right is a directory  of 
all of the Icon Screens that are used with your current menu 
and are listed in the order they appear in the final  format 
of a menu.
 
IMPORTANT:  In order to better understand how a set of Icons 
is  created  and displayed, think of each Icon Screen  as  a 
different set of Icons displayed together in your  drawings. 
The  list on the right is a directory of the names of  these 
Icon  Screen displays.  Please note that it does not  matter 
what order they are listed as Autocad moves to whatever Icon 
screen you have requested.

Move the cursor through the directory of Icon Screens to the 
one you want to edit.  The up, down, Pg Up, Pg Dn, Home  and 
End keys will move you through this directory.  You may also 
type  the  first  letter  of the  Icon  Screen  desired  and 
Menumaker  will take you to the first Icon  Screen  starting 
with that letter.  After placing the marker next to the Icon 
Screen you wish to edit press [F2] or <RETURN> and Menumaker 
will move to that Icon Screen.

Other commands to be used in the Icon-Box Editor are:
 
  [F2] Go to the Icon
       When you have placed the marker adjacent to the  Icon 
       Screen  you wish to edit, press [F2] to move to  that 
       Icon Screen for that submenu.
         
  [F3] Delete an Icon Screen
       Move  the marker on the directory to the Icon  Screen 
       you wish to delete.  Then press [F3].  Menumaker will 
       ask  you if you are sure you want to delete the  Icon 
       Screen  you have marked.  Enter a Y or N to  complete 
       the deletion.
 
  [F4] Rename an existing Icon Screen
       Move  the marker on the directory to the Icon  Screen 
       you wish to rename.  Then press [F4].  Menumaker will 
       ask you for the new name you would like to call  this 
       Icon  Screen.  Then it will check to see if the  Icon 
       Screen  already exists, and if not will  then  rename 
       it.  If the name already exists, Menumaker will  tell 
       you so and not permit a duplication.
 
  [F5] Create a new Icon Screen
       Press  [F5] to create a new Icon  Screen.   Menumaker 
       will  then  ask  you for the name of  your  new  Icon 
       Screen.  Enter in any 10 digit text without including 
       spaces.
 
  [F6] Copy an Icon Screen
       Move  the marker on the directory to the Icon  Screen 
       you  wish to copy to another name.  Then press  [F6]. 
       Menumaker  will  ask you for the new name  you  would 
       like  to be created using the contents of the  other. 
       Then  it  will check to see if the  new  Icon  Screen 
       already  exists,  and if not will then  complete  the 
       process.   If the name already exists Menumaker  will 
       tell you so and not permit a duplication.  The  newly 
       created Icon Screen will appear below the marker when 
       it is copied.
 
On-Screen Help is available by pressing [F1].

Please  note that when an Icon screen is chosen  the  screen 
that appears is divided into 4,9 or 16 boxes which represent 
the  arrangement  of Icons as they would appear  when  using 
them  in an Autocad drawing.  At the top of the boxes is  an 
area reserved for the title that will appear when used.   At 
the  bottom  left is an area where the description  of  your 
command  used  in conjunction with the  Icon  is  displayed. 
Along the bottom of the screen are the various function keys 
used to edit your Icons as detailed below.

Function Keys
____________________________________________________________
Specific function keys have been programmed to assist in the 
editing of Icon-Boxes as shown below:
 
  [F2] Done
       Throughout Menumaker the [F2] key will save what  you 
       are currently doing and return to the previous menu.
 
  [F3] Delete
       Move  the cursor to the Icon-Box you wish  to  delete 
       and  press  "F4".   Menumaker  will  delete  the  box 
       immediately without asking if you are sure.

  [F4] Edit Description
       Menumaker  allows for the editing of the  description 
       command  without modifying the command string.   This 
       may be used to make notes only visible to you as  the 
       programmer.  In order to do this, move the cursor  to 
       the  appropriate  box and press [F4].  Then  type  in 
       your comments and press <RETURN>.
 
  [F5] Change #
       At  any time you may change the number of Icon  boxes 
       you see on your screen to correspond to the number of 
       Icons  you  are  using.  Simply press  [F5]  and  the 
       screen  will toggle between 4, 9 or 16  boxes.   Note 
       that if you have a slide and command in a box that is 
       not  shown  because  you have  toggled  to  a  lesser 
       number, that information is not lost.  Simply  toggle 
       again  and the screen will eventually return   to  16 
       boxes.
 
  [F6] Slide
       This  function key allows you to designate the  slide 
       that will appear when used in a drawing.  Simply move 
       the Marker to the Icon-Box you wish to edit and press 
       [F6].   The slide window will appear  requesting  the 
       name  of  the  slide  you wish  to  use.   There  are 
       examples  of  how Autocad requires the  slide  to  be 
       designated.   If  you  place a  space  as  the  first 
       character,  the  following text that you  enter  will 
       appear instead of a slide.  Once you have  designated 
       a slide you will move on to Custom, Prompt or Command 
       Entry to place a command string with the slide.

  [F7] Title
       The title is the area above the Icons as they  appear 
       in  an Autocad drawing.  In order to create  or  edit 
       the title press [F7] and enter whatever text you want 
       to appear above the Icon Screen.  Note that depending 
       upon  the resolution of your monitor not all  of  the 
       characters  may  appear when used in a  drawing.   If 
       this should happen, simply shorten the title.
 
  [F8] Custom Entry
       Custom  Entry will allow you to add a command to  the 
       Icon  Box.   In  order to  enable  the  Custom  Entry 
       function of Menumaker, move the marker to the box you 
       wish  to  edit  using this  method  and  press  [F8]. 
       Custom Entry is discussed in detail in Chapter 5.
 
  [F9] Prompt Entry
       Prompt  Entry  will  allow you to  add  one  or  more 
       commands  to  the Icon Box.  In order to  enable  the 
       Prompt  Entry function of Menumaker, move the  cursor 
       to  the  box you wish to edit using this  method  and 
       press  [F9].  Prompt Entry is discussed in detail  in 
       Chapter 4.
 
 [F10] Command Entry
       Command  Entry will allow you to add commands to  the 
       Icon  Box.   In  order to enable  the  Command  Entry 
       function of Menumaker, move the cursor to the box you 
       wish  to  edit  using this method  and  press  [F10]. 
       Command Entry is discussed in detail in Chapter 4.
 
The  creation of slides and the use of slide  libraries  are 
discussed in detail in your Autocad manual.


4.3d  Editing Pull-Down Submenus
____________________________________________________________
Menumaker   also  supports  the  editing  of  the  Pull-Down 
windows  in  Autocad Release 9.  For the  purposes  of  this 
chapter  much of the process of editing a Pull-Down menu  is 
exactly  the  same as the editing for a SubMenu.   For  this 
reason, only the differences will be discussed.
 
Pull-Down Window Restrictions
____________________________________________________________
Before adding Pull-Down windows to your menu, you must  make 
sure that you are using Release 9.  Also you must make  sure 
your  video  card supports this feature.  You may  edit  the 
Pull-Down  windows without creating a problem in your  menu, 
but the windows would not appear on your screen.
 
When you read an existing menu into Menumaker that has Pull-
Down,  Menumaker will list them in the directory.  If  there
are no Pull-Down menus, Menumaker will allocate 10  submenus
and  place  them in the  directory  automatically.   Autocad
allows  each  title  of  a Pull-Down menu to  be  up  to  14 
characters  long, but since most displays provide a  maximum 
of  80 characters for the menu bar, Menumaker  averages  the 
title length to 8 characters assuming that all 10 menus will 
be used.  Should you read in a menu with titles longer  than 
8 characters, Menumaker will drop the additional characters.  
Should this happen, simply modify the titles to fit.
 
Under each Pull-Down window up to 20 lines are supported  at 
this time in Menumaker.  You should be using the same number 
of lines as allowed in the Submenu on the right side of your 
drawing.
 
Editing Pull-Down Windows
____________________________________________________________
In  order to begin the editing process type in a "P" at  the 
main menu.

Notice that the screen is basically the same as the  Submenu 
Editor.   All of the commands perform the same as those  for 
the  Submenus.  To edit a Pull-Down Submenu move the  marker 
down the list using the up, down, Pg Up, Pg Dn, Home or  End 
keys and press [F2] or <RETURN>.
 
Menumaker designates its Pull-Down Windows as *POP1,  *POP2, 
etc.  and  retains this designation  throughout  the  menus. 
Menumaker  also maintains this designation with  each  "POP" 
title  standing for an individual column across the  top  of 
your  screen.  
 
After  you have finished editing these Pull-Down Menus  with 
Submenu  Editor, Autocad will ignore those Submenus  (*POP7, 
*POP8, etc.) that do not have any commands underneath  them. 
Autocad will take those that do and spread them from left to 
right  across  the top of your drawing  screen.   Therefore, 
there is no reason to delete these extra Pull-Down Submenus. 
Should one be accidentally deleted and you would like to add
another column simply add another "*POP" title (*POP5, etc.)
that has not already been used.
 
 
Editing The Pull-Down Submenu
____________________________________________________________
After  you have placed the marker adjacent to the  Pull-Down 
menu you wish to edit press [F2] or <RETURN>.
 
If  there had been existing menu items from a menu that  you 
had read into Menumaker, they would have been placed in  the 
appropriate places within this Submenu.  If there were  none 
the menu would appear as above.
 
Editing  of  the  individual lines is done  exactly  as  the 
Submenus are done for the main menu.  The only exception  is 
that  the first command on each of the Pull-Down windows  is 
reserved.   Menumaker has placed a reminder at the  location 
for you (* * * * * Reserved * * * * *).  Whatever you  place 
on line 1 of a "POP" menu (*POP1, *POP2, etc.) will be  what 
Autocad  displays  across the top of the drawing  over  that 
particular column.  Please note that if a command is  placed 
in addition to a title, Autocad will ignore it at this time.
 
Function Keys
____________________________________________________________
The function keys used in the Pull-Down windows are  exactly 
the  same  as those used in Command Entry and  will  not  be 
repeated  here.   Refer  to  Chapter  4.3e  for   additional 
information.


4.3e Editing the Screen Menu
____________________________________________________________
In  order to begin editing your current menu type a  "S"  at 
the  main  menu and you will move to the  Submenu  Directory 
Editor.
 
Shown  above is the Submenu Directory Editor.  On  the  left 
side  of  the  screen  is a list  of  the  various  commands 
available for the manipulation of the your submenus.  At the 
right  is  a directory of all of the submenus that  make  up 
your current menu and are listed in the order they appear in 
the final format of a menu.
 
IMPORTANT:   In  order to better understand how  a  menu  is 
created and displayed, think of each Submenu as a  different 
screen display used in your drawings.  The list on the right 
is  a  directory  of the names  of  these  screen  displays. 
Please  note  that it does not matter what  order  they  are 
listed  as  Autocad moves to whatever screen menu  you  have 
requested.   The only item to remember is that  the  Submenu 
name at the top of the directory is the one that will appear 
on your screen when you first start a drawing in Autocad.
 
Move  the cursor through the directory of  submenus  (screen 
displays) to the one you want to edit.  The up, down, Pg Up, 
Pg  Dn,  Home  and  End keys  will  move  you  through  this 
directory.   You  may  also type the  first  letter  of  the 
Submenu  desired  and Menumaker will take you to  the  first 
Submenu starting with that letter.  After placing the marker 
next to the submenu you wish to edit press [F2] or  <RETURN> 
and  Menumaker  will  move to the Submenu  Editor  for  that 
screen display.
 
Other  commands to be used in the Submenu  Directory  Editor 
are:
 
  [F2] Go to the Submenu
       When  you  have  placed the marker  adjacent  to  the 
       Submenu  you wish to edit, press [F2] to move to  the 
       Submenu Editor for that submenu.
         
  [F3] Delete a Submenu.
       Move  the marker on the directory to the submenu  you 
       wish to delete.  Then press [F3].  Menumaker will ask 
       you  if you are sure you want to delete  the  Submenu 
       you  have  marked.  Enter a Y or N  to  complete  the 
       deletion.
 
  [F4] Rename an existing Submenu.
       Move  the marker on the directory to the Submenu  you 
       wish to rename.  Then press [F4].  Menumaker will ask 
       you  for  the new name you would like  to  call  this 
       Submenu.   Then it will check to see if  the  submenu 
       already  exists, and if not will then rename it.   If 
       the  name already exists, Menumaker will tell you  so 
       and not permit a duplication.
 
       NOTE:   Be  careful  when  renaming  submenus   since 
       throughout  your  other submenus you may have  had  a 
       menu  item that would change the submenu to  the  old 
       name  and  now would not work.  You must  go  through 
       these and change the name to the new one.

  [F5] Create a new submenu
       Press  [F5] to create a new submenu.  Menumaker  will 
       then ask you for the name of your new submenu.  Enter 
       in any 10 digit text without including spaces.
 
       If  you add one space after the title followed  by  a 
       number, Menumaker will start that submenu that number 
       of  lines down form the top of the screen.  NOTE:  Be 
       careful, as this may cause items on your menu to fall 
       below  the  number of lines supported by  your  video 
       card.

  [F6] Copy a Submenu.
       Move  the marker on the directory to the Submenu  you 
       wish  to  copy  to another name.   Then  press  [F6]. 
       Menumaker  will  ask you for the new name  you  would 
       like  to be created using the contents of the  other. 
       Then it will check to see if the new Submenu  already 
       exists,  and if not will then complete  the  process. 
       If the name already exists Menumaker will tell you so 
       and  not  permit a duplication.   The  newly  created 
       submenu  will  appear  below the marker  when  it  is 
       copied.
 
On-Screen Help is available by pressing [F1].
 
Submenu Command Editing
____________________________________________________________
After requesting a specific Submenu, Menumaker will  replace 
the window with the Submenu Editor.
 
The  name of the main menu and the Submenu you  are  working 
with  will  be  shown  at the  right  side  the  screen  for 
reference.  Two columns make up the layout for your submenu. 
On  the  left are lines 1 through 20 representing  what  you 
will  see  on the right side of your  drawing  screen.   The 
right column provides a brief description of your command.
 
Please  note that Menumaker Ver. 3.02 offers a maximum of 20 
lines for each Submenu.  Higher resolution video cards allow 
more  than 20 lines but at this time you are unable to  edit 
them  on the Menumaker screen.  A trick that can be used  to 
show  more  than 20 lines is to display two or  more  screen 
menus  at a time.  The first might start at line 1  and  the 
second  at line 21.  You must remember that to do  this  the 
submenu  names  must be followed by a number that  you  want 
them  to start on.  Also when using them, you need  to  call 
them  up  at the same time.  This can  be  complicated,  but 
offers  a  solution  to  editing more  than  20  lines.   Be 
careful!  This is for experienced Menumakers only.

You may want to place descriptions in your menus to show the 
user  such things as titles, company names, etc.  To do  so, 
simply type whatever description you would like to appear as 
shown below.  In addition a command statement can be written 
as  shown on line 4 on the example above.  Please note  that 
this  statement can be in any form familiar to the  user  as 
the actual Autocad command will be added later.
 
Function Keys
____________________________________________________________
Specific function keys have been programmed to assist in the 
editing of Submenus as shown below:
 
  [F2] Done
       Throughout Menumaker the [F2] key will save what  you 
       are currently doing and return to the previous menu.
 
  [F3] Delete
       Move  the cursor to the line on the Submenu you  wish 
       to delete and press "F4".  Menumaker will delete  the 
       line  immediately  without asking if  you  are  sure. 
       With  the Insert on, Menumaker will remove  the  line 
       and  replace it with a blank.  With Insert  off,  the 
       line will be deleted and everything moved up a line.
 
  [F4] Edit Description
       Menumaker  allows for the editing of the  description 
       command without creating a command string.  This  may 
       be  used  to make notes only visible to  you  as  the 
       programmer.  In order to do this, move the cursor  to 
       the  appropriate line and press [F4].  Then  type  in 
       your comments and press <RETURN>.
 
  [F5] Marker for Editing Purposes
       Move  the cursor to the line on the Submenu you  wish 
       to  highlight  for either copying or  moving.   Press 
       [F5] and a marker will appear to the left of the line 
       number.
 
  [F6] Copy
       Place the cursor at the location on the Submenu where 
       you  would like the new command copied  to.   Another 
       line  must  have  been "marked"  using  the  [F5]  as 
       discussed  above.  Now press [F6] and Menumaker  will 
       copy the existing line together with all commands  to 
       the  new  location.   You may  then  modify  the  new 
       location.  Be careful.  If there is something at  the 
       location you are copying to, it will be erased.
 
  [F7] Move
       Place the cursor at the location on the Submenu where 
       you  would  like the new command moved  to.   Another 
       line  must  have  been "marked"  using  the  [F5]  as 
       discussed  above.  Now press [F7] and Menumaker  will 
       move the existing line together with all commands  to 
       the  new  location.   You may  then  modify  the  new 
       location.  Be careful.  If there is something at  the 
       location you are moving to, it will be erase.
 
  [F8] Custom Entry
       In  order  to  enable the Custom  Entry  function  of 
       Menumaker,  move the cursor to the line you  wish  to 
       edit using this method and press [F8].  Custom  Entry 
       is discussed in detail in Chapter 5.
 
  [F9] Prompt Entry
       In  order  to  enable the Prompt  Entry  function  of 
       Menumaker,  move the cursor to the line you  wish  to 
       edit using this method and press [F9].  Prompt  Entry 
       is discussed in detail in Chapter 4.
 
 [F10] Command Entry
       In  order  to enable the Command  Entry  function  of 
       Menumaker,  move the cursor to the line you  wish  to 
       edit  using  this method and  press  [F10].   Command 
       Entry is discussed in detail in Chapter 4.
 
In  either of these two cases, after entering the  statement 
press  [F10]  and  Menumaker  will  return  a  list  of  all 
available  Menumaker and Autocad commands on the right  side 
of the screen.

You may now tie a specific command to your statement.  To do 
so, move the  marker  to the appropriate command.   The  Up, 
Down, Pg Up, Pg Dn, Home and End keys will move you  quickly 
through this list.  In addition, if you know the command you 
are  going  to  use, simply type the  first  letter  of  the 
command  at any spot on the list of commands  and  Menumaker 
will  move to that area of the list.  When the marker is  at 
your  command  press  [F2]  or  <RETURN>  and  the   windows 
associated with that command will appear.
 
Menumaker  will  show  you  all  of  the  Autocad   commands 
available  through  ADE+3  for the version  of  Autocad  you 
indicated  in the Installation of Menumaker.  But if you  do 
not  have the corresponding version of Autocad the  commands 
will  not work.  This will not cause problems with the  menu 
in  other areas that are not supported with your version  of 
Autocad.
 
Command Windows
____________________________________________________________
After placing the marker adjacent to a command and  pressing 
either  [F2] or <RETURN>, a Command window  associated  with 
that specific command  will appear. 
 
Each  command  will  display a window  showing  the  options 
available  to  you for using the particular  command.   Some 
commands  that  offer  no options will  tell  you  what  the 
command will do and when you press any key to continue  will 
write  the command string.  Other commands offer no  options 
but  require  a single input.  Menumaker will ask  for  this 
value and once you have typed it in, the command string will 
be completed.
 
At any time a specific command window is being displayed  on 
the  screen, help with that Menumaker or Autocad command  is 
available  by  pressing  [F1].  In the case  of  an  Autocad 
command  the Help Window will look just like the window  you 
see  while  editing a drawing in Autocad.  The  Help  Window 
will  also  refer  you to the  appropriate  chapter  in  the 
Autocad Reference Manual.
 
When options are available, Menumaker will provide a list of 
the  options  with  a  window  for  each  showing  a   brief 
description as shown in the example.  Shift between  options 
using  the Up and Down arrow keys.  Notice that as  you  do, 
the description at the right changes to the new option.  
 
Move  the  box  to  the option you wish  to  use  and  press 
<RETURN>.   Menumaker  may  ask  for  any  additional  input 
required to complete the command string as shown below.   In 
some cases an additional set of window prompts will  appear. 
Answer all of the questions filling in the required data.

Repetitive Commands
____________________________________________________________
Many  times  in a drawing it is useful to repeat  a  command 
more than once in order to eliminate going back to the  menu 
to  choose  the  command again.   Menumaker  allows  you  to 
program this into your menus for most commands as follows:
 
After you have answered the appropriate questions within the 
command window, Menumaker will ask you if you would like  to 
repeat  the command in your command string.  Enter a Y or  N 
and  press RETURN.  The command string is then  created  and 
placed with your statement.
 
Please  note.   Because  of the complex  nature  of  Autocad 
commands,  not all of then can be repeated in  your  command 
string.  Menumaker will give you the option to repeat  where 
ever possible.
 
Command Descriptions
____________________________________________________________
Once the command string has been created a brief description 
appears  to  the  right of  your  statement.   In  addition, 
several  other items will appear that have  significance  as 
discussed in the following list.
 
       R
       An  "R"  appearing  at  the  start  of  your   string 
       indicates  that this command will repeat itself  when 
       used  AND/OR  is restricted to no  further  appending 
       because of the complex nature of the command.  Please 
       Note:  Once a command string has an "R" in  front  of 
       the description, you should not append to it  because 
       the end result may not work.  In some cases appending 
       may  work,  but  you  should  experiment  with   this 
       carefully.
 
       ++
       Several  pluses (++) after the string  indicates  the 
       string has been appended to.
 
       CE
       A "CE" after the string indicates that it was  either 
       entered  or  edited with the  "Custom  Entry"  option 
       discussed later.
 
       *Prompt Entry*
       A "Prompt Entry" instead of the string indicates that 
       it  was  created  using  the  "Prompt  Entry"  option 
       discussed later.
 
       Several  of  these options may be  included  in  your 
       description as you continue to edit your commands.

       Existing Command
       An "Existing Command" instead of the string indicates 
       that it was read in from an existing menu and has not 
       yet been modified.
 
       Menumaker  also  lets  you  add  on  to  an  existing 
       command.   To do so, move the cursor to the line  you 
       wish  to  append  and  press  [F8],  [F9]  or  [F10]. 
       Menumaker  may ask if you want to Append  or  Replace 
       it.  Enter an "A" or "R" and Menumaker will  continue 
       with the list of commands from which you will  choose 
       from.   When appending, Menumaker will  automatically 
       combine it with your current string.  You may  append 
       to a string as many times as you like.  You are  only 
       limited to a total of 150 characters in the  ultimate 
       command  string.   If you do not want to  replace  or 
       append the command, simply press <ESCAPE>. Experiment 
       with  this  carefully,as some  combinations  may  not 
       work.
 
Menumaker Editing Notes
____________________________________________________________
Menumaker  also provides many additional editing tools  that 
can  be  used during the creation of your  menus.   A  brief 
description of these follows:
 
  [F4] Single Command (only while in Command Entry)
       Menumaker  also  allows for a  single  command  entry 
       without   requesting  additional  input.    This   is 
       normally done when you only want the command inserted 
       once without any further input from your menu.  To do 
       so, place the cursor on the line you wish to edit and 
       type  in  the  statement you wish to  appear  on  the 
       screen  and  press <RETURN>.  Then move  your  marker 
       through the list of commands to the one you want  and 
       press [F4].  This will place the command in the  menu 
       and  when used in a drawing will simply  execute  the 
       command and then wait for additional input.
 
  [F8] Custom Entry as a command viewer
       Many  times  it is desirable to  view  your  finished 
       command  string for format, spelling, etc.   Whatever 
       the  reason,  place the cursor on the line  you  have 
       chosen and press [F8].  This normally would allow you 
       to  custom edit the string but for your purposes  now 
       it  is simply a means of viewing your final  product. 
       After  viewing  simply press <ESCAPE>  and  Menumaker 
       will  return  without  making  any  changes.   Actual 
       Custom Editing is discussed in Chapter 6.
 
       Cursor Movement
       In  addition to the arrow keys mentioned  previously, 
       Menumaker also supports other editor keys.
         
       <CONTROL> E     Up Arrow
       <CONTROL> X     Down Arrow
       <CONTROL> R     Page Up
       <CONTROL> C     Page Down
       <CONTROL> A     Home
       <CONTROL> F     End
 
 
4.3f   Editing Tablet Menus
___________________________________________________________
Menumaker also allows for the customization of tablet  menus 
for  use  in  your Autocad drawings.  This  portion  of  the 
program  is referred to as Tabletmaker but is a part of  the 
total  Menumaker  software.  You are able to  layout  tablet 
menus  from  the  keyboard, specify command  strings  to  be 
associated with each point on the tablet and finally  create 
an Autocad drawing of your template automatically.

In order to begin press "T" at the main Menumaker Menu.   If 
no   tablet  has  been  defined  with  your  current   menu, 
directions for the calibration of your new tablet menu  will 
appear.

In  order  to  define the area to be used as  a  tablet  you 
should  have  it  with you in order  to  take  the  required 
measurements.   Please  note that Autocad does  not  require 
these  dimensions.   They  are  used to  create  an  Autocad 
drawing  of  your  template when you are  finished. However, 
it is a good practice to dimension all of your tablet menus.

When entering the dimensions of your tablet please note that 
       the requested dimensions are for the area to be  used 
       as  a  tablet, not necessarily the  total  digitizing 
       area.   If  you are starting a new template it  is  a 
       good  idea to place a piece of paper on  your  tablet 
       and  draw in the areas you wish to use so  that  good 
       measurements can be made.  Once you have entered  the 
       horizontal  and vertical dimensions, you must  decide 
       how  many  different tablet menus you  want  on  this 
       template.  Autocad allows up to four areas.  You  may 
       designate fewer than four and add more later  without 
       losing menu items.  The only requirement would be  to 
       redefine the individual areas.

After  the  answering  these  questions,  Tabletmaker   will 
display a layout of the template with the Tablet Menu  areas.

Note that in addition to the Tablet Menu areas there is also 
       an area reserved as a screen area designated with  an 
       "S".

If  you  had already been working with  a  template  layout, 
Tabletmaker  will display the current configuration.   Also, 
if you have read-in an existing menu which already  contains 
a tablet, Tabletmaker will require you to define the  areas. 
Once  the areas are defined, the existing commands  will  be 
available for modification.

Defining Templates
____________________________________________________________
The template drawing appearing on your screen allows you  to 
create a graphic representation of what your final  template 
will  look like.  Function keys displayed on the  bottom  of 
the screen have been programmed to assist you in your layout 
as follows:

  [Esc] Abort allows you to leave this editing session  with 
        or  without saving your changes.   Tabletmaker  will 
        ask you if you want to save your changes or not.

  [F1]  On  screen  help is available at any time  for  both 
        Tabletmaker and Autocad commands.

  [F2] Done.   When  ever you are finished  press  [F2]  and 
       Tabletmaker  will  save all of your  current  editing 
       session and return you to the previous menu.

  [F3]  Edit.  Once you have defined your tablet areas, move 
        to  the area you wish to edit commands in and  press 
        [F3].   This  will display a grid of  that  specific 
        area  and  allow  you to  move  through  it  editing 
        commands utilizing Custom, Prompt or Command  Entry. 
        This area is explained in detail later.

  [F4]  Define.  Once you have manipulated the areas on  the 
       screen  to a position you desire, press  [F4].   Note 
       the questions asked by Tabletmaker in the upper left-
       hand corner.  If you plan to have Tabletmaker  create
       your  template as an Autocad drawing, you must  enter
       all measurements in inches as accurately as  possible
       (use fractions of an inch in decimal form).
        If this is not required, simply press [Esc] for each 
        dimension.  Lastly the number of columns and rows is 
        required  for ALL tablet menus.  When  utilizing  an 
        existing menu, it is critical that you designate the 
        exact number for each on your existing template.

  [F5]  Next.   By pressing [F5] you will move  between  the 
        tablet and screen areas.

  [F6] Redo.  This command allows you to redefine the tablet 
       and  screen  areas  associated  with  your  template. 
       Please  note that if you Redo the template,  you  are 
       required  to redefine all of the areas (start  over). 
       The commands associated with each area are not  lost. 
       You would use this command to add an additional  menu 
       if you did not already have four areas.

  [F8]  Middle.  This command places the arrows within  your 
        current  area  in  the middle of each  of  the  four 
        sides.   With the arrows in this position, when  you 
        press  the arrow keys on your keyboard,  the  entire 
        block is moved around the screen.

  [F9]  Upper  Left.   This command places 2  arrows  within 
        your  current  area at the upper left  hand  corner. 
        With the arrows in this position, when you press the 
        arrow keys on your keyboard, the upper or left  side 
        of the area is either stretched or shrunk.

 [F10]  Lower  Right.  This command places 2  arrows  within 
        your  current area at the lower right  hand  corner. 
        With the arrows in this position, when you press the 
        arrow keys on your keyboard, the lower or right side 
        of the area is either stretched or shrunk.
 

Template Notes
____________________________________________________________
When laying out your areas on the screen you should not have 
the screens overlap although the border lines for  different 
ones can be on top of each other.


Defining Tablet Commands
___________________________________________________________
Once  you have laid out the graphic representation  of  your 
template and defined the grids for each, move the arrows  to 
the  tablet you wish to edit commands in by  pressing  [F5]. 
When  the  area  is indicated press [F3] to  edit  the  grid 
within that area.

The  Tablet area (1-4) is designated at the  top  right-hand 
corner  for your reference.  At the bottom left-hand  corner 
is  a brief description of the command associated  with  the 
box  that  your marker is in.  Next to  the  description  is 
the location of the marker designated as rows x columns.

Your  screen will display a maximum grid area of 17  columns 
by 9 rows at one time.  If there are more grids to the right 
or  below, you will notice the lines extend slightly  beyond 
the last grid.  To see the additional grids, simply use  the 
arrow  keys  on your keyboard to scroll  to  the  additional 
grids.

Move  your  marker around the grid  editing  the  individual 
boxes with the function keys described below.


Function Keys
____________________________________________________________
Specific function keys have been programmed to assist in the 
editing of Tablet Menus as shown below:
 
  [F2] Done
       Throughout Menumaker the [F2] key will save what  you 
       are currently doing and return to the previous menu.
 
  [F3] Delete
       Move  the marker to the box on the grid you  wish  to 
       delete and press "F4".  Menumaker will delete the box 
       immediately without asking if you are sure.   

  [F4] Edit Description
       Menumaker  allows for the editing of the  description 
       command without creating a command string.  This  may 
       be  used  to make notes only visible to  you  as  the 
       programmer.  In order to do this, move the marker  to 
       the  appropriate  box and press [F4].  Then  type  in 
       your comments and press <RETURN>.
 
  [F5] Marker for Editing Purposes
       Move  the marker to the box on the grid you  wish  to 
       highlight  for either copying or moving.  Press  [F5] 
       and  an  asterisk will appear on both  sides  of  the 
       marker.
 
  [F6] Copy
       Place  the marker at the location on the  grid  where 
       you  would like the new command copied  to.   Another 
       box  must  have  been  "marked"  using  the  [F5]  as 
       discussed  above.  Now press [F6] and Menumaker  will 
       copy  the existing box together with all commands  to 
       the  new box.  You may then modify the new  location. 
       Be  careful.  If there is something at  the  location 
       you are copying to, it will be erased.
 
  [F7] Move
       Place  the  marker at the box on the grid  where  you 
       would  like  the new command moved to.   Another  box 
       must  have been "marked" using the [F5] as  discussed 
       above.   Now press [F7] and Menumaker will  move  the 
       existing  box together with all commands to  the  new 
       location.   You  may  then modify the  new  box.   Be 
       careful.   If there is something at the box  you  are 
       moving to, it will be erase.
 
  [F8] Custom Entry
       In  order  to  enable the Custom  Entry  function  of 
       Menumaker,  move  the marker to the box you  wish  to 
       edit using this method and press [F8].  Custom  Entry 
       is discussed in detail in Chapter 5.
 
  [F9] Prompt Entry
       In  order  to  enable the Prompt  Entry  function  of 
       Menumaker,  move  the marker to the box you  wish  to 
       edit using this method and press [F9].  Prompt  Entry 
       is discussed in detail in Chapter 4.
 
 [F10] Command Entry
       In  order  to enable the Command  Entry  function  of 
       Menumaker,  move the cursor to the line you  wish  to 
       edit  using  this method and  press  [F10].   Command 
       Entry is discussed in detail in Chapter 4.


4.3g   Utilities
____________________________________________________________
Menumaker provides several utilities as additional tools  in 
the  editing process.  To access the Utility Menu press  "U" 
on the Main Menu.
 
Each of the Utilities perform a specific function and are 
listed below:
 
   [C] Change the current menu
       _____________________________________________________
       Menumaker allows you to move between menus during the 
       editing  process.   Please note.   The  menus  inside 
       Menumaker  are  not in a .MNU format.  They  must  be 
       converted to a .MMU format  before editing.  This  is 
       done  in  the Utilities directory  and  discussed  in 
       detail  in  Chapter  4.3e.  In order  to  change  the 
       current menu you are working with in Menumaker.
 
       Type  in the name of the new menu you would  like  to 
       work  with.  If the menu is existing, Menumaker  will 
       load it and designate your new menu as being  current 
       in the upper left corner of the screen.  If the  menu 
       does  not  exist in a Menumaker format, you  will  be 
       told  so and asked if you would like to start  a  new 
       menu by that name.  You may press <RETURN> to  create 
       the  new menu or <ESCAPE> to abort back to  the  Main 
       Menu.  If you tell Menumaker to start a new menu,  it 
       will   create  a  blank  menu  with  only  a   Master 
       Subdirectory ready for you to edit.
 
       On-Screen help is available by pressing [F1].
 

   [R] Read in Existing Menu
       Menumaker  allows  you to read in  an  existing  menu 
       provided it is in a .MNU format for editing purposes. 
       In  order to Read a menu into Menumaker , it must  be 
       in the Menumaker DOS subdirectory.  When the menu  is 
       present  ,  type  an  "R" at  the  Utility  Menu  and 
       Menumaker  will ask you for the name of the menu  you 
       would like to read in.  Type in the name leaving  off 
       the  .MNU extension and press <RETURN>.  If the  file 
       does not exist, Menumaker will say so and return  you 
       to the Utility Menu.
 
       If  the menu does exist, Menumaker will  transfer  it 
       into a format with the same name and a .MMU extension 
       ready  for  editing.   After  you  have  read  in  an 
       existing  menu you must still make it  the  "current" 
       menu by typing a "C" at the Main menu and designating 
       this new menu as the one you want to edit.
 
   [W] Write a New Menu
       Once  you  have finished editing your new  menu  this 
       utility will return it to a .MNU format and place  it 
       in your Autocad directory ready for use.  To do this, 
       be  sure  the  menu  you want to  write  out  is  the 
       "current"  menu as shown at the top of  your  screen, 
       then type a "W" at the Utility Menu.  Menumaker  will 
       ask for the name of the menu you would like to create 
       using  the  current menu.  Type in a name  and  press 
       <RETURN>.   Menumaker  also  shows the  path  to  the 
       location  where you use Autocad which was  designated 
       in the installation program.  If you move Autocad  to 
       another  subdirectory,  simply  re-install  Menumaker 
       providing the new subdirectory.
 
       When  Menumaker  moves the new menu to  your  Autocad 
       directory  and  a menu already exists with  the  same 
       name, you will be asked if you want to overwrite  the 
       existing  menu.   Answer "Y" or "N".  If Yes  then  a 
       back-up  file  (.BAK) for the existing menu  will  be 
       created.   Each  time you write a menu the  old  .BAK 
       file  will  be  replaced  by a  newer  one.   A  good 
       practice  for  editing an existing menu would  be  to 
       name  it differently when writing it out (ie.  TEST), 
       so that you can run all of your experiments with that 
       menu  before saving it to its permanent  name.   That 
       way   you  would  always  have  the   original   menu 
       unchanged.
 
   [T] Create a Template File
       Tabletmaker allows you to produce an Autocad  drawing 
       file  of your template grid for editing  in  Autocad. 
       To  do  so, press [T] and Tabletmaker will  ask  what 
       name you would like to give to the new drawing  file. 
       After typing the name, press <RETURN> and the drawing 
       file will be created and transferred to your  Autocad 
       directory.  Please note.  The drawing file will  only 
       be as good as the information you supplied during the 
       configuration of your template.  Also, only the  grid 
       is shown.  You may add whatever you wish to each  box 
       before it is plotted out.

   [P] Print Menu on Printer
       Menumaker  also allows you to produce a hard copy  of 
       your menu. The print out is broken into three columns. 

       The menu is printed in the order the submenus  appear 
       within  Menumaker.  The first column  represents  the 
       titles of the various parts of the menu designated by 
       asterisks  (*).   Under each submenu  title  are  the 
       various  statements  as they appear on  your  Autocad 
       drawing screen.  The second column contains up to  30 
       characters  of the actual command string  as  Autocad 
       uses  it.   If the string is longer than  30  spaces, 
       Menumaker  drops  off the rest of  the  string.   The 
       third column is the brief description that appears in 
       Menumaker when you are editing the submenu.
 
       This print out represents another means of  reviewing 
       your menu and using it as a tool in designing others. 
       Please  note.   If  your computer  is  not  100%  IBM 
       compatible,  an error may occur when you send a  menu 
       to the printer and the printer is not turned on.

   [S] System Information
       Menumaker   provides   a  brief   overview   of   the 
       information  associated   with your  version  of  the 
       program.   To review this information type an "S"  on 
       the  Utility Menu.  In addition to your  version  and 
       serial  number  at the top of the  page,  your  name, 
       address  and phone number are included as a means  of 
       personalizing your software.  Should you change  your 
       address  you may return the distribution disks  along 
       with $3.00 for postage and handling to IntelliCADD at 
       the  address  shown,  and  a  new  diskette  will  be 
       returned with your new information.
 
   [D] Display Colors
       Menumaker  makes extensive use of  colors  throughout 
       the  program.   This  utility simply  allows  you  to 
       adjust your monitor for color balance.  To do so type 
       a  "D"  at the Utility Menu and the  color  bar  will 
       appear.  On a monochrome monitor you will see various 
       shades and should adjust your monitor to show as many 
       as possible.
 
   [X] Exit Back to Main Menu
       This command moves you from the Utility Menu back  to 
       the  Main  Menu once you have  finished  and  changes 
       saved.
 

4.3f   Quit Menumaker
____________________________________________________________
Once  you have completed your editing process  this  command 
ends Menumaker and returns you to DOS.  Simply type a "Q" at 
the Main Menu and Menumaker will close all of your files and 
return the DOS prompt.
 

Chapter 5  Prompt Entry
 
5.1   General
____________________________________________________________
Here the lies the real power of Menumaker.  In prompt Entry, 
Menumaker displays  exactly what you would see at the bottom 
of  your  Autocad  drawing.  You simply type  in  a  command 
exactly  as  you  would  inside a  drawing.   As  you  type, 
Menumaker  responds with the same responses and prompts  you 
would  in  your  drawing.  You may  type  several  commands, 
together  including the responses, to form a single  string, 
being only limited to 150 total characters.
 
After you have completed the command string, one button [F2] 
saves all that you have entered as a single command in  your 
new  menu.   You may also Append to or Replace  an  existing 
command using this method.
 

5.2  Prompt Entry
____________________________________________________________
In order to edit an item on your submenu using Prompt  Entry
you  must first display the Submenu you wish to edit on  the
screen.   From the Main Menu press "E" to edit the menu  you
are  currently  working with.  Then  select  the  particular
Submenu  you  wish to display and press [F2].   The  Submenu 
will be displayed.
 
To use Prompt Entry move the cursor to the line you wish  to 
edit.   If there is no Statement of what "You'll See",  type 
in  what  you would like to appear on your  drawing  screen, 
then  press [F9].  If there is a command  already  existing, 
Menumaker  will  ask  if  you  would  like  to  (A)ppend  or 
(R)eplace  it.   Enter an "A" or "R" depending on  what  you 
would  like to do.  Menumaker will then display  the  Prompt 
Entry.

Notice that the bottom of the screen looks exactly like  the 
bottom  of  a  screen  when you are  editing  a  drawing  in 
Autocad.  Anything you type in at this point will generate a 
response  as  if you were typing in Autocad.  As  you  type, 
Menumaker  is  saving  everything  in  your  command  string 
exactly.  For instance, if you make a mistake and type a  ^C 
(Control  C) to stop, Menumaker will react exactly the  same 
way  as Autocad and clear your previous input.  Notice  that 
the  length  of  the command string shown  goes  back  to  4 
because  you have typed ^C and told Menumaker that you  want 
to cancel the command and start over.
 

5.3  Prompt Entry Editing Notes
____________________________________________________________
Because  of the complexity of some of the  Autocad  commands 
and  the  unique characteristics in each of  your  drawings, 
there are several editing notes that must be clarified:
 
       Length:
       Menumaker  will  display the current  length  of  the 
       command  string you are creating.  This  number  will 
       begin  with  at least 4  (^C^C  automatically  starts 
       every new command string) when you begin your  Prompt 
       Entry.  If you are appending an existing command, the 
       value  will represent the length of the existing  one 
       that  you  will be adding to.  Every time  you  press 
       <RETURN> this value will be updated.  This will  help 
       you  as you go because your total string  length  can 
       not exceed 150 characters.
 
       You  will  note that if you append an  existing  line 
       that  has a repeating command (indicated with an  "R" 
       at the beginning of the description) the Length  will 
       be 150 plus or minus.  You must change the command to 
       remove  the repetition using Custom Entry [F8] or  by 
       simply  deleting  it and starting  over  with  Prompt 
       Entry.
 
       <default>
       Throughout Prompt Entry, Menumaker will return  lines 
       including  the  term <default> in  response  to  your 
       commands.   In  a  drawing  Autocad  would  return  a 
       default   value  for  those  values  which  you   are 
       requesting  to be changed (ie. Layer,  Ltype,  Color, 
       Style, etc.).  Because Menumaker  does not not  these 
       it  will return the word <default> instead.   As  you 
       are  creating your menu using Prompt Entry,  you  can 
       either press <RETURN> to use the default settings  in 
       your drawings or type an the new value.
 
       <SPACE BAR> and <RETURN>
       Menumaker  allows you to utilize the <SPACE BAR>  and 
       <RETURN>  exactly  as  you  would  in  Autocad.   For 
       instance, when you use the space bar between commands 
       in Autocad, the previous command is executed again.
 
       <Insert>
       During  your Prompt Entry you will be asked to  input 
       answers to the various questions associated with each 
       command.  If you were in Autocad your response  would 
       be  from either your keyboard or a "pick"  from  your 
       input  device  (your mouse).  In  Menumaker  you  may 
       provide  the same response to a "pick" by  press  the 
       <Insert> key.

       Notice that when you press the <Insert> key Menumaker 
       places  a <pick> statement after the question  asked. 
       This shows that your menu, when executing, will  stop 
       and  wait  for  a  "pick"  from  your  mouse   before 
       proceeding.
 
       <Del>
       In  addition to "pick" entries from your  mouse,  you 
       may want to specify your keyboard as the input device 
       to answer the prompt from Autocad.  When asked during 
       your  Prompt  Entry to input answers to  the  various 
       questions and you want to designate a keyboard entry, 
       simply  press  the <Del> key.
 
       Notice that when you press the <Delete> key Menumaker 
       places  a  <keyboard> statement  after  the  question 
       asked.   This shows that your menu,  when  executing, 
       will  stop  and  wait for  a  keyboard  entry  before 
       proceeding.
 
       <^C>  <CONTROL C>
       Menumaker  allows you to use <CONTROL> C  exactly  as 
       you would in an Autocad drawing.  Any time you are in 
       the Prompt Entry and type a ^C, Menumaker will cancel 
       whatever  you  have been doing and return  a  command 
       prompt.   However, if you have completed one or  more 
       commands and are back at the command prompt and  type 
       ^C,  Menumaker  interprets this as  your  wanting  to 
       start  over.  Your complete string would be  canceled 
       and return a command prompt.  Notice the length  will 
       grow  as you execute each line but when you press  ^C 
       it returns to 4.
 
       <?>
       A  question mark reacts the same in Menumaker  as  it 
       does  in Autocad.  When you you type a  ?,  Menumaker 
       will  come back with same response as  Autocad.   You 
       may  type  <RETURN> for a list of  the  commands  for 
       which  help  is  available or type  the  command  for 
       specific  help.   Remember when  you  are  requesting 
       help, Menumaker is saving all of these responses  and 
       will  combine them in your string unless you  type  a 
       ^C.
 
       <'> Transparent Commands
       Transparent  commands are denoted with  a  apostrophe 
       (') in front of the command which tells Autocad  that 
       this command is not to interrupt the current  command 
       but  to execute this command once and then  continue. 
       Because   these   transparent  commands   cannot   be 
       predicted as to their outcome, Menumaker is unable to 
       support them in Prompt Entry.  Normally they are used 
       by   themselves  in  a  command.   To  create   these 
       commands, use the Command Entry, [F10].
 
       If  a transparent command is entered on  the  command 
       line (ie. 'ZOOM or 'PAN), Menumaker will respond with 
       the  statement,  "Transparent commands  can  only  be 
       entered  under  Command  Entry".   As  a  result,  no 
       command is saved to your menu.
 
       <ARRAY>, <MINSERT> and <PURGE>
       Because  of the complexity of these  three  commands, 
       Menumaker can only support these commands through the 
       first response.  For example: the purge command  will 
       ask  you what items you want to purge and  since  you 
       won't  know what has or has not been purged, you  are 
       unable to provide a response at this time.  Menumaker 
       will  accept  the initial command and  response,  but 
       then  will  be return a statement "Prompt  Entry  can 
       only  support  this  command to  this  point".   Your 
       command  will  be saved to that point and  a  command 
       prompt will appear.
 
       Should   your  application  be  specific  enough   to 
       complete  the  command  string,  you  may  enter  the 
       additional information through Custom entry.
 
       PLEASE  NOTE:  The number of combinations that  exist 
       with Autocad commands as they apply to your  drawings 
       is virtual limitless.  Because of this, we are unable 
       to  test  them all.  There may be  combinations  that 
       create  unwanted  results.   Should  this   situation 
       arise,  the normal cure is to develop the  string  in 
       Prompt Entry including the "bug" and then  experiment 
       with  it by adding to or deleting from it  in  Custom 
       Entry.
 

Chapter 6  Custom Entry
 
6.1   General
____________________________________________________________
Menumaker  also provides for the user who wishes to do  more 
with  their  menus.   At any time you  are  working  with  a 
command  string  created through either  Command  or  Prompt 
Entry,  you  may  view what Menumaker has  created  for  the 
individual  menu  string.  Then you may actually  edit  this 
string  to obtain any additional effects you  desire.   Once 
you have completed the editing using this method,  Menumaker 
will save your changes in your menu.
 

6.2  Custom Entry
____________________________________________________________
In order to edit an item on your submenu using Custom  Entry 
you  must first display the Submenu you wish to edit on  the 
screen.   From the Main Menu press "E" to edit the menu  you 
are  currently  working with.  Then  select  the  particular 
Submenu  you  wish to display and press [F2].   The  Submenu 
will be displayed.
 
To use Custom Entry move the cursor to the line you wish  to 
edit.   If there is no Statement of what "You'll See",  type 
in  what  you would like to appear on your  drawing  screen, 
then  press [F8].  If there was a command already  existing, 
Menumaker  will  ask  if  you  would  like  to  (A)ppend  or 
(R)eplace  it.   Enter an "A" or "R" depending on  what  you 
would  like to do.  Menumaker will then display  the  Custom 
Entry format.
 
Menumaker  has  shown the command string in  its  executable 
format.  You may now modify it to fit whatever your  special 
situation  is.   Normal word processing "control  keys"  and 
arrow  keys can be used for cursor movement.   The  <INSERT> 
and  <DELETE> keys allow you to insert or remove  characters 
without retyping the string. 
 
Once  you have completed your modifications, press  [F2]  to 
save  your modifications and return to your  Submenu.   Your 
modified command is now part of your menu.
 

6.3  Custom Entry Editing Notes
____________________________________________________________
Custom  Entry allows you to edit every possibility  you  can 
think  of.   You are only limited to 150  total  characters. 
Because of the ability to completely change a command string 
with a single character, care should be used.  Take the time 
to look at the commands as Menumaker creates them, and  then 
experiment with small changes and see what happens when they 
are used in a drawing.
 
 
 
Appendix A              IF DISASTER OCCURS
____________________________________________________________
Listed below are a list of possible error messages that  you 
may encounter while running Menumaker. Hopefully these codes 
should help you find the problem and solve it with out  much 
difficulty.
 
Not enough memory or
Fatal error: 8 or
Fatal error: 43
       The  most common reason for this message is a  memory 
       resident  program  is currently in  use  (ie.  Norton 
Commander, Sidekick, system managers etc.). Solution: Remove 
memory resident program and try again.
 
Fatal error: Not enough disk space  or
Fatal error: 26 or
Fatal error: 24
       Menumaker  is  telling you that there is  not  enough 
room  on  your  hard  disk to  run  the  program.  Menumaker 
requires at least .5 mb (500000 bytes) for the program  help 
files and a couple of your menus for editing.  Menumaker may 
require  even  more disk space if you are  working  with  or 
reading  in a very large menu.  Solution: Remove any  unused 
software from your hard disk and try again.
 
Fatal error: <file name> not found !
       Menumaker  is  telling you a file that  is  vital  to 
       Menumaker is missing.  Solution: Reinstall  Menumaker 
       from your distribution diskettes and try again.
 
Fatal error: Can't have files called Menumakr
       Menumaker  reserves the name "Menumakr" for its  own 
       use and will not allow it for a menu name.  Solution:
       Rename menu to a deferent name and try again.
 
Fatal error: 10
       Menumaker went looking for a vital file that was  not            
       found. Solution: Reinstall Menumaker from the  master 
       disks or reread in your .MNU file to try and  recover 
       any missing files.
 
 
Fatal error: 17
       You  may  have specified in the installation  a  disk 
       drive  that is not present in your system.  Solution: 
       Reinstall Menumaker specifying correct drives.
       
Fatal error: 17 or
Fatal error: 22 or
Fatal error: 23 or
Fatal error: 43
       Check  your CONFIG.SYS. The BUFFERS should be  20  or 
       more  and the FILES should be 20 or  more.  Solution: 
       Increase FILES and/or BUFFERS and try again.
 
Fatal error: 31
       Menumaker is telling you a file vital to the  program 
       has  deteriorated  in some way.  Solution:  Reinstall 
       Menumaker  off master disks, and try again or  reread 
       in the working menu file.
 
If none of the above help the problem or your error code  is 
not  shown above, try and get the error to occur  more  than 
once.  If  the error is not really hindering your  work  but 
only  happens  once  or rarely, please fill  out  the  "BUG" 
report   in  the  back  of  this  manual  and  send  it   to 
IntelliCADD.  If  the error is persistent  and  interrupting 
your  work you may contact IntelliCADD directly and we  will 
do our best to solve your problem.




Appendix B              ARCHIVING FILES
_________________________________________________________________
We recommend highly that if you a going to edit you menus to 
any  extent  that you back up you files menus on  a  regular 
bases. If in the event your hard disk should fail and it was 
the only place you had your menu you may lose a lot of  hard 
work.  When  backing up files you should keep  in  mind  one 
thing,  When we where creating Menumaker we wanted it to  be 
FAST so for the benefit of speed we had to translate an  MNU 
file  into  a large format to increase the  speed  at  which 
Menumaker  it  can  access parts of the  menu.  Example  the 
Autocad  menu  translates  to about 650000k  even  know  the 
actual menu file if about 32000k. To back up your menus  you 
can do it two ways:

1. Requires a large amount of floppy space.
Copy  all  the  files associated with your  menu  to  floppy 
disks. We recommend that if you save all the files you  copy 
them onto a high density disk so that your entire translated 
menu  will all be in one place. The files you will copy  are 
as follows:
 
           <name>.BTN  -  Button and Auxiliary commands
           <name>.MMU  -  Screen commands
           <name>.POP  -  Pull Down window commands
           <name>.ICN  -  Icon commands and Slide names
           <name>.TAB  -  Tablet menu commands
           <name>.DEF  -  Template dimensions
 

2. Requires a small amount of floppy space.
Write the menu out ([W] on the Utilities menu) into MNU form 
and save only the MNU file. If you have to restore the  file 
from archive you can Read it back into Menumaker format  and 
your  off again. The only setback to this way is all of  the 
command  descriptions will be shown as * Existing Command  * 
when you read the menu back in to Menumaker. You might  also 
want  to save the template dimensions also so you  will  not 
have  to  re-enter all of the template  dimensions  and  the 
number of rows and columns.

           <name>.MNU  -  Menu file in Autocad format
           <name>.DEF  -  Template dimensions

Note: <name> is the same as the current menu.



Appendix C              TEMPLATE MAKER
_________________________________________________________________
Template Maker (TEMPLMKR.LSP) is a Autolisp utility that was 
put  it  your Autocad directory during the  installation  of 
Menumaker. With this utility you can automatically create an 
Autocad  drawing  of  your template  with  your  own  custom 
commands to be placed over you tablet.

To  use template maker first you must enter  the  dimensions 
and  the number of rows and columns of your  template.  This 
can  be  done  in the [T] Tablet portion  of  Menumaker.  By 
starting  a  new menu with no defined template areas  or  by 
pressing the [F6] key while working on the tablet area.  The 
dimensions  for  the layout of the tablet while  working  in 
Menumaker are in the file <name>.DEF. Note the file ACAD.DEF 
was  placed  in  the Menumaker directory this  file  is  the 
dimensions  for the standard Autocad template you  may  copy 
this  file to another name if you like to make your  current 
menu have the standard layout for the Autocad template.
 

 

 
                        BUG  REPORT
--------------------------------------------------------------
--------------------------------------------------------------

                                    Date________________

Name____________________________________________________

Company_________________________________________________

Address_________________________________________________

City____________________  State_______  Zip_____________

Country_________________  Phone (      )________________

Menumaker Version_________ Serial number________________

Computer brand name________________ Model_______________

Memory_______________  Expanded memory__________________

DOS Version_____________  Clock speed________________Mhz

Hard disk size_______________  Autocad Version__________

Graphics adapter_________________  Monitor______________

 
                    Problem Description

__________________________________________________________
 
__________________________________________________________
 
__________________________________________________________
 
__________________________________________________________  

__________________________________________________________
 
__________________________________________________________
 
__________________________________________________________
 
 


End of Menumaker DOC