////////                   //      ///////                  /////
          //    //         //        //      //                       //
         //    //                   //      //                       //
        //    // //   // // ////// // //// /////// //   // // ///   //
       //    // //   // // //     ////         // //   // ////   //////
      // // // //   // // //     // //        // //   // //       //
     //////// /////// // ////// //   // /////// /////// //       //   TM
       //                                                       //


		   Generic Contouring Utility for AutoCAD(R)

				  Version 1.87

				   April 1988






			   U S E R ' S   M A N U A L


	      (c) Copyright 1987,1988 Schreiber Instruments, Inc.
			      All rights reserved.











			   SCHREIBER INSTRUMENTS, INC.
			 7250 Eastmoor Drive, Suite 226
				Denver, CO 80237
				 (303) 759-1024

	    _______________________________________________________
	    QuickSurf is a trademark of Schreiber Instruments, Inc.
	    AutoCAD is a registered trademark of Autodesk, Inc.




			       TABLE OF CONTENTS


	1.  Introduction  .  .  .  .  .  .  .  .  .  .  .  .  .  .  1
	2.  Input Requirements  .  .  .  .  .  .  .  .  .  .  .  .  1
	3.  Output  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  2
		a.  Control points .  .  .  .  .  .  .  .  .  .  .  2
		b.  Triangles   .  .  .  .  .  .  .  .  .  .  .  .  2
		c.  Grid .  .   .  .  .  .  .  .  .  .  .  .  .  .  3
		d.  Contours .  .  .  .  .  .  .  .  .  .  .  .  .  3
	4.  Installation  .  .  .  .  .  .  .  .  .  .  .  .  .  .  3
	5.  Operation and Options  .  .  .  .  .  .  .  .  .  .  .  4
	6.  AutoLISP Commands   .  .  .  .  .  .  .  .  .  .  .  .  5
		a.  GEN - Generate random points  .  .  .  .  .  .  6
		b.  QSX - Extract control points from drawing .  .  6
		c.  QSXPL - Extract polylines  .  .  .  .  .  .  .  6
		d.  QS - Invoke QuickSurf   .  .  .  .  .  .  .  .  7
		e.  LABEL - Label contours with elevations .  .  .  8
		f.  SMOOTH -  Smooth contours  .  .  .  .  .  .  .  8
		g.  INDEX - Change width of selected contours .  .  9
		h.  TICK - Draw tickmarks ("hatchuring")   .  .  .  9
		u.  POST - Post elevations of control points  .  .  9
		j.  TILT - Tilt objects for plan view   .  .  .  .  9
	7.  Custom Menu   .  .  .  .  .  .  .  .  .  .  .  .  .  . 10




			     THE "CONVERTIBLE DEMO"

		A unique new method is being used to deliver this
		version of QuickSurf.

		The distributed version is the complete, documented
		system, except for two things:

			o Contours are generated at randomly
			  selected elevations
			o The grid is only partially generated

		This version may be copied and distributed freely
		in its complete, unaltered form.  It is a demo,
		and we encourage you to share it with your friends,
		and upload it to public bulletin boards.

		To convert a demo version to a working system, call
		Schreiber Instruments, Inc.  When arrangements for
		payment are made, the conversion can be performed
		immediately.  Major credit cards are accepted, and
		no modem is required.

		Please copy all files to your hard disk drive C:,
		and have the system available when you call for the
		conversion password.

		Our number is (303) 759-1024, and the price is $499.







			   Q u i c k S u r f


	1. Introduction

	QuickSurf is a fast and flexible contouring system for
	use in conjunction with AutoCAD(R), Version 2.6 or later,
	as well as other graphics systems capable of interpreting
	AutoCAD's .DXF format files.

	With unsurpassed performance, versatility, and ease of use,
	QuckSurf is the right tool for any discipline in which spatial
	or other three-dimensional data can be meaningfully represented
	by surfaces.  QuickSurf supports all the usual features of
	contour mapping systems: smoothing, labeling, hatchuring,
	indexing, grid mesh views from arbitrary viewpoints and with
	hidden lines removal.  With the extensive editing features
	of AutoCAD, QuickSurf provides an environment where interactive
	contour mapping is a reality, and allows preparation of high
	quality hard copy maps on virtually every graphic output device
	in existence.

	2. Input Requirements

	QuickSurf requires that data be provided in an ASCII text
	file in a very free-form format.

	Basically, control points must be provided as x-y-z
	triplets in a text file, one point per line.  Standard
	decimal or scientific (exponential) notation may be used
	for the coordinate values, and any group of characters
	that cannot be mistaken for a number may be used to
	separate the three values on a line.  Hence, spaces,
	tabs, commas, semicolons, parentheses, etc., may act
	as separators of values on a line.

	Input can easily be created by spreadsheets, data base
	report generators, manual entry, or application programs
	easily written in any language.  An AutoLISP utility is
	also provided that can be used to extract selected items
	from an AutoCAD drawing, and create an input file for
	QuickSurf.

	By default, QuickSurf will process the smallest rectangle that
	encloses all the control points provided.  QuickSurf will
	NOT extrapolate outside the perimeter of the control points,
	and, like any other contouring method, it won't do very
	well around the edges.

	Therefore, a smaller rectangle may be specified for contouring
	than the extrema of the control points.  Ideally, this area
	should be well within the perimeter of the control points,
	with some control points in all directions around it.

				     Page 2


	The rectangle to be contoured may be specified by providing
	FOUR rather than THREE values on the first line of the input
	file.  These four values are two x-y pairs, which are opposite
	corners of the desired rectangle.

	Values beyond the fourth on the first line, and beyond the
	third on subsequent lines are ignored, as are all lines with
	fewer than three recognizable numeric values.

	The maximum number of control points that QuickSurf can
	process depends on memory available.  Approximately 64K
	bytes are required for the program and static data, and
	each additional 64K bytes allows for about 640 control
	points.  Thus, when running stand-alone (outside AutoCAD)
	in a system with 640K bytes of memory, QuickSurf can
	process between 4000 and 6000 points, depending on the
	size of the operating system.  From within AutoCAD, under
	standard configuration QuickSurf can process about 550
	control points.  If the ACAD.PGP file is modified so that
	the SHELL command requests 256000 bytes (rather than the
	usual 127000), up to 1800 control points can be processed.

	If the input file contains more control points than can
	be processed with the memory available, QuickSurf will issue
	a warning message, and continue by ignoring the points beyond
	the limit.

	The extension ".QS" is preferred for the input file name,
	but any extension is acceptable.

	3.  Output

	QuickSurf generates an AutoCAD .DXF file, with the same
	name as the input file.  The file may contain one or more
	of the following:

		a.  Control points

		The control points in the input file are posted as
		point entities, with appropriate elevations, on the
		designated layer (POST by default).

		b.  Triangles

		The triangles are generated by connecting the control
		points in an optimal pattern, for subsequent processing,
		and visual examination.  The triangles are created as
		3DFACE entities. This makes them useful for use with
		the AutoCAD HIDE command, as well as AutoShade.  A
		deisignated layer (TRI by default) may be specified
		for the triangles.

				     Page 3


		c.  Grid

		An array of approximately square cells is generated,
		also as 3DFACE entities, that covers the area to be
		contoured.  This is not very interesting in plan view,
		but in a view with an elevated VPOINT, it produces the
		common fishnet display of the surface. The default layer
		name is GRID.  Either cell size or the number of cells
		in the longer dimension of the contoured area may be
		specified by the user.  Cells that are not totally within
		the control point perimeter are not generated.

		Like the triangles, the grid may be used with HIDE and
		AutoShade to produce strikingly beautiful and visually
		effective displays of surfaces.

		d.  Contours

		Contour lines are generated within the area covered by
		the grid cells as POLYLINEs, with appropriate elevations.
		By default, all contours are placed on layer CONT, with
		a different color assigned to each elevation, starting
		with color 1 (red) for the lowest elevation.

		Alternatively, contours may be generated without color
		specifications (BYLAYER), or placed on a different layer
		for each elevation, with automatically generated unique
		names for the layers.

		Either the contour interval, or the number of intervals
		may be specified by the user.  By default, 15 or fewer
		optimally selected elevations are chosen.

		Since the contours are POLYLINEs, they may be further
		smoothed using the Spline or Fit options of PEDIT.

	4.  Installation

	Three files are required to operate QuickSurf with AutoCAD:
	QS.EXE, QS.MNU, and QS.LSP.

	QS.EXE should be copied to a directory that is in the normal
	search path of your system (your DOS directory, e. g.).

	QS.LSP may be copied to any directory.  If you wish to use its
	features (discussed below), it must be loaded into AutoCAD either
	manually (using (load "<path>/QS"), e.g.), or a line must be
	added to ACAD.LSP to cause automatic loading of QS.LSP.  Consult
	your AutoLISP manual for details.

	QS.MNU, likewise, may be copied to any directory, but must be
	invoked by the MENU command, or renamed to ACAD.MNU, to be
	loaded automatically.  Consult your AutoCAD manual for details
	on menus.

				     Page 4


	DOS environment variables LISPHEAP and LISPSTACK should be set
	to at least 25000 and 6000, respectively.  DOS manual, Chapter
	6 of AutoLISP manual.

	If you expect to process more than 500 control points at a time,
	you should edit the ACAD.PGP file as described in Section 2 above.

	If QS.LSP and QS.MNU are renamed to ACAD.LSP and ACAD.MNU, they
	must reside in the current directory to be loaded automatically
	when AutoCAD is started.

	5.  Operation and Options

	QuickSurf may be run from DOS directly, but more likely it will
	be invoked by a SHELL command from AutoCAD, since its output
	is intended for AutoCAD, or any system that can interpret .DXF
	files.

	By typing just "QS" in DOS or "SHELL QS" in AutoCAD, you will
	get a help screen that summarizes various options, discussed
	in detail here.

	Usage:  QS [options] filename[.ext]

	Options:  (xxx = numeric value;  sss = label)
		-lxxx	Maximum contour levels <15>
		-zxxx	Contour interval (overrides -l)
		-nxxx	Grid cells in longer dimension <32>
		-dxxx	Grid cell size (overrides -n)
		-p[sss]	Post control points on layer sss <POST>
		-t[sss]	Draw triangles on layer sss <TRI>
		-g[sss]	Draw grid on layer sss <GRID>
		-c[sss]	Draw color contours on layer sss <CONT> (default)
		-m[sss]	Draw monochrome contours on layer sss <CONT>
		-y[sss]	Draw contours on layers prefixed by sss <CONT>
		-	Suppress contours
		-v	Verbose

	Extension .QS assumed if none specified

	-lxxx	Approximate number of elevations at which contours are
		to be generated.  The entire range of elevations (as
		determined by QuickSurf) will be divided by xxx+1 and
		rounded to obtain the contour interval, and xxx or
		fewer elevations will be contoured.

	-nxxx	The number of cells in the longer of the two ranges
		(x or y) is set to xxx, and cell size is set to cover
		the contouring area, whether the area is chosen
		automatically, or specified explicitly on the first
		line of the input file (see Section 2.).

	-zxxx	This option specifies the contour interval, and hence
		is mutually exclusive with option -l.

				     Page 5


	-dxxx	Here xxx specifies the cell size, and the number of
		cells in each direction (x and y) will be determined
		by QuickSurf.  If -d is specified, -n is ignored.

	-p[sss]	sss specifies the layer on which the control points
		are to be placed as POINT entities.  If sss is omitted,
		the layer name POST is used.  If the option is entirely
		omitted, the control points are not drawn.  This option
		is useful if you plan to edit the points with AutoCAD.

	-g[sss]	Normally, the grid is not generated.  If you want
		a grid, for examination only, or for final output,
		use this option.  Use sss to specify a unique layer,
		so that you can easily isolate or erase the grid.
		If not specified, grid will be drawn on layer GRID.

	-t[sss] Same as -g, for triangles.  The default layer is TRI.
		Note that both the grid and the triangles are generated
		as 3DFACEs, suitable for VPOINT display, HIDEing, and
		AutoShadeing.

	-c[sss]	By default, contours are generated in multiple colors
		on layer CONT.  Use this option to designate a different
		layer.

	-m[sss]	Contours are generated on layer sss (CONT by default)
		without color specifications (BYLAYER).

	-y[sss]	Contours are generated on a different layer for each
		elevation, without color specifications.  The layer
		names are constructed by appending the elevation to
		the specified prefix sss.  If an elevation contains
		a decimal point, it is replaced by an underscore
		character (_), since layer names cannot contain point
		characters.  If sss is omitted, there is no prefix.

	-	To completely suppress contour generation, (if grid
		only is desired, e. g.), use this option.

	-v	Verbose.  This option gives you more information on
		progress of things as QuickSurf runs.  Normally only
		the times of main processing phases are displayed.

	If the input file (described in Section 2.) is specified without
	an extension, ".QS" is assumed; if the file name has no extension,
	it should be terminated with a period; otherwise, the complete
	file name should be used.  In all cases, QuickSurf will generate
	a file with the same name as the input file, and extension ".DXF".

	6.  AutoLISP Commands

	The file QS.LSP contains a minimal user interface and several
	useful utilities for creation of contour or grid maps.  The
	approach is completely generic, and allows QuickSurf to be
	adapted to any application in which contour or grid display
	of three-dimensional data is useful.

				     Page 6


	The commands are listed in a tutorial sequence, i. e., in
	order in which you can run through them as you are learning
	to use QuickSurf.

		a.  GEN - Generate random points

		Intended for demonstration, experimentation, or
		learning, this command will provide you with a data
		set, if you don't have real-world data available.

		Command: GEN
		Number of points: xxx

		GEN uses a random number generator to create POINT
		entities suitable for processing by QuickSurf.
		The ranges are as follows:

			x:	0 to 13
			y:	0 to 9
			z:	0 to 3

		b.  QSX - Extract control points from drawing

		If your drawing contains POINT, SHAPE, or INSERT
		entities that represent control points, use QSX
		to create a file suitable for input to QuickSurf.
		The entities must, of course, have appropriate
		elevations.

		Command: QSX
		File name <default>: filename
		First corner of area <MAX>: corner1
		Second corner of area: corner2
		Select objects: control-point-set

		The drawing name is used for the initial default file.
		A different name may be specified, and the file will
		have the extension ".QS", as preferred by QuickSurf.

		Any two opposite corners of the rectangle to be mapped
		may be specified, if desired.  Ideally, there will be
		control points in all directions outside this area,
		to get best results at the edges of the area, but this
		is not required.

		If you give a null response to the prompt for the first
		corner point, the second point will not be requested,
		and the area will default to the smallest rectangle
		that encloses all the  selected control points.

		The normal AutoCAD select mechanism may be used to
		select control points from the drawing.  Anything may
		be selected, but only POINT, SHAPE, and INSERT entities
		will be used, and all other entities are ignored.

				     Page 7


		The file created by QSX can be examined or edited using
		any text editor.

		Note:	Grid and contours will be generated only in
			the area that is both inside the rectangle
			defined by the two corner points, and inside
			the perimeter of the control points.  A minimum
			of three points are required.  The maximum
			depends on memory available (see Section 2.).

		c. QSXPL - Extract polylines

		Same as QSX, but only vertices from polylines are extracted.
		The polylines should NOT be splined nor fitted.

		This command is useful for reprocessing manually created or
		edited contours, possibly some imported from another system.

		d. QS - Invoke QuickSurf

		If you have created a valid ".QS" file, using either
		QSX or otherwise, you can use QS to process the file
		and draw the contours, and (optionally) the grid.

		Command: QS
		File name <default>: filename

		QS will invoke the SHELL command to run QS.EXE,
		and then the DXFIN command to load the output
		file (filename.DXF).  By default, QS.EXE is
		executed with no options.

		The QS command is suitable for most interactive
		work, where the automatic contour interval, grid
		density, layer nomenclature, etc., provide fast,
		convenient, and adequately precise results for
		screen display.

		Prior to generating a hard-copy plot, you will
		probably want to run QuickSurf with a higher
		grid density, to achieve more accurate results,
		and specify a smaller contour interval than
		the one chosen automatically by QuickSurf.
		You may do this by using the SHELL command
		to run QuickSurf with any of the options
		described in Section 5., or by setting certain
		AutoLISP variables.  The following variables
		are available:

			gridcells	Default 32
			interval	Default nil (auto)
			clayer		Contour layer - default CONT
			tlayer		Triangle layer - default nil
			glayer		Grid layer - default nil
			player		Control point layer - default nil
			suppress	Suppress contours - default nil

				     Page 8


		The menu file QS.MNU contains submenus for convenient
		control of these variables (see Section 7.).

		e.  LABEL - Label contours with elevations

		Places labels at selected locations on contour lines.

		Command: LABEL
		[Label location: point]
		Text height: value

		Use a pointing device to specify one or more points
		on contour lines at which a label is to be drawn.
		A small circle will be drawn at each location as
		you point to it.  After the last desired location
		is entered, a null response will go on to the prompt
		for text height, which you can enter as a distance
		relative to the last label location specified.

		LABEL will erase a portion of each selected contour
		line to make room for the text, tilt the text so that
		it follows the general direction of the contour line,
		and post its elevation using the current style.  The
		label will have the same layer, color, and elevation
		as the contour line.

		It's best to label contours on straight sections,
		where neighboring contours are relatively sparse.
		Careless labeling may produce strange results.
		If some overwriting or bad placement occurs, you
		can use the MOVE and ROTATE commands to make minor
		adjustments.

		UNDO All must be active during labeling.  It will take
		two or three U's to undo a badly placed label.

		f.  SMOOTH -  Smooth contours

		The Fit or Spline (not available prior to AutoCAD
		Release 9.0) options of PEDIT are used to smooth
		contour lines.

		Command: SMOOTH
		Select objects: countour-lines

		You may select anything (including the entire drawing).
		Selected entities that are POLYLINEs will be smoothed,
		and other entities will be ignored.

		By default, SMOOTH uses Fit on Version 2.6, and
		Spline with system variable SPLINESEGS set to -1 on
		Release 9.0.  Some crossing of contours may occur with
		Fit, and PEDIT can be used to edit offending contours
		manually.

				     Page 9


		The following AutoLISP variables allow other options:

			howsmooth	D(ecurve), F(it) or S(pline)
			splinesegs	See AutoCAD manual (R9.0)

		g.  INDEX - Change width of selected contours

		The Width option of PEDIT is used to emphasize major
		contour elevations.

		Command: INDEX
		Line width <default>: line-width
		Select objects: contour-lines

		Typically, line width should be sligtly greater than
		pen width for plotting, or resolution of the printer
		for printer plotting.  Set line width to 0 to remove
		indexing.  Anything may be selected, but only polylines
		will be modified.

		h.  TICK - Draw tickmarks ("hatchuring")

		Marks selected contours with downward pointing tickmarks.

		Command: TICK
		Select objects: contours
		Distance between ticks <defdist>: distance
		Length of ticks <deflen>: length

		One or more contours may be selected for hatchuring.
		After a null response, the distance between ticks
		and lenght of ticks may be entered as relative lengths.
		The defaults are .25 and .0625, respectively.

		A negative value for tick length will cause the ticks
		to point upward, rather than downward, as is customary.

		Note:	The recommended sequence of operations on a
			contour is LABEL, SMOOTH, TICK.  The first two
			may be reversed, but TICK must always be last.

		i.  POST - Post elevations of control points.

		Elevation values are drawn next to selected control
		points.

		Command: POST
		Select objects: control-points
		Text position: offset-point
		Text height: value
		Layer <default>: layer-name

		Anything may be selected, but only POINTS, SHAPES, and
		INSERTS will be processed.

				     Page 10


		The text position relative to each control point is
		specified relative to one of the selected control
		points, and will be the same for all others.  The
		lower left corner of the text string is the reference
		point.

		Overwriting of text or other important features may
		occur in dense areas.  The MOVE command can be used to
		clean up such situations manually.

		j.  TILT - Tilt objects for plan view

		Rotates selected objects from a VPOINT view so that
		they are rotated in plan view.

		Command: TILT
		Select objects: objects

		The purpose of this command is primarily to allow you
		to present both a plan view of contours and an oblique
		view of the grid in the same drawing.

		After generating a grid, freeze all layers except the
		one containing the grid, or other objects to be tilted.
		Use VPOINT to obtain the desired view.  Now run TILT,
		selecting only the desired objects.  Return to plan
		view (VPOINT 0,0), thaw all layers, and run MOVE, using
		select option "previous", to move the tilted objects
		to the desired position in the plan view drawing.

		The above proceedure may be repeated for multiple
		views of the same or different items in one drawing.

	7.  Custom Menu

	QS.MNU contains enhancements to ACAD.MNU to simplify the use
	of QuickSurf.

	The QuickSurf pull-down menu contains all the above AutoLISP
	commands, and brings up side-bar submenus that allow easy
	manipulation of certain options.  To invoke some of the more
	arcane features of QuickSurf, you must use the SHELL command,
	and refer to Section 5. of the manual.

	Users skilled in AutoCAD customization are encouraged to modify
	QS.MNU, as well as QS.LSP to suit their requirements.