Autodesk Product Support                              November 29, 1989

               386 Memory Managers and Extended AutoLISP


 Some of the more frequently asked questions on Release 10 c2 have
been on configuration and installation issues regarding Extended
AutoLISP (referred to here as ExtLISP).  We will attempt to set the
record straight on this.

 The basic problem arises when setting up EXTended memory on 386
machines to emulate EXPanded memory for storing display lists, as well
as dedicating the remainder of the memory for ExtLISP node space and/or
Extended I/O page space use by AutoCAD. Customers may also elect to
use a RAM disk in addition to all of these. The number of permutations
and combinations of these settings is enormous.

Note:

 This applies to 386-based machines only.  On 286 machines, EXPanded
 memory must be physically present (in hardware), and cannot be
 simulated by a software driver.

 The customer must have Release 10 c2a (or c2 with the update disk) in
 order to allow Extended AutoLISP to coexist with simulated EXPanded
 memory.

 The customer must be using a VCPI-compatible memory manager.  The
 memory managers known to work in this fashion are:

      386 to the Max version 4.0.5  from Qualitas       (301)
      469-8848
      QEMM           version 4.2    from Quarterdeck    (213)
      392-9701
      Compaq CEMM    version 4.0    from Compaq         (714)
      370-0670

NOTE!:  The only CEMM version compatible with VCPI is the one
shipped with Compaq DOS 4.01.  This is marked as CEMM version 4.00. 
Compaq plans to make this available on DOS 3.3 as well.  Earlier versions
of CEMM are NOT compatible with the VCPI specification and as a
result, Extended AutoLISP will not work with this memory manager.

Mixing EXTended and EXPanded memory
 Customers often wish to partition the EXTended memory on a 386
machine as partly EXTended and partly EXPanded.  While this is
understandable, under VCPI it becomes extremely difficult to further
divide the remaining EXTended memory between ExtLISP and Extended
I/O page space.  Under VCPI, all the addresses that could be assigned to
the LISPXMEM, ACADXMEM, and ACADLIMEM environment variables are
no longer valid, since absolute addresses are outside AutoCAD's domain,
and are under the VCPI manager's.

Recommendations
 Autodesk Product Support recommends this procedure:

 Set up ALL of the EXTended memory as EXPanded, under the VCPI
 manager's control.

 Allow the display list driver to acquire a portion of this.  ADI display
 drivers typically require about 1MB of EXPanded memory.

 SET ACADXMEM=none
 SET ACADLIMEM=<size>
      Choose a size to limit AutoCAD's use of the entire
      EXPanded memory area.  AutoCAD customers typically elect
      to set aside about 2MB of memory, from a total of about
      4MB of system memory, for I/O paging purposes.

 DO NOT SET LISPXMEM.  Extended AutoLISP acquires the remaining
memory from the EXPanded memory pool.  Remember: under VCPI,
EXPanded and EXTended memory are treated
synonymously by the VCPI manager.
 
For example, (with QEMM on a 386 system with 4MB EXTended
memory):

In CONFIG.SYS:       device=c:\qemm.sys on

In a batch file:     acadi                    /* ADI driver
acquires about 1M */
                extlisp                  /* LISP acquires about 1M
*/
                set acadxmem=none        /* No EXTended memory
*/
                set acadlimem=2048K      /* Muzzle AutoCAD
Extended I/O */
                acad
                remlisp

 Note that Extended AutoLISP acquires 1MB by using the leftover
memory.  ExtLISP does not explicitly acquire the memory at boot
time, but AutoCAD and ADI drivers generally do.  ExtLISP allocates
enough memory to hold 4096 nodes at boot time, and expands its
memory pool while acquiring more node space later.  It will use up
to 1MB in the above example, since the VCPI manager will protect
the memory pool acquired by the real-mode AutoCAD and ADI driver
executables.
 
 As far as RAM disks are concerned, set up the device driver in
CONFIG.SYS prior to setting up the 386 memory manager.  The
amount of EXTended memory acquired by the RAM disk will be
subtracted from the amount of memory made available to the 386
memory manager when it fires up.  This net amount can then be
treated according to the guidelines outlined above.

 Do not use any fancy options of the 386 memory manager (rom,
cache, etc.)  Encourage your customers to upgrade to AutoCAD 386,
which utilizes the PharLap 386|DOS-Extender to circumvent these
environment issues, and offers a considerable improvement in perfor-
mance as well.

                   Addendum for Release 10 c7

 Release 10 c7, an updated version of AutoCAD Release 10,
addresses some of the problems associated with Extended AutoLISP
installation and configuration.

 There are now 3 versions of Extended AutoLISP:

 DOS 16/M Runtime Version      Version        Shipped with
           2.48                i4.04e    Release 10 and Release 10
           c2
           3.18                i4.05e    The c2a update to Release
           10
           3.18                i4.06e    Release 10 c7

 The c2a update addressed the problem of running Extended
AutoLISP in conjunction with a VCPI-compatible 386 memory
manager.  Prior to that, this was not possible.

 Prior to Release 10 c7, Extended AutoLISP had 2 problems at the
time of execution:

      It would honor the LISPXMEM environment variable
      even under VCPI, where the model of true, linear
      extended memory is no longer valid. Under VCPI,
      Extended AutoLISP now ignores absolute addresses and
      honors the "size" parameter only.

      It would detect all the available memory at start-up, but
      not reserve it, permitting applications such as
      AutoCAD's Extended I/O pager to write over its own
      node space.  Extended AutoLISP protects itself from
      this now by reserving all the available memory at start-
      up.

 The Release 10 c7 update does not fundamentally alter the approach
outlined earlier, but circumvents common problems and
misconceptions associated with 386 memory managers and Extended
AutoLISP.